The 16550A UART

by Randol Tigrett

If your computer includes a 16550A UART, chances are you'll get faster 
throughput during your communications sessions if your software takes 
advantage of it. To experiment with the UART in your machine, you can 
use the DEBUG script shown in Figure 1 to generate a small program 
called FIFO.COM. You simply run FIFO.COM once when you turn on your PC 
and it activates the FIFO buffers in the UART, displaying what type of 
UART you have in your machine, 8250 or 16550 or 16550A.
	 We emphasize the word experiment because some communications 
programs, written before the introduction of the 16550A, might lock up 
when the UART activates the previously unused upper bits of the 
Interrupt ID Register. Even if your communications software doesn't 
lock up with the FIFO buffer activated (and most don't) you still 
won't get the full benefit of the FIFO buffer unless the program makes 
use of it. 
	Programs not specifically written for the 16550A won't move 
data in large blocks the way more modern programs do, and FIFO.COM 
can't make your communications program recognize the UART or utilize 
its FIFO buffer better. However, activating the buffer with FIFO.COM 
can potentially eliminate problems of overrunning the UART, 
particularly in a PC on the receiving side of a high-throughput file 
transfer. Although it may help in this way, FIFO.COM mainly 
demonstrates how programmers can activate the buffer.
	The NS16550AF UART (Universal Asychronous 
Receiver/Transmitter) contains two 16-byte FIFO (first in, first out) 
buffers. Slower machines, like an 8-MHz AT, using fast modems need 
these buffers, as do faster machines, like a 33-MHz 386, that attempt 
to run other programs in a multitasking mode while using asynchronous 
communications. The interrupts generated by communications sessions 
can have a serious impact on the effectiveness of computers running 
multitasking operations. Programs in other sessions suspend 
processing, displays don't update, and characters typed at the 
keyboard don't register while the CPU services the UART.
	The 16-byte FIFO buffers reduce the interrupt activity of the 
CPU because they can hold more data before generating an interrupt 
requesting a transfer. This makes it easier for slower CPUs to avoid 
dropping characters when they receive a fast stream of data. You can 
set the receive FIFO buffer to receive 1, 4, 8, or 14 characters 
before the UART generates an interrupt.
	If your computer contains a 16550 UART instead of the 16550A 
or AF, be aware that the plain 16550 was flawed and will not work 
correctly if the FIFO buffers are activated. When you buy a new 
computer, make sure the manufacturer either sockets the UART or 
installs the new 16550A UART. If you can install the UART yourself, it 
costs only about $12. The 16550A UART is especially useful for 
communicating with high-speed modems because, with the advent of 
V.32bis modems, you can now enjoy a carrier rate of 14,400 bits per 
second between modems. With V.42bis data compressions of 4 to 1, you 
must set the DTE (Data Terminal Equipment) speed of the RS-232C link 
to 57,600 bps for optimum performance during file transfers. Slower 
PCs cannot handle the high RS-232C DTE speed without the 16550A UART.
	If you want more information on programming the 16550A UART, 
National Semiconductor makes available a book called Data 
Communications: Local Area Networks: UARTs. The book sells for $10 and 
you can call National Semiconductor at 408-721-5000 to ask about its 
availability.

HOW TO GET FIFO.COM
You can download FIFO.COM from library 2 of PC MagNet's Utilforum/Tips 
forum (type GO PCM:TIPS from PC MagNet or CompuServe to get there) or 
create it using the DOS DEBUG program.
	Assuming DEBUG is available in the C: root directory, redirect 
the following text to DEBUG by typing 

c:\debug <fifo.scr

The text below contains comments to illustrate the program's 
operation. Remove all comments enclosed in /* */ before redirecting to 
DEBUG. Note that this program will cause the 16550 UART to work 
improperly by enabling its flawed FIFO buffer.

A
JMP     0123
NOP
AND     [BX+DI],DH
SS:
XOR     AX,3035
AND     [DI+41],DL
PUSH    DX
PUSH    SP
AND     [BX+SI],AH
AND     [BX+SI],AH
AND     AL,20
CMP     [BP+SI],DH
XOR     AX,2030
PUSH    BP
INC     CX
PUSH    DX
PUSH    SP
AND     [BX+SI],AH
AND     [BX+SI],AH
AND     [SI],AH
MOV     DX,03F8     /* PORT ADDRESS - 0040:0000 */
ADD     DX,+02      /* set offset to IIR Register */
MOV     AL,C1       /* set receive buffer to 14 and enable */
OUT     DX,AL       /* change the 14 = 0x0C to 1,4,or 8 */
XOR     AX,AX
IN      AL,DX
PUSH    AX
AND     AL,C0       /* set up for 16550A UART */
CMP     AL,C0       /* is it a 16550A ?       */
JNZ     013D        /* no                     */
LEA     DX,[0103]   /* yes                    */
JMP     0141
NOP
LEA     DX,[0113]   /* print either 16550 or 8250 */
MOV     AH,09
INT     21
POP     AX
MOV     AH,4C       /* show the IIR setup as errorlevel */
INT     21
RET

N FIFO.COM
RCX
4B
W
Q

Figure 1: DEBUG script to generate FIFO.COM, a program that activates
the 16550A UART's FIFO buffer and identifies the type of UART in your 
machine.
===============================================
Toad Hall Note:

The above horribleness can be circumvented by using the new FIFO.ASM
I just produced with a *real* disassembly of FIFO.COM.

And if you want something a wee bit more sophisticated, look at
UARTTYPE.ASM (with its accompanying UARTTYPE.MSG).  It not only activates
the UART, but specifically identifies just which one it is!

David Kirschbaum
Toad Hall
kirsch%maxemail@uunet