WHATPORT.COM 
 
                               Version 4.0 
                              October, 1990 
 
                  For detecting installed serial ports, 
              type of mouse, IRQs used by ports and mouse,
                      and potential IRQ conflicts
 
               Copyright 1989-1991 Life Sciences Software 
                    8925 271st St., N.W., Suite 112
                                Box 1560
                        Stanwood, Washington 98292 
 
 
AUTHOR: Pete Petrakis (CIS 76555,1175)


IMPROVEMENTS IN THIS VERSION:
 
    Version 4.0 of WhatPort is a substantial improvement over all previous
    versions.  For the first time the program is able to detect the IRQ
    line actually being used by the serial ports, instead of assuming that
    the standard IRQs are being used.  This greatly increases the program's
    usefulness in situations where unconventional IRQs have been assigned 
    to serial ports.  The new version also detects and reports the base
    address of each installed serial port.

 
DESCRIPTION: 
 
    This program detects what serial ports (COM1-COM4) are installed 
    in a standard (PC, XT, AT) or PS/2 system.  The type of mouse, if
    present, is also shown (serial, bus, InPort, PS/2, HP) together with
    the interrupt request (IRQ) line it's using (unless it's a PS/2).
    The program warns of potential IRQ line conflicts between the
    mouse and serial ports.  In the case of PS/2 computers, where
    there should be no possibility of conflict between a PS/2 mouse
    and a serial port, WHATPORT only reports the presence of the
    PS/2 mouse and the characteristics of the serial ports it finds
    installed (up to COM4).







                                  -1-

    
    PRINCIPLE:

    Because standard PCs have only two IRQ lines for serial ports,
    COM3 must share COM1's IRQ line and COM4 must share COM2's 
    IRQ line.  Unfortunately, two devices using the same IRQ 
    line can't be active at the same time.  COM3 can't be used for 
    a printer or modem if a serial mouse is active on COM1, for 
    example.  Likewise, COM4 can't be used if a serial mouse is 
    active on COM2.  In other words, if you have four COM 
    ports and a mouse is attached to one of them, you do not 
    have three COM ports available for other devices, you only 
    have two.  The COM port that shares the IRQ line being 
    used by the mouse is not usable.  WHATPORT detects and
    reports such conflicts.
 
    The following table shows what ports are available for other
    devices in a conventionally configured PC, XT, or AT when a 
    serial port mouse is present on a multiple-port system:

       Serial port mouse on     Ports available for other devices 
       _____________________    _________________________________
        COM1 or COM3 (IRQ4)          COM2 or COM4 (IRQ3) 
        COM2 or COM4 (IRQ3)          COM1 or COM3 (IRQ4) 

    Conflicts with serial ports are also possible in the case of a
    bus mouse.  For example, if a bus mouse is configured to use
    IRQ3, there will be a conflict with both COM2 and COM4.  If it
    is configured to use IRQ4, there will be a conflict with both
    COM1 and COM3.  WHATPORT also detects and reports these conditions
    so a different IRQ can be selected for the bus mouse.

    The PS/2 has a different arrangement.  COM1 in a PS/2 uses IRQ4,
    and COM2, COM3, and COM4 share IRQ3.  There should not be any IRQ
    conflicts with a PS/2 mouse in a PS/2 system since the PS/2 mouse
    has its own port and does not use either IRQ3 or IRQ4.  However, it
    seems theoretically possible that someone could attach an ordinary 
    (non-PS/2) serial or bus mouse to a PS/2 machine, in which case
    there could be IRQ conflicts.  With that kind of setup, a bus mouse
    using IRQ3 could make three serial ports (COM2, COM3, and COM4)
    unusable on a standard PS/2.

    As noted above, Version 4.0 does not assume that serial ports 1 to
    4 are using the standard IRQ lines for a conventional or PS/2 computer.
    Instead, it performs tests to determine which IRQ line each installed
    serial port is actually using.  Furthermore, it determines the base 
    address for each installed serial port.  Thus Version 4.0 should
    be useful with virtually any system configuration.
    
                                   -2-


HOW TO USE THE PROGRAM:

    Just run it and read the results.  Adjustment for color or
    monochrome display is automatic, but monochrome can be forced
    by putting M on the command line.
    
    Some special considerations apply in the case of PS/2 systems, 
    because the port addresses they use for COM3 and COM4 are different
    from those in PCs, XTs, and ATs.  Version 4.0 of WHATPORT will
    automatically detect the presence of an IBM PS/2 system and check
    the right port addresses.  The option to declare the presence of a
    PS/2 system with a command line switch has been eliminated from version
    4.00 since experience shows that automatic detection of the system type
    is reliable.

    IRQ conflicts between the mouse and a port are reported with the message, 

         "POTENTIAL IRQ CONFLICT -- COMx and the mouse share IRQy"
 
    where x is the number of the serial port and y is the number of the
    IRQ line.  The message will be printed for each installed serial port
    that is using the same IRQ line as the mouse.  If you see this message,
    it means the specified serial port is probably useless for communications
    or any other purpose.  With a bus mouse, the conflict can be resolved
    by assigning a different IRQ line either to the serial port (in a few
    systems) or, most commonly, to the mouse.  Options with a serial port
    mouse are more limited.  For example, a serial port mouse on COM1 will
    not only tie up that port, it will also tie up COM3 unless there is
    some way to give COM3 a different IRQ.  (Note: The user assumes any
    risk involved in IRQ assignments.  It is advisable to consult the
    mouse or serial port installation manual for guidance in picking the
    right IRQs.)
 

SHAREWARE NOTICE

    WhatPort is widely used by computer consultants and others involved in
    equipment installation and development, which is most gratifying to any
    program author.  Since the effort to continuously improve the program
    is not without expense, it has become necessary to make the program
    shareware and ask people to register and pay if they use it regularly.
    Obviously, many people will use it only once, when they install a new
    mouse, for example, and it seems pointless to expect them to register.
    However, it does seem appropriate to ask those who use it regularly for
    business, professional, or institutional purposes to support its

                                      -3-


    continued development.  Beginning with Version 4.00, WhatPort is a 
    shareware program.  The registration fee is modest, only $15 U.S.,  
    and your support will be very much appreciated.  Please mail your
    registration payment to the above address.


 
DISTRIBUTION AND DISCLAIMER: 
 
    WHATPORT.COM and this document are provided by Life Sciences Software,
    Stanwood, Washington.  They may be copied and distributed promiscuously
    provided they are not sold, modified, or separated.  Companies involved
    in the distribution of diskettes containing shareware or free programs
    are permitted to distribute these files and charge their normal fees for
    that service.  Although WhatPort has been extensively tested, Life
    Science Software and Pete Petrakis make no warranty concerning its
    usefulness in all systems and accept no responsibility or liability for
    any harm resulting directly or indirectly from its use.

                                             Pete Petrakis
                                             Life Sciences Software
                                             Stanwood, Washington


























                                       -4-