FIXCNTRL.EXE - cuts unwanted conferences from QWK control.dat files
===================================================================

syntax: fixcntrl [n]  where n - 1 is an [optional] highest numbered
                      conference to leave in the file.  Default is 999.

purpose:  Some older QWK readers were set up to handle only a limited
          number of conferences.  For example, PowerQWK (PQ 2.15) uses
          pseudo-conference #1000 as its storage area for the user's
          personal messages.  When Channel One BBS in Cambridge, MA
          added conference slots for a few hundred "rsrvd" conferences
          in early 1993 it overran PQ's limits, and message traffic in
          the CH1 Main Board indicated some other readers may have been
          affected as well. 
          
          The file "control.dat" in the QWK packet contains a list of
          all the active conferences on the BBS.  If you are using the
          QMAIL door, it can be instructed to send only the conferences
          which you have selected in control.dat - but this is a poor
          solution, as you can't use offline processing to join a new
          conference if your reader doesn't know it exists, and you
          may prefer the facilities in Cam-mail or another door.
          Fixcntrl.exe will remove conferences above #999 (or another
          number you specify) from the control.dat file, making it
          palatable to older QWK readers like PQ.  Of course, the
          inevitable tradeoff is that your reader cannot access these
          removed conferences.
          
          I wrote fixcntrl.exe specifically to make PQ 2.15 work with
          Channel One, but it may also be useful with other QWK readers
          or on other BBSs.  It is intended to be run from a batch file.
          The control.dat file must be extracted from the QWK file and
          available in the current working directory when fixcntrl is run,
          although fixcntrl itself can be anywhere on the path.  If
          fixcntrl fails for any reason (can't find control.dat, disk
          full, etc.) it returns errorlevel 1, which can be tested in
          your batch file.  Here is an excerpt from mine:

========

:channel1
md mtemp
cd mtemp
copy c:\data\zc\channel1.qwk .
lha e channel1.qwk control.dat
fixcntrl
if errorlevel 1 goto uhoh
lha u -m channel1.qwk control.dat
copy channel1.qwk c:\data\zc\mail\in\channel1.qwk
copy channel1.qwk c:\data\zc\doncha.qwk
del c:\data\zc\channel1.qwk
del /y *.*
cd ..
rd mtemp
return

:uhoh
{...error processing...}

========

          By default, fixcntrl.exe will remove all conferences numbered
          999 or above from the control.dat file.  You can optionally
          specify a highest numbered conference to retain, which should
          be one higher than the highest conference number you need (to
          take the Main Board, conference #0, into account). For example,
          "fixcntrl 7" would retain the Main Board (conf #0) and confs
          1 through 6 (for a total of 7), and discard all the others.
          If you specify a number higher than the number of conferences
          on the BBS control.dat will remain unchanged, and most silly
          entries (fixcntrl -33 or fixcntrl 100000) should revert to the
          default, although I'll bet you can break this if you try hard
          enough.  Your original control.dat file will be irreversibly
          overwritten by fixcntrl.exe - so you should probably experiment
          on a copy of control.dat from an old QWK file to assure yourself
          that all is well.  (Control.dat is a plain ASCII file that you
          can read with LIST or any ASCII editor.  Line #11 is the number
          of conferences, minus one.  Try "fixcntrl 4" on a spare copy
          of control.dat to see how it works.  You should end up with 3
          on line #11, and conferences 0-3 listed after).  Fixcntrl.exe
          retains all the optional user statistics information (time
          used, # of downloads, etc.) which is appended to control.dat by
          Cam-Mail and other mail doors, so it is available for your
          reader to display if it has this function.

warranty: None.  I wrote fixcntrl.exe for myself, and it works for me.
          You are free to use it if you'd like to, with no obligation
          whatsoever and entirely at your own risk.  If you run into
          trouble with fixcntrl.exe, you may leave a message on the Main
          Board at Channel One (617-354-8873) and I'll see if I can help
          you out, but as far as "support" goes, that's it.  Have fun!

                                                      Ken Haverly
                                                      May 26, 1993