Documentation for XGROUP v0.02, an XBBS Groupmail/Echomail/Netmail
          Scanner/Tosser copyright (c) 1991 by M. Kimes
                      all rights reserved


 Overview, disclaimer, restrictions, BS...

Warning:  these docs written late at night by an opinionated jerk.

XGroup is a fast 5-D echo/net/groupmail processor for XBBS (MS-DOS and
OS/2) message bases that supports file locking so that it can be used
while message bases are active in other tasks.

     License:

XGroup is free for the using in non-commercial environments.  That means
if you make money using it, or use it within commercial walls, you are
violating my copyright.  "Commercial" includes businesses, government
agencies and religious groups.  Go away.  If you think you're an
exception, ask *first*.  You can make XGroup available for download if
you don't charge anything for access to it or the time to get it as long
as you don't alter the original archive. If that's too much trouble,
don't do me any favors; don't keep it around.

     Warranty:

XGroup has no warranty whatsoever.  If it breaks, you have two (or more)
pieces. I guarantee only that it will take up space on your storage
media at least until deleted.  Other old, tired sayings.

     Warnings:

XGroup normally makes little attempt to support crappy topology.  Don't
make dupes or you will probably become familiar with the word
"excessively" followed by the word "annoying."  Stars are good topology.
Fully enclosed polygons are garbage as far as I and XGroup are
concerned.  See additional comments under KEEPPATH and CHECKSEENBYS
below if you just have to.

XGroup doesn't handle messages longer than 64K.  When the atmosphere
among developers gets better, I'll fix it.  Yes, that does mean it's
broken, and that I'm lazy.

Do you feel alienated yet?  Did I mention there's no warranty?  :-)


 Brief primer:

Fidonet-technology mail (echomail, netmail, and groupmail) arrive on
your system in the form of packets: a bunch of messages crammed
together.  This is called the "transport layer."  Packets have a
specific pre-defined format so that every node that receives packets
knows how to disassemble them into messages. A packet consists of a
header followed by zero or more packed messages. You can examine packets
directly with programs like LIST (they'll look like Greek,
though...unless you're Greek) and PKTHDR or PACKPEEK if you're curious.

Netmail refers to a message (usually private) from one node (usually a
BBS) to another, or more specifically, from a user at one node to a user
at another node. Netmail usually goes direct (sender calls receiver to
deliver), but routing schemes are becoming more common (where sender
calls another node that calls another node, and so on, until finally the
receiver is called and the route is complete).

Echomail, which is rarely private, is the more common of the two types
of broadcast mail (groupmail, while superior, is less popular.  This
seems common in computerland where MS-DOS is more popular than OS/2 for
no good reason at all).  Echo messages literally "echo" from one node to
another in a sometimes-huge moebius loop.  The difference between routed
netmail and echomail is that echomail may exist in readable form on all
or some of the transit nodes; each node can be a recipient.  Netmail is
normally only unpacked and placed into the message base on the receiving
node (unless processed by braindead software, which -- surprise --
happens).  Due to problems with hardware, software, topology and the
base technology of echomail, duplicate messages (dupes) tend to be a
problem.  Echomail also requires "customized" packets built specifically
for each recipient (this is more a requirement of existing echomail
processing software than the technology itself, but I digress). Although
most echomail conferences have moderators (someone responsible for and
in charge of the conference), echomail is by nature rather wild and
wooly (some might say uncontrolled and uncontrollable).  But, for all
its faults, it works fairly well.  Remember that echomail was kludged
together before the idea of broadcast mail, at least in a Fidonet
technology network, was commonplace; no one dreamed it would reach the
scale it has today.

Groupmail attempts to rectify some of echomail's problems, with a fair
degree of success.  It falls into the "cracks" of typical net and
echomail processing.  "Upbound" groupmail (headed toward the moderator,
or "topstar") is sent as pseudo-netmail so that it avoids echo
processing.  At the topstar a common packet is compiled and shipped back
out to all participants.  In this way, messages on all systems are
identical (consider that with echomail replies sometimes arrive before
original messages).  While it might seem at first glance that more mail
must be handled in this fashion, remember that Groupmail disseminates
the "extra" load over all participating systems and doesn't have to
carry the excess baggage echomail often does (SEEN-BYs, PATHs, etc.) and
that dupes are rare in groupmail due to the method of disseminating
these packets, called "update requesting."  It all evens out, and the
flow is smoother than with echomail.  Finally, groupmail conferences can
actually be policed by their moderators, though there is no
technological requirement to do so.  And, unlike echomail, if groupmail
is deleted at some point, it shows up; you never get your message back.
With echomail your messages might never leave your uplink, and you'd
never know it.  Groupmail can also allow files to follow messages.

For more information on packets and netmail, see FTS-0001, FSC-0039,
FSC-0045 (the packet header format XGroup uses) and FSC-0048.  For more
info on echomail and topology, see FTS-0004.  Groupmail is discussed in
more detail in FSC-0036.  These FTS-* and FSC-* documents are available
from the FTSC (Fidonet Technical Standards Committee) chair; see your
nodelist or ask your bossnode, whichever applies.


 Back to XGroup...

Version 0.02 is a bound executable (runs under both MS-DOS and OS/2).
Although parts of XGroup are still in beta stages (particularly the
groupmail support), the functions used in day-to-day Fidonet technology
net and echomail processing have worked fine for an extended testing
period.  It shouldn't spit garbage out onto the net if you don't screw
up its setup (like telling it to forward to someone you shouldn't).

XGroup uses those asshole files that HeadEdit can create, so if you mark
your assholes noimport, you won't waste any more time on them than
absolutely necessary.

It is fairly important to remember to always run XGroup from the same
directory.  This is because XGroup keeps a "marker file" called
XGROUP.SF$ open while it is working on importing a packet.  This marker
file contains the name of the current packet and the position in that
packet (it's updated every sixteen messages, a compromise between safety
and speed).  If interrupted by something awful, like a system crash,
XGroup will resume the packet at or close to the last place it was
working before.  It's not foolproof, but it's better than nothing...



 OS/2 users note:

Only one instance of XGroup may run at one time.  XGroup should take
care of this on its own and wait for other instances of itself to finish
before continuing if it's already active in another process.  XGroup
will wait for the OS/2 XMsg to finish working, and vice versa.  XGroup
supports full record locking while importing and exporting, however, and
should run fine with other programs that access the XBBS message areas
that also support record locking (like XBBS and HeadEdit).  Note that
XMsg is *not* one of those, for reasons that'll be obvious once you
think about it a bit.


 Desqview/Windoze users note:

If you run more than one instance of XGroup at one time, it'll screw you
up, and it's your tough luck for running on top of DOS.





 And now, the blood and guts:




 Usage:  XGROUP [configfile[(appid)]] [command]

[configfile] defaults to XGROUP.CTL with no (appid) and must be included
if passing a [command]


 Command line options [command]:

E (xport only)

XGroup will export from your XBBS message areas.  No importing will take place.


I (mport only)

XGroup will import mail.  No exporting will take place.


C (leanup only)

XGroup will tidy up the groupout (see below) directory only.


A (ll of the above)

XGroup will Import, then Export, then Cleanup (same as no command line
command -- default).


M (ake Update Requests)

XGroup will make update requests for groupmail conferences based on the
group date files in the groupin (see below) directory.


P (artially moderated group export okay)

Allows partially moderated group conferences to be exported.


F (ully moderated group export okay)

Allows fully moderated group conferences to be exported.


NE (no echoes)

Performs no echomail processing.


NG (no groups)

Performs no groupmail processing.


RO (do routing)

Performs XBBS-OS/2 routing.  This action is implied by A(ll) and
E(xport), so RO is ignored if A or E is in effect (including the default
A).  XGroup doesn't do routing under MS-DOS.  Get a real operating
system.


IP

Idle priority (overrides config file PRIORITY statement)

NP

Normal priority (overrides config file PRIORITY statement)

HP

High priority (overrides config file PRIORITY statement)


r <full FTN address> <echotag> [<startat>]

Performs a rescan of echo <echotag> for address <FTN address> USE ONLY
WITH EXTREME CAUTION!  You can easily create a load of dupes. Seenbys
and PATHs will likely be gone, and definitely not "properly" updated
(Tiny Seenbys are added).  Be sure the receiver can handle it correctly
and not cause dupes on his end.  BE SURE. Better yet, don't use it at
all.  Note that rescanned messages are clearly stamped with a
^aRESCANNED <address> kludge line indicating for whom they were
rescanned.  Advise the recipient that his name will be mud on the net if
he screws up and forwards them *anywhere.*  I can assume no
responsibility for your improper use of the rescan function.  If in
doubt, DON'T DO IT.  Remember those words:  "excessively" and
"annoying."


? (print help)


Examples:
    XGROUP ALTCFG.CTL E F
    XGROUP XGROUP.CTL NE E





 Configuration file keywords/data:

;

Begins a comment.  Comments are rudely ignored by XGroup.  You can place
the comment indicator anywhere; everything after the semi-colon on the
line will be tossed into the bit bucket.


APPLICATION <appid>

Begins an "application-specific" area.  The application id (appid) is
passed in parentheses after the name of the config file (for example,
XGROUP MYCFG.CTL(MYAPP)).  This can allow you to have several different
configurations in one config file, and even to have information for more
than one program in the same config file.


ENDAPP

Ends an "application-specific" area.  XGroup behaves as though it had
encountered EOF (end-of-file).  In other words, it stops reading from
the config file.  If an AREAFILE was specified, it is then read.


AREAFILE

Gives XGroup the name of a file to "include" that contains area
information.  Actually, it can contain anything a normal config file
can, but the primary use of this will probably be to separate area
listings from the normal config file for use with an area manager-like
program.  XGroup will have that built-in someday.  This allows the area
manager to rebuild the file containing area information without worrying
about other config information and comments being lost.


GROUPOUT  <drive:/directory>

This is the directory that groupmail files available for update request
will be placed in.


GROUPIN   <drive:/directory>

This is the directory that groupmail files are moved to just prior to
processing.  Note that if this directory is on the same drive as
GROUPOUT a "move" instead of a "copy" can be used to transfer files
between these areas (that's a Good Thang).  Group date files are also
kept in this directory (these marker files are stamped with the date of
the last groupmail you received; they are used when generating update
requests).


GROUPHOLD <drive:/directory>

This is the directory where groupmail files that seem to be damaged in
some way are stored for you to inspect manually.  If this parameter is
omitted XGroup deletes files it can't process.


INBOUND   <drive:/directory>

This is the directory into which you receive mail.  Normally it's the
same directory into which your mailer places incoming files.


OUTBOUND  <drive:/directory>

This is the directory where XGroup will place *.OUTs (Opus/Bink-style
packets) or P.* (XBBS-OS/2 packets).  In the case of *.OUTs, this
directory should *not* have an extension.  BinkleyTerm uses similarly
named directories with extensions to designate different zones.  For
instance, if this directory is C:\BT\OUT and your primary zone is zone
1, mail destined for zone 2 will be placed into C:\BT\OUT.002 and mail
destined for zone 255 will go into C:\BT\OUT.0FF.  I know it's
confusing.  Get AMAX and BOOM if you have to use Opus/Bink-style
outbounds; they'll help.  XBBS-OS/2 uses one (count 'em, one) outbound
directory and long filenames that store the full address of the
recipient.


MSGDIR    <drive:/directory>

The directory for your XBBS message bases.  In case you don't know (and
care), XBBS stores its message areas as two files per area, one of
headers and one of text.  The headers contain pointers into the text
file.  It seemed the best compromise; it's fairly fast, but you don't
have all your eggs in one basket.


MESSAGES  <drive:/directory>

The directory for *.MSGs (if req'd by TONAME entry).  Note that XBBS
doesn't use *.MSGs; this facility is provided to allow you to link
directly to programs that rely on the old, slow, wasteful and, last
but not least, braindead *.MSG format.


LOGFILE   <drive:/directory/filename>

This is the file where XGroup will write informational entries.  XGroup
should maintain enough info there to allow you to implement any type of
vicious bloodsucking echomail cost recovery plan you like :-).


ADDRESS   <FTN address(es)>

An FTN address has the form  "zone:net/node.point@domain"
Examples:
            1:380/100.0@Fidonet 2:4177/1.0@Fidonet 1:380/16.1@Fidonet

Note that XGroup is 5-D and addresses must be complete (actually,
guessing takes place if an incomplete address is encountered.  But at
least the first address *must* be complete so XGroup can have some basis
to guess from).


ARCHIVE   <create archive command>

The command that XGroup will spawn to create an archive.  Simple
example:    ARC mwn


UNARCHIVE <extract archive command>

The command that XGroup will spawn to crack an archive.  Simple
example:    ARC ewn

Something like Polyxarc might be a good idea for this command.


NETAREA   <# of netmail area>

The number corresponding to your XBBS netmail area.  Messages without
AREA: tags are placed here.  Hopefully they're really netmail and not
something some broken software spewed forth in a fit of NIH.


PACKSIZE  <# bytes at which to compress msgs>

The minimum message size to LZSS compress.  1024 bytes is the minimum
you can set this to.  If omitted, no compression will be performed. If
and when to perform compression is a matter of how you use your message
bases.  If diskspace is at a premium and you carry a lot of messages,
you'll probably want to compress.  When you read a compressed message
there'll be a slight pause while the text is decompressed.  So if you
scan areas at high speed picking out good stuff (and actually looking at
the text while doing it; it's easy to scan headers without the text),
you might want to compress while packing the message bases with XMsg
instead of while importing with XGroup, giving yourself the chance to
read before compression occurs (note:  don't worry about it on a fast
machine).  But the choices, compress or not, when to compress, are yours
to make.

If you insist on my recommendation, I'd say compress when XMsg runs, not
when XGroup runs.  But I've got a slow machine.  (Note:  did; have a
486/33 now and run OS/2.  Now I say compress at will.)


XBBSOS2

This OS/2-only keyword tells XGroup to use XBBS-OS/2 conventions when
naming files.  It enables the ROUTE command below.  Note that this
keyword cannot be used under DOS.  Further note that the outbound
directory must be on an HPFS partition as long filenames are used.


NOROUTEPOINTS

Normally XGroup routes mail for points other than your own to their boss
node.  This keyword overrides that action.


ROUTE     <mask> <type> <FTN address or SAME> <archive command>

This is an XBBS-OS/2 only keyword.  It requires an HPFS drive to work.
<mask> is a partial filename mask.  XBBS-OS/2 uses filenames that are
a type-indicating character followed by the destination FTN address.
For instance, a packet destined for 1:380/100.0@Fidonet will be named
P.1.380.100.0.FIDONET in the outbound.  To archive this packet as
Crashmail you might use the following line:

    ROUTE 1.380.100.0.FIDONET C SAME ARC mwn

Note that the "P." or "T." isn't prepended to the filename in the
example; XGroup does that for you.  To hostroute this packet (in fact,
all mail to net 1:380@Fidonet) you might use the following line:

    ROUTE 1.380.*.*.FIDONET N 1:380/1.0@Fidonet ARC mwn

To simply archive and hold all mail (that wasn't processed by previous
route statements -- route statements are processed sequentially) use
something like:

    ROUTE *.*.*.*.* H SAME PKZIP -m

A couple more shortcuts:

To host route all nodes in Zone 2 of Fidonet, use:

    ROUTE 2.*.*.*.FIDONET N HOSTROUTE ARC mwn

To route all point mail to 1:380/16.0@Fidonet's points to the boss node,
use:

    ROUTE 1.380.16.*.FIDONET N POINTROUTE ARC mwn

See also PRIORTOROUTE, NOROUTENET and NOROUTEPOINTS keywords.

You MS-DOS and/or Bink/FD/d'Broke/etc. guys can do routing with another
program, like MakeArc or oMMM.  Note that although domains should work
fine with Bink, XGroup knows nothing about these new-fangled "point
directories" since I quit running Bink before they were invented.  All
that directory hoopla is too damned confusing anyway...


PRIORITY  <#> <#>

This is an OS/2-only keyword.  The first <#> is the priority class
(1-3), the second the priority within that class (0-31).  XGroup will
set its priority accordingly and run at that priority (handy for making
it run at idle class:  PRIORITY 1 31).


NOTINY

Tells XGroup not to use Tiny Seenbys. Since SEEN-BYs are pretty much
useless, even dangerous (they're 2-D), don't use this keyword unless you
have some overriding (read: political BS) reason to do so.  It wastes
space (read: your money on the phone bill, and that of everyone downwind
of you until someone cleans up the mess).  Tiny Seenbys are grudgingly
added to echomail for backward compatibility as the default.


NOFORWARD

Don't forward mail to "foreign" nodes (nodes outside your net).


NOLOCALFORWARD

Don't forward mail to "local" nodes (nodes inside your net).  Please
don't use this without a really good reason.  I have no idea what that
reason might be, but I'm just an ugly American.


FORWARDFILES

Not implemented yet, but remember that groupmail will do it already...


MAXDUPES <# of dupe recs/echo area to keep>

Dupe records require 8 bytes each.  The maximum you can set this to is
8150; the default is 1000.  To turn it off completely use NODUPES.

XGroup uses MSGID kludge lines for dupe checking.  Don't you think we
have too many one-purpose kludge lines?  Just nod like you know what I
mean...

Note:  Maximus 2.0 produces false duplicates (invalid MSGIDs) for many
of it's QWK-imported messages.  Scott Dudley has been contacted and is
working to remedy the situation.


NODUPES

Turns off dupe checking, letting you reclaim the space those XDUPES.*
files take up.


KEEPPATH

Retain ^aPATH lines locally.  Mainly for debugging.  XGroup uses 5-D
^aSPTH lines on forwarded messages.  SPTH lines are located at the top
of the message, not the bottom, and retain their usefulness across zone
and domain boundaries where PATH lines do not, so they can be used for
dupe checking throughout a message's topology (which SEEN-BYs cannot be
used for; PATH lines cannot be used for dupe checking in any case).
Relax; this is backward compatible and won't choke any properly
functioning but ancient mail processor that still uses ^aPATH lines.
For those who doubt it, FTS-0004 clearly states this about the PATH
line:  "This is not a required field."  So if someone complains, tell
them to read FTS-0004 (the FTSC's official echomail "bible") and get
their defective software fixed.

^aSPTH lines have the format:

 <domain><#zone><:net></>node<.point>

Note that ^aSPTH lines are "sticky" and carry the least amount of
information that will convey a full address when coupled with preceding
addresses.  For example, if 1:380/16.0@Fidonet 1:380/16.1@Fidonet,
1:380/100.0@Fidonet, 1:396/100.0@Fidonet, 2:4177/1.0@Fidonet and
2:4177/1.0@Othernet processed a message, in that order, you'd have:

 ^aSPTH: Fidonet#1:380/16 .1 100 :396 #2:4177/1 Othernet

Note that point 0 is assumed if missing and that punctuation *precedes*
an address element except in the case of a domain change (and when the
net element is the first change -- note this dictates that domain names
begin with an alphabetical character).  This compacts SPTH entries as
much as possible for most typical topologies.


KEEPSEENBYS

Retain SEEN-BY lines locally.  Mainly for debugging.  Who would want the
useless things around just to look at?  By default XGroup ditches
SEEN-BY lines (but puts on Tiny Seenbys for backward compatibility with
ancient mail processors, and protection for small fully enclosed
polygons (read: poor topology.  Add an IMHO if offended.)).


KEEPDUPES

Places dupe msgs into AREDUPES.$$$ in the inbound directory for your
inspection (it's a packet).  If you suspect the dupe checker is killing
valid messages, turn it on and take a look.  Chances are you'll kill a
few valid messages if you turn on PSEUDOEIDs, as EIDs don't guarantee
uniqueness the way MSGIDs do (when properly implemented:  see note about
Maximus 2.0 bug at MAXDUPES above).


KILLBADDATES

Causes XGroup to unceremoniously kill messages with non-Fidonet-
compatible date fields (some software is broken; ain't it amazing?)
XGroup "fixes" bad dates as they pass through by padding them to
the proper length with "Q"s, to indicate what probably fouled them
up to begin with.  Note that the node you received the packet from
might not be responsible, and the messages's originating node might
likewise be blameless; some intermediate node's software might be
doing you the favor of screwing up the dates for you.  How nice.  One
might hope that GMD and some *Cs would take note of that simple fact...


ALLOWBADAREAS

Allows echo messages with ^a in front of the AREA: tag to pass through.
Also sends the node that built the packet a message informing them that
their software is (surprise) broken.  The default is to ignore AREA:
tags with ^a in front.  BTW, nodes sending out messages with ^a in front
of the SEEN-BYs also get a nice message from XGroup.  Either of these
conditions are caused by the software that built the packet.  Aren't you
sick of putting up with broken software yet?  (Nod sagely)


MAXTOHIBIT <#>

Sets the maximum number of high-bit (>127) characters that can be in the
To: field of a message before the message is considered grunged.  Set to
100 to disable completely.  Example:
 MAXTOHIBIT 6
Messages with blank To: From: and Subj: fields are always considered
grunged.  I wouldn't use this if you take international echos that allow
extended character sets to be used.


MAXFROMHIBIT <#>

As for MAXTOHIBIT above except that it controls the From: field.


MAXSUBJHIBIT <#>

As for MAXTOHIBIT above except that it controls the Subj: field.


NOROUTENET

If this XBBS-OS/2 routing modifier keyword is used, XGroup will create
T.* packets for netmail instead of P.* packets.  XGroup won't route T.*
packets.  You can rename and route afterwards using a separate control
file/application if desired.


PRIORTOROUTE <OS/2 command>

Lets you run a .CMD file or program before XBBS-OS/2 routing takes place.
This is ignored if routing occurs due to a RO(ute) command line [command].


PSEUDOEIDS

Tells XGroup to calculate pseudo-EID information for messages that don't
have MSGIDs.  It does *not* cause XGroup to put EIDs in messages.  I
recommend against using this; it can (and probably will) declare
messages as dupes that aren't (even though the poor messages may be
blameless) due to the flawed method used.  What method is that?  The
same one that QMail, Squish, Confmail, etc. use...


ACKNOWLEDGERRQ

XGroup will send a receipt for any netmail messages received with the
MSGRRQ (return receipt request) bit set.  The default is not to send
receipts, but HeadEdit will let you send them manually.


CHECKSEENBYS

Don't use this unless you're involved in a Fully Connected Topology.
Even then, attempt to fix your braindead topology first.  Not
recommended except as a last gasp.  Remember:  SEEN-BYs must die.
Ramsey Campbell told me so.


PVTECHOASNET

Export echomail messages marked Private as netmail instead of echomail.
HeadEdit allows other methods of replying by netmail to an echomail
message, so this normally isn't used so that private messages can be
allowed in echomail areas (in case someone has a use for them).


GRUNGEATTEMPTS

Number of times to attempt to resync with a grunged packet before giving
up. Default is 25 attempts, minimum is 10, maximum is 65534.


TONAME <"to name"> <ROUTE or PROG (OS/2 only) or MSG> [FTN address or prgname]

This allows messages addressed to a certain name to be treated
specially. Only TONAME "to name" MSG and TONAME "to name" ROUTE
<address> are available under DOS.  Under OS/2 you can also spawn a
detached process to act on the message.  In this case XGroup first
creates a *.MSG containing the message, then spawns the detached process
with the *.MSG's filename as an argument.

Examples:
    TONAME "AREAFIX" MSG
    TONAME "John Doe" ROUTE 1:380/16.65500@Fidonet
    TONAME "Route Request" PROG ROUTER.EXE


ECHO      <tag> <#> [<FTN address(es)>]

ECHO prefaces information that tells XGroup about an echo.  <tag> is the
"name" of the echo (what follows the AREA: tag; i.e. FLAME for
AREA:FLAME or C_ECHO for AREA:C_ECHO).  You can get this information
from your echomail link.  <#> is the number of the XBBS message area
that this echo is tied to.  The <FTN address(es)> are your links for the
echo (where you get it from and anyone you give it to).

Note that XGroup is a "secure" echo processor.  It won't import mail
from anyone not listed as a link.  If you get mail from someone you
shouldn't it's stored in INSECURE.$$$ (a packet) in the inbound area.
If it's from someone you forgot to add to the links, add them, rename
INSECURE.$$$ to INSECURE.PKT and rerun XGroup.  Otherwise, better think
about passwording out the node in question.

The exceptions to secure processing are "read-only" echo areas.  This
is any area with no forwarding nodes listed.  Also handy for importing
local areas from a mailerless point.  Messages will never be scanned
or forwarded from a read-only echo area.

Examples:
    ECHO  UGH       12 1:380/100.0@Fidonet 1:380/20.0@Fidonet 380/5
    ECHO  SCHWARTZ  32 2:4177/1.0@Fidonet 1:380/16.12@Fidonet
    ECHO  READ_ONLY 51


GROUP     <id> <#> <numdays> <FTN address or !topstar option>

GROUP prefaces information that tells XGroup about a groupmail
conference.  <id> is similar to ECHO's <tag>; it's the AREA: name of the
conference which you can obtain from your uplink.  <#> is the XBBS
message area associated with the conference.  <numdays> is the number of
days that you want to keep downbound groupmail bundles available for
update request by your downlinks.  XGroup <ctlfile> C cleans up the
groupout directory based on these numbers.  The final data item is the
address of your uplink or, if you're the topstar for a conference, the
"topstar option:"

    [F]ully moderated, [P]artially moderated, [N]o moderation
    (only use first letter)

Fully moderated conferences are never exported from unless you use the
"XGroup <ctlfile> E F" command line.  Partially moderated conferences
are never exported from unless you use the "XGroup <ctlfile> E P"
command line. Non-moderated conferences behave "normally," they export
without a special command line option.

Examples:
    GROUP XBBS     7  1:380/100.0@Fidonet
    GROUP MOJO     25 !N ;we're the topstar for this one


That's a lot of info.  If you need a reminder, type XGROUP ? | MORE




 More BS...

If you have a bug report or suggestion, here's where to reach me.  If
you have a flame for me, sit on it.  What do you expect, a refund?

Note that support, such as it is, is on your nickel.  Poll for answers
a few days after leaving a question (or send an SASE or whatever).  The
program is free; don't expect me to foot the bill for support.

Hope you find XGroup useful.  It was kind of a kick to write, in a
masochistic sort of way.




M. Kimes
542 Merrick
Shreveport, LA  71104
(318)222-3455 data