ARCDIAG

                          ARCNET DIAGNOSTIC PROGRAM

                                 USER GUIDE



                                Version 2.5







                                For use with
                       Novell Netware/SM/RX Type Networks
               











                       (c) Copyright 1986, 1989, 1990, 1992
                                     by
                             Olympic Software Co
                                8424 Warner Rd
                              Saline, MI  48176
                               (313) 996-5750

                        All Rights Reserved Worldwide


The information in this document is subject to change without notice and 
should not be construed as a commitment by Olympic Software Co.  Olympic 
Software Co. assumes no responsibility for any errors that may appear in 
this document.

The software described in this document is furnished under license and may 
only be used or copied in accordance with the terms of such license.



                      COPYRIGHT NOTICE AND LICENSE 
 
This  document; other  accompanying  written and  disk-based  notes  and
specifications; and all referenced and related program files, demonstration 
code and  object modules  accompanying  this  document are  copyrighted by 
Olympic Software.   The copyright owner hereby  licenses you to:  use the  
software; make as many copies of the software and documentation as you wish;
give exact copies of the original to anyone; and distribute the software and 
documentation in its unmodified form via electronic means. There is no charge
for any of the above. 
 
This is not free software.  This license allows you to use this software 
without charge  for a period of 30 days.  In order to include this software 
as part of any product, either commercial, shareware, freeware, or public 
domain, registration is required. Any such use of the Arcdiag product is in 
violation of federal copyright laws and will be prosecuted. 
 
No copy  of the  software may  be distributed  or given  away without  this
accompanying documentation; this notice must not be removed. 
 
                    DISCLAIMER OF ALL WARRANTIES                            

There is no warranty of any kind associated with this software, and the 
copyright owner is not liable for damages of any kind.  By using this 
software, you agree to this.  Every effort has been made by Olympic Software 
to make this product bug-free.   However, the nature of software development
is that it is impossible to guarantee bug-free software. 
 
                           REGISTRATION 
 
Upon receipt of the appropriate registration fee,  Olympic Software will send
the user a disk containing a version of Arcdiag without the shareware 
registration screen,  and entitle him to full telephone support. 
 
            BULLETIN BOARDS, USERS GROUPS AND DISK VENDORS 
 
No Bulletin Board, User Group or Disk Vendor that charges any fee for access 
or disks may distribute Arcdiag without completing the application form 
below.  Free, public access bulleting boards may distribute Arcdiag with no 
written permission, but are encouraged to send the application form, in order
to receive the latest version of the product. 
 
Operators of Bulletin Boards may receive an official copy of Arcdiag, its
documentation, and all related materials in archived form, by completing the
application form below, and returning it to Olympic Software. You must
provide free access to your BBS for you to receive this disk. This will also 
entitle you to free upgrades of the product. 
 
Non-Profit Users Groups may distribute unregistered copies of Arcdiag, as 
long as the group charges no more than $10 per disk.  To receive 'official' 
master copies of Arcdiag and automatic updates, please fill in and return 
the application form below.  You should add Olympic Software to your group's 
mailing list, and send a copy of your group's newsletter (if applicable). 


For-Profit disk vendors may distribute unregistered copies of Arcdiag, 
providing they return the application form below, pay a $10 fee for the 
master disk, shipping and handling, AND THE VENDOR MUST HAVE ATTAINED 
ASP-APPROVED STATUS. 

Olympic Software must be placed on the vendor's mailing list, and receive 
all promotional and advertising materials with the application.

UNDER NO CIRCUMSTANCES MAY ARCDIAG BE DISTRIBUTED WITHOUT THIS COMPLETE 
DOCUMENTATION FILE, ALL PROGRAMS, AND OTHER MATERIALS PROVIDED WITH THE 
OFFICIAL COPIES FROM OLYMPIC SOFTWARE.  ANY SUCH DISTRIBUTION OF ARCDIAG
OR ITS RELATED FILES, EXCEPT AS PROVIDED FOR IN THIS LICENSE, SHALL BE 
DETERMINED TO BE IN VIOLATION OF FEDERAL COPYRIGHT LAWS AND WILL BE 
PROSECUTED. 


INTRODUCTION

The ARCDIAG program is designed to be a service tool for network
administrator personnel for a network that uses ARCNET type hardware (see
specifications section for compliance).   The ARCDIAG.EXE program includes
two diagnostic sections that will help during installation of an ARCNET net-
work.  The diagnostic software can be operated at any workstation during
installation of the network or at any time while running the Novell Network
Operating System.

       NOTE: The ARCDIAG program is not intended to isolate
       Novell Software problems except in those cases where the
       physical network hardware is the prime cause of the
       problem.

The program exercises the network card by testing all of its internal functions,
RAM, RIM etc., and then displays a map of active nodes and packet counts. 
The latter also provides an indication of any reconfiguration that might be
occurring.

START UP

   The program can be run from the DOS prompt by typing:

       ARCDIAG  [-mxxxx] [-ixxxx] [-ffile descriptor] [-ttype] [-b] 

       Start Up Options:

           -b          Option for removing the preliminary board test.

           -ffile descriptor
                       Option for specifying the location of the logical
                       name file - ARCDIAG.DAT.  40 characters
                       maximum. (Registered version only).

           -ixxxx      Option for operating ARCDIAG at an I/O address of
                       xxxx (hex). ARCDIAG defaults to 02E0 (hex).  Must
                       use all 4 digits (Registered version only).

           -mxxxx      Option for operating ARCDIAG at a RAM memory
                       location of xxxx (hex).  ARCDIAG defaults to D000
                       (hex).  Must use all 4 digits. (Registered version
                       only).

           -q          Option allows board test only operation.  Place
                       [ARCDIAG -q] in the AUTOEXEC.BAT file for
                       automatic test of ARCNET card on power up.  If
                       an error condition is detected, the nature of the
                       error is displayed and the DOS error level is set
                       to 1.  Otherwise, nothing is displayed, and the
                       DOS error level is kept at 0.

           -ttype      Option for selecting different network interface cards. 
                       ARCDIAG defaults to standard SMC type cards with
                       memory mapped RAM and I/O mapped RIM
                       controllers.  (Registered version only). Use -t2 for
                       memory mapped cards such as Thomas Conrad in enhanced
                       mode.


ArcDiag will function in the file server or any work station, providing there
is a floppy drive available.  Work stations with no local file storage that use
boot proms to load Novell can not perform boards tests.

The ARCDIAG.EXE file may be copied onto and executed from the network hard 
disk, but keep in mind that board testing is disabled if the Novell Shell 
is loaded.

Type ARCDIAG at the DOS prompt of the drive containing ARCDIAG,
whereupon, if the Novell Shell is not loaded, the board test screen shown in
Figure 1 will appear:

  Map      Count     Names    Format     Board     Print     Reset     Quit    
+------------------------------------------------------------------++---------+
| Dec   1   2   3   4   5   6   7   8   9  10  11  12  13  14  15  ||         |
|   +--+---+---+---+---+---+---+---+---+---+---+---+---+---+---+--+||         |
|  0+                                                             +||---------|
| 15+    Network Board Test                                       +|| Rcn/Min |
| 30+                                                             +||         |
| 45+    PASSED: RAM test                                         +||---------|
| 60+    No Network Boot PROM Found                               +|| Station |
| 75+    PASSED: Internal RIM Test                                +||         |
| 90+    PASSED: Physical node address is 2                       +||---------|
|105+    PASSED: POR test                                         +|| Address |
|120+    PASSED: ETS test                                         +||         |
|135+                                                             +||---------|
|150+                                                             +|| Packets |
|165+                                                             +||         |
|180+                                                             +||---------|
|195+                                                             +|| Recnfgs |
|210+                                                             +||         |
|225+                                                             +||---------|
|240+                                                             +|| ActNode |
|   +--+---+---+---+---+---+---+---+---+---+---+---+---+---+---+--+||         |
+------------------------------------------------------------------++---------+
        ARCDIAG V2.4             Copyright Olympic Software  1989              

        Figure 1 - Board Test Screen

BOARD TESTS

Unless option [-b] is included in the startup command, the board test
function automatically begins when entering [ARCDIAG] at the DOS
prompt.  

Board Types
       ARCDIAG has been set to function on most Arcnet boards,
       with the exception of Nestar.  

       By including [-ttype] in the command line as a start up option,
       different board types may be selected, e.g. [-t1], [-t2], etc.  Following is
       an example of the command line:

           ARCDIAG [-mxxxx] [-ffile descriptor] 
           [-ttype]

       [-t1] is the default and is used for most Arcnet cards that use memory
       mapped RAM and I/O mapped RIM controllers such as SMC,
       Novell, Earth, etc.  


       [-t2] is used for memory mapped RIM controllers, such as Thomas
       Conrad, Arcmaster, etc.  When the [-t2] option is used, the [-I] option
       is disabled.  

       [-t3] is used for SMC type PC500 and PC550.  Use the [-I] option to
       configure I/O mapping if other than 2E0.

           Example:  To select a Thomas Conrad 6054 16 bit card
           at D000 hex, enter the following command line:

              ARCDIAG -mD000 -t2


           Note:  If you do not know the option codes for
           your board, contact Olympic Software Co., (313)
           996-5750.  

   The following tests are made during the board test phase:

       NOTE:  WHEN ARCDIAG IS FIRST EXECUTED, BOARD TESTING IS
       DISABLED IF THE USER HAS ALREADY LOADED THE NOVELL SHELL.

RAM TEST
   ARCDIAG exercises the ARCNET board's RIM RAM.  All 2K of RAM are tested 
   for shorted and open bits.  Also, the address lines are tested.  

   An error message is displayed if the RAM fails the test or if the DIP
   switch setting of the memory address set is incorrect. 

   A PASSED message is displayed if operation is verified.

NETWORK BOOT PROM TEST
   This test indicates whether or not a network boot PROM is installed.

RIM TEST
   The token controller IC (9026) is tested in the RIM test.  The network 
   microprocessor (9026) can perform its own internal diagnostics. 
   When the test is run, approximately 95% of the processor's operations are
   exercised.  If this test fails, replacement of the network card is
   recommended if it is verified that the I/O address DIP switches are set
   correctly.  

   A PASSED message is displayed if operation is verified.

SID TEST
   During the SID test, the Controller source ID is located and read.  The 
   returned value from this test is the station node address.  The test will 
   fail if it is at zero.  If failed, make sure the address switches are set
   to an address greater than zero.  

   A PASSED message is displayed if operation is verified.

ETS TEST
   The ETS test verifies the proper location of the (E)xtended (T)imeout 
   (S)etting jumper.  Newer ARCNET cards may not have a jumper.  Therefore, 
   the card needs to be replaced if an error occurs.  

   A PASSED message is displayed if operation is verified.


POR TEST
   During this test, a power-up cycle is activated and verified.  The 9026 
   RIM processor is reset and the ARCNET card is placed into an operational 
   state.

After performing all of the above tests, the program will halt for approximately
three seconds, then cycle into the Network Tests.

The Board Tests may be continued by selecting [Board] from the Lotus-type
menu at the top of screen, or by merely pressing [B].  


NETWORK TESTS

Network tests function both in and out of the Netware shell.  However, the file
server and workstations can be tested only if they are powered on.  

The Network Test Grid shown in Figure 2 appears after ArcDiag has been
started and the Board Tests are completed.

   Map      Count     Names    Format     Board     Print     Reset     Quit    
 +------------------------------------------------------------------++---------+
 | Dec   1   2   3   4   5   6   7   8   9  10  11  12  13  14  15  || 6/24/90 |
 |   +--+---+---+---+---+---+---+---+---+---+---+---+---+---+---+--+|| 8:30:23 |
 |  0+ FS1  .  MGR  .   .   .   .   .   .   .   .   .   .   .   .  +||---------|
 | 15+  .   .   .   .   .   .   .   .   .   .   .   .   .   .   .  +|| Rcn/Min |
 | 30+  .   .   .   .   .   .   .   .   .   .   .   .   .   .   .  +||    0    |
 | 45+  .   .   .   .   .   .   .   .   .   .   .   .   .   .   .  +||---------|
 | 60+  .  TST  .   .   .   .   .   .   .   .   .   .   .   .   .  +|| Station |
 | 75+  .   .   .   .   .   .   .   .   .   .   .   .   .   .   .  +||    2    |
 | 90+  .   .   .   .   .   .   .   .   .  LAB  .   .   .   .   .  +||---------|
 |105+  .   .   .   .   .   .   .   .   .   .   .   .   .   .   .  +|| Address |
 |120+  .   .   .   .   .   .   .   .   .   .   .   .   .   .   .  +||    3    |
 |135+  .   .   .   .   .   .   .   .   .   .   .   .   .   .   .  +||---------|
 |150+  .   .   .   .   .   .   .   .   .   .   .   .   .   .   .  +|| Packets |
 |165+  .   .   .   .   .   .   .   .   .   .   .   .   .   .   .  +||         |
 |180+  .   .   .   .   .   .   .   .   .   .   .   .   .   .   .  +||---------|
 |195+  .   .   .   .   .   .   .   .   .   .   .   .   .   .   .  +|| Recnfgs |
 |210+  .   .   .   .   .   .   .   .   .   .   .   .   .   .   .  +||    0    |
 |225+  .   .   .   .   .   .   .   .   .   .   .   .   .   .   .  +||---------|
 |240+  .   .   .   .   .   .   .   .   .   .   .   .   .   .   .  +|| ActNode |
 |   +--+---+---+---+---+---+---+---+---+---+---+---+---+---+---+--+||    4    |
 +------------------------------------------------------------------++---------Ù
         ARCDIAG V2.4             Copyright Olympic Software  1989              

         Figure 2 - Network Test Grid

Each dot on the grid represents a node.  As noted by the cursor rapidly moving
across the grid, the program polls all 255 nodes.  When a file server or
workstation is powered on, the node number or node name will be displayed in
the place of the dot.  


INFORMATION WINDOWS
       Information from the network diagnostics is provided in the windows
       on the right side of the screen.  The first window contains current
       date and time.  Following is a description of the information 
       contained in the other windows.

       RCN/MIN
           Indicates the number of reconfiguration per minute, relative to
           (1) the number of stations being powered on or off of the
           network, and (2) any type of fault condition occurring on the
           network.  

           This information may be used as a gross indication of network
           fault conditions (see "Recnfgs" below).   

       STATION
           If the Novell shell is running, the station number on which
           ARCDIAG is running is displayed in this window.  This number
           may be referenced to the station number which appears on the
           file server monitor.  

           If the shell is not loaded, the message "No Shell" is displayed.

       ADDRESS
           The physical address, or the dip switch setting, on the network
           interface card.

       PACKETS
           The number of packets that have occurred on the network since
           the last reset.  This information indicates relative network
           activity.

       RECNFGS
           Reconfiguration bursts are counted accumulatively and displayed
           in this window.  Reconfiguration bursts increment whenever any
           of the following occur: 

               1.  a workstation is powered onto the network.
               2.  a workstation is powered off of the network
                   (intermittent).
               3.  a network card is faulty.
               4.  the network connecting cable is faulty.

           A rapidly increasing reconfiguration count indicates a faulty
           network (refer to "Network Troubleshooting, Network Tests").

       ACTNODE
           The number of nodes that have powered onto the network.  


FUNCTION SELECTION

   At the top of the Network Test screen is a "Lotus" type menu for selecting
   various functions, such as "Map," "Count," "Names," etc.  To select a
   particular function, either move the cursor key to highlight the function
   and press [Enter], or merely type the first letter of the function label, 
   e.g. [M] for the "Map" function.  

   Note that a "help" statement, corresponding to each function, appears at 
   the bottom of the screen whenever a function is highlighted.  


   MAP
       Selection of this function displays all nodes on a grid, each node 
       being indicated by a dot.  The number range is from 1 to 255.  The 
       display is arranged in a matrix form.  Nodes are displayed 15 at a 
       time along the horizontal.  Therefore, nodes 1 through 15 are 
       displayed on the first line, nodes 16 through 29 on the next line.  

       Stations that are powered on are indicated by a node number or node
       name, in the place of a dot.

   COUNT
       In this mode, packets from each station are monitored and displayed
       on the grid.  Packet counts can be viewed as an indication of activity
       from each node.  Those nodes that transfer packets most frequently
       will increment the packet count much more rapidly.  

       Although the program is not fast enough to catch all packets, relative
       packet increases are displayed.  Therefore, the nodes that are assigned
       as fileservers should have packet counts increasing at a faster rate 
       than workstations.

   NAMES
       Any of the 255 nodes can be given an alpha-numeric designation
       which is useful for quick recognition of node locations.  

       These logical names can be assigned to physical node numbers by
       using the "Names" function.  For example, a file server that might be
       located on node 1 may be given the logical designation "FS1".  

       When selecting the "Names" function, the following message will
       appear at the bottom of the screen:

         Enter node number (1 to 255):

       At the blinking cursor, enter the number of the node to which you
       want to give a logical name, then press [Enter].  The following
       message will then appear:

           Enter name (3 char max):

       At the blinking cursor, enter a maximum of three characters and press
       [Enter].  You will then be asked:  


           Save (y/n) <return = yes>

       If your entry is correct and you want to save it to the ARCDIAG.DAT
       file on the disk, press [Enter], since "Enter" or "Return" is the 
       default. Otherwise, press [N] to ignore the entry.  

       The program uses the file ARCDIAG.DAT to store logical names for
       physical node numbers.  

       The ARCDIAG.DAT file can be located in either the default drive or
       when connected to a Novell network it can be located in the Z:
       (public) directory.  Optionally a command line argument (-f) can be
       used to tell ARCDIAG where to locate and what name to use for the
       logical name file (see "Start Up Options").


   FORMAT
       Physical node numbers can be displayed on the node map as either
       decimal, octal  or hexidecimal numbers.  The current mode of
       operation is displayed in the upper left hand corner of the display.  

       Pressing the [Enter] key more than once will toggle the display mode
       between decimal, octal and hexidecimal.  

   BOARD
       This function runs diagnostics on network interface cards.  In order
       for the board diagnostic test to operate, however, ARCDIAG cannot
       be running in conjunction with the Novell operating system. 

       When this test is initiated from the menu at the top of the screen, it
       will continue until the space bar is pressed or until an error is
       found.

   PRINT
       If an IBM graphics compatible printer is available, use PrtSc to
       produce an exact copy of the map including graphic borders.

       If an IBM graphics compatible printer is not available, or if you want
       to label and date the node map, select the "Print" function on the
       menu, whereupon the following statement will appear at the bottom of
       the screen:

                Enter map name:

       Type a name for the map, then press [Enter].  A node map with time
       and date stamp will be sent to the printer.  All borders are converted
       to characters that can be printed on any type of printer.  

       The printing program does not send a form feed character at the end
       of printing allowing two maps to be printed on one 8 1/2 by 11 inch
       piece of paper.

  
   RESET
       Select this function to reset all counters to zero and reformat 
       the grid.

   EXIT
       Select this function to exit the program.  




SPECIFICATIONS

   RIM RAM Base Address
           D000 (hex) segment default  - configurable at runtime

   Board I/O Address
           02E0(hex) default - configurable at runtime

   Interface Types
           8 bit cards with Standard Microsystem interface (type 1)
          16 bit cards with Thomas Conrad interface (6045)	(type 2)
          16 bit cards like Standard Microsystms PC500/550 (type 3)

   Active Nodes Displayed
           1 thru 255

   RIM RAM size
           2K bytes

   Computer Compatibility
           IBM PC/XT/AT or compatible Network Operating Systems
           Novell Netware 4.61 and above.  Novell Advanced Netware 1.02
           and above.  Does not perform reliably when executing a board test
           on a non-dedicated fileserver running ELS ver 1.0.


NETWORK TROUBLESHOOTING

Board Tests

Symptom            Corrective Action

RAM Test Fails 
                       Check network card memory address DIP
                       switches for proper settings.
  
                       RAM defective, replace card.

RIM Test Fails 
                       Check network card I/O address DIP switches for
                       proper settings.

                       9026 RIM controller defective, replace card

SID Test
                       The SID address should display the node address. 
                       Note:  Do not allow two network cards to have the
                       same physical address. 

ETS Test Fails
                       Newer network card does not have a jumper for
                       extended timeout.  Therefore, if this test fails, the
                       board needs to be replaced.
POR Test Fails
                       Before, continuing, remove the network cable and
                       try again.  If the test still fails, the network card
                       needs to be replaced.  Disconnecting the cable
                       removes any type of external interference with the
                       test.




Network Tests

Symptom                Likely Cause

Reconfiguration 
counter increments 
continuously
                       (1) no other nodes are connected to the  local
                       network card.
                       (2) the cable network is defective from the local
                       card to the rest of the network.
                       (3) an active or passive hub port is defective.


Multiple "phantom" 
nodes are 
displayed
                       (1) two nodes have been set to the same  address.
                       (2) a cable connection is not making solid contact.
                       (3) the memory address DIP switches are set
                       incorrectly.
                       (4) -i or -m options have been set incorrectly.

When run with Novell
shell - local node is
not displayed
                       Nothing is wrong with the display.  The Novell
                       shell has not passed the proper physical node
                       address to ARCDIAG.  Works correctly when not
                       running with the shell.  Fixed in Novell Advanced
                       Netware 2.0 and above.


ARCDIAG shows OK, but
cannot "find fileserver"
when shell is run
                       Make sure the interrupt jumper is used for all
                       network cards used with Advanced Netware 1.02
                       and above.  


      OLYMPIC SOFTWARE LICENSE AGREEMENT


License
     Olympic Software owns the enclosed software program ("Program") and all 
     copyrights and other rights and interest in such program.  Olympic 
     Software grants you a non-exclusive license to use the enclosed Program 
     subject to the terms and restrictions below.

Restrictions on Use
     You may use the program only on a single fileserver.  You may not use 
     the Program on a single user computer.  You may modify the Program or 
     merge it into any other program but all such portions remain subject 
     to the restrictions of this license.

Restrictions on Copying
     The Program and documentation are copyrighted and may only be copied 
     as permitted by this license.  You may copy the machine readable form 
     of the Program only for back-up or archive purposes, provided that nor 
     more than three(3) copies are in existence at any one time without 
     prior written consent from Olympic Software.  You must maintain a 
     record of the number and location of all such copies.  You must include 
     the Olympic Software Copyright notice on any copy, modification or 
     merged portion.   You may copy the documentation which is provided in 
     printed form with the program.

Restrictions on Transfer
     You may physically transfer the program from one of your own computers 
     to another as long as the matching key card is transported also.  You 
     may not distribute copies of the Program to others.  You may transfer 
     this license together with all originals, copies, modifications, and 
     merged portions of the Program and documentation, provided that the 
     person to whom you transfer agrees to be bound by the terms of this 
     license and notifies Olympic Software in writing.  You may not use, 
     copy, print, or transfer the program or documentation, except as 
     explicitly allowed by this license.

Term
     This license continues in effect until terminated.  You may terminate
     this license only by destroying all originals, copies, modifications,
     and merged portions of the Program and documentation, in any form.  It 
     will also terminate if you fail to comply with any term or condition of
     this license.  You agree upon such termination to destroy the Program 
     and documentation together with all copies, modifications, and merged 
     portions in any form.


No Warranty of Performance
     OLYMPIC SOFTWARE MAKES NO WARRANTIES, EITHER EXPRESSED OR IMPLIED, AS TO
     THE QUALITY, PERFORMANCE OR MERCHANTABILITY OF THIS PROGRAM, NOR AS TO 
     THE FITNESS FOR ANY PARTICULAR PURPOSE OR PARTICULAR RESULTS OBTAINED
     THROUGH USING THE PROGRAM.  YOU ACCEPT THIS PROGRAM "AS IS" AND ASSUME
     ALL RISK OF DEFECTS AND ALL COSTS OF SERVICING, REPAIRS AND CORRECTIONS.

Limited Warranty on Diskettes
     Olympic Software  warrants the original magnetic diskette on which the
     Program is recorded to be free from defects in material and faulty
     workmanship under normal use and service for a period of ninety (90)
     days from the date you receive it.  If, during this ninety day period,
     such a defect should occur, you may return the diskette to Olympic
     Software or an authorized Olympic Software dealer for a replacement 
     diskette at no charge, provided that you have previously returned the 
     enclosed Registration Form or send a copy of your receipt for the 
     Program.  Replacement of the diskette is your sole and exclusive remedy.
     Olympic Software assumes no responsibility under this limited warranty
     for, and will not replace, any diskette with defects due to accident,
     abuse or misapplication. Olympic Software makes this warranty to you as
     the original license only, and not to anyone to whom you transfer this
     license and Program.  This limited warranty gives you specific legal
     rights, and you may also have other rights which vary from state to
     state.

Limitation of Liability
     OLYMPIC SOFTWARE WILL NOT BE LIABLE FOR ANY DIRECT, INCIDENTAL, OR 
     CONSEQUENTIAL DAMAGES RESULTING FROM THE USE OF THE PROGRAM, EVEN IF
     OLYMPIC SOFTWARE HAS BEEN ADVISED OF THE POSSIBILITY OF SUCH DAMAGES.
     SOME STATES DO NOT ALLOW THE EXCLUSION OR LIMITATION OR DIRECT, 
     INCIDENTAL OR CONSEQUENTIAL DAMAGES, SO THE ABOVE LIMITATION MAY NOT 
     APPLY TO YOU.  THIS LICENSE IS THE COMPLETE AND EXCLUSIVE STATEMENT
     OF THE AGREEMENT BETWEEN YOU AND OLYMPIC SOFTWARE.  ALL OTHER 
     COMMUNICATIONS AND AGREEMENTS, WRITTEN AND ORAL, ARE SUPERSEDED.