TESTNET
                      Utility for Testing NetBIOS Networks
                               November 13, 1989
                           CROSS Information Company

          Forward.
          Several NetBIOS networks are not very stable and do not
          provide a correct NetBIOS emulation. This utility will allow
          one to test the network to verify that MCOM, UCOM, and
          NETDEV will operate correctly within the network environ-
          ment. Using this utility, one can simulate modem I/O over-
          night to verify that the network will not "hang up" on the
          procedure and that the systems involved will not crash.

          Using TESTNET.
          Find some workstation on your system that has a communica-
          tions adapter port (COM port). You must use a COM port even
          though you normally intend to use internal modems. Verify
          that the COM port operates correctly by using any ordinary
          "smart-terminal" program to access the port. You can do this
          by connecting a lead between the RS-232C terminals 2 and 3.
          This connects the transmit and receive leads together. When
          you type something on the keyboard, it should immediately
          echo on the screen. If your "smart-terminal" program does
          not echo characters, it probably means that the IRQ (inter-
          rupt request) lines are not enabled on the communications
          adapter card. Verify that COM1 uses IRQ4 and COM2 use IRQ3.
          After you have your communications adapter port operating
          correctly, leave the jumper between terminals 2 and 3 of the
          RS-232C connector and then load MCOM on the workstation.

          Using any other workstation on your system, execute TESTNET.
          The program should find the "COMM01" device and begin to do
          I/O with the MCOM device-driver.

          ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
          º TESTNET  NetBIOS Network Testing Utility  V1.01 º
          º  Copyright (c) 1989  Cross Information Company  º°°°
          º   All rights reserved worldwide.   Ser  12345   º°°°
          º   Phone (303) 444-7799    FAX (303) 444-4687    º°°°
          º                                                 º°°°
          º   Check network : Okay                          º°°°
          º        Add name : Okay                          º°°°
          º       Call name : Okay                          º°°°
          º       Send data : Okay                          º°°°
          º    Receive data : Okay                          º°°°
          º      Check data : Okay                          º°°°
          º   Send datagram : Okay                          º°°°
          º   Recv datagram : Okay                          º°°°
          º      Last error :                               º°°°
          º    Total errors : 0                             º°°°
          º      Total data : 12,799,872                    º°°°
          º         Hang up : Okay                          º°°°
          º     Delete name : Okay                          º°°°
          ÇÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¶°°°
          º Re:0000 Ab:004A Co:004F Tx:0FE1291A Rx:0FE11A9B º°°°
          ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼°°°
             °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°






                                     - 1 -

                                                        TESTNET Page 2


          You can also force a specifc device-driver to be called. You
          put it's name on the command-line:

                TESTNET COMM01  (Calls device COMM01)
                TESTNET COMM02  (Calls device COMM02)

          The following errors can be returned by TESTNET:

          Bad local session number:
                An error occurred within NetBIOS that forced the
          termination of a session. No such information was reported
          to TESTNET by NetBIOS so the very first indication that a
          session had been aborted was when NetBIOS refused to accept
          any more commands from the local session number.

          Can't cancel command:
                An attempt was made to cancel a command that had
          either already completed or was not allowed to be canceled.
          Because TESTNET only cancels one command (the CALL, if
          COMM01 is busy), and since the cancel is legal, If you get
          this error, your NetBIOS is returning errors not intended
          for TESTNET.

          Can't find name:
                A CALL was made to a named device but there was no
          response from the device. Either the device does not exist
          or it was busy. This is normal if you don't have the MCOM
          driver installed on a net-station somewhere on the local
          network.

          Command canceled:
                A CANCEL command was executed successfully. This
          should not appear because TESTNET does not issue any CANCEL
          commands after a session has been established.

          Command not canceled:
                A CANCEL command failed to execute properly. TESTNET
          does not issue any cancel commands after a session has been
          established.

          Command timed out:
                A timeout on a RECEIVE or SEND command occurred. If a
          timeout occurs during a send, the session is aborted. Time-
          outs during receive are normal if there are no data being
          received.

          Data error:
                The data received were not exactly the same as the
          data sent.

          Duplicate name:










                                     - 2 -

                                                        TESTNET Page 3

                An attempt was made to ADD NAME when the name was
          already in use. Since TESTNET always uses a new unique-name
          obtained by converting the system timer-tick into a hexa-
          decimal character string, no duplicate names are possible
          unless more than one copy of TESTNET is executing on the
          network at one time.

          Illegal buffer length:
                The length of either an output or input buffer was too
          long for the command. Since TESTNET always uses the correct
          buffer-length which is fixed, not a variable, this error
          should never occur.

          Illegal name-number:
                The session was aborted. The name-number no longer
          exists. Something caused the session to be aborted. The fact
          that the session had been aborted was not transmitted to
          TESTNET so it continued to attempt to communicate with the
          MCOM driver. The result was this error-code being returned.
          A properly designed NetBIOS would inform a session that
          communication has been lost so this error would never occur.

          Incompatible remote device
                Some hardware on the network is not responding cor-
          rectly when addressed. This can be caused by noise on the
          network.

          Interface busy:
                A SEND or RECEIVE command encountered a very busy
          network. The commands will be retried.

          Invalid command:
                Some data-corruption has occurred, destroying the
          network control-block. This is usually caused by a stack
          overflow. Entering STACKS=15,255 in the CONFIG.SYS file may
          help.

          Invalid NCB_LANA_NUM:
                Two NetBIOS programs are resident in memory. The wrong
          one is being addressed. Check your network configuration.

          Local session table full:
                Two many sessions have already been started. There is
          no more room. Reconfigure the network with more sessions
          defined. This can also happen when NetBIOS pretends to
          delete a name from the local name-table while in fact the
          name remains, using a necessary slot.

          Locator not responding:
                The master station (if any) has gone off-line. If you
          don't have a master-station the error-code probably means
          that the CALLed name can't be located.










                                     - 3 -

                                                        TESTNET Page 4


          Message incomplete:
                Data during a RECEIVE has been truncated because of a
          buffer overflow. This can happen if the network is very busy
          and the data-buffer length in the network configuration was
          not correctly chosen. The buffer length is normally a
          multiple of 1k (1024 bytes).

          Name conflict detected:
                An attempt was made to ADD NAME to the local session
          table when the name was in use somewhere else on the net-
          work. Since TESTNET guarantees a unique name, this should
          never happen unless TESTNET is executing somewhere else on
          the network.

          Name de-registered
                An attempt was name to DELETE NAME from the local
          session table while a command was outstanding. When the
          command completes, the same should be deleted. Experience
          shows that the name will never be deleted and you will have
          lost a slot in the name-table.

          Name deleted:
                A CALL or HANGUP command was made to a name that was
          already deleted. This could happen if a net-station has gone
          off-line forcing a session to be terminated.

          Name is in use:
                An attempt was made to ADD NAME to the local session
          table when the name is in use locally.  Since TESTNET
          guarantees a unique name, this should never happen unless
          TESTNET is executing somewhere else on the network.

          Name not found:
                The CALLed name was not present probably because MCOM
          was not loaded on a net-station.

          Name table full:
                No more slots are available in the local session
          table. Reconfigure the network and then re-boot.

          NetBIOS not active:
                NetBIOS was not loaded or not responding.

          No resource available:
                Too many TSRs are using resources that are necessary
          for the network to operate properly. Notice than some pro-
          grams take-over the system's timer-interrupt and therefore
          don't allow the network software to get any CPU time. Other
          programs actually destroy any interrupt vectors that exist.
          Such programs can't be used in a networking environment. To
          find such programs, attempt to operate with no TSRs on the










                                     - 4 -

                                                        TESTNET Page 5

          net-station. Add each TSR until you find the one that des-
          troys your system.

          Program is corrupt!
                The program file was damaged or changed. Obtain a new
          copy from the distribution disk. If the program is altered
          in any way this message will appear.

          Reserved name specified:
                Data corruption occurred causing the presence of
          reserved characters "*" in the name-field.

          Session closed:
                An error occurred which forced the session to be
          aborted.

          Session ended abnormally:
                An error occurred which forced the session to be
          aborted. This usually occurs when the net-station executing
          MCOM is rebooted when MCOM is in use.

          Session OPEN rejected:
                The CALLed name was found, but was busy.

          Stack overflow!
                There are too many TSRs using the user's stack during
          interrupts. This causes the user's stack to grow too large.

          Too many commands:
                The NetBIOS in use was unable to queue more than one
          command at a time. This is a very poor NetBIOS emulation.

          Undefined error:
                Something is getting corrupt which caused NetBIOS to
          return an error-code that is undefined. This can be caused
          by a stack overflow or a TSR that uses memory that doesn't
          belong to it.

          The status line on the bottom shows the adapter status from
          the remote net-station (the one you are communicating with).

          Re:0000 Ab:004A Co:004F Tx:0FE1291A Rx:0FE11A9B
            |       |       |       |           |_ packets received
            |       |       |       |_____________ packets transmitted
            |       |       |_____________________ collisions
            |       |_____________________________ datagram aborts
            |_____________________________________ retransmits.

                All numbers are hexadecimal.

          Running the program.
          You can execute TESTNET overnight to see if there will be
          any problems with aborted sessions. If you use UCOM to set









                                     - 5 -

                                                        TESTNET Page 6

          the baud-rate of the UART, you can send many millions of
          bytes in an 8 hour period. At high baud-rates like 9600
          baud, there may be a few data-errors, about one error for
          every 64k of data. At low baud-rates, there won't be any
          errors on a properly operating network. The data errors that
          can occur result from missed hardware interrupts, not data-
          corruption. If you have a fast machine or are using NetBIOS
          software that does not disable interrupts for a long period
          of time, the error-rate will be very low. Connecting a COM
          port with hardware loop-back as is done for this test is a
          worst-case situation because a byte is sent during an
          interrupt-service routine then immediately received, gener-
          ating another interrupt.

          - finis -















































                                     - 6 -