NETERR.ZIP - Network Error Workstation Reboot Utilities
=======================================================

   (c) Copyright 1990-91 by


                      ÜÜÛÛÛÛÜÜ
            ÜÛßÛÜ   ÜÛßß  ßßÛÛÛÜ
           Ûß   ßÛÜÛß        ÛÛÛ
           ßÛÜ ÜÛß ßÛÜÜ    ÜÛÛß
             ßßß      ßßßßßß
           ÛÛÛ           ÜÛÛÛ ÛÛÛ          ÛÛÛ  ÜÛÛ
           ÛÛÛ ÜÜÜ ÜÜÜ  ÜÛÛÛÜ ÜÜÜ ÜÜÜ ÜÜÜ  ÜÜÜ ÜÛÛÛÜ  ÜÜÜÜ
           ÛÛÛ ÛÛÛß ÛÛÛ  ÛÛÛ  ÛÛÛ ÛÛÛß ÛÛÛ ÛÛÛ  ÛÛÛ  ÛÛÛÜÛÛ
           ÛÛÛ ÛÛÛ  ÛÛÛ  ÛÛÛ  ÛÛÛ ÛÛÛ  ÛÛÛ ÛÛÛ  ÛÛÛÜ ßÛÛÜÜÜ

            T   E   C   H   N   O   L   O   G   I   E   S

                   11433 Cronridge Drive, Suite H
                       Owings Mills, MD 21117
                          +1-410-363-1097
                       FAX: +1-410-363-3779

                      MHS: Support @ Infinite
          CompuServe: >MHS:Support @ Infinite (or 73270,405)
            Internet: Support@Infinite.MHS.CompuServe.com

  Technical Support provided on the CompuServe Information Service in
                         PCVENF Section 13



These utilities may be freely used, abused and distributed as long as the
copyright information remains unchanged.

----------------------------------------------------------------------------


On Novell networks, PCs running automated tasks, like gateways, print servers,
etc., need to be rebooted if they receive a network error.  Network errors
could be file server failures, routine server maintenance, or cabling
modifications.

These utilities are designed to allow these types of PCs to automatically
reboot and restart, rather than requiring an operator to manually perform
this function.

CRITERR.COM - This is a TSR program that monitors DOS and network critical
errors (e.g., the infamous "Abort, Retry").  When such an error occurs,
CRITERR simply reboots the PC on which it is running.

TESTIPX.COM - This program should be loaded in the PC's AUTOEXEC.BAT file
immediately after the IPX command.  If IPX did not load successfully, TESTIPX
will reboot the PC on which it is running.  With some network topologies,
like Ethernet, IPX will not load if there is a cabling problem and NET3
will hang the workstation.  TESTIPX prevents this from happening.

SHATTACH.EXE - This program should be loaded in the PC's AUTOEXEC.BAT file
immediately after the NET3/NET4/NET5 command.  SHATTACH makes sure that your
workstation connects to the correct server (particularly useful in a
multiple server environment).
The NETx shell will simply connect to the first server that responds to
it when loading.  Specifying SHATTACH SERVER-NAME will make the server
name specified your preferred server.  An optional switch, /R (e.g.,
SHATTACH SERVER-NAME /R) will cause the PC to reboot if the specified
server is not available.



PRODUCTS FROM INFINITE TECHNOLOGIES
===================================

Infinite Technologies offers innovative and easy-to-use software
solutions, designed primarily for the networked environment.

We back our products with dependable service and special attention
to individual requirements.  All of our programs are easy to learn
and use, and are designed to increase your efficiency.

We also want to help keep you up-to-date with product information,
updates and technical support.

These services are provided via the following mechanisms:

On the CompuServe Information Service, Infinite Technologies offers
support and product updates in Section and Library 13 of the PCVENF
forum.

Via MHS (through CSERVE or NHUB), you can address technical support
and/or product information inquiries to SUPPORT @ INFINITE.

You can also subscribe to our MHS Librarian! mailing list, which
will include notices of product updates.  To join this mailing
list, send a message via MHS (CSERVE or NHUB) to LIBRARY @ INFINITE
with SUBSCRIBE on your subject line.  (CompuServe users can send a
message to >MHS:Library@Infinite via CompuServe Mail.)

For an index of files available via LIBRARY @ INFINITE, send a message
with INDEX on your subject line.


NETWORK UTILITIES
-----------------

*  I-Queue! - Simplifies network printing and print queue management
   in the Novell NetWare environment.  From within a small memory
   resident pop-up (0 to 2-1/2KB), I-Queue! allows users to easily
   change NetWare print queues and modify "capture" parameters.
   I-Queue! is compatible with Novell's PRINTCON/PRINTDEF and adds
   global PRINTCON support for Novell's own utilities.
   Queue management capabilities include:  delete/reorder print jobs,
   move/copy jobs between queues, and hold/delayed printing.
   Now includes a Windows version!

*  CastAway! - A better NetWare broadcast message trap.  Get NetWare
   message notification (e.g., SEND) without your PC locking up until
   you press CTRL-ENTER!  Get notified of new messages while in graphics
   based applications!  All in 0 to 1-1/2KB of conventional memory!

*  PopIT! - Gain pop-up access to almost ANY program with less than
   2-1/2 KB overhead.  Network administrators -- access SYSCON,
   RCONSOLE, FCONSOLE and all of your favorite network utilities
   without leaving your current application.

*  OnCall! - A memory resident "Chat" utility for Novell NetWare,
   that runs in between 0 and 2-1/2 KB of workstation memory.
   Simple, straightforward, and easy to use.

EXPRESSIT! ELECTRONIC MAIL
--------------------------

*  ExpressIT! Electronic Mail - The ExpressIT! Electronic Mail product
   family includes the following products:

   *  ExpressIT! - The network version of ExpressIT!, including
      the MHS-compatible DOS version, which runs in less than 2KB of
      resident memory.

   *  ExpressIT! Remote - A remote version of ExpressIT! (DOS) customized
      for use on stand-alone/remote PCs.  Includes Personal MHS and
      allows users to send and receive mail with any MHS based
      electronic mail system.  Includes the ability to run the MHS
      Connectivity Manager from within the 2KB TSR without exiting
      your current application.

   *  ExpressIT! Windows Client - An upgrade for the network version
      of ExpressIT! offering native support for the Microsoft Windows
      environment, and a wealth of additional features.

   *  ExpressIT! Remote Windows - A remote version of the Windows
      version of ExpressIT! customized for use on stand-alone/remote
      PCs.  Includes Personal MHS and allows users to send and receive
      mail with any MHS based electronic mail system.

      A special Windows based MHS configuration utility eliminates the
      need to use the MHS Directory Manager.

   All versions of ExpressIT! include ExpressIT! Directory Assistance,
   facilitating automatic exchange of user directories between ExpressIT!
   hosts.

MHS GATEWAYS AND UTILITIES
--------------------------

*  MHS Scheduler - An MHS mail agent that provides greater flexibility
   in configuring when MHS will connect to a host.  On a host-by-host
   basis, the MHS administrator can configure different frequencies of
   forced connections based on different times of the day, with
   separate weekday, weekend, and holiday scheduling possible.
   MHS gateways and internetwork connections can also be scheduled.
   The companion RunIT! utility simplifies the creation of batch file
   gateways...now you can run your tape backup system on your MHS
   server.

*  MHS Librarian! - An MHS Gateway that allows users to request
   information to be forwarded to them via MHS.  Requests are
   made by placing a keyword in the "SUBJECT" field of the message
   that you address to the library.  A list of files may be
   requested by sending a message with the keyword of INDEX.  The
   system Admin can also configure MHS Librarian so that selected
   users can request files or directories other than those that
   appear in the index.  Security is provided by a password program
   that generates unique daily passwords, a fixed password, or you
   can create your own password utility.

   MHS Librarian! also supports "discussion lists", similar to
   the "list server" concept on the internet.

*  PageIT! - An MHS gateway connecting MHS-based electronic mail
   systems to full text alphanumeric pagers.  Once configured,
   sending messages to an alphanumeric pager is as simple as
   sending a message from your favorite MHS application.

*  ForwardIT! - An MHS mail agent for automatically forwarding
   MHS based electronic mail messages.  ForwardIT! can forward
   (or copy) messages addressed to an MHS address to an alternate
   address.

   ForwardIT! is most useful in the MHS remote e-mail environment.
   By remote, we refer to field workers or business travelers who
   operate ExpressIT! Remote, or other MHS compatible remote
   software, on a PC or laptop to access their electronic mail
   from a distant location.  Examples could include a salesperson
   between sales calls, a business traveler in a hotel room,
   or work-at-home scenarios.

   Without ForwardIT!, when mail is sent to a recipient's office
   address, MHS does not allow for a remote user to dial into the
   network and retrieve mail waiting for their office address.  Mail
   addressed to this office address can only be picked up at the
   office.

   In order to send a message to the user's MHS remote, the sender
   must assume responsibility for sending a copy of the message to
   the remote MHS address.

   With ForwardIT!, the user leaves a forwarding address at the
   office, and while they're out, all messages will be forwarded,
   or copied, to their forwarding address, giving users transparent
   access to their electronic mail while away from the office.

   This forwarding address can be any valid MHS address, including
   addresses via MHS gateways.

*  MhsQ! - An MHS gateway interface to NetWare print queues.
   Messages can be sent via MHS to a NetWare print queue.
   This capability can be useful for MHS remote sites and/or
   MHS enabled applications for generating printed output
   and/or reports.

   MhsQ! can also redirect print queues on one file server
   to a remote print queue on another file server via MHS.

*  MHSNotify! - A TSR which runs on the MHS mail server only, and
   automatically notifies recipients of new electronic mail
   received from remote MHS sites, or across internetwork
   connections.  An excellent alternative to MHSALERT for
   DaVinci e-mail users!  (MHSNotify! is bundled with ExpressIT!)

REQUESTING TRIAL VERSIONS VIA MHS
---------------------------------

   30-Day Trial Versions of many Infinite Technologies Products can
   be requested via MHS.

   For more information, send an MHS message to LIBRARY @ INFINITE
   via CSERVE or NHUB, with a subject line of INDEX.

DOWNLOADING TRIAL VERSIONS FROM COMPUSERVE
------------------------------------------

   30-Day Trial Versions of many Infinite Technologies Products are
   available on CompuServe!  Look for the following files in the
   PCVENF Forum, Library 13:

      XPRESS.ZIP - ExpressIT! Electronic Mail (NetWare)
                   (DOS and Windows versions combined)
      EXPDOS.ZIP - ExpressIT! E-Mail (NetWare) (DOS Version)
      EXPWIN.ZIP - ExpressIT! E-Mail (NetWare) (Windows Version)
      XPRES2.ZIP - ExpressIT! E-Mail (Remote & non-NetWare)
                   (DOS and Windows versions combined)
      REMDOS.ZIP - ExpressIT! E-Mail (Remote & non-NetWare) (DOS Version)
      REMWIN.ZIP - ExpressIT! E-Mail (Remote & non-NetWare) (Windows Version)

      POPIT.ZIP  - PopIT!
      ONCALL.ZIP - OnCall!
      CASTAW.ZIP - CastAway!
      IQUEUE.ZIP - I-Queue!
      MHSCED.ZIP - MHS Scheduler
      PAGEIT.ZIP - PageIT!
      4WARD.ZIP  - ForwardIT!
      MHSNFY.ZIP - MHSNotify!
      MHSLIB.ZIP - MHS Librarian!
      MHSQ.ZIP   - MhsQ!

   And don't miss our *FREE* utilities (also in PCVENF Library 13):

      NETERR.ZIP - Network error handlers (CRITTER, SHATTACH)
                   to reboot unattended workstations and clear
                   network errors.
      MHSACT.ZIP - Automatically re-activate deactivated MHS
                   internetwork hosts without operator intervention.
      MHSSWP.ZIP - Redirect MHS swap files to a local drive or
                   VDISK.
      CREATQ.ZIP - Create NetWare print queues on a volume other
                   than SYS:
      MHSBPL.ZIP - Configure MHS 1.5C host to host communications
                   to use the B+ protocol.
      SENDIT.ZIP - Send MHS messages from the DOS command line
                   or batch files.

   Plus, other helpful text files and reports:

      DOSMEM.TXT - PC Memory management/architecture overview
      WINTIP.TXT - Windows vs. NetWare Troubleshooting Tips



   ...and stay tuned for MORE!!!





FOR MORE INFORMATION, CONTACT:


                      ÜÜÛÛÛÛÜÜ
            ÜÛßÛÜ   ÜÛßß  ßßÛÛÛÜ
           Ûß   ßÛÜÛß        ÛÛÛ
           ßÛÜ ÜÛß ßÛÜÜ    ÜÛÛß
             ßßß      ßßßßßß
           ÛÛÛ           ÜÛÛÛ ÛÛÛ          ÛÛÛ  ÜÛÛ
           ÛÛÛ ÜÜÜ ÜÜÜ  ÜÛÛÛÜ ÜÜÜ ÜÜÜ ÜÜÜ  ÜÜÜ ÜÛÛÛÜ  ÜÜÜÜ
           ÛÛÛ ÛÛÛß ÛÛÛ  ÛÛÛ  ÛÛÛ ÛÛÛß ÛÛÛ ÛÛÛ  ÛÛÛ  ÛÛÛÜÛÛ
           ÛÛÛ ÛÛÛ  ÛÛÛ  ÛÛÛ  ÛÛÛ ÛÛÛ  ÛÛÛ ÛÛÛ  ÛÛÛÜ ßÛÛÜÜÜ

            T   E   C   H   N   O   L   O   G   I   E   S

                   11433 Cronridge Drive, Suite H
                       Owings Mills, MD 21117
                          +1-410-363-1097
                       FAX: +1-410-363-3779

                      MHS: Support @ Infinite
          CompuServe: >MHS:Support @ Infinite (or 73270,405)
            Internet: Support@Infinite.MHS.CompuServe.com

  Technical Support provided on the CompuServe Information Service in
                         PCVENF Section 13