--------------------------------------------------------------------

		function 0  - initialize a port

 	fct entry : ah = 0,
 	            al = port parameters
 			 76543210
                         ||||||||
			 ||||||``-- Data bits : 00  = 5 bits
			 ||||||                 01  = 6 bits
			 ||||||                 10  = 7 bits
 			 ||||||                 11  = 8 bits
                         |||||`---- Stop bits :  0  = 1 bit
 			 |||||                   1  = 2 bits
 			 |||``----- Parity    : 00  = none
 			 |||                    01  = odd
 			 |||                    10  = none
 			 |||                    11  = even
 			 ```------- Baud rate : 000 =   110 baud
 				                    = 19200 if EBIOS supported
 						001 =   150 baud
 						010 =   300 baud
 						011 =   600 baud
 						100 =  1200 baud
 						101 =  2400 baud
 						110 =  4800 baud
 						111 =  9600 baud

 		    dx = any valid channel # (DX min - DX max)

 	  returns : ah = 0ffh if error, otherwise :
 		       = port status.
 		    al = modem status.

 --------------------------------------------------------------------

		function 1h  - output a character

 	fct entry : ah = 01h
 		    al = character
 		    dx = any valid channel # (DX min - DX max)

	returns   : ah = port status.
 		    al = character sent.

 --------------------------------------------------------------------

		function 2h  - input a character

 	fct entry : ah = 02h
 		    dx = any valid channel # (DX min - DX max)

	returns   : ah = port status
 		    al = received character

 --------------------------------------------------------------------

		function 3h  - return port status

 	fct entry : ah = 03h
 		    dx = any valid channel # (DX min - DX max)

 	returns   : ah = port status
 		    al = modem status register
 --------------------------------------------------------------------

		function 4h  - extended port initialization

 	( Differs from COM/XI, PC/X* and MC/Xi DOS driver )


 	fct entry : ah = 04h
 		    al = break setting
 			 0 = No break.
 			 1 = Break (Break will be set until reset)
 		    bh = Parity
 			 0 = no parity
 			 1 = odd parity
 			 2 = even parity
 			 3 = stick parity odd (not supported)
 			 4 = stick parity even (not supported)
 		    bl = Stop bits
 			 0 = 1 stop bit
 			 1 = 2 stop bits
 		    ch = Character length
 			 0 = 5 bits
 			 1 = 6 bits
 			 2 = 7 bits
 			 3 = 8 bits
 		    cl = Baud rate
 			 00h -   110 baud
 			 01h -   150 baud
 			 02h -   300 baud
 			 03h -   600 baud
 			 04h -  1200 baud
 			 05h -  2400 baud
 			 06h -  4800 baud
 			 07h -  9600 baud
 			 08h - 19200 baud
 			 09h - 38400 baud
			 0Ah - 57600 baud
			 0Bh - 76800 baud
 			 0Ch -115200 baud
 	         	 0Dh -    50 baud
 			 0Eh -    75 baud
 		         0Fh -   134 baud
 		         10h -   200 baud
 			 11h -  1800 baud
 		    dx = any valid channel # (DX min - DX max)

 	returns   : ah = 0ffh on error, otherwise :
 		    ah = port status
 		    al = modem status

 --------------------------------------------------------------------

		function 5h  - extended communications port control

 	( Differs from COM/XI, PC/X* and MC/Xi DOS driver )


 	fct entry : ah = 05h,
 		    al = 00h - read modem control register
 		    al = 01h - write modem control register
 		    	 bl  - modem control bits
 			       bit 0 = DTR
 			       bit 1 = RTS
 		    dx = any valid channel # (DX min - DX max)

 	returns   : ah = port status
 		    al = modem status
 		    bl = modem control register
   		         bit 0 = DTR
 			 bit 1 = RTS

  NOTE : Access to OUT1, OUT2, and Loop bits are not supported. Also,
  RTS and DTR will not be affected while hardware handshaking is active.

 --------------------------------------------------------------------

		Function 6h  - Get Driver/Board Information


   ( New to PC/X* and MC/Xi DOS drivers, extends COM/Xi DOS driver function )


 	fct entry : ah = 6h

    Sub-function 0

 		    dx = any valid channel # (DX min - DX max)
 		    al = 0h - get port name
 	 return	:
 		    ah    = 0FFh if error, else
 	            al    = Highest INT 14h function supported.
 		    es:bx = Pointer to 8 byte ASCII string
 		            String = "NoDriver" if No DOS support
 			             is provided (INT 14h only)
 		            String = Channel's DOS name
 				     (eg "COM5    ")

    Sub-function 1

 		    al = 1h - get driver information
 		    dx = any valid channel # (DX min - DX max)
 	 return :
   		    ah = 0FFh if error, else
 		    ax = Total number of channels supported.
 		    bx = Driver Version # (e.g. V 2.0.1 : BX = 0201h)
 	            cx = Total number of board's supported.
 	            dx = DX min - Lowest DX value for INT 14h calls.
 		         Maximum DX value = Minimum value + AX - 1

    Sub-function 2h

    		    al = 2h - get board information
 		    bx = Board Number (0-3).
 		    dx = any valid channel # (DX min - DX max).
          return :
 		    ah = 0FFh if error, else
 		    ah = IRQ number.
 		    al = Board Type .
 		         1 = COM/Xi
  			 2 = MC/Xi
 			 3 = PC/Xe
 			 4 = PC/Xi
 			 5 = PC/Xm
 		    bx = Board's Dual-Ported Memory Segment.
 	            cx = Number of channels on the board.
 		    dx = Board's I/O port Address.
 		    si = INT 14h DX value for board's first channel

    Sub-function 0ffh

 		    al = 0ffh - get driver name
 		    dx = any valid channel # (DX min - DX max).
          return :
 		    ax    = driver version #
 		    cx    = number of channels supported.
 	            es:bx = pointer to drivers name (8 bytes 'DIGIFEP5').

 --------------------------------------------------------------------

		function 7h  - Send Break

 	 ( New to PC/X* and MC/Xi DOS drivers. Old Com/Xi driver used
           a 55 msec interval instead of this drivers 10 msec interval. )


 	fct entry : ah = 07h
 		    al = 00h - Use default break time
 		       = 01h   then bx = break length in # of 10 msec
 			       intervals.
 		    dx = any valid channel # (DX min - DX max)

 	returns   : ah = 0ffh on error
 		       = 0    on success

 --------------------------------------------------------------------

		function 8h  - alternate status check

 	fct entry : ah = 08h
 		    dx = any valid channel # (DX min - DX max)

 	returns   : zf = 0 and
 		    ah = a non 0ffh number.
                         then  ah = line status
 			       al = Character queued
 		    zf = 1 and
 		    ah = 0ffh
 		         then no char queued

 Note : If zf = 1 then and only then will ah = 0ffh. Thus, you only need to
	check zf OR ah to determine the success or failure of the call.

 --------------------------------------------------------------------

		function 9h  - clear buffers

 	fct entry : ah = 09h,
 		    dx = any valid channel # (DX min - DX max)

 	returns   : ah = 0    fct good
 		    ah = 0ffh fct bad (ccb timeout error)
 --------------------------------------------------------------------

		function 0ah - input queue check

 	fct entry : ah = 0ah
 		    dx = any valid channel # (DX min - DX max)

	returns   : zf = 1 and dh = offh if error, otherwise
                    ax = number of queued characters


  Note : This function differs from FCT 15h. Fct 0Ah returns the number
         of data characters in the receive buffer, while function 15h
         returns the number of bytes used in the buffer. Typically, each
 	 recieved character uses only one byte of buffer space unless the
 	 data byte is 0ffh or unless an error is associated with it. In
 	 these cases, 2 and 3 bytes of buffer space are used, respectively.
 	 Fct 0Ah disregards these extra bytes in it's returned count, while
 	 function 15h does not.

 	 Use fct 0Ah when you wish to know how many data bytes to read when
 	 using functions 2h (input a character) or 0Fh (read string).

 	 Use fct 15h when you want to know how many physical bytes of buffer
         space are used.

 	 If you were previously using the COM/Xi DOS driver "XIM232.SYS"
         Functions 0Ah and 15h are swapped in this driver.

 	 Also note that status bytes are not stored with every character in
 	 the receive buffer as they where with the XIM232, XAPCM232 and
 	 XIM232MC DOS drivers.


      : If zf = 1 then and only then will dh = 0ffh. Thus, you only need to
	check zf OR dh to determine the success or failure of the call.

 --------------------------------------------------------------------

		function 0bh  - Drop Handshake Lines

 	 ( New to PC/X* and MC/Xi DOS drivers )



 	fct entry : ah = 0bh
 		    dx = any valid channel # (DX min - DX max)

        returns   : ah = 0ffh if errors
 		    ah = 0    on success

 	This Function drops DTR and RTS. If Hardware handshaking is
 	active, it is disabled, the lines are dropped, and then it is
 	re-enabled.

 --------------------------------------------------------------------

		function 0ch  - Get Channel Parameters

 	 ( New to PC/X* and MC/Xi DOS drivers  changes and extends
 	   COM/Xi DOS driver function.				  )



 	fct entry : ah = 0ch
 		    dx = any valid channel # (DX min - DX max)

 	returns   : ah = 0ffh on error
 		         otherwise
 		    ah = S/W flow control
 			 bit 0 = tx s/w flow control (XON/XOFF)
 			 bit 1 = rx  "    "     "        "
 	            al = H/W flow control
 			 bit 0 = DTR rx flow control
 			 bit 1 = RTS rx flow control
 			 bit 4 = CTS tx flow control
 			 bit 5 = DSR tx flow control
 			 bit 7 = DCD tx flow control
 		    bh = Parity
 			 0 = no parity
 			 1 = odd parity
 			 2 = even parity
 		    bl = Stop bits
 			 0 = 1 stop bit
 			 1 = 2 stop bits
 		    ch = Character length
 			 0 = 5 bits
 			 1 = 6 bits
 			 2 = 7 bits
 			 3 = 8 bits
 		    cl = Baud rate
 			 00h -   110 baud
 			 01h -   150 baud
 			 02h -   300 baud
 			 03h -   600 baud
 			 04h -  1200 baud
 			 05h -  2400 baud
 			 06h -  4800 baud
 			 07h -  9600 baud
 			 08h - 19200 baud
 			 09h - 38400 baud
 			 0Ah - 57400 baud
 			 0Bh - 75600 baud
 			 0Ch -115200 baud
 	         	 0Dh -    50 baud
 			 0Eh -    75 baud
 		         0Fh -   134 baud
 		         10h -   200 baud
 			 11h -  1800 baud

 --------------------------------------------------------------------

		function 0dh - get pointer to character ready flag

 	fct entry : ah = 0ah
 		    dx = any valid channel # (DX min - DX max)

 	returns   : es:bx = pointer to the flag
                            flag = 0    : rx buffer empty
 		            flag = 0ffh : char available in rx buffer

	note      : The driver uses interrupts from the board, therfore an
 		    IRQ line must be selected for this function to work.

 --------------------------------------------------------------------

		function 0eh  -  write string

	fct entry : ah    = 0eh
		    dx    = any valid channel # (DX min - DX max)
		    cx    = # of chars in string
		    es:bx = pointer to string

 	returns   : ax    = # chars transmitted
		    zf    = 1 and dh = 0ffh if errors

 NOTE : If zf = 1 then and only then will dh = 0ffh. Thus, you only need to
	check zf OR dh to determine the success or failure of the call.

 --------------------------------------------------------------------

		function 0fh  - read string

      	fct entry : ah    = 0fh
 		    dx    = any valid channel # (DX min - DX max)
                    cx    = # of chars to read
 	            es:bx = pointer to callers buffer

	returns   : ax    = # chars read
		    zf    = 1 and dh = 0ffh if errors
			    (line sts or wrong # chars rtnd)

 NOTE : If zf = 1 then and only then will dh = 0ffh. Thus, you only need to
	check zf OR dh to determine the success or failure of the call.

 --------------------------------------------------------------------

		function 10h  - clear rx buffer

 	fct entry : ah = 10h
 		    dx = any valid channel # (DX min - DX max)

 	returns   : ah = 0ffh error
 		    ah = 0    success

 --------------------------------------------------------------------

		function 11h  - clear tx buffer

 	fct entry : ah = 11h
 		    dx = any valid channel # (DX min - DX max)

 	returns   : ah = 0ffh fct error
 		    ah = 0    fct good

 --------------------------------------------------------------------

		function 12h  - get tx buffer free space

 	fct entry : ah = 12h
 		    dx = any valid channel # (DX min - DX max)

 	returns   : ax = # of free bytes

 --------------------------------------------------------------------

		function 13h  - Set Handshake Lines

 	 ( New to PC/X* and MC/Xi DOS drivers )


 	fct entry : ah = 13
 		    dx = any valid channel # (DX min - DX max)

 	returns   : ah = 0ffh if errors
 		    ah = 0    on success

 	This Function raises DTR and RTS. If Hardware handshaking is
 	active, it is disabled, the lines are raised, and then it is
 	re-enabled.

 --------------------------------------------------------------------

 		function 14h  - Non destructive character read

 	 ( New to PC/X* and MC/Xi DOS drivers )

    	fct entry : ah = 014h
 		    dx = any valid channel # (DX min - DX max)

 	returns   : ah = Line status
 		    al = Character queued

 --------------------------------------------------------------------

		function 15h  - input byte count

    	fct entry : ah = 015h
 		    dx = any valid channel # (DX min - DX max)

 	returns   : ah = # of used bytes in the receive buffer

 	( See note on FCT 0Ah )


 ------------------------------------------------------------------

		function 16h  - Reserved

		( Old PC/X* Send CCB Command )


 ------------------------------------------------------------------

		function 17h  - Pause / Resume transmit

   ( New to PC/X* and MC/Xi, Old COM/Xi Get / Clear transmit pause )

	fct entry:  ah = 17h
		    al = 0, pause transmit
		       = 1, resume transmit
 		    dx = any valid channel # (DX min - DX max)

          returns:  ah = 0ffh fct error
 		    ah = 0    fct good

 ------------------------------------------------------------------

		function 18h  - Pause / Resume receive

	( Old PC/X* and MC/Xi Send Bios Command, New to COM/Xi)

	fct entry:  ah = 18h
		    al = 0, pause receive
		       = 1, resume receive
 		    dx = any valid channel # (DX min - DX max)

          returns:  ah = 0ffh fct error
 		    ah = 0    fct good


 ------------------------------------------------------------------

		function 19h  - Reserved

 		( Old PC/X* set/reset special character Interrupt )

 ------------------------------------------------------------------

		function 1ah  - Reserved

 		( Old PC/X* get pointer to special character flag / counter )

 --------------------------------------------------------------------

		function 1bh  -  Get water marks / buffer size


	 ( New to PC/X*, MC/Xi and COM/Xi DOS drivers )

 	fct entry : ah = 1bh
 		    al = 0 - Get Transmit Low water mark.
 		       = 1 - Get Receive Low water mark.
 		       = 2 - Get Receive High water mark.
 		    dx = any valid channel # (DX min - DX max)

 	returns   : ax = requested water mark.
 		    bx = tx buffer size if al was 0
 		       = rx buffer size if al was 1 or 2
		    zf = 1 and dh = 0ffh if error

  Note : Transmit low water mark - The host may request an event (IRQ) when the
 	 number of characters in the transmit buffer falls below this number.

       : Receive low water mark - When receive is paused and the number
 	 of characters in the receive buffer falls below this number,
 	 receive is resumed.

       : Receive high water mark - When receive is not paused and the
 	 the number of characters in the receive buffer meets or exceeds
 	 this value, transmit is paused.

       : If zf = 1 then and only then will dh = 0ffh. Thus, you only need to
	 check zf OR dh to determine the success or failure of the call.

 --------------------------------------------------------------------

		function 1ch  -  Set water marks

	 ( New to PC/X*, MC/Xi and COM/Xi DOS drivers )


 	fct entry : ah = 1ch
 		    al = 0 - Set Transmit Low water mark.
 		       = 1 - Set Receive Low water mark.
 		       = 2 - Set Receive High water mark.
 		    bx = water mark value.
 		    dx = any valid channel # (DX min - DX max)

 	returns   : ah = 0 on sucess.
 		       = 0ffh on error.
 --------------------------------------------------------------------

		function 1dh  -  Reserved

 --------------------------------------------------------------------

		function 1eh  -  Set flow control

	 ( New to PC/X*, MC/Xi and COM/Xi DOS drivers )


 	fct entry : ah = 1eh
 		    bh = S/W flow control
 			 bit 0 = tx s/w flow control (XON/XOFF)
 			 bit 1 = rx  "    "     "        "
			 bit 2 = set new XON/XOFF characters in CX
		    bl = H/W flow control
 			 bit 0 = DTR rx flow control
 			 bit 1 = RTS rx flow control
 			 bit 4 = CTS tx flow control
 			 bit 5 = DSR tx flow control
 			 bit 7 = DCD tx flow control
		    ch = new XOFF character if BX bit 2 = 1
		    cl = new XON  character if BX bit 2 = 1
		    dx = any valid channel # (DX min - DX max)

 	returns   : ah = 0 on sucess.
 		       = 0ffh on error.

 --------------------------------------------------------------------

		function 1fh  -  Enable / Disable Events


	 ( New to PC/X*, MC/Xi and COM/Xi DOS drivers )


 	fct entry : ah = 1fh
 		    al = Event mask
 		     	 76543210
 		     	 |||||||`--- Event on BREAK received.
 		     	 ||||||`---- Event on TX low water mark.
 		     	 |||||`----- Event on TX buffer empty.
 		         ||||`------ Event on RX data present.
 		     	 |||`------- (Not Used)
 		    	 ||`-------- Event on Modem Change Signal.
 		    	 ``--------- (Not Used)
 	  	    bl = Modem Signal if al bit 5 = 1
 		    	 76543210
 		    	 ||||````-- (Not Used)
 		    	 |||`------ CTS
 		    	 ||`------- DSR
 		    	 |`-------- RI
 		    	 `--------- DCD
 		    dx = any valid channel # (DX min - DX max)


 	returns   : ah = 0 on success
 		    	ah = ff if error

 --------------------------------------------------------------------

	  EBIOS function 0f4h  -  Presence Test

	 ( New to PC/X*, MC/Xi and COM/Xi DOS drivers )


 	fct entry : ah = 0f4h
 		    dx = any valid channel # (DX min - DX max)

 	return    : ax = 0

 --------------------------------------------------------------------

	  EBIOS function 0fbh  -  Specify modem leads

	 ( New to PC/X*, MC/Xi and COM/Xi DOS drivers )


 	fct entry : ah = 0fbh
 		    al = modem leads
 		         bit 0 = set/reset DTR output
 		         bit 1 = set/reset RTS output
 		         bit 4 = use CTS for input flow control.
 		         bit 5 = use DSR for input flow control.
 		         bit 6 = RI not supported
 		         bit 7 = use DCD for input flow control.
 		    dx = any valid channel # (DX min - DX max)

  Note : If RTS or DTR flow control is active, these lines will not be
         affected until that flow control is deselected.

 --------------------------------------------------------------------

	  EBIOS function 0fch  -  receive with no wait

	 ( New to PC/X*, MC/Xi and COM/Xi DOS drivers )


 	fct entry : ah = 0fch
 		    dx = any valid channel # (DX min - DX max)

  	return    : ah = line status
 		    al = character

 --------------------------------------------------------------------

	  EBIOS function 0fdh  -  retrieve buffer count

	 ( New to PC/X*, MC/Xi and COM/Xi DOS drivers )


 	fct entry : ah = 0fdh
 		    al = 1 - Get transmit buffer count.
 		       = 2 - Get receive buffer count
 		    dx = any valid channel # (DX min - DX max)

 	return    : cx = character count

 	This function returns the number of characters in the specified
 	buffer.

 --------------------------------------------------------------------

	  EBIOS function 0feh  -  Set pacing mode

	 ( New to PC/X*, MC/Xi and COM/Xi DOS drivers )


      	fct entry : ah = 0feh
 	    	    al = 0   - no pacing.
 		       = 40h - XON/XOFF for Receive.
 		       = 80h - XON/XOFF for Transmit, no RX pacing
 		       = C0h - XON/XOFF for Receive and Transmit.
 		    dx = any valid channel # (DX min - DX max)

  Note : CTS and DSR transmit pacing is always activated by a call to this
 	 function to emulate BIOS pacing.  All other flow control (if any)
 	 is disabled.

 --------------------------------------------------------------------

	  EBIOS function 0ffh  -  Set buffered mode of operation

	 ( New to PC/X*, MC/Xi and COM/Xi DOS drivers )


 	fct entry : ah    = 0ffh
 	    	    al    = 1 - Transmit buffer.
 		          = 2 - Receive buffer.
 	            cx    = buffer size, 0 = terminate buffer mode.
 		    dx 	  = any valid channel # (DX min - DX max)
 		    es:bx = pointer to buffer.

 	This function really has no effect, since the intellegent boards
 	use on-board buffering and thus have no need for host buffering.

 --------------------------------------------------------------------