R E N E M A I L
                               ~~~~~~~~~~~~~~~

               Renegade Fidonet Compatible Network Mail Interface

                              Operations Manual

                                Version 1.00

                      Copyright (C) 1991-1992 by Cott Lang
                              All Rights Reserved



SHAREWARE LICENSE AGREEMENT
~~~~~~~~~~~~~~~~~~~~~~~~~~~

        This  software  and documentation is protected by both United States
        copyright law and international treaty provisions. Users are granted
        a  limited  license to make and use  a copy of  Renemail  for  their
        Renegade Bulletin Board System.

        You are free to make  copies  of  the  software  and  documentation,
        however, all materials relating to this license statement, software,
        documentation,    order   information,   copyright   and   trademark
        statements  must remain intact as supplied in the original shareware
        package.  You  may  not  distribute,  rent, sublicense, integrate or
        lease  the software or the documentation. You may not alter, modify,
        or  adapt  the  software or documentation, including but not limited
        to   translating,   decompiling,  reverse  assembling,  or  creating
        derivative  works.

        The author  disclaims all   warranties, either   express or implied,
        including but  not limited to implied warranties of  merchantability
        and fitness  for a particular purpose, with  respect to the software
        and any accompanying written materials. In no event shall the author
        be liable for any damages whatsoever (including, without limitation,
        damages for loss of business profits, business interruption, loss of
        business information, or  other pecuniary  loss) arising  out of the
        use of  this  product,  even if  the author  has been advised of the
        possibility of  such damges.  Because some  states do  not allow the
        exclusion or limitation of liability for consequential or incidental
        damges, the above limitations may not apply to you.


INTRODUCTION
~~~~~~~~~~~~

             This documentation assumes that you have a working knowledge of
        Fidonet  echomail  processing.  It  is  beyond  the  scope  of  this
        documentation  to  explain  the  concepts  of  networking  and  mail
        processing.  You should  refer to  your echomail processing system's
        documentation for more information.

             Renemail  is  an  interface  program  that allows  Renegade  to
        support  Echomail  from  any  network  supporting Fidonet standards.
        Renemail  is  a  very  simplistic  program  at  this  point  in  its
        development.  It has only three major functions:


          o    Scanning - Renemail will  scan  Renegade's  Echomail  message
               bases  and process outbound messages, translating  them  into
               Fidonet compatible *.MSG  files for  further processing by an
               echomail processing system and your front-end mailer.

          o    Tossing  - Renemail   will   import  *.MSG   format  messages
               prepared  by  your  front-end  mailer and echomail processing
               system into the appropriate Renegade message bases.

          o    Purging  - Renemail will optionally purge  imported or tossed
               messages from your echomail directories.


          o    Netmail  - Renemail will import and export netmail to and
               from your Email system.


             Renemail does  not have its own configuration.  Renemail relies
        completely  on your  Renegade Bulletin  Board System's configuration
        for all necessary information.


REQUIREMENTS
~~~~~~~~~~~~

             Renemail is  not a  stand-alone  package.  You  will  need  the
        following additional programs:

          o    The Renegade Bulletin Board System version 1.0

          o    A front-end mailer.  Front end  mailers  are  responsible for
               answering incoming calls, and the  transmission and reception
               of outbound and inbound mail and files. Some available front-
               end mailers are:

                 o Frontdoor    o BinkleyTerm   o SeaDog   o D'Bridge

          o    An echomail processing system. The echomail processing system
               is responsible for processing  inbound and  outbound mail for
               Renemail  and  the front-end  mailer to work  together.  Some
               commonly used echomail processing systems are:

                 o Confmail  o Vpurge  o Qmail  o SquishMail  o TosScan

          o    A  groupmail  processing  system  is   necessary  if  you are
               interested in  implementing groupmail  with Renegade.  Two of
               the more common systems are:

                               o Group         o Gmail


INSTALLATION
~~~~~~~~~~~~

             If you have not already, decompress the  Renemail  distribution
        archive onto your  hard drive.  RENEMAIL.EXE  is the  only  required
        program in the archive.It can be placed anywhere on your hard drive,
        and run from anywhere  on your system.  It  is, however, recommended
        that you place it in your main Renegade directory.

             When Renemail runs, it needs to be able to locate your system's
        RENEGADE.DAT file. Renemail will first search the current directory,
        then it will search your path.   If  you are  not  running  Renemail
        from your main Renegade directory, then make sure your main Renegade
        directory is part of your path.  It is strongly recommended that you
        run Renemail from your  main directory  and that you  NOT  have your
        Renegade main directory in your path statement for security reasons.


OPERATION
~~~~~~~~~

             Renemail has only three command line options. They are mutually
         exclusive.  Renemail will only perform the first function specified
         on the command line, regardless of  what it  is or  how many  other
         functions are specified.

              Syntax:

                         RENEMAIL [FUNCTION]

          Where [FUNCTION] is one of the following:

             -S   -  Scan messages.  As explained previously, this scans new
                     messages in Renegade echomail  bases and  prepares them
                     for outbound  processing  by  your  echo  or  groupmail
                     processor.  Do this before  any outbound echo/groupmail
                     processing.

                     -N  Do not Scan netmail.

             -T   -  Toss  messages.  Also  as  previously  explained,  this
                     tosses  inbound  echo  or  groupmail  messages into the
                     appropriate Renegade message  bases.  Do this after any
                     inbound echo/groupmail processing.

                     -N  Do not Toss netmail.

             -P   -  Purge messages.  This  function  deletes all  the *.MSG
                     files in all of your echomail directories.  This should
                     be used  with care as  not to delete  outbound messages
                     that  have  not  yet  been processed  by your  echomail
                     processor, or  inbound messages  that have not yet been
                     tossed by Renemail into Renegade message bases.  If you
                     are having problems with Renemail  NOT deleting all  of
                     the *.MSG  files, use  -P -F  which  specifies Renemail
                     should NOT use the fast method of purging.



USING THE SYSTEM
~~~~~~~~~~~~~~~~

             As stated before, Renemail has been created to  work with other
        programs to operate correctly.   Renemail  only  translates  between
        Renegade and the echo or groupmail processor of your choice. Because
        of this, you are  responsible for executing the previously mentioned
        processing system(s) in relation to Renemail.

             About the only  efficient way to perform these  tasks is to use
        batch files. It is recommended that you use one batch file that runs
        your front-end mailer, Renegade, Renemail, and anything else used in
        your BBS's daily routine.  This batch file should be written in such
        a way  that whenever  inbound mail is received, the front-end mailer
        exits and the  echomail processor and Renemail are both executed, in
        that order.  When Renegade signals via  ERRORLEVEL  that new echo or
        groupmail has been  entered in the  message bases, Renemail  and the
        echomail processor should again be run, in that order.

             Here is an example of what  should take  place when an incoming
        echomail packet is received.  This  example uses Confmail because it
        is the simplest echomail processor available.   The example  assumes
        your main Renegade directory is C:\RENEGADE,and that you are running
        both programs from there. It also assumes you will be using PKWare's
        PKUNPAK to unarc incoming Arcmail packets.


             CD C:\RENEGADE                   {Change to the main directory   }
             CONFMAIL IMPORT -A PKUNPAK       {Execute echomail processor     }
             RENEMAIL -T                      {Invoke Renemail's TOSS function}
             RENEMAIL -P                      {Optionally PURGE echomail dirs }


             Equally simplistic is the following example of  what your batch
        file should  do when  it is  detected that new echo or groupmail has
        been entered in  Renegade, or whenever  you want to process new out-
        bound mail.  Please note that  the order in which these two programs
        are executed is crucial to correct operation.


             CD C:\RENEGADE                   {Change to the main directory   }
             RENEMAIL -S                      {Invoke Renemail's SCAN function}
             CONFMAIL EXPORT                  {Execute echomail processor     }
             RENEMAIL -P                      {Optionally PURGE echomail dirs }


             The RENEMAIL -P (or PURGE) function is optional,but recommended
        mainly to save disk space.  It will not  affect mail  processing, as
        Renemail  and  your  echomail processing system will not process the
        messages twice.  The above  example for exporting mail does not have
        Confmail arcing outgoing packets.  This  can  be added  easily using
        Confmail's  -A and -D  commands.  Using  Arcmail  is recommended for
        shorter  mail  transmission times.  If  you  have  trouble  with the
        purging function, try:

              RENEMAIL -P -F

             We recommend that the first echo you  attempt to pick up is the
        National Renegade Echo.  The author  of this  program is in there to
        answer your questions and hear your comments!


CREDITS
~~~~~~~

             All  brand  and product names referenced in this  document  are
        trademarks,  registered trademarks, or  copyrighted  works  of their
        respective holders.

             Special thanks to all the beta sites in Atlanta and other parts
        of the United States that saw Renemail through early beta stages!