---------------------------------------------------------------------------
           deltaComm Development, PO Box 1185, Cary, NC  27512  USA

         (919)-460-4556 voice, (919)-460-4531 FAX, (919)-481-9399 BBS

    Telix Copyright (C) 1986,87,88,89,90,91,92,93 by deltaComm Development
  ---------------------------------------------------------------------------


  October 13th, 1993 -- Notes on Telix 3.21 patch:

       This patch fixes a minor problem with regard to Telix sometimes not
       being able to turn off the 16550 FIFO, which can cause problems with
       other ill-behaved software such as Prodigy's software and certain fax
       software.  This patch does NOT correct the problem in which a warm
       boot on certain AMI BIOS's can cause the comm port not to be seen or
       recognized at all.  Only a BIOS replacement can correct this problem.

       Thanks to our German distributors (Elsa GmbH, Aachen), specifically
       Elsa's software engineers led by Svan Geuer, who discovered an
       undocumented (and highly illogical) dependency with regard to the
       order in which certain serial port registers are restored when
       closing the comm port.  This patch corrects the problem, enabling
       Telix to correctly restore the state of the 16550 FIFO under all
       known circumstances.

       To apply this patch:

         1) This patch must be applied to the UNBRANDED, REGISTERED copy of
            Telix.  It cannot be applied to branded copies, or to the
            shareware version of Telix.  The unbranded TELIX.EXE file can be
            found on the distribution diskette in the file TLX321-1.ZIP and
            is exactly 274,078 bytes, dated 02-05-93.

         2) Place the files PATCH.EXE and PATCH.RTP in the same directory as
            the unbranded TELIX.EXE, and run the program PATCH.EXE from that
            subdirectory.

         3) The resultant copy of TELIX.EXE may then be branded and used.


       For those inclined to ask, Telix restored the comm registers in the
       inverse order of which they were initialized.  This included
       restoring the Interrupt ID (IID) register prior to the Line Control
       Register (LCR).  It was found that (although it shouldn't matter), on
       some systems the restoration of the LCR register after the IID
       register would sometimes reactivate the FIFO (or possibly the
       contents of the initialized LCR would prevent the FIFO from being
       deactivated at all -- we're really not sure).  By restoring the LCR
       to the original state before restoring the IID register, tests have
       confirmed that the 16550 FIFO is always thus restored.  Don't ask
       why, since we don't know -- this behaviour isn't documented in the
       National Semiconductor specs *or* their sample code (their sample
       code also restores the IID before the LCR).

Jeff Woods
October 13th, 1993