3_Drives v1.5 Shareware version Released February 1993

ÕÍÍÍÍÍÍµ  3_Drives v1.5  ³
³                                  ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿    ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
³      Dustbowl Designs, Inc.      ³     426 MB     ³    ³°°°°0   MB°°°°°°³
³      -=ð NOT REGISTERED ð=-      ³ ðþðððððððððððð ³    ³°°°°°°°°°°°°°°°°³
³    "Dedicated to enhancing the   ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ    ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
³    world's personal computers."  E:     Installed      4_Drives v2.1 only
³       (405) 741-2721 BBS
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
³     Copyright 1992 by Dustbowl Designs, Inc. All rights reserved.         ³
³         9606 N.E. 4th Street, Midwest City, Oklahoma USA 73130            ³
³   See 3_Drives.doc for v2.1 registration information. (405) 741-4705      ³
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

The universal device driver that lets you add an additional 16-bit
interface to your system.  Add up to two **= MORE =** MFM, RLL, ESDI
or AT/IDE hard disk drives regardless of the first interface type.

=====Introduction=============================
3_Drives v1.5 is a shareware CONFIG.SYS block device driver that
allows the utilization of a SINGLE hard disk drive on the standard
Secondary Port Address using the DOS operating system giving you the
potential total of FOUR fully functional hard drives in your system!
This unique device drive also permits two incompatible controllers
and/or host adapters to COEXIST in the same system.

        *  With 3_Drives you can combine MFM, RLL, ESDI, AT/IDE and
           SCSI hard disk drives......

               Primary Port       |       Secondary Port
                  Address         |           Address
                                  |
              Drive 1   Drive 2   |
              ÚÄÄÄÄÄ¿   ÚÄÄÄÄÄ¿   |   ÉÍÍÍÍÍÍ 4_Drives ÍÍÍÍÍÍ»
              ³ RLL ³   ³ RLL ³   |   º Õ 3_Drives ¸         º
              ÀÄÄÄÄÄÙ   ÀÄÄÄÄÄÙ   |   º ³ ÚÄÄÄÄÄ¿  ³ ÚÄÄÄÄÄ¿ º
              ÚÄÄÄÄÄ¿   ÚÄÄÄÄÄ¿   |   º ³ ³ IDE ³  ³ ³ IDE ³ º
              ³ MFM ³   ³ MFM ³   |   º ³ ÀÄÄÄÄÄÙ  ³ ÀÄÄÄÄÄÙ º
              ÀÄÄÄÄÄÙ   ÀÄÄÄÄÄÙ   |   º ³ ÚÄÄÄÄÄ¿  ³ ÚÄÄÄÄÄ¿ º
              ÚÄÄÄÄÄ¿   ÚÄÄÄÄÄ¿   |   º ³ ³ESDI ³  ³ ³ESDI ³ º
              ³ESDI ³   ³ESDI ³   |   º ³ ÀÄÄÄÄÄÙ  ³ ÀÄÄÄÄÄÙ º
              ÀÄÄÄÄÄÙ   ÀÄÄÄÄÄÙ   |   º ³ ÚÄÄÄÄÄ¿  ³ ÚÄÄÄÄÄ¿ º
              ÚÄÄÄÄÄ¿   ÚÄÄÄÄÄ¿   |   º ³ ³ MFM ³  ³ ³ MFM ³ º
              ³ IDE ³   ³ IDE ³   |   º ³ ÀÄÄÄÄÄÙ  ³ ÀÄÄÄÄÄÙ º
              ÀÄÄÄÄÄÙ   ÀÄÄÄÄÄÙ   |   º ³ ÚÄÄÄÄÄ¿  ³ ÚÄÄÄÄÄ¿ º
              ÚÄÄÄÄÄ¿   ÚÄÄÄÄÄ¿   |   º ³ ³ RLL ³  ³ ³ RLL ³ º
              ³SCSI ³   ³SCSI ³   |   º ³ ÀÄÄÄÄÄÙ  ³ ÀÄÄÄÄÄÙ º
              ÀÄÄÄÄÄÙ   ÀÄÄÄÄÄÙ   |   º ÔÍÍÍÍÍÍÍÍÍÍ¾         º
                                  |   ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
                                  |
             Our systems handle   |   Any one of these interfaces
             this side already.   |   can be added using 3_Drives
                                  |   or 4_Drives.
           Any of these works...>>>>> with any of these!


        *  This means you DO NOT have to retire your older MFM  or RLL
           drives if you purchase a new AT/IDE hard disk drive!!!

        *  Allows you to still boot to a SCSI drive in a system
           with IDE, MFM, RLL or ESDI.

        *  If you have two IDE drives that will not work together due
           to a manufacturer's Master/Slave incompatibility, 3_Drives
           lets them coexist without conflict.

        *  With 3_Drives you can easily use an AT/IDE, MFM, RLL or
           ESDI drive to backup data and/or transport large quantities
           of data between systems at hard drive speeds.

=====Upgrade Offer============================
As noted in the screen representation and at the beginning of this
document, 3_Drives shareware v1.5 supports a SINGLE primary partition
on a SINGLE hard disk drive at the Secondary Port Address.  In the
event that you may want to add a SECOND drive to the Secondary Port
Address, or desire access to logical drives in extended partitions, we
offer the programs: registered v2.1 3_Drives and 4_Drives.

Registered version features:
  * Ultra-fast program loading without delays or required user
    intervention.
  * Program supports up to 10 logical drives per physical drive.
  * Includes 4_Park, a four drive head-parking/screen-saver utility.
  * Discount on version upgrades.
  * Access to advanced technical support and registered user sections
    of our support BBS.
  * Postscript version of the documentation.

=====System Requirements======================
A few simple conditions must be met in order to utilize the 3_Drives
device driver.

They are:

   1. Computer system MUST be either a 286, 386sx, 386dx, 486sx or
      486dx.

   2. DOS level must be v3.0 or higher, including Digital Research
      DR DOS 6.0, with a single Primary partition (3_Drives v1.5
      shareware version, only).

   ** Registered 3_Drives or 4_Drives v2.1 also support Extended
      partitions with up to 10 logical drives per physical unit.

   3. A second Controller or Host Adapter which must have the option
      to set a Secondary Port Address to 170h and to disable IRQ14
      monitoring.  The Secondary Port Address feature is available on
      practically every hard drive controller made and the disable
      IRQ14 feature is found on about half of the adapters, but is
      "do-able" on 100% of them using a simple tape-over method (See
      App Note #10 for "Tape-Over Method"). Jumpers and settings for
      the Seagate ST-07A, ST-08A, Acculogic SIDE-3 AT/IDE Host
      Adapters and Western Digital WD1006-xxx, Adaptec ACB-231x,
      Adaptec ACB-237x or Data Technology DTC728x MFM/RLL ST506/ST412
      Interface controllers are included in this doc file to show you
      how this is done. (See Controller and Host Adapter Setup
      Instructions).


=====Preparing "Secondary Port" Disk Drives====
The disk drive that will be attached to the Secondary Port Address
needs to be partitioned and formatted on the Primary Port Address
prior to using the 3_Drives/4_Drives device driver.  Use the standard
DOS utilities, FDISK and FORMAT, or automatic installation software to
accomplish the task.  This will probably require temporarily removing
the existing hard disk drive controller or preparing the "Secondary"
drive in a different system.

BEFORE disengaging the "Primary" drives, BE SURE to write down the
CMOS drive type(s). If 'User Defined' or 'Custom' drive types are
being used, write down the associated cylinder, head, write precomp,
lzone and sector per track values.

      (If the drive you intend to install on the Secondary Port
      Address is prepared and ready to go, jump to step #9 below)

The installation steps to take for an unprepared drive without data
are roughly as follows:

  .5  Finish reading the rest of this document.

   1. Satisfy yourself that BACKUPs of your data are current and in
      good condition.

   2. Prepare a bootable floppy diskette and copy (or simply have
      available on a separate diskette) FDISK and FORMAT to this
      floppy.

   3. Install (on the default Primary Address) the controller or host
      adapter for the drives you eventually intend to use on the
      device driver and set the appropriate drive type number in the
      system CMOS setup. Remember, each controller will support one or
      two drives.  The drive jumpers that establish drive selects or
      Master/Slave relationships follow the same rules as they would
      in a single controller system. Do not set a MFM or RLL to Drive
      select three!

   4. Boot to the floppy diskette.

   5. Use FDISK to define the Partition(s). The system will
      automatically reboot to the A: drive after concluding FDISK.

   6. FORMAT C: /S (Registered versions: including any other logical
      drives in extended partitions without the /s).

   7. Confirm that the hard drive boots without the floppy in A: and
      can perform reads and writes, and is good working condition.

   8. Restore the CMOS drive types to the ones used on the original
      1st (and 2nd) drives. Power down the system and reinstall the
      controller for the original drives.

   9. Set the second Host Adapter for the "Secondary" drive to
      Secondary Port Address 170h and disable IRQ14 monitoring. (see
      below for examples of popular Host Adapter/Paddle Board and
      Controller jumper settings). You do not have to make any changes
      to the drive select jumpers or Master/Slave jumpers.

  10. Reboot. The system should start in the same way it always has.

  11. Copy the 3_DRIVES.HDD program into the root directory of the C:
      drive and Edit the CONFIG.SYS file to include the line:

               DEVICE=C:\3_DRIVES.HDD

      This line should precede any other block device drivers (such a
      RAMDRIVE.SYS). If a Disk Manager (tm Ontrack Computer Systems)
      partition is installed on the original "Primary" drives, the
      DEVICE=C:\3_DRIVES.HDD line should follow after DMDRVR.BIN.

  12. Reboot. An 3_Drives installation screen (shown above) will
      indicate the loading status of the device driver. The drive
      letters assigned to the "Secondary" drive(s) will depend on the
      number of partitions on your C: and D: drives.


=====Background===============================
In the past, three major factors have stood in the way of achieving
the elusive goal of supporting more than two hard disk drives or even
two disk drives of dissimilar interfaces.  First, DOS versions prior
to the v5.0 would support a maximum of two physical hard disk drives.
The v5.0 DOS FDISK supports up to eight physical hard disk drives if
the Host Adapter is designed to follow the FDISK conventions of DOS
v5.0. (Some SCSI interface Host Adapters are now out in the
marketplace which have this support.)

Second, standard interface hard disk drive controllers (except for
SCSI) are limited to two physical drives.  In the case of MFM, RLL and
ESDI, the drives usually have a Drive Select 3 and 4 jumper (DS3 &
DS4), but the controllers for these interfaces use the industry
standard "Daisychain" configuration which allows only two drives to be
connected. (The rare "Radial" configuration uses the DS3 and DS4.) In
the case of the new AT interface for hard disk drives, also known as
IDE, the controller is built onto the drive itself and is limited by
design to two physical drives per Host Adapter - Master and Slave.

Third, controllers for these interfaces usually require a drive type
number to be set in CMOS and only two slots are ever given by the
system BIOS.

Until 3_Drives/4_Drives, two AT controllers have generally been unable
to coexist because of a condition known as a "port address conflict."
In effect, both controllers canceled each other out because they
needed to use the same Hard Drive Primary Port Address, 1F0h.  In its
default configuration, DOS only recognizes hard disk drives that are
attached to this Primary Port Address and communicates with them
through the system bios and INT13.  A block device driver is required
to service drives that are attached to the common Secondary Port
Address, 170h; the 3_Drives/4_Drives device driver serves this
function.


=====Outline==================================
An brief outline of how 3_Drives works is as follows:

After partitioning and formatting in the DOS environment, every hard
disk drive, regardless of interface, controller, or CPU has a very
special sector of information called the Master Boot Record (MBR). The
MBR is always the very first physical sector on the disk (cyl 0, hd 0,
sector 1), the contents of which 1) preserve the defined partition
structure, 2) contain the first executable instruction to begin
loading the active operating system, and 3) a final word signature in
the sector, AA55h, indicating a valid Master Boot Record.

Once a valid MBR is identified, the values stored in the partition
record of the MBR indicate the location of the DOS Boot Record (DBR)
which is generally located at logical cyl 0, hd 1, sector 1.  This DOS
boot sector contains two vital components - the BIOS Parameter Block
(BPB) structure and a loader routine for the operating system .  The
BPB provides a logical description of the hard disk drive's geometry
(logical blocks, heads, sectors per track, bytes per sector, etc.),
while the operating system loader establishes the names of the system
files IO.SYS and MSDOS.SYS, their root directory locations and then
loads them into memory .

Next, the IO.SYS file is read into memory, followed by the MSDOS.SYS.
These are the names of the two hidden files which accompany
COMMAND.COM after formatting a bootable drive. These programs begin an
initialization routine which establishes the resident character and
block devices found during the Power On Self Test (POST) and
motherboard ROM BIOS initialization.  Once the basic hardware has been
identified and the DOS kernel has been positioned into low memory, the
next stage is to run a system module within IO.SYS called SYSINIT.  It
is at this time that the first of the Primary Port Address drive
letter designations are assigned (A:, B:, C:, etc.). These block
devices are given special handling at this point.  For each, a pointer
to a BPB array is established in memory.

Next, begins the process we are most interested in, namely the
processing of the CONFIG.SYS file.  The entire file is read into
memory and analyzed for block and character type device drivers.  When
block device drivers are identified, like 3_Drives, their entries
are added to the drive translation table and given the next available
drive letter designation.

Device drivers, like regular programs (but not quite like regular
programs), have initialization code and resident code.  The
initialization code in 3_Drives is the display banner and secondary
drive identification, while the resident portion is a collection of
routines handling very specific AT register set commands. The AT
register commands "talk" directly to the Secondary Port Address, 170h,
and therefore to the drive itself, and cover drive specific operations
like Read, Write, Recal, and Reset. It should be noted that the Format
command operation is not supported by 3_Drives, which is the reason
why the drive must be partitioned and prepared in a normal C:/D:
environment.

After all components of the CONFIG.SYS file are processed, SYSINIT's
final function is to load and execute the MS-DOS shell program,
COMMAND.COM.  How DOS manipulates the resident (critical error
handling, for example) and transient portions (batch file processes,
COPY, and RENAME, etc.) of the shell are beyond the scope of this
overview.

Thereafter, during the normal course of operation of the computer
system, DOS commands which are directed towards the drive letter(s)
assigned to the 3_Drives block device(s) are executed through the
memory resident portion of 3_Drives.

3_Drives v1.5 will occupy a minimum of 2,464 bytes of memory under DOS
5.0. In the registered versions of 3_Drives/4_Drives (v2.1), the
amount of memory required for the device driver will climb slightly by
÷48 bytes/drive, depending on the number of logical drives in extended
partitions, if any.


=====App Notes================================

Some Application Notes:

   1. The effect of the program on the performance of the system is
      negligible.

   2. The use of 3_Drives on XT's is DISALLOWED, since it relies
      exclusively on AT register set commands which are only available
      on 286's or higher.

   3. If power supply leads are in short supply, a simple "Y" adapter
      that splits two leads off of a single, are available at most
      computer supply stores.

   4. If two controllers are set to the SAME port address or share the
      same IRQ, either floppy or hard, the system will hang during the
      POST (Power On Self Test).

      If both controllers have support for floppy drives, disable the
      floppy support on the second. If a specific "disable floppy"
      jumper is unavailable, then set the floppy to a secondary port
      address (usually 370h) which effectively hides the conflict.

   5. 3_Drives can be moved into upper memory under DOS 5 with
      DEVICEHIGH=C:\your...path\3_DRIVES.HDD

   6. 3_Drives shows all signs of complete stability with Microsoft
      Windows (tm).  In fact, our entire Windows subdirectory
      structure is located on the "Secondary" drive! We have thrown in
      everything we can think of to test Windows compatibility, and
      all tests have proven successful. If you intend to use the drive
      supported by the 3_Drives for the Swap File, then in must be of
      the Temporary Swap File Type. (A Permanent Swap File requires
      Int13 support.)

   7. We've run three of the most popular file defragmenters without
      problems.  In any case, ALWAYS follow the software
      manufacturer's instructions and BACKUP you data first.

   8. DOS 2.x and above will run with the same partition and capacity
      limits allowed by that version of DOS, however only DOS 3.0 and
      above will show the proper drive letters on the 3_Drives
      initialization screen.

   9. 10 partitions per physical drive are allowed under 3_Drives
      support. Registered v2.1 only.

  10. "Tape-Over Method":  It is possible to install a single MFM, RLL
      or ESDI drive on the secondary port address and utilize
      3_Drives.  This process, however, is not as straight forward as
      putting the AT/IDE on the secondary because typical ST412
      interface controllers (MFM and RLL) usually do not have the
      built-in ability to disable the IRQ14.  If no jumper on the MFM
      controller exists to disable IRQ14, then the line can usually be
      disabled manually where it plugs into the motherboard.

      On a 16-bit controller, the IRQ14 line is found on the back side
      card edge, on the "short" 16-bit extension.  It is the 7th
      contact from the left or 12th from the right (D7). Usually,
      placing a piece of simple transparent tape over the contact will
      cause it to be disabled when the card is plugged into the
      motherboard.  It is advisable that you refrain from attempting
      this configuration unless you have prior experience with
      modifications of this sort. See below:

      ³
   Þ  ³ Metal Clamp
   ÞÄÄÅÄÄÄÄÄ¿
   Þ  ³  0  ³    Perspective: Looking at the backside of the card
   ÞÄÄÅÄÄÄÄÄÙ
   Þ  ³            8-bit long slot             16-bit short slot
   Þ  ³_____      31 total contacts        ___ 18 total contacts______
   Þ        ÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝ   ÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝ
   Þ                                                ³
   Þ                                               D7 (IRQ14) Tape over
                                              count 7 spaces from left or
                                                   12 spaces from right

         Note: Many manufacturers only plate the contacts that will be
               needed on the card.  Be sure to count spaces, not
               actual plated contacts.

  11. As noted earlier, some programs will not operate through
      3_Drives (i.e. FDISK, FORMAT).  This is because these programs
      bypass DOS and do not update the partition's FAT (File
      Allocation Table).  Other examples of this are usually drive
      diagnostics utilities.  If programs of this sort are deemed
      necessary to run, the drive will need to be reinstated on the
      primary port address in order to be "seen" by the program.

  12. The DOS ASSIGN utility can be used to set a drive on the
      Secondary Port Address to C:, if desired.  Simply execute the
      command    ASSIGN C:=E: E:=C:   This will effectively swap the
      assigned drive letters.  Remember that CHKDSK will not run on
      assigned or substituted drives.  Running ASSIGN again, without
      any command line parameters, will clear the assignment.

  13. Popular drive compression programs work well with 3_Drives and
      4_Drives.  (In fact, this document is being written on drive
      number 4, and is a compressed drive.)  The important points to
      remember are that 3_Drives needs to be loaded before the
      compression drivers IF the Secondary Port Address drives are
      being compressed.  If the system is already compressed prior to
      installing 3_Drives, then confusion could arise when it comes
      time for the compression driver to assign the drive letter
      designations, especially with the drive letter swapping and
      reserved drive settings that are typical of compression
      programs.  To be absolutely safe, BE SURE to backup all data
      prior to creating compressed drives.

  14. RLL and ESDI controllers usually operate on the Primary Port
      Address with an enabled on-board bios.  This bios needs to be
      disabled when used with 3_Drives on the Secondary Port Address.
      The drive does not have to be lo-level formatted with the bios
      disabled.


=====Error Messages===========================
The device driver may display a small assortment of error messages
during the loading process of the CONFIG.SYS file. These usually
relate to unformatted status, jumper, cabling and power issues.

The most common error messages are descriptive and will explain the
specific problem encountered. (i.e. "No controller found at the
Secondary Port Address" or "No valid DOS boot record found").

The less common errors are listed by number:

Error code #1  : Address Mark not found. cyl=xx hd=xx sect=xx
                 Drive may need lo-level format. Scan for defects.

Error code #2  : Drive Fails Recal
                 Check cables and drive select jumpers, etc.

Error code #4  : Aborted Command.
                 Invalid command request or drive fault problem like a
                 seek error.

Error code #5  : Write Fault.
                 Usually caused by power supply voltage fluctuations or
                 problems with termination resistors.

Error code #6  : Time-out.
                 General time out.

Error code #7  : Time-out while waiting for drive DRQ.

Error code #8  : Read Fault.
                 Check cables, connections and drive jumpers.

Error code #16 : Sector ID Not Found. cyl=xx hd=xx sect=xx
                 May need a lo-level format.

Error code #64 : CRC Error.
                 Scan for defects.

Error code #128: Block Marked Bad.



=====Legal Disclaimer=========================

                          LICENSE AGREEMENT

3_Drives 4_Drives 4_Park All versions.

Dustbowl Designs, Inc. provides  the accompanying object code software
("Software")  and nonexclusively  licenses  its  use on  the following
terms and conditions. The Software is copyrighted by Dustbowl Designs,
Inc. with all rights reserved.  YOU ASSUME FULL RESPONSIBILITY FOR THE
SELECTION OF THE  SOFTWARE TO ACHIEVE YOUR INTENDED  PURPOSES, FOR THE
PROPER INSTALLATION  AND USE. Dustbowl Designs,  Inc. DOES NOT WARRANT
THAT THE  SOFTWARE WILL MEET  YOUR REQUIREMENTS, THAT  THE SOFTWARE IS
FIT FOR ANY PARTICULAR PURPOSE OR THAT THE USE OF THE SOFTWARE WILL BE
ERROR FREE. Dustbowl Designs, Inc. EXPRESSLY DISCLAIMS ALL WARRANTIES,
WHETHER  ORAL  OR  WRITTEN,  EXPRESSED  OR  IMPLIED, INCLUDING WITHOUT
LIMITATION WARRANTIES  OF MERCHANTABILITY OR FITNESS  FOR A PARTICULAR
PURPOSE. IN  NO EVENT WILL  Dustbowl Designs, Inc.  BE LIABLE TO  YOU,
YOUR  CUSTOMERS   OR  OTHER  USERS   FOR  ANY  INDIRECT,   INCIDENTAL,
CONSEQUENTIAL,  SPECIAL  OR  EXEMPLARY  DAMAGES  ARISING  OUT OF OR IN
CONNECTION WITH THE USE OR INABILITY TO USE THE SOFTWARE.

3_Drives is a trademark of Dustbowl  Designs, Inc. The 3_Drives
software and documentation are Copyright 1992 by Dustbowl Designs with
all rights reserved. The 3_Drives v2.1, 4_Drives v2.1 and 4_Park v1.1
software programs ARE NOT shareware or freeware and unauthorized
redistribution is STRICTLY PROHIBITED.

End of License agreement.

*****************************************************************

Revision History:
v1.1    08/92 public release of 3_Drives shareware v1.1.
        08/92 public release of 3_Drives and 4_Drives REGISTERED v1.1.
        Support terminated for NON-registered v1.1 users.
v1.5    02/93 public release of 3_Drives shareware v1.5. Smaller
        memory resident size (37% smaller!). Optimized for faster
        execution.  Improved error handling and added new error
        messages.  DOS support beginning with v3.0.  Stopped hang
        problem when driver installed and controller isn't.
        Documentation upgraded. Introduces new company name and BBS.
v2.1    02/93 public release of 3_Drives and 4_Drives REGISTERED v2.1.
        Same as shareware v1.5 including extended partition support
        with up to 10 logical drives per physical unit.

Contents of the 3_Drives Distribution Set. 3DRVS150.ZIP (3DRVS.ZIP on
CompuServe (tm) go IBMHW forum Lib 1)

3_DRIVES.HDD    Device driver file
3_DRIVES.DOC    Documentation file with installation instructions.
4DRVDEMO.EXE    Simple demo that gives a look at registered
                4_Drives v2.1 and 4_Park v1.1
ORDER3.FRM      Mail-in registration form
README3.TXT     User shareware policy
VENDOR.DOC      Shareware vendor distribution policy

All files dated 2-10-93 01:50:00.
*****************************************************************


Controller and Host Adapter Setup Instructions

===== AT IDE Host Adapters ===================

=====Seagate ST-07A and ST-08A================
The ST-08A is a combination floppy drive and hard drive host adapter,
while the ST-07A is for hard drives only.  The floppy support on the
ST-08A can be disabled making it functionally equivalent to the
ST-07A.

   J2                    ÚÄ Drive-on-a-Card Mounting Point
 Diskette                ³
 Connector     J3 LED    ³      J1 AT Interface
 (ST08A only)  ³     ÚÄÄÄÙ      Hard Disc Connector
 ³  ÚÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ Ýßßßß
 ³  ³   1      1     ø             ³                    ÚÄÄÅÄÝ
 ³  ³   ::     øøøø             ::::::::::::::::::::    ÀøÄÅÄÝ
 ³  ³   ::                      1                          ³ Ý
 ÀÄÄÅÄÄ ::                           ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄ JP2
    ³   ::                           1 JP2                 ³ Ý  Disc/Diskette
    ³   ::                          øø                     ³ Ý  Address
    ³   ::         (ST08A only)                            ³ Ý  Select
    ³   ::  Ú1ÄÄÄÄ JP4 Diskette Controller Enable          ³ Ý
    ³       :                                   ÚÄÄÄÄÄÄÄÄÄÄÅÄÄÄ JP6 I/O
    ³       ððÝð}ÄÄ J4 Aux DC Power to          1       ÚÄÄÅÄÝ  Channel
    ³            1¿    Hard Disc                øø      ÀøÄÅÄÝ  Ready
    ³          øøøÀÄÄÄ¿                                    ³ Ý
    À¿ Ü Ü Ü Ü Ü Ü ÜÚÄÅÄÄ¿ Ü Ü Ü Ü Ü Ü Ü Ü Ü Ü Ü Ü Ü ÜÚÄÄÄÄÙ Ý
     ÀÄßÄßÄßÄßÄßÄßÄßÙ ³  ÀÄßÄßÄßÄßÄßÄßÄßÄßÄßÄßÄßÄßÄßÄßÙ      Ý
                      ÀÄ JP5 Disable Interrupt or            Ý
                             Interrupt While Busy IRQ14

If set up as the 2nd Host Adapter for use with 3_Drives:

1.  Add a jumper to JP2 (Disc/Diskette Address Select) which sets the
    port to the secondary address at 170h. (New Seagate documentation
    does not describe this jumper.)

2.  Remove jumper from JP5 (Interrupt While Busy, IRQ14). The jumper
    can be conveniently stored on a single pin.

3.  If ST-08A, then remove jumper from JP4 (Diskette Controller
    Enable) to disable the Floppy Controller).



=====Acculogic SIDE-3================

         ÚÄ 40-pin IDE Hard drive
         ³    connector (pin-20   ÚÄ 34-pin Floppy drive     Ýßßßß
         ³   removed for keying)  ³    connector (pin-5      Ý
 J1      ÀÄÄÄÄÄ¿                  ³  removed for keying)     Ý
 LED Ä¿        ³                  ³                          Ý
    ÚÄ³ÄÄÄÄÄÄÄÄ³ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ³ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ Ý
    ³1øøøø     ³         ::::::   ³ :::  (see below)       ³ Ý
    ³          ³      JP 123456   ³ 789                 ÚÄÄÅÄÝ
    ³ :::::::::ù::::::::::      ::ù::::::::::::::       ÀøÄÅÄÝ
    ³ 1    J2                   1    J3                    ³ Ý
    ³                                                      ³ Ý
    ³                                                      ³ Ý
    ³               :                                   ÚÄÄÅÄÝ
    ³               JP10                                ÀøÄÅÄÝ
    À¿ Ü Ü Ü Ü Ü Ü ÜÚÄÄÄÄ¿ Ü Ü Ü Ü Ü Ü Ü Ü Ü Ü Ü Ü Ü ÜÚÄÄÄÄÙ Ý
     ÀÄßÄßÄßÄßÄßÄßÄßÙ    ÀÄßÄßÄßÄßÄßÄßÄßÄßÄßÄßÄßÄßÄßÄßÙ      Ý
                                                             Ý

            Detail on JP    1 2 3 4 5 6     7 8 9
                            : : : : : :     : : :
                            ³ ³ ÀÄÂÄÙ ³     ³ ³ ³
     *  Normal   IRQ 14     1 0   ³   ³     ³ ³ 0 Precompensation = 125ns *
        Delayed  IRQ 14     0 1   ³   ³     ³ ³ 1 Precompensation = 187ns
     !  Disabled IRQ 14     0 0   ³   ³     ³ ³
                                  ³   ³     ³ 0   Single speed floppy *
        Reserved ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ   ³     ³ 1   Dual speed floppy
                                      ³     ³
     * Primary Floppy Address (3F7h)  0     0 Primary IDE Address (1F7h) *
   ! Secondary Floppy Address (370h)  1     1 Secondary IDE Address (170h) !

       * = Default Setting, ! = 3_Drives Setting, 1 = ON, 0 = OFF.



===== ST412 MFM RLL Controllers ==============

Adaptec ACB-2370B  ST412 Interface (RLL)


ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ Ýßßßß
³ ³³³³                    Data 1      Data 0      Hard               ÚÄÄÅÄÝ
³ ÏÏÏÏ                    %::::::::%  %::::::::%  %:::::::::::::::%  ÀøÄÅÄÝ
³ LED                     1           1           1                     ³ Ý
³                                                                       ³ Ý
³    1øø                                                                ³ Ý
³    2øøÄÄ JP6                                                          ³ Ý
³    3øø                                               JP14             ³ Ý
³    4øø                                              1øøø              ³ Ý
³    5øø                                                                ³ Ý
³                                                                    ÚÄÄÅÄÝ
³                      JP13                                          ÀøÄÅÄÝ
³                     1øøøø                                             ³ Ý
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ Ü Ü Ü Ü Ü Ü ÜÚÄÄÄ¿ Ü Ü Ü Ü Ü Ü Ü Ü Ü Ü Ü Ü Ü ÜÚÄÄÄÄÙ Ý
                   ÀÄßÄßÄßÄßÄßÄßÄßÙ   ÀÄßÄßÄßÄßÄßÄßÄßÄßÄßÄßÄßÄßÄßÄßÙ      Ý
                                                                          Ý
     JP6  Hard   Drive Port Address:   Primary 1F0h jumper 1   open *
                                     Secondary 170h   ""     closed !

     JP13 Hard Drive Interrupt Req :    IRQ14       pins 1-2 closed *
                                        IRQ15       pins 2-3 closed
                                        Disabled    pins all   open !

     JP14 Bios Memory Address      :    C800-CBFFh  pins 1-2 closed *
                                        CC00-CFFFh  pins 2-3 closed
                                        Disabled    pins 1-2-3 open !

       * = Default Setting, ! = 3_Drives Setting, 1 = ON, 0 = OFF.



Adaptec ACB-2372B  ST412 Interface (RLL)

                                         ÚÄÄÄÄÄ Hard Drive Controller
ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ³ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ Ýßßßß
³ ³³³³     1234567              1¿  1¿  1¿  1¿Ä Floppy Drive         ÚÄÄÅÄÝ
³ ÏÏÏÏ     :::::::              ::  ::  ::  ::                       ÀøÄÅÄÝ
³ LED            ³              ::  ::  ::  ::                          ³ Ý
³            JP2 Ù              ÀÙ  ÀÙ  ::  ::                          ³ Ý
³                                ³   ³  ::  ::                          ³ Ý
³                   HDD 1 Data ÄÄÙ   ³  ::  ::                          ³ Ý
³                   HDD 0 Data ÄÄÄÄÄÄÙ  ÀÙ  ÀÙ                          ³ Ý
³                                                                       ³ Ý
³                                    ø4 JP7                             ³ Ý
³                                  1øøø3                             ÚÄÄÅÄÝ
³                      JP13   JP22       JP21   JP20                 ÀøÄÅÄÝ
³                     1øøø    øøø        øøø    øøø                     ³ Ý
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ Ü Ü Ü Ü Ü Ü ÜÚÄÄÄ¿ Ü Ü Ü Ü Ü Ü Ü Ü Ü Ü Ü Ü Ü ÜÚÄÄÄÄÙ Ý
                   ÀÄßÄßÄßÄßÄßÄßÄßÙ   ÀÄßÄßÄßÄßÄßÄßÄßÄßÄßÄßÄßÄßÄßÄßÙ      Ý
                                                                          Ý
     JP2  Hard   Drive Port Address:   Primary 1F0h jumper 1   open *
                                     Secondary 170h   ""     closed !

     JP2  Floppy Drive Port Address:   Primary 3F0h jumper 2   open *
                                     Secondary 370h   ""     closed !


     JP7  Bios Memory Address      :    C800-CBFFh  pins 1-2 closed *
                                        CC00-CFFFh  pins 2-3 closed
                                        Disabled    pins 2-4 closed !

     JP13 Hard Drive Interrupt Req :    IRQ14       pins 1-2 closed *
                                        IRQ15       pins 2-3 closed
                                        Disabled    pins 1-2-3 open !

       * = Default Setting, ! = 3_Drives Setting, 1 = ON, 0 = OFF.



Adaptec ACB-2372C  ST412 Interface (RLL)                      ÚÄÄÄ JP8
        ACB-2370C                                             ³ ÚÄ JP9
                                                    JP7 Ä¿    ³ ³
ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ³ÄÄÄÄ³Ä³ÄÄÄÄÄÄÄ¿ Ýßßßß
³ ³³³³           1          1¿  1¿  1¿  1¿              1ø    ø ø    ÚÄÄÅÄÝ
³ ÏÏÏÏ    ::::::::          ::  ::  ::  ::               ø    ø ø    ÀøÄÅÄÝ
³ LED       ³               ::  ::  ::  ::               ø              ³ Ý
³           ÀJP2            ÀÙ  ÀÙ  ::  ::                              ³ Ý
³                            ³   ³  ::  ::                              ³ Ý
³                            ³   ³  ::  ::                              ³ Ý
³                            ³   ³  ÀÙ  ÀÙ                              ³ Ý
³                            ³   ³   ³   ÀÄ Floppy Drive                ³ Ý
³                            ³   ³   ÀÄÄÄÄÄ Hard Drive Controller       ³ Ý
³                            ³   ÀÄÄÄÄÄÄÄÄÄ HDD 0 Data               ÚÄÄÅÄÝ
³                            ÀÄÄÄÄÄÄÄÄÄÄÄÄÄ HDD 1 Data               ÀøÄÅÄÝ
³                                                                       ³ Ý
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ Ü Ü Ü Ü Ü Ü ÜÚÄÄÄ¿ Ü Ü Ü Ü Ü Ü Ü Ü Ü Ü Ü Ü Ü ÜÚÄÄÄÄÙ Ý
                   ÀÄßÄßÄßÄßÄßÄßÄßÙ   ÀÄßÄßÄßÄßÄßÄßÄßÄßÄßÄßÄßÄßÄßÄßÙ      Ý
                                                                          Ý
     JP2  Hard   Drive Port Address:   Primary 1F0h pins 1-2 open   *
                                     Secondary 170h pins 1-2 closed !

     JP7  Bios Memory Address      :    C800-CBFFh  pins 1-2 closed *
                                        CC00-CFFFh  pins 2-3 closed
                                        Disabled    pins 1-2-3 open !

     JP8  Floppy Drive Port Address:            Primary 3F0h open   *
                                              Secondary 370h closed !

     JP9  Floppy Drive Enable      :               Enabled   open   *
                                                  Disabled   closed !

       * = Default Setting, ! = 3_Drives Setting, 1 = ON, 0 = OFF.

      ³
   Þ  ³ Metal Clamp
   ÞÄÄÅÄÄÄÄÄ¿
   Þ  ³  0  ³    Perspective: Looking at the backside of the card
   ÞÄÄÅÄÄÄÄÄÙ
   Þ  ³            8-bit long slot             16-bit short slot
   Þ  ³_____      31 total contacts        ___ 18 total contacts______
   Þ        ÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝ   ÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝ
   Þ                                                ³
   Þ                                               D7 (IRQ14) Tape over
                                              count 7 spaces from left or
                                                   12 spaces from right

         Note: Many manufacturers only plate the contacts that will be
               needed on the card.  Be sure to count spaces, not
               actual plated contacts. (READ App Note # 10)



Adaptec ACB-231x  ST412 Interface models.


ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ Ýßßßß
³ ³³³³           1          1¿  1¿  1¿  1¿                           ÚÄÄÅÄÝ
³ ÏÏÏÏ      ::::::          ::  ::  ::  ::                           ÀøÄÅÄÝ
³ LED       ³               ::  ::  ::  ::                              ³ Ý
³           ÀJP6            ÀÙ  ÀÙ  ::  ::                              ³ Ý
³                   JP10     ³   ³  ::  ::                              ³ Ý
³                   ³  1     ³   ³  ::  ::                              ³ Ý
³                   ÀÄÄ ooo  ³   ³  ÀÙ  ÀÙ                              ³ Ý
³                   ÚÄÄ ooo  ³   ³   ³   ÀÄ Floppy Drive                ³ Ý
³                   ³  1     ³   ³   ÀÄÄÄÄÄ Hard Drive Controller       ³ Ý
³                   ³        ³   ÀÄÄÄÄÄÄÄÄÄ HDD 0 Data               ÚÄÄÅÄÝ
³                   JP11     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄ HDD 1 Data               ÀøÄÅÄÝ
³                                                                       ³ Ý
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ Ü Ü Ü Ü Ü Ü ÜÚÄÄÄ¿ Ü Ü Ü Ü Ü Ü Ü Ü Ü Ü Ü Ü Ü ÜÚÄÄÄÄÙ Ý
                   ÀÄßÄßÄßÄßÄßÄßÄßÙ   ÀÄßÄßÄßÄßÄßÄßÄßÄßÄßÄßÄßÄßÄßÄßÙ      Ý
                                                                          Ý
     JP10 Floppy Drive Port Address:   Primary 3F0h pins 1-2 closed *
                                     Secondary 370h pins 1-2 open   !

     JP11 Hard   Drive Port Address:   Primary 1F0h pins 1-2 closed *
                                     Secondary 170h pins 1-2 open   !

       * = Default Setting, ! = 3_Drives Setting, 1 = ON, 0 = OFF.

      ³
   Þ  ³ Metal Clamp
   ÞÄÄÅÄÄÄÄÄ¿
   Þ  ³  0  ³    Perspective: Looking at the backside of the card
   ÞÄÄÅÄÄÄÄÄÙ
   Þ  ³            8-bit long slot             16-bit short slot
   Þ  ³_____      31 total contacts        ___ 18 total contacts______
   Þ        ÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝ   ÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝ
   Þ                                                ³
   Þ                                               D7 (IRQ14) Tape over
                                              count 7 spaces from left or
                                                   12 spaces from right

         Note: Many manufacturers only plate the contacts that will be
               needed on the card.  Be sure to count spaces, not
               actual plated contacts. (READ App Note # 10)



Data Technology Corp. (DTC) DTC728x ST412 Interface models


ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ Ýßßßß
³ ³³³³                      1¿  1¿  1¿  1¿             W4 Ä  oo      ÚÄÄÅÄÝ
³ ÏÏÏÏ       JP6 ¿          ::  ::  ::  ::             W7 Ä  oo      ÀøÄÅÄÝ
³ LED            oo         ::  ::  ::  ::                              ³ Ý
³                           ÀÙ  ÀÙ  ::  ::                              ³ Ý
³                           ³    ³  ::  ::                              ³ Ý
³               HDD 1 Data ÄÙ    ³  ::  ::         ÚÄÄ W2               ³ Ý
³               HDD 0 Data ÄÄÄÄÄÄÙ  ÀÙ  ÀÙ         ³                    ³ Ý
³    Hard Drive Controller ÄÄÄÄÄÄÄÄÄÄÙ   ³       : : :                  ³ Ý
³             Floppy Drive ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ       ³   À W3               ³ Ý
³                                                ³                   ÚÄÄÅÄÝ
³                                                ÀÄÄÄÄ W5            ÀøÄÅÄÝ
³                                                                       ³ Ý
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ Ü Ü Ü Ü Ü Ü ÜÚÄÄÄ¿ Ü Ü Ü Ü Ü Ü Ü Ü Ü Ü Ü Ü Ü ÜÚÄÄÄÄÙ Ý
                   ÀÄßÄßÄßÄßÄßÄßÄßÙ   ÀÄßÄßÄßÄßÄßÄßÄßÄßÄßÄßÄßÄßÄßÄßÙ      Ý
                                                                          Ý
    Primary Port Addresses Hard 1F0h and Floppy 3F0h : W2 and W3 open *
  Secondary Port Addresses Hard 170h and Floppy 370h : W2 and W3 closed !

       * = Default Setting, ! = 3_Drives Setting, 1 = ON, 0 = OFF.

      ³
   Þ  ³ Metal Clamp
   ÞÄÄÅÄÄÄÄÄ¿
   Þ  ³  0  ³    Perspective: Looking at the backside of the card
   ÞÄÄÅÄÄÄÄÄÙ
   Þ  ³            8-bit long slot             16-bit short slot
   Þ  ³_____      31 total contacts        ___ 18 total contacts______
   Þ        ÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝ   ÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝ
   Þ                                                ³
   Þ                                               D7 (IRQ14) Tape over
                                              count 7 spaces from left or
                                                   12 spaces from right

         Note: Many manufacturers only plate the contacts that will be
               needed on the card.  Be sure to count spaces, not
               actual plated contacts. (READ App Note # 10)



Western Digital WD1003V, WD1006V ST412 -MM (MFM) Interface models


ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ Ýßßßß
³ ³³³³ Data 1      Data 0      Hard               Floppy             ÚÄÄÅÄÝ
³ ÏÏÏÏ %::::::::%  %::::::::%  %:::::::::::::::%  %:::::::::::::::%  ÀøÄÅÄÝ
³ LED  1           1           1                  1                     ³ Ý
³                                                                       ³ Ý
³                    JP1                                                ³ Ý
³                    ::::                                               ³ Ý
³                   1                              oo Ä JP3 Hard        ³ Ý
³                                                  oo Ä JP4 Floppy      ³ Ý
³                                                  oo - JP5             ³ Ý
³                                                                    ÚÄÄÅÄÝ
³                                                              :     ÀøÄÅÄÝ
³                                                              JP6      ³ Ý
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ Ü Ü Ü Ü Ü Ü ÜÚÄÄÄ¿ Ü Ü Ü Ü Ü Ü Ü Ü Ü Ü Ü Ü Ü ÜÚÄÄÄÄÙ Ý
                   ÀÄßÄßÄßÄßÄßÄßÄßÙ   ÀÄßÄßÄßÄßÄßÄßÄßÄßÄßÄßÄßÄßÄßÄßÙ      Ý
                                                                          Ý

      JP3 Hard   Drive Port Address:   Primary 1F0h  = open   *
                                     Secondary 170h  = closed !

      JP4 Floppy Drive Port Address:   Primary 3F0h  = open   *
                                     Secondary 370h  = closed !

       * = Default Setting, ! = 3_Drives Setting, 1 = ON, 0 = OFF.

      ³
   Þ  ³ Metal Clamp
   ÞÄÄÅÄÄÄÄÄ¿
   Þ  ³  0  ³    Perspective: Looking at the backside of the card
   ÞÄÄÅÄÄÄÄÄÙ
   Þ  ³            8-bit long slot             16-bit short slot
   Þ  ³_____      31 total contacts        ___ 18 total contacts______
   Þ        ÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝ   ÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝ
   Þ                                                ³
   Þ                                               D7 (IRQ14) Tape over
                                              count 7 spaces from left or
                                                   12 spaces from right

         Note: Many manufacturers only plate the contacts that will be
               needed on the card.  Be sure to count spaces, not
               actual plated contacts. (READ App Note # 10)



Western Digital WD1003V, WD1006V ST412 -SR (RLL) Interface models


ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ Ýßßßß
³ ³³³³ Data 1      Data 0      Hard               Floppy             ÚÄÄÅÄÝ
³ ÏÏÏÏ %::::::::%  %::::::::%  %:::::::::::::::%  %:::::::::::::::%  ÀøÄÅÄÝ
³ LED  1           1           1                  1                     ³ Ý
³                                                     Ú JP2 Bios        ³ Ý
³                    JP1                              ³ enabled open    ³ Ý
³                    :::                              ³ disabled off    ³ Ý
³                   1                              oo Ù                 ³ Ý
³                                                  oo Ä JP3 Hard        ³ Ý
³                                                  oo - JP4 Floppy      ³ Ý
³                                                                    ÚÄÄÅÄÝ
³                                                              :     ÀøÄÅÄÝ
³                                                  oo - JP5    JP6      ³ Ý
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ Ü Ü Ü Ü Ü Ü ÜÚÄÄÄ¿ Ü Ü Ü Ü Ü Ü Ü Ü Ü Ü Ü Ü Ü ÜÚÄÄÄÄÙ Ý
                   ÀÄßÄßÄßÄßÄßÄßÄßÙ   ÀÄßÄßÄßÄßÄßÄßÄßÄßÄßÄßÄßÄßÄßÄßÙ      Ý
                                                                          Ý
     JP2 On-board Bios status:       enabled = open   *
                                    disabled = closed !

     JP3 Hard   Drive Port Address:   Primary 1F0h  = open   *
                                     Secondary 170h  = closed !

     JP4 Floppy Drive Port Address:   Primary 3F0h  = open   *
                                     Secondary 370h  = closed !

       * = Default Setting, ! = 3_Drives Setting, 1 = ON, 0 = OFF.

      ³
   Þ  ³ Metal Clamp
   ÞÄÄÅÄÄÄÄÄ¿
   Þ  ³  0  ³    Perspective: Looking at the backside of the card
   ÞÄÄÅÄÄÄÄÄÙ
   Þ  ³            8-bit long slot             16-bit short slot
   Þ  ³_____      31 total contacts        ___ 18 total contacts______
   Þ        ÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝ   ÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝ
   Þ                                                ³
   Þ                                               D7 (IRQ14) Tape over
                                              count 7 spaces from left or
                                                   12 spaces from right

         Note: Many manufacturers only plate the contacts that will be
               needed on the card.  Be sure to count spaces, not
               actual plated contacts. (READ App Note # 10)

*********************************************************************


Dustbowl Designs, Inc.          |
9606 N.E. 4th Street            |
Midwest City, Oklahoma   73130  |
U.S.A.                          | CIS: 71062,2542

phone:
(405) 741-4705 ordering, tech support, general information
(405) 741-2721 BBS (Tech Support, Hard disk drive shareware, drive
                    specs, Online Shareware Registration for VISA or
                    MasterCard orders! )

    NAME : ___________________________________Password:_________________

 ADDRESS : _____________________________________________________________

           ___________________________________________ ZIP :____________

TELEPHONE: ___________________________________________ (Day & Night)

COMMENTS : _____________________________________________________________

           _____________________________________________________________

           ___________________________________________________________

     Qty    Description                            Each       Total

     ____   Special Upgrade from Registered v1.1    $0.00    THANKS!!
            to v2.1 4_Drives
     ____   3_Drives.HHD v2.1 Registration         $30.00     ________

     ____   4_Drives.HDD v2.1 Registration         $40.00     ________

     ____   Upgrade from v2.1 3_Drives             $10.00     ________
            to v2.1 4_Drives
                                                     Subtotal ________

  (Oklahoma residents add 6.5% sales tax)                 Tax ________

U.S. diskette orders add $3 shipping & handling, Foreign diskette
orders add $5 U.S. shipping. This also applies to Special Upgrade from
Registered v1.1 (If you want to download from our BBS put $0.00
dollars for shipping and write the password you'll be using next to
your name above.  Allow 7 days for Postal transit.)
                                                      Shipping ________


                                                       TOTAL $________
PAYMENT:
 [ ] Visa/MasterCard  [ ] Check (number ____________)
       (see below)       (make checks payable to Dustbowl Designs, Inc.)

 [ ] Cash US$         [ ] US$ Money Order (No foreign  currency)


Total amount enclosed or authorized: $________________


_______________________________________________________________________
If Payment by Visa or MasterCard:

We can only accept Visa or MasterCards (no American Express, please.)
We will need the following information:

Credit card number: ______________________________________________________

Expiration date: _________________________________________________________

Bank the card's drawn on: ________________________________________________

The name as it appears on the card: ______________________________________

The signature of its owner authorizing us
to debit it for the amount indicated above: ______________________________

_______________________________________________________________________

 THE FOLLOWING INFORMATION IS REQUIRED FOR REGISTRATION:

 HARD DISK  #1 MAKE ____________________MODEL_________________SIZE________

 HARD DISK  #2 MAKE ____________________MODEL_________________SIZE________

 HARD DISK  #3 MAKE ____________________MODEL_________________SIZE________

 HARD DISK  #4 MAKE ____________________MODEL_________________SIZE________

 CONTROLLER #1 MAKE_____________________MODEL_________________

 CONTROLLER #1 MAKE_____________________MODEL_________________


 COMPUTER   286 ( )   386 ( )  486 ( )      OTHER ( ) ______________________
             SX ( )    DX ( )  DX2 ( )  OverDrive ( )

 OPERATING SYSTEM / DOS VERSION ___________________

 VIDEO CARD  Standard VGA ( )  Super VGA ( )  Coproccessed/Accelerator  ( )

 MOUSE      YES ( )  NO ( )

 JOYSTICK   YES ( )  NO ( )

 MEMORY     640 ( )  1 meg ( )   2 meg ( )   4 meg ( )  more ( ) ______

 MODEM      YES ( )  NO ( )  .... BAUD RATE ___________________________

 HOW DID YOU ACQUIRE THIS PROGRAM: bbs name &#__________________________

Fold the pages at the break below with print facing out.  Fold letter style
with mailing address exposed.  Tape/staple edges, enclosing payment.



___________________________                                          .-----.
                                                                     |Place|
___________________________                                          |Stamp|
                                                                     |Here |
___________________________                                          `-----'



                                     Dustbowl Designs, Inc.
                                     9606 N.E. 4th Street
                                     Midwest City, OK    73130
                                     U.S.A.
3_Drives v1.5



-=EOF: 3_DRIVES.DOC=-