JP Software

                            4DOS Application Notes

                        Version 4.02 -- March 30, 1993


   Copyright 1988 - 1993, JP Software Inc., All Rights Reserved.  Published
   by JP Software Inc., P.O. Box 1470, E. Arlington, MA 02174 USA, (617)
   646-3975.


   This file provides information on using 4DOS with a variety of other
   software products.  It is intended for use whenever you have a question
   about using another product with 4DOS, or suspect a compatibility
   problem.

   Inclusion of a product in this file does NOT mean there are
   compatibility problems with it!  It only indicates that we have some
   information that may be useful to you when you use the product with
   4DOS.

   Items in this file which were changed in 4DOS 4.02 are marked with
   "4.02" in the left margin.  Other items have not been changed since
   version 4.01.

   This file is formatted at 58 lines per page, and contains form feeds and
   page footers.  It is somewhat long, so you may prefer to view it with a
   file viewer such as the 4DOS LIST command.  You can print this file on
   most PC printers using the command:

              copy appnotes.doc prn

   Printing it with a program that formats the pages is not likely to work
   due to the formatting included in the file.

   Our customers regularly ask us for recommendations on software to use
   with 4DOS.  While we can't tell you what is best for your use or your
   system, at the end of this file we have included some comments on
   software we like and have found useful on our own systems here at JP
   Software.










                                                               (3/93-4.02A)



   4DOS 4.02  [3-30-93]          APPNOTES.DOC                        page 1






                               Table of Contents

   Introduction  . . . . . . . . . . . . . . . . . . . . . . . . . . .    4

   General Information . . . . . . . . . . . . . . . . . . . . . . . .    5
      Running 4DOS along with COMMAND.COM  . . . . . . . . . . . . . .    5
      Executing DOS Commands from Your Applications: . . . . . . . . .    7
      Swapping to RAM Disks  . . . . . . . . . . . . . . . . . . . . .    8
      4DOS and Other Command Line Editing Programs . . . . . . . . . .    8
      4DOS and EXE File Compression Programs . . . . . . . . . . . . .    9
      Mouse Compatibility with 4DOS HELP . . . . . . . . . . . . . . .    9

   Information on Specific Products  . . . . . . . . . . . . . . . . .   10
      MS-DOS APPEND Command  . . . . . . . . . . . . . . . . . . . . .   10
      MS-DOS DATE and TIME Commands  . . . . . . . . . . . . . . . . .   11
      MS-DOS FASTOPEN Command  . . . . . . . . . . . . . . . . . . . .   12
      MS-DOS 4.0 and 5.0 FORMAT /S and SYS Command . . . . . . . . . .   12
      MS-DOS 6.0 MOVE Command  . . . . . . . . . . . . . . . . . . . .   12
      MS-DOS 4.0 and 5.0 SELECT Command  . . . . . . . . . . . . . . .   13
      MS-DOS 6.0 MEMMAKER Command  . . . . . . . . . . . . . . . . . .   13
      1DIR+ (Bourbaki) . . . . . . . . . . . . . . . . . . . . . . . .   13
      3COM Networks (3Com) . . . . . . . . . . . . . . . . . . . . . .   14
      AllClear (AllClear Software) . . . . . . . . . . . . . . . . . .   14
      Alpha 4 (Alpha Software) . . . . . . . . . . . . . . . . . . . .   15
      ANSI.SYS (various manufacturers) . . . . . . . . . . . . . . . .   15
      Bookshelf CD-ROM (Microsoft) . . . . . . . . . . . . . . . . . .   15
      DESQview (Quarterdeck) . . . . . . . . . . . . . . . . . . . . .   15
      DOORWAY BBS Software . . . . . . . . . . . . . . . . . . . . . .   17
      DR-DOS (Digital Research)  . . . . . . . . . . . . . . . . . . .   17
      Epsilon (Lugaru Software)  . . . . . . . . . . . . . . . . . . .   21
      Extra! 3270 Emulator . . . . . . . . . . . . . . . . . . . . . .   21
      FoxPro (Microsoft) . . . . . . . . . . . . . . . . . . . . . . .   21
      Hijaak (Inset Systems) . . . . . . . . . . . . . . . . . . . . .   21
      LapLink (Traveling Software) . . . . . . . . . . . . . . . . . .   22
      LOGIMENU (Logitech)  . . . . . . . . . . . . . . . . . . . . . .   22
      Manifest (Quarterdeck) . . . . . . . . . . . . . . . . . . . . .   22
      Netware (Novell) . . . . . . . . . . . . . . . . . . . . . . . .   22
      Novell MENU (Novell) . . . . . . . . . . . . . . . . . . . . . .   25
      OS/2 1.2, 1.3, and 2.0 (IBM / Microsoft) . . . . . . . . . . . .   25
      OS2SPEED DOS Sessioon Enhancer . . . . . . . . . . . . . . . . .   25
      Personal REXX (Quercus Systems)  . . . . . . . . . . . . . . . .   26
      QEMM and QRAM (Quarterdeck)  . . . . . . . . . . . . . . . . . .   27
      RBase (MicroRim) . . . . . . . . . . . . . . . . . . . . . . . .   28
      RoboComm Communications Software . . . . . . . . . . . . . . . .   28
      Software Carousel (SoftLogic Solutions)  . . . . . . . . . . . .   28
      TSRCOM Utilities (TurboPower Software) . . . . . . . . . . . . .   29
      UltraVision (Personics)  . . . . . . . . . . . . . . . . . . . .   29
      Windows 3.0 and 3.1 (Microsoft)  . . . . . . . . . . . . . . . .   30
      XyWrite (XyQuest)  . . . . . . . . . . . . . . . . . . . . . . .   30



   4DOS 4.02  [3-30-93]          APPNOTES.DOC                        page 2



      Programs Requiring PATH to be Under 128 Characters . . . . . . .   30
          Checkit (Touchstone); Computer Select CD-ROM (Ziff-Davis);
          RenderMan (AutoDesk); VINES Network (Banyan); Windows 3.0
          (Microsoft)

   Software For Use With 4DOS  . . . . . . . . . . . . . . . . . . . .   32

















































   4DOS 4.02  [3-30-93]          APPNOTES.DOC                        page 3




   Introduction
   ------------

   We have made every effort to ensure that this file is as accurate and up
   to date as possible.  Our information is based on our own
   investigations, reports from 4DOS beta testers, technical support calls,
   discussions with manufacturers of other products, and reports from our
   customers.  Unfortunately, varying conditions between systems or between
   software releases can easily invalidate the results of previous tests. 
   Therefore we cannot guarantee that every item in this file is accurate
   for all systems or will remain accurate over time; you may have to do
   your own testing to determine what works well on your system with the
   software you own.

   If you have a question or problem related to another program, first read
   through chapter 7 of the 4DOS manual ("Using 4DOS With Your Hardware And
   Software").  Chapter 7 gives general suggestions for using 4DOS with
   other products and for solving compatibility problems, and should always
   be used along with this file.

   If the information in Chapter 7 doesn't help, check below for both
   additional general suggestions which pertain to your question, and
   information on the specific product you are working with.  Please note
   that some products are listed by category rather than or in addition to
   specific listings by product name; check the Table of Contents carefully
   to see where any particular product may be covered.

   Many of the items below refer to the 4DOS.INI file.  See chapter 6 of
   the manual for a complete explanation of 4DOS.INI and the directives
   which can be used there.  If you have a printed manual, also check
   MANMOD.DOC for directives which were added or modified since the manual
   went to press.

   Virtually all of your software will work with 4DOS with no trouble.  If
   you do find an interaction or compatibility problem, it can probably be
   diagnosed easily with one of three methods:  checking this file for
   specific information; trying different 4DOS swapping methods; and
   testing for interactions by removing all drivers and TSRs which are not
   absolutely necessary and then replacing them one at a time.  These
   methods and other related techniques are described in Chapter 7 of the
   manual.

   Many popular software products are not covered in this file.  If a
   program does not appear here, it simply means that as far as we know no
   additional information is necessary or useful when using that program
   with 4DOS.

   If you have a question or problem related to how 4DOS works with other
   hardware or software products, and it isn't addressed in chapter 7 or by
   these notes, contact JP Software or your dealer for technical support.




   4DOS 4.02  [3-30-93]          APPNOTES.DOC                        page 4




   General Information
   -------------------

      Running 4DOS along with COMMAND.COM:

          You may find a very rare program which will not work under 4DOS,
          but runs properly under COMMAND.COM.  If you have determined that
          the problem cannot be solved through configuration changes or by
          eliminating or reconfiguring a third program which is causing the
          problem, use this section to see how to run 4DOS and COMMAND.COM
          together in order to diagnose such a problem.

          There are two methods of loading COMMAND.COM before another
          program.  The first is to load it only when a specific program is
          running.  This can be accomplished with the following command
          (assuming COMMAND.COM is in the root directory of drive C:):

                    c:\command /c progname options

          where "progname" is the program name (with path if necessary) and
          "options" are any parameters for the program.  This command will
          run COMMAND.COM, load and run the program, and upon exit from the
          program will exit from COMMAND.COM and return to 4DOS.  If this
          is necessary to run a specific program, it can be defined as an
          alias:

                    alias progname `c:\command /c progname %&`

          The "%&" passes all command line arguments on to the program.

          With this method, if the program is large COMMAND.COM may need to
          reload itself when the program exits.  It will not be able to do
          so unless the COMSPEC is set properly.  If you experience
          problems such as "Invalid COMMAND.COM" errors when using this
          method, use a batch file like the following to run the program in
          question (the SETLOCAL and ENDLOCAL cause COMSPEC to be restored
          to its previous value after the program exits).  You will need to
          modify this file if your copy of COMMAND.COM is not stored in the
          C:\ directory:

                    setlocal
                    set comspec=C:\COMMAND.COM
                    c:\command /c progname %&
                    endlocal

          The second method is more drastic:  you can start your system
          under COMMAND.COM, then run 4DOS.  This approach is rarely
          necessary, and will use about 4 - 5K of additional RAM for the
          resident portion of COMMAND.COM.  





   4DOS 4.02  [3-30-93]          APPNOTES.DOC                        page 5



          The following steps will set your system up to boot with
          COMMAND.COM, and run 4DOS automatically as part of the boot
          process:

              (1) Set up the SHELL= statement in CONFIG.SYS to run
              COMMAND.COM, or leave it out entirely.  In other words, set
              it up just as you would if 4DOS were not on your system.

              (2) Separate your AUTOEXEC file into two parts:  part 1,
              which remains in AUTOEXEC.BAT, should contain any commands
              you wish to have COMMAND.COM execute before 4DOS is started. 
              This might include loading any TSRs which you cannot get to
              load properly under 4DOS.  Part 2, which you must place in a
              separate batch file (we suggest the name 4DAUTO.BAT, but you
              can use any name with a .BAT or .BTM extension), should
              contain the commands you wish to have 4DOS execute when it is
              started.

              (3) Place the following line as the last line in the modified
              AUTOEXEC.BAT:

                    4DOS parameters filename

              where "parameters" represents the appropriate 4DOS parameters
              for swapping, environment and history size, etc. (see the
              Installation section of the manual), and "filename" is the
              name of the new batch file you created for part 2 of your old
              AUTOEXEC file.  Do NOT include a /P in the "parameters" or
              4DOS will re-run AUTOEXEC and therefore load itself again, ad
              infinitum!

              (4) Be sure that KSTACK.COM is loaded in your AUTOEXEC.BAT
              file or your 4DOS startup file if you wish to use the 4DOS
              KEYSTACK command.

          This will load COMMAND.COM, execute the commands in AUTOEXEC,
          load 4DOS, execute the commands in your new batch file, and then
          give you the normal 4DOS prompt.

          There is one drawback to this second approach:  because 4DOS is
          not loaded with a /P, the EXIT command will return you to
          COMMAND.COM if you inadvertently enter it at the primary shell
          prompt.  You can get around this by including the /P parameter
          despite the caution above, and then placing the following line at
          the start of AUTOEXEC.BAT:

                    if "%@eval[2+2]"=="4" quit

          This line tests the 4DOS variable function %@EVAL, which will
          return "4" under 4DOS and remain unchanged under COMMAND.COM.  If
          %@EVAL returns a "4" the statement QUITs the batch file,
          preventing the infinite loop described above.



   4DOS 4.02  [3-30-93]          APPNOTES.DOC                        page 6





      Executing DOS Commands from Your Applications:

   4.02   In general you should have no trouble running DOS commands or
          "shelling to DOS" from within your applications.  If you do,
          first follow the instructions in Chapter 7 of the manual, check
          your COMSPEC setting, and check that enough memory is available
          for 4DOS to execute as a secondary shell.

          If those techniques do not resolve the problem, it may be due to
          one of the issues covered below:  either the application was
          developed with a compiler that does not handle the format of
          4DOS.COM properly, or it is using interrupt 2E and you have
          disabled interrupt 2E support.

          Compilers and the Format of 4DOS.COM:

              If you have an application which can run DOS commands from
              inside the application and that particular feature does not
              work, try to determine if the application was developed with
              Borland C or Lattice C.  Some versions of these compilers
              cannot properly execute 4DOS.COM to start a secondary shell,
              because 4DOS.COM (despite its name) is really an EXE file,
              and the libraries shipped with these compilers do not use the
              proper method to determine what type of file they are
              running.

              If you suspect sucha problem, make a copy of 4DOS.COM named
              4DOS.EXE, and SET your COMSPEC variable to this file, for
              example:

                    d:\4dos> copy 4dos.com 4dos.exe
                    d:\4dos> set comspec=d:\4dos\4dos.exe

              Then run the application in question and see if it works.  If
              so, you can use the above workaround to run the application. 
              Be sure to contact the application vendor to see if they have
              an update which corrects this problem.

              For users of Borland C and C++, a fix is available for this
              problem (the fix updates certain functions in the Borland C
              run-time library).  You can download this fix from the
              Borland support area on CompuServe, and it is distributed
              with newer copies of the Borland compilers.

          Re-Enabling Interrupt 2E Support:

              COMMAND.COM contains an undocumented feature which allows
              programs to execute DOS commands by passing the command
              through software interrupt number 2E (hex).  Very few
              programs use this feature, but full, documented support for



   4DOS 4.02  [3-30-93]          APPNOTES.DOC                        page 7



              it is available within 4DOS for those circumstances where
              it's needed.

              Interrupt 2E support is normally enabled within 4DOS, but can
              be disabled to save memory (INT 2E support requires about 100
              bytes of resident memory).

              If you have a program which is supposed to execute DOS
              commands and it does not work under 4DOS, check your 4DOS.INI
              file.  If you see a line like this:

                    FullINT2E = No

              then you have disabled INT 2E support.  If the line is there,
              try removing this line or replacing it with one reading:

                    FullINT2E = Yes

              to re-enable support for interrupt 2E, then chcek whether
              your program works properly.

              See Appendix C of the ASCII manual, or the MANMOD.DOC file if
              you have a printed manual, for technical details on the INT
              2E interface.


      Swapping to RAM Disks:

          In order to swap the primary shell to a RAM disk the RAM disk
          must be completely defined in CONFIG.SYS via a DEVICE= statement
          (most RAM disks are set up this way).  RAM disks completely or
          partially defined in AUTOEXEC.BAT (such as the RAM disk / cache
          combination in Multisoft's PC Kwik Power Pak) cannot be used for
          swapping the primary shell, because AUTOEXEC.BAT has not been
          executed at the time that the root shell is loaded, and hence the
          RAM disk does not exist at that point.


      4DOS and Other Command Line Editing Programs:

          Programs such as Anarkey (Moderne Software), PCED (Cove
          Software), and ReDOS (Multisoft) will work properly with 4DOS. 
          However these programs require the use of SETDOS /L1 to operate,
          which will disable 4DOS's command recall and command line
          editing.  In most cases you will be able to switch back and forth
          between 4DOS editing and the other editor by toggling the SETDOS
          /L state.

          When another editor is used 4DOS's command history will be
          maintained, and can be viewed with HISTORY, but will not be
          available for recall until a SETDOS /L0 is executed.  4DOS
          aliases, executable extensions, and other features will be active



   4DOS 4.02  [3-30-93]          APPNOTES.DOC                        page 8



          regardless of the SETDOS /L state.  Aliases will be processed
          after any processing done by the other editing program.  You must
          use care with other programs that provide an aliasing capability
          to avoid confusion if a command is expanded by both the other
          program and 4DOS!


      4DOS and EXE File Compression Programs:

          If you use a file compression program like PKLITE, LZEXE, or
          DIET, you must use caution when compressing 4DOS files.  Most
          such programs should be able to compress the 4DOS.COM file with
          no trouble.  However if you have a copy of 4DOS that you intend
          to brand with your name and serial number, you must brand it
          BEFORE you run the file compression program, or the BRAND program
          will fail.  Similarly, HELPCFG will not be able to modify your
          HELP system colors if you compress the 4HELP.EXE program.  The
          only compressed program files distributed with 4DOS are
          HELPCFG.EXE, and 4MAKE.EXE on the 4DOS / 4OS2 Utility Disk; these
          files are compressed with the PKLite Professional package.


      Mouse Compatibility with 4DOS HELP:

          The 4DOS HELP system depends on correct operation of your mouse
          driver.  If your mouse doesn't work in HELP, or you have trouble
          with mouse "droppings" (characters left behind by the mouse
          cursor), be sure you have the most up to date working version of
          your mouse driver that is available.

          Users of Microsoft serial and PS/2 mice may notice a long delay
          when the HELP system starts.  This is due to the long
          initialization time required for these mice, and is a function of
          the mouse driver, not the HELP system.  If you don't use the
          mouse in HELP and want to speed up HELP startup, set
          HelpOptions = /X in 4DOS.INI.  This will disable all mouse access
          in the HELP system.


















   4DOS 4.02  [3-30-93]          APPNOTES.DOC                        page 9




   Information on Specific Products
   --------------------------------

   The information below is listed alphabetically by product, with
   manufacturers' names included.  MS-DOS commands are listed before other
   software products.

   Items marked with two asterisks [**] after the product name were
   supplied by users, and have not been tested by JP Software.


      MS-DOS APPEND Command:

          Unlike most other commands in MS-DOS, APPEND has both an external
          portion and an undocumented internal portion.  The first time
          APPEND is run the external portion is executed, and loaded into
          memory as a TSR (memory-resident program).  Subsequent uses of
          APPEND to adjust the APPEND path use an undocumented internal
          interface between COMMAND.COM and the TSR portion of APPEND.

          4DOS does not support the internal portion of APPEND command. 
          This means that you cannot change the APPEND path directly from
          4DOS.  However you can still use APPEND with 4DOS.

          APPEND should initially be loaded in the usual way, from AUTOEXEC
          or any other batch file, or from the command line.  However to
          change the APPEND path after APPEND has been loaded for the first
          time, you must run APPEND from COMMAND.COM, not from 4DOS.  To do
          this, enter the following command (modify the command
          appropriately if COMMAND.COM is not in the directory C:\):

                    c:\command /c append [new append path list]

          You could also set up a 4DOS alias to do the above command for
          you, for example:

                    alias app `c:\command /c append`

          which would be invoked with the command

                    app [new path list]

          The /X switch can be used, and it will affect 4DOS directory
          searches for many 4DOS commands (as it does for COMMAND.COM). 
          Please note that this makes APPEND very dangerous:  if you APPEND
          a directory with /X and then (say) delete *.BAK when no such
          files exist in the current directory, then the .BAK files in the
          APPENDed directory will be deleted instead.

          The APPEND /E switch will not work with 4DOS.




   4DOS 4.02  [3-30-93]          APPNOTES.DOC                       page 10



      !   CAUTION:  In our opinion APPEND is an extremely dangerous
          command.  It is capable of "fooling" programs into thinking they
          are accessing one file when they are really accessing another one
          with the same name in a different directory.  This can either do
          just what you want, or cause all sorts of trouble, depending on
          the circumstances.  In particular, this behavior can cause 4DOS
          to place descriptions which go with files in one directory in the
          description file for another directory, because with APPEND
          running 4DOS can't tell whether APPEND has opened a file
          different from the one it asked for.

          If you must use APPEND to make certain applications work, we
          STRONGLY suggest that you set up the aliases described above, and
          load APPEND in AUTOEXEC.BAT with an empty path.  Then, for each
          application, set up an alias to run it that is similar to the
          following:

              alias myprog `app c:\mydata^d:\util\myprog.exe^app ;`

          This alias sets the APPEND path, runs the application, and clears
          the APPEND path.  When used in this way APPEND is less likely to
          cause trouble because it is disabled except when it is explicitly
          needed.

   4.02   In MS-DOS 4.0 and above, and in OS/2 2.x, the APPEND /PATH:OFF
          switch mitigates this problem somewhat; in particular it will
          keep 4DOS file description files from getting mixed up between
          directories.  For this reason 4DOS will automatically set this
          switch if it detects that you are running APPEND and DOS 4.0 or
          above.


      MS-DOS DATE and TIME Commands:

          Most PC systems automatically set the hardware clock date and
          time (which is maintained while the system is turned off, and is
          different from the DOS date and time) when the corresponding DOS
          command is executed.  In most such cases the hardware
          manufacturer has implemented this capability within the BIOS
          built into the system.  This type of implementation is compatible
          with 4DOS, and the 4DOS DATE and TIME commands will set the
          hardware clock properly.

          A very small number of manufacturers have modified the version
          COMMAND.COM which they sell with their PCs to perform this
          function.  In these cases, 4DOS's DATE and TIME commands, which
          do not have such hardware-specific modifications, will not set
          the hardware clock.  If you normally set the hardware clock's
          date and time with DOS commands, and they don't work under 4DOS,
          first check your clock's battery!  If it's OK, either run a
          secondary copy of COMMAND.COM to set the date and time, or invoke
          your system's SETUP or other utility program to do so.



   4DOS 4.02  [3-30-93]          APPNOTES.DOC                       page 11




      MS-DOS FASTOPEN Command:

          The MS-DOS FASTOPEN command generally works with 4DOS, but does
          not properly detect renamed directories, and may have similar
          problems when directories are removed.  This is a problem in
          FASTOPEN, not in 4DOS.  If you use FASTOPEN and rename a
          directory with the 4DOS REN command, then do a DIR command, you
          may see the old name and not the new one displayed; you may also
          occasionally have trouble accessing files under the new name. 
          You can usually solve this problem by including a DiskReset = Yes
          directive in 4DOS.INI.  If DiskReset = Yes does not work, the
          only other solution we are aware of is to reboot your system
          after renaming a directory.

          Our opinion is that, if you have the memory to support it, a disk
          caching program will provide a much greater and more effective
          performance improvement than FASTOPEN.


      MS-DOS 4.0 and 5.0 FORMAT /S and SYS Commands:

   4.02   The FORMAT /S and SYS commands in DOS 4 and DOS 5 will copy
          4DOS.COM to a newly formatted floppy disk and rename it
          COMMAND.COM, which may not be what you want and is confusing at
          best.  See the discussion of "4DOS and DOS" in Chapter 7 of the
          manual for more information on this issue.  This problem has been
          addressed in MS-DOS 6.0, where the FORMAT /S and SYS commands
          will properly copy COMMAND.COM to the floppy disk even when 4DOS
          is the command processor.


      MS-DOS 6.0 MOVE Command:

   4.02   MS-DOS 6 includes an external MOVE command which is generally
          compatible with the 4DOS MOVE command.

          The syntax and features of the MS-DOS 6 MOVE command are slightly
          different than those offered by 4DOS's MOVE, so batch files
          written for one command may not work exactly the same way with
          the other, especially if more advanced or complex features are
          used.  If you write batch files which use both commands, check
          the 4DOS and MS-DOS 6 documentation for your particular usage.

          One difference is that, unlike 4DOS, the MS-DOS 6 MOVE command
          will rename directories if the source refers to a directory, the
          destination name is in the same path, and the destination
          directory does not exist.  For example, if you enter this
          command:

                    c:\data> move olddir newdir




   4DOS 4.02  [3-30-93]          APPNOTES.DOC                       page 12



          when OLDDIR exists and NEWDIR does not, then MS-DOS 6 MOVE will
          rename OLDDIR to NEWDIR, whereas 4DOS will treat NEWDIR as a
          destination file name (not a directory name).  If you use
          MOVE /D, 4DOS will treat NEWDIR as a directory name, and prompt
          you for whether to create the directory, but 4DOS will not rename
          OLDDIR automatically as MS-DOS 6 MOVE will.  For more details on
          how 4DOS MOVE handles destination names, see MOVE in the 4DOS
          manual or online help.


      MS-DOS 4.0 and 5.0 SELECT Command:

          In MS-DOS 4.0 and 5.0, a SELECT command was included.  This
          external command is totally unrelated to the 4DOS internal SELECT
          command.  If you need to use both, you can set up aliases to
          adjust how the command names are handled.  For example, the
          following two aliases set up SELECT to access the DOS 4.0
          external SELECT command (assumed to be stored in
          C:\DOS\SELECT.EXE), and SEL to access the internal 4DOS SELECT
          command:

                    alias select c:\dos\select.exe
                    alias sel *select


      MS-DOS 6.0 MEMMAKER Command:

   4.02   4DOS 4.02 is fully compatible with MemMaker.  MemMaker adds
          commands to the end of your AUTOEXEC.BAT file during its
          operation, and removes them when it is finished.  If for some
          reason you have used a QUIT command in AUTOEXEC.BAT, remove it
          before running MemMaker.  Otherwise, MemMaker's commands will not
          run and the memory optimization process will not work properly.


      1DIR+ (Bourbaki):

          The information below was obtained from tests with 1DIR+ version
          3.02, and verified with version 3.5 as well.

          1DIR+ will work properly under 4DOS in its partially resident or
          EMS modes when set up as described below.  It will work in its
          fully resident mode but cannot reliably exit back to 4DOS once
          started.

          If your copy of 1DIR+ is set up for fully resident mode, you can
          load it into memory under 4DOS to switch it to partially resident
          or EMS mode.  To do so, from the directory where you normally run
          1DIR+, type the commands:

                    setdos /l1
                    1dirplus



   4DOS 4.02  [3-30-93]          APPNOTES.DOC                       page 13



          When 1DIR+ starts go to the "Wonder" / "Setup" menu and switch
          the mode to partially resident or EMS.  Hit Esc to exit, and take
          the "Exit/Save" option (not "Save/Reset").  Back at the main
          menu, exit with "Wonder" / "Exit".  At this point the system will
          probably hang.  Reboot your computer.  You should then be able to
          run 1DIR+ as described below.

          The above steps only need to be done once, when you install or
          re-install 1DIR+.

          Once 1DIR+ is set to EMS or partially-resident mode, you can
          start it from 4DOS using the following alias:

                    alias 1dir `setdos /L1 ^ 1dirplus`

          The SETDOS /L1 is necessary to allow 1DIR+ to send command lines
          to 4DOS.

          You must do a SETDOS /L0 when you are done with 1DIR+ in order to
          get normal 4DOS command-line editing back.  You can NOT do this
          within the alias above, as 1DIR+ returns to 4DOS in order to
          accomplish its work, and you don't want to switch back to /L0
          mode until 1DIRPLUS has been removed from memory.  If, after
          exiting from 1DIR+, you find that 4DOS's command line editing and
          history are unavailable, it is because you forgot to do the
          SETDOS /L0.  If you go in and out of 1DIR+ regularly aliases like
          the following can be used to make the process quick:

                    alias 1d `setdos /L1 ^ 1dirplus`
                    alias 1e setdos /L0

          If you run batch files from the 1DIRPLUS "compose" feature, you
          may find that INPUT commands in the batch file don't work
          properly unless they are preceded by SETDOS /L0.  You must also
          do a SETDOS /L1 before the end of the batch file, or 1DIRPLUS
          won't pop up properly when the batch file is finished.  For
          example:

                    setdos /l0
                    input Enter your name:  %%name
                    setdos /l1


      3COM Networks (3Com):  [**]

          Some users report that 3Com network software will not load
          properly if UMBLoad = Yes is used in 4DOS.INI.  If you have
          trouble with a 3Com network and 4DOS, try removing the UMBLoad
          and UMBEnvironment directives from your 4DOS.INI file.


      AllClear (AllClear Software):  [**]



   4DOS 4.02  [3-30-93]          APPNOTES.DOC                       page 14



   4.02   AllClear may not work properly under 4DOS unless if it is invoked
          with a simple program name, such as A.COM.  However it works
          properly if invoked with its full path name, for example
          D:\ALLCLEAR\A.COM.  If you use AllClear, you can set up an alias
          to do this, for example:

              alias ac d:\allclear\a.com


      Alpha 4 (Alpha Software):  [**]

          Alpha 4 does not work properly if you have too much environment
          space in use when it is started.  You can use the 4DOS SETLOCAL,
          ENDLOCAL, and UNSET commands to decrease the amount of
          environment space in use before starting Alpha 4.  For details on
          this technique see the section on "Solving Software Compatibility
          Problems" in chapter 7 of the 4DOS manual.


      ANSI.SYS (various manufacturers):

          If you have trouble with screen scrolling in 43-line or 50-line
          mode, try a different version of ANSI.  We have had good results
          with PC Magazine's free utility ANSI.COM, and with the ANSI-
          UV.SYS program distributed with Personics' UltraVision EGA / VGA
          enhancement software.

          Some display-related device drivers may "fool" 4DOS into thinking
          an ANSI driver is present when this is not the case.  If this
          happens you will see ANSI strings like "[2J" displayed on-screen
          when you use the CLS and COLOR commands.  To correct the problem,
          place an ANSI = No directive in 4DOS.INI, or a SETDOS /A2 command
          in AUTOEXEC.BAT.


      Bookshelf CD-ROM (Microsoft):  [**]

          Microsoft Bookshelf uses the environment variable CDPATH, which
          is also used (for a totally different purpose) by 4DOS.  If you
          are using MS Bookshelf and want to set a CDPATH variable for
          4DOS, set _CDPATH instead.  4DOS will search for _CDPATH first;
          when it is found, 4DOS will use it, and ignore CDPATH.


      DESQview (Quarterdeck):

          Most information about DESQview is in chapter 7 of the manual.

          4DOS 4.0 automatically "cleans up" its resources (releases the
          shell number and deletes any disk swap file) when you Close a
          DESQview window from the DESQview menu without EXITing from 4DOS. 
          However this feature has a side effect:  it disables the Quit



   4DOS 4.02  [3-30-93]          APPNOTES.DOC                       page 15



          option on the DESQview menu (this is due to the design of
          DESQview, not to anything within 4DOS).  4DOS gives you control
          over this behavior with the DVCleanup directive in 4DOS.INI.  If
          DVCleanup is set to Yes (the default), 4DOS will work as it did
          in version 4.0.  Setting DVCleanup to No will disable 4DOS's
          DESQview close window cleanup code and thereby reenable the Quit
          choice on the menu.  However this will prevent 4DOS from cleaning
          up its resources when you Close a 4DOS window from the menu,
          rather than with the EXIT command.

   4.02   Some users report that DESQview uses all upper memory space when
          it loads, leaving no upper memory available to 4DOS.  If you have
          UMBLoad and / or UMBEnvironment set to Yes in 4DOS.INI, this will
          result in a couple of harmless error messages when 4DOS is
          started under DESQview.  To eliminate these messages, place the
          following lines at the end of 4DOS.INI:

                    [Secondary]
                    UMBLoad = No
                    UMBEnnvironment = No

          DESQview includes the ability to assign "logical drives" to
          subdirectory paths to make access to commonly used directories
          easier, or to support older applications that can't handle
          subdirectories.  This is similar to the DOS SUBST command.  4DOS
          commands like DIR and COPY may not work as you expect on DESQview
          logical drives, because DESQview does not support certain
          standard DOS calls which 4DOS uses to determine whether a name
          you enter is the name of a file or a subdirectory.  If you are
          using specific filenames without wildcards, 4DOS commands will
          generally work properly on DESQview logical drives.  However
          problems may occur with "implied wildcards" (for example, when
          4DOS interprets DIR A* as DIR A*.*), filename completion, and
          other wildcard file access.  We know of no circumstances where
          these problems would cause a loss of data.  However for the sake
          of safety, when using DESQview logical drives we suggest you use
          the /N switches on commands like COPY and MOVE to verify the
          command's operation before files are actually modified.

          Under 4DOS, the DESQview DOS Services option will not work in its
          default configuration.  To make DOS Services work under 4DOS, you
          must first create a batch file, DOSSERV.BAT, in your DESQview
          directory to run DOS Services under COMMAND.COM.  (We are
          assuming that DESQview is in directory C:\DV and COMMAND.COM is
          in directory C:\; you will need to modify the settings below if
          your system is configured differently.)  The batch file is:

                    set comspec=c:\command.com
                    c:\dv\dosserv
                    c:\command
                    exit




   4DOS 4.02  [3-30-93]          APPNOTES.DOC                       page 16



          Then, make the following changes on the DESQview change a program
          screen for DOS Services (items marked ** are on the second page
          of the screen):

                    *   Memory Allocation = 128K or greater
                    *   Program Name = C:\DV\DOSSERV.BAT (modify from
                        previous value of C:\DV\DOSSERV).
                    **  Close on Exit to DOS = N
                    **  System Memory = 10K or greater
                    **  Allow Close Window = N

          Once these steps are taken, you should be able to open the DOS
          Services window normally.  However you will not be able to close
          it with a close window command.  Instead, go to the window where
          DOS Services allows you to compose a DOS command, and type EXIT
          to close the window.


      DOORWAY BBS Software:

          DOORWAY uses the caret [^] in certain command line arguments. 
          4DOS will interpret this symbol as a command separator, and will
          not pass the line to DOORWAY properly.  You can work around this
          problem by changing your 4DOS command separator permanently (with
          the CommandSep directive in 4DOS.INI) or temporarily when
          starting DOORWAY (with the SETDOS /C command), or by using the
          4DOS escape character (ctrl-X) before each caret in the DOORWAY
          command line.


      DR-DOS (Digital Research):

          4DOS will work properly as a command processor (including as the
          primary shell) under DR-DOS 3.4, 5.0, or 6.0.  The information
          below was developed by testing 4DOS under DR-DOS 5.0 and 6.0.

          Internal vs. External Commands:

              DR-DOS 5.0's design makes the ASSIGN, JOIN, MORE, and SUBST
              commands internal (in MS-DOS / PC-DOS they are external). 
              4DOS supports all MS-DOS internal commands, but does not have
              internal support for ASSIGN, JOIN, MORE, and SUBST.  To
              access these DR-DOS internal commands when using 4DOS as the
              command processor, you must set up aliases which run DR-DOS's
              COMMAND.COM.  The following 4DOS aliases accomplish this
              (adjust these if COMMAND.COM is not in C:\):

                    alias assign `c:\command /c assign %&`
                    alias join `c:\command /c join %&`
                    alias more `c:\command /c more %&`
                    alias subst `c:\command /c subst %&`




   4DOS 4.02  [3-30-93]          APPNOTES.DOC                       page 17



              In DR-DOS 6.0 ASSIGN, JOIN, and SUBST were changed back to
              external commands, so the corresponding aliases are not
              necessary.

              For the MORE command, a much better alternative can be set up
              by aliasing it to the 4DOS LIST command:

                    alias more list /s

              This provides a scrollable, full-screen display rather than
              the simple paged display offered by DR-DOS (or MS-DOS) MORE.

          HILOAD:

              4DOS supports DR-DOS's HILOAD feature using the MS-DOS / PC-
              DOS command names of LOADHIGH or LH.  To load a TSR high
              under DR-DOS, simply use the command:

                    LH [programname] [options]

              If you want the command to be called HILOAD for complete DR-
              DOS compatibility, just set up an alias before using it:

                    alias hiload lh

              Just as under MS-DOS, LOADHIGH and LH will not work properly
              unless you have memory management software loaded to provide
              upper memory block support.  Because DR-DOS does not return
              any error to 4DOS if a LOADHIGH operation fails, 4DOS cannot
              report this condition to you.  This means you must use the
              DR-DOS MEM program or another similar memory mapping utility
              to determine if your TSR was actually loaded high.

   4.02       The MS-DOS 6.0 switches for the 4DOS LH command (/L and /S)
              will not work with DR-DOS.

          File Passwords:

              4DOS includes support for DR-DOS file passwords.  However the
              command syntax used to access files with passwords is
              slightly different than under DR-DOS.

              First, the character used to separate passwords from
              filenames under DR-DOS is a semicolon [;], which 4DOS uses to
              separate parts of an "include list" (see the manual for
              details).  Therefore, a slightly different syntax must be
              used when including a DR-DOS password in a 4DOS internal
              command which accepts wildcards:  TWO semicolons should be
              used to separate the password and filename.  4DOS directory-
              related commands like MD and CD do not use wildcards and
              therefore a single semicolon should be used before a password
              in these commands.  All other 4DOS commands which accept



   4DOS 4.02  [3-30-93]          APPNOTES.DOC                       page 18



              wildcards must use the double semicolon.  DR-DOS external
              commands which accept the "password;filename" syntax will
              still use only a single semicolon.

              Second, DR-DOS hides files which are password-protected. 
              This means that you must use 4DOS command switches which
              allow processing of hidden files (COPY /H, DEL /Z, DIR /A,
              MOVE /H, and SELECT /A) to access a password-protected file
              under DR-DOS.

              Passwords are not automatically preserved when copying or
              moving a file with 4DOS.  However the hidden attribute will
              be preserved.  This means that if you move or copy a
              passworded file and want it to be visible in its new location
              or under its new name, you will have to manually remove the
              hidden attribute with ATTRIB.

              For example, to password-protect the file JUNK, copy it to
              drive A:, and then delete it:

                    password junk /r:fred
                    copy /h junk;;fred a:
                    del /z junk;;fred

              To unprotect the password-protected file JUNK:

                    password junk;fred /n

          CONFIG.SYS SETs:

              DR-DOS allows you to put SET commands in CONFIG.SYS to set
              environment variables.  4DOS will retrieve this information
              and store it in the 4DOS environment, as DR-DOS COMMAND.COM
              does.  If you wish you can disable this feature by setting
              DRSets = No in 4DOS.INI.

          SuperStor:

   4.02       The version of SuperStor shipped with DR-DOS works well with
              4DOS.  However some users report that 4DOS.COM cannot be
              stored on a compressed drive, and that if it is, DR-DOS will
              not be able to find 4DOS during the boot process.  If you
              experience this problem, store 4DOS on your uncompressed boot
              drive instead.

          TASKMAX:

              4DOS will work with TASKMAX as long as you start new tasks
              according to the instructions below.

              You cannot load 4DOS's resident portion high with UMBLoad =
              Yes in your 4DOS.INI file when running TASKMAX.  TASKMAX will



   4DOS 4.02  [3-30-93]          APPNOTES.DOC                       page 19



              hang the system if it is started while 4DOS is loaded high. 
              In our tests we have found that the same restriction does not
              apply to the UMBEnvironment directive, which does appear to
              be compatible with TASKMAX.  Some users also report that
              UMBLoad = Yes will work for secondary shells but not for the
              primary shell; the exact behavior appears to depend on your
              system and DR-DOS configuration.

              When TASKMAX is loaded it leaves the primary command
              processor running as task 1.  One way to start another task
              is to pop up TASKMAX and press Ins.  This starts another
              "instance" of the primary command processor, and may cause
              significant problems with 4DOS.  The reason is that each task
              started in this way is a copy of the primary command
              processor, so all such tasks will use the same swap area. 
              This will make changes to things like aliases, history, and
              SETDOS settings in one task "bleed through" to other tasks. 
              The exact nature of the bleed-through will depend on the
              sequence of operations and the type of 4DOS swapping you use. 
              This bleed-through will not necessarily hang your system but
              it may lead to very strange and undesired results, especially
              when running batch files simultaneously in more than one
              task.  There is no way for 4DOS to detect or prevent this
              condition.  We strongly recommend that you do NOT use Ins to
              start new 4DOS tasks, even if it temporarily appears to work
              properly on your system.

              Fortunately TASKMAX offers another way to start new tasks: 
              the TASKMAX /C command.  When executed from task 1, a command
              like:

                    taskmax /c c:\4dos.com

              will start a new secondary copy of 4DOS as a new task.  This
              new copy is a true secondary shell (not a copy of the primary
              shell) and will not cause the undesirable interactions
              described above.  The same approach should be used when
              starting any task which needs a command processor.  To start
              a task which runs a .BTM or .BAT file, use a command like
              this:

                    taskmax /c c:\4dos.com /c startwp.bat

              This tells 4DOS to run the specified batch file, and exit
              automatically (removing the task from the task list) when the
              batch file is done.

              If you have tasks you start regularly using the approach
              described above, use a batch file or a set of 4DOS aliases to
              help automate the process.





   4DOS 4.02  [3-30-93]          APPNOTES.DOC                       page 20



              Some users also report success at improving compatibility
              between TASKMAX and 4DOS if the FullINT2E directive is set to
              Yes in 4DOS.INI.  JP Software has not tested this approach
              but you may wish to experiment with it on your system.


      Epsilon (Lugaru Software):  [**]

          Epsilon can run 4DOS as a concurrent process, and pass commands
          to 4DOS for execution.  In this mode it traps 4DOS's input
          requests and feeds the keystrokes to 4DOS.  However it does not
          feed backspaces etc. -- only actual characters.  This means that
          editing of input isn't seen by 4DOS.  To fix the problem, either
          run 4DOS as a shell, and not as a concurrent process, or use a
          SETDOS /L1 for the copy of 4DOS that is run under Epsilon.  

          To use the more flexible SETDOS /L1 approach you must use
          4START.BAT (or .BTM) to set up the SETDOS /L1 before running
          Epsilon.  Epsilon sets the environment variable EPSRUNS=Y
          whenever it starts a secondary shell; you can use this variable
          to set up 4START to work with Epsilon.  Place the following line
          in 4START to issue the SETDOS /L1 command in a secondary shell
          started by Epsilon, but ignore it otherwise:

                    if "%epsruns"=="Y" setdos /l1


      Extra! 3270 Emulator:  [**]

   4.02   User reports indicate that Extra! will not work properly if 4DOS
          or the master environment is loaded high (in a UMB).  If you have
          trouble running Extra! with 4DOS, try removing any
          UMBEnvironment = Yes line in 4DOS.INI; if that doesn't help, try
          removing any UMBLoad = Yes line as well.


      FoxPro (Microsoft):  [**]

          FoxPro works well with 4DOS, but may have trouble if 4DOS or the
          master environment is loaded high (in a UMB).  If you experience
          compatibility problems between FoxPro and 4DOS, try removing any
          UMBEnvironment = Yes line in 4DOS.INI; if that doesn't help, try
          removing any UMBLoad = Yes line as well.


      Hijaak (Inset Systems):

          The Resident Program Manager (RPM) cannot be loaded from Hijaak's
          menu when 4DOS is the command processor.  If you try to load RPM
          from the menu you will receive "Out of memory" errors once it is
          loaded.  This is due to the internal design of Hijaak and is not
          a 4DOS bug.  To work around this problem, use the LOADRPM command



   4DOS 4.02  [3-30-93]          APPNOTES.DOC                       page 21



          from the 4DOS prompt, as described in the Hijaak manual.  LOADRPM
          will load RPM with no trouble under 4DOS, the problem occurs when
          loading from the Hijaak menu only.


      LapLink (Traveling Software):  [**]

   4.02   LapLink's "self-cloning" feature is not compatible with 4DOS's
          CTTY command.  If you need to use the self-cloning feature, start
          a temporary copy of COMMAND.COM first (see "Running 4DOS along
          with COMMAND>COM" at the beginning of this file for details).


      LOGIMENU (Logitech):  [**]

          When using Logitech's LOGIMENU with 4DOS, LOGIMENU may leave a
          file open each time a menu is unloaded.  Some users have been
          able to work around this problem by loading the menu from a
          floppy disk or RAM disk rather than the hard disk, but in general
          you will probably need to load and unload LOGIMENU with a product
          like MARK and RELEASE (from TurboPower's freeware TSRCOM package,
          available on the 4DOS Utility Disk), which can help to clean up
          files left open by other programs.


      Manifest (Quarterdeck):

          Manifest generally works well with 4DOS.  However if there is too
          little environment space free in 4DOS's master environment, the
          Hints Detail screen in Manifest may give unexpected results or
          hang your system.  If this occurs, increase your environment size
          and / or remove some environment variables when starting Manifest
          if you plan to use the Hints Detail screen.


      Netware (Novell):  [**]

          The information below was obtained from tests with Netware
          versions 2.12, 2.15, and 3.11 - 3.2, and Netware 386, and from
          discussions with Novell support personnel.

          Compatibility problems between Netware and 4DOS should be quite
          rare.  When they do occur, the usual problem is a conflict
          between 4DOS and the Netware shell (NET3, NET4, NET5, NETX,
          EMSNETX, etc.).  As a general rule, you should find that Novell's
          newer "NETX" shell versions have considerably fewer problems than
          the older NET3 / NET4 / NET5 versions, and we recommend their use
          with 4DOS whenever possible.

          4DOS includes a 4DOS.INI directive for Netware, NetwareNames. 
          You should always set NetwareNames = Yes on Netware systems. 
          This will include strings in the resident portion of 4DOS which



   4DOS 4.02  [3-30-93]          APPNOTES.DOC                       page 22



          Netware searches for when it loads, and thereby avoid problems
          with destroyed environment variables during LOGIN.  Setting
          NetwareNames = Yes will increase the resident size of 4DOS by 112
          bytes.

          If you use NetwareNames = Yes and UMBLoad = Yes, and you do not
          actually have any upper memory blocks available, then
          NetwareNames will be ignored, and you may see problems with your
          environment after using LOGIN.  To correct this, do not use
          UMBLoad with NetwareNames unless you have enough space in upper
          memory for the resident portion of 4DOS.  See your 4DOS manual
          for more information on UMBLoad.

          [CAUTION:  If NetwareNames is set to Yes and you BOOT FROM a
          Netware drive (a rare situation), the TEMP4DOS or TEMP variables
          must be SET explicitly to the appropriate drive and directory for
          each user to avoid conflicts in the directory used for pipe
          files.  If NetwareNames is not used or you boot from a local
          drive, 4DOS and Netware will automatically set the proper drive
          and directory for pipe files.]

   4.02   Under Netware version 3 and above, 4DOS commands which scan a
          directory tree (e.g. COPY /S, DIR /S, GLOBAL, etc.) may stop
          without scanning the entire tree, and without displaying an error
          message.  This is because such commands can exceed the size of
          the directory search table on your server; it is a Netware design
          issue, and not a 4DOS bug.  You can address any such problem by
          having your system administrator increase the Maximum Oustanding
          NCP Searches parameter for the server in question.  This
          parameter is documented in the Netware System Administrator's
          manual, Console Set Parameters section, under Miscellaneous
          Advanced parameters.  The default value is 51, the minimum is 10,
          and the maximum is 1000.  The parameter can be set "on the fly"
          without restarting the server.

   4.02   4DOS can be set up to run properly on Novell Netware diskless
          workstations which boot from the server.  To do so, you must make
          several changes to 4DOS.INI and your other startup files.  JP
          Software has a separate technical document on the steps required. 
          If you need a copy, contact us and we will mail it to you.  You
          can also download a copy from our CompuServe support area; the
          file name is DISKLS.ZIP.

          Some versions of Netware may occasionally produce a "pipe not
          found" message when loading under 4DOS.  This message refers to
          Netware features related to COMMAND.COM, and does not apply to
          4DOS; the message can be ignored.

          The 4DOS TRUENAME command and the @TRUENAME variable function
          will return true Netware server names when given a file name that
          refers to a Netware drive.  However the returned name will not be
          correct if only the root directory name is given as a parameter



   4DOS 4.02  [3-30-93]          APPNOTES.DOC                       page 23



          (for example TRUENAME K:\).  This is because Netware fails to
          recognize the true name request properly when only a root
          directory name is given; it is not a bug in 4DOS.  If necessary,
          you can work around this problem by adding a simple "." to the
          request (TRUENAME K:\.).

          If you use 4DOS input redirection in a .BAT file which resides on
          a Netware drive, you may experience incorrect file assignments on
          some systems.  When this occurs, an application run from within
          the batch file, or a secondary shell run from such an
          application, may loop forever attempting to read lines from the
          batch file rather than accepting input from the keyboard.  For
          example:

                    copy /r *.* g: < YES
                    wp
                    rem  Now if the user shells from WP, the system will
                    rem  loop forever reading lines from the batch file or
                    rem  blank lines at the prompt.

          This problem occurs because Netware does not handle file
          assignments properly when 4DOS input redirection is used in a
          .BAT file.  We are working with Novell to attempt to resolve the
          problem.  You can work around it in several ways:

              * Change the batch file to a .BTM file.

              * Place the file BTM mode with the LOADBTM command at any
              point prior to the use of input redirection.

              * Move the file to a non-Netware drive.

              * User reports indicate that adding a line which does a
              "dummy" output redirection just before the input redirection
              will prevent the problem from occurring.  For example:

                    echo This is junk > junk.dat
                    copy /r *.* g: < YES
                    wp
                    del junk.dat

          When loading a secondary 4DOS shell under Netware you can swap
          the shell to a network drive if you configure 4DOS properly.  To
          do so you must take into account the fact that Netware closes all
          files -- including the 4DOS swap file -- each time an application
          exits.  Under the default 4DOS configuration, the next time 4DOS
          uses the swap file, a swap file seek error will occur.  However
          if you set SwapReopen = Yes in 4DOS.INI, 4DOS will reopen its
          swap file each time such an error occurs, and the swapping will
          work.  See the manual for details on SwapReopen.  You can also
          avoid this problem by swapping to EMS, XMS, or a local hard disk
          or RAM disk.



   4DOS 4.02  [3-30-93]          APPNOTES.DOC                       page 24



          Use caution with the 4DOS UNSET command under Netware.  When
          Netware is loaded it remembers the exact location of the COMSPEC
          variable in the master environment, and it may therefore have
          problems if variables such as COMSPEC and PATH are removed and
          reloaded in a different sequence.

          The UMBLoad directive in 4DOS.INI is compatible with Netware. 
          The UMBEnvironment directive is compatible with Netware 3.11 and
          above, but not with earlier versions.


      Novell MENU (Novell):

          The Novell MENU system distributed with Netware uses Interrupt 2E
          to execute menu options, and therefore requires the use of the
          FullINT2E = Yes directive in 4DOS.INI.  Once INT 2E support is
          enabled with this directive, Novell MENU should work normally
          under 4DOS.


      OS/2 1.2, 1.3, and 2.0 (IBM / Microsoft):

          4DOS works properly as the shell in OS/2 DOS sessions under OS/2
          1.2, 1.3, and 2.0.  When installing OS/2's dual boot option you
          may receive a warning because your SHELL command in CONFIG.SYS
          points to 4DOS rather than COMMAND.COM.  In our experience this
          warning can be ignored, and OS/2 will install properly.

   4.02   If you see a message like "Cannot find OSO001.MSG" when running
          external utilities like TREE or DISKCOPY in OS/2 DOS sessions,
          you probably need to include the line:

                    loadhigh append c:\os2;c:\os2\system

          in your AUTOEXEC.BAT file used by these DOS sessions, or set up
          the append path in an alias or batch file used to run such
          programs (change the drive letter if OS/2 is installed on a
          different drive).  Be sure to read the notes and cautions on
          MS-DOS APPEND in this file before using APPEND.

          If you use OS/2, you will probably want to use our companion
          product 4OS2 in your OS/2 sessions.  See the ORDERINF.DOC file
          for more information.  The 4OS2 manual also includes detailed
          information on fine-tuning 4DOS for use in your OS/2 DOS
          sessions.


      OS2SPEED DOS Sessioon Enhancer:







   4DOS 4.02  [3-30-93]          APPNOTES.DOC                       page 25



          OS2SPEED is a small freeware program which is supposed to release
          unused CPU time in OS/2 DOS sessions when certain applications
          are running, and thereby improve performance.  It accomplishes
          this task by fooling DOS applications into thinking they are
          running under DESQview, then converting the applications'
          commands to release unused time to DESQview into similar commands
          for OS/2.

          Unfortunately, the version of OS2SPEED available as of this
          writing is flawed because it provides only a partial emulation of
          DESQview, and can cause "DESQview-aware" applications -- like
          4DOS -- to crash the DOS session.  We recommend that you use
          OS/2's IDLE_SECONDS and IDLE_SENSITIVITY DOS settings to adjust
          DOS session performance.  If you must use OS2SPEED, you may be
          able to make it work properly with 4DOS by disabling 4DOS's
          DESQview awareness with this directive in 4DOS.INI:

                    DVCleanup = No


      Personal REXX (Quercus Systems):  [**]

          Personal REXX generally works well with 4DOS.  However there are
          some issues you must take into account when using certain
          personal REXX features.

          The Personal REXX Batch Manager will not work with 4DOS as the
          command processor.  The Batch Manager allows REXX programs to be
          executed from the command line without requiring a REXX or RX
          command prefix.  The Batch Manager accomplishes this by using an
          undocumented feature of COMMAND.COM, and Mansfield Software
          states that this may not work on OEM versions of DOS, and advises
          that if it does not work, you should not use it.  To work around
          this problem, use executable extensions to tell 4DOS to execute
          .REX files using REXX.EXE.  To set this up, add a command like
          this to your AUTOEXEC.BAT file:

                    set .rex=d:\path\rexx.exe

          where "d:\path" is the drive and directory where REXX.EXE is
          stored.  Once this executable extension is set up, REXX programs
          will run as though the Batch Manager was installed.  Note,
          however, that the Batch Manager would attempt the execution of
          REXX programs before .BAT files, whereas 4DOS executable
          extensions are executed after .BTM and .BAT files.

          Personal REXX also provides the ADDRESS DOS statement, which
          allows the REXX program to pass commands to the DOS command
          processor.  This function is implemented through the undocumented
          INT 2E interface to the command processor, which can be enabled
          in 4DOS with the FullINT2E=Yes directive in 4DOS.INI.  If you use
          FullINT2E=Yes and have trouble with ADDRESS DOS, use Personal



   4DOS 4.02  [3-30-93]          APPNOTES.DOC                       page 26



          REXX's OPTIONS NEWCOM, or an environment variable, SET
          RXNEWCOM=YES, to force ADDRESS DOS to shell to a new copy of
          4DOS.  Note that the normal Personal REXX ADDRESS DOS function
          permits the environment to be permanently modified, whereas using
          OPTIONS NEWCOM, or setting the environment variable will not
          permit this.  Quercus Systems discourages the use of the INT 2E
          approach in DOS 4.00 or later, and Personal REXX will default to
          not using INT 2E with these versions of DOS.


      QEMM and QRAM (Quarterdeck):

          The information below was obtained from tests with QEMM versions
          5 and 6, and user reports on QRAM.

          Both QEMM and QRAM are compatible with 4DOS, and will allow you
          to load the 4DOS resident code and the master environment into
          high DOS memory (UMBs) via the UMBLoad and UMBEnvironment
          directives in 4DOS.INI.  For these directives to work with QRAM
          you must have QEXT loaded also (this is the normal method of
          loading QRAM).

          QEMM's Stealth mode is compatible with 4DOS, but can decrease
          general system stability on some systems.  If you have unusual
          problems or system hangs with Stealth turned on, try turning it
          off and see if the problems clear up (this is the procedure
          recommended by Quarterdeck in their Stealth documentation).

          QEMM allocates both XMS and EMS memory from the same memory area. 
          Therefore it always reports the exact same amount of free XMS and
          EMS memory.  You will see this in the free EMS and free XMS
          values displayed by the 4DOS MEMORY command -- they will be
          exactly the same under QEMM.  Just remember that if both values
          are (say) 512K, that means you have 512K of free memory which can
          be allocated either way -- not 1024K!

          If you use FILES.COM to load part of the DOS file handle table
          into high memory, you must follow Quarterdeck's recommendations
          and keep a minimum of FILES=8 in CONFIG.SYS.  Lower values may
          cause 4DOS to hang during boot, especially if disk swapping is
          used.

          If you use QEMM's OPTIMIZE and your AUTOEXEC has 4DOS-specific
          commands like GLOBAL, IFF, aliases, etc., OPTIMIZE will recognize
          them based on the 4DOS.CMD file distributed with QEMM 6.  Note
          that in QEMM version 6.00 this file is incomplete in that it does
          not include the ELSE, ELSEIFF, and ENDIFF commands; you should
          add these commands to 4DOS.CMD if you use them in your AUTOEXEC
          file.  This error in 4DOS.CMD was corrected in version 6.01 of
          QEMM.  To use 4DOS.CMD it must be renamed to OPTIMIZE.EXC before
          running OPTIMIZE; see your QEMM documentation for details.




   4DOS 4.02  [3-30-93]          APPNOTES.DOC                       page 27



          OPTIMIZE cannot take account of the fact that 4DOS may be loaded
          high with UMBLoad = Yes in 4DOS.INI, and therefore may not give
          the best optimization results when UMBLoad = Yes is used
          (OPTIMIZE has this problem with all programs which load
          themselves into UMBs, not just with 4DOS).  Some users also
          report that OPTIMIZE is unstable on their systems when UMBLoad =
          Yes is used.


      RBase (MicroRim):  [**]

          When used with 4DOS disk swapping, RBase closes 4DOS's swap file
          when it exits.  This generates "4DOS Unrecoverable error DS" and
          other similar fatal error messages.  You can avoid this problem
          by changing 4DOS swapping to go to EMS or XMS, or by setting
          SwapReopen = Yes in 4DOS.INI.


      RoboComm Communications Software:  [**]

          If you have trouble shelling out of RoboComm (for example, to use
          an external protocol like DSZ), try increasing the setting for
          Files and Extract memory to 256K.


      Software Carousel (SoftLogic Solutions):

          Please see the general section on multitaskers in chapter 7 of
          the manual before reading this section.

          The information below was obtained from tests with Software
          Carousel version 3, and discussions with SoftLogic technical
          support.  It applies to all versions of Software Carousel.

          Software Carousel will not work properly with 4DOS loaded as the
          primary shell.  It is designed with the assumption that
          COMMAND.COM is the system command processor, and contains logic
          which specifically depends on COMMAND.COM and the way it is
          written, and which actually modifies the copy of COMMAND.COM in
          memory.  This makes it impossible to write a program which works
          properly as an alternate command processor loaded underneath
          (i.e. before) Software Carousel.

          However, 4DOS can be run without difficulty inside a Software
          Carousel partition, if the instructions below are followed.

          When loading 4DOS into a Carousel partition, the best method is
          to leave the COMSPEC set to COMMAND.COM when Carousel is loaded. 
          4DOS should then be set up in the Carousel options file just like
          any other program.  For example, to load 4DOS into partition 1:

                    d:\path\4DOS.COM [parameters] [filename]



   4DOS 4.02  [3-30-93]          APPNOTES.DOC                       page 28



          where:

              d:\path         is the drive and path where 4DOS.COM is
                              located

              [parameters]    is any 4DOS command line parameters (/E,
                              @ininame, etc.; do NOT use /P here)

              [filename]      is the name of a batch file to be executed
                              when the partition is started

          To use different 4DOS.INI files for different Software Carousel
          partitions, use the "@ininame" parameter in the "parameters"
          section of your Carousel setup to invoke a specific file.  For
          example, the parameters could be set to @D:\WP\4DOSWP.INI to use
          that initialization file for the WP partition.

          Because 4DOS can only be loaded in a partition when running
          Software Carousel, and not as the primary command processor,
          using 4DOS disk swapping in multiple partitions is subject to the
          cautionary note on this subject in the general information
          section on multitaskers in the manual; please read it carefully. 
          As stated in that note, if you use disk swapping you will
          probably want to use the UniqueSwapName directive in 4DOS.INI to
          avoid swap file name conflicts.


      TSRCOM Utilities (TurboPower Software):

          The TSRCOM utilities will work properly with 4DOS as long as you
          use TSRCOM version 2.6 or later.  The current release is version
          3.4, and is available on the 4DOS Utility Disk and on many
          bulletin boards and on-line systems.

          If you use TSRCOM's MARK and RELEASE to manage your TSRs, 4DOS
          swapping (as set with the SWAPPING command) must be in the same
          state when RELEASE is run as it was when MARK (or FMARK) was run. 
          This is a characteristic of the design of MARK and RELEASE (or
          any other such products), and not a bug.  If you do not observe
          this rule (for example, if you run MARK with SWAPPING OFF in
          AUTOEXEC and later run RELEASE from the prompt with SWAPPING ON),
          you may receive unusual error messages or hang your system.  The
          same restriction applies to MARKNET and RELNET.


      UltraVision (Personics):

          The DE program distributed with UltraVision is written
          specifically for COMMAND.COM, and cannot be used to set directory
          colors with 4DOS.  Use 4DOS's built-in directory colorization
          instead.




   4DOS 4.02  [3-30-93]          APPNOTES.DOC                       page 29



      Windows 3.0 and 3.1 (Microsoft):

          Most information about Windows 3.0 is in chapter 7 of the manual. 
          4DOS has been tested thoroughly and works well with Windows 3.1;
          the instructions in the manual on Windows 3.0 also apply to
          Windows 3.1.  (See the section on PATH problems below for one
          caution related to the Setup Applications program in Windows
          3.0.)

   4.02   Under some circumstances you may find that Windows overrides the
          environment size specified in your 4DOS.INI file, and creates a
          smaller environment.  This can leave insufficient environment
          space for your 4DOS sessions running under Windows.  If you
          experience this problem, edit the SYSTEM.INI file in your Windows
          directory, and find the section labelled [NonWindowsApp].  Add
          the following line to this section:

                    CommandEnvSize = 0

          This tells Windows not to force a particular environment size,
          which will allow 4DOS to set the size itself.

          If you set up a PIF file for a 4DOS window, please note that the
          4DOS MEMORY command will report the maximum amount of EMS memory
          which Windows can theoretically make available in that window. 
          Because Windows provides a virtual memory capability, this number
          may be much larger than the size of physical RAM.  For example,
          if you set the EMS Limit in your PIF file to -1, Windows will
          report total EMS memory of 64 MB to 4DOS as this is the
          theoretical limit on Windows' virtual memory manager.  Virtual
          memory figures which give the appearance of excess memory are a
          feature of Windows, and not a bug in 4DOS.


      XyWrite (XyQuest):  [**]

          XyWrite's "shell to DOS" capability shells to COMMAND.COM, even
          if you have your COMSPEC variable set to 4DOS.  The only way we
          know of to work around the problem is to make a copy of 4DOS.COM
          and call it COMMAND.COM.  If you do this, be sure to save the
          real COMMAND.COM in another directory in case you need it for
          another purpose.  Some users have reported that the same problem
          occurs with Signature, a newer word processor from XyQuest.


      Programs Requiring PATH to be Under 128 Characters:

          The following programs contain bugs which prevent them from
          working properly if you have a PATH which is over 128 characters
          long.  Since 4DOS allows you to create a PATH up to 255
          characters long this can appear to be a conflict between the
          program involved and 4DOS.  If your path is longer than 128



   4DOS 4.02  [3-30-93]          APPNOTES.DOC                       page 30



          characters, see the section headed "Solving Software
          Compatibility Problems" in chapter 7 of the manual for
          information on creating a batch file to reduce the PATH length
          while one of these programs is running.

              Checkit (Touchstone):  [**]  Checkit version 3 requires a
              path length under 128 characters.

              Computer Select CD-ROM (Ziff-Davis):  [**]  Computer Select
              cannot find its help program if your PATH is over 128
              characters long.  

              RenderMan (AutoDesk):  RenderMan will hang your system if it
              is started with a PATH longer than 128 characters.

              VINES Network (Banyan):  [**]  VINES' installation may not
              work properly if your PATH is longer than 128 characters.

              Windows 3.0 (Microsoft):  The Windows 3 Setup Applications
              option, which scans your disk drives for applications to be
              added to Windows program groups, will not work properly if
              your PATH is more than 128 characters long.  This problem is
              fixed in Windows 3.1.
































   4DOS 4.02  [3-30-93]          APPNOTES.DOC                       page 31




   Software For Use With 4DOS
   --------------------------

   We receive many requests for recommendations on software that works well
   with 4DOS, or that we have found especially useful.

   While we can't recommend what will work well on your system or to meet
   your needs, we can tell you what packages we have used and found
   valuable.  We will confine our comments to our primary area of expertise
   -- system software -- and avoid discussing applications programs like
   spreadsheets and word processors.

   Please note that this is NOT actually a list of what works well with
   4DOS -- the answer to that is, almost everything!  And remember this is
   only our opinions -- you need to choose what will work best for you.

      Memory Managers:  We generally use 386MAX and BlueMax (Qualitas) on
      our own systems because we find it offers some important technical
      advantages, and takes a conservative approach to memory management. 
      This approach may leave slightly less memory available on some
      systems, but in our view this is a small price to pay for the
      increased reliability provided by more conservative memory management
      techniques.  Many 4DOS users also report excellent results with QEMM
      (Quarterdeck), and we use it at times as well.  We have less
      experience with other memory managers like Netroom (Helix) and Memory
      Commander (V Communications), so we can't comment on them.

      Task Switchers:  For switching between applications which run one at
      a time, the primary products we're aware of are Back & Forth
      (Progressive Solutions) and Software Carousel (SoftLogic).  This
      category is an exception to our "everything works well with 4DOS"
      rule:  Software Carousel does work with 4DOS, but is designed to
      depend on COMMAND.COM and requires special care when used with 4DOS
      (see above for details).  Back & Forth works seamlessly with 4DOS,
      and many 4DOS users are enthusiastic about its features, support, and
      price.  Back & Forth contains a number of features specifically
      created with 4DOS in mind (for example, it knows that .BTM files are
      executable like batch files), and JP Software and Progressive
      Solutions communicate regularly to make sure that 4DOS and Back &
      Forth continue to work well together.

      Disk Caches:  There are dozens of products available in this
      category.  We use Super PC-Kwik (MultiSoft), HyperDisk (Hyperware),
      and SmartDrive (Microsoft), and have found all of them to be reliable
      and to work well with 4DOS.  We can't speak from any direct
      experience about other caching programs.

      Disk Expanders:  We have had excellent results using Stacker (Stac
      Electronics) to expand disk drive space.  We currently run Stacker on
      both notebook and desktop systems.  We sometimes get a little less
      than Stac's claimed 2:1 disk space savings, but this is a minor point



   4DOS 4.02  [3-30-93]          APPNOTES.DOC                       page 32



      compared to Stacker's reliability, speed, and value.  We have also
      tested the DBLSPACE utility included with MS-DOS 6.0, and it works
      well with 4DOS 4.02.  We haven't used DBLSAPCE extensively enough to
      comment on its overall reliability.  There are other products which
      perform the same function; we have not used or evaluated any of them.

      Video Utilities:  We use UltraVision (Personics) regularly on all of
      our systems which have VGA video or better, and we use Laptop
      UltraVision on laptop or notebook systems.  UltraVision allows
      excellent control over all aspects of VGA and EGA video systems
      including fonts, colors, and screen sizes.  It is fully compatible
      with 4DOS and many 4DOS users have found it to be a valuable tool. 
      We are not aware of any other products which do what UltraVision
      does.  ANSI-UV.SYS which comes with UltraVision is an excellent ANSI
      driver; we also use ANSI.COM from PC Magazine.

      Boot Utilities:  We can't speak about this issue from any distance
      because we sell one such utility, BOOT.SYS, and use it on all our
      systems.  BOOT.SYS was the first of these utilities to allow
      selection of a configuration during the boot process, and is an
      excellent tool for configuration management.  There are other
      products in this category but we are not familiar with them.

































   4DOS 4.02  [3-30-93]          APPNOTES.DOC                       page 33