PMEM: Protected Mode Monitor                           Version 2.4A

                      PMEM: A Protected-Mode Memory Monitor

       Introduction

          PMEM  is   a  protected-mode   environment   for   interactively
       examining/changing/testing the  entire 4  Gigabyte memory space and
       64K I/O  ports of 80386 or 80486 processors.  PMEM is not a program
       debugger.   Rather, PMEM  is a  very useful  tool for examining and
       debugging hardware  systems.   PMEM  is particularly useful for the
       following applications:

            -    For  system   hardware  designers,   PMEM  allows  system
                 integrity  to  be  verified  very  early  in  the  design
                 process.
            -    For PC board and peripheral designers, PMEM allows you to
                 exercise your  product to  verify that  it is  functional
                 even before software drivers have been written.
            -    For programmers, PMEM allows you to "peek under the hood"
                 to see  how your program is using memory and other system
                 resources.   Thus,  even  though  PMEM  isn't  a  program
                 debugger, it  can be  very  useful  for  system  software
                 authors.  Also, PMEM's special I/O capabilities allow you
                 to test  your hardware  initialization sequences  without
                 writing a line of code!
            -    For technicians and engineers, PMEM can be used to create
                 "scope loops" which can greatly simplify finding hardware
                 problems.
            -    For general  use, PMEM  is a  useful 32-bit  programmer's
                 calculator,  with   arithmetic  and   logical  operators,
                 variables, and more.
            -    PMEM is  also extremely  useful as a learning tool, since
                 it allows  you to  examine areas of your system which are
                 normally inaccessible.

          All of PMEM's commands can directly read and write memory or I/O
       ports  8-bits,  16-bits,  or  32-bits  at  a  time.    This  unique
       capability is  one of  PMEM's most  powerful features  -  very  few
       inexpensive tools exist which have this capability.


       Caveats

          PMEM is not a simple program.  While a fair degree of effort has
       been spent  trying to  make it an easy-to-use tool, PMEM works at a
       level of  detail which  is beyond  most users.    If  you  are  not
       familiar with bits, bytes, or bus cycles, PMEM probably won't be of
       much help  to you.   Also, PMEM runs in 80386 protected mode, so if
       you don't have an 80386 or an 80486 CPU, it's time to upgrade!

          IF YOU  ARE RUNNING  PROTECTED MODE  PROGRAMS SUCH AS THE EMM386
       DRIVER THAT  IS SUPPLIED  WITH MS-DOS VERSION 5, PMEM WILL NOT RUN!
       IN ADDITION,  PMEM WILL  NOT  RUN  UNDER  WINDOWS!    To  run  PMEM
       properly, you  should create  a "simple"  MS-DOS system, which does
       not use EMM386, QEMM, 386^Max or similar programs.


       Page 1               (C) 1992, Mark J. Foster         July 14, 1992







       PMEM: Protected Mode Monitor                           Version 2.4A

       Overview of PMEM

          The commands supported by PMEM include:

            S:   Set the  command defaults.   You can set the DEFAULT word
                 size to  bytes (8-bits),  words (16-bits), or dwords (32-
                 bits),  and   the  numeric   input  base  to  decimal  or
                 hexadecimal.
            ":   The quote  command allows  you to  display specific  text
                 prompts.
            C:   Compare two different regions of memory
            D:   Display Memory location(s)
            E:   Examine Memory (command-line and interactive forms)
            F:   Fill memory locations with an arbitrary string
            H:   Hex Math  calculator:  displays  the  result  of  a  math
                 expression.  PMEM has a broad range of math capabilities,
                 including arithmetic and logical operators.
            I:   Input from I/O port(s)
            M:   Move a block of memory to another location
            O:   Output to an I/O port
            R:   Set new refresh rate, or compute current rate
            V:   Verify a block of RAM against an arbitrary string
            T:   Test Memory with a predefined pattern sequence
            Q:   Quit back to MS-DOS
            ?:   Show a brief program help message

          In  addition,  PMEM  provides  facilities  to  combine  multiple
       commands on  a single  command line,  along with  the capability of
       repeatedly executing  individual commands and/or the entire command
       line in order to perform "scope loops".


       Overview of PMEM

          In general,  PMEM operates very much like program debuggers like
       DEBUG.   One major  difference between  DEBUG and PMEM is that PMEM
       normally utilizes  linear addresses  (since there  is  no  standard
       segment value for addresses beyond 1 megabyte).  However, PMEM will
       permit you  to enter  addresses in segment:offset form if you wish.
       In this  format, the  ':' simply tells PMEM to multiply the segment
       number you  enter by  16, and  to add  in the offset which follows.
       For example,  entering FE00:1234 will translate to a linear address
       of 000FF234H.   Under  any circumstances, every address you specify
       will range  from 0 to FFFFFFFF (4 gigabytes-1).  All numbers may be
       entered in  hexadecimal,  decimal,  or  as  expressions  with  both
       logical and mathematical operators.

          Another feature  unique to  PMEM  is  that  it  understands  the
       difference between  Bytes, Words, and Dwords.  All commands in PMEM
       have the  capability of  performing their unique function in any of
       these modes.   In  other words,  the Display  command can  not only
       display memory as Bytes, Words, or DWords, it will also perform the
       actual memory and I/O bus cycles in this form.  This will allow you



       Page 2               (C) 1992, Mark J. Foster         July 14, 1992







       PMEM: Protected Mode Monitor                           Version 2.4A

       to check  out unique  hardware problems which may only occur during
       32-bit memory reads, etc.

          Beyond the  default word  size (set  by  the  S  command),  each
       command can  optionally have its own override attached to it.  This
       will permit  you to  normally use, say, Words, but still be able to
       execute a single command with Bytes or DWords.

          The general form of PMEM's commands is as follows:

                 <Command>[<Override>] <parameters>

       ...where the  optional word-size  override is  one of the following
       characters:
                           B    (For Bytes)
                           W    (For Words)
                           D    (For DWords)

       Note that  there is  NO space  between the command and its optional
       word-size override,  while there is a space between the command and
       its parameters.   This  can  lead  to  some  confusion,  but  is  a
       necessary evil.   Consider  the following.   The command to display
       memory is 'D'.  Let's say that you want to display memory at D0000.
       Typing DD0000  will look  to PMEM like a request to display double-
       words at  0000.   Instead, you can type D D0000 to get the job done
       (in this  second case,  PMEM will display the memory at D0000 using
       the word-size specified by the last Setmode command).

          The following examples may help confuse you...

                 DB0  Display bytes at 0
                 D B0 Display using the defaults at B0
                 DBB  Display bytes starting at 0B
                 D0   Display memory at 0 using the default

       Note from  the last  example that  when the  first character  of  a
       command's parameters  is not  'B', 'D',  or 'W',  no problems  will
       arise.  However, to prevent confusion, your best bet is to either:

            1)   Always enter  a space following every command, before its
                 parameters, when  you want  to use the default word size,
                 or...

            2)   Always enter a word-size override on every command, as in
                 DB, DW, or DD.  Then, the space isn't necessary.

          When  entering   numbers,  PMEM   normally  accepts  hexadecimal
       numbers.   However, PMEM  also has  the capability  to allow you to
       specify numbers in decimal, optionally in megabytes or Kbytes (this
       saves you  from having  to type  in all those zeroes).  To do this,
       just follow  any decimal  number with  a 'K' for Kbytes, an 'M' for
       Megabytes, or  a 'T'  (for base  Ten) for  simple decimal  numbers.
       Again, note  that a  suffix of  'K', 'M'  or 'T' indicates that the
       number you  are entering is decimal, not hex.  In other words '64K'


       Page 3               (C) 1992, Mark J. Foster         July 14, 1992







       PMEM: Protected Mode Monitor                           Version 2.4A

       is 64  * 1K,  not 64H  * 1K.   If no suffix is entered, the current
       input base  (which is  normally hexadecimal)  is  assumed  for  all
       numbers.   Ergo, if  you've left the input base set to hexadecimal,
       entering plain '64' is equal to 100 decimal, not 64.  If you try to
       enter hex  digits in  a number, followed by 'M', 'K', or 'T' (as in
       1F00T), PMEM will complain about an invalid number.

          If you  are entering  lots of decimal numbers (particularly when
       using PMEM  as a calculator), you may wish to set the default input
       base to  decimal.   The SetMode  command, in addition to specifying
       Bytes/Words/DWords as  a default,  can also  set the  input base to
       either decimal  or Hex.   Once  the input  base  has  been  set  to
       decimal, you  can still enter Hex numbers by following them with an
       'H' (ie,  FF3CH).  In fact, all of the input base specifiers (T, K,
       M, and  H) can  be used regardless of whether PMEM is in decimal or
       Hex mode  - it simply isn't necessary to specify the base specifier
       for numbers  being entered  with the default base.  For example, in
       decimal mode,  adding a  'T' after  a number has no effect.  In Hex
       mode, adding an 'H' after a number has no effect.

          One final  point about  entering numbers.    PMEM  now  has  the
       capability to  allow  you  to  enter  arbitrary  math  expressions.
       Anywhere a  number is  required, PMEM  will allow  you to  enter an
       expression which includes the following operators:

                 +  Addition         -  Subtraction

                 *  Multiplication   /  Division

                 %  Remainder        &  Bit-wise AND

                 |  Bit-wise OR      ~  Bit-wise Invert

                 ^  Bit-wise XOR     !  Logical NOT

                 == Equal to         != Not Equal

                 <  Less than        >  Greater than

                 ++ Increment var.   -- Decrement variable

                 :  Segment:offset input format for numbers

          Each of these operators may be combined in the usual manner, and
       parentheses may  be used  to delineate subexpressions.  With regard
       to precedence,  negation has  the highest precedence, then multiply
       and divide,  then addition  and subtraction,  then  binary  logical
       operations (AND, OR, and XOR).  Examples include:

                      100000+64K     1M*100+7T      4M%317

                      1K+100-5       1B7C0/2ACD     500*(2-16)

                      FFE0:27B&!3C   87|127&F0      22^15T


       Page 4               (C) 1992, Mark J. Foster         July 14, 1992







       PMEM: Protected Mode Monitor                           Version 2.4A

       NOTE! Be  careful with the segment:offset operator (':'), which has
       the same  precendence as  multiply and  divide.  If you want to use
       multiply/divide/modulus   with   a   segment:offset   number,   use
       parenthesis to eliminate any confusion, as is: "(12C0:33FB) * 2" or
       "12C0:(33FB *  2)".   With other operators such as addition, typing
       "F000:400+C6C7" is the same as typing "F000:(400+C6C7)"


       Command Summary


       S    Setmode -  sets  the  default  modes  used  by  PMEM  for  all
            subsequent commands.   When you first invoke PMEM, the default
            word size is Bytes, and the default input base is Hex.  If you
            just want  to use a command or two in Words or DWords, you can
            specify an override for the command.  Likewise, if you want to
            enter just  one or  two numbers in decimal, you can follow the
            numbers with  a 'T'.  If, on the other hand, you want to semi-
            permanently work in Word/DWord mode, or in decimal input mode,
            the Setmode  command will  change the  default mode so that it
            isn't necessary  to keep  entering overrides for each command.
            The syntax is:

                 S <mode>

            <Mode> can  be used  to set  the default  word size  to B (for
            Bytes), W  (for Words), or D (for DWords).  <Mode> can also be
            used to set the input base: T for decimal (base Ten), or H for
            Hexadecimal.  Examples:

                 SB        Set Byte Mode
                 SW        Set Word Mode
                 SD        Set DWord Mode
                 ST        Set Decimal input mode
                 SH        Set Hexadecimal input mode

       C    Compare memory.   This  command performs  a direct  comparison
            between two  different regions of protected memory (which must
            be the  same length).    As  the  regions  are  compared,  any
            differences between  the source  address (the first address on
            the command  line) and  the destination  address  (the  second
            address on  the line)  are displayed  on the  screen, with the
            contents of  the failing  addresses.    The  syntax  for  this
            command is:

                 C[<override>] <range>,<address>

            If, instead  of comparing  two different  memory regions,  you
            want to  verify that  memory holds a specific sequence of data
            values, see the Verify command, below.  Examples:

                 C 1M L1M,4M         Compare the 2nd megabyte to the 5th
                 CD1000,1FFF,300C    Compare dwords between the two areas



       Page 5               (C) 1992, Mark J. Foster         July 14, 1992







       PMEM: Protected Mode Monitor                           Version 2.4A

       D    Display Memory.   This  command can  display any  area in  the
            4-gigabyte 386/486  memory space.   Used just like the monitor
            ROM, the syntax is:

                 D[<override>] [<range>]

            The range can be specified in one of four different ways:

                 1)   <Start>,<End>       Start address to end
                 2)   <Start> L <BYTEcnt> Start address w/length
                 3)   <Start>             Start only, length is 128
                 4)   -nothing-           Continue from last Display

            Examples:

                 DB0            Display bytes at 0
                 DW FFFFFF80    Display last 128 bytes of ROM
                 D 0,3FFF       Display first 16K RAM w/default
                 DD90L10T       Display 10 bytes worth of DWords @90
                 D F000:800C    Display the ZDS Machine ID in slushware



       E    Examine Memory.   This command takes two forms.  In the first,
            you specify  a data  string to  be written  to memory.  In the
            second, you  just specify  an address,  and can  interactively
            examine and change memory.  The first form is:

                 E[<override>] <address>,{<number>|"<string>"}, ...

            In this  form, the  specified data  is written directly to the
            memory address  you specify.   This is equivalent to filling a
            memory block which is exactly as long as the data you specify.
            For more  details on entering strings, see the 'Fill' command,
            below.   In the second form of the Examine command, the syntax
            is:

                 E [<override>] <address>

            When you  use this form, PMEM will display the contents of the
            specified memory  location, and will prompt you for a new data
            value.  If you want to change the contents as shown, type in a
            new value,  followed by  Enter.   To move  forward to the next
            location in  memory, just  press Enter,  or a  space.  To move
            backwards to the previous location, press BackSpace.  When you
            are finished examining a block of memory, press Escape.

            Examples:

                 ED100000       Examine the DWord at 100000 (interactive)
                 E 32K-17       Examine w/default at 7FE9 (interactive)
                 EW1234,5678    Write 5678H at location 1234H
                 EB9000,"ABC"   Write bytes of 41H,42H,43H to 9000H-9002H



       Page 6               (C) 1992, Mark J. Foster         July 14, 1992







       PMEM: Protected Mode Monitor                           Version 2.4A



       F    Fill Memory with a user-specified string.  The fill command is
            used to  write a  block of memory with a distinct memory value
            or values.  The syntax is:

                 F[<override>] <range>,{<number>|"<string>"}, ...

            The string  can be  any mixture  of hex  numbers and/or  ASCII
            characters.   When  numbers  are  entered,  they  are  entered
            according  to   the  appropriate  word  size.    For  example,
            'FD 100000L100,1' would  fill the  256 bytes  starting at  the
            base of  the second  megabyte with the value 00000001.  If you
            then   display    this    as    bytes,    you    would    see:
            01H,00H,00H,00H,01H,00H,00H,00H..., since  the 386/486  places
            bytes in reverse order.

            Whenever you  enter ASCII  characters, they  are automatically
            byte-packed to  correspond to  the correct  word  size.    For
            instance, 'FD 200000L10000 "Hi!",D' will fill the 64K starting
            at 200000  with 48H,69H,21H,0DH,00H,00H,00H,00H which would be
            displayed in  double-word mode  as 4869210DH,00000000H.   Note
            that ALL  entities are  byte packed,  so that  if you enter an
            ASCII string  which is  five bytes long, followed by a number,
            the number  will be shifted to align with the string (in other
            words, if you want numbers to appear with the proper alignment
            following ASCII  strings, make sure the strings evenly fit the
            word size you are using if you are in Word or DWord mode).

            Regardless of  what you  enter, if  the sum total of the bytes
            you have  entered does not evenly match the current word size,
            PMEM will pad trailing 0s into the fill string.  For instance,
            if you  do a  DWord Fill with "ABC", PMEM will write 00434241H
            to each DWORD.

            Examples:

                 F  8000:0,8FFFF,"Hello"  Fill 64K with "Hello"
                 FD 80000L100,12345678    Fill 256 bytes w/12345678
                 FW 1M,1M+1M/2,9999,7A+CD Fill 1.5M+2 w/9999H,0147H
                 FB B800:0 L 16K,"1",17H  Fill screen w/white on blue '!'s



       H    Hex Math.   PMem  can directly display the results of a simple
            math expression  in both hexadecimal and decimal.  To do this,
            just type in the expression to be displayed.  Syntax:

                 H <number>[+|-<number>]...

            Examples of this command include:

                 H 1M+64K+4K+256T+10+1    Displays: 00111111H  1118481T
                 H 3FCD0+FFE0             Displays: 0004FCB0H  326832T


       Page 7               (C) 1992, Mark J. Foster         July 14, 1992







       PMEM: Protected Mode Monitor                           Version 2.4A

                 H 1M-16T                 Displays: 000FFFF0H  1048560T
                 H 2900/17T+FF*120        Displays: 00012149H  74057T
                 H 55 | 37 ^ (2C & !15)   Displays: 0000005FH  95T



       I    Input from  one or  more  I/O  ports.    As  with  the  memory
            commands, I/O  can also be done using Bytes, Words, or DWords.
            Unlike the  monitor ROM,  the Input command can also display a
            range of I/O ports.  The syntax is:

                 I[<override>] <range>

            The range  is very  much like  that specified  for the display
            function,  except   that  if  no  end  address  or  length  is
            specified, the  result is  that a single I/O port is displayed
            (rather than 128).

            Examples:

                 IB 0,3FF       Display the 1K PC/AT ports as bytes
                 I80            Read w/default from I/O port 80H
                 IW80           Read I/O ports 80H,81H as 1 word



       M    Move a  block of  memory to  another location.   This  command
            operates identically  to the  monitor ROM, except that it does
            NOT check  for overlapping  moves.  In other words, if you are
            moving a  block of  memory to  another location which overlaps
            with the source block, data will be lost.  The purpose of this
            choice was to ensure that what you type, you get! Syntax:

                 M[<override>] <range>,<destination>

            Examples:

                 MD B000:0L64K,1M         Move all video RAM to 1M
                 M  320K,640K-1,100000    Copy the top 320K to Extended
                 MW 0,16M,0               Rewrite the base 16M with self


       O    Output to  a single I/O port.  This command operates just like
            the monitor  ROM (except for the override option).  The syntax
            for this command is as follows:

                 O [<override>] <port>,<value>

            Examples:

                 OBFB,0              Enable the ZDS Privy port
                 OD 80H,12345678     Write ports 80-83 w/78,56,34,12.
                 OFFF0,1             Write a 1 to default width at FFF0



       Page 8               (C) 1992, Mark J. Foster         July 14, 1992







       PMEM: Protected Mode Monitor                           Version 2.4A



       R    Refresh rate  set/determine.   This command allows you to slow
            down or  speed up  the refresh  rate  to  help  find  refresh-
            associated failures.   To  set the refresh rate, enter the new
            desired refresh  rate in  microseconds (from  3-50000).  If no
            number is  entered, the  routine will  attempt to  compute the
            current approximate refresh rate.  Syntax:

                 R [<uSec>]

            Examples:

                 R                   Display the current refresh rate
                 R10                 Set refresh to 16T (Normal rate)
                 R128T               Set slow-refresh mode


       T    Test a  block of memory.  PMEM now uses a "March Test" to test
            a block  of memory,  by making  sequential passes  which  both
            verify memory  and write  new contents  in each pass (the test
            makes a  total of  nine passes over each block).  To help show
            test  progress,   PMEM  will  display  a  single  digit  which
            increments to  show you  the phase of the memory test (from 0-
            9). This  new test  procedure is  very  effective  at  finding
            read/write errors, as well as addressing errors.

            Another option  offered by  the test  command  is  to  perform
            refresh testing.   If  specified, the  routine will wait for a
            user-entered number  of seconds  between test passes, with the
            CPU halted.   This  will help "encourage" any potential memory
            refresh failures  in the system being tested.  To specify this
            option, enter 'W' after the range.  Syntax:

                 T[<override>] <range> [W<waitcount_in_seconds>]

            Examples:

                 T100000L100000           Test second megabyte of RAM
                 TW2M,3M-1,W5             Test 3rd Meg as words w/5 second
                                          delay between passes
                 TB100000,1C2FF0          Test specified block as bytes


       V    Verify a  block of  memory against  an arbitrary string.  This
            command is  just like  Fill, except  that it verifies that the
            data in  the memory  block is correct, rather than writing the
            data.  The syntax is:

                 V[<override>] <range>,<string>

            This command will display any discrepancies between the string
            and the  memory block  by printing the address of the failure,
            along with the good data (what SHOULD have been there) and the


       Page 9               (C) 1992, Mark J. Foster         July 14, 1992







       PMEM: Protected Mode Monitor                           Version 2.4A

            bad data  (what WAS  there).  If the entire block verifies OK,
            the routine won't print anything.

            Examples:

                 VD1ML5M,0                Is 1st 5 Meg of extended RAM=0?
                 VB80000L100,12345678     Verify 64 DWords are 12345678
                                          (Remember, L specifies # BYTEs)



       W    Wait for  a specified  number of  seconds.  This option uses a
            'hard' delay,  where  the  entire  system  will  be  quiescent
            throughout the delay.  This is accomplished by placing the CPU
            in a  halt state,  and then  using the real time clock's alarm
            output to  wake up  the CPU once the requested time period has
            elapsed.  Syntax:

                 W <seconds>

            Example:

                 W5                       Wait for 5 seconds, with the
                                          CPU halted.

       "    The Quote  command (")  is used  to display  a prompt message.
            The syntax is:

                 "<ascii string>",[<number>|"string"]...

            Examples include the following:

                 "Result is ";D@0L1  Display msg followed by memory at @1
                 "",0D,0A            Display a blank line
                 "2+2=";2+2          Display 2+2=4!


       Repeating Command Execution

          One of  the most  powerful features  of PMEM  is its  ability to
       repeat both  individual commands,  as well  as repeating the entire
       command line.   To  repeat an  individual command, follow it with a
       backslash ('\').   Optionally,  you may follow the backslash with a
       repeat count - if you do not enter a repeat count, PMEM will repeat
       the requested command forever (until you press ESCape).  Examples:

                 I41\                Repeatedly display the refresh timer
                 T1ML1MW5\10         Test the 2nd meg of RAM, with a 5
                                     second delay between passes, for a
                                     total of 16 passes.

          It is  also possible to string multiple commands together on the
       same command  line by separating them with a semicolon (';').  This
       allows multiple functions to be performed at the same time.  Alone,


       Page 10              (C) 1992, Mark J. Foster         July 14, 1992







       PMEM: Protected Mode Monitor                           Version 2.4A

       this isn't  a very  useful capability,  but in conjunction with the
       ability to repeat the entire command line, it can be quite helpful.

          To repeat  a command line, enter either a forward slash ('/') or
       a backslash  ('\') command at the end of the command line.  Using a
       slash will simply repeat the command, while a backslash will repeat
       the command  and then  print a pass number on the screen after each
       repetition (this  will enable  you to verify that the loop is still
       executing).

          Note here  an important  syntax difference  between repeating  a
       command, and  repeating the  command line.    To  repeat  a  single
       command, follow the command directly with a backslash (and optional
       repeat count).   To repeat an entire command line, enter the '\' or
       '/' as a separate command (in other words - follow the last command
       on the  line with  a semicolon,  then with  a slash  or backslash).
       Examples include:

                 FD1ML1M,0\          Fill the 2nd meg of RAM w/0
                                     forever, displaying a pass count.

          If, instead,  you just  want to  write a pattern and continually
       look for read failures, you can type:

                 FD1ML1M,0           Fill the memory
                 VD1ML1M,0\          Verify it forever

          Another takeoff on this concept permits you to continually write
       memory with different patterns, as follows:

                 F512KL4K,55;F80000,80FFF,AA;/

       This command  will repeatedly  write the same block of memory first
       with 55H,  then with  0AAH  (note  the  two  different  methods  of
       specifying the  same memory  block, and the usage here of repeating
       the entire command line, rather than a single command.

          Whenever you  are performing  a repeated  command such  as those
       noted above,  PMEM will  loop forever  (or until  you  stop  it  by
       pressing ESCape).   If you simply want to execute a loop a specific
       number of times, just follow the repeat command ('/' or '\') with a
       count value.  PMEM will then repeat the command the number of times
       you specify and stop automatically.

          To abort  any command,  press ESCape.   If  ESCape doesn't work,
       you've probably hosed the machine - PMEM makes no effort whatsoever
       to prevent  you from  blowing important things away.  Keep in mind,
       however, that  some commands do take quite a while to execute.  For
       example, testing big blocks of extended memory (multiple megabytes)
       can take tens of seconds or more; you may have to be patient.






       Page 11              (C) 1992, Mark J. Foster         July 14, 1992







       PMEM: Protected Mode Monitor                           Version 2.4A

       Variables

          For some  more complex  tests, it is sometimes necessary to have
       additional flexibility.   To support these more complex tests, PMEM
       provides fifty numeric variables, which can be assigned, displayed,
       used in  any command,  etc.   These variables are specified with an
       '@', sollowed by a variable index.  Legal variable names include @0
       to @49T  (equivalently, @00H to @31H).  These variables can be used
       anywhere a number would be used, and will serve the same purpose as
       a number.   Specify a variable name alone (as in @1), and the value
       used will  be the  current contents of the variable.  Additionally,
       you can  follow a  variable name  with a  equals sign to assign the
       result of an expression to the variable.

          When you  specify a  variable index,  you will  normally type  a
       simple number, as described above.  However, it is also possible to
       enter a  parenthesized subexpression  following the '@' sign.  This
       will allow  you to  specify a variable name indirectly (essentially
       providing the same function as a CPU index register).  For example,
       "@(5) =  1" is  simply another  way of  setting variable  @5 to  1.
       However, "@(@5)  = 1" is a very different beast.  This means to set
       the variable  pointed to  by @5  to 1.  In this case, if @5 was 17,
       then "@(@5) = 1" would set @17 to 1 (@5 remains unchanged).

          The final  capability offered  for variables  is the  ability to
       increment and  decrement them,  as a  convenient shorthand.   To do
       this, follow  a variable  name with  ++ (to add 1 to it), or -- (to
       subtract 1  from it).   Note  that this  is  equivalent  to  typing
       @var=@var+1, or @var=@var-1, respectively.

            Some examples of variable usage include:

            @0++                      Increment variable 0
            @0                        Displays the contents of variable 0
            D@0L@1                    Displays memory starting at (@0),      
                                      for length (@1)
            @0*@1                     Show result of multiplying @0 and @1

            @0=1                      Set variable 0 to 1
            @(@0)=55H;@0++;/10T       Set variables 1 to 10 to 55H

            @0=@1=1                   Set @0 and @1 to 1
            @0;@2=@0+@1;@0=@1;@1=@2;/ Display the Fibonacci numbers!

            @0=1M                     Set @0 to the start of extended RAM
            E@0,@0&FF;@0++;/4K        Fill 4K with 0,1,2...FF,0,1,2...etc.

          As a  final example of the power of PMEM, consider the following
       test:

          @0=16T

          R@0;R;M1ML512K,1M+512K\200;T1ML1MW3;@0=(@0*110T)/100T;\



       Page 12              (C) 1992, Mark J. Foster         July 14, 1992







       PMEM: Protected Mode Monitor                           Version 2.4A

          This incredibly  complicated looking  pair of  commands  can  be
       broken down  as follows.   The first command simply sets variable 0
       to 16  - which  is the  normal memory refresh rate in microseconds.
       The next line can be interpreted as follows:

          R@0                   Set the refresh rate to the contents of @0
                                (initially, this is 16 microseconds)
          R                     Display the current refresh rate
          M1ML512K,1M+512K\200  This command will move memory from 1M to
                                1.5M to the area from 1.5M to 2M, and will
                                repeat the move 200H (512T) times.
          T1ML1MW3              Test the second megabyte with a wait-for-
                                refresh test of 3 seconds between phases.
          @0=(@0*110T)/100T     Increase the value of @0 by 10%.  Since
                                PMEM doesn't have floating point, the use
                                of a multiply/divide pair provides the
                                same capability.

       In total,  then, this  pair of  commands will first run memory very
       hard to ensure as much heat build-up as possible occurs (this helps
       to induce  memory refresh  errors), then it tests to see if refresh
       errors will  actually occur.   After  doing this  test, the refresh
       rate is  increased by  10% and  the entire  process repeats.   This
       single  command  provides  a  very  simple  way  of  verifying  how
       resistant a system is to refresh failures.


       Memory and I/O Pseudo-Arrays

          One final  capability offered  by PMEM (and potentially the most
       powerful) is  that it  supports direct  access to  memory  and  I/O
       within expressions.   PMEM  uses built-in pseudo-arrays which allow
       you to  specify any memory or I/O location in a manner very similar
       to the  @xx variables  mentioned above.   This  is much  easier  to
       demonstrate than to explain:

            M[0]           Memory location 0, in the current mode
            IW[80]         The word-sized input port at 80H
            OB[F2]         Byte-sized output port at F2H

          These pseudo-arrays  may be  treated just  like variables in any
       expression.   For instance,  you can  see the  contents  of  memory
       location 0  just by  typing M[0].  In addition, these pseudo-arrays
       may also  be written to.  To change the contents of memory at 1M to
       55H, type:  M[1M]=55.  Write to an I/O port in the same manner, ie,
       O[F2]=AA.

          The real power of the memory and I/O arrays comes from their use
       in repeated expressions.  Some examples include:

            @0=0;@1=1M                    Set @0 to 0, @1 to 1 Megabyte
            M[@1]=I[@0];@0++;@1++;\400    Copy all I/O ports to 1M RAM!
            O[F2]=M[1ABCD];/              Copy memory data to output port



       Page 13              (C) 1992, Mark J. Foster         July 14, 1992







       PMEM: Protected Mode Monitor                           Version 2.4A

       Summary

          In summary,  I hope that you find PMEM useful.  Just remember to
       run it  only on  386 or 486-based systems, and be somewhat cautious
       until you've learned the program.  PMEM has been around awhile, but
       no doubt  still has  a few  bugs lurking  in it.   If you happen to
       encounter one, please drop me a line as to what went wrong, and how
       you made  it happen.  Have fun with it, and please let me know what
       you think!

                                Mark J. Foster
                                4284 White Pine Circle
                                St. Joseph, Michigan  49085
                                Compuserve ID: [76505,2436]
                                                        









































       Page 14              (C) 1992, Mark J. Foster         July 14, 1992







       PMEM: Protected Mode Monitor                           Version 2.4A

       Change History

       07/14/92: Version 2.4A
            - Added ability to repeat individual commands


       07/14/92: Version 2.4
            - Corrected expression evaluator errors in complex expressions
            - Added the 'Wait' command to help find refresh errors
            - Changed syntax of the Test Refresh command to Test Wait
            - Modified Test Wait to use the new full-halt WAIT for
              more complete refresh error testing

       07/13/92: Version 2.3
            - Added comparison operators: <, ==, >, !=
            - Added tertiary if-then-else: <cond> ? <expr1> ` <expr2>
            - Added memory pseudo-array variables
            - Added I/O pseudo-array variables
            - Added Increment and Decrement commands

       07/12/92: Version 2.2
            - Added Refresh Test option to the memory test
            - Added ability to set new refresh rate for memory testing
            - Added "display refresh rate" capability

       07/11/92: Version 2.1A
            - Fixed error on the last byte of a block while doing a
              Test or Verify command.  In this situation, PMEM would
              continue verifying past the end of the block.
            - Improved error handlers to show pass count where errors
              occurred, if the passcount feature is being used.

       07/11/92: Version 2.1
            - Added Fast Block Clear to memory test during phase 0
            - Added Fast Block Clear during Fills with a string length
              of just one entity.

       07/10/92: Version 2.0A
            - Corrected problem with repeat counts following a '\'

       07/10/92: Version 2.0
            - Modified memory test to make 10 phases with worst-case data
            - Added memory phase display to indicate progress of testing.

       07/09/92: Version 1.9
            - Rewrote memory test to use predefined data, in 7 phases.
              This march test is much better at finding errors than the
              prior PMEM algorithms.
            - Modified '\' to display a pass counter instead of a period.
            - Modified Compare, Verify, and Test NOT to display 'OK'
              after testing a block, to prevent errors from scrolling off
              the screen.

       03/16/92: Version 1.8B


       Page 15              (C) 1992, Mark J. Foster         July 14, 1992







       PMEM: Protected Mode Monitor                           Version 2.4A

            - Fixed exit-to-DOS bug with MS-DOS 5
            - Adapted source to compile under Borland's BCC Compiler
            - Updated and improved documentation

       07/24/90: Version 1.8A
            - Modified help message to include variables, repeat counts
            - Fixed error message on missing quotes (used to say missing
              parenthesis).

       07/20/90: Version 1.8
            - Added variable support (@0-@50T)
            - Added assignment to variables (@xxx = <expression>)
            - Added quote (") command for text prompts
            - Limited input line length to 128 characters
            - PMEM now allows negation of parenthesized subexpressions
            - Added ability to use parenthesized subexpressions in strings

       07/19/90: Version 1.7B
            - Corrected problem with long input lines overwriting internal
              variables (caused various weird behaviors).

       07/18/90: Version 1.7A
            - Corrected problem w/V1.7 which displayed the current modes
              every time an override was used.

       07/18/90: Version 1.7
            - PMEM now uses SCP Gate-A20, instead of Fast-A20.  This lets
              it run on all ATs, not just ZDS machines.

       07/18/90: Version 1.6B
            - Added decimal/Hex default input modes
            - Added 'H' to specify Hex numbers in decimal mode
            - Added current mode display to setmode, and at startup
            - Added divide-by-zero check

       07/17/90: Version 1.6A
            - Corrected problem where a compare error on the last byte
              of a block would compare past the end of the block
            - Added a CPU Type Check so PMem will complain about the
              wrong CPU, rather than just die.
            - Added optional repeat count following a repeat command
              (either '/' or '\').

       07/13/90: Version 1.6
            - Added segment:offset format numeric input

       07/12/90: Version 1.5B
            - Corrected problem with Verify Bytes w/length > 64K
            - Fixed spurious error message after interactive Examine

       07/11/90: Version 1.5A
            - Added logical binary operators (&:AND, |:OR, ^:XOR)
            - Added unary negation operator (!:NOT)



       Page 16              (C) 1992, Mark J. Foster         July 14, 1992







       PMEM: Protected Mode Monitor                           Version 2.4A

       07/11/90: Version 1.5
            - Added multiply, divide, and modulus operators
            - Added parenthesis handling for subexpressions
            - Added decimal display to the hex math command
            - PMEM once again requires a ';' before a repeat command
              ('/') to prevent the slash  from  being misinterpreted
              as a division request.

       07/09/90: Version 1.4A
            - Added ability to accept math expressions
            - Added <expression> 'command'
            - Display speed substantially increased
            - PMEM has been reduced in size by ~3.5K

       07/06/90: Version 1.4
            - Added the Compare Memory command

       07/06/90: Version 1.3B
            - Disabled NMIs to prevent reboots while in protected mode
            - Added '\' (loop with '.' echo on each pass)
            - Eliminated need for ';' before '/' or '\'

       07/05/90: Version 1.3
            - Added Move command

       07/05/90: Version 1.2B
            - Added 'M' and 'K' suffixes for numerical entries
            - Changed input base on 'M' and 'K' numbers to decimal
            - Fixed verify count problem on long blocks

       07/03/90: Version 1.2A
            - Corrected inability to use lower-case in strings
            - Fixed problem with non-aligned fills
            - Corrected documentation bug w/FD200000L10000,"Hi!",D






















       Page 17              (C) 1992, Mark J. Foster         July 14, 1992