**********************************************************************
     *                                                                    *
     *                       RunWen Users Manual                          *
     *                                                                    *
     *              RunWen - A Boot-up Program Scheduler                  *
     *                                                                    *
     *               Copyright (c) 1992 Richard Hiester                   *
     *                       All Rights Reserved                          *
     *                                                                    *
     **********************************************************************

     INTRODUCTION
     ============

     RunWen is a DOS Program Scheduler which is normally started from your 
     AUTOEXEC.BAT file.  This means that the programs you specify will be
     started by RunWen when you boot-up your computer.  RunWen can age
     the specified programs to run everytime you boot your computer, once 
     a day, or once every N days.  Options are available to specify how
     you want RunWen to run (in prompt or noprompt mode), to list the 
     RunWen source file (RUNWEN.FIL), to display the RunWen Version number,
     and to display a two-page help screen.

     INSTALLATION
     ============

     The following files are part of this release of RunWen:

          RUNWEN.EXE   - The RunWen executable.
          RUNWEN.FIL   - The RunWen source file.
          RUNWEN.DOC   - This documentation file.
          ORDERFRM.DOC - The order form used to register RunWen.

     The installation of RunWen is easy:

     1)  Copy the above files into your desired directory.

     2)  Edit the RUNWEN.FIL source file to specify which DOS programs 
         you want aged.

     3)  Edit your AUTOEXEC.BAT file adding the following lines:

              set RUNWEN=DRIVE:\DIRECTORY_TO_RUNWEN.FIL

              [DRIVE:PATH]RUNWEN -BOOT [-NOPROMPT]

     4)  Reboot your computer to start using RunWen.

     CONFIGURATION
     =============

     The only configuration necessary for using RunWen is to add your
     desired programs to the RUNWEN.FIL source file.  The RUNWEN.FIL
     file contains one line for each program you want aged.  For you
     UNIX types, the RUNWEN.FIL format is simular to the crontab.  The
     RUNWEN.FIL format is as follows:

     YYYYMMDD DYS DOS_COMMAND_LINE


                                                                   Page 2

     where YYYYMMDD is the four-digit year, two-digit month, and two
     digit day that you want RunWen to start aging the program from,
     DYS is the number of days you want between executions of the program,
     and DOS_COMMAND_LINE is the DOS command line you would enter to start
     the program.  For instance, one of the programs I use RunWen for
     is to run the Norton AntiVirus program.  I have the following entry in
     my RUNWEN.FIL to run the Norton AntiVirus (full scan, all disks)
     every seven days:

     19920801 7 C:\NDW\NAV.EXE /A

     By placing the above line in the RUNWEN.FIL file, Norton AntiVirus 
     will be run the first time you boot your computer on (or after) 
     August 8, 1992.  When the program is run, the RUNWEN.FIL is updated
     to the NEW last date the program was run.  That is, if the AntiVirus
     program is run on August 8, 1992, the the new entry in the RUNWEN.FIL
     file will be:

     19920808 7 C:\NDW\NAV.EXE /A

     and the AntiVirus program will not be run by RunWen again until 
     August 15, 1992.  

     Please read the comment lines in the RUNWEN.FIL file for further
     information about the RUNWEN.FIL file.

     OPTIONS
     =======

     The command line for RunWen is as follows:

     C> RUNWEN [-BOOT [-NOPROMPT]] | [-LIST] | [-VER] | [-HELP]

     The options available on the RunWen command-line are as follows:

     -BOOT (abbreviated to -B) is used to tell RunWen to process the 
          RUNWEN.FIL file.

     -NOPROMPT (abbreviated to -NOP) is used in conjunction with -BOOT
          to tell RunWen not to prompt you whether you want to run 
          the program which is due to be run by RunWen.

     -LIST (abbreviated to -L) is used to list the RUNWEN.FIL on the 
          screen.  This option cannot be used in conjunction with the 
          -BOOT [-NOPROMPT] options and is mutually exclusive of the
          -VER and -HELP options.

     -VER (abberviated to -V) displays the version of RunWen you are
          using on the screen.  This option cannot be used in conjunction
          with the -BOOT [-NOPROMPT] options and is mutually exclusive of 
          the -LIST and -HELP options.

     -HELP (abbreviated to -H or -?) displays a two-page help screen on
          the use of RunWen.  This option cannot be used in conjunction 
          with the -BOOT [-NOPROMPT] options and is mutually exclusive 
          of the -VER and -LIST options.


                                                                   Page 3

     REGISTRATION
    ============

     Registering your copy of RunWen is simple.  Just print out the 
     ORDERFRM.DOC file, fill in the required information, and send it with
     the requested payment amount.  Your registration will be processed per
     your request and you will be placed on my mailing list for any future
     upgrades.

     LICENSE
     =======

     You are free to use, copy, and distribute the Shareware version of
     RunWen so long as:

     1)  No fee is charged for its use.

     2)  If a fee is charged, it must be only to cover the cost of copying
         or distribution.

     3)  It must be distributed in its original form with all of the 
         originally released files intact.

     4)  It has not been modified in ANY way EXCEPT for compression.

     No part of the REGISTERED version of RunWen may be reproduced or
     transmitted in any form or by any means, electronic or otherwise,
     for any purpose other than the purchasers personal use, witout
     the express written permission of the author.


     WARRANTY
     ========

     All warranties are disclaimed, including any damage to hardware and/or
     software, from the use of this product.  In no event will I be held 
     liable to you for any damage including lost profits, lost savings or
     other incidental or consequential damages arising out or your use or
     inability to use this program, or any other claim by any other party.