SHADOW RAM MEMORY CONTROLLERS

                                  supported by


                        THE LAST BYTE MEMORY MANAGER (tm)







                                  Version 2.11










                              Copyright (C) 1990-92
                               All Rights Reserved


                                       by


                              KEY SOFTWARE PRODUCTS

                                440 Ninth Avenue
                          Menlo Park, California 94025
                                  415-364-9847














        The Last Byte Memory Manager is a trademark of Key Software Products.



        



                                TABLE OF CONTENTS



        CHAPTER 1 - INTRODUCTION        ...........................    1
           1.1  Hardware Requirements       .......................    1
           1.2  Supported Chipsets       ..........................    1
              1.2.1  Chips and Technologies      ..................    1
              1.2.2  ETEQ Microelectronics       ..................    2
              1.2.3  Forex Computer Corporation      ..............    2
              1.2.4  Headland Technology (G2)      ................    2
              1.2.5  Intel Corporation       ......................    3
              1.2.6  OPTi Electronics       .......................    3
              1.2.7  Sun Electronics (SUNTAC)      ................    4
              1.2.8  Symphony Laboratories       ..................    4
              1.2.9  Texas Instruments       ......................    4
              1.2.10  United Microelectronics Corporation (UMC)        4
              1.2.11  VLSI Technology       .......................    5
           1.3  Unsupported Chipsets       ........................    5
              1.3.1  No Shadow Ram Support     ....................    6
              1.3.2  Shadow Ram is not Read/Write    ..............    6
              1.3.3  Overly Complex Control      ..................    6
              1.3.4  Locked Configuration Registers      ..........    6
           1.4  Checking Compatibility Using CHIPSET     ..........    7

































        




        Aug 11, 1992      SHADOW RAM MEMORY CONTROLLERS                 1


                        CHAPTER 1 - INTRODUCTION        


        1.1 Hardware Requirements        

        To  install The Last Byte Memory Manager, your computer must have
        a  means  of providing read-write memory in the Upper Memory Area
        between  640k  and  1 megabyte.  This is possible if you have any
        of the following: 

             o  Fixed  RAM memory already resident in the upper area
                (such  as  the 32-bit "Built In Memory" installed in
                some Compaq 386 machines), or 

             o  An  expanded memory board (EEMS, LIM 3.2 EMS, or LIM
                4.0 EMS), or 

                        ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
                        ³ NOTE: Using a LIM 3.2 EMS board is not advised  ³ 
                        ³ as a method of providing upper memory.  It pro- ³ 
                        ³ vides only 64k of upper memory and prevents ap- ³ 
                        ³ plication software from using expanded memory.  ³ 
                        ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ 

             o  A  386sx,  386,  486,  or  486sx  processor  and the
                Microsoft  Windows  3.0/3.1  or  DOS  5  versions of
                EMM386, or 

             o  One  of  the  shadow  ram  memory  controller  chips
                listed in the next section.  


        1.2 Supported Chipsets        

        Key  Software  Products  is  continually  adding  support for new
        chipsets  as  they  become  known to us and technical information
        can  be  obtained.  Those that are currently supported in version
        2.11  are  listed in the paragraphs below.  Some that we know of,
        but which cannot be supported are listed in the next section.  


        1.2.1 Chips and Technologies       

        The  following  chips  all  provide 384k of memory in twenty-four
        16k blocks between A0000-FFFFF.  









        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Aug 11, 1992      SHADOW RAM MEMORY CONTROLLERS                 2


             82C212 - From the CS8221 NEAT (tm) chipset
             82C222 - From the CHIPS/250 PS/2 50/60 chipset
             82C230 - The PS/2 30 Single Chip Controller
             82C235 - The SCAT (tm) Single Chip AT VLSI chip
             82C241 - From the CS8223 LeAPset (tm) chipset
             82C302 - From the CS8230 386/AT CHIPSet (tm)
             82C307 - From the CS8231 386/AT CHIPSet (tm)
             82C311 - From the CS8233 PEAK 386/AT CHIPSet (tm)
             82C351 - From the CS82310 PEAK DM/386 AT CHIPSet (tm)
             82C812 - From the CS8281 NEATsx (tm) chipset
             82C836 - The SCATsx (tm) Single Chip AT VLSI chip
             82C841 - From the CS8283 LeAPset-sx (tm) chipset

             (The  82C212  is  identical  to the UMC82C212 made by United
             Microelectronics Corporation.) 

        The  following chip provides 384k of memory in sixteen 16k blocks
        between A0000-DFFFF and one 128k block between E0000-FFFFF.  

             82C322 - From the CHIPS/280 PS/2 70/80 chipset


        1.2.2 ETEQ Microelectronics        

        These  chips  all  provide  192k  of  memory in twelve 16k blocks
        between  C0000-EFFFF.   If you have a VGA or EGA adapter, you may
        get  additional  memory  by  using  the  MOVE=OVERLAY  option  of
        LASTBYTE.SYS.  

             ET82C391  - From the Bobcat 386DX/486DX chipset
             ET82C491  - From the Cougar 386DX/486DX chipset
             ET82C4901 - From the Bengal 386DX/486DX chipset

             (The  ET82C391  and  '491  are  indistinguishable;  both are
             reported as a '491.) 


        1.2.3 Forex Computer Corporation       

        The  following  chip  provides  256k  of memory in six 32k blocks
        between C0000-EFFFF and one 64k block between F0000-FFFFF.  

             FRX36C300 - From the FRX36C300/200 Cache chipset


        1.2.4 Headland Technology (G2)       

        The  following  chip provides 64k of memory by using the four 16k
        blocks of the EMS page frame.  





        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Aug 11, 1992      SHADOW RAM MEMORY CONTROLLERS                 3


             HT12  - Single 286 AT Chip

        The  following  chips all provide 128k of memory by using the EMS
        mapping area between C0000-DFFFF.  

             HT18  - 286/386SX Advanced Memory Manager Chip
             HT21  - 286/386SX Advanced Memory Manager Chip
             HT22  - 286/386SX Advanced Memory Manager Chip
             HT103 - 286/386SX Advanced Memory Manager Chip
             HT113 - 286/386SX Advanced Memory Manager Chip


        1.2.5 Intel Corporation        

        The  following  chips provide 192k of memory in twelve 16k blocks
        between  C0000-EFFFF.   If you have a VGA or EGA adapter, you may
        get  additional  memory  by  using  the  MOVE=OVERLAY  option  of
        LASTBYTE.SYS.  

             82343 - From the 82340SX Chip Set
             82346 - From the 82340DX Chip Set

             (The  82343  and  82346  are  identical  to the VL82C320 and
             VL82C330 made by VLSI Technology.) 

        The  following  chip  provides  384k of memory in twenty-four 16k
        blocks between A0000-FFFFF.  

             82359 - From the 82350DT EISA Chip Set


        1.2.6 OPTi Electronics        

        The  following  chips  all  provide  192k of memory in twelve 16k
        blocks  between  C0000-EFFFF.   If you have a VGA or EGA adapter,
        you  may  get  additional memory by using the MOVE=OVERLAY option
        of LASTBYTE.SYS.  

             82C281 - From the Cache SX/AT chipset (w/posted write)
             82C282 - From the Cache SX/AT chipset (w/o posted write)
             82C283 - From the Block Interleave SX/AT chipset
             82C382 - From the HiD/386 AT chipset
             82C391 - From the 386WB PC/AT chipset
             82C461 - From the Notebook PC/AT chipset
             82C482 - From the HiB/486 AT chipset
             82C491 - From the 486SXWB PC/AT chipset
             82C493 - From the 486SXWB PC/AT chipset
             82C495 - From the 486SXWB PC/AT chipset
             82C496 - From the DXBB PC/AT chipset

             (The  '281,  '282, and '283 are software compatible; all are



        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Aug 11, 1992      SHADOW RAM MEMORY CONTROLLERS                 4


             reported  as an 82C281.  Similarly, the '491, '493, and '495
             are both reported as an 82C493.) 

        The  following  chip  provides 256k of memory in eight 16k blocks
        between C0000-DFFFF and two 64k blocks between E0000-FFFFF.  

             82C682 - From the 386/486WB EISA chipset


        1.2.7 Sun Electronics (SUNTAC)       

        All  SunTac  chips  provide  128k  of  memory  in four 32k blocks
        between  E0000-FFFFF.   An  additional  128k  in eight 16k blocks
        between  C0000-DFFFF  is available at the expense of all Expanded
        Memory  by adding the word NOEMS to the SUNTAC Physical option as
        in: Physical=ST62C202,NOEMS.  

             ST62C202 - From the chipset 20 for 286
             ST62C241 - From the chipset 24 for 386
             ST62C251 - From the chipset 25 for 286 and 386sx


        1.2.8 Symphony Laboratories        

        The  following  chips  provide 256k of memory in eight 16k blocks
        between   C0000-DFFFF   andanother   two   64k   blocks   between
        E0000-FFFFF.  

             SL82C361 - From the SL82C360 80386DX/SX chipset
             SL82C461 - From the SL82C460 80486 chipset


        1.2.9 Texas Instruments        

        The  following  chips  provide  384k of memory in twenty-four 16k
        blocks between A0000-FFFFF.  

             TACT82411  - The Snake Single-Chip AT Controller
             TACT82S411 - The Snake+ Single-Chip AT Controller


        1.2.10 United Microelectronics Corporation (UMC)      

        The  following  chip  provides  384k of memory in twenty-four 16k
        blocks between A0000-FFFFF.  

             UM82C212 - From the UM82C210 386SX/286 AT Chip Set

             (The  UMC82C212 is identical to the 82C212 made by Chips and
             Technologies.) 




        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Aug 11, 1992      SHADOW RAM MEMORY CONTROLLERS                 5


        The  following  chip  provides 256k of memory in eight 16k blocks
        between C0000-DFFFF and two 64k blocks between E0000-FFFFF.  

             UM82C481 - From the UM82C480 50Mhz 80486 Chip Set


        1.2.11 VLSI Technology        

        The  following  chip  provides  384k  of memory in six 64k blocks
        between A0000-FFFFF.   

             VL82C202 - PC/AT-Compatible High Speed Memory Controller

                ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
                ³ Pin 69 on th VL82C202 controls whether its      ³ 
                ³ shadow ram is enabled or relocated.  This pin   ³
                ³ is usually tied to a jumper on the motherboard  ³ 
                ³ which must be set properly to work.             ³
                ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ 

        The  following  chips  provide  384k of memory in four 32k blocks
        between  A0000-BFFFF,  eight  16k blocks between C0000-DFFFF, and
        four 32k blocks between E0000-FFFFF.  

             VL82C310 - From the SCAMP 286/386sx Chip Set
             VL82C311 - From the SCAMP 286/386sx Chip Set

        The  following  chips provide 192k of memory in twelve 16k blocks
        between  C0000-EFFFF.   If you have a VGA or EGA adapter, you may
        get  additional  memory  by  using  the  MOVE=OVERLAY  option  of
        LASTBYTE.SYS.  

             VL82C320 - From the TOPCAT 286/386sx Chip Set
             VL82C330 - From the TOPCAT 386 DX Chip Set

             (The  VL82C320  and  VL82C330 are identical to the 82343 and
             82346 made by Intel Corporation.) 

        The  following  chip  provides  384k of memory in twenty-four 16k
        blocks between A0000-FFFFF.  

             VL82C486 - Single Chip, High Performance 486 PC/AT Controller


        1.3 Unsupported Chipsets        

        If  your computer has shadow ram capability, then it probably has
        a  shadow ram memory controller.  However, some of these chipsets
        cannot  be  supported by The Last Byte Memory Manager for reasons
        shown below.  




        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Aug 11, 1992      SHADOW RAM MEMORY CONTROLLERS                 6


        Some  of  these  chips, however, do have hardware EMS support and
        thus  many  of  their motherboards come with an EMS device driver
        designed  specifically  to take advantage of this capability.  So
        in  many  cases,  you can install this driver first, and then The
        Last  Byte  Memory  Manager can use it to manage the upper memory
        area.  


        1.3.1 No Shadow Ram Support      

        Some   of   the   older   chipsets  do  not  provide  shadow  ram
        capability.  

        Examples: VLSI Technologies 82C100 series
                  Western Digital chipsets
                  Texas Instruments TACT82300 series
                  Early Suntac chipsets (ST62BC001-6)
                  United Microelectronics Corp. UM82C231


        1.3.2 Shadow Ram is not Read/Write     

        Some  chipsets  have  shadow ram, but can only put it into either
        write-only  mode  (for copying rom contents to ram), or read-only
        mode  (to  prevent accidental writes into what's supposed to be a
        copy of rom).  

        Examples: ACC Microelectronics chipsets
                  Headland/G2 Technologies chipsets
                  CONTAQ chipsets


        1.3.3 Overly Complex Control       

        The  Last Byte Memory Manager software is table-driven, making it
        relatively   easy   to   adapt  to  different  memory  controller
        architectures, but there are limits!   

        Examples: Zymos chipsets
                  United Micro. Corp. UM82C384, '388, '389
                  Forex Computer Corp. FRX36C100
                  Silicon Integrated System Corp. (SIS)
                        chipsets


        1.3.4 Locked Configuration Registers       

        Some  memory  controllers  are  designed  so  that  they  can  be
        "locked"  at  the  end  of  software  initialization, requiring a
        hardware  reset  to  unlock,  and  thus  preventing The Last Byte
        Memory Manager from accessing the controller.  



        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Aug 11, 1992      SHADOW RAM MEMORY CONTROLLERS                 7



        Examples: Intel 82335, 82335SX


        1.4 Checking Compatibility Using CHIPSET      

        CHIPSET  is a program that attempts to determine if your computer
        has  one  of the memory controllers required to use The Last Byte
        Memory  Manager.   To  run  CHIPSET, simply enter its name on the
        command line: 

                A>CHIPSET 

        and  follow  the  prompts.   CHIPSET  will  try  to  identify the
        particular  memory controller you have, if any.  If it can't find
        a  memory  controller, it will look for fixed memory in the upper
        area  or  expanded  memory as a means of installing The Last Byte
        Memory  Manager.   If  it  is  successful,  it  will give you the
        option  of  automatically linking to the INSTALL program to setup
        for use of The Last Byte Memory Manager.  

        CHIPSET   automatically  senses  whether  you  have  a  color  or
        monochrome  display  to  determine  how  to  present  data on the
        screen.   However,  you  may  force  the mode by using one of the
        command  line  options:  /MONO,  /COLOR,  or /LCD (for monochrome
        liquid crystal displays).  

        If  your  computer  has  one of the listed devices, then The Last
        Byte Memory Manager should work on your computer.  

























        Copyright (C) 1990-92, Key Software Products. All Rights Reserved