XRAY  by Tom Kihlken
Version 1.5 - February 1990


  XRAY is a DOS programming tool which displays informative messages about 
the operating system (DOS) functions.  With XRAY, you'll be able to snoop 
in on the operating systems inards and diagnose obscure programming bugs.  
The high resolution timer and summary display can also help optimize your 
program's I/O.  It can be used with programs written in any language and 
requires no special compiler.  

  This program is shareware.  Shareware allows you to try the program out 
before you buy it.  You may also make copies for your friends or post it 
on another BBS.  If you like the program and want to continue using it, 
you must register by sending your name, address, $15, and the version 
number shown above to the following address.  You may purchase a copy of 
the assembler language source code for $30.  Your support of shareware 
insures continued development of good low cost software.


Tom Kihlken
3665 McKibbon Road
Saint Louis, Missouri 63114



  XRAY is a memory resident program which provides either a detailed 
report or a summary of exactly which DOS functins (including lots of 
undocumented ones) your program is making.  Whether your use it to snoop, 
or to monitor you system as it crashes, you're bound to see some 
surprises.  Also included is a high resolution timer which helps detect 
I/O bound code which can bog down even your tightest assembler program.
  If your a programmer, use XRAY to check that your program is working 
efficiently (or discover why it's crashing!).  Of course it's just as easy 
to spy on someone elses code to learn how it works.  With XRAY, you'll be 
able to see how data base files are updated and even how some copy 
protection techniques work!
  XRAY works by intercepting interrupt 21h.  Each DOS function call 
outputs a single line of information.  The first two items on the line are 
the function number and a brief description of it (Appendix A shows a 
complete list of the DOS functions).  Next, you will find any important 
input parameters, such as file names, handles, buffer sizes, etc.  
  Next, the actual function is performed, and its elapsed time is shown 
(accurate to 0.00001 seconds!).  If the function caused any physical disk 
activity, the number of sectors read or written is shown.  If the function 
returns information (like a filename, directory, etc.), that is shown 
next.  Finally, either a descriptive error message or "OK" is output to 
indicate the result of the operation.
  A summary table of all the past DOS functions is displayed when XRAY is 
run with the "/T" option.  It shows the number of functions which have 
ocurred, the number of sectors of disk I/O, and the total time they 
required.  This table is written to standard output and may be redirected 
into a file with normal DOS redirection methods.
  The output may at first look complicated, but if you study it along with 
a good DOS programming manual you're guaranteed to learn lots.

  You may run XRAY as many times as you like to change the options.  To 
restore the defaults, just uninstall (/U) XRAY and then reinstall it.  
Here is a complete list of the parameters.

		XRAY  [options] [filename]

Where the options are:

   /C = Send XRAY output to the console (this is the default mode).
        The BIOS write TTY video function is used to display characters.

/Dn-m = Display only DOS function calls numbered betweem n and m (n and m
	are entered in hex).  The default is to display functions numbered 
        0C-FFh (except 2Eh).  By displaying only selected functions you can 
        minimize the amount of output XRAY produces. You may repeat the
        /D (and /I) parameter to select several ranges.

   /F = Send XRAYs output to a disk file (the default is to display the output 
        on the screen).  When /D is specified, all output is internally 
        buffered in a 1K buffer.  The default filename is is C:\XRAY.LOG,
	but a differant name may be specified on the command line.  Be 
	sure to specify the full drive, directory, and name.

   /H = Display the meaning of the optional parameters.

   /J = Causes XRAY to JMP to the original interrupt address rather than
        CALLing it.  This causes the XRAY to be less obtrusive, so give
	it a try if your program doesn't run normally without it.  If you
	use the /J option, you won't be able to see the result code or 
	the elapsed time of the call however.

/In-m = Ignore DOS function calls numbered between n and m (n and m are 
        entered in hex).  The default is to ignore functions numbered 
        0-0Bh and 2Eh.  By ignoring low numbered functions XRAY 
        produces less output and your program will run faster. You may 
        repeat the /I (and /D) parameter to ignore several ranges.

  /Kn = Use Scan code n (n is entered in hex) for the Hot key.  You can 
        press ALT and the hot key to toggle XRAYs output ON and OFF. 
        The default is to not use a hot-key (for maximum keyboard 
        compatiblity).  See appendix B for a table of scan codes.

	Note:  You must use the /K parameter the very first time you 
	install XRAY to make the hot key to work.  This prevents the
        keyboard interrupt vector from being redirected if you don't
	use the hot key option.

   /O = Turns XRAY OFF.  You may turn it back on with either the hot 
        key or by running XRAY again from the command prompt.

  /Pn = Send XRAY output to LPTn.  The default is to display its output 
	on the screen.  The printer is the best real-time output option 
	since it is available up to the time of a system crash.

  /Sn = Use the shift state n (n is entered in hex) combined with the hot key
        to toggle XRAYs output ON and OFF.  The default value is 8 which is
        to press Alt with the hot key.  See appendix C for a table of shift
        state values.

   /T = Display a summary table of all DOS function calls showing the total
	number of each function, sectors of disk I/O, and total elapsed time.

   /U = Uninstall XRAY from memory (if possible).  XRAY can only be 
	uninstalled if no other TSR programs (which use interrupts 9 or
	21h) have been loaded.

   /V = Display function calls made by COMMAND.COM.  The default is to 
        ignore these calls.  If you use the /C option, XRAY will 
        produce lots of output which may not be of interest for your 
        application but it's facinating to see how the command interpreter
        does its thing.  When you use /V, calls from COMMAND.COM are 
	marked with an asterick.



OUTPUT OPTIONS

  XRAY produces two types of output.  Realtime output of each DOS function 
call, and a cumulative table of all the function calls which have been 
made.  The cumulative table is displayed only when the /T parameter is 
given.
  The real-time output from XRAY is sent to either the screen, printer, or 
a disk file.  Which one you choose depends on what you are using XRAY for.  
  The screen is the easiest since it is fast and you can watch it easily.  
Unfortunately, it usually makes a mess of the overlying applications video 
output.  XRAY uses the BIOS write TTY function to drive the display.
  Sending the output to a file is better for large amounts of output.  The 
disadvantage of using a file is that some output is lost in the event of a 
system crash (due to internal buffering).  The size of this buffer is 1K 
(about 20 function calls).  
  The printer is the best output method for observing a system crash since 
all of the output is displayed, right up until the machine locks up.  
Printing will slow down your program however and in some cases may cause 
time critical programs to timeout.  XRAY uses the BIOS print character 
function (INT 17h) to drive the printer.



ELAPSED TIME MEASUREMENT

  XRAY uses the 8253 timer/counter to measure elapsed time of DOS function 
calls.  This counter is calibrated as part of the installation process 
such that it measures only the actual time executing DOS code.  It is 
accurate to within approximately 10 microseconds (times are displayed to 
the nearest .01 millisecond).  The largest time which can be displayed is 
about 450 seconds.  This shouldn't be a problem since most functions are 
completed in less than a second.
  To record the elapsed time, the 8253 (timer 0) is reprogrammed to mode 2 
(divide by n) on every DOS call.  This doesn't affect the clock tick rate, 
however it can cause a few extra ticks which make the system clock seem to 
run a bit fast.  If you're concerned about restoring the time after 
running XRAY, you should reboot the machine.



SELECTING FUNCTIONS

  Most programs make lots of calls to the operating system.  When this 
happens, XRAY produces lots of output if you don't suppress some of it. An 
example of this is when a program continuously reads the clock in order to 
display the time on screen.  It is easy to filter out this uninteresting 
stuff with XRAY, using the /D (Display)) and /I (Ignore) options.
  The default setting for the filter is to ignore functions numbered lower 
than 0Ch and function 2Eh.  To ignore additional functions, just use the 
/In-m option.  To add functions to the filter, use /Dn-m.  You can specify 
as many ranges as you like.  You can also specify a single function number 
such as /I2C.  
  As each range is parsed from the command tail, it takes precedence over 
previous ranges, so the order in which you specify them controls how they 
are combined.  Remember, you always start with the default filter (or the 
existing filter if XRAY has already been installed).
  Let's look at an example.  Say we're interested in the functions 3Ch to 
40h, 16h to 17h, and 4C.  The correct parameters would be:

       /I0-FF /D16-17 /D3C-40 /D4C

  Notice the first "/I" turned off everything, the next three "/D's" turn 
on the ranges we want.  When selecting ranges, it's best to avoid the 
console I/O functions (01h through 0Bh) since there are millions of them 
in most programs.



I/O SECTOR COUNT

  DOS generally buffers most I/O operations in such a way that a write 
request may not be passed to the disk until a full sector of data is ready 
to be written.  Disk buffering and caching also affect the physical 
transfer of data to the disk.
  XRAY lets you observe this buffering by displaying the actual amount of 
I/O in terms of number of physical sectors.  If you compare the sector 
count with the elapsed time, you'll be able to determine the effective 
access time of the disk in real life situations (something benchmarks 
can't really do).  Be prepared for surprises here!  Remember, some I/O 
commands will hit the cache (you should be using one by now) and complete 
very quickly.
  The sector count is obtained by intercepting the BIOS diskette interrupt 
(INT 13h) and saving the number of sectors.  Disks which have their own 
device driver (RAMDISKs, etc.) won't show up in the sector count if they
don't use interrupt 13h.



USING A HOT KEY

  Normally XRAY does its job continously after installed.  You can switch 
XRAY off by running it again with the /O option.  An easier method is to 
specify a hot key which will toggle XRAY off and on.
  To enable use of a hot key, you MUST specify a scan code (with the /K 
parameter) during the initial installation.  The default scan code is 0FFh 
which indicates that the keyboard interrupt vector is not to be 
intercepted and the hot key is disabled.  You can change the scan code 
later if you want but you MUST enable it the FIRST time XRAY is installed.
  Scan codes are selected from appendix B.  You must hold down the Alt key 
together with the selected hot key.  If you want a shift key other than 
ALT, specify a shift mask with the /S option.  Valid shift codes are shown 
in appendix C.



A NOTE ABOUT COMPATIBILITY

  XRAY was written to be as compatible as possible with most programs.  
Like all TSR's however, there will always be some programs which may not 
run correctly with it installed.  If you seem to have trouble, there are a 
couple things you can try.  
  First of all, remove any other TSR programs you are using (or load them 
in a different order).  Second, If the hot key interfers with your 
application, try a different scan code or reinstall XRAY with the hot key 
disabled (by not specifying a scan code).  
  Third, try the /J option.  This causes XRAY to JMP to the original 
interrupt 21 address rather than CALLing it, makint it less obtrusive.  
When you do this however, you won't be able to see the result code or the 
elapsed time of the call however.



DIGGING DEEPER

  After spending a little time with XRAY, you're bound to see things 
you've never heard of or don't understand.  I can't possibly explain 
everything about DOS, so I'll recommend a couple good books on the 
subject.

   Duncan, Ray. Advanced MS-DOS.  Redmond, Redmond, Wash.: Microsoft 
	Corporation, 1986.

   Lafore, Robert. Assembly Language Primer for the IBM PC&XT.
	New York: Plume/Waite, 1984.

   Scanlon, Leo J. IBM PC Assembly Language: A Guide for Programmers.
	Bovie, Md.: Robert J. Brady Co. 1983.


CHANGES FOR VERSION 1.5

1. Added several more undocumented DOS calls.  


CHANGES FOR VERSION 1.4

1. Added /T parameter to display summary table.
2. The time display routine was extended to display times up to 450 
   seconds.


CHANGES FOR VERSION 1.3

1. The default for the filter table was modified to ignore function 2Eh.
2. Extended error codes were added to the error table.
3. More parameters are shown with each functions.
4. Elapsed time is shown to the nearest .01ms (for times less than 2ms).
5. Number of disk sectors read/written is shown.
6. The "/T" option was deleted (time measurement is the default now).
7. You may specify a filename for the log file on the command line.



Appendix A
DOS FUNCTION CALLS

  Following is a list of the DOS function calls.  For more information, 
see the DOS technical reference manual.

	00h - TERMINATE PROCEDURE
	01h - READ KEYBOARD WITH ECHO
	02h - DISPLAY CHARACTER
	03h - AUXILARY INPUT
	04h - AUXILARY OUTPUT
	05h - PRINT CHARACTER
	06h - DIRECT CONSOLE I/O
	07h - DIRECT CONSOLE INPUT
	08h - READ KEYBOARD
	09h - DISPLAY STRING
	0Ah - BUFFERED KEYBOARD INPUT
	0Bh - CHECK KEYBOARD STATUS
	0Ch - FLUSH KEYBOARD BUFFER
	0Dh - DISK RESET
	0Eh - SELECT DEFAULT DISK
	0Fh - OPEN FILE (FCB)
	10h - CLOSE FILE (FCB)
	11h - SEARCH FOR FIRST FILE (FCB)
	12h - SEARCH FOR NEXT FILE (FCB)
	13h - DELETE FILE (FCB)
	14h - SEQUENTIAL READ (FCB)
	15h - SEQUENTIAL WRITE (FCB)
	16h - CREATE FILE (FCB)
	17h - RENAME FILE (FCB)
	19h - GET CURRENT DISK
	1Ah - SET DISK TRANSFER ADDRESS
	1Bh - GET ALLOCATION TABLE INFO FOR DEFAULT DRIVE
	1Ch - GET ALLOCATION TABLE INFO FOR SPECIFIED DRIVE
	21h - RANDOM READ (FCB)
	22h - RANDOM WRITE (FCB)
	23h - FILE SIZE (FCB)
	24h - SET RELATIVE RECORD (FCB)
	25h - SET VECTOR
	26h - CREATE NEW PROGRAM SEGMENT
	27h - RANDOM BLOCK READ (FCB)
	28h - RANDOM BLOCK WRITE (FCB)
	29h - PARSE FILENAME (FCB)
	2Ah - GET DATE
	2Bh - SET DATE
	2Ch - GET TIME
	2Dh - SET TIME
	2Eh - SET/RESET VERIFY FLAG
	2Fh - GET DATA TRANSFER AREA
	30h - GET DOS VERSION NUMBER
	31h - KEEP PROCESS
	33h - CONTRL BREAK CHECK
	34h - GET BUSY FLAG
	35h - GET VECTOR
	36h - GET DISK FREE SPACE
	38h - GET/SET COUNTRY INFORMATION
	39h - MAKE DIRECTORY
	3Ah - REMOVE DIRECTORY
	3Bh - CHANGE DIRECTORY
	3Ch - CREATE FILE
	3Dh - OPEN FILE HANDLE
	3Eh - CLOSE FILE HANDLE
	3Fh - READ FROM FILE/DEVICE
	40h - WRITE TO A FILE/DEVICE
	41h - DELETE FILE
	42h - MOVE POINTER
	43h - CHANGE FILE ATTRIBUTE
	44h - I/O CONTROL FOR DEVICES
	45h - DUPLICATE FILE HANDLE
	46h - FORCE DUPLICATE FILE HANDLE
	47h - GET CURRENT DIRECTORY
	48h - ALLOCATE MEMORY
	49h - FREE MEMORY
	4Ah - MODIFY MEMORY BLOCK
	4Bh - EXECUTE A PROGRAM
	4Ch - TERMINATE PROGRAM
	4Dh - RETRIEVE THE RETURN CODE OF A CHILD
	4Eh - FIND FIRST MATCHING FILE
	4Fh - FIND NEXT MATCHING FILE
	50h - SET PROGRAM SEGMENT PREFIX
	51h - GET PROGRAM SEGMENT PREFIX
	54h - GET VERIFY SETTING
	56h - RENAME A FILE
	57h - GET/SET FILE DATE
	59h - GET EXTENDED ERROR
	5Ah - CREATE UNIQUE FILE
	5Bh - CREATE NEW FILE
	5Ch - LOCK/UNLOCK FILE ACCESS
	5Eh - PRINTER SETUP
	5Fh - DEVICE REDIRECTION FUNCTIONS
	60h - GET TRUE NAME OF A FILE
	61h - SET PROGRAM SEGMENT PREFIX
	62h - GET PROGRAM SEGMENT PREFIX

	

Appendix B
KEYBOARD SCAN CODES

  The following is a partial list of values which can used with the /K 
option to specify a hot key scan code.  The keys which are described as 
"KP" are on the numeric keypad on the right side of the keyboard.  Other 
codes can be found in any good technical reference.
  The default condition is for the hot key to be disabled.

Code   Key             Code   Key              Code     Key

 1Eh     A              01h   Esc              3Bh       F1
 30h     B              02h     1              3Ch       F2
 2Eh     C              03h     2              3Dh       F3
 20h     D              04h     3              3Eh       F4
 12h     E              05h     4              3Fh       F5
 21h     F              06h     5              40h       F6
 22h     G              07h     6              41h       F7
 23h     H              08h     7              42h       F8
 17h     I              09h     8              43h       F9
 24h     J              0Ah     9              44h      F10
 25h     K              0Bh     0              57h      F11
 26h     L              0Ch     -              58h      F12
 32h     M              0Dh     =              47h      KP7
 31h     N              0Eh    BS              48h      KP8
 18h     O              0Fh   TAB              49h      KP9
 19h     P              1Ah     [              4Ah      KP-
 10h     Q              1Bh     ]              4Bh      KP4
 13h     R              1Ch    CR              4Ch      KP5
 1Fh     S              2Ah   L-SHIFT          4Dh      KP6
 14h     T              39h     SPACE          4Eh      KP+
 16h     U              36h   R-SHIFT          4Fh      KP1
 2Fh     V              33h     ,              50h      KP2
 11h     W              34h     .              51h      KP3
 2Dh     X              35h     /              52h      KP0   
 15h     Y                                     53h      DEL 
 2Ch     Z
 


Appendix C
KEYBOARD SHIFT STATE MASK CODES

  The following is a list of values which can used with the /S option to 
specify a hot key shift state code.  The default value for this option is 
8 (Alt key held down).  You may numerically add values to create multiple 
shift conditions.  For example, "/S09" would be used to specify both the 
Right shift and Alt key held down when the hot key is pressed.  Only the 
four lower bits of the shift mask are used.


   Value          Shift State

     0          No shift key needed
     1          Right shift held down
     2          Left shift held down
     4          Ctrl key held down
     8          Alt key held down



Appendix D
IOCTL FUNCTIONS

  IOCTL (IO control for devices) functions are involked by using DOS 
function 44h.  The following subfunctions are defined.

	0 - Get Device information
	1 - Set device information
	2 - Read character device
	3 - Write character device
	4 - Read block device
	5 - Write block device
	6 - Get input status
	7 - Get output status
	8 - Is device changeable?
	9 - Is device local or remote?
	A - Is handle local or remote?
	B - Change retry count
	C - Reserved
	D - Generic IOCTRL request
	E - Get logical drive
	F - Set logical drive