Howdy...
This is super quick documentation to explain exactly why TRICK.EXE
was created, and what it does....

* I needed a way to run doors with the Wildcat IM version.
  Since the IM version comes with Doorway, I could run any non bit-
  mapped program as a door, but the question was, how could I get the
  door to look for the door.sys file AND not send the output through
  the serial port... Well, after some serious thought, I figured out
  a way to make it work....
  When you log on your board local, and go into a door, the Door.sys
  file says you are on com0 and at 38400 baud.... so it gets your info
  from the Door.sys file, but doesn't try to send it out any com ports..
  BINGO... problem solved... TRICK.EXE simply changes the door.sys file
  to "local" so the door runs local, but gets the callers info from the
  door.sys file as it normally would, and then Doorway sends it out
  the digiport...

* Here are some goodies to know...
  Run TRICK.EXE in the same directory as the door.sys file.
  Only type TRICK, and if the door.sys file is there, it will be 
  converted... if not, it will give an error, but no harm done.

* Sample batch file:
  This is the batch file used on 99% of my doors....

  DOOR1.RUN
  
 COPY DOOR.SYS C:\WC30\DOORS\DOORGAME
 CD\WC30\DOORS\DOORGAME
 TRICK
 WCDRWY SYS /S:C:\WC30\WCWORK\NODE%WCNODEID%\  (cont)----
                          /B:X /K:V /V:D /P:DOOR.EXE GAME.CFG


  That's it!  If your doors are already set up to run with a serial port,
  (as mine were when I switched to the IM version) then all you need
  to add is the Doorway line to your Doorx.run files (and trick too!)

  Note that the command line tells Doorway to look for the UNMODIFIED
  Door.Sys in the /NODEx directory, but you MUST tell the door to use
  the Door.Sys located in it's own directory.  But this will only
  work if you have the SET WCNODEID=x in your CATx.BAT file...

  Here is my Cat1.bat file:
  c:
  dvansi <==== make sure DVANSI.COM is in your path
  :relog
  cd\wc30
  set wcnodeid=1
  set wcportid=1
  set wchome=c:\wc30
  set wcmdm=node1
  Wildcat
  if errorlevel 1 goto reload
  id errorlevel 0 got end
  :end

  What have I noticed to be a problem with this way of running doors?
  Well, some people that have monochrome monitors or non-ansi terminal
  emulation, may not get the display as it should be in there...
  Doorway is peculiar.... and unless you are using a NEW type of ANSI,
  it may not be too neat... but if you have a good computer, with a color 
  monitor, and are using QMODEM or something quality like that, you
  will have no problem...
  What else?
  If someone drops carrier in a door, Doorway will cut the program off
  without exiting nicely, and this mmay mess up some doors... but none
  of mine have had a problem other than TELEHANG, which would sometimes
  lock a particular game, so I had a little utility made that would erase
  the word LOCK from the particular cfg file each time the door is run..


   One more thing.... there is a new (newer than Mustang has released)
   copy of WCDRWY.EXE ... it has improved screen writes.... if you want
   it, call up Marshall Dudley's board and get it from him.... it
   is not the bug fix Doorway, that Mustang released, it is NEW!!
                                       Bye!

  TRICK.EXE was written in Turbo Pascal v6 so it's speedy, and compact.

  Have fun.... Long live Public Domain!