WHICH NODE 1.0 - Copyright (c) 1992 By: Roel Sarceno
	          of Video ViSion BBS (916) 682-1655


  The reason why I wrote WHICH NODE (WNODE.EXE) is to determine which node
  called the batch file.  Most of the shareware door program, you have to
  specify /B for lock baud rate in the command line.  This could be a big
  problem if node1 has LOCK DTE of 19200, node2 has LOCK DTE of 2400 and
  node3 is not configured for LOCK DTE using one batch file.

  WNODE.EXE, will determine (as fast as possible) which is the current
  node number by reading DOOR.SYS or the environment setting. The syntax
  for WHICH NODE is  WNODE {E:(environment) | F:(filename)}

  Eg: Using DOOR.SYS (DOOR.BAT)  | Eg: Using Environment (DOOR1.BAT)
                                 |
  @echo off	                 | @echo off
  wnode F:DOOR.SYS               | wnode E:WCNODEID
  if errorlevel 3 goto node3     | if errorlevel 3 goto node3
  if errorlevel 2 goto node2     | if errorlevel 2 goto node2
  if errorlevel 1 goto node1     | if errorlevel 1 goto node1
  Echo "Error read file"         | Echo "Environment not set"
  goto exitnode                  | goto exitnode
  			         |
  :node3                         | :node3
  program.exe                    | program.exe
  goto exitnode                  | goto exitnode
  			         |
  :node2                         | :node2
  program.exe /B2400             | program.exe /B2400
  goto exitnode                  | goto exitnode
  			         |
  :node1                         | :node1
  program.exe /19200             | program.exe /19200
  goto exitnode                  | goto exitnode
  :exitnode                      | :exitnode


  WHICH NODE 1.0 SUPPORTED FILES
  ------------------------------
  CALLINFO.DAT
  DOOR.SYS



  DISCLAIMER - I do not warrant that the functions of the software will
  meet your specific requirements or WHICH NODE operation will be error-free
  or uninterrupted.  I have endeavored to minimize defects and errors on
  WHICH NODE.  However, You (the user) assume the risk of any damage or loss
  from it's use.

   If you experience any problems or for latest update on WHICH NODE call:

                             Video ViSion BBS
                            THE GRAPHIC LIBRARY
                          (916) 682-1655 / 24 Hrs
                          300-1200-2400-9600-19200

==============================================================================