AA4RE BBS now supports the HAL-4000 CLOVER card.  A typical port
would look like:

    port

        port_type               = HAL4000-CLOVER
        addr                    = $360
        max_connect             = 1
        max_channel             = 2
        call_set                = AA4RE
        no_busy_fwd             = yes
        max_pac                 = 230
        speed                   = 9600
        max_pending             = 1
        monitor                 = yes
        time_out                = 180
        fwd_min                 = 0
        minimum_class_allowed   = new_user
        remote_sysop            = Y
        upload_download         = Y
        broadcast               = n
        port_name               = Clover
        monitor_color           = 121
        disconnect_delay        = 10
        default_forward_order   = TA
        new_user_display_format = 0
        remove_ssid_addresses   = y

    endport

The following commands are available..

-- These commands take a parameter of a callsign

   C  xxxxx  -- Connect normal to xxxxx
   CN xxxxx  -- Same as C
   CR xxxxx  -- Connect robust to xxxxx
   I xxxxx   -- Set callsign

-- No parameters allowed on these commands

   D         -- Disconnect
   CQ        -- Start ARQ CQ
   FEC       -- Begin FEC mode
   ANSWER    -- Answer ARQ CQ
   ID        -- Send CW ID

-- Query Commands (no parameters)

   Q CSDN    -- Query channel spectral data (narrow)
   Q CSDW    -- Query channel spectral data (wide)
   Q CSTAT   -- Query channel statistics
   Q LS      -- Query link state
   Q VSB     -- Query voice subband
   Q WAVE    -- Query clover waveform
   Q DSPV    -- Query DSP software version
   Q CSWV    -- Query controller software version
   Q EPROMV  -- Query EPROM version
   Q EPROMC  -- Query EPROM checksum

-- Monitor -- special parameters

   M N       -- Monitor off
   M xxxx    -- Monitor on.   xxxx can be one or more letters from list below:
                   L -- Link status
                   S -- Channel status
                   I -- Data from other QSOs but only when not connected

-- Waveform setting -- special parameters

   WAVE CWID     -- These set the waveform
   WAVE 2DFSM
   WAVE 4DFSM
   WAVE FSM
   WAVE 2DPSM
   WAVE BPSM
   WAVE QPSM
   WAVE 8PSM
   WAVE 8P2A
   WAVE 16PSM
   WAVE 16P4A

   WAVE SIZE nn  -- Set the blocksize to 17, 51, 85, or 255

   WAVE FEC  nn  -- Set the error correction to 60, 75, 90, or 100 %


-- These commands set a numeric parameter

   P n       -- Set chat threshold
   RLRM n    -- Set robust link retry maximum
   NLRM n    -- Set normal link retry maximum
   CCBRM n   -- Set CCB retry maximum
   VSB  n    -- Set Voice subband
   BIAS n    -- Set bias
   SCAN n    -- Set scan mode

-- These are on/off commands.  b = 1 or Y or YES or ON
                               b = 0 or N or NO or OFF

   Y b       -- Allow connect
   RCS b     -- Report channel stats
   ARPA b    -- Automatic Remote Power Adjust
   ACWF b    -- Adaptive Clover Waveform
   CWID b    -- CW ID every ten minutes
   LISTEN b  -- Enable monitor of FEC
   EMS b     -- Enable Monitor Status
   TEST b    -- Start/stop Clover test


*** Note to testers.  CLOVER support is still very very new.  This doc
only outlines the base set so I can get it out to you testers.  More
will come later.

*** The PCC.S28 and PCC.LOD files must be in the C:\PCC subdirectory!!!!!!