FAX DISPLAY
                               for the                            
                        KANTRONICS KAM and KPC3

          Copyright (c) 1993, 1994 by Richard R. Hensel N8WLC
                         All Rights Reserved
 




   This program is distributed as SHAREWARE and the author retains 
   all copyrights.  You are encouraged to give copies to all of your
   friends and upload this program to any BBS as long as this document
   is included.  If you like the program, please support further 
   development by sending $5.00 to 

   Richard Hensel N8WLC
   715 Joselyn Avenue
   Lexington, Ohio USA 44904
   
   
   
   



   This program will interface with the fax capabilities built into
   the KAM and KPC3 TNC's from Kantronics Inc.  The command are as 
   follows:
   
Keys        use
1-0         set line skipping ie 1 = 1 to 1   2 = 2 to 1
F1-F10      picture skew left,  skip (1 - 10) pixels to align fax on screen
AF1-AF10    picture skew right, skip (1 - 10) pixels to align fax on screen
ALT X       exit
ESC         Start fax recieve and leave terminal mode 
i           invert picture ie black on white to white on black
t           return to terminal mode.  Stops fax receive
c           clear screen
s           save incoming fax to FAX.FIL 
r           copy the saved fax to annother file name
p           playback 
   
   1-0         These set the aspect ratio of the displayed fax picture.
               0 displays all lines of the incomming fax, and 9 displays
               every 9th line.  I have found the most natural aspect is
               found using 1.

   F1-F10     The fax must be centered on the monitor screen.  If you   
   AF1-AF10   need to move the picture left use the F1 - F10 keys.  If 
              instead it would be better to move right use Alt F1 to 
              Alt F10.  These keys shift the picture 1 to 10 pixels
              in the intended direction.
   
   ALT X      Exits the program and re sets the TNC.
   
   ESC        The Escape key causes the program to leave terminal
              mode and start recieving a fax.

   i          Invert the picture, that is change from white dots on a 
              black background to balck dots on a white background.
              I have found that the best pictures come from using 
              upper side band and when revieving a satalite foto, 
              inverting the picture.
   
   t          Return to terminal mode from fax recieve.  This will 
              put you into a simple terminal emulation connected
              to the TNC.

   c          Clear the screen, this will clear the screen of the
              picture while in FAX recieve mode.
   
   s          Save the incoming fax.  This will start saving the 
              fax to a file called FAX.FIL for later playback.
   
   r          Will copy the FAX.FIL to another file so multiple 
              images can be saved.
   
   p          Playback will cause the program to play FAX.FIL back 
              to the screen.
  
  
  
  
  Coments and sugestions are wellcome.  I can be reached at the address
  at the beginning of this doc file or on packet at 
  N8WLC @ W8WE.OH.USA.NA
  
  
  Hardware Requirements
  
  1      IBM PC/AT 80286 or equivelant with 640 Kbytes of menory.

  2      Microsoft or IBM PC DOS 3.1 or higher.

  3      EGA or VGA adapter card and monitor

  
  Comming Attractions:
  
  1     Printing the fax to you dot matrix printer.
  
  2     Enhancements you request.
  
  
  Bugs
  
  1     Due to the COM port interface routines I am currently using
        the program will not run if your computer has a 16550 uart
        with the buffering turned on.  So i have provided a short
        program "16550.exe" that will turn the buffering off.
        just issue the command "16550 x off" where x is the COM port
        1 or 2 that you are using.