1




                               TstHost version 1.39
                               --------------------
       Features
       --------
       TSTHOST   is  a software  written for  TNC2 and  clones with   HOST
       mode  EPROM type  TF8, TF23,  TF24 etc.  It is possible  to use the
       software with other TNCs set in KISS mode.

       A  TNC in  KISS mode  requires a  serial driver (like TFPCX/TFPCR),
       but  don't forget  to set  the TNC  in  KISS  mode  BEFORE  running
       TSTHost.

       A  TNC in  WA8DED Host  mode  requires  a  serial    driver    like
       COMBIOS,  MBBIOS etc.  The  GKJBIOS    driver    is    an    MBBIOS
       compatible   driver  optimised for   TSTHost,  that   detects   the
       special   16550A  UART.   For  the    driver    configuration,  run
       GKBIOCFG.EXE and follow the instructions displayed on the screen.

       As  far as  TSTHOST is  written for  8 channels,   you  cannot  use
       the  software with  the original  WA8DED  or  TF4  EPROMs,  because
       these  EPROMs have  only four  channels. It is possible the use the
       software  with   EPROMs that  support more   of  8   channels,  but
       only  8  are available.

       TSTHOST  offers 8  independent  communication    channels,    where
       every  channel has  a 300 lines receive buffer,  circular  keyboard
       buffer  to recall  the  ten  previous  commands,  automatic    text
       justification,  up   to    8  simultaneous  YAPP (with  resume  and
       yappC  options) or  ASCII file  transfers,   up to   8 PMS channels
       with  RLI-type forward  with  a master  BBS. All  received data can
       be   saved   in   a   disk file. Every session may have a different
       callsign.

       There   is   a  separated window for monitoring, and it is possible
       to capture in a file all the traffic displayed in that window.

       The  text entered  from the  keyboard is  recognised as commands to
       run  for every  COMMAND mode session, while in CONVERSATION mode is
       sent  to   the   connected   station.   For this  reason it  is not
       possible  to switch  in conversation  mode if  the session  is  not
       connected.  The exception     is   the  Monitor  window,  where all
       keyboard data  is transmitted as Unproto packets.

       For   every  session   there is  a receive buffer, useful to review
       all  the received  data. By  receiving data  from   a  channel  not
       actually  selected, the  related callsign  in the  status line will
       blink.   All  unconnected  channels  are  set  by  default  to  PMS





       TSTHOST v1.39 (c) IK1GKJ                                     2


       sessions.  So, when  an user  connects your  station, he  goes into
       the   personal  mailbox system,  but if  YOU  connect  a  user  the
       channel  is set   for  a normal  conversation mode.  Naturally, you
       have  a specific command to switch  a PMS session into conversation
       mode  and vice-versa.  During a  PMS session, the user can read and
       write  messages, view  the users directory, up or download programs
       with  the YAPP  protocol. The   PMS  session can  also run external
       server   programs,   send   a   Break  to other PMS users, talk the
       sysop.

       TSTHost   automatically  recognises the  standard password  format,
       and  the   extended MD2   algorithm.  The  standard password format
       accepts  from   one to   ten  letters,    but  normally    all  the
       programs require five letters for the password.

       Other features are the Unproto list capability and a full forward
       protocol  MBL-RLI or  FBB COMPRESSED  type, even  if  the  the  BBS
       require a password for the access.

       The  program can  also extract  any 7plus  code from the unproto or
       pms   messages,  and   write  this  code  to  a  file,  for  furter
       processing.  TstHost support remote SERVER technique and PG program
       to increase the pms command for particoular applications.

       The  communication in   HOST-mode   between  the PC and the TNC has
       a  3 seconds  timeout. After  this time,  if the  program does  not
       receive  a reply  from the  TNC, attempts to synchronise the serial
       port.


























       TSTHOST v1.39 (c) IK1GKJ                                     3


       Tsthost with TNC in KISS or BAYCOM modem
       ----------------------------------------
       You   need  the driver  TFPCR or  TFKISS for  KISS mode,  TFPCX for
       modem  BAYCOM.   TFPCX version 2.10 supports both the KISS and  the
       BAYCOM modes.

       Using  a KISS-mode   TNC,  set the  TNC in  KISS mode  manually  or
       with   the     appropriate  command     line    switch    of    the
       TFPCR/TFPCX/TFKISS driver.

       TFPCX  uses the  IRQ 253  for the  internal  communications,    the
       other drivers uses the IRQ 254.

       Load the driver
       Load TSTHost with the command:  TSTHOST /T /I254 (or /I253)

       /T  sets TSTHost   to   use   the  TFPCX/R  driver, and  /I254 sets
       the IRQ for the driver communication.

       NOTE:  when started,  TSTHost automatically  sends the  commands to
       the driver:  JHOST1, USERS 8, @U0

       Example for TFPCR or TFKISS:
       TFKISS command line parameters
       TSTHOST /T /I254

       Example for TFPCX:
       TFPCX command line parameters
       TSTHOST /T /I253

       WARNING:   I  have noticed   that  TFPCR   version 3.30   does  not
       work  properly with  high speed transfers over 400  cps (G3RUH 9600
       baud).  I don't  know the  reason, but  version 2.10  of TFKISS and
       TFPCX  does not have this bug.




















       TSTHOST v1.39 (c) IK1GKJ                                     4


       Tsthost with the standard HOST mode
       -----------------------------------
       Configure  GKJBIOS or  other  COMBIOS  drivers  for  the    correct
       serial port parameters. Load the driver in memory

       Load TSTHost with the command TSTHOST /H /Cx /Bzzzz
       where   /H  selects the  software to use the  standard host mode, x
       is  the   serial port   where  you   have connected the TNC (1..4),
       zzzz  is the  baud rate  of  the  port.  TSTHost  supports  a  data
       transfer rate of 9600, 19200 and 38400 baud.

       NOTE:  when started,  TSTHost automatically  sends the  commands to
       the TNC:  JHOST1, USERS 8, Z0, @U0

       At  the end   of  the   program, you  must remove  from memory  the
       serial driver with the command:  GKJBIOS U

       For instance:
       GKJBIOS
       TSTHOST /H /C1 /B19200
       GKJBIOS U

































       TSTHOST v1.39 (c) IK1GKJ                                     5


       Tsthost with 2 or more tnc
       --------------------------
       You   may  connect   two or   more  interfaces to the program. This
       can  be done with the TFPCX v2.10 driver. This  driver supports  up
       to  8 interfaces   like  KISS,  BAYCOM,  MODEM  etc. This is only a
       small  description,  because  the  complete  documentation  of  the
       commands  is shipped with the driver files.

       Since   the  driver   may support  up to  8 port,  the driver  have
       a  command to  define which  channels assign  to  which  port.  The
       extended  host command is @PO xxxxxxxx. Each 'x' is a value between
       0  and the  number   of   installed   interfaces.   0 is  the first
       interface,  1 the  second, etc. TSTHost uses 8 channels so you must
       define 8 digits.

       Of  course,   if you   use  the   driver for   one  interface only,
       the  @PO  command  is  not  requested,  because  all  channels  are
       assigned  to that interface.

       Here are some examples:

       1)   We  have two  TNCs,   connected to  COM1 and  COM2.  The  TNCs
       are  already   set in  KISS mode,  the baud  rate is 19200 baud, we
       want  to assign   channels  1234  to the TNC on COM1, channels 5678
       to the TNC on COM2.

       TFPCX -PKISS1 -PKISS2 -B19200:19200 -CH8
       TSTHOST /T /I253
       To assign the channels type the command:   PARAM 0 @PO 00001111
       (This command can also be written in the tsthost.cfg file)

       2)   We  have 2  TNC and  a  BAYCOM  modem.  The  BAYCOM  modem  is
       connected  to COM1, 1200 baud; a TNC is on COM2 at 19200 bauds, the
       second  TNC is   on  COM3,   IRQ10, 38400  baud. The  two TNCs  are
       already  set in  KISS mode.  We to  want assign channels 123 to the
       BAYCOM, 456 to the first TNC, and 78 to the second TNC.

       TFPCX -PCOM1 -PKISS2 -PKISS3:03E8:10 -B1200:19200:9600 -CH8
       TSTHOST /T /I253
       To assign the channels, type the command PARAM 0 @PO 00011122
       (This command can be executed from the tsthost.cfg file)

       3)   A  TNC in  KISS mode,  already set  in   KISS mode,  on  COM1,
       19200 baud.

       TFPCX -PKISS1 -B19200 -CH8
       TSTHOST /T /I253
       In this case the command @PO is not requested.






       TSTHOST v1.39 (c) IK1GKJ                                     6


       Memory usage
       ------------
       TstHost  use the  memory dinamically.  This means  that the  memory
       will  be request  to the  system when needed, and released when not
       more  requested. But,  some type  of data, like revision buffer and
       channel structure, cannot be released.

       Actually  tsthost need about 500 Kbyte of memory to run, this for a
       standard  use, and  all pc that have installed almost 640 kbyte may
       run tsthost. But others memory usage may be needed:

       1) TFPCX-TFPCR, if used, need about 64K
       2) Unproto list, (little mode), require 24K
       3)  RUN command,  and generally  any  other  application  like  the
       SERVER  that require  a shell  to operating system, need memory for
       command.com and the program to execute.
       4)  Compressed data  received with  forward and uproto list require
       other 19K.



       Expanded memory and /NOEMS command
       ----------------------------------
       TstHost  detect and  use EMS  memory if  found in  the sistem.  EMS
       memory may free up to 240Kbyte of conventional memory.

       If  you   have any  problem using  the  expanded  memory,  you  can
       disable  the function  with the  command line  switch  /NOEMS.  For
       example:

             TSTHOST /H /B19200 /C1 /NOEMS


       Reduction of RX buffers, /Rsize command
       ---------------------------------------
       If  you do  not have memory for all your applications, you may free
       memory  reducing the  size of  the rx  buffer. Normally  any buffer
       have  a capacity  of 300  lines. The  /Rsize permit  to define  the
       number  of line  allocated in  the review  buffer, from 100 to 300.
       Any line cost 82 bytes.

       For example, with TSTHOST .... /R200, you may free:
       (300-200)x82x9=73800 byte, 73K

       This  command do  not affect  buffer allocated  in EMS memory, that
       have always 300 line.








       TSTHOST v1.39 (c) IK1GKJ                                     7


       VGA mode
       --------
       Add  the parameter  /VGA to  the command  line, to  get  43  or  50
       screen lines on an EGA or VGA monitor.

       Example: TSTHOST /H /B19200 /C3 /VGA




       Short cut keys
       --------------
       ALT F1             Automatic transmission of the password.
       ALT F2             Displays the MHEARD list
                          (depending on the driver/TNC software)
       ALT F3             Enables the monitor traffic to IUSC
       ALT F4             Disables the monitor traffic
       ALT F5             Set monitor traffic to U
       ALT F6             Like the command ULIST VIEW
       ALT F10            Turn off the new mail indicator.
       CONTROL ESC or F10 Switches command<>conversation mode.
       PAGE UP            Activates review buffer, or if already active
                          displays the previous page.
       PAGE DOWN          Displays next page in review buffer
       SHIFT UP           One line up in review mode
       SHIFT DOWN         One line down in review mode
       CONTROL PAGE DOWN  Quit from review mode
       CONTROL HOME       Top of review buffer
       CONTROL END        Bottom of review buffer
       ENTER              In command mode: executes the command.
                          In conversation mode: transmits the text.
                          In both mode, if the revision buffer is active,
                          it will be disabled.
       CURSOR UP          Recalls the previous line from kbd buffer.
       CURSOR DOWN        Recalls the next line from the kbd buffer.
       F1...F8            Switches to session 1 to 8
       F9                 Switches to the Monitor window
       CTRL-F1..F10       User defined.
       SHIFT-F1..F10      User defined.
       CTRL_BACKSPACE     Clears from cursor to the previous word.
       CTRL_LEFT          Moves the cursor one word to the left
       CTRL_RIGHT         Moves the cursor one word to the right
       HOME               Moves the cursor at the beginning of the line
       END                Moves the cursor at the end of the line
       BACKSPACE          Deletes char to the left of the cursor
       DELETE             Deletes char under the cursor
       INSERT             Inserts mode toggle
       ESCAPE             Clears the current line
       CTRL-Y             Deletes the current line (internal ).





       TSTHOST v1.39 (c) IK1GKJ                                     8


       Path of the files
       -----------------
       There  isn't a  particular directory  for the TstHost installation,
       but  you MUST  create, within  that directory, three subdirectories
       with the names: MAIL, PG, USERS.

       This can be a standard installation:

       \TSTHOST         <DIR>
         |-PG           <DIR>
         |-MAIL         <DIR>
         |-USERS        <DIR>
            |-UPLOAD    <DIR>
         |-TSTHOST.EXE
         |-TSTHOST.DOC
         |-TSTHOST.PSW  File for automatic password
         |-TSTHOST.CFG  Configuration file for the program
         |-TSTHOST.ENT  Input text when connect the pms
         |-TSTHOST.HLP  Help file for pms
         |-TSTHOST.SYS  Password file for remote pms access.
         |-TSTHOST.PGS  List/description of the available PG server
         |-TSTHOST.ULS  Unproto list file, created/used by TSTHOST
         |-TSTHOST.SHD  Tnc configuration file when shutdown program
         |-TSTHOST.IN   Mail import file
         |-TSTHOST.LOG  created from TSTHOST if LOG=ON
         |-TSTHOST.BID  Bid file, managed by TSTHOST
         |-TSTHOST.DMS  PMS messages database, created/used by TSTHOST
         |-DBFMSG.OLD   Old messages database, created/used by TSTHOST
         |-Files for source command (if you create source files)


       Detailed description of files and directory:


       PG - Server directory
       You  must place the PMS server in this directory. If this directory
       does not exist, the PMS PG command does not work.
       The next section of the manual describes the PG Server.


       MAIL - Messagges directory
       The  bulletins/personal   messages of  the PMS  will be  stored  in
       this  directory. If  this path  does not exist, the electronic mail
       section of the PMS does not work properly.










       TSTHOST v1.39 (c) IK1GKJ                                     9


       USERS - Users directory
       This  is the  directory   that   the  users  access with  the W, YU
       YD  commands. This  is the   only   path   that  can point to other
       parts  of your   hard  disk.   If not  otherwise specified, TSTHost
       uses  the path  USERS from  the directory   where   tsthost.exe  is
       loaded.   You   can  specify any  other  drive/directory  with  the
       USERDIR command.


       UPLOAD - Users upload directory
       This  is the  directory where will be stored any file uploaded by a
       pms  users  with  the  YU  command.  If  you  do  not  create  this
       directory, the YU PMS command will not work.


       WORKDIR - Standard work directory
       The  default value  is the  directory where  tsthost.exe is loaded,
       but  you can  select any  other drive/directory  with  the  WORKDIR
       command.  This path is used for the WRITEBUF, RECORD,  SEND,  YPUT,
       YREC  and  MAILCOPY  commands.  With  these  commands,  unless  the
       filename  does not contain a  specified  drive  and/or  path,   the
       file   will   be   accessed in  the  WORKDIR  path.  For  instance,
       by   executing   the  command WRITEBUF  TEXT, the  contents of  the
       review  buffer will  be written  in   a file   called  TEXT  in the
       directory  that  you have specified with  the WORKDIR  command, but
       WRITEBUF  E:\ASC\TEXT will  write the buffer  into  a  file  called
       TEXT   in  E:\ASC. The  purpose of  this command is to separate the
       tsthost files  in  capture, YAPP receive and the other files.



       TSTHOST.PSW - Automatic password file
       This   file  contains the  password for  those systems that require
       an access password, like BBS and node sysop.
       The  next manual  section describes  this aspect with more details.
       If  you do  not need  any password,  or do  not need  an  automatic
       password,  do not  create this  file. Anu  line starting  with  the
       '#' symbol is a remark and is ignored.

       TSTHOST.SYS - Password file for PMS SYS command.
       This file is similar to the tsthost.psw file. The format is:

            CALLSIGN_without_ssid VALIDATION_FLAG PASSWORD

       every  line start  with   a callsign   without  SSID,  a  space,  a
       validation   flag  and  the  user  password  not  longer  than  255
       alphanumeric  characters. Only  the users write here may do the SYS
       command. For instance:






       TSTHOST v1.39 (c) IK1GKJ                                     10


            IK1GKJ 3 aabbcc
            IK1MSL 1 8873mnhbkjAST

       Flag is a bit field:

            1 means  that user  may access  with the YD, W, V to any drive
       and path of your system, but may YU only in the UPLOAD path.

            2 is like 1, but the user may access to any disk and path also
       for write a file (YU)

            4 means that the user may do the DOS command.


       TSTHOST.CFG - Automatic configuration file
       This   is   an   ASCII    text  file,  that  contains  the  command
       sequence  for   the   automatic  configuration.  This  file will be
       searched  by TSTHost  when   started and,  if present,  the program
       executes  all the  commands   in the  file. Every   line    is    a
       command.   This   file  can contain  any TSTHost command.  Any line
       starting  with the '#' symbol is  a remark  and  will  be  ignored.
       The  line  length  MUST  not exceed 78 characters.


       TSTHOST.SHD - Shutdown configuration file
       Like   the  tsthost.cfg   file,  this  file  contains  the  command
       sequence that is executed at the program shutdown.


       TSTHOST.ULS - Unproto list file
       This   file  is created  and  managed  by  the  program.  When  you
       activate  the   unproto   list  the  program  reads  this  file, if
       present,  so TSTHost   can  handle the  message list  from the last
       number  received. When   you   close   the  list  or  shutdown  the
       system,  the program  saves the  content of  the list  in this disk
       file.  If   this   file  is not found or you delete it, the program
       will  ask to  the HomeBBS  the Unproto message starting from number
       one.


       TSTHOST.ENT - PMS connection text
       This  is an   ASCII   text   file.  When a remote user connects the
       PMS  system,   TSTHost sends  the content  of this  text  file  (if
       found) to the user before the PMS command prompt.

       WARNING:  Do not use the square brackets '[' and ']' in this file,
       because they are used for SID forward protocol.







       TSTHOST v1.39 (c) IK1GKJ                                     11


       TSTHOST.HLP - PMS help file
       This  is an   ASCII   text  file. When the remote user connected to
       the  PMS issues the  HELP  command,  TSTHost  sends  the content of
       this  file to  the user,  otherwise sends  the message 'NO HELP' if
       the file is not present on the system.


       TSTHOST.PGS - PMS PG server list
       Another   ASCII file.  It can be created by the sysop according  to
       his  requests, because  it is  related to  the PG  section. When  a
       user  connected   to   the   PMS   issues   the  command PG without
       arguments,  TSTHost sends the contents of this file to the user, or
       the  message NO PG AVAILABLE if the file does not exists. This file
       can be used to list and describe the available PG server programs.


       TSTHOST.LOG - Connections log
       This  file will  be created  and   managed   by  TSTHost  when  the
       LOG  command  is  ON.  It  contains  the  list  of the  connections
       with callsign, date and time.


       SOURCE files
       These  files are  similar   to   the  tsthost.cfg  file,  but  will
       be  executed  only  when  you  type  the  command.  This is  useful
       to  activate specific  configurations on  demand. Any line starting
       with the '#' symbol is considered a remark and is ignored.



























       TSTHOST v1.39 (c) IK1GKJ                                     12


       TSTHOST.BID - Bid file.
       This  is a very important file, and must NOT be altered or deleted.
       The  purpose of this file is to have a list of the received bid and
       to  store the number of the last bid used by tsthost. But what is a
       BID?  Simple, think  to a  bid like  a word  that unique identify a
       message.  Every time a new message will be created, from tsthost or
       other  bbs, a  unique bid  will be appended to the message, this to
       avoid duplicate.

       For  example, assume  that i forward the message XX to homebbs, the
       message  have bid  YY. Next i use the command FA to force again the
       forward  of this  message to  homebbs.  When  homebbs  receive  the
       proposal,  it detect  that the  bid YY  was already  received,  and
       refuse the message.

       The  internal bid of tsthost are a sequential numbers and a string,
       you callsign: 12345+IK1GKJ
       (1->2->3->..65535->1->2 etc etc).

       Now, if you delete or lose this file, you obtain 2 things:
       1)  will be  lose the  list of  the received  bid, this is a little
       problem,  at most,  if you  receive forward from more than one bbs,
       is possible that you receive a duplicate message.

       2)  tsthost must  restart the  bid sequence,  and this  is a  great
       problem.  For example,  tsthost  have  created  and  forwarded  ten
       message,  this messages  have bid  from 1 to 10. Now, if you delete
       the  file, tsthost must restart the sequence from 1, but since your
       homebbs  have already  received bid  1..10, it will refuse any your
       message with bid number under 11.

       To  avoid this  problem, you can use the command NBID, to assign an
       high  value to  the bid  number.  This  is  a  emergency  solution,
       because  assume that  you know what was the last bid number used by
       tstshost.....  The best  thing is  to NOT  DELETE or  altered  this
       file.  Pleas note  that the  NBID command  must be  used  ONLY  for
       emergency situation, normally you MUST NOT usa this command.

       When  tsthost start,  if the bid file do not exist, the program ask
       for  its creation  (normally the  first time  you  start  tsthost).
       Insert  Y to  create the  file, (and  if the  file was  lost do the
       command NBID BID_NUMBER), or N to exist and provide a backup copy.

       TSTHOST.BID  a routing file of 3001 record. Every record is long 13
       byte,  and is  the bid  of the message (char[13]). The first record
       is  an exception,  it  have  two  unsigned  integer  number  (ascii
       format),  separated by  space; the  first is  the next internal bid
       that  tsthost will  be use,  the  other  is  the  first  record  to
       overwrite into the tsthost.bid file.





       TSTHOST v1.39 (c) IK1GKJ                                     13


       TSTHOST.IN - Mail import file
       This   is   an  ASCII text file. The purpose is to allow SERVER and
       PG  programs   to   add   messages   to   the    PMS.     The  file
       presence  is tested    every  minute  and  processed,  when  found.
       TSTHost  searches in  this   file a  sequence of SP or SB commands.
       Note  that you  MUST use  the   correct syntax.   When processed, a
       line  starting with SP or SB is searched, discarding the others. If
       such  line is  found, the  next one is considered the message title
       and  the others  are the  message text.  A line  starting with  /EX
       ends the message.

       Example:

       SP IK1AAA @ IK1MSL < IK1BBB
       message title
       message line 1
       message line 2
       ....
       /EX
       SB ALL @ EU
       message title
       message line 1
       message line 2
       ....
       /EX
       The   TO  field   MUST be  specified, the  ROUTE (@)  and FROM  (<)
       fields
       are  optional.   If the  route field is specified, the message will
       be
       forwarded   to  the   HomeBBS. If  the FROM field is not specified,
       the
       default value of the PMS callsign will be used.

       NOTE: The line length MUST NOT exceed 80 characters.




















       TSTHOST v1.39 (c) IK1GKJ                                     14


       TSTHOST.DMS - PMS messages database
       This   is  a   binary file,   and is  used by  TSTHost to  maintain
       the  messages   list in   the  MAIL directory. Do not alterate this
       file  if you do not know what you are doing!. The easiest method to
       destroy all messages is to delete this file, so be careful  ......

       This   is    the    tsthost.dms    file    structure,    for  those
       programmers interested in writing server programs:

       struct dirmes {
           char type;                  /* type of message B P */
           char status;                /* status of message N F K Y */
           long number;                /* number of message */
           int  da_year;               /* creation date, year */
           char da_day;                /* day */
           char da_mon;                /* mounth */
           unsigned char ti_min;       /* creation time, minutes */
           unsigned char ti_hour;      /* hour */
           unsigned char ti_hund;      /* hundredths of seconds */
           unsigned char ti_sec;       /* seconds */
           char to[7];                 /* destination, TO field */
           char route[7];              /* destination BBS, @ field */
           char from[7];               /* sender, FROM field */
           char title[61];             /* message title */
           char frombbs;               /* <> 0 if received in forward */
           char startbbs[7];           /* BBS where the message started*/
           char bid[13];               /* BID or MID of the message */
           char rcvbbs[7];             /* BBS that have fwd the msg */
           char free[4];               /* reserved */
                    };                 /* total 128 bytes */

       All char fields end with a 0 byte, according to the C default.
       The  message is  decoded with  the number  field. The message is in
       the  MAIL   directory:   the   filename   correspond to  the NUMBER
       field  and the  extension is  .MES. The  filename is always 8 chars
       long,   right aligned by padding the remaining left positions  with
       ASCII  '0's. For   instance,   if  NUMBER is  4,   the      message
       filename   will  be 00000004.MES

       The  message number  is consecutive   and,    when    the    server
       appends  a new  message,   it   has   to  read the last record from
       tsthost.dms  and increment  the number  field  to  obtain  the  new
       message number.

       WARNING:   all  fields in  the dirmes  structure must  be always be
       set;  for instance,  if the  @ route is not requested, you MUST set
       it, so *dirmes.route=0;

       DO NOT ALTER THIS FILE WHILE TSTHOST IS RUNNING !





       TSTHOST v1.39 (c) IK1GKJ                                     15


       FORWARD,   UNPROTO   list,   CHANNEL   8   and (optional) automatic
       password request.
       --------------------------------------------------------------
       TSTHost  connects the  HomeBBS  for  forward  or  unproto  list  on
       channel  8 only.  If this  channel is  BUSY, the  program waits and
       retries   to connect the station when this channel is free. For the
       forward,  the program  always calls  the master  BBS to  allow  the
       reverse  forwarding but  the unproto  list  is  requested  only  if
       active and there are some selected messages.

       NOTE:  in a  multiport system  (multiport TFPCX),  you MUST  ensure
       that the channel 8 is associated to the same port of the HomeBBS.
       Again,  since it  is possible  that the program  calls  the station
       while you are already connected to the HomeBBS on another channel,
       it is suggested to set for channel8 a  unique  SSID (AX25 PORTCALL
       command).

       It  is possible  to ask  for the  forward and  unproto list EVEN if
       your  HomeBBS requires  a password  to access  the system.  To  get
       this,   you  must   set the command HPASPROMPT. If you need to pass
       trought  a node, the program provide the command HNODE. HOMEBBS and
       HNODE  commands accept  a list  of callsign  that may  be used like
       digipeaters,  if needed.  For node  like BPQ  that may  require  to
       specify  a port  number to do a connection, example CON 5 IK1MSL-8,
       the software have the command HCHANNEL.

       Here is some examples:

       The  IK1MSL bbs  may be  connected directly,  and do  not require a
       password to access it:

            HOMEBBS IK1MSL-8

       But, if HomeBBS requires a password, and the prompt is:

            PASSWORD? 11 22 33 44......

       The command must be:

            HOMEBBS IK1MSL-8
            HPASPROMPT PASSWORD?

       Of  course,   this prompt   and  the relative password must be also
       set  in    the   TSTHOST.PSW   password   file.  Check the  section
       about  the AUTOMATIC     PASSWORD   for more  informations on  this
       matter.

       Now,  the bbs  may be  connected only trought the IK1ABC and IK1DEF
       digipeaters:





       TSTHOST v1.39 (c) IK1GKJ                                     16



            HOMEBBS IK1MSL-8 via IK1ABC, IK1DEF

       If a node is required to connect the bbs, and the node is IK1HHH:

            HOMEBBS IK1MSL-8
            HNODE IK1HHH

       First  will be  connected the  IK1HHH node,  next the IK1MSL-8 bbs.
       But,  if the  node require  to specify the channel 4 to connect the
       bbs:
            HOMEBBS IK1MSL-8
            HNODE IK1HHH
            HCHANNEL 5

       Another  example, you  need a node, but also you need a digipeaters
       to access the node. Digipeaters is IK1ABC

            HOMEBBS IK1MSL-8
            HNODE IK1HHH via IK1ABC

       To  end, the  node as  far as  the bbs required a digipeaters. Digi
       for  connect the  node are  IK1ABC, IK1DEF,  digi to connect bbs is
       IK1QWE:

            HOMEBBS IK1MSL-8 via IK1QWE
            HNODE IK1HHH via IK1ABC, IK1DEF

       First  will be  connected the  node trought  the  digi  IK1ABC  and
       IK1DEF,  next the program ask the node to connect IK1MSL trough the
       digi IK1QWE.























       TSTHOST v1.39 (c) IK1GKJ                                     17


       FORWARD protocol
       ----------------
       The   PMS  can forward  with a master BBS according to the standard
       MBL/RLI  or FBB  COMPRESSED protocol.  Any BBS  may connect the PMS
       and  forward data,  but the   PMS  will  send  the  message only to
       the BBS defined with the HOMEBBS command.

       The   PMS   will  send  to  the HomeBBS  all the messages that have
       a  specified   route set  ( @Field not blank), and locally created.
       If  a received   message   has  been forwarded  by another  BBS, it
       will   be forwarded to the  connected  BBS  only  if  the  callsign
       of   the  connected   BBS is not the same of the callsign stored in
       the RCVBBS field.

       For  personal  messages,  they  will  be  forwarded  only  if  the
       addressee of the message has not read it.

       In   the message list, the letter 'L'  near the type/status of  the
       message  shows that   this  message was  written locally, otherwise
       the message was received by the forwarding activity.

       You  may always  connect Home  Bbs and  send your mail, but to have
       forward,  you must be enabled from the sysop of the bbs. So contact
       the sysop and ask for this feature, if you are interesting.

       To do this, the sysop of Home Bbs must:

       1) Create a forward file like this:
          #
          A IK1GKJ
          P B
          R
          B IK1GKJ
          F IK1GKJ
          C C IK1GKJ
          ----------
          #
        If  you also need  the  @AMSAT  messages, the  sysop  must  add
        the G AMSAT statement after the F IK1GKJ line

       2) Edit the BBS.SYS file, and add your CALLSIGN to the list
       3)  Edit your  record and  change the bbs field, now it must be set
       not to bbs callsign, but to YOUR callsign. (NH command.)

       This  info is  for fbb  type bbs,  i do not know how work the other
       sotware.








       TSTHOST v1.39 (c) IK1GKJ                                     18


       Problem to connect for UNPROTO and FORWARD
       ------------------------------------------
       TstHost  use to  call homebbs  for fwd  or unproto message a simple
       protocol.  First, will  be connected the bbs, always on the channel
       8,  using HNode  if set,  or  directly.  Next  TstHost  wait  until
       receive  the from  the BBS,  the SID  and/or PASSWORD  request, the
       order  is not  rilevant. But  the SID must be received, (sid is the
       string  [FBB-5.15-ABFHM$] or  similar). The  program  MUST  receive
       this  string, because  from the sid the program can detect the type
       of protocol to use.

       Now,  tsthost wait  for a  bbs  prompt.  When  the  bbs  prompt  is
       received,  the sequence  is completed,  and forward or unproto list
       request may started.

       The  bbs prompt,  is a  char >  at the end of a line. This may do a
       problem  on some  bbs, since  many sysops  have set the char > into
       the  welcome text  on their  bbs. In  the normal connection this is
       not  a problem,  but with a remote protocol yes, because if tsthost
       receive  this character,  it think  that it  is the bbs prompt, and
       the sequence was not corrected.

       For example, if the bbs welcome text have a line line this:
       HALLO MARIO, FOR HELP TYPE THE COMMAND <?>

       surely  you will  not be  able to start fwd or unproto, because the
       character > at the end of the line confuse tsthost.

       But,  this line,  HALLO MARIO, TYPE <?> TO HELP, do not do any type
       of problem.

       If  you have  this problem, you may ask to the sysop bbs to set you
       like  a real  bbs. The  bbs nevar  send text  to real bbs, but when
       connected send only the prompt (or password request).

       NOTE:  If you cannot start fwd o unproto list, and cannot solve the
       problem,  to obtain  help, please  switch on  channel  8,  manually
       start  a fwd  or unproto  request, and  when disconnected,  do  the
       command  WRITEBUF ABC.  Next send me a message whit the contents of
       the ABC file, so i cam examine it.














       TSTHOST v1.39 (c) IK1GKJ                                     19


       FORWARD command
       ---------------
       * FL
       This   command  list all  messages that  must be forwarded but have
       not yet been sent to the HomeBBS.

       * FA nbr nbr nbr (up to 10 numbers)
       Add the specified messages to the forward list.

       * FR nbr nbr nbr (up to 10 numbers)
       Remove the specified messages from the forward list.

       * FBbmode ON OFF
       Enable  (default) or  disable the fbb compressed forward mode. This
       type   of  forward  require  about  32  kbyte  of  memory  for  the
       compression  routine, if  the program do not found enough memory to
       start  the compressed  forward, automatically switch to the MBL/RLI
       forward type.

       * FTIME 0..60 minutes
       Every  FTIME minutes,  the PMS  will connect  the master BBS asking
       for  the  forward. Any value  below  10 disables the function,  and
       the forward is performed only if the HomeBBS calls your station.

       * FWD
       Manual start of the forward with the HomeBBS.

       * HIeraddr TEXT | OFF
       Is  a field  of max 20 characters, used to define your hierarchical
       address, for example .IPIE.ITA.EU
       OFF  disable the  function. This  field, if  present, is  used with
       RLine command.

       * RLine ON | OFF
       If  ON, when your PMS forward a message, your R: line will be added
       to  the message,  if OFF  no. WARNING:  with RLine  ON, you will be
       considered  exactly like a regular bbs, so, if a user use a command
       SR  on your  mail, the  return address  will  be  YOURCALL@YOURCALL
       insted  of YOURCALL@YOURHOMEBBS. If @YOURCALL is not defined in the
       homebbs  and/or adiacent  bbs inhis  forward file, mail sent to you
       vill  nevar arrive  to you,  this because  you are not a bbs in the
       regular  path. Whit  off this  is not  a problem, because your mail
       will be returned to your homebbs, and homebbs is know in the path.

       But,  some server have the capability to communicate one to another
       trougth  the RLine,  and in  this case,  if you do not enable RLine
       this type of server cannot work properly. So see you need.....







       TSTHOST v1.39 (c) IK1GKJ                                     20


       * LBheld ON | OFF
       Any  bulletins locally  generated will  be put in status HELD. This
       meand  that only the sysop and the sender of the message may accest
       to this mail.

       * LPheld ON | OFF
       Like LBHELD, but works on personal mail

       * FH
       Display all HELD messages

       * FF message_nbr
       Free the HELD messages and put it into the New state.









































       TSTHOST v1.39 (c) IK1GKJ                                     21


       PG SERVER
       ---------
       The  PG servers  are programs  written to  expand the capability of
       the  software. They  MUST be  placed in the directory PG, one level
       below  the  location  of  tsthost.exe. As  the  system  is inactive
       while  executing   the  PG  servers, they must be small and use the
       minimum  machine time. The displayed  image  is  saved  during  the
       program  execution. The  server  must  NOT  access  the  video  RAM
       directly.

       The server receives the following command-line:
       argv[0]     Drive\path\servername;
       argv[1]     Callsign of the user, with ssid
       argv[2]     Server level, 0 the first call, up to 255 the next.
       argv[3...]  User-specified parameters, each word  is  a  separated
                   argument.

       The  server data  output (with  printf() and putf()) is transmitted
       to the user.

       The server may return:

       0 - The output of the server is  sent  to  the  user  and  returns
           to the PMS prompt

       1 - The output of the server is sent to the user and the server is
           called again.

       2 - The output of the server is executed like a PMS  command,  and
           the user is reconnected to the PMS interface.

       3 - The output of the server is executed like a PMS  command,  and
           the server is called again.


       NOTE   for  2   and 3:   The  output must be maximum 80 chars long,
       and  must start  at the  line beginning;   the  line must NOT start
       with   a  carriage   return or  line feed.  The server  must  NEVER
       return another PG command.















       TSTHOST v1.39 (c) IK1GKJ                                     22


       For   instance, this is a very simple ECHO server  that  returns to
       the user all he have typed, until the user types BYE:


       #include <stdio.h>
       #include <string.h>
       main(int argc, char **argv)
       {
       int i,mode;
       sscanf(argv[2],"%d",&mode);
       if(!stricmp(argv[3],"BYE") && mode)
            {
            printf("\nBest 73\n");
            return 0;
            }
       printf("\nHallo %s, you have send:\n",argv[1]);
       for(i=3;i<argc;i++) printf("%s ",argv[i]);
       printf("\nType BYE to end.\n");
       return 1;
       }


       The user IK1AAA calls the server with PG ECHO AA BB.
       The server returns HALLO IK1AAA, YOU HAVE SEND AA BB,
                         TYPE BYE TO END
       the user types I AM MARIO
       The server returns HALLO IK1AAA, YOU HAVE SEND I AM MARIO,
                         TYPE BYE TO END
       the user types BYE
       The   server returns BEST 73,  and the  user will return to the PMS
       prompt.























       TSTHOST v1.39 (c) IK1GKJ                                     23


       AUTOMATIC PASSWORD
       ------------------
       The  TSTHOST.PSW  file  contains  the  passwords to use with those
       systems where it is requested for the access. The file format is:

                      STRING_TO_SEARCH PASSWORD

       STRING_TO_SEARCH   is   the   system  prompt when  the password  is
       being  requested, max  50  character long  with no spaces, PASSWORD
       is  your  password,  up  to  255  alphanumeric  characters  without
       spaces.

       Example:
       IK1MSL-8> abcdef
       IW1BRX-8> 123456
       IK1GKJ-8> ABCEDF

       Warning:  Upper and  lower case are ignored  in  the  string being
       searched, but are important in the password string.

       Here  are some  example for  the BBS  prompt, that  can  solve  any
       doubt,  and make you write the correct tsthost.psw. In the example,
       my demo password is ABCDEF

       IW1BRX-8> 11 22 33 44 55 [0123....           IW1BRX-8> ABCDEF
       Password? IW1BRX-8> 11 22 33 ....            IW1BRX-8> ABCDEF
       IW1BRX-8> Password? 11 22 33 .....           Password? ABCDEF
       IW1BRX-8> Password ? 11 22 33 ....           ? ABCDEF

       As  you have  seen, the  string being  searched is  ALWAYS the LAST
       word or characters that came before the password code.

       If the BBS prompt is:
       Insert your password 11 22 33 44 55

       and you insert in your tsthost.psw file:
       Insert your password ABCDEF

       TSTHost  will interpret  "Insert" as the string to be matched, and
       "your"  as your  password. This  is an   error! The correct form in
       tsthost.psw must be:

       password ABCDEF











       TSTHOST v1.39 (c) IK1GKJ                                     24


       PMS INTERFACE
       -------------
       Every  channel of  the software is a PMS and  a  normal connection
       channel at the same time. All non-connected  channels  are  set by
       default in PMS mode. This means that a remote  user  that connects
       your station will operate in PMS mode.

       But,  if YOU  issue the  Connect command,  the  channel  becomes  a
       normal conversation channel.

       There  is   an exception  to this. When the software starts, if one
       or  more   channel in   your  TNC   are already  connected for  any
       reasons,  they are  conversation channels,  not PMS.  The reason is
       that   it   is  impossible to  know if  those  channels  have  been
       connected by  us  or by a remote user.

       You   can  switch   from PMS   or  NORMAL  channel  mode  with  the
       commands  TALK   (from PMS to NORMAL, for example after a chat with
       the  remote user),   and   PMS   (from  NORMAL to  PMS). You cannot
       switch  a session  if the  task is  not stand-by. The PMS cannot be
       executed  if there is an active file transfer on the channel (YAPP,
       send  or capture). A  TALK  command  has  no  effect  if the PMS on
       that channel is processing a user command.

       Moreover,  you cannot switch a window to conversation mode  that is
       already  active in  PMS mode.  This is  correct because  you cannot
       chat  with a  user, or  your  text  will  interfere  with  his  PMS
       activity. You have to switch to TALK mode before chatting.


























       TSTHOST v1.39 (c) IK1GKJ                                     25


       THE SERVER
       ----------
       What  is the  server? The  server are programs com or exe that must
       be  exist in  the tsthost.exe  directory. When  a personal  message
       arrive  to your  pms interface,  and tsthost  detect a  server (see
       SERVER  command), tsthost  copy the  contents of  this message to a
       file,  next execute  the related  com or  exe file  and  pass  like
       argument  the name  of this  file. This is a standard forward file,
       so  the first  line will  contain SP SERVERNAME < IK1AAA, next line
       will  be the title of the messages, next to end the contents of the
       messages.  Server may  do anything, but any return message from the
       server  to sender must go into the tsthost.in file. When the server
       stop  the execution,  control return  to tsthost,  messaged  copied
       will  be deleted,  original message  will  be  put  into  K  state.
       Remember that will server are running, tsthost is stopped.




       THE SCROLL LOCK LED FLASH, MAIL IN SCREEN, /NOLED COMMAND
       ---------------------------------------------------------
       When  a new  mail for you arrive on the pms interface, the keyboard
       scroll  lock will  flash, and  MAIL will be displayed on screen. In
       the  previsuly version  the led  function was  be removed, since on
       some  system the  flash cause  problems. Now i have chenge the code
       of  the flash routine, and this cose seems be ok. If you note again
       any  type of  problem, you  may disable  the led flash routine with
       the command line parameters /NOLED.

       To  stop flashing,  you MUST  press ALT-F10  key or do the LM or RM
       command from KEYBOARD; i have used this soluction for two reasons:

       1)  TSTHOST.DMS is  not in  memory, and scan it to see if your mail
       is already read cost some time.

       2)  a PIRATE  user may  connect your  pms with  your callsign, read
       your  mail, and  next kill  this message.  I case  1) the line will
       flash off, and you do not see that new mail was arrived. With this
       system,  you may  note that  mail is arrived, even if that mail was
       killed or read.














       TSTHOST v1.39 (c) IK1GKJ                                     26


       PMS command from KEYBOARD
       -------------------------
       * ENdmessage filename | OFF
       This  command defines  a file  that will  be automatically added at
       the  end   of any  message written  with the S?/SR functions of the
       PMS.  If the   S?/SR  command already have the +FILENAME extension,
       first  will be  added the  FILENAME contents,  then the  ENDMESSAGE
       contents.

       OFF Disables this function.

       If ENDMESSAGE does not have a specified path, it will  be searched
       in the program directory.


       * R [XR]  to read messages
       * K       to kill messages
       * L       to list messages

       Optional parameters for commands R, L, K:
       (The example is for List command, but most of them also work for
       Read and Kill)

       L              List all messages  (only LIST, not READ/KILL)
       LL 50          List last 50 messages (only LIST, not READ/KILL)
       L 100          List message number 100
       L 100 102 150  List messages 100 102 and 150 (max 10 numbers)
       L 100-150      List message from 100 to 150
       L -150         List message from begin to 150
       L 150-         List message from 150 to end
       L< CALL        List all messages sent by CALL
       L> CALL        List all messages for CALL
       L@ ROUTE       List all messages for that route.
       LS STRING      List all messages that have STRING in the title.
       LM             List all my messages

       NOTE:  From keyboard, the sysop can access all  messages,  even if
       the message is for someone else and if the message is Killed.
       The exception is for the LM RM KM commands, that access  the sysop
       messages and do not access the Killed messages.

       XR  work exactly  like R, but while R compress the R line like fbb,
       XR display the line in full format.











       TSTHOST v1.39 (c) IK1GKJ                                     27


       * S  CALL [@ ROUTE] [+FILENAME]    * SB CALL [@ ROUTE] [+FILENAME]
       * SR[R] MESSAGE_NUMBER [+FILENAME] * SP CALL [@ ROUTE] [+FILENAME]
       * SC    MESSAGE_NUMBER CALL [@ROUTE] [+FILENAME]

       The 'SP' sets the message to Personal,  that  means  that only the
       addressee can read the  message.  The  'SB'  sets  the message  to
       Bulletin,  that means  that anybody  can read  the message.  If the
       'SB'  or 'SP'  are not  expressly specified, (the 'S' command), the
       program  assigns the 'P' mode for any valid CALL, otherwise the 'B'
       mode.

       SR  automatically replies  with a  P-type message  to the sender of
       the  specified   message number.  The title  of the message will be
       "Re:" and the title of the original message.

       SRR  work like  SR, but insert in the editor a copy of the contents
       of message_number

       SC send a copy of the specified message number to CALL.

       During   those   command,   you   cannot   switch the task, but you
       must  terminate the  message editing  session. The  space for   the
       internal  editor  is  200  lines.  If +FILENAME exists, the content
       of  the specified  file is  appended to the end of your message. If
       FILENAME  has a drive/path specification, the file is read from the
       selected  location, otherwise  it will  be searched  in the WORKDIR
       path.


       * EDit msg_nbr
       Permit to edit the contents of the message number specified.


       * HNode [CALL-SSID | OFF][via digipeaters]
       To  define a  node to  use for  connect homebbs  in UL  get and FWD
       command.  OFF disabel  the NODE  usage. Pratically,  first will  be
       connected  the HNODE  callsign, next will be connected the homebbs.
       Example:
            HNODE IK1QQA
            HNODE IK1QQA via IK1ABC, IK1QWE......


       * HChannel CHANNEL | OFF
       Since  is possible  that the  node required a specified port number
       to  connect HomeBbs,  (ieg BPQ),  CHANNEL define  the  port  number
       where  the node connect the bbs. If for example the PORT value is 2
       and  Home bbs  is IK1MSL-8,  once connected to the node the program
       issue:  C 2 IK1MSL-8






       TSTHOST v1.39 (c) IK1GKJ                                     28


       * HOmebbs CALL-SSID [via digipeaters list]
       Defines  the BBS  where the  PMS messages  have to  be transmitted,
       those  with the  routing field  (@) set. SSID must be specified, as
       IK1MSL is different from IK1MSL-8. For example:
            HOMEBBS IK1MSL-8
            HOMEBBS IK1MSL-8 via IK1ABC, IK1DWE......


       * HPasprompt PASSWORD_PROMPT | OFF
       PASSWORD PROMPT  is  an optional  field used  ONLY if  the HomeBBS
       requires a password for  the  system  access,  check  the relative
       section in this manual.


       * HAlias CALL-SSID
       To  define an extra callsign that will be considered like a homebbs
       when connected.


       * MAilcopy message_number destination_filename [/A]
       Similar  to READ  msg_nbr, the output will be written in a file. If
       file  name does  not have a drive/path specification, the file will
       be written in the workdir directory.

       Note:  with /A  parameters,  the  message  will  be  appended,  not
       overwrite destination_filename


       * MHeader MESSAGENBR HEADERFIELD=HEADERDATA
       This  command is  useful to change the header of any message in the
       pms.  HEADERFIELD is  a single  letter that  identify the  field to
       change:
            A for address of the mail, the TO recipient.
            R for the routing of the mail, the @ recipient.
            F for the sender of the mail, the FROM recipient.
            B for the bid of the message.
            D for the description, the TITLE of the message.
            S for the status of the message, may be [K]illed,[N]ew,[Y]read
              [F]orwarded, [H]eld. Any of this setting may be done to a
              personal mail, but bulletin message do not accept the Y
              status.
            T for the type of the message, may be [B]ulletin or [P]rivate

       For  example, we  have a  messagge for  P IK1ABC @ IK1FUZ, title is
       ABOT YOUR MAIL. We want correct the title an the TO callsign, so:
            MH 1 D=ABOUT YOUR MAIL
            MH 1 A=IK1BBB







       TSTHOST v1.39 (c) IK1GKJ                                     29


       * NBID bidnumer (1...65535)
       To  assign a new bid start sequence. DO NOT USE THIS COMMAND IF YOU
       DO NOT KNOW WHAT YOU ARE DOING!!. Read TSTHOST.BID section before.
       If   you  do  this  command  without  parameters,  simple  will  be
       displayed the next internal bid number.


       * PMS
       The current task is switched in PMS mode, for instance after a QSO
       with the remote user that called you. The user returns to  the PMS
       prompt. You cannot switch if you have any active file  transfer in
       the channel (YAPP, record, send). See the TALK command.


       * RIng
       If ON (default), when the user does the 'T' command  the  Sysop is
       called,  otherwise the  user receives  a message  that the Sysop is
       not available.


       * SAvemsg +/-TOFIELD +/-TOFIELD .... up to 20
       To  define up  to 20  address field. Whe a message will be received
       on  the pms interface, if its TO field match one field in the list,
       the  message will  be copied  into a file in the WORKDIR path, with
       the TO address like a name and .MSG extension.


       * SERver +/-SERVERNAME +/-SERVERNAME .... up to 20
       To  define up  to 20  server program  that will  be  executed  when
       arrive a personal message addressed to SERVERNAME@YOURPMS.
       +  ADD server,  - REMOVE server from list. Do not specify extension
       or  path to  the server  statement,  only  the  filename,  and  the
       executable file must be located into the TSTHOST.EXE directory.


       * TALK
       The  current task is switched  to  the  normal  conversation mode,
       for  example when  the remote  user TALKs the sysop (see PMS). You
       cannot switch if the PMS is not in stand-by status.


       * Timeout minutes
       Specify  the time after, without activity on  the channel,  i will
       be automatically disconnected. Time is between 0 and 60 minutes; 0
       (default) disables the timeout function.









       TSTHOST v1.39 (c) IK1GKJ                                     30


       * UPdatedms pday bday
       When  a message  is killed, the file is not  deleted from the disk
       but the status flag becomes 'K'. This command allows  the deletion
       from the system of those messages that are killed, status 'K', and
       the  PERSONAL   messages that   have   been   already  read, status
       'Y', or forwarded, status 'F'.

       PDAY  is the number  of  days (from creation) that a PERSONAL type
       message  can exist  in  the  system,  BDAY is  for  BULLETIN  type
       messages.  When a  message is  older than  this number  of days, it
       will be deleted from the system, without checking the status flag.

       Please  note that  you cannot run  this  command  if  any  user is
       connected to the PMS interface.

       For  example, to  erase  all  private messages after 10  days, and
       bulletin messages after 4 days:

         UP 10 4


       * USerdir [path]
       Sets the directory for the users connected to the PMS interface.
       The default path is a subdirectory within  the  one  that contains
       tsthost.exe, but you can change to a new path with this command.
       Note that TSTHOST does not CREATE  the  directory,  the  path MUST
       EXIST.



























       TSTHOST v1.39 (c) IK1GKJ                                     31


       PMS commands for remote users
       -----------------------------


       NOTE:  ANY COMMAND, BEFORE TO BE DECLARED UNKNOWN, WELL BE SEARCHED
       LIKE  A PG,  THIS PERMIT TO EXPAND THE PMS COMMAND WITH PG PROGRAMS
       WRITTEN FOR PARTICULAR FUNCTION.



       * R [XR]  to read messages
       * K       to kill messages
       * L       to list messages

       The valid parameters for the R, L, K commands are listed in the
       following table (the examples are for the List command) :

       L              List all messages (only LIST, not READ/KILL)
       LL 50          List last 50 message (only LIST, not READ/KILL)
       L 100          List message number 100
       L 100 102 150  List messages 100 102 and 150 (max 10 number)
       L 100-150      List message from 100 to 150
       L -150         List message up to number 150
       L 150-         List message from number 150 on

       L< CALL        List all messages sent by CALL
       L> CALL        List all messages for CALL
       L@ ROUTE       List all messages for that route.
       LS STRING      List all messages that have STRING in the title.

       LM             List all my messages

       NOTE:   Any  users have  access  to  all  bulletin    and  personal
       messages  addressed to his callsign or that  he  have  sent. Killed
       messages will never be listed.

       XR  work exactly  like R, but while R compress the R line like fbb,
       XR display those line completely.

       * B
       Disconnects the system.


       * DOS DOS_COMMAND
       If enabled, TSTHost executes the  specified DOS command.









       TSTHOST v1.39 (c) IK1GKJ                                     32


       * PG [[NAMESERVER] SERVER PARAMETERS]
       If called without  arguments, the  program sends  to the  user the
       contents   of  the   file TSTHOST.PGS, if exist, otherwise sends NO
       PG  AVAILABLE. In  this way  it is  possible for  the sysop to have
       some  PG servers  not declared. A user will not execute the servers
       but  the sysop,   or  a  restricted  group  of  users,  can  easily
       activate these extra services.

       If  the server  name parameter  is specified,  the program executes
       the  specified  server. The  output of  the server  is sent back to
       the user.


       * SYS
       When   the  user  performs  the SYS command,  his callsign  will be
       searched  in   the TSTHOST.SYS  file, and,  if  found,  the  system
       requires  a password, ALWAYS CODIFIED WITH THE  MD2 SYSTEM.  If the
       user  enters the  corrected password,  to the user will be assigned
       some   privileges,  specified  in  tsthost.sys  file  by  the  flag
       parameters. At the actual version, flag is a bit field:

            1 means  that user  may access  with the YD, W, V to any drive
       and path of your system, but may YU only in the UPLOAD path.

            2 is like 1, but the user may access to any disk and path also
       for write a file (YU)

            4 means that the user may do the DOS command.

       The  password prompt is the PMS callsign without SSID,  with _PMS>
       and the password request, like:

       IK1GKJ_PMS> [0123456789]

       To  cancela previusly authorization, you may repeat the sys command
       and  do a  bad  or  null  password.  If  you  change  the  flag  in
       tsthost.sys  while a  user with a valid authorization is connected,
       the  new flag  will not have effect until the current authorization
       will not be cleared.


       * S  CALL [@ROUTE]   * SB CALL [@ROUTE]           * SR MSG_NBR
       * SP CALL [@ROUTE]   * SC MSG_NBR CALL [@ROUTE]
       Stores  a message  into the   PMS.  SB is for bulletin messages, SP
       for  personal  mail. The  field @ROUTE  is optional.  If specified,
       the  message will  be forwarded to the specified HomeBBS. If  the P
       or  B types are not expressly specified,  the program automatically
       assignes the P type for  any  valid  CALL, otherwise the B type.
       SR replies a P-type message to the sender of a specific message.





       TSTHOST v1.39 (c) IK1GKJ                                     33


       SC send a copy of message number # to call.
       To terminate the message editing, send CTRL-Z  or /EX in the first
       text column.


       * T
       Calls  the sysop.  The program  displays a  video message to notify
       the  sysop  the  user  request.  If CBELL is ON the programs sounds
       the speaker, together with the message.


       * U
       List the users connected to the PMS interface.
       NOTE:  Only the stations connected to the PMS are listed. Channels
       not in PMS-mode are not listed.


       * V FILENAME
       Display  to the  users the  contents of an ascii file. File must be
       in USERSDIR or its subdirectory.


       * YD FILENAME
       Sends  to the   user  the specified  file using  YAPP protocol. The
       file must  be in  the  USERS  (USERDIR  command) directory or  its
       subdirectories.

       * YU FILENAME
       TSTHost receives a file from the user, with the YAPP protocol.
       The Resume option is always enabled, so if the transfer  stops for
       any reason, the user can reconnect the system and restart the file
       transfer from the  point where  he was  arrived. The file will  be
       put in the USERS\UPLOAD directory.

       * W [PATH]
       Display the contents of the USERDIR directory.

       * ?
       Sends to the  user the  contents of  the TSTHOST.HLP file. If this
       file   do  not  exist,  the  user  receives  the  message  NO  HELP
       AVAILABLE.

       * @ CALL TEXT
       Interrupts  the  user  CALL,  that  must  be  connected to the PMS
       interface, by notifying the TEXT message.









       TSTHOST v1.39 (c) IK1GKJ                                     34


       UNPROTO LIST
       ------------
       When a FBB BBS receives a new  message,  emits  a  special Unproto
       frame  with the  message description.  Also, it  is possible to get
       the BBS message list without connecting the system.


       With  those  features,  a  user with the PC active all the day can
       receive and maintain the list of the messages present on the BBS.
       It is not needed to connect the BBS to get the message list, too.


       To  use this feature  you must be enabled on the BBS system so, if
       you need the Unproto list, contact the Sysop.


       Even  if you are not enabled, the program  can  create  a  list by
       intercepting  the Unproto  messages, but  cannot resyncronize  with
       the BBS system if a packet is lost.

       NOTE: to use the unproto list, monitor channel  must  be  open for
       the  Unproto frames,  letter U.  AX MON  U,  AX MON US, AX MON UC,
       AX MON USC are correct, some other modes without the 'U' aren't !

       The  Unproto list  can save in memory up to 300 message headers, or
       if  you have more than 200 kbyte with tsthost installed, up to 800.
       The  older messages  are then  discarded to leave the space for new
       ones. The Unproto list feature requires 24/64 KBytes of RAM.


       The  HOmebbs  command  sets the BBS from which the Unproto list is
       accepted.  You must  specify  the callsign SSID, because IK1GKJ is
       different from IK1GKJ-8.


       You can set up  to 20 fields that are automatically  selected when
       received,  like is possible to set up to 20 fields that will not be
       inserted  in the  list. The  list  can  be  obtained  without  user
       operations,  or by  issuing   a special  command (please  read  the
       section  about channel  8 on  the manual), even if the BBS requires
       an   access  password.   Unproto  list   is  transferred  with  the
       compressed  FBB protocol.  This protocol  requires about 19K of RAM
       for the message decoding.

       The  files are  then saved  in the  WORKDIR  directory,  where  the
       filename  is the  TO field and with the .MSG extension, or put into
       the PMS interface, see the UL INTERFACE command.







       TSTHOST v1.39 (c) IK1GKJ                                     35


       IMPORTANT NOTE

       Some  programs allow the use of unproto frames with  the  poll bit
       set, that is not a  problem  for  the  Unproto  list.  However, in
       certain conditions, this can become a problem.

       For  instance, you  are connected  to your  HomeBBS on  channel  1.
       TSTHost  emits   a Sync   Unproto  frame  towards your HomeBBS, for
       the  Unproto  list.  The  HomeBBS, when receives the Unproto  frame
       with  the poll  bit set, returns you  a  DM  frame. This is correct
       since your monitor channel is not connected.

       But  your AX25 interface receives the DM frame ,  and  then  it is
       redirected to the channel 1 where you are connected, to disconnect
       the   link.  In this  case you  are disconnected by your TNC, while
       for the BBS you are still connected.

       To  avoid this  problem, TSTHost  starts by sending the @U0 command
       to  disable the  poll bit  in unproto  frames. Maybe some Eproms or
       Driver  do not recognise the command (as far as I know, only  TFPCR
       v2.10)  and if  the Eprom/Driver  starts with  the poll bit set you
       cannot  fix the  problem so  you'll be randomly disconnected by the
       system.































       TSTHOST v1.39 (c) IK1GKJ                                     36


       UList Subcommands
       -----------------
       Use these commands after the ULIST prefix, for instance:
       ULIST QUERY 122

       * Autoselect +/-TO_Field +/-<FROM_field
       Automatic selection of the messages in the  Unproto list according
       to  the desired  TO_Fields (up  to 20). For instance, to select the
       ALL, DX and NEWS fields the command is:
       UL A +ALL +DX +NEWS

       Then, to add the KWD field and remove the ALL field:
       UL A +KWD -ALL

       With  the same  format of  above, you may select the FROM field; to
       do  this, you must add the prefix '<' to the sender of the message.
       For example, UL A +ALL +<IK1GKJ

       UL A  without parameters displays the autoselect list.


       * Disable
       Disables the  Unproto list. The  Unproto frames are not decoded to
       the list. The list is saved in the TSTHOST.ULS file in the TSTHost
       default  directory. The memory used for the list is released. NOTE:
       the list will be automatically saved every hour.


       * Enable
       Activates the Unproto list.  The previous list is loaded from disk
       (TSTHOST.ULS), then any new message is added to the list.
       Being  enabled by  the HomeBBS, a missing message activates a synch
       request so to keep the list always updated.

       * Get
       Connects the HomeBBS to receive the selected messages.


       * Interface File (default) | Pms
       To  determine if  the received  unproto message  will be saved to a
       disk file or conneted to the pms interface.


       * List
       To display the unproto messages selected and not yet received.









       TSTHOST v1.39 (c) IK1GKJ                                     37


       * Not +/-TO_Field +-<FROM_field +/-@ROUTE_field
       Work  exactly like  Autoselect, but  the fields  set into this list
       will  not be  inserted in  your unproto list. Whit the NOT command,
       is accepted also the @ routing field.


       *Pmsg ON | OFF
       If  OFF, only  personal mail  addresses to  your callsign  will  be
       added  to the  unproto list,  other P mail will be discarded. If ON
       all P mail will be added to the unproto list.


       * Query [msg_nbr]
       Manual  request to  the BBS  to send  a  list  from  the  specified
       message  number. This  command should  not  be  needed,  since  the
       program  is always  automatically synchronised.  If msg_nbr  is not
       specified,  automatically the  program ask  for the  last  received
       message  in the list. NOTE: if a manual or automatic QUERY will not
       receive an answer, after 1,5 minuts the program will ask again.

       *Rpath [OFF | digipeater list]
       Normally  you do  not need  to use  this command,  may be some case
       where  the connection  bbs have  a digi  list, and  resync  request
       another  path. If  you define  a digipeater here, the connection to
       homebbs  will be  executed with  the path defined in HBBS and HNODE
       command,  but the  RESYNC request  will  be  addressed  to  homebbs
       trought this path.


       * Time 0..60 minutes
       This  command    sets  the  time  interval,  in  minutes,  for  the
       automatic  connection. If  there is   any message selected, TSTHost
       connects  the HomeBBS  for the message request. Any value below  15
       min.  disables this feature.


       * View
       Displays  in a  window the  message list.  Use the  standard cursor
       keys  to scroll  the list,  INSert to  select/deselect  a  message,
       ESCape  or RETURN to close the window. A "-" displayed in the first
       column,  means that  the message was already present at the time of
       the  last view command, an "R" means that the message was requested
       and received from HomeBbs











       TSTHOST v1.39 (c) IK1GKJ                                     38


       TSTHost commands description
       ----------------------------
       The uppercase letters are the minimum command abbreviation for the
       command recognition. Facultative parameters are  shown  in  square
       brackets, while mutually exclusive options are separated by |.


       Send,Delete,Dir,Yput,View parameter window
       ------------------------------------------
       If the parameters for the SEND, DELETE and DIR commands  have  not
       been  specified,  the  program  activates  a request window on the
       screen showing the files contained in the WORKDIR directory.
       Select  the  desired  file  with  the  ENTER  key,  by  moving  the
       selection   bar  with   the  cursor  keys. To log to another drive,
       press  the TAB key and type the corresponding  letter.  The  ESCape
       key  aborts the  request. The  ENTER key  has no  effect in the DIR
       window.


       * 7PCopy ON | OFF
       If  ON, any message arrived in your pms, or with unproto list, that
       have  any valid 7plus code, will be copied into the file 7PDATA.FWD
       in  the WORKDIR  path. This  file is  in the  standard  MBL-RLI-FBB
       forward-export  mode, and  may be  processed from server or prigram
       that recognize this format, or directly from 7plus etc......


       * AUtoyapp [on|off]
       When  activated, TSTHost  starts automatically  the  YAPP  protocol
       when  the init  protocol code   is   received  from  the  connected
       station,  otherwise you  have to  start the  file download with the
       YREC command. The file is saved in the WORKDIR directory.


       * AX25 subcommand command
       TNC setup command, read the description further on.


       * Bell [on|off]
       If OFF, disables the PC-speaker beep when a CTRL-G is received.


       * CBell [on|off]
       When  activated,  the program will emit an acoustic signal for any
       connection and disconnection.


       * CLS
       Clears the receive screen for the active channel.





       TSTHOST v1.39 (c) IK1GKJ                                     39


       * CLRbuf
       Clears the receive buffer for the active channel.


       * COLor process_number color_number
       Selects the color for the screen display. Read  the  help  text by
       issuing this command without parameters.


       * Connect callsign [v digipeater digipeater]
       Connect the specified  callsign. If the command is executed in the
       monitor  windows or  in an  already    connected    channel,    the
       program   will  attempt  to  connect  the  callsign  on  the  first
       available channel


       * COPy source destination
       Copies the source file in the  destination name. If a path name is
       not specified, the default directory is the WORKDIR. Wildcards are
       not allowed, and you cannot  overwrite an existing file.


       * CRon filename | OFF
       OFF  disable  the  function,  otherwise  every  hour  tsthost  will
       execute  the specified file. This file for default will be searched
       in  tsthost.exe directory,  if in  the filename  is not  present  a
       specified  drive or  path. The file may be EXE, COM or BAT. Tsthost
       always  attempt to  trapping the  output of the program , but for a
       batch  file, is  possible trap  the output  of the  bat but not the
       output  of the  program called  by the  batch file. To do this, you
       must  redirect to  a file or NUL device any program called from the
       batch  file. This  is not  a problem, even the program write to the
       screen  while executed,  when return  to tsthost  anything will  be
       restored. Example of good .bat file:

       @ECHO OFF
       DOTHIS1 > NUL
       DOTHIS2 /a /b >NUL
       .....


       * DElete [filename]
       Deletes  the file.  If  no drive/path  is  specified,  the default
       directory is the WORKDIR path. Wildcards are not  allowed.  If the
       filename  is not  specified, TSTHost  provides a  screen window for
       the selection.








       TSTHOST v1.39 (c) IK1GKJ                                     40


       * DIR
       Directory  display  in the screen window. The directory start from
       the WORKDIR directory.


       * DISconnect
       Disconnects the station.


       * ECho [on|off]
       If enable,  the  text entered from the keyboard is also written in
       the receive window,  in the receive buffer and (if active)  in the
       capture file.


       * EXIT
       Quit from program. No connected channel is disconnected.


       * FUnction function_key(1-20) [command.....]
       It   is   possible   to  define ten  commands (up  to 80 characters
       long)  that will be executed by depressing the keys  CTRL + F1/F10.
       Issue  the   command  with  the  function key number to display the
       current  assignment. For  instance,  FU 1 CON IK1MSL-8  assignes to
       CTRL-F1   the  connect command to IK1MSL-8. Value from 1 to 10 will
       be  associated to  CTRL-F1..F10, value  from 11  to  20  to  SHIFT-
       F1..F10

       * Help or ?
       Displays a command list.


       * LOg [on|off]
       Enables/disables the connection  record  log,  saved  in  the file
       TSTHOST.LOG  in the  program directory.  Every  line  in  the  file
       contains  the callsign,  time and  date   for any  connection   and
       disconnection.   To avoid that this  file  grows  too much,  it  is
       suggested   to   move   and   rename  the file in another directory
       for further storage every month.

       NOTE:   the  file   data  is   valid  only   if   connections   and
       disconnections  happen   while   the programs are active (including
       the  shell command  RUN). If  the program  starts while  the TNC is
       already  connected, the  missing data  are logged  in the  file  as
       question marks (??).









       TSTHOST v1.39 (c) IK1GKJ                                     41


       * PARam channel text
       Use   this   command  with care,  only if  you know  very well  the
       WA8DED  host mode software. This command set a specific value for a
       channel  or   an    extended  command  not  included  in  the  AX25
       subcommands  using the   host  mode commands,  and the  data is not
       checked  by TSTHost.  It is  used for  particular settings  or non-
       standard  Eproms. The  user is responsible  for  any  data  sent to
       the  host interface.  The global communication  channel  is  number
       0,   the   others   from   1   to  8 correspond  to  the eight task
       windows.  Notice that  data written  on channel  0 is stored as the
       default,   while   those   written  on  the other channels are used
       until  the next  disconnection on  the channel  and return  to  the
       channel 0 default value.


       * PASsword
       Automatic transmission  of  the  requested  password.  Support the
       standard  request and  the MD2  algorithm. It  is also  possible to
       send the password with the ALT_F1 key.


       * RECord filename | off
       Captures to a disk file the task activity. The file  logging stops
       with  the OFF  filename or with the task  disconnection. The status
       line  displays the  disk file  size  and  not  the  received  bytes
       number  because   logging to  an existing  file appends data to the
       end of the file without deleting the previous text.

       To  send the  data to the printer, instead of the disk file, RECord
       to a DOS device name (LPT1 PRN etc); REC OFF disables the printer.
       It  is not  suggested to  print a  heavy and fast traffic on a slow
       printer,  as this  can slow  down the whole system. This command is
       not active in a PMS session.


       * REName old_name new_name
       Change  the name for the specified file. Wildcards are not allowed.
       The   default  directory is  WORKDIR. It is possible to move a file
       in  the same  disk to  a different  directory by specifying the new
       path. For instance:

            REN  pippo.txt pluto.txt
                 The file pippo.txt becomes pluto.txt
                 The file remains in the default directory.

            REN  e:\bin\utils\vp.exe e:\bin\vp.exe
                 moves the file vp.exe from the path e:\bin\utils into
                 e:\bin






       TSTHOST v1.39 (c) IK1GKJ                                     42


       * RUn [filename]
       Executes  the  Filename  DOS  program. If  the program name is not
       specified, the command interpreter (COMMAND.COM) is run  until the
       EXIT   command,   that   returns  to  TSTHost. The TSTHost activity
       is suspended while executing DOS programs.


       * SEnd [filename | OFF]
       Sends the specified file to the connected station. OFF  closes the
       file, or  it  is closed at the end of the file or when the task is
       disconnected.  The file  must contain  ASCII text  and  not  binary
       data,  and the  SEnd command cannot be issued in a PMS session. The
       status  line   counter   displays the  number of  bytes sent to the
       TNC,   so the file  can  be  closed when the TNC still have data in
       the  buffer  to  be  transmitted.  If  the    filename    is    not
       specified,  a  selection window is displayed on the screen.


       * SOurce filename
       Executes  a command  file. The  file contains  the commands  in the
       same  form   as   for   the    keyboard.    Each  line  (up  to  80
       characters)  must contain  a command.  The source  file is searched
       ONLY in the  program directory.


       * TNCDelay X Y
       This   command   set  some program timings, that you shouldn't need
       to  change. The  values are  expressed in  18th of  second and  the
       range is from 3 to 255, that correspond to 2 tenth and 14 seconds.

       The  X parameter  is   the maximum  delay for the TNC reply. If the
       TNC  does   not   reply to  TSTHost   in  the  specific  time,  the
       program  retries to synchronise the serial port. The Y parameter is
       the speed for the serial port synchronisation.

       If   your  Y parameter  is too  high, you  can go  to have a coffee
       while  the program  resynchronises! You  must  increase  X  to  fix
       frequent  timeouts, and  Y if  the program cannot resync the serial
       port.

       To   display   the   current  values  of  the  timings,  issue  the
       command without parameters.


       * UList subcommand command
       Command  for FBB  Unproto list,  read   the   specific  section  in
       this manual.







       TSTHOST v1.39 (c) IK1GKJ                                     43


       * View [filename]
       Display  the contents of an ascii file, predefined path is WORKDIR.
       If  you do  not provide  a filename,  a selection is made in window
       mode.


       * WOrkdir [path]
       Set the default work path for TSTHost.  Usually, it corresponds to
       the  directory where  the program  is stored.  When a filename does
       not  have a  drive/directory path,  it will  be   searched  in  the
       WOrkdir directory.


       * WRitebuf filename
       Writes  the contents  of the  receive buffer in an ASCII disk file.
       If  the filename does not have a drive/directory path specified, it
       is saved in the WOrkdir directory.


       * YABort
       Starts the procedure to interrupt the YAPP transfer protocol.
       The  interruption is  not immediate  because the  terminal  station
       must  empty   his   buffer   before   accepting   the   command. To
       perform  an immediate abort, type this command TWICE.


       * YAPpc [on|off]
       Enables/disables  the YAPPC  protocol version.  You  cannot  change
       this option if there is any YAPP file transfer active.


       * YRec filename
       YAPP  receive protocol  manual  start.  If  Autoyapp  is  on,  this
       command  is not  requested. If  Autoyapp is  off, you  must execute
       this  command just  after having  received by the connected station
       the   Init  YAPP transmit  code. If  the filename  does not  have a
       drive/directory  path specified,  it will  be saved  in the WOrkdir
       directory.  This command is not active in a PMS session.


       * YPut [filename]
       Start  the   YAPP transmit  protocol. If  a drive/directory path is
       not  specified, the  file is  taken  from  the  WOrkdir  directory.
       This  command is   not  active   in a  PMS session. If the filename
       parameter is not specified, the program activates a select window.









       TSTHOST v1.39 (c) IK1GKJ                                     44


       AX25 Subcommands
       ----------------

       These   parameters   must   follow  the AX25  command, for instance
       AX25  MONITOR N.  The TNC manual reports  more  informations  about
       these commands.


       * AX25l2v2 [On|Off]
       Enables the level 2 of the Ax25 protocol.


       * Beacon [0-60] [Beacon Text | <Beacon file]
       Set   the   beacon   text.  The time value is expressed in minutes,
       and  any value  below 5  disables   the   beacon.    If  the  first
       character  of the   beacon   text   is '<', then the others are the
       text  filename. If  no drive/directory  is specified, then the file
       will be  searched in the TSTHOST.EXE directory.

       Example for text beacon:   AX BE 30 ST. IK1GKJ * IJ45IK
       Example for file beacon:   AX BE 30 <F:\UTILS\BEACON.TXT


       * Check [0..65535]
       After  this time,  if was  not detect  traffic on  the channel, the
       program test the integrity of the link. In 10ms.


       * CLock ON | OFF | SET
       The SET parameter sets the current time/date on the TNC.
       ON enables the time/date display in the monitor window and  in the
       status  messages, OFF  disables this  time/date display.  NOTE: Not
       all  TNC EPROMs  accept this  command; it  works fine  on TF24  and
       TF26.


       * Digipeat [On|Off]
       Enables/disables the digipeating capability of the TNC.


       * FRack [1..65535]
       Pause  (if ACK  has not  been received)  for the TNC before sending
       the  data packet  again. This  value can  be from  1 to 15 seconds.
       Some  TNC EPROMs  accept valid  data from  16 to  65535,  expressed
       in 1/33  of second.


       * FUllduplex [On|Off]
       Enables/disables the full duplex transmission of the TNC.





       TSTHOST v1.39 (c) IK1GKJ                                     45


       * MAxframe [1..7]
       Max number of data packets to transmit before waiting for ACK.


       * MHeard [ON | OFF | CLR 3..MAX]
       Without parameters, displays the list of the received stations.
       CLR clears the list.
       ON  enables the list automatic update.
       OFF disables the list automatic update.
       The  list size,  set by  CLR, must be a value between 3 and the max
       supported  by the  tnc, but  warning, since  the mheard list is not
       maintained  in memory, but only displayed, you you ask for a number
       greater  than the  screen dimension, due to the scroll you may lose
       the  first callsign  displayed.  Warning:  This  command  has  been
       tested  with EPROMs  TF24 and  TF26, but  not any EPROM accept this
       command.


       * MYcall callsign
       Set my callsign.


       * MOnitor [NIUSC] [+- callsign callsign...]
                           N disable
                           I display I  Frames
                           U display UI frames
                           S display Supervisory frames
                           C display Connections frames
                           + Include max. 8 callsign
                           - Exclude max. 8 callsign


       * PAclen [80..250]
       Byte size of the transmitted packet.


       * PErsist [0..255]
       Transmit  chance. When   the  TNC  must transmit data, it generates
       a  random   number between 0 and 255.  If the number is higher than
       the  PErsist value it can transmit, otherwise  the  TNC  must  wait
       for SLottime time before generating a new number.


       * POrtcall [channel 1..8] [call|OFF]
       This  command  assigns  a  different  SSID  or  callsign  for every
       channel.   The  command without  parameters displays  the  list  of
       those  channels with  a callsign  different from  the  AX25  mycall
       value.  OFF   sets  the  channel  to  use  the callsign-ssid set by
       the AX25 mycall command.





       TSTHOST v1.39 (c) IK1GKJ                                     46


       To   activate   the  default callsign, use the OFF parameter. Note:
       a  channel with  a particular  callsign will  not  change  even  by
       changing  the global callsign. To disable the extended callsign use
       OFF.  This command  has effect,  for a  connected  channel,    only
       after  the disconnection

       Example: AX25 MYCALL IK1GKJ     AX25 PORTCALL 2 IK1GKJ-2


       * PTt [ON | OFF]
       Enables/disables the TNC PTT line. The  software  works correctly,
       but, while in the OFF state, the TNC  does  not  activate  the PTT
       line.


       * RESptime [0..65535]
       Wait time before ACKing an incoming packet, in 10ms.


       * RETry [0..127]
       Retry  number before  failure and  station disconnection.  0 stands
       for forever.


       * Slottime [0..127]
       See PErsist, in 10ms.


       * Txdelay [0..127]
       Delay   before   data   transmission after the PTT line activation,
       in 10ms.


       * UNproto [text]
       Unproto text and route where the Unproto messages are addressed.


       * USers [0..8]
       Max number of incoming connections.


       * Validcall [On|Off]
       Enables/disables the valid callsign control.











       TSTHOST v1.39 (c) IK1GKJ                                     47


       THE STATUS LINE
       ---------------
       From the bottom to the top of the screen:
       The  last screen  line displays  the channel  status, the number of
       bytes  transmitted for  send file,  the disk file size for incoming
       text  capture. Only  the TNC  status and the number of free buffers
       are displayed for Monitor and Unconnected channels.

       * FR is the number of free buffers in the TNC (or TFPCX/R driver).
       Every buffer contains 32 bytes. This values helps detecting if the
       TNC   is   collapsing,   as  the Host software disables the monitor
       if  this value  is under  256. The  TNC collapses  when the  FR  is
       around  128. Among   the   various   reasons,  check the high speed
       traffic  and slow    serial   connection  baud rate,   the  monitor
       active   with  multiconnection, etc.  The free  buffers   value  is
       global and not referred to a single channel.

       *  BF is  the number  of packet  in the TNC queue to be transmitted
       for  the channel.  TSTHost has a ten buffers queue. If the FR value
       drops  below 300,  the queue  is reduced to 5, and if FR goes below
       210 then the queue is reduced to 2.
       This  function does  not  interfere with the MAXFRAME 7 parameter,
       since the correct number of packets is BUF+UNACK.

       * UN is the number of packets transmitted still to be confirmed.
       This value depends on AX25 maxframe.

       * RE is the time of the TNC attempts to  transmit  the  unack data
       without   receiving   ACK   from   the   other  station. After AX25
       retry value, the station will be disconnected.

       * US is the amount of memory used by the system

       * OK is the free memory in the system

       * TX is displayed only by sending a file. This value is the number
       of bytes read from the file and  transferred intothe TNC. When the
       file transfer terminates on the PC side,  it  can  still  continue
       because of the TNC buffer.

       * RX is displayed only when the RECORD command is active, and this
       value corresponds to the disk file size.

       Next line up on the screen  displays the TSTHost status:  CONV for
       conversation  mode   (typed data  is sent   to  the other station),
       CMD   for  command   mode  (enter   commands  for   TSTHost  to  be
       interpreted).  On the  right side  there  is  the  current  channel
       number and the callsign and duration of the active connection.






       TSTHOST v1.39 (c) IK1GKJ                                     48


       Then there is  the  program  version.  REVIEW  indicates  that the
       revision  buffer is  activated (PageUp  key);   PMS for the channel
       set in a PMS session (default) or active in a PMS session.

       Above  these lines,  there is  a line  containing the  callsign for
       each  connected channel, from 1 to 8. If there is new data that you
       have not yet read from a channel, TSTHost will flash the callsign.

       Another line is for the YAPP transfer status line, active  only if
       the channel is running a YAPP file transfer.





















       PROBLEMS
       --------
       Please   report  any   kind of   problem or  defect with  a message
       to
       IK1GKJ@IK1MSL, reporting:

       - Defect type.
       - Which operation you have done when you have noticed the defect.
       - PC model and configuration
       - Memory driver (EMM, QEMM etc.)
       - PC Operating system version.
       - (If possible) the TSR programs loaded in memory.
       - TNC model and driver type

       Thanks.








       TSTHOST v1.39 (c) IK1GKJ                                     49


       Features ........................................................1
       Tsthost with TNC in KISS or BAYCOM modem ........................3
       Tsthost with the standard HOST mode .............................4
       Tsthost with 2 or more tnc ......................................5
       Memory usage ....................................................6
          Expanded memory and /NOEMS command ...........................6
          Reduction of RX buffers, /Rsize command ......................6
       VGA mode ........................................................7
       Short cut keys ..................................................7
       Path of the files ...............................................8
          PG - Server directory ........................................8
          MAIL - Messagges directory ...................................8
          USERS - Users directory ......................................9
          UPLOAD - Users upload directory ..............................9
          WORKDIR - Standard work directory ............................9
          TSTHOST.PSW - Automatic password file ........................9
          TSTHOST.SYS - Password file for PMS SYS command. .............9
          TSTHOST.CFG - Automatic configuration file ..................10
          TSTHOST.SHD - Shutdown configuration file ...................10
          TSTHOST.ULS - Unproto list file .............................10
          TSTHOST.ENT - PMS connection text ...........................10
          TSTHOST.HLP - PMS help file .................................11
          TSTHOST.PGS - PMS PG server list ............................11
          TSTHOST.LOG - Connections log ...............................11
          SOURCE files ................................................11
          TSTHOST.BID - Bid file. .....................................12
          TSTHOST.IN - Mail import file ...............................13
          TSTHOST.DMS - PMS messages database .........................14
       FORWARD,  UNPROTO  list,  CHANNEL  8  and (optional) automatic
              password request. .......................................15
          FORWARD protocol ............................................17
          Problem to connect for UNPROTO and FORWARD ..................18
       FORWARD command ................................................19
       PG SERVER ......................................................21
       AUTOMATIC PASSWORD .............................................23
       PMS INTERFACE ..................................................24
          THE SERVER ..................................................25
          THE SCROLL LOCK LED FLASH, MAIL IN SCREEN, /NOLED COMMAND ...25
          PMS command from KEYBOARD ...................................26
          PMS commands for remote users ...............................31
       UNPROTO LIST ...................................................34
          IMPORTANT NOTE ..............................................35
          UList Subcommands ...........................................36
       TSTHost commands description ...................................38
          Send,Delete,Dir,Yput,View parameter window ..................38
          AX25 Subcommands ............................................44
       THE STATUS LINE ................................................47