VK3UM INTERFACE BOARD DIAGNOSTIC CHECK-OUT

Firstly it cannot be more strongly emphasized that the printed circuit board 
is 100% and should you find that the interface does not work then it is 
something other than the board.

In all but one case, (a component placed in a wrong hole) most faults have
been caused by faulty IC's. The most common have been the 74LS00, 74LS05 and
74LS08. One board I have repaired was due to solder bridges between tracks!
The guy must have used a kilo of solder and a 1kW soldering iron!!!

I have also been asked about the timing aspects of the board. No it is NOT
critical and the components need not be precise. 5% is more than adequate
as the design is quite broad. Accordingly the pulse widths as described
here under are typical and a 5% variation (apart from the clock) may be
seen.

I have been at a loss just why some people have bought faulty IC's. In this 
country I have been fortunate? to have not run into the problem. It seems to 
be associated with European suppliers but all I can say is to be careful that
you obtain your IC's from a reliable source. They (the 74LSxx) only cost cents.

The design of the board is NOT repeat NOT critical of IC tolerances. Just
make sure that the IC's you get work in the first place!!!!!!

The decoding is fairly complex and should you run into a problem a single
faulty IC will totally upset the logic and the board will not work. Two
faulty IC's make the task even more complex.

Note    It is NOT necessary to install Relays RL7-8, transistors T7-8,
        Diodes D7-D8, Resistors R7-8 and R15-16 to make the board function.

Here is an overview of how to go about isolating your problem.
Note IC11/1 refers to Integrated circuit number 11 pin 1 for example.

1. Double check your IC orientation.
   All of the vertical IC's, pin 1 should be to the top/left of the board.
   (relays are at the top).
   All of the horizontal IC's, pin 1 should be to the left/bottom of the
   board.

2. The relay driver transistors. T1-T8. Make sure that the flat is pointing
   to the bottom of the board.

3. The diodes across the relays (D1-D8) have all their bands to the top of
   the board.

4. Check the polarity of the tantalum capacitors with the layout. Note that
   C20 and C21 run in opposite directions.

5. Check the polarity orientation of the remainder of the diodes. D9 and D10
   have their bands to the top of the board whilst with D10 the band is
   closest to the bottom of the board.

6. Check for the correct location of components between IC10 and IC11 as well
   as between IC11 and IC12.

7. When applying power check the total current drawn as measured WITHOUT the
   regulator (ie the +5v rail) will be between 170-190mA with NO RELAYS
   operated. If it is greater than this you most likely have IC problems and
   a quick check with your finger will locate the hot faulty chip and burn
   your digit!! Be careful!!

   NO RELAYS WILL BE OPERATED WHEN THE BOARD IS FIRST SWITCHED ON.

8. Run the software and select the Pulse Mode.
   Again NO RELAYS SHOULD BE OPERATED UNTIL the Up/Down and CCW/CW keys are
   selected. Each additional relay will increase the current drawn by
   approximately 200mA. ie if two relays are operated the total current drawn
   will be 570-590mA. Again this is a function of the relays chosen.

9. If the relays do not operate you have a problem!!! You will now need a 
   logic probe or a Cathode Ray Oscilloscope, and most assuredly a 
   replacement IC or two !!!!!!!

10. Baud Rate Oscillator.
    IC19/7 (pin 7). You should see 5v square wave with a pulse width of 
    2.75uS. This will also appear on IC1/40, IC1/17 and IC20/10. If it is
    not present then check around IC19 as it is not oscillating!

11. Are you sending data to the interface? 
    Have you selected the correct COM port and plugged it into the right 
    socket of your computer?  Now look on IC2/13 and you should see Data 
    coming from the computer of approx 26v p-p positive going pulses.
    If you cannot see the data then you have the wrong RS232 connection or 
    the wrong COM port selected.

12. Is the MAX232 IC outputting the data?
    Check IC2/12 and you should see the reverse of 11 above but at 5v p-p.
    The pulses will be going negative. If not then you have a faulty IC2 or
    the components around this chip maybe incorrectly placed.

13. IC3/5. You should see +5v positive going pulses 47uS wide repeated as
    seen in 12 above. If this is not true then IC3 is faulty or even IC1
    (very unlikely). Check around IC3 for problems.

This is where it becomes tricky as all the following IC's are interlocked and
it is not possible to diagnose the exact IC if one is faulty. However the
following checks will help to a considerable extent. In any case the faulty
IC or IC's will be one or more of  IC's 7-14.

14. IC10/13, IC4/1 and IC11/1 should all have the same wave form. This is in
    the form of +ve going pulses 25uS wide similar to that seen in 12 above,
    HOWEVER each time the Up/Down or CW/CCW keys are pressed you will see an
    additional pulse.

15. IC11/3. In the normal state there will be 0v raising to a +5v pulse 25uS
    wide each time a key (refer 14) is pressed.

16. IC13/12 will be the reverse of 15 above. That is +5v normally, with a
    negative going pulse.

17. Relay selection and decoding.
    IC11/11 and IC6/9 you will see a +ve 5v pulse 25uS wide each time the up
    or down keys are selected. IC11/8  and IC5/9 will show the same pulses
    when the CW or CCW keys are selected.

18. Relay drivers.
    The normal state of the following conditions is 0v raising to +5v and
    holding at this voltage whilst the motor direction is on. The respective
    relays should operate.
    CW   IC5/2   0 ---> +5v   seen also on RHS of resistor R1
    CCW  IC5/15  0 ---> +5v   seen also on RHS of resistor R2
    Up   IC6/15  0 ---> +5v   seen also on RHS of resistor R3
    Down IC6/2   0 ---> +5v   seen also on RHS of resistor R4
  Failure to see the above indicates a faulty IC 5 or 6 or transistors T1-T4.

Well that's about all I can do to help at this distance. I include this file
for those unlucky enough not to have the board run first go.

Remember that if you are using a Pulse Mode input then it has to be held high
(+5v) and go low to count.

It's no use me saying that I and many others have not had any problems if YOU
are reading this and HAVE a problem!!!

Hopefully this document will enable you to find the trouble fast!  I know I
am repeating myself when I say the fault is most likely an IC!!

If all else fails post it back to me (with sufficient return postage!) and I
will fix it for you !...................

Regards

Doug McArthur (VK3UM)


February 1993