DOCUMENTATION HANDBOOK

                          VK3UM AUTOTRACK

                       Version 5:10 Nov 1993

INDEX

     Para  Section                                    Page
     1.0   Introduction ............................... 2
     2.0   Hardware requirements ...................... 3
     3.0   Software requirements ...................... 3
     4.0   Main Menu .................................. 4
     5.0   Main Menu Options .......................... 4
     6.0   Tracking Modes ............................. 4
           6.1  Real Time Track ....................... 4
           6.2  Auto Track ............................ 5
           6.3  Graph Track ........................... 6
     7.0   General Set Up ............................. 10
           7.1  Home Location Change .................. 11
           7.2  Summer/Winter Time .................... 11
           7.3  Operating Frequency ................... 11
           7.4  UTC/Local Computer Time ............... 11
           7.5  Display Source Target ................. 11
           7.6  Transmit Sequence ..................... 11
           7.7  Period of Transmission ................ 11
           7.8  Warning Sound On/Off................... 11
           7.9  Save Set Up parameters ................ 11
           7.10 Change Computer Time .................. 11
     8.0   Auto Track Set Up .......................... 11
           8.1  Mode Selection Analog/Digital/Pulse ... 11
           8.2  Digital Set Up Parameters ............. 12
           8.3  Analog Set Up Parameters .............. 12
                Motor Run On .......................... 12
           8.4  Pulse Set Up Parameters ............... 12
           8.5  Home (Park) Position of Antennae ...... 14
           8.6  Azimuth Motor Hysteresis .............. 14
           8.7  Elevation Motor Hysteresis ............ 14
           8.8  Drive Update Period ................... 14
           8.9  End Stops of Antennae ................. 14
           8.10 Communication Port .................... 15
           8.11 Antennae Mount ........................ 15
           8.12 Motor Speed Control ................... 15
           8.13 Save Parameters to Disk ............... 15
     9.0  Printed Circuit Board Interconnect .......... 16
    10.0  Component List and Sources .................. 18
    11.0  Check Out Procedure ......................... 20
    12.0  Summary ..................................... 22
          12.1  Printed Circuit Board Changes ......... 23
    13.0  ADDENDUM OF FUNCTION KEYS USED .............. 23
          13.1 Real Time Track Screen ................. 23
          13.2 Auto Track Screen ...................... 23
          13.3 Graphic Screen ......................... 24
          13.4 Target Screen Options via [F2] ......... 24

1.0 INTRODUCTION

       The Software was developed primarily as an aid for Amateur
       Radio Operators wishing to communicate by reflecting
       signals off the Moon. This communication mode is commonly
       referred to as EME. (Earth -Moon - Earth).

       The facilities provided by this software, when used with
       the VK3UM Serial Interface controller attached to your
       Computer, will allow you to automatically track the Moon,
       (or any other Quiet or Noise Source).

       The Software and Hardware has been designed to suit Analog,
       Digital and Pulse Tracking Systems and may be used in both
       Hemispheres.

       Facilities are provided to Graph Noise, and Moon Echos. You
       can also store these graphs on disk and recall them at a
       latter date. Moreover the graphs may be overlaid for
       comparison purposes. Printing of these graphs has also been
       provided. Help instructions are available for graphic
       facilities via [F1] within the Software.

       The Software is quite complex and is an on going project by
       the author. Not all the Authors' proposed facilities have
       been included at this stage (Automatic Polarisation
       Tracking for example). Accordingly when revisions become
       available they will be announced and distributed at a
       moderate cost. All options described in this document apply
       to this version of the software.

       It should be clearly understood that this Project is for
       Amateur purposes and should any bugs be found or you have
       suggestions for improvement please convey your
       correspondence to the following :

                 Doug McArthur (VK3UM)
                 30 Rolloway Rise
                 Chirnside Park
                 Victoria 3116
                 AUSTRALIA

       Home Phone        (61 3 7264484)
       Work FAX - 24Hrs  (61 3 7286464)  ** Inwards Only **
           Note. I am +10 hours ahead of UTC.

       Again I stress that this is an Amateur project developed on
       a cost covered basis for the advancement of our Hobby.
       Unlike my EME PLANNER SOFTWARE that has been distributed
       free for many years, the cost of the very complex interface
       board has to be covered.

2.0 HARDWARE REQUIREMENTS

       This Software will only run with the associated Interface
       board. The board is complex and contains 20 "standard
       IC's", 8 miniature relays and transistors plus an
       assortment of capacitors and resistors. Because of the
       complexity it was decided to produce the board as a plated
       through hole (980!) fiber glass identity. A parts layout is
       provided to clearly identify placement of components. A
       circuit has not been provided as such is deemed unnecessary
       due to the simplistic nature of construction. It is
       recommended, but not essential, that IC sockets be used.
       Input and output connections are via standard IDC
       connectors. It is left to the user to package the unit as
       desired. A +5v regulator has been provided on the board (as
       well as reverse supply protection) for those that wish to
       feed the unit with an unregulated +7 - +10 volt supply.
       Total current, which is dependent upon the number of relays
       operated at the time, is approximately 350mA.

3.0 SOFTWARE REQUIREMENTS
       IBM or a compatible XT/AT/286/386/486 configuration is
       necessary. The Graphic options used for graphing requires a
       EGA or VGA driven monitor. Auto Track is provided for
       monochrome, Hercules and CGA monitors however the extra
       graphing facilities are not available with these monitors.
       The software is "downward compatible" to EGA for higher
       resolution screens. (350x640 16 Colors). The program
       requires approximately 330k RAM to run.

NOTE  IF YOU DO NOT HAVE THE INTERFACE CONNECTED AND YOU WISH TO
      RUN THE SOFTWARE THEN SELECT THE REAL TIME TRACK OPTION.
      THEN PRESS THE HOME KEY AND THE SOFTWARE WILL BE CONFIGURED
      TO THE DEMONSTRATION MODE.

      This will select the Pulse Mode with internally generated
      Pulses. To return to interface control exit the program and
      re-boot.

3.1.1  Software/Hardware Debugging Functions.
       These can only be selected from the Auto Track Screen but
       are used in the graphics screen.

3.1.2  [F1]. When in the AutoTrack Screen and when using the Pulse
       Mode, this will enable the display of Azimuth and Elevation
       Pulse Counts. Pressing [F1] again will disable this
       display. This is a useful option when calibrating your
       Pulse System if you are unsure of the number of pulses per
       degree. (pulses per 360 degrees is required to configure
       your input for the pulse mode). This is achieved by first
       turning on the pulse counter and running your drive over a
       known number of degrees of travel. The pulse count will
       indicate the number of pulses for that travel. Multiply the
       number of pulses by the number of degrees and you have the
       pulses per 360 degrees required in section 8.4. Note you
       can input decimal degrees.

3.1.3  Control[F1] will reset the Pulse Counter.

3.1.4  Shift[F1]. When in the AutoTrack Screen and when using the
       Pulse Mode, this facility will generate simulated pulses
       from within the Software without the need for an external
       pulse input. The one hundredth digit will turn red when
       internally generated pulses are selected. Pressing
       Shift[F1] again will return the control to the external
       pulse input. This facility can be used as a training aid to
       become familiar with the software and all the options
       provided.

4.0 MAIN MENU.
       After the opening Logo Screen the Main Menu Headings are
       displayed. The following sections provide the user with the
       information necessary to configure and interface your
       system to the hardware. Please read this carefully as the
       software is most comprehensive and abounds with many user
       options. The [F1] key provides the Version Number of the
       Software.

5.0 MAIN MENU OPTIONS.
       Selection of these options may be achieved by either moving
       the highlighted bar with the cursor keys (arrow keys) or by
       typing the first letter of that option required. For
       detailed description please refer to the following
       sections:-
         6.0 Tracking Modes.     7.0 General Set Up.
         8.0  Auto Track Set Up.

6.0 TRACKING MODES.
       Before running the various tracking modes please set all
       your parameters to suit your Station as detailed in
       Sections 7.0 and 8.0. This Sub Menu enables selection of
       the Tracking Mode desired. The Real Time Track option
       provides the location of the Tracking Source commensurate
       with your Computer Clock. The Auto Track Modes, in
       association with the Serial Interface, enable the automatic
       or manual control of the antennae.

6.1 Real Time Track.
       This option provides real time (Computer Set Time),
       calculations of Azimuth, Elevation, Doppler Shift for any
       "Tracking Source" (Moon - Sun - Noise), which may be chosen
       from General Set Up Sub Menu or [F2] from within this
       screen. This mode does not allow for automatic Antennae
       control as is provided in Auto Track. It does provide
       Azimuth/Elevation and Doppler Shift of the "Tracking
       Source" relative to your location and Computer Time. The
       screen will indicate both the Transmit (red) and Receive
       (blue) periods and sound a warning prior to the change over
       sequence. The Tx Sequence and Period as well as the bell
       may be set as desired in the General Set Up Menu. (refer
       7.6 and 7.7).

6.1.1  [F2] key will allow you to select any of the available
       Target Sources available. The [TAB] key allows you to
       select additional noise sources.

6.1.2  [F3] key will allow you to input a DX Station's Grid
       Square. This will then provide a display, in the centre of
       the screen, of the Azimuth, Elevation, Doppler Shift and
       Spatial Offset of the distant station. The latter two
       displays will only be present if you both have coincident Moon.

6.2 Auto Track.
       This option provides Auto Tracking of any Target Source
       provided in the EME Software. The Auto Track Setup Menu
       allows you to configure the Software to suit both the
       Hardware Interface and your own specific Station
       requirement. The Antenna will then track the Target Source
       or you may manually steer the Array as desired.

6.2.1  [F1] will this will enable the display of Azimuth and
       Elevation Pulse Counts. This is a useful option when
       calibrating your Pulse System if you are unsure of the
       number of pulses per degree. This is achieved by first
       turning on the pulse counter and running your drive over a
       known number of degrees of travel. The pulse count will
       indicate the number of pulses for that travel. Multiply the
       number of pulses by the number of degrees and you have the
       pulses per degree and then translate this to the number of
       pulses per 360 degrees as required in section 8.4. Note you
       can input decimal degrees but the greater the travel will
       provide a higher order of accuracy. Pressing [F1] again
       will disable this display. (Pulse Mode only).

6.2.2  Shift[F1] will generate simulated pulses from within the
       Software without the need for an external pulse input. The
       one hundredth digit will turn red when internally generated
       pulses are selected. Pressing Shift[F1] again will return
       the control to the external pulse input. This facility is
       most useful as a training aid to become familiar with the
       software and all the options provided. (available only for
       Pulse Mode of operation).

6.2.3  Control[F1] will reset the Pulse Counter. (Pulse Mode only)

6.2.4  [F2] key will allow you to select any of the available
       Target Sources available or input a Azimuth Bearing. The
       positions of all the Targets are available on screen.
       This facility will also permit using a beacon as a source and
       plot a beam pattern or position the array to a known Az / El
       for Auroa or FAI transmissions. In addition you may input a Grid
       Square for terrestrial purposes. The software provides you
       with the Azimuth bearing and distance.

6.2.5  [F3] key initiates the Automatic Tracking functions. When
       in the automatic tracking mode ANY key will disable the
       automatic tracking and return you to Manual Tracking.

6.2.6  Shift[F3] allows you to input a DX Station's Grid Square.
       This will then provide a display, in the top left hand
       corner of the screen, of the Azimuth, Elevation, Doppler
       Shift and Spatial Offset of the distant station. The latter
       two displays will only be present if you both have
       coincident Moon.

6.2.7  [F4] key will automatically park your antennae to the home
       position as defined by you in the Auto Track Set Up Menu.
       (refer 8.5).

6.2.8  [F5] key allows you to re-calibrate your antennae readout.
       Simply enter the new headings to change your display.
       (Pulse Mode only).

6.2.9  [F6] key allows you to transfer your Target source bearings
       into your Azimuth and Elevation antennae headings. This can
       be very useful should you be unsure of your headings. If
       for example, you are tracking the Sun and find that the
       peak Noise heading is different to your beam heading you
       can then transfer the Target to your own beam headings
       (Pulse Mode only).

6.2.10 [F7] key allows you to save your current indicator Azimuth
       and Elevation readouts. This allows you to leave your array
       where you would prefer without driving it to the set park
       position. You may then turn off your computer and recall
       your previous position by the Shift[F7] key. (Pulse Mode
       only).

6.2.11 Shift[F7] key allows you to recall your previously stored
       Azimuth and Elevation Indicator position. When initiating
       the program enter into the Auto Track Screen and hit
       Shift[F7]. The programed Park position will be changed to
       the "Temporary Parked" position as previously stored.
       (Pulse Mode only).

6.3 Graph Track. (Requires EGA/VGA Monitor)

       This is the real heart of the Software and provides
       advanced facilities to check your system and to perform
       accurate and or scientific measurements. It is this area
       the author has concentrated his efforts.

       The options provided by Graph Track allow you to select
       many sources and:
          (a) automatically position the array and then graph
              either E or H Plane polar patterns.
          (b) calculate the Antennae Gain and beam angle directly
              from the screen. You can calculate gains either
              separately or as a composite gain figure.
          (c) graph your Moon echos.
          (d) obtain a time domain/amplitude plot of received
              signals.
          (e) Utilize the received signals to perform rudimentary
              Digital Signal Processing and recover the actual CW
              signal and play it on the internal computer speaker.

          (f) Sample a noise source and display level variations
              on an expanded graph.

       As with all the above facilities the Graphs may be stored
       on disk and later retrieved (overlaid on top of another
       graph and/or printed) for evaluation.

       Whilst in the Graphic Screen help is provided by hitting
       [F1] and stepping through the function key designations.
       (Shift,Alt,Ctrl). The key functions are displayed on the
       right hand side of the screen.

6.3.1  Graphic Screen Options.
       To utilise the Graph Track facilities you must have a
       monitor capable of displaying EGA or VGA. The software is
       "downward compatible" to EGA and will result in a 640x350
       resolution graphics screen. The options are now described
       in function key order.

6.3.2  [F1]. Step through the Function keys accessed from the
       Graphics Option. (Shift,Alt,Ctrl).

6.3.2  [F2]. Select a Target Source. You may select any of the
       Menu displayed options provided. They include the Sun and
       other Noise Sources as well as the Cold Sky areas. The
       Software will then Track your selection. You may also input
       a Azimuth Bearing (set in Autotrack Screen) which will permit
       using a beacon as a source and then plot a beam pattern.
       The [TAB] key allows you to select additional noise sources.

6.3.3  Shift[F2]. This is the DSP option. First load the receiver
       file you wish to analyse with Shift[F10] before hitting
       Shift[F2]. The displayed waveform will change to grey and a
       yellow horizontal line will appear across the screen. This
       line (set level), may be moved to a position representing
       the DSP point. A counter on the left hand side of the
       screen indicates its position.
       [F1] will then translate the signal into a square wave
            representing the level chosen. This will be displayed
            in white.
       [F2] will provide the CW output of this signal via the
            computer speaker.
       [F7] will return you to the set level condition so you may
            alter the level as desired and repeat [F1] and [F2] as
            often as desired.
      [Esc] will return you to the main Graphics menu where you
            may load another file (Shift[F10]).

6.3.4 Alt[F2]. Scan and Track a noise source (eg Sun) and record
       the variations in level over a period of time. After
       hitting this key, if the source chosen is above the
       horizon, the software will position your array at the
       source. If the source is below the horizon plotting will
       commence immediately on the top half of the screen. The
       sampling time is calculated commensurate with your computer
       and is displayed at the bottom of the screen. On the right
       hand side of the receiver input display the peak input
       level is displayed. Your input level should be adjusted to
       indicate 0.0dB (or as near as you can make it), and under
       these conditions the level plotted on the top half of the
       screen (yellow) will be referenced to 0dB. You will notice
       that the display is linear and has a range of +/- 6dB. You
       may check this by placing an attenuator in line with your
       receiver. The input level is in this case the peak level as
       seen by the A/D. Levels greater than or less than 6dB with
       respect to the reference level will clip the plot. If you
       are expecting a variation greater than 6dB then the level
       can be set accordingly (-3 or -6dB for example). At the
       commencement of the scan the time will be displayed on the
       screen. When the scan reaches the far right hand side of
       the display (or you hit any other key to stop the function)
       the end date and time will be shown. The graph display may
       be stored on disk by [F10] or the whole procedure repeated
       with the Alt[F2] key.

6.3.5  Control[F2]. This option allows you to vary the time
       between updating the Antennae heading with the Source when
       using the Scan function. Alt[F2]. The default setting is 30
       counts before updating. You will see the count reducing at
       the end of each scan. When it reaches 0 it will update.
       This function allows the user to input a value commensurate
       with their Antennae Gain (Beamwidth). The maximum value is
       499 which is the full screen width of the display. If you
       choose such a value you will infact plot the beam width
       slope of your array.

6.3.6  [F3]. Position your array for graphing Moon Echos. (Auto
       Track the target in the Graphics Mode). The array will be
       then set to track the Moon. After obtaining Lock you are
       ready to plot your Echos by hitting Shift[F3].

6.3.7  Shift[F3]. Plot Moon Echos. When Lock is obtained with [F3]
       hitting this key will send seven 200mS dashes which
       activate the PTT Relay. Following the last dash and two
       seconds after the rising edge of the first pulse, the graph
       will plot the returned echo on the screen for the next two
       seconds. You will also note that if you wish to plot
       another Echo this will be done in another colour or if you
       chose, you may clear the screen first with [F7]. There are
       4 alternating colours selected automatically by the
       software. This applies to all plotting options except for
       the Receiver Scan functions where only green has been
       provided.

6.3.8  [F4]. Park Antennae. You may Park your Antennae to the
       Azimuth and Elevation positions as chosen and set in the
       Auto Track Setup Menu.

6.3.9  Shift[F4]. Target to Indicator. If you are using the Pulse
       mode of operation this facility allows you to re-calibrate
       your indicator. Manually peak your array on a noise source
       or your Moon Echos and then by hitting Shift[F4] you will
       transfer the Target source Az and El positions to that of
       your Indicator readout. This may upset your Park position.

6.3.10 [F5]. Position for Azimuth. This will position your array
       the number of degrees counter clock wise from your Tracking
       Target (eg the Sun).  The number of degrees offset will be
       that as chosen from the four available scales provided in
       the Change Degree Scale under Shift[F8].

6.3.11 Shift[F5]. Graph Azimuth Noise. After positioning your
       array and obtaining "Offset Lock" with [F5], hitting this
       key will start the Az Drive and plot the Noise on the
       Graphics Screen. The motors will drive through the Target
       and stop at the corresponding Azimuth on the other side of
       the source. Again hitting Shift[F5] (after completing a
       plot), will repeat the plot in the opposite direction in
       another colour.

6.3.12 Alt[F5]. Graph Azimuth Noise. This is the same as Shift[F5]
       except it provides for Non-Linear readouts. If your indicators
       do not produce a linear step (increment in 0, 1, 3, 5, 7, 9
       or similar) then this option should be used to Graph your Noise.

6.3.13 [F6]. Position for Elevation. This option functions the
       same way as for Azimuth as previously explained in option
       [F5] above noting that the array will initially be
       positioned below the Target.

6.3.14 Shift[F6]. Graph Elevation Noise. Again as explained in
       option Shift[F5] the Elevation Noise will be plotted in
       this option.

6.3.15 Alt[F6]. Graph Elevation Noise. Again as explained in
       option Alt[F5] the Elevation Noise will be plotted in
       this option.

6.3.16 [F7]. Clear Graphics Screen. After plotting a graph you may
       clear the screen by hitting this key or continue to "paint"
       another graph, in another colour, over your previous
       graphs.

6.3.17 Shift[F7]. This will calculate Antennae gain and Beam Angle
       after plotting a graph. The 3dB calculation points will be
       shown on the screen as small crosses.

6.3.18 [F8]. Change Degree Scale. This allows the user to select
       the offset Azimuth and Elevation headings from where the
       array will be positioned before commencing to graph noise.
       (Options [F5] and [F6]). The offsets provided are +/- 5,
       12.5, and 25 degrees. In other words if you select +/- 5
       degrees and plot a Elevation noise response the antennae
       will first be positioned 5 degrees below the Target and
       then run through the target and stop 5 degrees above the
       Target. The Azimuth will track correctly.  Hitting [F6]
       again will drive your array downwards and provide another
       plot in a different colour from where you came.  (less
       Target change of position ofcourse!)

6.3.19 Shift[F8]. Change (invert) the dB Scale. Depending upon the
       measurements you are making it is sometimes useful to
       present the display in an inverted format. This option
       provides this function where the dB Scale can be set for
       either 0-30 or 30-0 dB.

6.3.20 Control[F8]. Calibrate input Voltage to the Receiver Input
       A/D. This function will enable you to display your receiver
       input voltage to the A/D converter. It will be displayed as
       a open bar and vary in level commensurate to your input
       voltage. The Maximum voltage will ofcourse correspond to +5
       volts. (0dB reference for noise measurements or +x dB for
       receiver S/N+N level). Press any key to clear screen and
       resume.
6.3.21 [F9] Receiver Scan 10 Seconds. This option allows the user
       to use the graph option to plot the receiver output. This
       is a Time domain/amplitude display referenced to the levels
       as set in Shift[F8] above. The graph will plot the receiver
       for 10 seconds and then stop. Hitting the [F9] key again
       will clear the graph screen and repeat the operation.
       During the scan if you hit any key it will stop the
       operation. You can store this graph and print it out later,
       for inclusion with your QSL of the station you worked!!

6.3.22 Shift[F9]. Receiver Scan 50 Seconds. This option is exactly
       the same as explained in [F9] except the scan period has
       been extended to 50 seconds.

6.3.23 [F10]. Store the Graph to Disk. The default file extension
       has been chosen for you depending upon the graph you have
       just plotted. The program asks you the file name. Remember
       to keep the file name down to 8 letters. The file is then
       stored with the extension associated with the graph.
               Azimuth         xxxxxxxx.AZM
               Elevation       xxxxxxxx.ELV
               Moon Echo       xxxxxxxx.ECO
               Receiver        xxxxxxxx.REC
               Scan            xxxxxxxx.SCN
               xxxxxxxx = user chosen file name.
       The file size is approximately 63kB long so make sure you
       have enough room on your disk to store the file! The Graph
       Plot provided in all the above options also Date and Time
       stamps your plot. This is saved and will be displayed on
       the screen when recalled. It also saves the dB and Degree
       Scales. Note You don't type the extension as this is added
       automatically).

6.3.24 Shift[F10]. Load a graph from disk. This option allows you
       to recall and overlay any file, on any other, or on a blank
       screen. The colours and scales will be the same as those
       stored. The Software will step you through the types of
       files available to which you respond to the one required
       with a "Y". A [CR] or any other key will be a default "no"
       response! After selecting the file type, respond with the
       file name and this will be displayed on the screen! If the
       file does not exist it will tell you so! A Directory of
       files, (in the associated colours), appears on LHS of the
       screen. (in place of the Function help keys).

6.3.25 Alternate[F10]. Print a Graph. This option will print the
       graphics screen on any standard printer with a graphics
       option. You may load from disk the display(s) you wish or
       print direct from the screen.

6.3.26 Control[F10]. This option allows you to Erase a stored
       Graph file. Choose the file type you wish to erase (this is
       colour coded), and simply type in the File Name. The file
       extension is NOT required.

7.0 GENERAL SET UP.
       This Sub Menu provides the default parameters that are
       stored as your own Home Location and are used on start up.
       You may also set the Computer Time from within this Menu.
       Remember to save any changes when you are finished.

7.1 Home Location Change.
       This option provides the ability to input your Home
       Location Data that is used for all calculations and is
       called when initiating the Program.

7.2 Local Winter/Summer Time.
       This option allows you to select either Summer (+1 hour),
       or Normal Time.

7.3 Operating Frequency.
       This option allows you to select any frequency from 50 MHz
       to 24 GHz. It is used for doppler calculations.

7.4 UTC/Local Computer Time.
       This option allows the user to run your Computer Time as
       UTC if desired.

7.5 Display Source Target.
       The user may select either the Moon, Sun or any Noise
       Source for use in the Tracking Mode Routines. It is also
       provided in the other screens.

7.6 Transmit Sequence.
       This option allows the user to select either First or
       Second TX sequencing.

7.7 Period of Transmission.
       The user may select Transmission periods of 1, 2 or 2 1/2),
       Minutes as desired as used in the Real Track Mode.

7.8 Warning Sound On/Off.
       The user may turn off the Warning Alarm as used in the Real
       Time Track Mode.

7.9 Save Set up Parameters.
       This option allows you to save all options to Disk.

7.10 Change Computer Time.
       You may correct your Computer Time with this option. Select
       the highlighted figure you wish to change, with the [arrow]
       keys, and use the [+/-] keys to increment or decrement the
       value as required. [Esc] to exit when finished.

8.0 AUTO TRACK SET UP.
       This Sub Menu provides all the facilities required to
       utilise the Auto Tracking options of the Software. As your
       Station will most likely be different from all others,
       adjust the parameters to suit your particular situation.

8.1 Mode Selection ... Analog / Digital / Pulse.
       This Option allows the user to select the method of
       Computer Interface that is most adaptable to existing
       Azimuth and Elevation Displays.  The available Modes are as
       follows.
        (a) The Analog facility requires a voltage input varying
            from 0v to +5 Volts [Maximum] for both the Azimuth and
            Elevation, (G.H.A. / Dec) displays. The user should
            arrange their system to provide this maximum variation
            for the best resolution. Calibration and scaling of
            the input voltage is achieved from the "Analog Set Up
            Parameters" Menu. Refer connection details P3 Section
            9.0.
        (b) The Digital Inputs [4 per digit] are connected in
            parallel to the Azimuth 000.0 and Elevation 00.0
            displays.  Normal logic levels are required. Refer
            connection details P4 and P5 Section 9.0. Used as
            input for the VK3UM/ZL3AAD Gray Code position
            indicator hardware.
        (c) The Pulse input requires +5v to 0 Volt pulses (50%
            Duty Cycle - use a D Flipflop) corresponding to the
            drive movement of the antennae. The reference starting
            point is the Park position of the Array. The "Pulse
            Set Up Parameter" Menu allows the user to specify the
            number of pulses per degree which then provides
            automatic calibration the display. Key [F5] allows the
            user to Re-calibrate Az and El if required. Refer
            connection details P3 Section 9.0.

8.2 Digital Setup.
       This mode is for Operators that may already have a Digital
       Display attached to some form of decoder. The interface
       allows such a display to be utilised as input to the "VK3UM
       EMETRAK" Software. The Connection for each group of BCD
       lines, (four for each digit) and is designated Hun Ten Uni
       and Dec). The maximum accuracy is 0.1 degree with overall
       Software capable of 0.05 degs. Unused Decimal Degree inputs
       should be tied Low if not required. (Refer Section 9
       Connector P4).

8.3 Analog Setup Parameters.
       This option has been designed to utilise potentiometers
       attached to the Az and El of the Array. It is suggested
       that quality 10 turn potentiometers be employed. It is left
       to the user to design a system to allow a 0v - +5 volt
       variation to be presented at the interface. The 0 and +5v
       should correspond to the maximum range of movement. For
       example should you wish to track from 90 to 270 degrees
       then the maximum displayed resolution is (270-90)/255 or
       0.7 degrees. Accordingly, set both the Az and El to suit
       your needs. The 0v always corresponds to the smaller value.
       Tracking in both hemispheres is automatic from your Home
       Station information and the resolution is computed and
       displayed from your designated range values.

8.4 Pulse Setup Parameters.
       This option has been designed for those who choose to
       employ an optical or a mechanical shaft encoder to generate
       pulses during rotation. The software will count these
       pulses and display the respective heading. Due to the speed
       of the computer there is naturally a speed limitation. This
       is approximately 25 pulses per SECOND for a 4 MHz machine.
       THE PULSES MUST BE 50% DUTY CYCLE FOR MAXIMUM SPEED. LESS
       THAN 50% DUTY CYCLE WILL SEVERELY LIMIT THE SPEED. Note I
       am talking speed of rotation or the number of 50% duty
       cycle pulses sent to the interface from your shaft encoder
       in one second. Do not confuse this with pulses per degree.
       With higher speed machines the figure naturally increases.
       I use the 4MHz machine as a worst case scenario. Always
       check this out first (assuming you are presenting sharply
       defined pulses to the interface) to make sure you are not
       "dropping or missing pulses". The resolution is a function
       of pulses per 360 degrees as defined in this Menu by the
       user. The reference point is set by the Home Position of
       the Antennae as defined by the user. Re-setting is provided
       by [F5] but will void the Home Position. Built into this
       function is the ability to only Track in Azimuth or
       Elevation. The drive you wish disabled should be set to 0
       pulses per 360 degrees. This will inhibit that drive for
       all modes. (Pulse, Digital and Analog). Since February 1993
       Version 2:02, the software has been changed to permit
       Pulses per 360 degrees to reduce possible cumulative
       errors.

This now means that:
         360 = 1.0 pulse per degree,
        3600 = 0.1 pulses per degree or
       36000 = 0.01 pulses per degree.
Other values will permit exact scaling to suit your system. Note
that the input pulse must be negative going as fed to the tracking
interface. A pull up resistor to +5v may be required to achieve
this depending upon the encoder you employ. ie. the pulse shall go
from +5v to 0v to count and held at +5v whilst idle. (RF immunity
design).

Azimuth and Elevation Motor Run-on.
       These options allow for the correction of added pulses
       that are not counted after the motor off command is
       given.  You may input the number of run on pulses by
       implementing the internal pulse counter [F1] (reset by
       [ShiftF1]) and viewing the extra pulses after you stop
       the motor. The extra pulses are added as soon as the
       motor starts and as such will stop prior to reaching
       the true heading. The resultant operation will provide
       for correct tracking commensurate with any motor over-
       run. The maximum number of added pulses is 99. A
       substitute for stopping the motor dead !!  Note.. If
       you require this motor run-on facility then the
       hysteresis factor will have to be increased
       commensurate to the distance travelled. This generally
       means that a hysteresis factor of 3 or more is
       required. Check the hysteresis window, as displayed in
       degrees, with respect to the added run on pulses and
       derive a factor suitable for your needs. (refer 8.6).
       Again problems will be experienced as a result of the
       time the motor is run and the time it will take to
       stop! (an "un-programable" variable!)

8.5 Home (Park) Position of Antennae.
       This facility provides for the parking of the Array
       automatically by the [F4] key. Both Az and El will drive at
       the same time.  Should you be in the tracking Mode this
       will be disabled. The values input here are also used as
       the reference starting point for those using the Pulse
       Input Mode. You may enter a negative value for the Park
       Elevation/Declination. In Auto Track this value will be
       displayed in red to indicate a negative number.

8.6 Az Motor Hysteresis.
       This facility allows the user to control the "window"
       within which tracking will be maintained. If you have a
       motor drive that runs on, (does not stop quickly enough),
       then you may extend the "window" by a multiplication
       factor. This factor, (normally set to 1), is used to
       multiply your tracking accuracy. Set this factor to suit
       your system.
         examples:
          a. If you are running an analog position indicator and
             you are spanning 359 degrees (0 volts = 0 degrees and
             +5 volts = 359 degrees), then your tracking
             resolution = 359/255 or 1.41 degrees. If you choose
             to use a Az Hysteresis Factor of 2 then you will then
             have a window of +/- 2.82 degrees.
          b. If you are running a pulse position system and you
             are using 1 pulse per degree then your tracking
             accuracy is 1.0 degree. Should you choose a Az
             Hysteresis Factor of 5 then your tracking window will
             be +/- 5.0 degrees.
          c. If you are running a digital input positioning system
             with 0.1 degree resolution and then using a
             Hysteresis Factor of 10 the window becomes +/- 1.0
             degrees.
       The factor is stored as part of your start up file in
       EMETRAK.DAT.

8.7 El Motor Hysteresis.
       The functions are identical to that of the Azimuth
       Hysteresis function.

8.8 Drive Update Period in Minutes.
       This option allows the user to select how often you wish
       the Az / El Motors to operate. If you enter 0 then the
       motors will drive every 15 seconds as this is the update
       Target calculation period. When using the Pulse Mode, the
       time and Target is frozen until Lock has been achieved. The
       period starts again after Lock has been achieved.

8.9 End Stops of Antennae.
       This option allows the user to set Software End Stops to
       prevent over run of their Array. Two, for each Azimuth and
       Elevation, (G.H.A. / Dec) have been provided. Always set #1
       as the lower value. You may enter a negative value for the
       Elevation/Declination. In Auto Track this value will be
       displayed in red to indicate a negative number.

       UNDER NO CIRCUMSTANCES SHOULD THE USER RELY UPON THE
       SOFTWARE ENDSTOPS, BUT AS A MATTER OF SAFETY, PROVIDE THEIR
       OWN FAIL SAFE ELECTRICAL INTERLOCK PROTECTION.

8.10 Communication Port [9600/8/1/N].
       This facility allows the user to choose either COM1 or
       COM2 Serial Ports as defined by the IBM (or compatible)
       configuration. Variation of the speed, number of data and
       stop bits as well as parity can not be changed in Software.

8.11 Antennae Mount. Az/El or G.H.A./Dec.
       This option allows the user to select either of the
       Antennae mounts and track the Sources as required. The
       respective displays will change according to the type of
       mount selected.

8.12 Motor Speed Control
       This option allows the user to control the speed of the
       drive motor. The "Spare" relay is used for this purpose. As
       only one relay is available, you only have the option of
       controlling one motor. This is selected from the sub menu
       from within this option. You may select either the Azimuth
       or Elevation drives and input a "window" within which, the
       "Spare" relay will NOT be actuated. That is, the relay will
       operate for FAST speed and NOT operated for SLOW speed. The
       figure you input sets a +/- value for the window. If you do
       not require this option then make both the Azimuth and
       Elevation windows equal to 0.
8.13 Save Set Up Parameters to Disk.
       This option allows the user to save all Auto Track Setup
       parameters as well as the General Set Up Parameters to
       Disk. They are stored in the Data File EMETRAK.DAT. These
       parameters are used on start up so remember to save all
       your changes prior to exiting the Program!

9.0 PRINTED CIRCUIT BOARD CONNECTIONS.

Connector P1  (RS232).

      1   Protective Ground
      2   Transmit Data
      3   Receive Data
      4   Request to Send
      5   Clear to Send
      6   Data Set Ready
      7   Signal Ground
      8   Received Line Signal Detect
      20  Data Terminal Ready
At the Computer end of the cable join 4-5 and join 6-8-20.

Connector P2 (Relay Output).

      1   Azimuth - Clockwise.
      2   Azimuth - Counter Clockwise.
      3   Elevation - Down.
      4   Elevation - Up.
      5   PTT - Echos.
      6   Polarity CW  - not used in the current software.
      7   Polarity CCW - not used in the current software.
      8   Spare now designated for Motor Speed Control.
      9         Earth
      10        Earth
      11        Earth
      12        Earth
      13        Earth
      14        Earth
      15        Earth
      16        Earth
The "Relay Outputs" may be Ground or +5v as selected by the
Interface Link.

Connector P3 (Analog and Pulse Input).

      1         Not Used
      2         Not Used
      3         Not Used
      4         Not Used
      5         Not Used
      6         Receiver  Audio Input [0 - +5v]
      7         Elevation Pulse Input [0 - +5v]
      8         Azimuth   Pulse Input [0 - +5v]
      9          +5v      (available for external use)
     10          +5v      (available for external use)
     11         Earth
     12         Earth
     13         Earth
     14         Earth
     15         Earth
     16         Earth

 Connector P4 (Azimuth Digital Input). External 4511 Pin

      1         Az Ten     0              7   (A)
      2         Az Ten     2              1   (B)
      3         Az Ten     4              2   (C)
      4         Az Ten     8              6   (D)

      5         Az Unit    0              7   (A)
      6         Az Unit    2              1   (B)
      7         Az Unit    4              2   (C)
      8         Az Unit    8              6   (D)

      9         Az Decimal 0              7   (A)
     10         Az Decimal 2              1   (B)
     11         Az Decimal 4              2   (C)
     12         Az Decimal 8              6   (D)

     13         Az Hundred 0              7   (A)
     14         Az Hundred 2              1   (B)
     15         Az Hundred 4              2   (C)
     16         Az Hundred 8              6   (D)

Connector P5 (Elev. Digital Input). External 4511 Pin

      1         El Ten     0              7   (A)
      2         El Ten     2              1   (B)
      3         El Ten     4              2   (C)
      4         El Ten     8              6   (D)

      5         El Unit    0              7   (A)
      6         El Unit    2              1   (B)
      7         El Unit    4              2   (C)
      8         El Unit    8              6   (D)

      9         El Decimal 0              7   (A)
     10         El Decimal 2              1   (B)
     11         El Decimal 4              2   (C)
     12         El Decimal 8              6   (D)

     13         Earth
     14         Earth
     15         Earth
     16         Earth

10.0  COMPONENT LIST - VK3UM EME AUTOTRACK INTERFACE.

10.1  Integrated Circuits.
      IC1  AY-3-1015D               IC11 74LS08
      IC2  ICL232 (MAX232)          IC12 74LS04
      IC3  74LS123                  IC13 74LS05
      IC4  74LS155                  IC14 74LS00
      IC5  74LS175                  IC15 74LS374
      IC6  74LS175                  IC16 74LS374
      IC7  74LS00                   IC17 74LS374
      IC8  74LS04                   IC18 74LS374
      IC9  74LS00                   IC19 74HC4060P
      IC10 74LS08                   IC20 ADC0809CCN

10.2  Capacitors.
      C1 - C2   27 pf  Ceramic
      C3        22 nf  Green Cap         (223K)
      C4       1.5 mfd Tantalum 16vW     (Watch Polarity!)
      C5       2.2 nf  Green Cap         (222K)
      C6       4.7 nf  Green Cap         (472K)
      C7        22 nf  Green Cap         (223K)
      C8       2.2 nf  Green Cap         (222K)
      C9       0.1 mfd Green Cap         (104K)
     C10       10 nf   Green Cap         (103K)
     C11 - C17 10 mfd  Tantalum 16VW     (Watch Polarity!)
     C18 - C21 22 mfd  Tantalum 16VW     (Watch Polarity!)
        Green Cap = polycarbonate or similar capacitor.

10.3  Resistors.
   R1  - R8  1.5k ohm 1/4 Watt
   R9  - R16  390 ohm 1/4 Watt (180 ohm parallel LEDs used)
   R17 - R18  22k ohm 1/4 Watt
   R19        10M ohm 1/4 Watt
   R20        10k ohm 1/4 Watt
   R21       2.2k ohm 1/4 Watt
   R22        10k ohm 1/4 Watt
   R23       100k ohm 1/4 Watt
   R24        10k ohm 1/4 Watt
   R25       1.2k ohm 1/4 Watt
   R26        10k ohm 1/4 Watt

10.4  Transistors.
   T1  -  T8  BC547
   T9         7805 (Voltage Regulator)
              Use Link if not required.

10.5  Crystal.
   X1   2.4576 MHz

10.6  Diodes.
   D1  - D11  1N914
   D12        1N4004
   D13 - D20  5.6v Zeners

10.7  LED's.
   1 - 8  Miniature Red - note these can be mounted on the board
          plus remote LEDs on the front panel. If used in parallel
          reduce R9-R16 from 390 ohms to 180 ohms.

10.8  Relays.
   RL1 - RL8  NEC MR62-5S (5v DPDT)

10.9  Fuse.
   F1 - 1A (Off Board Mounting - bridge if not required)

10.10 Sockets.
   P1       26 pin IDC  Vertical Non Clip Mounting
   P2 - P5  16 pin IDC  Vertical Non Clip Mounting

10.11 Alternative IC Component Designations.
   IC1  AY-3-1015D TR1865PL (UART)
   IC2  MAX232  MAX232CPE  AD232JN  DS14C232CN
   IC19 74HC4060 MM74HC4060N M74HC4060B1N PC74HC4060P
        PCF74HCT4060P CD74HCT4060E
   RL1 - R8  Relays.
       Also known in USA as Potter & Brumfield T82NI D113-05
       The pin configuration is as follows:
         1-2 = 5 volt coil.
           C = Common. NC = Normally Closed Contacts
                       NO = Normally Open Contacts
             1    C  NC NO
             o    o  o  o

             o    o  o  o
             2    C  NC NO

10.12 Component Sources. To the best of my knowledge they
      stock all the above components.
      USA.
         Jameco Electronics            Ph 415-5928121
         1355 Shoreway Rd              Ph 415-5928097
         Belmont CA 94002              FAX 415-5922503

      EUROPE
         Export Department             Ph +44-532-636311
         Farnell Electronic
            Components Ltd.            FAX +44-532-633411
         Canal Road
         Leeds  LS12 2TU
         United Kingdom
       On the order, write "Please charge credit card (say
       Visa or MasterCard) number xxxx, expiry date xx/xx"
       and sign the order. I am told that the card will be
       charged in local currency in most countries at a fair
       exchange rate.

11.0 CHECK OUT PROCEDURE.
       As most of you that will be undertaking this project
       are highly competent and experienced in the EME field
       you will find this a breeze!!! Be assured that, if it
       does not work, it is due to something YOU have done
       wrong!  Refer to File "BOARDFIX.DOC" for additional
       information before applying power to the board.

11.1 Assemble the board as per the component layout paying
     careful attention to the orientation of the components.
     I recommend the use of IC sockets but this ofcourse is
     not necessary. Just be sure that the IC's are aligned
     properly before soldering!! You may mount the LED's on
     the interface card or externally.  Additionally you can
     do both providing you reduce the resistor values as
     shown.

11.2 Apply power be it 7 - 9 volts DC or +5 volts if you
     choose to bridge out the onboard regulator. Measure the
     current. It should be in the vicinity of 100 - 200 mA
     depending upon your voltage source. All relays should
     not be operated as indicated by the LED's.

11.3 Interconnect the board to your Computer (refer Section 9
     for connection details). Plug the interface into COM1
     (default Serial Port) or COM2 should you desire. In the
     latter case remember to change to this Port in the
     AutoTrack Set up options.
11.4 Run the EMETRAK Software and select the Auto Track
     Option under Tracking Modes from the Main Menu.

11.5 Using the Cursor Keys (Arrow Keys), select in turn the
     Right Arrow, (Clockwise) Left Arrow (Counter Clockwise)
     and Up Arrow (Elevation Up) keys. The respective LED's
     should light! I would advise you not to connect your
     drive motors yet until you become familiar with the
     software. Remember that the Space Bar or any other "Text
     Key" will stop the motor(s) and restore you to Manual
     Track if you happen to be in Auto Track.

11.6 You can now go back to the other Screens and set you QTH
     and all other parameters you will be using. To detail
     how to do this here is difficult as you have so many
     combinations to chose from. It is very straight forward
     and logical! The explanations within this document will
     point you in the right direction. It all depends upon
     just what you will be using for your position read outs.

11.7 Calibration of your readouts can be done directly from
     the screen if you are using Analog Potentiometers.
     Remember that the maximum count is equal to +5 volts and
     should not be exceeded.  Zener diode protection is
     provided but the board is not "Goof Proof".  When using
     Digital inputs their connection is as previously
     indicated. As a check you will mimic your readout directly on
     the screen. If you chose to utilise the Pulse option then
     provide a +5 to 0 volt pulse to the interface. I would
     suggest that you use a Schmitt trigger driving a monostable.
     A 74LS123 would be suitable and this would give you the
     option to double the resolution of your pulse system. eg. If
     you feed the output from your pulse encoder, (via a schmitt
     trigger), to the respective inputs of both halves of the
     74LS123 and configure them to trigger on +ve and -ve pulse
     transitions and then "OR" their output you will provide two
     pulses to the interface instead of one! This will make a one
     pulse per degree encoder capable of 0.5 degree resolution.
     Don't forget to set your pulses/360 degrees to 720!. Remember
     that 3600 pulses per 360 degrees will give you a 0.1 degree
     readout and anything less will be scaled accordingly. The
     Pulse input will allow for greater input but, to be sure, and
     this depends upon your speed of rotation, use a variable
     frequency pulse generator to simulate what you will be using.

11.8 The relays can handle up to 2.5A but it is recommended that
     you don't use them to directly control your motors. One of
     each is provided for UP/DOWN/LEFT/RIGHT as well as a PTT Line
     for Transmitter control when using the Echo Graphing Option.
     Two are currently not used (CW and CCW Polarity) whilst the
     "Spare" can be used for the motor speed option as provided.
     You do not need to mount these components at this time should
     you desire. (relays can cost up to $5!).

11.8 The Analog input from your receiver may be interfaced to the
     Auto Track board via a suitable audio detector and DC
     amplifier. An interface should be calibrated to provide the
     level commensurate with the dB scale provided in the graphics
     option. Again the reference voltage should be set to +5 volts
     peak relative to the scale chosen.

11.9 Now that you have had a play with the options you can get
     serious! Go to the Auto Track Options Menu and select the
     Pulse Mode. You may not intend to use this mode but it is fun
     to play with and you can get the feel of the software!!! Next
     select the Auto Track mode and energize the internal Pulse
     generator with Shift[F1]. Now you can now play with the
     options!! Simulate Auto Tracking, Parking, testing your End
     Stops etc. You can also check out your Graphic facilities
     from within Graph Track. Watch your respective control LEDs
     light. (alternatively select REAL TIME TRACK and hit the HOME
     key which will place it in the Demonstration Mode).

NOW ALL YOU HAVE TO DO IS INTERFACE IT TO YOUR REAL SYSTEM!!!!

12.0 SUMMARY
       As you can see the interface options are quite profound. I
       leave it up to you to select which mode suits you best. In
       general, the concept of this system has been conceived to
       cover nearly all the current readouts being used today. The
       accuracy is commensurate to the information you present to
       the interface!

       Its no good striving for 0.01 degree accuracy when you have
       backlash in your drive, the readout system or the antennae
       moves in a strong breeze! The more attention you place on
       YOUR input the more accurate will be your tracking!

       Similarly for those that promote 12 bit A/D converters and
       claim a higher degree of resolution should consider the
       potentiometers they hang across it!! Even with the most
       expensive available 0.5% you cannot realize the accuracy
       provided by the A/D!!

       A final point with respect to the Software. As you can see
       it is highly complex! There are well over 14,000 lines of
       Pascal code. It is most difficult to be 100% sure that
       there is not a bug. I have gone to extreme lengths to check
       out as much as is practical. Should you have a problem
       please document, as best you can, the nature, effect, and
       events that caused the difficulty.

       I use the total system (with digital Gray code position
       indicators) all the time so that most problems are quickly
       revealed, but one cannot be absolutely sure! I have based
       the options from practical experience and from input from
       other users. If you have any suggestions for improvement
       please do not hesitate to write. (Don't ask me about
       Satellite tracking facilities or CW options please ... I am
       not interested! This is for those interested in EME and
       Radio Astronomy operators, not telephone users!!). The
       Software was written and developed as an Amateur project to
       fill a need. (My need!) It is not my full time profession
       nor do I expect to benefit financially! The cost has been
       kept to the barest minimum. Accordingly I would appreciate
       your help to cover costs of any future correspondence or
       software updates.

12.1 Changes to Printed Circuit Board May 1991.
     On Printed Circuit Board (Version May 91) there are two minor
     changes to the Artwork. Both are on the solder side of the
     board.
     (a) Near 7805 Regulator - a small section of track has been
         removed.
     (b) IC 6 track to pin 10 has been re-routed from pin 11.
         This is the input to the Spare relay. The error has been
         corrected. In addition, the hole sizes for the 7805 are
         too small. Bend ends of the leads over and solder direct
         to the top side of the board.

12.2 Changes to Printed Circuit Board May 1992.
     On some Printed Circuit Boards (Version May 92) there is a
     solder link in a large track near the centre of the board.
     The board manufacturer forgot a hole during the drilling
     process!

12.3 Finally!! The board has been put together by some 70 Stations
     so far, (1st Sept 1992) and the ONLY PROBLEMS HAVE BEEN
     FAULTY IC's, solder bridges (please don't use a 300 watt
     soldering iron!) and the odd wrong wiring of the serial
     interface cable. The faulty IC's have been the inexpensive
     ones like the 74LS00, 74LS04, 74LS05 and 74LS08. Make sure
     you get them from a good source!!

13.0 FUNCTION KEYS
      [F1] Main Screen .. Software Version Number.

13.1 Real Time Track Screen.
      [F2] Select Target Sources.
      [F3] Input a Grid Square.

13.2 Auto Track Screen.
       [F1] Enable/Disable display of Az and El pulse counts
  Shift[F1] Enable/Disable internal Pulse Generator.
Control[F1] Reset Pulse Counter (refer [F1]).
       [F2] Select Target Sources.  [TAB] More Sources.
       [F3] Initiate Auto Tracking Mode.
  Shift[F3] Input a Grid Square.
       [F4] Park Antennae.
       [F5] Recalibrate Az/El indicators.
       [F6] Transfer Target Az/El to Indicator Az/El.
       [F7] Save Indicator Az/El.
  Shift[F7] Recall Indicator Az/El.

13.3 Graph Track.
       [F1] Help Screen of Graphic Function Keys.
       [F2] Select Target Sources.  [TAB] More Sources.
  Shift[F2] Digital Signal Processing (Rudimentary)
            Load Receiver file with Shift[F10] first.
            [F1] Set Level with arrow keys first then perform DSP.
            [F2] Replay CW on Computer Speaker.
            [F7] Repeat Set Level Procedure.
            [Esc] Returns to Menu.
    Alt[F2] Long Term Scan and signal variation Graph option.
   Ctrl[F2] Change Tracking Update Scan Count. (Max 499).
       [F3] Auto Track Target (Position for Echos).
  Shift[F3] Plot Moon Echos.
       [F4] Park Antennae.
  Shift[F4] Transfer Target Az/El to Indicator Az/El. (Pulse Mode).
       [F5] Position for Azimuth E Plot.
  Shift[F5] Plot Azimuth E graph.  Linear increment Indicator mode.
    Alt[F5] Plot Azimuth E graph.  Non-linear increment Indicator mode.
       [F6] Position for Elevation H Plot.
  Shift[F6] Plot Elevation H graph.  Linear increment Indicator mode.
    Alt[F6] Plot Elevation H graph.  Non-linear increment Indicator mode.
       [F7] Clear Graphics Screen;
  Shift[F7] Calculate Antennae Gain and Beam angle.
       [F8] Change offset Degree Scale. +/- 5 , 12.5 or 25 degrees.
  Shift[F8] Invert dB Scale.
   Ctrl[F8] Calibrate A/D input voltage.
       [F9] Receiver scan plot 10 Seconds.
  Shift[F9] Receiver scan plot 50 Seconds.
      [F10] Store Graph Plot to Disk.
 Shift[F10] Load Graph Plot from Disk.
  Ctrl[F10] Erase a Graph File.
   Alt[F10] Print Graph.

13.4 [F2] Target Source Options  ( plus [TAB] for more)
       [F1] Moon.                 Shift[F1]   P1641-45
       [F2] Sun.                  Shift[F2]   P1831-03
       [F3] Aquarius.             Shift[F3]   P1858+03
       [F4] Leo.                  Shift[F4]   P1354-62
       [F5] Pictor.               Shift[F5]   Orion M42
       [F6] Cassiopeia.           Shift[F6]   Taurus A
       [F7] Sagittarius.          Shift[F7]   Centurus A
       [F8] Cygnus.               Shift[F8]   Virgo
       [F9] Omega M17.            Shift[F9]   Perseus A
      [F10] User Input Az / El.  Autotrack and Graphics only.
 Shift[F10] Input a Grid Square. Autotrack and Graphics only.



Doug McArthur (VK3UM)

22nd November 1993