********************CALLERID v.1.1*********************

     CALLERID.EXE is a TSR for KBBS, or any other BBS that has a script
language and can read from an external text file.  CALLERID.EXE grabs the
Caller I.D. information from a compatible modem and writes it to a formatted
textfile to be used by a BBS or comm program while online.

Loading:
\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\

1)	CALLERID.EXE loads into upper memory from AUTOEXEC.BAT with the
	following command line:

	LOADHIGH CALLERID [port] [irq] [path]

	[port]	One of the four standard com ports; 3F8, 2F8, 3E8, or 2E8.
	[irq]	IRQ 3, 4, or 5.
	[path]	(optional) Path to write the text file 'CALLERID.TMP', which
		contains the Caller I.D. information.  Must have trailing
		backslash.  If [path] is omitted, file will be written to the
		current directory.

	EX:	LOADHIGH CALLERID 2F8 3 C:\KBBS\

2)	Next, you need a way for your BBS to read the text file that
	CALLERID.EXE will write.  Included in this archive is the file
	'CALLID.SEQ' which is used to read the text file for KBBS.
	Compile this file, and then add the following to the beginning
	of your ONLINE.SEQ:

	define filename:callidseq;

	callidseq:='CALLID';
	IF SYSOPNAME<>USERNAME
	  THEN CALLSEQ(callidseq);
	  ENDIF;

	This will call 'CALLID.SEQ' before the user has been allowed into
	the main part of the BBS.  Of course, you may program your .SEQ or
	script any way you like...

3)	Set the delay-until-answer to about 8 seconds (or long enough for
	the line to ring twice, but not 3 time).  Then load the BBS as you
	normally would.

Notes:
\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\

     Do not allow the phone to ring while DTR is low.  This TSR does not 
initialize the modem: it allows your BBS program to do that.  In other words,
always use this TSR while a BBS or com program is running.  If that conflicts
with the use of your computer, either unplug the phone line or don't use
this program.

     If, for whatever reason, you are unable to load it high, it will load
low just fine.  It will use about 6-7k of memory while resident.  However,
with all the excellent memory managers available, you should have no problem
loading it high.

     If speed is a concern: The testing of CALLERID.EXE while writing it was
on a generic 12mHz 286 running KBBS.  It showed no loss of speed during normal
operation, including file transfers. 

Registration:
\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\

     None.

Guarantees:
\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\

     None.

History:
\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\

     v1.0 - Initial release.
     v1.1 - Bug fix.  CALLERID.EXE would lock up some computers if a call
            was recieved while a KBBS background task was running.

Support:
\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\

     Send me $5.00 and I will try to modify the code to suit your system.
That is about how much Caller I.D. costs per month, so I think that is fair.
If it works for you as-is, great.  Drop me a note and let me know what BBS
system you are running it on.


Frank Gilliland
E517 Gordon
Spokane WA, 99207
BBS: (509)487-7746  (Entropy BBS)