WATCHDCD


                                                               Version 1.0


      by Gary Chanson
      (C) 1994


          WATCHDCD  is Copyright 1994  by  Gary Chanson  and Starquest
          Systems.   No restrictions are  placed on the non-commercial
          use of this program.  This program and its documentation may
          be  copied and redistributed provided that it is not changed
          and  no fee is  charged for it.   An exception is granted to
          not-for-profit user's groups, which are authorized to charge
          a nominal fee for materials and handling.  Starquest Systems
          and  Gary Chanson assume no  liability for damages caused by
          the use of these programs.


    Description:

        WATCHDCD  is a DESQview  utility which monitors  the serial port
        status  of  the  specified  COM  port and restarts the specified
        DESQview  task  if  a  disconnect  is  detected.   Disconnect is
        assumed if DCD drops and stays low for the specified delay time.

        During  operation,  WATCHDCD  looks  for  messages  sent  to its
        mailbox   (named  'WATCH:<name>'  where  <name>  is  the  string
        specified  as the mailbox parameter passed to WATCHDCD).  If the
        message   'STOP'  is   received,  WATCHDCD   terminates  without
        affecting  the  target  program.   If  'CLEAR'  is received, any
        pending  restart is  canceled and  WATCHDCD's state  is reset to
        off-line.

        If  a log  file is  specified with  the -L option, all character
        output  is  sent  to  the  specified  file  (default log file is
        WATCHDCD.LOG).

        WATCHDCD  can run  in a  DESQview window  with less  then 50K of
        memory allocated.


    Usage:

        WATCHDCD port mailbox dvp-file [-options]

            port     - serial port as COMx or a port address
            mailbox  - name assigned to the mailbox of the BBS node or
                       the DV handle in hex in the form: nnnn:nnnn
            dvp-file - task to restart if triggered


    Options:

        -Dn1        reboot Delay in MS (65,535 max)
        -L[file]    Send output to Log file (default=WATCHDCD.LOG)
        -Q          Quiet mode


    Messages:

        CLEAR       cancel pending restart and reset to off-line
        STOP        terminate monitoring


    Error levels returned:

        0           Normal exit
        1           Task terminated and restarted successfully
        2           Task terminated and restart failed
        3           Unrecognized option
        4           Specified mailbox not found
        5           Not running under DESQview


    Installation:

        The  purpose of WATCHDCD is to monitor on-line applications such
        as  BBS  "doors"  in  order  to prevent unreliable programs from
        "hanging" the BBS.  This is accomplished by monitoring the state
        of  the modem Data  Carrier Detect line.   If WATCHDCD detects a
        disconnect, it uses the DESQview API to terminate the BBS window
        and  restart it.  Optionally, a delay interval can be specified,
        giving  the target program time  after disconnect for a graceful
        exit.

        Typically,  WATCHDCD is  loaded and  unloaded in  the batch file
        which  runs the application to be monitored.  The commands might
        look like (without the comments):

            MAILBOX NODE1                   ; assign name to this window
            SPAWN WATCHDCD COM1 NODE1 N1-PIF -d1000 -lWATCHDCD.LOG
            <program>                       ; run application
            SENDMAIL WATCH:NODE1 STOP       ; end watch

        SPAWN,  MAILBOX and  SENDMAIL are  available separately (MAILBOX
        and  SENDMAIL as part  of DVToolKIT).  These  functions are also
        supported by other DESQview utilities.

        In  this example, WATCHDCD runs in an additional DESQview window
        with  the name 'WATCH:NODE1' assigned to its mailbox.  <program>
        runs in the current window with the name 'NODE1' assigned to its
        mailbox.

        Normally,  <program>  will run  to completion and  exit with the
        caller  still  connected.   WATCHDCD  will  receive  the  'STOP'
        message  and allow the batch file  to complete and return to the
        BBS program.

        If <program>  detects a disconnect  and exits gracefully  within
        the  delay interval  (1 second  in this  example), WATCHDCD will
        still  receive its  'STOP' message  and allow  the batch file to
        complete.

        If <program>  is unable to respond  to the disconnect condition,
        WATCHDCD will not receive its 'STOP' message.  It will terminate
        the  target window and will restart  the BBS node by running the
        specified program (N1-PIF.DVP in this example).


    -----------------------------------------------------------------------

            Please forward all comments and bug reports to:

                Gary Chanson
                31 Chester Avenue
                Waltham, MA  02154

                Voice:  617-899-4771
                Email:  Gary.Chanson@Channel1.com

    -----------------------------------------------------------------------

                      For on-line support, call our BBS!

                              Arcane Incantations
                                 617-899-6672

    -----------------------------------------------------------------------