eXtended Memory Specification (XMS), ver 2.0


July 19, 1988


Copyright (c) 1988, Microsoft Corporation, Lotus Development
Corporation, Intel Corporation, and AST Research, Inc.

Microsoft Corporation                                            
Box 97017
16011 NE 36th Way                                       
Redmond, WA 98073

LOTUS (r)
INTEL (r)
MICROSOFT (r)
AST (r) Research

This specification was jointly developed by Microsoft Corporation,
Lotus Development Corporation, Intel Corporation,and AST Research,
Inc. Although it has been released into the public domain and is not
confidential or proprietary, the specification is still the copyright
and property of Microsoft Corporation, Lotus Development Corporation,
Intel Corporation, and AST Research, Inc.

Disclaimer of Warranty

MICROSOFT CORPORATION, LOTUS DEVELOPMENT CORPORATION, INTEL
CORPORATION, AND AST RESEARCH, INC., EXCLUDE ANY AND ALL IMPLIED
WARRANTIES, INCLUDING WARRANTIES OF MERCHANTABILITY AND FITNESS FOR A
PARTICULAR PURPOSE. NEITHER MICROSOFT NOR LOTUS NOR INTEL NOR AST
RESEARCH MAKE ANY WARRANTY OF REPRESENTATION, EITHER EXPRESS OR
IMPLIED, WITH RESPECT TO THIS SPECIFICATION, ITS QUALITY,
PERFORMANCE, MERCHANTABILITY, OR FITNESS FOR A PARTICULAR PURPOSE.
NEITHER MICROSOFT NOR LOTUS NOR INTEL NOR AST RESEARCH SHALL HAVE ANY
LIABILITY FOR SPECIAL, INCIDENTAL, OR CONSEQUENTIAL DAMAGES ARISING
OUT OF OR RESULTING FROM THE USE OR MODIFICATION OF THIS
SPECIFICATION.

This specification uses the following trademarks:

Intel is a registered trademark of Intel Corporation, Microsoft is a
registered trademark of Microsoft Corporation, Lotus is a registered
trademark of Lotus Development Corporation, and AST is a registered
trademark of AST Research, Inc.


                       Extended Memory Specification
                       =============================

    The purpose of this document is to define the Extended Memory Specifica-
tion (XMS) version 2.00 for MS-DOS.  XMS allows DOS programs to utilize
additional memory found in Intel's 80286 and 80386 based machines in
a consistent, machine independent manner.  With some restrictions, XMS adds
almost 64K to the 640K which DOS programs can access directly.	Depending on
available hardware, XMS may provide even more memory to DOS programs.  XMS
also provides DOS programs with a standard method of storing data in extended
memory.

DEFINITIONS:
------------

    Extended
    Memory      -   Memory in 80286 and 80386 based machines which is located
                    above the 1MB address boundary.

    High Memory
    Area (HMA)  -   The first 64K of extended memory.  The High Memory
		    Area is unique because code can be executed in it while
		    in real mode.  The HMA officially starts at FFFF:10h
		    and ends at FFFF:FFFFh making it 64K-16 bytes in length.
                    
    Upper Memory
    Blocks (UMBs)-  Blocks of memory available on some 80x86 based machines
                    which are located between DOS's 640K limit and the
                    1MB address boundary.  The number, size, and location
                    of these blocks vary widely depending upon the types
                    of hardware adapter cards installed in the machine.
                    
    Extended Memory
    Blocks (EMBs)-  Blocks of extended memory located above the HMA which
                    can only be used for data storage.
                    
    A20 Line    -   The 21st address line of 80x86 CPUs.  Enabling the A20
                    line allows access to the HMA.

    XMM         -   An Extended Memory Manager.  A DOS device driver which
                    implements XMS.  XMMs are machine specific but allow
		    programs to use extended memory in a machine-independent
		    manner.
    
    HIMEM.SYS   -   The Extended Memory Manager currently being distributed
                    by Microsoft.


Helpful Diagram:

    |                                                       |   Top of Memory
    |                                                       |
    |                                                       |
    |                        /\                             |
    |                       /||\                            |
    |                        ||                             |
    |                        ||                             |
    |.......................................................|
    |                                                       |
    |                                                       |
    |             Possible Extended Memory Block            |
    |                                                       |
    |                                                       |
    |.......................................................|
    |                        ||                             |
    |                        ||                             |
    |                       \||/                            |
    |                        \/                             |
    |                                                       |
    |                                                       |
    |       Other EMBs could exist above 1088K (1MB+64K)    |
    |                                                       |
    |                                                       |
    |-------------------------------------------------------|   1088K
    |                                                       |
    |                                                       |
    |                The High Memory Area                   |
    |                                                       |
    |                                                       |
    |=======================================================|   1024K or 1MB
    |                                                       |
    |                        /\                             |
    |                       /||\                            |
    |                        ||                             |
    |                        ||                             |
    |.......................................................|
    |                                                       |
    |             Possible Upper Memory Block               |
    |.......................................................|
    |                        ||                             |
    |                        ||                             |
    |                       \||/                            |
    |                        \/                             |
    |                                                       |
    |        Other UMBs could exist between 640K and 1MB    |
    |                                                       |
    |-------------------------------------------------------|   640K
    |                                                       |
    |                                                       |
    |                                                       |
    |             Conventional or DOS Memory                |
    |                                                       |
    |                                                       |
    |                                                       |
    |                                                       |
    |                                                       |
    +-------------------------------------------------------+   0K

DRIVER INSTALLATION:
--------------------

    An XMS driver is installed by including a DEVICE= statement in the
machine's CONFIG.SYS file.  It must be installed prior to any other
devices or TSRs which use it.  An optional parameter after the driver's 
name (suggested name "/HMAMIN=") indicates the minimum amount of space in
the HMA a program can use.  Programs which use less than the minimum will
not be placed in the HMA.  See "Prioritizing HMA Usage" below for more
information.  A second optional parameter (suggested name "/NUMHANDLES=")
allows users to specify the maximum number of extended memory blocks which
may be allocated at any time.

    NOTE: XMS requires DOS 3.00 or above.


THE PROGRAMMING API:
--------------------

    The XMS API Functions are accessed via the XMS driver's Control Function.
The address of the Control Function is determined via INT 2Fh.  First, a
program should determine if an XMS driver is installed.  Next, it should
retrieve the address of the driver's Control Function.  It can then use any
of the available XMS functions.  The functions are divided into several
groups:

        1. Driver Information Functions (0h)
        2. HMA Management Functions (1h-2h)
	3. A20 Management Functions (3h-7h)
        4. Extended Memory Management Functions (8h-Fh)
        5. Upper Memory Management Functions (10h-11h)


DETERMINING IF AN XMS DRIVER IS INSTALLED:
------------------------------------------

    The recommended way of determining if an XMS driver is installed is to
set AH=43h and AL=00h and then execute INT 2Fh.  If an XMS driver is available,
80h will be returned in AL.

    Example:
            ; Is an XMS driver installed?
            mov     ax,4300h
            int     2Fh         
            cmp     al,80h  
            jne     NoXMSDriver
            

CALLING THE API FUNCTIONS:
--------------------------

    Programs can execute INT 2Fh with AH=43h and AL=10h to obtain the address
of the driver's control function.  The address is returned in ES:BX.  This
function is called to access all of the XMS functions.  It should be called
with AH set to the number of the API function requested.  The API function
will put a success code of 0001h or 0000h in AX.  If the function succeeded
(AX=0001h), additional information may be passed back in BX and DX.  If the
function failed (AX=0000h), an error code may be returned in BL.  Valid
error codes have their high bit set.  Developers should keep in mind that
some of the XMS API functions may not be implemented by all drivers and will
return failure in all cases.

    Example:
            ; Get the address of the driver's control function
            mov     ax,4310h
            int     2Fh
            mov     word ptr [XMSControl],bx        ; XMSControl is a DWORD
            mov     word ptr [XMSControl+2],es
            
            ; Get the XMS driver's version number
            mov     ah,00h
            call    [XMSControl]    ; Get XMS Version Number

    NOTE: Programs should make sure that at least 256 bytes of stack space
	  is available before calling XMS API functions.


API FUNCTION DESCRIPTIONS:
--------------------------

    The following XMS API functions are available:

       0h)  Get XMS Version Number
       1h)  Request High Memory Area
       2h)  Release High Memory Area
       3h)  Global Enable A20
       4h)  Global Disable A20
       5h)  Local Enable A20
       6h)  Local Disable A20
       7h)  Query A20
       8h)  Query Free Extended Memory
       9h)  Allocate Extended Memory Block
       Ah)  Free Extended Memory Block
       Bh)  Move Extended Memory Block
       Ch)  Lock Extended Memory Block
       Dh)  Unlock Extended Memory Block
       Eh)  Get Handle Information
       Fh)  Reallocate Extended Memory Block
      10h)  Request Upper Memory Block
      11h)  Release Upper Memory Block

Each is described below.


Get XMS Version Number (Function 00h):
--------------------------------------

    ARGS:   AH = 00h
    RETS:   AX = XMS version number
	    BX = Driver internal revision number
	    DX = 0001h if the HMA exists, 0000h otherwise
    ERRS:   None

    This function returns with AX equal to a 16-bit BCD number representing
the revision of the DOS Extended Memory Specification which the driver
implements (e.g. AX=0235h would mean that the driver implemented XMS version
2.35).	BX is set equal to the driver's internal revision number mainly for
debugging purposes.  DX indicates the existence of the HMA (not its
availability) and is intended mainly for installation programs.
    
    NOTE: This document defines version 2.00 of the specification.


Request High Memory Area (Function 01h):
----------------------------------------

    ARGS:   AH = 01h
            If the caller is a TSR or device driver,
                DX = Space needed in the HMA by the caller in bytes
            If the caller is an application program,
                DX = FFFFh     
    RETS:   AX = 0001h if the HMA is assigned to the caller, 0000h otherwise
    ERRS:   BL = 80h if the function is not implemented
	    BL = 81h if a VDISK device is detected
	    BL = 90h if the HMA does not exist
	    BL = 91h if the HMA is already in use
	    BL = 92h if DX is less than the /HMAMIN= parameter

    This function attempts to reserve the 64K-16 byte high memory area for
the caller.  If the HMA is currently unused, the caller's size parameter is
compared to the /HMAMIN= parameter on the driver's command line.  If the
value passed by the caller is greater than or equal to the amount specified
by the driver's parameter, the request succeeds.  This provides the ability
to ensure that programs which use the HMA efficiently have priority over
those which do not.

    NOTE: See the sections "Prioritizing HMA Usage" and "High Memory Area
          Restrictions" below for more information.


Release High Memory Area (Function 02h):
----------------------------------------

    ARGS:   AH = 02h
    RETS:   AX = 0001h if the HMA is successfully released, 0000h otherwise
    ERRS:   BL = 80h if the function is not implemented
	    BL = 81h if a VDISK device is detected
	    BL = 90h if the HMA does not exist
	    BL = 93h if the HMA was not allocated

    This function releases the high memory area and allows other programs to
use it.  Programs which allocate the HMA must release it before exiting.  
When the HMA has been released, any code or data stored in it becomes invalid
and should not be accessed.


Global Enable A20 (Function 03h):
---------------------------------

    ARGS:   AH = 03h
    RETS:   AX = 0001h if the A20 line is enabled, 0000h otherwise
    ERRS:   BL = 80h if the function is not implemented
	    BL = 81h if a VDISK device is detected
	    BL = 82h if an A20 error occurs

    This function attempts to enable the A20 line.  It should only be used
by programs which have control of the HMA.  The A20 line should be turned
off via Function 04h (Global Disable A20) before a program releases control
of the system.

    NOTE: On many machines, toggling the A20 line is a relatively slow
          operation.


Global Disable A20 (Function 04h):
----------------------------------

    ARGS:   AH = 04h
    RETS:   AX = 0001h if the A20 line is disabled, 0000h otherwise
    ERRS:   BL = 80h if the function is not implemented
	    BL = 81h if a VDISK device is detected
	    BL = 82h if an A20 error occurs
	    BL = 94h if the A20 line is still enabled
    
    This function attempts to disable the A20 line.  It should only be used
by programs which have control of the HMA.  The A20 line should be disabled
before a program releases control of the system.

    NOTE: On many machines, toggling the A20 line is a relatively slow
          operation.


Local Enable A20 (Function 05h):
--------------------------------

    ARGS:   AH = 05h
    RETS:   AX = 0001h if the A20 line is enabled, 0000h otherwise
    ERRS:   BL = 80h if the function is not implemented
	    BL = 81h if a VDISK device is detected
	    BL = 82h if an A20 error occurs

    This function attempts to enable the A20 line.  It should only be used
by programs which need direct access to extended memory.  Programs which use
this function should call Function 06h (Local Disable A20) before releasing
control of the system.

    NOTE: On many machines, toggling the A20 line is a relatively slow
          operation.


Local Disable A20 (Function 06h):
---------------------------------

    ARGS:   AH = 06h
    RETS:   AX = 0001h if the function succeeds, 0000h otherwise
    ERRS:   BL = 80h if the function is not implemented
	    BL = 81h if a VDISK device is detected
	    BL = 82h if an A20 error occurs
	    BL = 94h if the A20 line is still enabled

    This function cancels a previous call to Function 05h (Local Enable
A20).  It should only be used by programs which need direct access to
extended memory.  Previous calls to Function 05h must be canceled before
releasing control of the system.

    NOTE: On many machines, toggling the A20 line is a relatively slow
          operation.


Query A20 (Function 07h):
-------------------------

    ARGS:   AH = 07h
    RETS:   AX = 0001h if the A20 line is physically enabled, 0000h otherwise
    ERRS:   BL = 00h if the function succeeds
	    BL = 80h if the function is not implemented
	    BL = 81h if a VDISK device is detected

    This function checks to see if the A20 line is physically enabled.  It
does this in a hardware independent manner by seeing if "memory wrap" occurs.


Query Free Extended Memory (Function 08h):
------------------------------------------

    ARGS:   AH = 08h
    RETS:   AX = Size of the largest free extended memory block in K-bytes
	    DX = Total amount of free extended memory in K-bytes
    ERRS:   BL = 80h if the function is not implemented
	    BL = 81h if a VDISK device is detected
	    BL = A0h if all extended memory is allocated

    This function returns the size of the largest available extended memory
block in the system.

    NOTE: The 64K HMA is not included in the returned value even if it is
	  not in use.


Allocate Extended Memory Block (Function 09h):
----------------------------------------------

    ARGS:   AH = 09h
            DX = Amount of extended memory being requested in K-bytes
    RETS:   AX = 0001h if the block is allocated, 0000h otherwise
            DX = 16-bit handle to the allocated block
    ERRS:   BL = 80h if the function is not implemented
	    BL = 81h if a VDISK device is detected
	    BL = A0h if all available extended memory is allocated
	    BL = A1h if all available extended memory handles are in use
            
    This function attempts to allocate a block of the given size out of the
pool of free extended memory.  If a block is available, it is reserved
for the caller and a 16-bit handle to that block is returned.  The handle
should be used in all subsequent extended memory calls.  If no memory was
allocated, the returned handle is null.

    NOTE: Extended memory handles are scarce resources.  Programs should
	  try to allocate as few as possible at any one time.  When all
	  of a driver's handles are in use, any free extended memory is
	  unavailable.


Free Extended Memory Block (Function 0Ah):
------------------------------------------

    ARGS:   AH = 0Ah
            DX = Handle to the allocated block which should be freed
    RETS:   AX = 0001h if the block is successfully freed, 0000h otherwise
    ERRS:   BL = 80h if the function is not implemented
	    BL = 81h if a VDISK device is detected
	    BL = A2h if the handle is invalid
	    BL = ABh if the handle is locked

    This function frees a block of extended memory which was previously
allocated using Function 09h (Allocate Extended Memory Block).  Programs
which allocate extended memory should free their memory blocks before
exiting.  When an extended memory buffer is freed, its handle and all data
stored in it become invalid and should not be accessed.


Move Extended Memory Block (Function 0Bh):
------------------------------------------

    ARGS:   AH = 0Bh
            DS:SI = Pointer to an Extended Memory Move Structure (see below)
    RETS:   AX = 0001h if the move is successful, 0000h otherwise
    ERRS:   BL = 80h if the function is not implemented
	    BL = 81h if a VDISK device is detected
	    BL = 82h if an A20 error occurs
	    BL = A3h if the SourceHandle is invalid
	    BL = A4h if the SourceOffset is invalid
	    BL = A5h if the DestHandle is invalid
	    BL = A6h if the DestOffset is invalid
	    BL = A7h if the Length is invalid
	    BL = A8h if the move has an invalid overlap
	    BL = A9h if a parity error occurs

    Extended Memory Move Structure Definition:

        ExtMemMoveStruct    struc
            Length              dd  ?   ; 32-bit number of bytes to transfer
            SourceHandle        dw  ?   ; Handle of source block
            SourceOffset        dd  ?   ; 32-bit offset into source 
            DestHandle          dw  ?   ; Handle of destination block
            DestOffset          dd  ?   ; 32-bit offset into destination block
        ExtMemMoveStruct    ends
            
    This function attempts to transfer a block of data from one location to
another.  It is primarily intended for moving blocks of data between
conventional memory and extended memory, however it can be used for moving
blocks within conventional memory and within extended memory.

    NOTE: If SourceHandle is set to 0000h, the SourceOffset is interpreted
          as a standard segment:offset pair which refers to memory that is
          directly accessible by the processor.  The segment:offset pair
          is stored in Intel DWORD notation.  The same is true for DestHandle
          and DestOffset.
          
	  SourceHandle and DestHandle do not have to refer to locked memory
	  blocks.
          
	  Length must be even.	Although not required, WORD-aligned moves
	  can be significantly faster on most machines.  DWORD aligned move
	  can be even faster on 80386 machines.
          
	  If the source and destination blocks overlap, only forward moves
	  (i.e. where the source base is less than the destination base) are
	  guaranteed to work properly.
          
	  Programs should not enable the A20 line before calling this
	  function.  The state of the A20 line is preserved.

	  This function is guaranteed to provide a reasonable number of
	  interrupt windows during long transfers.
          
          
Lock Extended Memory Block (Function 0Ch):
------------------------------------------

    ARGS:   AH = 0Ch
            DX = Extended memory block handle to lock
    RETS:   AX = 0001h if the block is locked, 0000h otherwise
	    DX:BX = 32-bit linear address of the locked block
    ERRS:   BL = 80h if the function is not implemented
	    BL = 81h if a VDISK device is detected
	    BL = A2h if the handle is invalid
	    BL = ACh if the block's lock count overflows
	    BL = ADh if the lock fails
            
    This function locks an extended memory block and returns its base 
address as a 32-bit linear address.  Locked memory blocks are guaranteed not
to move.  The 32-bit pointer is only valid while the block is locked.
Locked blocks should be unlocked as soon as possible.

    NOTE: A block does not have to be locked before using Function 0Bh (Move
          Extended Memory Block).
          
	  "Lock counts" are maintained for EMBs.


Unlock Extended Memory Block (Function 0Dh):
--------------------------------------------

    ARGS:   AH = 0Dh
            DX = Extended memory block handle to unlock
    RETS:   AX = 0001h if the block is unlocked, 0000h otherwise
    ERRS:   BL = 80h if the function is not implemented
	    BL = 81h if a VDISK device is detected
	    BL = A2h if the handle is invalid
	    BL = AAh if the block is not locked
    
    This function unlocks a locked extended memory block.  Any 32-bit
pointers into the block become invalid and should no longer be used.


Get EMB Handle Information (Function 0Eh):
------------------------------------------

    ARGS:   AH = 0Eh
	    DX = Extended memory block handle
    RETS:   AX = 0001h if the block's information is found, 0000h otherwise
	    BH = The block's lock count
	    BL = Number of free EMB handles in the system
	    DX = The block's length in K-bytes
    ERRS:   BL = 80h if the function is not implemented
	    BL = 81h if a VDISK device is detected
	    BL = A2h if the handle is invalid

    This function returns additional information about an extended memory
block to the caller.

    NOTE: To get the block's base address, use Function 0Ch (Lock Extended
	  Memory Block).
          
          
Reallocate Extended Memory Block (Function 0Fh):
------------------------------------------------

    ARGS:   AH = 0Fh
	    BX = New size for the extended memory block in K-bytes
	    DX = Unlocked extended memory block handle to reallocate
    RETS:   AX = 0001h if the block is reallocated, 0000h otherwise
    ERRS:   BL = 80h if the function is not implemented
	    BL = 81h if a VDISK device is detected
	    BL = A0h if all available extended memory is allocated
	    BL = A1h if all available extended memory handles are in use
	    BL = A2h if the handle is invalid
	    BL = ABh if the block is locked

    This function attempts to reallocate an unlocked extended memory block
so that it becomes the newly specified size.  If the new size is smaller
than the old block's size, all data at the upper end of the old block is
lost.


Request Upper Memory Block (Function 10h):
------------------------------------------

    ARGS:   AH = 10h
	    DX = Size of requested memory block in paragraphs
    RETS:   AX = 0001h if the request is granted, 0000h otherwise
	    BX = Segment number of the upper memory block
            If the request is granted,
		DX = Actual size of the allocated block in paragraphs
	    otherwise,
		DX = Size of the largest available UMB in paragraphs
    ERRS:   BL = 80h if the function is not implemented
	    BL = B0h if a smaller UMB is available
	    BL = B1h if no UMBs are available

    This function attempts to allocate an upper memory block to the caller.
If the function fails, the size of the largest free UMB is returned in DX.

    NOTE: By definition UMBs are located below the 1MB address boundary.
	  The A20 Line does not need to be enabled before accessing an
	  allocated UMB.

	  UMBs are paragraph aligned.

	  To determine the size of the largest available UMB, attempt to
	  allocate one with a size of FFFFh.

	  UMBs are unaffected by EMS calls.


Release Upper Memory Block (Function 11h):
------------------------------------------

    ARGS:   AH = 11h
	    DX = Segment number of the upper memory block
    RETS:   AX = 0001h if the block was released, 0000h otherwise
    ERRS:   BL = 80h if the function is not implemented
	    BL = B2h if the UMB segment number is invalid

    This function frees a previously allocated upper memory block.  When an
UMB has been released, any code or data stored in it becomes invalid and
should not be accessed.



PRIORITIZING HMA USAGE:
-----------------------

    For DOS users to receive the maximum benefit from the High Memory Area,
programs which use the HMA must store as much of their resident code in it as
is possible.  It is very important that developers realize that the HMA is
allocated as a single unit. 

    For example, a TSR program which grabs the HMA and puts 10K of code into
it may prevent a later TSR from putting 62K into the HMA.  Obviously, regular
DOS programs would have more memory available to them below the 640K line if
the 62K TSR was moved into the HMA instead of the 10K one.

    The first method for dealing with conflicts such as this is to require 
programs which use the HMA to provide a command line option for disabling
this feature.  It is crucial that TSRs which do not make full use of the HMA
provide such a switch on their own command line (suggested name "/NOHMA").

    The second method for optimizing HMA usage is through the /HMAMIN=
parameter on the XMS device driver line.  The number after the parameter
is defined to be the minimum amount of HMA space (in K-bytes) used by any
driver or TSR.	For example, if "DEVICE=HIMEM.SYS /HMAMIN=48" is in a
user's CONFIG.SYS file, only programs which request at least 48K would be
allowed to allocate the HMA.  This number can be adjusted either by
installation programs or by the user himself.  If this parameter is not
specified, the default value of 0 is used causing the HMA to be allocated
on a first come, first served basis.

    Note that this problem does not impact application programs.  If the HMA
is available when an application program starts, the application is free to
use as much or as little of the HMA as it wants.  For this reason,
applications should pass FFFFh in DX when calling Function 01h.



HIGH MEMORY AREA RESTRICTIONS:
------------------------------

-   Far pointers to data located in the HMA cannot be passed to DOS.  DOS
    normalizes any pointer which is passed into it.  This will cause data
    addresses in the HMA to be invalidated.

-   Disk I/O directly into the HMA (via DOS, INT 13h, or otherwise) is not
    recommended.
       
-   Programs, especially drivers and TSRs, which use the HMA *MUST* use
    as much of it as possible.  If a driver or TSR is unable to use at
    least 90% of the available HMA (typically ~58K), they must provide
    a command line switch for overriding HMA usage.  This will allow
    the user to configure his machine for optimum use of the HMA.
       
-   Device drivers and TSRs cannot leave the A20 line permanently turned
    on.  Several applications rely on 1MB memory wrap and will overwrite the
    HMA if the A20 line is left enabled potentially causing a system crash.
        
-   Interrupt vectors must not point into the HMA.  This is a result of
    the previous restriction.  Note that interrupt vectors can point into
    any allocated upper memory blocks however.

ERROR CODE INDEX:
-----------------

If AX=0000h when a function returns and the high bit of BL is set,

    BL=80h if the function is not implemented
       81h if a VDISK device is detected
       82h if an A20 error occurs
       8Eh if a general driver error occurs
       8Fh if an unrecoverable driver error occurs
       90h if the HMA does not exist
       91h if the HMA is already in use
       92h if DX is less than the /HMAMIN= parameter
       93h if the HMA is not allocated
       94h if the A20 line is still enabled
       A0h if all extended memory is allocated
       A1h if all available extended memory handles are in use
       A2h if the handle is invalid
       A3h if the SourceHandle is invalid
       A4h if the SourceOffset is invalid
       A5h if the DestHandle is invalid
       A6h if the DestOffset is invalid
       A7h if the Length is invalid
       A8h if the move has an invalid overlap
       A9h if a parity error occurs
       AAh if the block is not locked
       ABh if the block is locked
       ACh if the block's lock count overflows
       ADh if the lock fails
       B0h if a smaller UMB is available
       B1h if no UMBs are available
       B2h if the UMB segment number is invalid


IMPLEMENTATION NOTES FOR DOS XMS DRIVERS:
-----------------------------------------

-   A DOS XMS driver's control function must begin with code similar to the
    following:

XMMControl  proc    far

	    jmp     short XCControlEntry    ; For "hookability"
	    nop 			    ; NOTE: The jump must be a short
	    nop 			    ;  jump to indicate the end of
	    nop 			    ;  any hook chain.	The nop's
					    ;  allow a far jump to be
					    ;  patched in.
XCControlEntry:


-   XMS drivers must preserve all registers except those containing
    returned values across any function call.

-   XMS drivers are required to hook INT 15h and watch for calls to
    functions 87h (Block Move) and 88h (Extended Memory Available).  The
    INT 15h Block Move function must be hooked so that the state of the A20
    line is preserved across the call.	The INT 15h Extended Memory
    Available function must be hooked to return 0h to protect the HMA.

-   In order to maintain compatibility with existing device drivers, DOS XMS
    drivers must not hook INT 15h until the first non-Version Number call
    to the control function is made.

-   XMS drivers are required to check for the presence of drivers which
    use the IBM VDISK allocation scheme.  Note that it is not sufficient to
    check for VDISK users at installation time but at the time when the HMA
    is first allocated.  If a VDISK user is detected, the HMA must not be
    allocated.	Microsoft will publish a standard method for detecting
    drivers which use the VDISK allocation scheme.

-   XMS drivers which have a fixed number of extended memory handles (most
    do) should implement a command line parameter for adjusting that number
    (suggested name "/NUMHANDLES=")

-   XMS drivers should make sure that the major DOS version number is
    greater than or equal to 3 before installing themselves.

-   UMBs cannot occupy memory addresses that can be banked by EMS 4.0.
    EMS 4.0 takes precedence over UMBs for physically addressable memory.

-   All driver functions must be re-entrant.  Care should be taken to not
    leave interrupts disabled for long periods of time.

-   Allocation of a zero length extended memory buffer is allowed.  Programs
    which hook XMS drivers may need to reserve a handle for private use via
    this method.  Programs which hook an XMS driver should pass all requests
    for zero length EMBs to the next driver in the chain.

-   Drivers should control the A20 line via an "enable count."	Local En-
    able only enables the A20 line if the count is zero.  It then increments
    the count.	Local Disable only disables A20 if the count is one.  It
    then decrements the count.	Global Enable/Disable keeps a flag which
    indicates the state of A20.  They use Local Enable/Disable to actually
    change the state.


IMPLEMENTATION NOTES FOR HIMEM.SYS:
-----------------------------------

-   HIMEM.SYS currently supports true AT-compatibles, 386 AT machines, IBM
    PS/2s, AT&T 6300 Plus systems and Hewlett Packard Vectras.

-   If HIMEM finds that it cannot properly control the A20 line or if there
    is no extended memory available when HIMEM.SYS is invoked, the driver
    does not install itself.  HIMEM.SYS displays the message "High Memory
    Area Unavailable" when this situation occurs.

-   If HIMEM finds that the A20 line is already enabled when it is invoked,
    it will NOT change the A20 line's state.  The assumption is that whoever
    enabled it knew what they were doing.  HIMEM.SYS displays the message "A20
    Line Permanently Enabled" when this situation occurs.

-   HIMEM.SYS is incompatible with IBM's VDISK.SYS driver and other drivers
    which use the VDISK scheme for allocating extended memory.  However, 
    HIMEM does attempt to detect these drivers and will not allocate the
    HMA if one is found.

-   HIMEM.SYS supports the optional "/HMAMIN=" parameter.  The valid values
    are decimal numbers between 0 and 63.

-   By default, HIMEM.SYS has 32 extended memory handles available for use.
    This number may be adjusted with the "/NUMHANDLES=" parameter.  The
    maximum value for this parameter is 128 and the minimum is 0.  Each
    handle currently requires 6 bytes of resident space.


Copyright (c) 1988, Microsoft Corporation