MAXLIB.DOC
                   ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                   Documentation for MAXLIB For PB










                                  Copyright 1994 Brian McLaughlin
                     ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                                              All Rights Reserved








                         TABLE OF CONTENTS

                                                      line number

    INTRODUCTION .......................................   62

         About This Document ...........................  105
         MAXLIB For PB is Shareware ....................  124
         PBFiles is Yours - Free! ......................  158
         Requirements for Using MAXLIB For PB ..........  191
         Limited Warranty ..............................  227


    HOW TO USE MAXLIB FOR PB

         Using $LINK and $INCLUDE ......................  265
         Using MAXLIB in the IDE  ......................  310
         Getting Started with MAXFiles .................  340
         Getting Started with MAXArray .................  537
         Handling Errors ...............................  711


    GENERAL TOPICS

         About File Pointers ...........................  852
         About Expanded Memory .........................  967
         About DOS STDxxx Devices ...................... 1040
         Avoiding Problems With HUGE Arrays ............ 1116
         Safeguarding Your Data ........................ 1218





    INTRODUCTION


    MAXLIB For PB is designed to make your programs faster and more
    capable than ever before.  And because MAXLIB For PB builds upon
    familiar BASIC commands and ideas, it is easy to learn and easy
    to incorporate into your code.

    MAXLIB for PB consists of two complete sets of routines:
    MAXFiles and MAXArray.  Both of them provide you with easy, but
    sophisticated memory management.  Each one presents you with a
    different interface and its own set of strengths, so you can
    choose the one that best suits your needs.

    The 25 commands in MAXFiles are patterned after the BASIC
    commands used with disk files (especially files opened for
    binary access).  MAXFiles speeds up your program's disk file
    access by loading disk files into expanded memory as they are
    opened.  From then on, your program will read from and write to
    the file in expanded memory, which is much faster than if the
    file were accessed directly from the disk.

    MAXFiles takes advantage of whatever expanded memory is
    available (if any) and will automatically fall back to using
    disk space when expanded memory is exhausted.  For that reason,
    programs written using MAXFiles can run on computers with no
    expanded memory, or with very little, or a lot -- all using the
    same few lines of code!

    The 16 commands in MAXArray are patterned after the BASIC
    commands used to dimension and manage arrays in conventional
    memory.  With MAXArray you can create and manage arrays that are
    much larger than 640K, right up to the limit of available EMS
    memory, without having to learn all the intricacies of expanded
    memory management.

    MAXArray lets you copy entire files or conventional arrays into
    and out of expanded memory using a single line of code!  And
    because it has less internal complexity, MAXArray is even faster
    than MAXFiles.



    ABOUT THIS DOCUMENT


    This file (MAXLIB.DOC) discusses topics of general interest to
    anyone using MAXLIB For PB.  Technical details for each routine
    are available in the file MAXLIB.REF.

    In this document the terms "expanded memory" and "EMS" are used
    (somewhat loosely) to mean the same thing.

    In this document the term "EMS file" refers to a file loaded
    into expanded memory and being accessed there, as opposed to a
    file that is located on a disk drive.  The term "EMS array"
    refers to an array stored in expanded memory and accessed there,
    as opposed to an array stored in conventional memory.




    MAXLIB FOR PB IS SHAREWARE


    MAXLIB For PB is shareware.  It is not free software.  You are
    expected to pay for MAXLIB For PB, if you decide to keep it and
    use it.

    Shareware may be freely copied and distributed, eliminating the
    high distribution costs associated with most commercial
    software.  The shareware method also allows you to evaluate
    whether MAXLIB For PB meets your needs and does what it is
    supposed to do, before you pay for it.

    Programs you write using this evaluation copy of MAXLIB For PB
    must be for the purpose of evaluation only.  Under no
    circumstances are you allowed to compile and distribute programs
    incorporating MAXLIB For PB, unless you have the appropriate
    license.  To obtain an appropriate license you must register
    MAXLIB For PB.

    All the information you need in order to register MAXLIB For PB,
    including what it costs and what you get when you register, is
    contained in the file REGISTER.TXT.  You'll find an easy to
    print order form in the file ORDER.FRM.

    MAXLIB For PB represents the end product of hundreds of hours of
    skilled labor, spent in designing, programming, testing and
    documentation.  I believe MAXLIB For PB will meet your
    professional standards and that it compares well to any
    programming library of its kind.  I hope you agree.




    PBFILES IS YOURS - FREE!


    As part of the package distributed with MAXLIB For PB, you will
    find a file called PBFILES.ZIP.  It contains the source code,
    object file and documentation for a file i/o library called
    PBFiles.  PBFiles is functionally identical to MAXFiles, except
    it has no support for emulated file i/o in expanded memory.

    I have placed the source code for PBFiles into the public
    domain.  That means PBFiles is free for you to use as you wish.
    It requires no payment or fees of any kind.  PBFILES.ZIP also
    includes PBFILES.DOC, a copyrighted file you may freely
    distribute.

    The only conditions I have placed on copying PBFILES.DOC is that
    it must not be altered, and it must always be accompanied by
    unaltered copies of the source code file and two other files.

    I wrote PBFiles and included it with MAXLIB For PB so that the
    code you write for the purpose of evaluating MAXFiles will
    remain useful, even if you decide not to register MAXLIB.  This
    should adequately compensate you for the time and effort you
    spend in evaluating MAXLIB For PB.

    It is simple to convert any code you have written for MAXFiles
    to use PBFiles instead.  If you change your mind later and
    decide to register MAXLIB For PB, all the code you wrote using
    PBFiles will painlessly convert back for use with MAXLIB For PB.




    REQUIREMENTS FOR USING MAXLIB FOR PB


    To use MAXLIB For PB you must have a copy of the PowerBASIC 3.0b
    compiler or later.  I have tested MAXLIB For PB with the
    PowerBASIC 3.0a release and found that because of bugs in that
    compiler, MAXLIB For PB is not stable.

    You must also have a copy of the library file MAXLIB.PBL which
    is included as part of MAXLIB For PB.

    MAXLIB is written in 8086 assembly language and should run on
    any 80x86-based computer.  MAXLIB only uses DOS functions that
    are present in every version of DOS numbered v2.1 and later.

    The MAXFiles portion of MAXLIB For PB is designed to operate
    with or without expanded memory, but it requires the presence of
    an EMM driver v4.0 (or better) for the EMS features to be
    active.

    The MAXArray portion of MAXLIB For PB requires the presence of
    expanded memory.  MAXArray should work with all versions of EMM
    driver software numbered v3.0 and later.

    NOTE: Although MAXLIB For PB includes some support for networks,
    it has not been tested in a networked environment.  If you
    intend to use MAXLIB For PB on a network, you should test your
    code thoroughly to ensure it is network-safe.

    PowerBASIC is a trademark of PowerBASIC, Inc of Carmel,
    California.





    LIMITED WARRANTY


    THIS COPY OF MAXLIB FOR PB (THE "SOFTWARE") IS PROVIDED ON AN
    "AS IS" BASIS.  BRIAN MCLAUGHLIN (THE "AUTHOR") DISCLAIMS ALL
    WARRANTIES RELATING TO THE SOFTWARE, WHETHER EXPRESSED OR
    IMPLIED, INCLUDING BUT NOT LIMITED TO ANY IMPLIED WARRANTIES OF
    MERCHANTABILITY OR FITNESS FOR A PARTICULAR PURPOSE.  NEITHER
    THE AUTHOR NOR ANYONE ELSE WHO HAS BEEN INVOLVED IN THE
    CREATION, PRODUCTION, OR DELIVERY OF THE SOFTWARE SHALL BE
    LIABLE FOR ANY INDIRECT, CONSEQUENTIAL, OR INCIDENTAL DAMAGES
    ARISING OUT OF THE USE OR INABILITY TO USE SUCH SOFTWARE, EVEN
    IF THE AUTHOR HAS BEEN ADVISED OF THE POSSIBILITY OF SUCH
    DAMAGES OR CLAIMS.  THE PERSON USING THE SOFTWARE BEARS ALL RISK
    AS TO THE QUALITY AND PERFORMANCE OF THE SOFTWARE.

    This agreement shall be governed by the laws of the State of
    Oregon and shall inure to the benefit of the author and any
    successors, administrators, heirs and assigns.  Any action or
    proceeding brought by either party against the other arising out
    of or related to this agreement shall be brought only in a STATE
    or FEDERAL COURT of competent jurisdiction located in Clackamas
    County, OR.  The parties hereby consent to in personam
    jurisdiction of said courts.





    HOW TO USE MAXLIB FOR PB


    This section contains enough information to get you started
    using MAXLIB For PB.  More detailed information is available in
    the file MAXLIB.REF.



    USING $LINK AND $INCLUDE


    Every program that uses MAXLIB For PB must meet a few simple
    requirements: it must make the library file MAXLIB.PBL available
    to the PB compiler, and it must include declarations for all the
    routines it uses from MAXLIB For PB.

    By far the easiest way to meet these requirements is to add two
    simple lines of code near the beginning of your source code.
    The first line uses the $LINK metacommand to incorporate
    MAXLIB.PBL into your program.  You must place this line before
    any executable commands in your source code:


        $LINK "MAXLIB.PBL"


    If MAXLIB.PBL is not in the current directory, you must tell PB
    how to find it by including the full path in the the file spec.
    For instance, if MAXLIB.PBL were on a RAM disk designated as
    your D: drive, in a subdirectory named LIB, the full file spec
    would be:


        $LINK "D:\LIB\MAXLIB.PBL"


    You will also need to include a second line near the top of your
    source code:


        $INCLUDE "MAXLIB.BI"


    MAXLIB.BI contains the declarations for all the routines in
    MAXLIB For PB.  The above line of code above includes those
    declarations in your code.  Again, if MAXLIB.BI is not in the
    current directory, you will need to let PB know how to find it
    by including the full path in the file spec.





    USING MAXLIB IN THE IDE


    If you program within the PowerBASIC IDE (called PB.EXE), you
    should realize that the IDE, by default, uses all the EMS
    resources on your computer.

    If you do not change this default behavior, there will not be
    any expanded memory available to your programs that use MAXLIB,
    when you compile them and test them from inside the IDE.  With
    no EMS to work with, commands in MAXFiles will always fall back
    to disk access and commands in MAXArray will not work at all.

    The same problems apply to running your programs under PBD.EXE.

    To change the defaults for PB.EXE or PBD.EXE, you must run
    PBINST.EXE.  Choose the menu item "Limit EMS/XMS usage".  You
    must choose an amount of EMS other than "ALL".

    NOTE: If you use EMM386.SYS or another memory manager that uses
    upper memory to simulate both XMS and EMS memory, then you must
    also use PBINST.EXE to limit XMS usage to an amount other than
    "ALL".  If you do not, no EMS memory will be available to your
    program, even if you limit EMS usage to zero.

    




    GETTING STARTED WITH MAXFILES


    The information in this section is designed to get you started
    with MAXFiles.  Consult MAXLIB.REF to get answers to specific
    questions about how each routine works.

    Disk access is the slowest operation on any computer.  Access to
    memory is one of the fastest.  MAXFiles is designed to speed up
    your programs by transferring as many disk operations as
    possible from the disk drive into expanded memory.

    MAXFiles is simple to learn.  You open or create the files you
    want to work with and read from them or write to them using a
    set of routines that are very similar to the file commands you
    would use with OPEN FOR BINARY files in PB.

    Here's a list of the MAXFiles routines that have close
    counterparts in PowerBASIC:


       OpenX% ................ OPEN (...FOR BINARY)
       SetAccessCode ......... ACCESS LOCK/UNLOCK/READ/WRITE, etc.
       CloseX ................ CLOSE# (close one open file)
       ClearX ................ CLOSE  (close all open files)
       PutX .................. PUT  (as a file statement)
       GetX .................. GET  (as a file statement)
       PutStX ................ PUT$
       GetStX ................ GET$
       SaveX ................. BSAVE
       LoadX ................. BLOAD
       GetLineX$ ............. LINE INPUT#
       EndX% ................. EOF  (used only with GetLineX$)
       GetLocX& .............. SEEK (as a function)
       SetLocX ............... SEEK (as a statement)
       SizeX& ................ LOF
       KillX ................. KILL
       FlushX ................ FLUSH
       ErrorCode% ............ ERR
       SetErrorCode .......... ERROR
       SetPtrBase ............ OPTION BASE



    MAXFiles also includes the following commands that have no close
    equivalent in BASIC:


       InitMAXFiles .......... initializes MAXFiles
       ClipX ................. truncates a file
       GetPtrBase% ........... returns value set by SetPtrBase
       HandleX% .............. returns latest handle opened
       SaveLineX ............. allows GetLineX to read multiple files
       SetBufferSize ......... sets size of buffer used by GetLineX
       SetDiskFile ........... (dis/en)ables use of EMS memory



    To use MAXFiles, you must call InitMAXFiles once, before you
    call any other routines.  If you do not, MAXFiles will not use
    EMS, but will only use ordinary disk i/o.  Typically, the top
    few lines of a program using MAXFiles look like this:


       $LINK "MAXLIB.PBL"        'include the MAXLIB library
       $INCLUDE "MAXLIB.BI"      'include the declarations file
       InitMAXFiles              'initialize MAXFiles


    Among other things, InitMAXFiles determines what sort of EMM
    driver is on the host machine.  If there is no EMM driver, or if
    the driver has a version number prior to v4.0, the files you
    open with MAXFiles will be ordinary disk files.

    As with BASIC, with MAXFiles you must open files before you can
    use them.  To open a file, you use the command OpenX%.  The
    command looks like this:


        FileSpec$ = "D:\SUBDIR\FILENAME.EXT"
        Handle% = OpenX%(FileSpec$)


    If there is enough expanded memory to hold the entire file,
    OpenX% copies the file into expanded memory and returns a handle
    for the file, similar to a file number in BASIC.

    On the other hand, if there isn't any expanded memory on the
    host machine, or if there isn't enough to hold the entire file,
    OpenX% opens the file as a disk file and passes the DOS file
    handle back to your program.

    You MUST keep track of the handle OpenX% returns.  You will
    refer to the file using this handle, in much the same way you
    refer to a file opened in BASIC by its file number.

    Once a file is opened, you can use other commands from MAXFiles
    to read from it or write to it, get its size, find its pointer,
    move its pointer, or close it.

    Here's an example.  Suppose you want to open a file full of long
    integers and read individual long integers from it, as randomly
    requested by the user.  The following code shows how that might
    look in BASIC:


        FileName$ = "C:\DATA\LONGINT.DAT"       ' set file spec
        FileNum% = FREEFILE                     ' get file number
        OPEN FileName$ FOR BINARY AS FileNum%   ' open the file
        Bytes& = LOF(FileNum%)                  ' get the size
        NumRecords% = Bytes& \ 4                ' calculate records

        DO
          LINE INPUT "Enter record number: "; Record$
          IF LEN(Record$) = 0 THEN EXIT LOOP
          RecordNum% = VAL(Record$) - 1         ' convert to zero-based

          SEEK FileNum%, (RecordNum% * 4)       ' set the pointer
          GET FileNum%, , RecordVal&            ' get the value
          PRINT "That record is" ; RecordVal&   ' report it
        LOOP

        CLOSE FileNum%                          ' close file



    Here is the same code, written for MAXFiles:



        FileName$ = "C:\DATA\LONGINT.DAT"       ' set file spec
        FileNum% = OpenX%(FileName$)            ' open the file
        Bytes& = SizeX&(FileNum%)               ' get the size
        NumRecords% = Bytes& \ 4                ' calculate records

        DO
          LINE INPUT "Enter record number: "; Record$
          IF LEN(Record$) = 0 THEN EXIT LOOP
          RecordNum% = VAL(Record$) - 1         ' convert to zero-based

          SetLocX FileNum%, (RecordNum% * 4&)   ' set the pointer
          GetX FileNum%, 4&, RecordVal&         ' get the value
          PRINT "That record is" ; RecordVal&   ' report it
        LOOP

        CloseX FileNum%                         ' close file


    You can see how closely the two examples resemble one another.

    As a rule, MAXFiles treats files as binary files, but there is
    one obvious exception to this rule: text files.  Because they
    are difficult to read using purely binary methods, MAXFiles
    includes the command GetLineX$, for reading text files one line
    at a time, like BASIC's LINE INPUT# command.  It comes with its
    own substitute for EOF, too, called EndX%.

    You call GetLineX$ in a loop, like this:


        Handle% = OpenX%("TEXTFILE.TXT")
        DO
           TextArray$(X%) = GetLineX$(Handle%)
           INCR X%
        LOOP UNTIL EndX%


    Reading a text file is just that simple.

    Normally, when you append data to an EMS file there will be
    enough expanded memory to hold it.  But sometimes there simply
    won't be any more expanded memory available to hold the new
    data.  In those cases, MAXFiles will convert the EMS file to a
    disk file, on the fly.

    IMPORTANT: When MAXFiles converts an EMS file into a disk file
    on the fly, the value of the Handle% variable will be changed,
    too.  From then on, all references to the file must use the new
    value in Handle%.  This may cause problems if your program
    maintains secondary copies of the Handle% variable.

    Overall, if you are comfortable with binary file handling in
    BASIC, you should have no trouble adapting to MAXFiles.  Even
    so, one topic where you might need extra guidance is error
    handling with MAXFiles.  For more information, see the chapter
    on HANDLING ERRORS.

    If you are not familiar with binary file handling and file
    pointers, see the chapter ABOUT FILE POINTERS.

    Lastly, before you use MAXFiles to read from or write to HUGE
    arrays, you should read the chapter AVOIDING PROBLEMS WITH HUGE
    ARRAYS.




    GETTING STARTED WITH MAXARRAY


    The information in this section is designed to get you started
    with MAXArray.  Consult MAXLIB.REF to get answers to specific
    questions about how each routine works.

    Arrays are a central part of most programs.  They are easy to
    create and fast to access.  But sometimes you want to make more
    arrays or larger arrays than will fit in conventional memory.
    MAXArray can help to solve those problems.

    MAXArray is simple to use.  You create the arrays you want to
    work with and read from them or write to them using a set of
    routines that are very similar to the commands you would use to
    manipulate arrays in BASIC.

    Using MAXArray you can create arrays in expanded memory in which
    you can store or retreive numeric or TYPE variables, as well as
    fixed-length string variables.  However, MAXArray cannot store
    or retrieve variable length strings or flex strings.

    Here's a list of the MAXFiles routines that have close
    counterparts in PowerBASIC:


       DimEMS% ............... DIM
       InEMS ................. Array(Index) = Variable
       OutEMS ................ Variable = Array(Index)
       EraseEMS .............. ERASE
       RedimEMS .............. REDIM
       LBoundEMS% ............ LBOUND
       UBoundEMS% ............ UBOUND
       BytesFreeEMS& ......... FRE
       ErrorCode% ............ ERR
       SetErrorCode .......... ERROR


    In addition, MAXArray has many routines that have no counterpart
    in ordinary BASIC.


       InitMAXArray .......... initializes MAXArray routines
       ArrayInEMS ............ copies conventional array to EMS
       ArrayOutEMS ........... copies EMS to conventional array
       ClearEMS .............. erases/deallocates all EMS arrays
       FileInEMS ............. copies entire file to EMS array
       FileOutEMS ............ copies entire EMS array to file
       HandlesEMS% ........... returns max number of undimmed arrays
       VersionEMS% ........... returns version number of EMM driver


    To use MAXArray you must call InitMAXArray once, before you call
    any other routines.  Unless you call InitMAXArray the routines
    in MAXArray cannot function.

    Typically, the top few lines of a program using MAXArray look
    like this:


         $LINK "MAXLIB.PBL"        'include the MAXFiles OBJ code
         $INCLUDE "MAXLIB.BI"      'include the declarations file
         InitMAXArray              'initialize MAXArray


    The next step in using MAXArray is to dimension an array and
    put data into it.  Suppose you want to dimension an array of 100
    double precision numbers, and set the value of the 100th element
    to 2.77777.  Your code might look like this in BASIC:


        DIM DoubleArray# (1 TO 100)           ' dim array
        DblVal# = 2.77777
        DoubleArray#(100) = DblVal#           ' set value


    Here's the same code written using MAXArray:


        DoubleArray% = DimEMS%(1, 100, 8)     ' dim array
        DblVal# = 2.77777
        InEMS DoubleArray%, 100, DblVal#      ' set value


    As you see, to dimension an EMS array using DimEMS you must know
    the length (in bytes) of the elements of the array you are
    dimensioning.

    With ordinary BASIC you do not need to know that each element in
    a double precision array takes 8 bytes of storage space.  DimEMS
    requires this information.  Luckily, you can write code that
    this information very simply, by using the LEN command.

    Most BASIC programmers know that LEN will return the length of a
    string.  Many of them do not know that LEN can be used with
    variables other than strings.  For instance:


        DblLen% = LEN(DblVar#)


    In this example, DbleLen% will equal 8, which is the number of
    bytes needed to store a double precision variable.  LEN also
    works with TYPE variables, fixed length strings and all numeric
    variables.

    In ordinary BASIC, you identify an array by its name.  In
    MAXArray, you identify an array by the handle passed back to
    your program by DimEMS.  To give your array a name, just give
    the handle variable the same name you want to give to the array.

    To assign a value to an array element in MAXFiles, you use
    InEMS.  To assign a value to a variable from an array element,
    you use OutEMS.  I have given the order of the parameters in
    each of these commands the same order as their counterpart code
    in BASIC, to help you remember. Here's how they compare:


        Variable = ArrayName(Element)           'BASIC
        OutEMS Variable, ArrayHandle, Element   'MAXArray

        ArrayName(Element) = Variable           'BASIC
        InEMS ArrayHandle, Element, Variable    'MAXArray


    Once you know how to dimension arrays in EMS using DimEMS, and
    how to store or retrieve values in those arrays using InEMS and
    OutEMS, you know enough to start using MAXArray.  But there is
    more.

    To erase an array when it is no longer needed, use the command
    EraseEMS.  To erase every array you have dimensioned, all at
    once, use the command ClearEMS.  In most cases, this command
    (ClearEMS) will also be called automatically as your program
    ends, so you won't need to worry about deallocating the EMS
    memory your program has allocated through MAXArray.

    If you discover that the array you have dimensioned is too small
    or too large to hold the data you want to store, you can use
    RedimEMS to make the array larger (or smaller) without erasing
    it.  Unlike the REDIM command in PowerBASIC, data in the EMS
    arrays you redimension will be preserved.

    MAXArray also provides routines to help you determine whether or
    not sufficient EMS resources are available to meet your needs.
    These routines are functions, called BytesFreeEMS, HandlesEMS
    and VersionEMS.

    VersionEMS% returns a zero when there is no EMM driver
    installed.  Otherwise it returns the driver's version number as
    an integer, where 40 means version 4.0.

    BytesFreeEMS& returns a long integer telling how many bytes of
    EMS memory are currently unallocated and available to use.

    HandlesEMS% returns the number of unused handles in an internal
    table maintained by MAXArray.  You can only dimension as many
    arrays as there are handles, and when HandlesEMS% returns a zero
    you can't dimension another array unless you erase another array
    that is already dimensioned.

    You can also use MAXArray to copy entire arrays to or from files
    or to and from conventional memory.  To learn how, consult the
    entries for FileinEMS/FileOutEMS and ArrayInEMS/ArrayOutEMS in
    MAXLIB.REF.

    This short introduction should give you enough information to
    get started with MAXArray.  I also recommend that you read the
    chapters HANDLING ERRORS, and AVOIDING PROBLEMS WITH HUGE
    ARRAYS.




    HANDLING ERRORS


    The usual method of error handling in BASIC requires that you
    use some variation of the ON ERROR statement.  I have always
    found ON ERROR to be cumbersome, code-bloating and difficult to
    program.  Even PowerBASIC's own manual (p.288) suggests that you
    consider using a third party library.

    I think you will find the error trapping in MAXLIB to be simple
    to understand and easy to use.  Whenever an error takes place
    (including critical errors), the MAXLIB routine that was running
    at the time of the error will store the error code in an
    internal variable and return directly to your program.

    Your program must test the value of the error code variable in
    order to find out whether an error has occured.  MAXFiles and
    MAXArray share a single routine for reporting the value of
    the error code variable.  Reasonably enough, the routine is
    called ErrorCode%.

    The process of testing the value of an error code variable is
    called polling.


        Handle% = OpenX%(FileName$)
           IF ErrorCode% THEN CALL HandleError...


    In the above example, the code polls for an error directly after
    opening a file, and if ErrorCode% reports an error the code
    calls a SUB named HandleError.

    You can poll for errors as often or as seldom as you think
    necessary.  If an error takes place in one MAXLIB routine and
    your program calls several more routines before polling for an
    error, the value of the error code variable will report the most
    recent error to take place.

    The internal error code variable is initialized to zero only
    once, at the beginning of your program.  Its value will remain
    zero so long as no error takes place.

    However, when the first error takes place, the value of the
    variable will change to reflect the error code, and it will
    remain unchanged until one of two things intervenes to change
    its value:

       1) another (different) error takes place, or
       2) your program resets the value, using SetErrorCode


    SetErrorCode is similar to the function ERROR in BASIC.  You may
    use it to clear the error code variable back to zero like this:


       SetErrorCode 0


    SetErrorCode may also be used to simulate errors (for example,
    during the testing of your error handler) by passing non-zero
    values corresponding to error codes.  Then ErrorCode% will
    report these values back to your program as errors:


       SetErrorCode 2
       IF ErrorCode% THEN ....    'ErrorCode% always returns 2 here


    A list of error codes and what they mean can be found in the
    file ERRCODE.LST.  It includes descriptions of several
    non-standard error codes that might be returned by MAXLIB
    routines.  (They are: -1 through -4.)

    Because MAXLIB For PB requires your program to poll for errors,
    the error handling in MAXLIB For PB is roughly the same as ON
    ERROR RESUME NEXT used with ERR, in this fashion:


        ON ERROR RESUME NEXT             'if error happens keep going
        .
        .
        OPEN FileName$ FOR BINARY AS #1  'an error might happen here
           IF ERR THEN                   'see if an error occured
              CALL ErrorHandler          'if so, go handle it



    The equivalent code in MAXLIB would be:


        FileNum% = OpenX%(FileName$)     'an error might happen here
           IF ErrorCode% THEN            'see if an error occured
              CALL ErrorHandler          'if so, go handle it


    It is important to realize that MAXLIB For PB won't handle
    errors for you.  What MAXLIB For PB will do is trap the error
    and let you know which error it was.  To handle errors actively,
    you must use an error handler in your program.

    The writing of an error handler is not difficult to understand.
    A typical error handler will consist of a SELECT CASE structure
    in which the various errors you anticipate are grouped according
    to the various messages you want to display or actions you want
    your program to take.


        SELECT CASE ErrorCode%
           CASE 2
              PRINT  "File not found."
           CASE 3
              PRINT  "Path not found."
           CASE 4
           .
           .
           CASE ELSE
              PRINT  "Unknown error. Error code:"; ErrorCode%
        END SELECT


    At the very least, an error handler reports error codes along
    with descriptive messages.  A more comprehensive error handler
    will allow your program the chance to resolve the error, or to
    shut down gracefully and save your data if possible.





    GENERAL TOPICS


    The following section covers several topics of general interest
    to programmers using MAXLIB For PB in their programs, including
    information about some problems you might encounter when using
    MAXLIB For PB, and how to avoid them.




    ABOUT FILE POINTERS


    It is possible to program in BASIC without ever learning about
    file pointers.  However, MAXFiles requires that you understand
    file pointers, so if you are unfamiliar with them, please read
    this section.

    NOTE: DOS, PB and MAXFiles all consider a file's first byte to
    be byte zero rather than byte 1. Although MAXFiles does let you
    choose the one-based convention, this section will use the
    zero-based convention throughout.

    Think of a file pointer as an invisible finger pointing at the
    exact byte where MAXFiles will begin to read from or write to a
    file.  It will move itself as you read (or write), like a finger
    following text on the page of a book.  As you stop reading (or
    writing) the finger stops itself one byte beyond the last byte
    read (or written).

    When a file is first opened the pointer is at the first byte of
    the file: byte zero.  If you start writing to a file right after
    opening it, you will start writing at byte zero.  And if any
    data is in the file it will be overwritten by the new data,
    starting with byte zero.

    Luckily, you can move the pointer anywhere you want, anytime you
    want.  For the sake of simplicity, let's suppose you have a file
    that is four bytes long and you want to append some data to the
    end of this file.  The four bytes would run from zero to 3:


       BYTES:  0  1  2  3
               ^

    Since you have just opened the file, the pointer (^) is at byte
    zero.  Before you can append data to the end of a file, the
    pointer must point one byte beyond the file's last byte.  In
    this case the last byte is byte 3, and one byte beyond byte 3 is
    byte 4.

    To move a pointer for appending data, first you need to know how
    long the file is.  In BASIC you could use LOF, but in MAXFiles
    you would use SizeX&, like so:


       Handle% = OpenX%(FileName$)
       Size& = SizeX&(Handle%)


    In this case, Size& will equal 4, because our file is four bytes
    long.  And, conveniently, the byte that is one byte past the end
    is byte 4. You may move the pointer to byte 4, using SetLocX:


       Size& = SizeX&(Handle%)    'Size& = 4
       SetLocX Handle%, Size&     'pointer is at byte 4


    Now our file looks like this:


       BYTES:  0  1  2  3 (4)
                           ^

    I put the 4 in parentheses because it really doesn't "belong to"
    our file yet, even though the pointer points there.  Now, if we
    write something to our file, no old data will be overwritten.

    Now let's write some data to our file and see what happens.  To
    write data, you can use PUT in BASIC.  In MAXFiles you could use
    PutX.  This is how you'd write an integer to the file:


       PutX Handle%, 2&, Variable%


    This writes 2 bytes to the end of our file, so it looks like
    this:


       BYTES:  0  1  2  3  4  5  (6)
                                  ^

    Now there are six bytes in our file (0-5) and the pointer has
    moved to byte 6. The pointer moves each time we write OR read
    bytes.  It moves exactly one byte forward for every byte we read
    or write.

    Those last two sentences are VERY important:

    * The pointer moves each time you write OR read bytes.  It moves
    exactly one byte forward for every byte you read or write. *

    If you do not know where the pointer is, you can get into big
    trouble.  To avoid such trouble you can always ask where the
    pointer is by calling GetLocX&.  Just remember that when
    GetLocX& tells you the pointer is at byte 1, it is referring to
    the second byte of the file.

    That covers all you need to know about file pointers.  All in
    all, file pointers allow you to read or write anywhere you want
    in a file.  You can open a file, read a few bytes, jump
    somewhere, write over some other bytes, jump to the end, tack on
    some bytes there, then jump back to the start - all without
    having to close and reopen your file.

    You are not required to having same-length records.  You are not
    required to start at the front and plow straight to the end.
    You can order your data anyway you like and put it anywhere
    that's convenient, just by jumping the pointer there.




    ABOUT EXPANDED MEMORY


    This chapter gives you a quick overview of expanded memory and
    how it works.  If you are already familiar with EMS, you may
    skip this section.

    The first verison of EMS was version 3.0.  More precisely,
    versions prior to 3.0 were not made public.  As of this writing,
    the EMS specification is in version 4.0 and it looks likely to
    stay there.

    All manipulation of EMS memory is accomplished through calls to
    an EMM driver, a piece of software loaded through CONFIG.SYS.
    Calls to the EMM driver are made through interrupt &H67.  One
    common EMM driver is EMM386.SYS.  It has been distributed with
    DOS since v5.0.  Without a driver, EMS can't be used, even if it
    is installed.

    EMS requires that one 64K segment be set aside for its exclusive
    use, in the memory area starting at D000:0000 or E000:0000.
    This 64K segment is subdivided into 4 areas of 16K each,
    numbered 0-3.  These areas are sometimes called "frames".

    To use expanded memory, you must allocate it first.  Normally,
    EMS memory is allocated 16K bytes at a time.  This is the method
    used by MAXLIB For PB.  Each 16K chunk of memory is called a
    "page".  It is no accident that pages and frames are the same
    size.

    You may allocate a group of many pages or just a single page.
    The group is assigned a handle, like a file handle.  Most calls
    to the EMM driver require that you refer to this handle.

    The first page in a group is called page 0, the next is page 1,
    and so on.  At the hardware level, no two pages in a single
    group need to be stored in contiguous memory.  They can be
    scattered all over the physical address space of the EMS memory.
    But the driver takes care of that detail for you.  As far you
    know, page 0 comes first, page 1 comes next.  Sometimes
    ignorance is bliss!

    Before you can write to or read from any of the pages you have
    allocated, the page must first be "mapped" into a frame.  This
    is done by calling the EMM driver.  Once a page is mapped into a
    frame, the whole contents of the EMS page are copied into the
    memory that resides inside that frame.  After this is done, any
    alteration to the memory inside the frame will be reflected in
    the memory of the page.

    Since only 4 frames exist, but a much larger number of pages may
    exist, pages generally must be shuffled in and out of these
    frames (a lot).  This scheme is called "bank switching" and it
    has been around a long time.

    One peculiarity of EMS memory is the fact that it will not be
    deallocated as your program ends.  Program memory (the famed
    first 640K) is automatically released by DOS when a program
    ends, unless the program is a TSR.  But EMS memory remains
    allocated to the same handle until you actively deallocate it by
    calling the EMM driver.

    A program that allocates EMS and ends without releasing it, can
    effectively prevent any subsequent programs from using that EMS
    memory.  To prevent this from happening in your programs, MAXLIB
    For PB will automatically deallocate all the EMS memory you have
    allocated with them, as your program ends.  For more details
    about this, see ClearX and ClearEMS in MAXLIB.REF.





    ABOUT DOS STDXXX DEVICES


    Each time your computer boots, DOS opens a set of 5 handles,
    numbered 0-4.  These handles are assigned to 5 standard devices.
    DOS uses these handles to access the devices for its own input
    and output.  They are:


       Device:      Handle:      Initialized as:
       -------      -------      ---------------
        STDIN          0            Keyboard
        STDOUT         1             Screen
        STDERR         2             Screen
        STDAUX         3           Com port 1
        STDPRN         4          Printer (LPT1)



    Because MAXFiles uses the same handle-based services that DOS
    uses, you can take advantage of these STDxxx devices by passing
    their handles to the various MAXFiles routines.

    You should realize that using DOS devices can be a crude method
    of input and output.  Only in a few situations will there be any
    advantage to using them, and in many cases there will be
    disadvantages.  Most especially, I would NOT recommend using
    MAXFiles with STDAUX as a replacement for the built-in
    communications ability of PowerBASIC!

    However, two examples come quickly to mind where a STDxxx device
    has an advantage over using BASIC's own commands.  One is where
    you want to direct your program's output through the ANSI.SYS
    device driver.  The other is when you want to be able to
    redirect or pipe input or output from the command line.

    To output a string to the screen through DOS services, you could
    use BASIC code similar to this:


       OPEN "CONS:" FOR OUTPUT AS #1
       OutPut$ = "This will reach the screen via DOS."
       PRINT #1, OutPut$


    The MAXFiles equivalent would be this:


       %STDOUT = 1
       OutPut$ = "This will reach the screen via DOS."
       PutStX %STDOUT, OutPut$ + CHR$(13,10)


    In this example, OutPut$ would be (normally) be written to the
    screen by DOS.  If DOS redirection were in effect, the string
    would be output to the device or file indicated by the
    redirection symbol on the command line, instead of to the
    screen.

    If OutPut$ included ANSI escape codes, routing OutPut$ through
    DOS makes it available to interpretation by ANSI.SYS.

    Most of the routines in MAXFiles will accept STDxxx handles,
    with two exceptions.  CloseX will not close a handle numbered
    0-4, and GetLineX$, because of its internal buffer and internal
    pointer, cannot accept a DOS device handle, either.

    Overall, if you require DOS redirection in your programs, you
    should be able to swing it, using just the routines in MAXFiles.
    But it may take some experimentation.  For more information
    about DOS STDxxx devices, you should consult a good DOS
    reference.




    AVOIDING PROBLEMS WITH HUGE ARRAYS


    HUGE arrays are larger than a single 64K segment.  PowerBASIC
    3.0 lets you create HUGE arrays where the length of each element
    is not a power of two (the length is not 2,4,8,16...etc).

    To accomplish this feat the PowerBASIC compiler must recognize
    when the end of the current array segment does not contain
    enough bytes to hold a complete array element.

    Let's say you want to dimension an array of 1000 fixed length
    strings, where each string is 80 bytes long:


        DIM HUGE FixedStrings(1 TO 1000) AS STRING * 80


    The compiler can put 819 elements of 80 bytes each into the
    first 64K segment.  At that point the segment contains 65520
    bytes of data with only 16 bytes left in the segment.  That's
    not enough to hold a complete element, so the compiler will
    insert 16 "padding" bytes into the array at that point.  This
    permits element 820 to start at a new 64K segment boundary.

    In PowerBASIC, placing a discontinuity like this into the data
    is not a problem, because array elements are always accessed
    individually.

    Unlike PowerBASIC, MAXLIB For PB has routines that allow you to
    access entire arrays all at once.  These routines are GetX and
    PutX in MAXFiles, and ArrayInEMS and ArrayOutEMS in MAXArray.

    These commands always read data as a continuous series of bytes.
    If the compiler has stored the data in a discontinuous series of
    bytes, it causes problems.  In our example using the fixed
    length string array, a discontinuity of 16 bytes occurs between
    elements 819 and 820.

    To demonstrate the problem more clearly, let's say you want to
    save a copy of that HUGE fixed length string array into a file,
    using PutX.  It might seem natural to write code like this:


        FileName$ = "FIXSTRNG.DAT"
        SaveHandle% = OpenX%(FileName$) ' open a file to save into

        Bytes& = CLNG(80 * 1000)        ' calculate bytes to save
        PutX SaveHandle%, Bytes&, FixedStrings(1)    'save them


    This code contains a bug.  The problem comes in the third line,
    where we calculate how many bytes we need to write into the
    file.

    Yes, there are 80000 bytes of data to be read, but because of
    the 16 unused bytes that were inserted at the end of the first
    64K segment, those 80000 bytes of data are stored across 80016
    bytes of memory!

    The bug comes in, because PutX is not smart enough to skip over
    the 16 bytes of non-data inserted into the array.  Instead it
    will read those 16 bytes of padding into the file and it will
    not read the final 16 bytes of data.

    The easy way to work around this problem is to read each element
    individually, in a loop, and write each one to the file:


        FileName$ = "FIXSTRNG.DAT"
        SaveHandle% = OpenX%(FileName$) ' open a file to save into

        Bytes& = 80&                    ' read one element at a time
        FOR X% = 1 TO 1000
          PutX SaveHandle%, Bytes&, FixedStrings(X%)
        NEXT X%


    This is not the fastest solution possible, but it is by far the
    simplest.  It is not the fastest because it requires your
    program to access the disk 1000 times, instead of once.

    Another possible work around is to make the disk file 80016
    bytes long, so it contains all the data, along with the gap in
    the data.  Then you could load the resulting file directly into
    any HUGE array that is identical to the original array, because
    an identical array will have the same gap in the data, located
    in the same place!

    This last approach is rather inflexible, but it is certainly
    fast, since it uses the least number of disk reads or writes.

    If you are using ArrayInEMS and ArrayOutEMS instead of GetX and
    PutX, the range of solutions is even narrower.  Simply put, you
    cannot use ArrayInEMS or ArrayOutEMS with any HUGE array that
    has an element size which is not a power of two.  With such
    arrays, you must use InEMS and OutEMS one element at a time.





    SAFEGUARDING YOUR DATA


    This section is meant to help you to design your programs
    written with MAXLIB For PB to be as safe as possible.  The major
    concern is that any data that is stored in EMS will disappear
    without a trace when the power turns off.  In this respect
    expanded memory is just like conventional RAM.

    Data stored in EMS arrays using MAXArray should be considered to
    be as vulnerable as data kept in ordinary arrays.  There are no
    ways to make it safer.  With MAXFiles, however, there are some
    safeguards built in, and others you can add.

    Normally, as your program ends, MAXFiles ensures that every file
    you have opened is written safely to disk.  However, power
    surges, frozen keyboards, critical errors and other disruptions
    do happen, and you should design your program around their
    possibility. This section tells you how.

    The first question you must ask is: how vital is this data?  I
    can't answer that one for you.  Among other things, you should
    consider whether the data can be reconstructed from existing
    data, and what portion of the data you could place at risk
    before the risk becomes unacceptable.

    The second question is: how can I make my data as safe as
    possible, using MAXFiles?  I will try to answer that one.

    For files that absolutely MUST be written to a physical disk as
    quickly as possible, MAXFiles gives you the option of forcing a
    particular file to be opened as a disk file.  The command for
    this is called SetDiskFile.

    When you call SetDiskFile with a non-zero value, the next file
    opened and all subsequent files will be disk files.  To permit
    MAXFiles to open EMS files again, call SetDiskFile once more,
    passing it a zero value.



        SetDiskFile 1                     'force disk-only
        Handle% = OpenX%("importnt.dat")  'open as a disk file
        SetDiskFile 0                     'resume default setting



    There is another, less drastic tool you can use to safeguard
    important data, while preserving the speed and convenience of
    letting MAXFiles manage your files in EMS.  It is called FlushX.

    When you call FlushX with the handle for an EMS file, FlushX
    will open a disk file and copy the entire current contents of
    that file from expanded memory onto disk.  It does this very
    rapidly.  Then the disk file is closed, which flushes the
    contents of any DOS buffers to disk as well.

    The drawback to FlushX is that writing an entire file to disk,
    even quite rapidly, is relatively slow.  Calling FlushX every
    time data is added to a file will completely defeat the purpose
    for using EMS in the first place - speed.  Such a strategy would
    be slower than simply opening a disk file and writing to it
    incrementally.

    A more successful strategy for using FlushX might be to call it
    at every 100th iteration of a loop.  Or you could invoke ON
    TIMER and call it every time a certain interval had passed.
    Only you can decide how to use this tool.  But it is there to be
    used if you need it.

    Bear in mind that these precautions are most applicable when a
    file has been opened as an EMS file.  Because MAXFiles will
    function perfectly well on computers having no EMS, you may want
    to determine whether a particular file has been opened as an EMS
    file or a disk file.

    To see if a file was opened as an EMS file or a disk file,
    examine the handle passed back by OpenX%.  A file stored in EMS
    will have a handle greater than 255.  A disk file will have a
    handle less than 255.