FUNCTION: NETPERSIST()
 Persistent attempt execute a code block.
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
 Syntax:
      NetPersist( <bBlock>, [<nSeconds>] ) --> lSuccess

 Arguments:

     <bBlock> is a code block which NetPersist will attempt
     repeatedly to execute.  The attempts will be made at
     intervals of NET_WAIT seconds while the block returns FALSE.
     The attempts terminate when either 1) the block returns
     TRUE, or 2) the lessor of a) nSeconds or b) NET_SECS has
     been exceeded.

     [<nSeconds>] is the time in seconds to retry operation,
     defaults to NET_SECS.  If zero is specified, then the
     operation is attempted without time limit.

 Returns:

     TRUE if <bBlock> was executed, FALSE otherwise.

 Description:

     This function is useful in networked applications where
     certain operations may fail due to network conflicts on the
     initial attempt, such as obtaining record or file locks, but
     may be successful on subsequent attempts.

     NetPersist will make repeated attempts to execute any code
     block until either the codeblock returns TRUE, or the upper
     limit of persistency time is exceeded (in which case
     NetPersist returns FALSE).

     The codeblock you supply must return FALSE if the attempt to
     execute fails and must return TRUE when the operation is
     successful.

     The file netutils.ch defines pre-processor commands that
     implement NetPersist for file and record locking and
     for appending records

 Examples:

     lSuccess := NetPersist({|| FLOCK() })

 Header File: netutils.ch

 Source: N_PERSIS.PRG

 Author: Berend M. Tober
See also: NETAPPEN NETDEL NETMODE NETPACK NETRLOCK NETUSE NETUTILS