DISKSECURE II version 2.42


Hard Disk Protection Program	      Copyright (c)1990, 1991, 1993, 1994 
				      by Padgett Peterson
                                      All Rights Reserved
	




		  I  - Why low-level protection ?

		 II  - What is DISKSECURE II ?

		III  - How is DISKSECURE II Loaded ?

		 IV  - How is DISKSECURE II Removed ?

		  V  - Malicious Software (viruses) and DISKSECURE II

		 VI  - Return Codes

		VII  - Licensing - Now FreeWare

	       VIII  - Weasel-words

	 Appendix A  - Hidden Sectors/Changing MBR/Changing DBR

	 Appendix B  - DS2BYP and DS2MOVE

	 Appendix C  - Other Files


                  I - Why Low-Level Protection ?

	Today there are many anti-viral software products available
for the IBM-PC (and clones) platform running MS-DOS, OS/2, and UNIX but 
nearly all are invoked following load of the operation system (usually
from CONFIG.SYS or AUTOEXEC.BAT in MS-DOS).  In many cases this is too late
for effective protection from common boot sector infectors (BSI) such as
STONED, MICHELANGELO, or the MUSICBUG.  In the case of the "stealth" 
variants, even state-of-the-art anti-virus routines such as the McAfee 
programs must rely on detection of a viral signature in memory rather than 
detection of infected files.

	At the operating system level, too many extra programs have been 
piled upon the basic disk access routines to be able to reliably separate 
the actions of legitimate drivers and TSRs from the activity of malicious 
software.

	There is a point at which executable code may be placed that
will always be executed during the boot of a hard disk when the low
level activities have not yet been masked - during the execution of
the Master Boot Record.  At this point the organization of a PC is defined 
according to the IBM BIOS specification. In most cases this structure is
impossible for malicious software to subvert without causing a detectable 
change.  As of August, 1993 there are no known boot sector viruses that 
can bypass detection at this level.

	Additionally, there are many access control packages available
that provide strict control and full encryption of systems.  DISKSECURE II
does not attempt to do this, rather it is intended as a simple, unobtrusive
primary access and virus control mechanism that does not require 
administration, and which may be installed/removed/modified with a simple 
menu-driven interface.




                   II - What DISKSECURE II Does

	Simply put, DISKSECURE II replaces the Master Boot Record on
a hard disk with its own code.  The necessary elements of the original
partition table are stored on an unused part of the disk and presented 
to the authenticated operating system as required. Unauthorized boot 
programs (such as the BRAIN, STONED, or AZUSA viruses) will not be
able to access the partition table as expected.

	DISKSECURE II has multiple elements: three are contained in the file
DISKSEC2.EXE supplied with this document.  The first is an interactive
installation/maintenance/removal module that allows the user to activate,
change, or remove DISKSECURE II from a hard disk. The second is a replacement
for the hard disk partition table that performs load-time checking, prevents
DOS access to the hard disk if booted from a floppy, and contains the 
password access routine if implemented.  The third element is a resident
protection program that takes up 1k of RAM memory and protects the partition
table, hidden sectors, and boot sector of a conventionally partitioned hard 
disk.

	To this, DISKSECURE II adds Novell Server compatability, Windows
3.1 32BitDiskAccess compatability, and the ability to transform itself
from a 1K TSR at the Top of Memory into a 304 byte TSR in low memory (DOS
3.2 and above only).

	Once loaded, DISKSECURE II will prevent access to the fixed disk from
DOS if the resident portion of DISKSECURE II is not in memory.  If password
access has been invoked, this password must be given before DISKSECURE II 
will become resident, allow the OS to load, and before DISKSECURE II can be 
changed or removed.

	In the event of accidental booting from an infected floppy disk,
DISKSECURE II adds the ability to automatically detect and disinfect any
virus that does not overwrite the MBR. Such viruses are rare though these 
will render the system unbootable. In this event, the Recovery Disk has two
different means for recovery (use of the DiskSec2.exe and the Dspart.dat
files). 

	Recently, a single easily detectable virus has been seen which 
blindly corrupts the Dos Boot Record. DS II will detect these and removal 
is generally a matter of booting through DS II to a floppy and using the 
BYPASS module to SYS the fixed disk. This mechanism should work so long as 
the fixed disk is accessible on a floppy boot (cntrl key depressed).

        However, the user must realize that should a boot from an infected
floppy occur before DS II loads, anything could happen and the best that
can be done is to detect that action. See the comments on BIOSes which allow
boot disk selection.

	DISKSECURE II adds the capability to boot from a conventional floppy
if the Ctrl key is held down during boot. No special Maintenance floppy is 
needed. This should remove all opposition to setting those BIOSes which
permit it to boot from the fixed disk only. 

	Other elements of DISKSECURE II include an automated installation 
program  (DS2INST.BAT) - installation may be dome manually if desired,
a program to verify proper operation of DISKSECURE II (DS2CHK.EXE), a
program to move the DISKSECURE II TSR into low memory (DSMOVE.SYS), and 
a program to allow compatability with incompatible programs (DS2BYP.EXE).




               III - How  DISKSECURE II is Loaded 

	The modification program may be loaded either from the fixed
disk or from a separate, bootable floppy (recommended).  It is designed
to recognize if DISKSECURE II is resident, will make many checks to
ensure the integrity of the program, and will warn the user of anything
unusual that it finds.  

	If DOS 6.0 or above is in use, it is suggested that DS II be 
installed following a "Bypass Boot" (press F5 during boot so that
CONFIG.SYS and AUTOEXEC.BAT are bypassed)

	THE DISKSEC program is invoked by executing from either the DOS 
prompt (automatic installation from other OSs is not yet available) or a
batch (DSINSTALL.BAT) file.  DISKSECURE II will check the number of fixed 
disks present and verify this with the user before proceeding.  Following 
this, DISKSECURE II will require the user to input a password if this 
additional protection is in use before proceeding.  At this point, a 
first-time user will be presented with a warning message before the menu 
is presented.  The user may then select a choice from the menu (the menu 
will change to accommodate the state of DISKSECURE II in the system).

	During installation, the user will be asked to save the partition
tables to a file (default: DSPART.COM).  This file should be copied to
a known clean, bootable floppy disk.  If all else fails, the system may be
booted from the floppy, and DSPART executed. Even if the disk is 
unrecognizable by DOS, this will replace the partition table.  WARNING: if 
this file is executed on a machine other than the original or the partition 
table has been changed by repartitioning all data on the disk could be lost.

	Where multiple machines are to be protected, it is suggested that
each machine have a unique and identifiable recovery disk and DSPART.DAT
be renamed to identify it with each creating PC. However recovery files
for multiple machines can be stored on a single floppy along with a single
copy of DiskSec2.exe.

	Should it be necessary to repartition a disk or the operating
system upgraded, it is necessary that the simple removal procedure be 
followed first as DISKSECURE II will trap any attempt to write to the MBR,
hidden sectors, or the boot record. DS2BYP should not be used for this
function as essential signatures will have changed and on the next boot
the machine may be restored to the previous condition.

	Also provided is the program DS2CHK.EXE.  This will allow the user 
to check if DISKSECURE II is in memory - on activation, nothing will return 
if DISKSECURE II is not active - the DISKSECURE II logo will display if it is 
active.  An errorlevel of (0) will return if DISKSECURE II is not found, 
(1) if DISKSECURE II is resident but not in control (e.g. QEMM 6.0+ "stealth"
in use), and (2) if in memory and in control. DS2CHK.EXE may be invoked
as part of a network login script to verify proper use on a client PC.

	The other two major programs included are DS2MOVE.SYS (explained
above) and DS2BYP.EXE. The second should be used with care and only when 
necessary to accommodate programs requiring low level access. See also
Appendix B


Note: After activation, if booted from a floppy DOS will not recognize
      the hard disk(s) and, if additional removable media are present,
      DOS may recognize them as the C: drive.  This will not affect
      the operation of DS2CHK.EXE nor will it endanger the data on the
      fixed disk.  If DISKSECURE II is removed, on the next boot the fixed 
      disk(s) will again be recognizable by DOS from a floppy. The disk will 
      always be recognized when booted from a floppy disk through DISKSECURE
      II (by holding the Ctrl key down during boot) so long as DISKSECURE II 
      maintains validity. (if failure occurs, see RECOVERY above).

      Use of the DSPART.DAT file as outlined above from a standard DOS
      bootable floppy will recover the disk even if DOS reports the 
      disk unavailable. On the next boot, the drive will be again 
      accessible, however DISKSECURE II will have been removed and must
      be re-installed to restore protection.



		   IV - How DISKSECURE II is Removed

	In the event that it is necessary to remove DISKSECURE II from a PC,
the best way is to utilize the DiskSec.EXE program either from the
MAINTENANCE floppy, or from the c:\ds2 directory. When DS is resident, the
program will detect this and modify the menu to include a REMOVE option. 
If a password is in use, it will be necessary to provide this also.

	Secondly, the machine can be booted from a regular floppy disk
and the DiskSec2.exe program executed. If a password is in effect this
must be entered for activity.

	If the disk should become corrupt, often booting from floppy and
running the DiskSecure2 program will enable recovery. Should this fail,
the DSPART.COM program on the RECOVERY disk may be used for an emergency 
recovery of the low levels after which the machine may be rebooted and 
conventional recovery tools used.


		  V - Malicious Software and DISKSECURE II

	DISKSECURE II is a software program.  Consequently, even though it 
is the first software loaded from a fixed disk it CAN be infected or 
damaged , should an indadvertant boot from an infected floppy disk take 
place, even though DOS will not recognize the fixed disk .  Only hardware 
in the form of a ROM extension or custom BIOS can prevent this.  

	One effective means with newer BIOSes is to set the CMOS so that
the PC will always boot from the C: drive first. Since DISKSECURE II
allows transfer of a boot to floppy by holding the Ctrl key down during boot,
selection of the A: drive need never be automatic. This combined with
DiskSecure II is effective against every known virus or viral technique
(and a few that haven't been seen yet - don't ask 8*).

	What DISKSECURE II can and does do is to recognize immediately 
when it is loaded that an infection has occurred, display an error
message as listed below, and refuse to proceed with the boot process until
corrected (in most case this will be automatic and wait only permission from 
the user. In rare cases, booting from a floppy will be necessary for 
correction however the machine will not boot unless DISKSECURE II's
multiple redundant criteria are met.

	Additionally, certain destructive viruses (such as AZUSA) can 
destroy DISKSECURE II. In this event, the disk will be unable to boot and
the drive will be unrecognizable from a floppy. The use of DSPART.DAT,
stored on a bootable floppy, renamed DSPART.COM, and executed will
restore the partition table to a usable condition. In any event, the 
attack will be immediately noticeable and containable.

DISKSECURE II boot error messages: see ERROR.MSG file.

	Additionally, some malicious software (as well as some low-level
programs) may try to write to DISKSECURE II protected areas on the disk.  In
this case a message may appear on the screen "DISKSECURE II TRAP: x" where x 
indicates the trapped function.  If this should happen during a legitimate 
program, use of DS2BYP will be necessary. This should be done only under
known safe conditions.

	A DISKSECURE II trap will occur on an attempt to write to any of the 
"hidden" sectors as well as the first partition's boot sector, or an 
attempt to format any sector on the protected disk(s) (note: many OS format
programs do not actually "format" the disk, only the low-level formatting
such as done by programs that set the interleave of a disk may do this.  (A
MS-DOS 3.3 "FORMAT" will not trigger a DISKSECURE II trap until it is nearly
complete and information may be lost).

	Generally, this will only occur if a program attempts to change disk 
interleave, boot record/partitioning, or on complete replacement of the 
operating system (Central Point Software's COMPRESS and Peter Norton's 
SpeedDisk are not affected, Peter Norton's CONFIGUR, MS-DOS FDISK, and
Steve Gibson's SPINRITE are).  


	Further, DISKSECURE II has proven safe with all major disk 
compression programs including Stacker, SuperStor Pro, and DblSpace as
well as nearly all other anti-virus programs though some may flag
its activity.

	DISKSECURE II cannot protect the FATs or Directory structure since 
the user must be able to modify these.  Other programs such as Enigma-
Logic's VIRUS-SAFE, Symantec's NAV, Fischer's PC-WATCHDOG, the McAfee 
Programs, the Dr.  Panda Utilities, Ross Greenberg's FLUSHOT, and Fridrik 
Skulasen's F-PROT exist for this function.  DISKSECURE II was created
to plug a hole that exists under the operating system so that a reasonable
expectation of a clean system can be had when the "C:\>" prompt appears.  



                      VI - Return Codes

On termination (if not a reboot) DISKSECURE II returns various error
codes to indicate the reason.  These may be used by a batch file 
for checking/corrective action, however DISKSECURE II is primarily
a manual, interactive program.

DISKSEC2.EXE

user terminated codes

code (hex)
 0   (0)	Program completed with no errors
 1   (1)	Following warning message
 2   (2)	Following TOM/COMPARE message - possible virus
 3   (3)	Following number of fixed disks message
 7   (7)        Following save to file request

program terminated codes

code (hex)
 8   (8)	No hard disk responding
 9   (9)	Disk access failure
10   (A)	No active partition table located
11   (B)	Error in sector one on disk - possible virus
12   (C)	Active partition table not in proper place - possible virus
14   (E)        No "Hidden Sectors" on disk (used early version of FDISK).
		or Changing MBR (see actual error message) See Appendix B

DS2CHK.EXE

0    (0)	DISKSECURE II not present in memory
1    (1)        DISKSECURE II present in memory but not in control
                (low interrupt vector seen only with QEMM 6.0+ "stealth")
2    (2)        DISKSECURE II present in memory and in control
4    (4)	DISKSECURE II has been disabled in some other manner
8    (8)        Disk did not respond (should not occur)

  		         VII - Licensing

	DISKSECURE II is copyrighted material distributed both as individual
copies and on site/entity licenses. 

	With version 2.4, DISKSECURE follows the trend I began with the
FixUtilities of being FreeWare to individuals, however retaining Copyright.
It is not public domain material. It may not be altered in any way or 
distributed except as a complete package (see the DSxx.VAL file for a list 
of contents). 

	Customized versions including special switches, logos, encryption,
full partition protection, enforced acceptance, and disclaimers such as:

  "Property of the XYZ Corporation & is for Authorized Users Only. 
The right is reserved to monitor any and all transmissions, keystrokes, 
                 and storage on this system." 

are available on a site licensing basis.

Donations cheerfully accepted 8*) Padgett Peterson
                                  POB 1203
                                  Windermere, Florida, 32819
                                  407.352.6027


                    VII - Weasel-Words

No guarentee for usefulness or fitness of any kind is made and the user
is responsible for whatever happens. While I have made every reasonable 
effort to make sure that this software will do what it is supposed to,
I cannot check every possible combination of equipment/software possible
(though heaven knows I've tried). I will try to fix any reported and 
verified bugs. 


                Appendix A - Hidden Sectors / Mutable MBR

	While all disk partitioning schemes since the release of PC-DOS
3.0 in early 1984 have aligned partitions on cylinder boundaries,  very
early disk partitioning programs (e.g.  FDISK 1.00) did not perform this 
alignment.  DISKSECURE II relies on this alignment for installation and 
protection, therefore the installation procedure verifies that no partition 
violates this requirement.

Should a disk be found on the system (DISKSECURE II checks all fixed disks),
the installation process will terminate with the warning "No Hidden 
Sectors...".  In this case, it will be necessary to repartition the disk 
using a later version of the partitioning software.

Note: It is possible to be running a later version of DOS or other OS
      with a disk partitioned using the early scheme so the DOS "VER"
      command cannot be used to reliably test for this condition.  Peter
      Norton's DI (DiskInfo) and other software will report the number 
      of "hidden sectors" on a disk.  This value should be equal to the
      number of sectors per track.
      
                        Changing MBR

	 Another condition that DISKSECURE II cannot cope with is that 
a very small number of disk controllers write directly to the MBR at 
intervals. This has only been observed on early XT hard disk units, 
however the integrity of a DISKSECURE IId disk's MBR must be maintained. 
If discovered at load time, the installation process will issue a warning
and the installation will abort. If this should occur during a boot,
the  MATCH ERROR termination will occur and the recovery disk should
be used to restore the disk. Re-installation should not occur until the
cause (viral or otherwise) has been determined.

			Changing DBR

	Even rarer are the operating systems which write often to the 
DBR but they do exist. Zenith ZDS 3.0, 3.1, and 3.2 plus a few early 
HP Vectras are known to exhibit this behavior. Should periodic "DS II
TRAP: 3" messages occur during the boot process, this may be the cause
since DS II will protect the DBR from writing by any software. Certain
later OS software may also exhibit this charactorisitic, for example MS
-DOS 5.0 & later will attempt to change the Disk serial number in the 
DBR if a LABEL command is issued & two or more TRAP errors will display. 
The label will however be properly changed.

        One virus has been seen which on boot from floppy will blindly
write to a common DBR location. If DS II is not running then there is
no means of protection from this. It will be detected on the next full
boot. (see section 2). It is unlikely that this virus will be very
successful.


		Appendix B - DS2BYP and DS2MOVE

	The two special adjunct files provided with DISKSECURE II have
unique properties that are only functional with versions of DOS of 3.2
or above.

DS2MOVE.SYS is the most important as it allows moving of DISKSECURE II
  from a 1k area at the Top of Memory (a 640k machine will report 639k)
  to a 304 byte area of low memory restoring the full 640k to DOS. This
  program is placed in CONFIG.SYS (best if first driver loaded except when
  QEMM DOSDATA driver is in use) and has no switches.

DS2BYP.EXE is for use *only* when a program proves completely incompatable
  with DISKSECURE II (such as WIndows 3.1 in 32BitDiskAccess mode). It
  is invoked as follows DS2BYP <drive>:<path><filename.ext>. DS2BYP
  only accepts programs with .COM and .EXE extensions and the drive, path
  and filemname must be fully expanded (no PATH searches or wildcards
  are permitted). Only one program will run on each invocation. This
  rigorous approach is to prevent as far as possible any possibility of a 
  spoof or companion attack. Use with caution.

		Appendix C - Other executable and batch files

DS2INST.BAT  - a batch file to be used when installing DISKSECURE II
               from a floppy disk. It will create a directory \DS
               on the C: drive, copy the files from the floppy
               into that directory, patch the AUTOEXEC.BAT file
               to include  verification of DISKSECURE II in memory on
               boot (recommended but may be omitted), and invoke
               the main program for installation.

DS.B         - Batch file commands to be added to AUTOEXEC.BAT for
               checking referred to in DSINSTAL.BAT

ASK.COM      - 10 byte file for making .BATch files interactive. ASK
               will wait for a keystroke and return an errorlevel
               that may be used by an "IF ERRORLEVEL" construct.

CHK512.COM   - Short .COM file to identify certain incompatable drives

CHKINT13.COM - Short .COM file to verify a "clean" path to the BIOS disk
               access.

DOS32.COM    - Short .COM file to verify use of DOS 3.2 or later.

QEMMST.COM   - Short .COM file to detect use of QEMM 6.0 & above "stealth"