i

                          CHAPTER 0.1 - NUMBERS AND ARITHMETIC


             You don't habitually use the base two system to balance your
             checkbook, so it would be counterproductive to teach you machine
             arithmetic on a base two system. What number systems have you had
             a lot of experience with? The base 10 system springs to mind. I'm
             going to show you what happens on a base 10 system so you will
             understand the structure of what happens with computer
             arithmetic.


             BASE 10 MACHINE

             Each place inside the microprocessor that can hold a number is
             called a REGISTER. Normally there are a dozen or so of these. Our
             base 10 machine has 4 digit registers.  They can represent any
             number from 0000 to 9999. They are exactly like an industrial
             counters or the counters on your tape machines.{1} If you add 27
             to a register, the microprocessor counts forward 27; if you
             subtract 153 from a register, the microprocessor counts backwards
             153.   Every time you add 1 to a register, it increments by 1 -
             that is 0245, 0246, 0247, 0248. Every time you subtract 1 from a
             register, it decrements by 1 - that is 3480, 3479, 3478, 3477.

             Let's do some more incrementing.  9997, 9998, 9999, 0000, 0001,
             0002. Whoops! That's a problem. When the register reaches 9999
             and we add 1, it changes to 0000, not 10,000. How can we tell the
             difference between 0000 and 10,000? We can't without a little
             help from the CPU.{2}  Immediately after an arithmetical
             operation, the CPU knows whether you have gone through 10,000
             (9999->0000). The CPU has something called a carry flag. It is
             internal to the CPU and can have the value 0 or 1. After each
             arithmetical operation, the CPU sets the CARRY FLAG to 1 if you
             went through the 9999/0000 boundary, and sets the carry flag to 0
             if you didn't.{3}

             Here are some examples, showing addition, the result, and the
             carry flag. The carry flag is normally abbreviated by CF.

                    number 1       number 2        result     CF

                      0289           4782           5071      0 
                      4398           2964           7382      0
                      8177           5826           4003      1
             ____________________

                1. Exactly like industrial counters that have several hundred
             thousand parts, that is.

                2. The CPU (central processing unit) is the chip(s) that does
             all the arithmetic. In the case of the PC, it is the 8086.

                3. When you set a flag to 0, it is called CLEARING the flag.

             ______________________

             The PC Assembler Tutor - Copyright (C) 1989 Chuck Nelson





             The PC Assembler Tutor                                         ii
             ______________________

                      6744           4208           0952      1

             Note that you must check the carry flag immediately after the
             arithmetical operation. If you wait, the CPU will reset it after
             the next arithmetical operation.

             Now let's do some decrementing. 0003, 0002, 0001, 0000, 9999,
             9998. Golly gosh! Another problem. When we got to 0000, rather
             than getting -1, -2, we got 9999, 9998. Apparently 9999 stands
             for -1, 9998 stands for -2. Yes, that's the system on this, on
             the 8086, and on all computers. (Back to that in a moment.) How
             do we tell that the number went through 0 ; i.e. 0000->9999? The
             carry flag comes to the rescue again. If the number goes through
             the 9999/0000 boundary in either direction, the CPU sets the CF
             to 1; if it doesn't, the CPU sets the CF to 0. Here's some
             subtraction, with the result and the carry flag.

                    number 1       number 2       result     CF

                      8473           2752           5721      0
                      2836           4583           1747      1
                      0654           9281           8627      1
                      9281           0654           8627      0

             Look at examples 3 and 4. The numbers are reversed. The results
             are the same but they have different signs. But that is as it
             should be. When you reverse the order in a subtraction, you get
             the same absolute value, only a different sign (15 - 7 = 8 but 
             7 - 15 = -8). Remember, the CF is reliable only immediately after
             the operation.


             NEGATIVE NUMBERS

             The negative numbers go 9999=-1, 9998=-2, 9997=-3, 9996=-4,
             9995=-5 etc. A more negative number is denoted by a smaller
             number in the register; -5 = 10,000 -5 = 9995; -498 = 10,000 -498
             = 9502, and in general, -x = 10,000 -x. Here are some negative
             numbers and their representations on our machine.

                     number     machine no              number     machine no

                        -27          9973                -4652          5348
                      -8916          1084                -6155          3845

             As you will notice, these numbers look exactly the same as the
             unsigned numbers. They ARE exactly the same as the unsigned
             numbers. The machine has no way of knowing whether a number in a
             register is signed or unsigned. Unlike BASIC or PASCAL which will
             complain whenever you try to use a number in an incorrect way,
             the machine will let you do it. This is the power and the curse
             of machine language. You are in complete control. It is your
             responsibility to keep track of whether a number is signed or
             unsigned. 

             Which signed numbers should be positive and which negative? This
             has already been decided for you by the computer, but let's think





             Chapter 0.1 - Numbers and Arithmetic                          iii
             ____________________________________

             out what a reasonable solution might be. We could have from 0000
             to 8000 positive and from 9999 to 8001 negative, but that would
             give us 8001 positive numbers and 1999 negative numbers. That
             seems unbalanced. More importantly, if we take -(3279) the
             machine will give us 6721, which is a POSITIVE number. We don't
             want that. For reasons of symmetry, the positive numbers are
             0000-4999 and the negative numbers are 9999-5000.{4} Our most
             negative number is -5000 = 10,000 -5000 = 5000.


             10'S COMPLEMENT

             It's time for a digression. If we are going to be using negative
             numbers like -(473), changing from an external number to an
             internal number is going to be a bother: i.e. -473 -> 9527. Going
             the other way is going to be a pain too: i.e. 9527 -> -473. Well,
             it would be a problem except that we have some help.

                 0000 =    10,000    =     9999     +1
                                          - 473
             result                        9526     +1   = 9527

             Let's work this through carefully. On our machine, 0000  and
             10000 (9999+1) are the same thing, so 0 - 473 is the same as
             9999+1-473 which is the same as 9999-473+1. But when we have all
             9s, this is a cinch. We never have to borrow - all we have to do
             is subtract each digit from 9 and then add 1 to the total. We may
             have to carry at the end, but that is a lot better than all those
             borrows. We'll do a few examples: 

             (-4276)
                 0000 =    10,000    =     9999     +1
                                          -4276
             result                        5723     +1   = 5724


             (-3982)
                 0000 =    10,000    =     9999     +1
                                          -3982
             result                        6017     +1   = 6018


             (-2400)
                 0000 =    10,000    =     9999     +1
                                          -2400
             result                        7599     +1   = 7600


             (-1989)
                 0000 =    10,000    =     9999     +1
             ____________________

                4. That way, if we tell the machine that we are working with
             signed numbers, all it has to do is look at the left digit. If
             the digit is 5-9, we have a negative number, if it is 0-4, we
             have a positive number. Note that 0000 is considered to be
             positive. This is true on all computers.





             The PC Assembler Tutor                                         iv
             ______________________

                                          -1989
             result                        8010     +1   = 8011

             This is called 10s complement. Subtract each digit from 9, then
             add 1 to the total. One thing we should check is whether we get
             the same number back if we negate the negative result; i.e. does
             -(-1989)) = 1989?  From the last example, we see that -1989 =
             8011, so:

             (-8011)
                 0000 =    10,000    =     9999     +1
                                          -8011
             result                        1988     +1   = 1989

             It seems to work. In fact, it always works. See the footnote for
             the proof.{5} You are going to use this from time to time, so you
             might as well practice some. Here are 10 numbers to put into 10s
             complement form. The answers are in the footnote. (1) -628, (2)
             -4194, (3) -9983, (4) -1288, (5) -4058, (6) -6952, (7) -162, (8)
             -9, (9) -2744, (10) -5000.{6}


             The computer keeps track of whether a number is positive or
             negative. After an arithmetical operation, it sets a flag to tell
             whether the result is positive or negative. This flag has no
             meaning if you are using unsigned numbers. The computer is
             saying, "If the last arithmetical operation was with signed
             numbers, then this is the sign of the result." The flag is called
             the sign flag (SF). It is 0 if the number is positive and 1 if
             the number is negative. Let's decrement again and look at both
             the sign flag and carry flag.

                        NUMBER    SIGN     CARRY

                           3         0         0
                           2         0         0
                           1         0         0
                           0         0         0
                        9999         1         1
             ____________________

                5. Let x be any number. Then:
             -x     = ( 10,000 - x)     = ( 9999 + 1 - x ) ;

             -(-x)  = ( 10,000 - (-x) ) = ( 9999 + 1 - (-x) )
                                       = ( 9999 + 1 - ( 9999 + 1 - x ) )
                                       = ( 9999 + 1 - 9999 - 1 + x )
                                       = x

                6.   (1) -628 = 9372 , (2) -4194 = 5806 , (3) -9983 = 0017,
                     (4) -1288 = 8712 , (5) -4058 = 5942 , (6) -6952 = 3048
                     (7) -162 = 9838 , (8) -9 = 9991 , (9) -2744 = 7256,
                     (10) -5000 = 5000. This last one is a little strange. It
             changes 5000 into itself. In our system, 5000 is a negative
             number and it winds up as a negative number. This happens on all
             computers. If you take the maximum negative number and take its
             negative, you get the same number back.





             Chapter 0.1 - Numbers and Arithmetic                            v
             ____________________________________

                        9998         1         0
                        9997         1         0
                        9996         1         0

             That worked pretty well. The sign flag changed from 0 to 1 when
             we went from 0 to 9999 and the carry flag was set to 1 for that
             one operation so we could see that we had gone through the
             9999/0000 boundary. 

             Let's do some more decrementing.

                        NUMBER    SIGN     CARRY

                        5003         1         0
                        5002         1         0
                        5001         1         0
                        5000         1         0
                        4999         0         0
                        4998         0         0
                        4997         0         0
                        4996         0         0

             This one didn't work too well. 5000 is our most negative number
             (-5000) and 4999 is our most positive number; when we crossed the
             4999/5000 boundary, the sign changed but there was nothing to
             tell us that the sign had changed. We need to make another flag.
             This one is called the overflow flag. We check the carry flag
             (CF) for the 0000/9999 boundary and we check the overflow flag
             for the 5000/4999 boundary. The last decrementing example with
             the overflow flag:

                        NUMBER    SIGN     CARRY     OVERFLOW

                        5003         1         0         0
                        5002         1         0         0
                        5001         1         0         0
                        5000         1         0         0
                        4999         0         0         1
                        4998         0         0         0
                        4997         0         0         0
                        4996         0         0         0

             This time we can find out that we have gone through the boundary.
             We'll come back to how the computer sets the overflow flag later,
             but let's do some addition and subtraction now.


             UNSIGNED ADDITION AND SUBTRACTION

             Unsigned addition is done the same way as normally. The computer
             adds the two numbers. If the result is over 9999, it sets the
             carry flag and drops the left digit (i.e. 14625 -> 4625, CF = 1,
             19137 -> 9137 CF = 1, 10000 -> 0000 CF = 1). The largest possible
             addition is 9999 + 9999 = 19998. This still has a 1 in the left
             digit. If the carry flag is set after an addition, the result
             must be between 10000 and 19998.






             The PC Assembler Tutor                                         vi
             ______________________

             Since this is unsigned addition, we won't worry about the sign
             flag or the overflow flag for the moment. Here are some examples
             of unsigned addition.

                      NUMBER 1       NUMBER 2       RESULT         CF

                        5147           2834          7981           0
                        6421           8888          5309           1
                        2910           6544          9454           0
                        6200           6321          2521           1

             Directly after the addition, the computer has complete
             information about the number. If the carry flag is set, that
             means that there is an extra 10,000, so the result of the second
             example is 15309 and the result of the fourth example is 12521. 
             There is no way to store all that information in 4 digits in
             memory so that extra information will be lost if it is not used
             immediately. 

             Subtraction is similar. The machine subtracts, and if the answer
             is below 0000, it sets the carry flag, borrows 10000 and adds it
             to the result. -3158 -> -3135 + 10000 -> 6842 CF = 1 ; -8197 ->
             -8197 + 10000 -> 1803  CF = 1. After a subtraction, if the carry
             flag is set, you know the number is 10000 too big. Once again,
             the carry flag information must be used immediately or it will be
             lost. Here are some examples:

                      NUMBER 1       NUMBER 2       RESULT         CF

                        3872           2655          1217           0
                        9826           5967          3859           0
                        4561           7143          7418           1
                        2341           4907          7434           1

             If the carry flag is set, the computer borrowed 10000, so example
             3 is 7418 - 10000 = -2582 and example 4 is 7434 - 10000 = -2566.


             MODULAR ARITHMETIC

             What the computer is doing is modular arithmetic. Modular
             arithmetic is like a clock. If it is 11 o'clock and you go
             forward 1 hour it's now 12 o'clock; if it's 11 and you go
             backwards 1 hour it's now 10. If it's 11 and you go forward 4
             hours it's not 15, it's 3. If it's 11 and you go backward 15
             hours it's not -4, it's 8. 

             The clock is doing  mod 12  arithmetic.{7} 

                 (A+B) mod 12
                 (A-B) mod 12

             From the clock's viewpoint, 11 o'clock today, 11 o'clock
             yesterday and 11 o'clock, June 8, 1754 are all the same thing. If
             ____________________

                7. To be a perfect analogy 12 o'clock should be 0 o'clock.





             Chapter 0.1 - Numbers and Arithmetic                          vii
             ____________________________________

             you go forward 200 hours (that's 12X16 + 8) you will have the
             same result as going forward 8 hours. If you go backwards 200
             hours (that's -(12X16 + 8) = -(12X16) -8) you get the same result
             as going backwards 8 hours. If you go forward 4 hours from 11
             (11+4) mod 12 = 3 you get the same result as going backwards 8
             hours (11-8) mod 12 = 3. In fact, these come in pairs. If A + B =
             12, then going forward A hours gives the same result as going
             backwards B hours. Forwards 9 = backwards 3; forwards 7 =
             backwards 5; forwards 11 = backwards 1.

             In the mod 12 system, the following things are equivalent:

                 (+72 + 4)      (+72 - 8)
                 (+60 + 4)      (+60 - 8)
                 (+48 + 4)      (+48 - 8)
                 (+36 + 4)      (+36 - 8)
                 (+24 + 4)      (+24 - 8)
                 (+12 + 4)      (+12 - 8)
                 (  0 + 4)      (  0 - 8)
                 (-12 + 4)      (-12 - 8)
                 (-24 + 4)      (-24 - 8)
                 (-36 + 4)      (-36 - 8)
                 (-48 + 4)      (-48 - 8)
                 (-60 + 4)      (-60 - 8)

             They form what is known as an equivalence class mod 12. If you
             use any one of them for addition or subtraction, you will get the
             same result (mod 12) as with any other one. Here's some
             addition:{8}

                 (+48 + 4) + 7 = (48 + 11) mod 12 = 11
                 (-48 - 8) + 7 = (48 - 1 ) mod 12 = 11
                 (  0 - 8) + 7 = ( 0 - 1 ) mod 12 = 11
                 (-60 + 4) + 7 = (-60 +11) mod 12 = 11

             And some subtraction:

                 (+48 + 4) - 2 = (48 + 2 ) mod 12 = 2
                 (-48 - 8) - 2 = (48 - 10) mod 12 = 2
                 (  0 - 8) - 2 = ( 0 - 10) mod 12 = 2
                 (-60 + 4) - 2 = (-60 + 2) mod 12 = 2


             Our pretend computer doesn't cycle every 12 numbers, it cycles
             every 10,000 numbers - it is a mod 10,000 machine. On our
             machine, the number 6453 has the following equivalence class:

                 (+30000 + 6453)               (+30000 - 3547)
                 (+20000 + 6453)               (+20000 - 3547)
                 (+10000 + 6453)               (+10000 - 3547)
                 (     0 + 6453)               (     0 - 3547)
                 (-10000 + 6453)               (-10000 - 3547)
                 (-20000 + 6453)               (-20000 - 3547)
                 (-30000 + 6453)               (-30000 - 3547)
             ____________________

                8. (-10) mod 12 = 2 ;   (-11) mod 12 = 1





             The PC Assembler Tutor                                       viii
             ______________________


             Any one of these will act the same as any other one. Notice that
             10000 - 3547 is the subtraction that we did to get the
             representation of -3547 on the machine. 

             -3547    = 9999 + 1
                        3547
                        6452 + 1 = 6453

             6453 and -3547 act EXACTLY the same on this machine. What this
             means is that there is no difference in adding signed or unsigned
             numbers on the machine. The result will be correct if interpreted
             as an unsigned number; it will also be correct if interpreted as
             a signed number.

                 6821 + 3179 = 10000  so  -3179 = 6821   and  3179 = -6821
                 5429 + 4571 = 10000  so  -4571 = 5429   and  4571 = -5429

             Since -3179 and 6821 act the same on our machine and since -4571
             and 5429 act the same, let's do some addition. Take your time so
             you understand why the signed and unsigned numbers are giving the
             same results mod 10000:

                  ---------------------------------------------------------
                  6821 + 497 = 7318
                 -3179 + 497 = (10000 - 3179) + 497 = 10000 -2682  = -2682

                  7318 + 2682 = 10000      so    -2682 = 7318

                  ----------------------------------------------------------

                  5429 + 876 = 6305
                 -4571 + 876 = (10000 - 4571) + 876 = 10000 - 3695 = -3695

                  6305 + 3695 = 10000      so    -3695 = 6305

                  ----------------------------------------------------------

             Here's some subtraction:

                  -----------------------------------------------------------

                  6821 - 507 = 6314
                 -3179 - 507 = (10000 - 3179) - 507 = 10000 - 3686 = -3686

                  6314 + 3686 = 10000     so     -3686 = 6314

                  ----------------------------------------------------------

                  5429 - 178 = 5251
                 -4571 - 178 = (10000 - 4571) - 178 = 10000 - 4749 = -4749

                  5251 + 4749 = 10000    so      -4749 = 5251

                  -----------------------------------------------------------

             It is the same addition or subtraction. Interpreted one way it is





             Chapter 0.1 - Numbers and Arithmetic                           ix
             ____________________________________

             signed addition or subtraction; interpreted another way it is
             unsigned addition or subtraction.

             The machine could have one operation for signed addition and
             another operation for unsigned addition, but this would be a
             waste of computer resources. These operations are exactly the
             same. This machine, like all computers, has only one integer
             addition operation and one integer subtraction operation. For
             each operation, it sets the flags of importance for both signed
             and unsigned arithmetic.

             For unsigned addition and subtraction, CF, the carry flag tells
             whether the 0000/9999 boundary has been crossed.

             For signed addition and subtraction, SF, the sign flag tells the
             sign of the result and OF, the overflow flag tells whether the
             result was too negative or too positive.


             SIGN EXTENSION

             Although our base 10 machine is set up for 4 digit numbers, it is
             possible to use it for numbers of any size by writing the
             appropriate software. We'll use 12 digit numbers as an example,
             though they could be of any length. The first problem is
             converting 4 digit numbers into 12 digit numbers. If the number
             is an unsigned number, this is no problem (we'll write the number
             in groups of 4 digits to keep it readable):

                 4816      ->   0000 0000 4816
                 9842      ->   0000 0000 9842
                  127      ->   0000 0000 0127

             what if it is a signed number? The first thing we need to know
             about signed numbers is, what is positive and what is negative?
             Once again, for reasons of symmetry, we choose positive to be 
             0000 0000 0000  to  4999 9999 9999 and negative to be 5000 0000
             0000 to 9999 9999 9999.{9}  This longer number system cycles from

             9999 9999 9999 to 0000 0000 0000. Therefore, for longer numbers,
             0000 0000 0000 = 1 0000 0000 0000. They are equivalent. 
             0000 0000 0000 = 9999 9999 9999 + 1.

             If it is a positive signed number, it is still no problem (recall
             that in our 4 digit system, a positive number is between 0000 and
             4999, a negative signed number is between 5000 and 9999). Here
             are some positive signed numbers and their conversions:

                 1974      ->   0000 0000 1974
                    1      ->   0000 0000 0001
                 3909      ->   0000 0000 3909

             ____________________

                9. Once again, the sign will be decided by the left hand
             digit. If it is 0-4 it is a positive number; if it is 5-9 it is a
             negative number.





             The PC Assembler Tutor                                          x
             ______________________

             If it is a negative number, where did its representation come
             from in our 4 digit system? -x -> 9999 + 1 -x = 9999 - x + 1.
             This time it won't be 9999 + 1 but 9999 9999 9999 + 1. Let's have
             some examples.

                 4 DIGIT SYSTEM       12 DIGIT SYSTEM

             -1964
                  9999     + 1        9999 9999 9999 + 1
                 -1964                         -1964
                  8035   -> 8036      9999 9999 8035 + 1 -> 9999 9999 8036

             -2867
                  9999     + 1        9999 9999 9999 + 1
                 -2867                         -2867
                  7132   -> 7133      9999 9999 7132 + 1 -> 9999 9999 7133

             -182
                  9999     + 1        9999 9999 9999 + 1
                  -182                          -182
                  9817   -> 9818      9999 9999 9817 + 1 -> 9999 9999 9818

             As you can see, all you need to do to sign extend a negative
             number is to put 9s to the left. 

             Can't those 9s on the left become 0s when we add that 1 at the
             end?  No. In order for that to happen, the right four digits must
             be 9999. But that can only happen if the number to be negated is
             0000:

                  9999 9999 9999 + 1
                           -0000
                  9999 9999 9999 + 1 -> 0000 0000 0000

             In all other cases, adding 1 does not carry anything out of the
             right four digits.


             It is impossible to truncate one of these 12 digit numbers to a 4
             digit number without making the results unreliable. Here are two
             examples:

             (number)      0000 0168 7451 ->   7451  (now a negative number)
             (actual value)     +168 7451     -2549 

             (number)      9999 9643 2170 ->   2170  (now a positive number)
             (actual value)     -356 7830     +2170


             We now have 12 digit numbers. Is it possible to add them and
             subtract them? Yes but only 4 digits at a time. When you add with
             pencil and paper you carry left from each digit. The computer can
             carry left from each group of 4 digits. We'll do the following
             addition:

                           0138 6715 6037
                         + 2514 2759 7784





             Chapter 0.1 - Numbers and Arithmetic                           xi
             ____________________________________


             Do this with pencil and paper and write down all the carries. The
             computer is going to do this in 3 parts:

                 1) 6037 + 7784
                 2) 6715 + 2759 + carry (if any)
                 3) 0138 + 2514 + carry (if any)

             The first addition is our regular addition. It will set the carry
             flag if the 0000/9999 boundary was crossed (i.e. the result was
             larger than 9999). In our case CF = 1 since the result is 13821.
             The register holds 3821. We store 3821. Next, we need to add
             three things: 6715 + 2759 + CF (=1). There is an instruction like
             this on all computers. It adds two numbers plus the value of the
             carry flag. Our first addition was ADD (add two numbers). This
             time the machine instruction is ADC (add two numbers and the
             carry). The result of our second addition is 9475. The register
             holds 9475 and CF = 0. We store 9475. Finally, we need to add
             three more things: 0138 + 2514 + CF (=0). Once again we use ADC.
             The result is 2652, CF = 0. We store the 2652. That is the whole
             result:

                 2652 9475 3821

             If CF = 1 at this point, the number has crossed the
             9999,9999,9999/0000,0000,0000 boundary. This will work for signed
             numbers also. The only difference is that at the very end we
             don't check CF, we check OF to see if the
             4999,9999,9999/5000,0000,0000 boundary has been crossed. 


             Just to give you one more example we'll do a subtraction using
             the same numbers:

                           0138 6715 6037
                           2514 2759 7784

             Notice that in order for you to do this with pencil and paper
             you'll have to put the larger number on top before you subtract.
             With the machine this is unnecessary. Go ahead and do the
             subtraction with pencil and paper.

             The machine can do this 4 digits at a time, so this is a three
             step process:

                 1) 6037 - 7784 
                 2) 6715 - 2759 - borrow (if any)
                 3) 0138 - 2514 - borrow (if any)

             The first one is a regular subtraction and since the bottom
             number is larger, the result is 8253, CF = 1. (Perhaps you are
             puzzled because that's not the result that you got. Don't worry,
             it all comes out in the wash). Step two subtracts but also
             subtracts any borrow (We had a borrow because CF = 1). There is a
             special instruction called SBB (subtract with borrow) that does
             just that. 6715 - 2759 - 1 = 3955, CF = 0. We store the 3955 and
             go on to the third part. This also is SBB, but since we had no





             The PC Assembler Tutor                                        xii
             ______________________

             borrow, we have 0138 - 2514 - 0 = 7624, CF = 1. We store 7624.
             This is the end result, and since CF = 1, we have crossed the
             9999,9999,9999/0000,0000,0000 boundary. This is going to be the
             representation of a negative number mod 1,0000,0000,0000. With
             pencil and paper, your result was:

                 -2375 6044 1747

             The machine result was:

                  7624 3955 8253

             But CF was 1 at the end, so this represents a negative number.
             What number does it represent? Let's take its negative to get a
             positive number with the same absolute value:

                 9999 9999 9999  + 1
                 7624 3955 8253
                 2375 6044 1746  + 1  = 2375 6044 1747

             This is the same thing you got with pencil and paper. The reason
             it looked wierd is that a negative number is always stored as its
             modular equivalent. If you want to read a negative number, you
             need to take its negative to get a positive number with the same
             absolute value.

             If we had been working with signed numbers, we wouldn't have
             checked CF at the very end, we would have checked OF to see if
             the 4999,9999,9999/5000,0000,0000 boundary had been crossed. If
             OF = 1 at the end, then the result was either too negative or too
             positive.



             OVERFLOW

             How does the machine decide that overflow has occured? First,
             what exactly is overflow and when is it possible for overflow to
             occur?

             Overflow is when the result of a signed addition or subtraction
             is either larger than the largest positive number or more
             negative than the most negative number. In the case of the 4
             digit machine, larger than +4999 or more negative than -5000.

             If one number is negative and the other is positive, it is not
             possible for overflow to occur. Take +32 and -4791 as examples.
             If we start with the positive number (+32) and add the negative
             number (-4791), the result can't possibly be too positive.
             Similarly, if we start with the negative number (-4791) and add
             the positive number (+32), the result can't be too negative.
             Therefore, the result can be neither too positive nor too
             negative. Make sure you understand this before going on. 

             What if both are positive? Then overflow is possible. Here are
             some examples:






             Chapter 0.1 - Numbers and Arithmetic                         xiii
             ____________________________________

                 (+3500) + (+4500) = 8000 = -2000
                 (+2872) + (+2872) = 5744 = -4256
                 (+1799) + (+4157) = 5956 = -4044

             In each case, two positive numbers give a negative result. How
             about two negative numbers?

                                (7154) + (6000) = 3154 = +3154
             (actual value)     -2946    -4000

                                (5387) + (5826) = 1213 = +1213
             (actual value)     -4613    -4174

                                (8053) + (6191) = 4244 = +4244
             (actual value)     -1947    -3809

             The numbers underneath are the negative numbers that the numbers
             above them represent. In these cases, adding two negative numbers
             gives a positive result.

             This is what the machine checks for. Before the addition, it
             checks the signs of the numbers. If the signs are the same, then
             the result must also be the same sign or overflow has
             occurred.{10}  Thus + and + must have a + result; - and - must
             have a - result. If not, OF (the overflow flag) is set (OF = 1).
             Otherwise OF is cleared (OF = 0).

              
             MULTIPLICATION

             Unsigned multiplication is easy. The machine simply multiplies
             the two numbers. Since the result can be up to 8 digits (the
             maximum result is 9999 X 9999 = 9998 0001) the machine uses two
             registers to hold the result. We'll call them R1 and R2.

                 5436 X 174     R1   0094
                                R2   5864

                 2641 X 2003    R1   0528
                                R2   9923

             You need to know which register holds which half of the result,
             but besides that, everything is straightforward. On this machine
             R1 holds the left four digits and R2 holds the right four digits.

             Notice that our machine has changed the modular base from N to
             N*N (from 1 0000 to 1 0000 0000). What this means is that two
             things which are modularly equivalent under addition and
             subtraction are not necessarily equivalent under multiplication
             and division.  6281 and -3719 will not work the same.
             ____________________

                10. The machine checks something considerably more obscure
             because it is easier to implement in semiconductor logic, but
             what it is actually doing is checking to see if the two numbers
             being added have the same sign. If they do, the result must be
             the same sign or overflow has occurred.





             The PC Assembler Tutor                                        xiv
             ______________________


             The machine can't do signed multiplication. What it actually does
             is convert the numbers to positive numbers (if necessary),
             perform unsigned multiplication, and then do sign adjustment of
             the results (if necessary). It uses 2 registers for the result.

                           SIGNED MULTIPLICATION      REGS         RESULT

             (number)           (5372) X (3195)     R1   8521  =  -1478 6460
             (actual value)     -4628  X +3195      R2   3540

             (number)           (9164) X (8746)     R1   0104  =   +104 8344
             (actual value)      -836  X -1254      R2   8344

             (number)           (9927) X (0013)     R1   9999  =        -949
             (actual value)      -73  X   +13       R2   9051

             Looking at the last example, if we performed unsigned
             multiplication on those two numbers, we would have
             9927 X 0013 = 0012 9051, a completely different answer from the
             one we got. Therefore, whenever you do multiplication, you have
             to tell the machine whether you want unsigned or signed
             multiplication.


             DIVISION

             Unsigned division is easy too. The machine divides one number by
             the other, puts the quotient in one register and the remainder in
             another. Once again, the only problem is remembering which
             register has the quotient and which register has the remainder.
             For us, the quotient is R1 and the remainder is R2.

                 6190 / 372          R1   0016           16  remainder 238
                                     R2   0238

                 9845 / 11           R1   0895           895 remainder 0
                                     R2   0000

             As with multiplication, signed division is handled by the machine
             changing all numbers to positive numbers, performing unsigned
             division, then putting back the appropriate signs.


                         SIGNED DIVISION         REGS            RESULT

             (number)      (7192) / (9164)     R1   0003      +3  rem. -300
             (actual value)-2808  /  -836      R2   9700

             (number)      (3753) / (9115)     R1   9996      -4  rem. +213
             (actual value)+3753  /  -885      R2   0213

             Looking at the last example, 3753 / 9115, if that were unsigned
             multiplication the answer would be 0 remainder 3753, a completely
             different answer from the signed division. Every time you do a
             division, you have to state whether you want unsigned or signed
             division.