*****************************************************************
                                 REGISTRATION

          Hey, Chuck, I'm no chump!

          I'm using your programs/manual, and I  want to pay my fair share.
          Please make me a registered user of "The  PC Assembler Tutor" and
          "The PC Assembler  Helper". Enclosed is  a check for $9.95  (plus
          6.5% tax or $10.60 for California residents). Say, that's cheaper
          than a large pizza!


          Name_________________________________________________________
                    Last                First               Initial

          Address______________________________________________________
                    Street Address

                 _______________________________________________________
                    City, State, and Zip Code

          I got my copy from ___________________________________________

          Make checks payable to NELSOFT and send your registration to:

               NELSOFT
               P.O. Box 21389
               Oakland, CA  94620

          +++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++
                             REGISTRATION BENEFITS
           
          As a  registered user of  "The PC  Assembler Helper" and  "The PC
          Assembler Tutor" you are entitled to:

          1) Use asmhelp.obj and helpmem.com for personal use.
          2) Make 1 (one) printer copy of "The PC Assembler Tutor".
          3) Use all programs in "The PC Assembler Tutor" for personal use.
          4) Make an archival copy of the disks.
          5) Distribute UNALTERED disks to friends for their perusal.
          6) Use any updates to either "The PC Assembler Helper" or "The PC
             Assembler Tutor" under the same registration conditions.

          Though copies  of  the disk  may be  given away  if  there is  no
          charge, it is illegal to charge for redistribution of the disk or
          its  contents  without   permission  of  the  author.   Under  no
          circumstances  may  you  distribute  printed  copies of  "The  PC
          Assembler  Tutor". If you  intend to charge  for distributing the
          disk or its  information, please read  and sign the  distribution
          agreement which is in INTRO1.DOC.

          *****************************************************************




                                                                            31

                            CHAPTER 5 - ADDITION AND SUBTRACTION


             The first arithmetic operations we will look at are addition and
             subtraction, but before we do that, we need to look at one
             instruction that controls program flow.

             LOOP

             We already have JMP which sends you to a label:

                 jmp  label3

             sends the program to label3, wherever that is in the code.
             Sometimes we want to repeat a section of code a specific number
             of times and then go on. For this, we have LOOP. LOOP decrements
             the CX register by 1. If CX is not zero after being decremented,
             LOOP jumps to the label indicated. If CX is zero after being
             decremented, LOOP falls through. 

             The 8086 does not have general purpose registers. A general
             purpose register is a register that can be used for ALL
             instructions. There are a number of instructions on the 8086
             which must be done with specific registers, and LOOP is the first
             one we meet. LOOP always looks at the CX register.


             This first program lets you enter a number and then loops that
             many times so you can watch the CX register. As usual, you exit
             the program by hitting Control-C. We use temp2.asm.

             temp2.asm
             ; - - - - START CODE BELOW THIS LINE
                 call show_regs      ; initialize

             outer_loop:
                 call get_unsigned
                 mov  cx, ax         ; number to cx

             inner_loop:
                 call show_regs_and_wait
                 loop inner_loop

                 jmp  outer_loop

             ; - - - - END CODE ABOVE THIS LINE

             A very simple program. As always, link it with asmhelp.obj.
             Get_unsigned gets a two byte number (less than 65536) and puts it
             in AX. We put that number in CX, and then watch the program loop.
             Make sure you use show_regs_and_wait, or everything will happen
             too fast for you to see. Try entering 0. On the first pass, loop
             will decrement CX from 0 to 65535. If CX is 0 when you enter, you

             ______________________

             The PC Assembler Tutor - Copyright (C) 1989 Chuck Nelson





             The PC Assembler Tutor                                         32
             ______________________

             have to repeat the loop 65536 times before you exit the loop. Hit
             Control-C now to exit. 

             Throughout the book, I will use label names that end in '_loop'
             to indicate that they are the destination of a jump or loop
             instruction. The single word "loop" is a reserved word and may
             not be used as a label - it can only be used as an instruction.

             The addition program will have 4 sections and LOOP will give us
             the ability to do each section a limited number of times before
             going on to the next section.


             ADDITION

             If you read the introductory section on numbers carefully, you
             know that it is the same instruction for both signed and unsigned
             addition. The 8086 sets the flags correctly for both signed and
             unsigned addition. For signed addition, the following flags are
             set:

                 OF   the overflow flag is set (1) if the result is too
                 negative or too positive, that is, if the result in the
                 register does not show the correct result of the addition.
                 It is cleared (0) otherwise.

                 ZF   the zero flag is 1 if the result is zero, and is
                 cleared (0) if the result is non-zero.

                 SF   the sign flag is set (1) if the result is NEGATIVE and
                 is cleared (0) if the result is POSITIVE. Zero is considered
                 a positive number.

             For unsigned addition, the following flags are set:

                 CF   the carry flag is set (1) if the result is too large
                 (over 255 for byte and over 65535 for word operations). It
                 is cleared (0) otherwise.

                 ZF   the zero flag is the same as above.

             In addition, there are two more flags (PF the parity flag and AF
             the auxillary flag) which will be set or cleared; we will learn
             about them later. 

             Show_regs shows all the flags. The setting for each flag is
             underneath its name. For the flags OF, ZF and CF, there is an 'X'
             if the flag is set and a blank if the flag is cleared. SF, the
             sign flag, is '-' if the flag is set and '+' if the flag is
             cleared. 

             The addition program is fairly long because there are four things
             to look at - unsigned word addition, unsigned byte addition,
             signed word addition and signed byte addition. For that reason,
             it has already been typed in for you. It is called ADD1.ASM and
             its pathname is \XTRAFILE\ADD1.ASM. Print out a copy of it.






             Chapter 5 - Addition and Subtraction                           33
             ____________________________________

             There are four blocks of code which are almost identical except
             the calls are a little different and two blocks refer to whole
             registers while the other two refer to half registers. At the
             head of each block is code to set the appropriate register styles
             for show_regs. SI, DI, and BP are not used and are set to 0 to
             make the screen easier to read. Here is the first block of code,
             which is typical.

             ; - - - CODE
                    ; UNSIGNED WORD ADDITION 
                    mov   ax_byte, 2          ; ax, bx, dx unsigned 
                    mov   bx_byte, 2 
                    mov   dx_byte, 2 
                    lea   ax, ax_byte         ; call set_reg_style 
                    call  set_reg_style 
              
                    mov   cx, 3               ; 3 iterations 
             unsigned_loop: 
                    mov   ax, 0      ; clear the registers for visibility
                    mov   bx, 0 
                    mov   dx, 0 
                    call  show_regs 
                    call  get_unsigned        ; first number to  ax 
                    call  show_regs 
                    push  ax                  ; temporarily save ax 
                    call  get_unsigned        ; second number to bx 
                    mov   bx, ax 
                    pop   ax                  ; get ax back 
                    mov   dx, ax              ; copy of ax to dx 
                    add   dx, bx              ; dx (=ax) + bx 
                    call  show_regs_and_wait 
                    loop  unsigned_loop 

             ; - - - CODE

             First, we set AX, BX, and DX for the appropriate register style.
             Here it is unsigned full register. We then put 3 in CX so we can
             have 3 iterations with loop. Upon entering the loop, AX, BX, and
             DX are cleared for reasons of visibility. We don't want the
             screen cluttered up with numbers. Get_unsigned gets a two byte
             unsigned number and returns it in AX. We want the first number to
             be visually on the top (which is AX), but there is a problem
             here. In order to get the second number we need to call
             get_unsigned again, and it is going to put another number in AX.
             We need to temporarily store the first number while we bring in
             the second number and transfer it to bx. 

             There is a special 8086 instruction to do this, it is called
             PUSH. Push temporarily stores a word. The word can be either a
             full register or a word (two bytes) in memory. You can have
             either:

                 variable1 dw   10000

                      push ax
                      push variable1






             The PC Assembler Tutor                                         34
             ______________________

             These are stored in a special place called the stack which we
             will talk about much later. When you want it back, you use the
             instruction POP. POP gets back the LAST thing that you pushed
             onto the stack. Things come off the stack in REVERSE order of how
             they were put on.

                 push variable1
                 push variable2
                 push variable3
                 push variable4
                 pop  variable4
                 pop  variable3
                 pop  variable2
                 pop  variable1

             is the correct order. This is used for temporary storage only,
             and the only thing which is accessable is the last thing which
             you PUSHed on the stack.

             We push AX to store it temporarily, call get_unsigned again and
             transfer the number to BX. We then pop AX to get the number back.
             The situation now is: the first number is in AX, the second
             number is in BX. For the actual addition, we transfer AX to DX
             and then add DX and BX. AX and BX contain the two numbers, and DX
             contains the result. Then you must press ENTER to continue. LOOP
             will jump to 'unsigned_loop' two times. The third time it will
             fall through to the next section of code. 

             This program illustrates a hallmark of assembler code. It
             normally takes scads of code just to do something simple.

             Assemble add1.asm and link it with asmhelp.obj. Run it:

             ******************** SCREEN SHOT ******************************

                 AX  17428                             SI  00000
                 BX  19755                             DI  00000
                 CX  00003                             BP  00000
                 DX  37183                             SP  00508

                 CS  0AA5H   DS  0A55H   ES  0A25H   SS  0A35H   IP  004DH

                 OF   DF  IEF   TF   SF   ZF   AF   PF   CF
                  x    +    x         -              E           COUNT  00004
             ----------------------------------------------------------------

             The PC Assembler Helper   Version 1.0
             Copyright (C) 1989  Chuck Nelson   All rights reserved.
             Enter a number from 0 to 65535  17428
             Enter a number from 0 to 65535  19755
             Press ENTER to continue

             *****************************************************************

             This is the screen after the first addition. I have added 17428
             (AX) and 19755 (BX). The result 37183 is in DX. CX is still 3
             because it hasn't LOOPed yet.





             Chapter 5 - Addition and Subtraction                           35
             ____________________________________


             Notice that even though it is the same assembler instruction:

                 add

             in all four blocks of code, it is doing both signed and unsigned
             addition correctly. When you are doing signed addition, you want
             to look at OF, the overflow flag, SF, the sign flag, and ZF, the
             zero flag after each addition to see how they are set. When you
             do unsigned addition, you want to look at CF, the carry flag, and
             ZF, the zero flag to see how they are set. Play around with this
             for a while, and then it is time for the next program.

             As in all 8086 instructions, the order is:

                 add  destination, source

             We add both numbers, and put the result in the destination, the
             thing on the left.


             There are five different types of addition you can do, (just as
             there are five different types of moves). They are:

                 1. add two registers
                 2. add a register to a variable (memory)
                 3. add a variable (memory) to a register
                 4. add a constant to a variable (memory)
                 5. add a constant to a register

             Here's a program that does all 5 things. Use template.asm to make
             this program. template.asm is almost the same as the other ones
             we have used. It has a few changes. First, it now lists ALL the
             subroutines you can call in asmhelp.obj.{1} Appendix 1
             (\APPENDIX\APP1.DOC) contains a description of all the
             subroutines, what they do, and how they are called. Second, the
             size of STACKSEG is larger. We don't need this large of a stack
             now; it is for later. Finally, there is a section:

             ; + + + + + + + + + + PUT SUBROUTINES BELOW THIS LINE 

             ; + + + + + + + + + + PUT SUBROUTINES ABOVE THIS LINE 

             for subroutines. Ignore this. This is for later. 


             From now on, we will always use template.asm unless it is
             explicitly stated that something else is being used. Here's the
             program:

             template.asm
             ; + + + + + + + + + + + + + + + START DATA BELOW THIS LINE 
             ____________________

                1 This does not change the size of the .EXE file by even
             one byte, but it adds a lot of information to the .OBJ file, so
             they are much larger.





             The PC Assembler Tutor                                         36
             ______________________

             variable1    dw     ? 
             variable2    dw     ? 
             ; + + + + + + + + + + + + + + + END DATA ABOVE THIS LINE 
              
             ; + + + + + + + + + + + + + + + START CODE BELOW THIS LINE 
                    call  show_regs 
             outer_loop: 
                    call  get_unsigned        ; first number to ax 
                    push  ax                  ; store ax 
                    call  get_unsigned        ; second number to bx 
                    mov   bx, ax               
                    pop   ax                  ; restore ax 
                    mov   variable1, ax       ; first number to variable1 
                    mov   variable2, bx       ; second number to variable2 
                    ; add 2 registers 
                    mov   cx, ax              ; cx + bx 
                    add   cx, bx 
                    ; add register to memory 
                    add   variable1, bx 
                    mov   dx, variable1       ; put in dx for display 
                    ; add memory to register 
                    mov   si, ax 
                    add   si, variable2 
                    ; add a constant to memory 
                    add   variable2, 25 
                    mov   di, variable2       ; put in di for display 
                    ; add a constant to a register 
                    mov   bp, bx 
                    add   bp, 25 
                    call show_regs 
                    jmp   outer_loop 
              
             ; + + + + + + + + + + + + + + + END CODE ABOVE THIS LINE 


             The program puts the first number in AX and the second number in
             BX. It then proceeds to do the same addition (first number plus
             second number) three times. These are:

                 1. CX = add two registers (CX + BX)
                 2. DX = add a register to memory (variable1 + BX)
                 3. SI = add memory to a register (SI + variable2)

             Finally it adds a constant (second number + 25). These are:

                 4. DI = add a constant to memory (variable2 + 25)
                 5. BP = add a constant to a register (BP + 25)     


             On the 8086, it is not possible to add two things in memory. That
             is:

                 add  variable1, variable2

             is an illegal instruction. Instead, you need to write:

                 mov  ax, variable2





             Chapter 5 - Addition and Subtraction                           37
             ____________________________________

                 add  variable1, ax 


             SUBTRACTION

             It is now time to do some subtraction. The instruction is SUB:

                 sub  destination, source

             subtracts source from destination and stores it in destination,
             the thing on the left.

                 sub  ax, cx         ; (ax - cx) -> ax

             In order to do subtraction we are going to modify add1.asm, so
             make a copy and call it sub1.asm:

                 >copy  add1.asm  sub1.asm

             How many instructions do we need to change to modify the program?
             Four.

                 add  dx, bx    ->        sub  dx, bx
                 add  dl, bl    ->        sub  dl, bl

             Each of these is changed twice, and we are ready to roll.
             Assemble it, link it, and run it. Once again we want to look at
             the flags at the end of each subtraction. For unsigned
             subtraction, look at ZF, the zero flag, and CF, the carry flag.
             This time, CF will be set if the result is below zero. For signed
             subtraction, look at OF, the overflow flag, SF, the sign flag,
             and ZF, the zero flag. As with addition, subtraction changes PF,
             the parity flag and AF the auxillary flag. They don't concern us.

             As with addition, there are five possibilities for subtraction.
             They are:

                 1. subtract one register from another
                 2. subtract a register from a variable (memory)
                 3. subtract a variable (memory) from a register
                 4. subtract a constant from a variable (memory)
                 5. subtract a constant from a register

             the code for these is:

                 sub  cx, bx         ; (cx - bx)         ->   cx
                 sub  variable1, bx  ; (variable1 - bx)  ->   variable1
                 sub  si, variable2  ; (si - variable2)  ->   si
                 sub  variable2, 25  ; (variable2 - 25)  ->   variable2
                 sub  bp, 25         ; (bp - 25)         ->   bp

             You can copy add2.asm to sub2.asm if you want and change the five
             ADD instructions to SUB instructions. It will then do those five
             types of subtraction. 






             The PC Assembler Tutor                                         38
             ______________________

             SIGNED AND UNSIGNED NUMBERS

             What should you do if you are doing unsigned addition or
             subtraction and the carry flag gets set? It depends. Sometimes it
             makes a difference, sometimes it doesn't. If you have an error
             handling routine, then you can call it with the following code:

                      add  ax, bx
                      jnc  go_on
                      call error_handler
                 go_on:

             JC and JNC are conditional jump instructions. JC (jump on carry)
             jumps if the carry flag is set (1) and JNC (jump on not carry)
             jumps if the carry flag is not set (0). Using reverse logic here,
             we skip the error handler if everything is ok.

             For signed numbers, it is certainly an error if there is
             overflow. You are making mathematical calculations and you now
             have invalid data. One possibility is to do the same as above but
             with the overflow flag.

                      add  ax, bx
                      jno  go_on
                      call error_handler
                 go_on:

             JO and JNO are two more conditional jump instructions.  JO (jump
             on overflow) jumps if the overflow flag is set (1) and JNO (jump
             on not overflow) jumps if the overflow flag is not set (0). We
             use the same logic here. 

             However, there is one special instruction for signed numbers, and
             that is INTO (interrupt on overflow). It is possible to have an
             error handler external to your program. It sits permanantly in
             memory. When you make a signed arithmetic error, INTO interrupts
             your program and goes to the external error handler. The code
             looks like this:

                 add  ax, bx
                 into

             You probably don't have an error handler in your computer right
             now. In that case, INTO simply goes looking for it and returns
             when it can't find it.

             Let's find out if you have an error handler installed. Once
             again, use template.asm

             ; + + + + + + + + + + + + + + + START CODE BELOW THIS LINE 
                    mov   ax_byte, 1          ; signed register style  
                    mov   bx_byte, 1 
                    mov   cx_byte, 1 
                    lea   ax, ax_byte 
                    call  set_reg_style 
                    call  show_regs 




             Chapter 5 - Addition and Subtraction                           39
             ____________________________________

             outer_loop: 
                    call  get_signed 
                    push  ax 
                    call  get_signed 
                    mov   bx, ax 
                    pop   ax 
                    mov   cx, ax 
                    add   cx, bx 
                    into 
                    call  show_regs 
                    jmp   outer_loop 
             ; + + + + + + + + + + + + + + + END CODE ABOVE THIS LINE 

             This is basically the same thing as before, but using AX, BX, and
             CX. They are set for signed style, and then we  get two signed
             numbers and add them. The result is in CX. Right after the
             addition instruction is INTO. If the result is too positive or
             too negative, OF will be set and INTO will look for the error
             handler. 

             Assemble this program and link it with asmhelp.obj. Try both
             numbers that do not set the overflow flag and numbers that do set
             the overflow flag. Did anything different happen when the
             overflow flag was set? If nothing different happened, you don't
             have an error handler for INTO. 

             Included on the disks is an error handler. It is called INTO.COM,
             and it's pathname is \XTRAFILE\INTO.COM. When you run it:

                 >into

             it will install itself and then return to the command prompt:

                 >

             INTO.COM will stay in memory until you reboot or shut off the
             machine. INTO.COM provides the type of sophisticated error
             handling that you might want to use in a real program. Install
             (run) INTO.COM, and then try the previous program again, both
             with numbers that cause an overflow and numbers that don't cause
             an overflow.



















             The PC Assembler Tutor                                         40
             ______________________

                                          SUMMARY


             ADD performs both signed and unsigned addition. It can:

                 1. add two registers
                 2. add a register to a variable (memory)
                 3. add a variable (memory) to a register
                 4. add a constant to a variable (memory)
                 5. add a constant to a register


             SUB performs both signed and unsigned subtraction. It can:

                 1. subtract one register from another
                 2. subtract a register from a variable (memory)
                 3. subtract a variable (memory) from a register
                 4. subtract a constant from a variable (memory)
                 5. subtract a constant from a register


             The flags affected by both ADD and SUB are:

                 CF   the carry flag (for unsigned). Set if the 0/65535
                 (0/255) border was crossed.

                 ZF   the zero flag (for signed and unsigned). Set if the
                 result is 0.

                 SF   the sign flag (for signed). Set if the result is
                 negative.

                 OF   the overflow flag (for signed). Set if the result was
                 too negative or too positive.

                 PF   the parity flag and AF, the auxillary flag

             The following jump instructions are conditional on the setting of
             the flags:

                 JC   jump on carry, JNC, jump on not carry
                 JO   jump on overflow. JNO, jump on not overflow

             LOOP
                 LOOP decrements cx by 1. If cx is then not zero, it jumps to
                 the named label. If cx is zero, it falls through to the next
                 instruction.

             INTO
                 If the overflow flag is set, INTO (interrupt on overflow)
                 interrupts the program and goes to an external error handler
                 if one exists. It returns immediately if one doesn't exist.

             PUSH and POP
                 PUSH stores either a register or a word (in memory) in a
                 temporary storage area. POP retrieves the last word PUSHed.