MICRO-C
    
                             A compact 'C' compiler
                               for small systems.
    
                                Technical Manual
    
    
    
    
    
                                  Release 2.0
    
                               Revised 10-Aug-90
    
    
    
    
    
    
    
    
    
    
    
    
    
    
    
                       Copyright 1988,1990 Dave Dunfield
                              All rights reserved

    MICRO-C                                                          Page: 1


    1. INTRODUCTION
    
          MICRO-C is a compact, portable compiler for a subset  of  the  'C'
       language which is suitable for implementation on small 8  or  16  bit
       computer systems. It may be used as a resident or cross compiler, and
       is capable of generating ROMable code. It is  distributed  in  source
       form, and thus provides a learning tool for those wishing to  examine
       the internals of a working compiler.
    
          The main goal in the development of MICRO-C, has been to provide a
       reasonably powerful language  which  will  be  portable  with  little
       difficulty to many  target  systems.  The  'C'  language  was  chosen
       because  it  was  designed  to  be  portable,  and   provides   ample
       programming power. MICRO-C provides  an  alternative  to  interpreted
       BASIC or assembly language  programming  which  are  often  the  only
       languages available on small 8 bit systems.
    
          With today's focus on larger computers and workstations,  software
       support for small  systems  and  micro-controller  sized  devices  is
       getting hard to find. MICRO-C helps fill that gap, because all  files
       necessary to port and maintain  the  compiler  are  included  on  the
       distribution disk, allowing it to be  moved  to  ANY  system  without
       dependance on a software vendor.
    
          Sample code generators  and  runtime  librarys  are  included  for
       several popular microprocessors.
    
          Also included with the compiler is the 'C' and 'ASM'  source  code
       for a complete library of system functions, as well  several  example
       programs.
    
          The MICRO-C "package" (software and documentation) is copyrighted,
       and may  not  be  re-distributed  in  any  form  without  my  written
       permission. If you have received the  "DEMO"  archive,  and  wish  to
       obtain the entire MICRO-C package complete with source code, fill out
       and send the order form contained in the "READ.ME" file,  along  with
       the required payment to:
    
                           Dave Dunfield
                           56 Burnetts Grove Circle,
                           Nepean, Ont. (Canada)
                           K2J 1N6
    
          If you choose not to order the complete MICRO-C package, you  MUST
       discontinue using MICRO-C within thirty days.
    
          MICRO-C is provided on an "as is" basis, with no warranty  of  any
       kind. In no event shall the author be liable for any damages  arising
       from its use or distribution.

    MICRO-C                                                          Page: 2


       1.1 Code Portability
    
             With few exceptions, this compiler follows the  syntax  of  the
          "standard" UNIX compiler (within  its  subset  of  the  language).
          Programs written in MICRO-C should compile with few changes  under
          other "standard" compilers.
    
          1.1.1 Unsupported Features:
    
                MICRO-C does not currently support the following features of
             standard 'C':
    
                    Long, Double, Float and Enumerated data types,
                    Structures, Unions, Typedef and Bit fields.
    
          1.1.2 Additional Features
    
                MICRO-C provides a few additional  features  which  are  not
             always included in "standard" 'C' compilers:
    
                    Unsigned character variables, Nested comments, 16 bit
                    character constants, Inline assembly code capability.
    
       1.2 Compiler Portability
    
             MICRO-C is written in standard 'C', and is capable of compiling
          itself. This allows any system  with  a  'C'  compiler  (including
          MICRO-C) to be used to port MICRO-C to another processor.
    
             The  parser  makes  very  few  assumptions  about  the   target
          processor  or  operating  system  architecture,  allowing  a  code
          generator  to  be  written  for  virtually   any   processor   and
          environment.
    
             With the exception of required I/O routines (described  later),
          the MICRO-C compiler uses no library functions, and relies  on  no
          system services.
    
             Assuming that the code generator is fairly efficent,  and  that
          the I/O routines and code generator are not unreasonably large,  a
          full MICRO-C compiler may be implemented on systems with as little
          as 32K of free ram and a single floppy disk.

    MICRO-C                                                          Page: 3


       1.3 The MCC command
    
             When  created  using  the  'io'  routines   supplied   on   the
          distribution disk, the format of the MICRO-C Compiler command line
          is:
    
                    MCC [input_file] [output_file] [options]
    
             [input_file] is the name of  the  source  file  containing  'C'
          statements to read. If no filenames are given, MCC will read  from
          standard input.
    
             [output_file] is the name of the file to  write  the  generated
          assembly  language  code  to.  If  less  than  two  filenames  are
          specified, MCC will write to standard output.
    
          1.3.1 Command Line Options
    
                -q      - Instructs MCC to be quiet, and not display the
                          startup message when it is executed.

    MICRO-C                                                          Page: 4


    2. THE MICRO-C PROGRAMMING LANGUAGE
    
          The following pages contain a brief summary of  the  features  and
       constructs implemented in MICRO-C.
    
          This document does not  attempt  to  teach  'C'  programming,  and
       assumes that the reader is familiar with the language.
    
       2.1 Constants
    
             The following forms of constants are supported by the compiler:
    
                <num>       - Decimal number        (0 - 65535)
                0<num>      - Octal number          (0 - 0177777)
                0x<num>     - Hexidecimal number    (0x0 - 0xffff)
                '<char>'    - Character             (1 or 2 chars)
                "<string>"  - Address of literal string.
    
             The following "special" characters may be used within character
          constants or strings:
    
                \n          - Newline (line-feed)   (0x0a)
                \r          - Carriage Return       (0x0d)
                \t          - Tab                   (0x09)
                \f          - Formfeed              (0x0c)
                \b          - Backspace             (0x08)
                \<num>      - Octal value <num>     (Max. three digits)
                \x<num>     - Hex value <num>       (Max. two digits)
                \<char>     - Protect character <char> from input scanner.
    
       2.2 Symbols
    
             Symbol names  may  include  the  characters  'a'-'z',  'A'-'Z',
          '0'-'9', and '_'. The characters '0'-'9' may not be  used  as  the
          first character in the  symbol  name.  Symbol  names  may  be  any
          length, however, only the first 15 characters are significant.
    
             The "char" modifier may be used to declare a symbol as an 8 bit
          wide value, otherwise it is assumed to be 16 bits.
    
                              eg: char input_char;
    
             The "int" modifier may be used to declare a symbol as a 16  bit
          wide value. This is assumed if neither "int" or "char" is given.
    
                                  eg: int abc;
    
             The "unsigned" modifier may be used to declare a symbol  as  an
          unsigned positive only value. Note that unlike some 'C' compilers,
          this modifier may be applied to a character (8 bit) variable.
    
                            eg: unsigned char count;

    MICRO-C                                                          Page: 5


             The "extern" modifier causes the compiler to be  aware  of  the
          existance and  type  of  a  global  symbol,  but  not  generate  a
          definition for that symbol. This allows the module being  compiled
          to reference a symbol which is defined  in  another  module.  This
          modifier may not be used with local symbols.
    
                            eg: extern char getc();
    
             A  symbol  declared  as  external  may  be  re-declared  as   a
          non-external at a later  point  in  the  code,  in  which  case  a
          definition for it will be generated. This allows  "extern"  to  be
          used to inform the compiler of a function or variable type so that
          it can be referenced  properly  before  that  symbol  is  actually
          defined.
    
             The "static" modifier causes global variables to  be  available
          only in the file where they are defined.  Variables  or  functions
          declared  as  "static"  will  not  be   accessable   as   "extern"
          declarations in other object files, nor will they cause  conflicts
          with duplicate names in those files.
    
                         eg: static int variable_name;
    
             The "register" modifier indicates to the  code  generator  that
          this is a high priority variable, and should be kept where  it  is
          easy to get at. Since  its  interpretation  depends  on  the  code
          generator, it is often  ignored  in  simple  implementations.  See
          "Functions" for a  special  use  of  "register"  when  defining  a
          function.
    
                          eg: register unsigned count;
    
             Symbols declared with a preceeding '*' are assumed to be 16 bit
          pointers to the declared type.
    
                             eg: int *pointer_name;
    
             Symbol names declared followed by square brackets  are  assumed
          to be arrays with a number of dimensions equal to  the  number  of
          '[]' pairs that follow. The size of each dimension  is  identified
          by a constant value  contained  within  the  corresponding  square
          brackets.
    
                          eg: char array_name[5][10];
    
          2.2.1 More Symbol Examples
    
                char a;                 /* 8 bit signed */
                unsigned char b;        /* 8 bit unsigned */
                int c;                  /* 16 bit signed */
                unsigned int d;         /* 16 bit unsigned */
                unsigned e;             /* also 16 bit unsigned */
                extern char f();        /* external function returning char */

    MICRO-C                                                          Page: 6


          2.2.2 Global Symbols
    
                Symbols  declared  outside  of  a  function  definition  are
             considered to  be  global  and  will  have  memory  permanently
             reserved for them. Global symbols are defined by  name  in  the
             output file, allowing other modules to access them.
    
                Note that the compiler IS case  sensitive,  however  if  the
             assembler you are using is NOT, you  must  be  careful  not  to
             declare any global symbols with names that differ only in case.
    
                All non-initialized global variables are  generated  at  the
             very end of the output file, after the literal pool is  dumped.
             Since non-initialized globals do not generate object code, this
             allows them to be excluded from the image file when it is saved
             to disk.
    
                Global variables may be initialized with one or more values,
             which are expressed as a single array of  integers  REGUARDLESS
             of the size and shape of the variable. If more than  one  value
             is expressed, '{' and '}' must be used.
    
                   eg: int i = 10, j[2][2] = { 1, 2, 3, 4 };
    
                When arrays are declared, a null dimension may  be  used  as
             the dimension size, in which case the size of  the  array  will
             default to the number of initialized values.
    
                         eg: int array[] = { 1, 2, 3 };
    
                Initialized global variables are automatically saved  within
             the code image,  insuring  that  the  initial  values  will  be
             available at run time. Any non-initialized elements of an array
             which has been partly initialized will be set to zero.
    
                Non-initialized global variables are not preset in any  way,
             and will be undefined at the beginning of program execution.
    
          2.2.3 Local Symbols
    
                Symbols declared within a function definition are  allocated
             on the stack, and  exist  only  during  the  execution  of  the
             function.
    
                To simplify the allocation and de-allocation of stack space,
             all local symbols must be declared  at  the  beginning  of  the
             function before any code producing statements are encountered.
    
                MICRO-C does not support initialization of  local  variables
             in the declaration statement. Since local variables have to  be
             initialized every time the function is entered, you can get the
             same effect using assignment statements at the beginning of the
             function.
    
                No type is assumed for  arguments  to  functions.  Arguments
             must be explicitly declared, otherwise they will  be  undefined
             within the scope of the function definition.

    MICRO-C                                                          Page: 7


       2.3 Arrays & Pointers
    
             When MICRO-C passes an array to a function, it actually  passes
          a POINTER to the array. References to arrays which  are  arguments
          are automatically performed through the pointer.
    
             This allows the use of pointers and arrays to be interchangable
          through the context of a function call. Ie: An array passed  to  a
          function may be declared and used as  a  pointer,  and  a  pointer
          passed to a function may be declared and used as an array.
    
       2.4 Functions
    
             Functions are  essentially  initialized  global  symbols  which
          contain executable code.
    
             MICRO-C accepts  any  valid  value  as  a  function  reference,
          allowing  some  rather  unique  (although  non-standard)  function
          calls.
    
          For example:
    
                function();     /* call function */
                variable();     /* call contents of a variable */
                (*var)();       /* call indirect through variable */
                (*var[x])();    /* call indirect through indexed array */
                0x5000();       /* call address 0x5000 */
    
             Since this is a single pass compiler, operands to functions are
          evaluated and pushed on the stack in the order in which  they  are
          encountered, leaving the last operand closest to the  top  of  the
          stack. This is the opposite order from which  many  'C'  compilers
          push operands.
    
             For functions with a fixed number of arguments,  the  order  of
          which operands  are  passed  is  of  no  importance,  because  the
          compiler looks after generating  the  proper  stack  addresses  to
          reference variables.  HOWEVER,  functions  which  use  a  variable
          number of arguments are affected for two reasons:
    
          1) The location of the LAST arguments are known (as fixed  offsets
             from the stack pointer) instead of the FIRST.
    
          2) The symbols defined as arguments  in  the  function  definition
             represent the LAST arguments instead of the FIRST.
    
             If a function is declared as "register", it  serves  a  special
          purpose and causes the accumulator to be loaded with the number of
          arguments passed whenever the function is called. This allows  the
          function to know how many  arguments  were  passed  and  therefore
          determine the location of the first argument.

    MICRO-C                                                          Page: 8


       2.5 Control Statements
    
             The following control statements are implemented in MICRO-C:
    
                if(expression)
                    statement;
    
                if(expression)
                    statement;
                else
                    statement;
    
                while(expression)
                    statement;
    
                do
                    statement;
                while expression;
    
                for(expression; expression; expression)
                    statement;
    
                return;
    
                return expression;
    
                break;
    
                continue;
    
                switch(expression) {
                    case constant_expression :
                        statement;
                        ...
                        break;
                    case constant_expression :
                        statement;
                        ...
                        break;
                        .
                        .
                        .
                    default:
                        statement; }
    
                label: statement;
    
                goto label;

    MICRO-C                                                          Page: 9


    2.5.1 Notes on Control Structures
    
        1)  Any "statement" may be a single statement or a compound
            statement enclosed within '{' and '}'.
    
        2)  All three "expression"s in the "for" command are optional.
    
        3)  If a "case" selection does not end with "break;", it will
            "fall through" and execute the following case as well.
    
        4)  Expressions following 'return' and 'do/while' do not have
            to be contained in brackets (although this is permitted).
    
        5)  Label names may preceed any statement, and must be any
            valid symbol name, followed IMMEDIATELY by ':' (No spaces
            are allowed). Labels are considered LOCAL to a function
            definition and will only be accessable within the scope
            of that function.

    MICRO-C                                                          Page: 10


       2.6 Expression Operators
    
             The following expression operators are implemented in MICRO-C:
    
    2.6.1 Unary Operators
    
        -           - Negate
        ~           - Complement
        !           - Logical complement
        ++          - Pre or Post increment
        --          - Pre or post decrement
        *           - Indirection
        &           - Address of
        (type)      - Typecast
    
    2.6.2 Binary Operators
    
        +           - Addition
        -           - Subtraction
        *           - Multiplication
        /           - Division
        %           - Modulus
        &           - Bitwise AND
        |           - Bitwise OR
        ^           - Bitwise EXCLUSIVE OR
        <<          - Shift left
        >>          - Shift right
        ==          - Test for equality
        !=          - Test for inequality
        >           - Test for greater than
        <           - Test for less than
        >=          - Test for greater than or equal to
        <=          - Test for less than or equal to
        &&          - Logical AND
        ||          - Logical OR
        =           - Assignment
        +=          - Add to self assignment
        -=          - Subtract from self assignment
        *=          - Multiply by self assignment
        /=          - Divide by and reassign assignment
        %=          - Modular self assignment
        &=          - AND with self assignment
        |=          - OR with self assignment
        ^=          - EXCLUSIVE OR with self assignment
        <<=         - Shift left self assignment
        >>=         - Shift right self assignment

    MICRO-C                                                          Page: 11


    NOTES:
    
        1)  The expression "a && b" returns 0 if "a" is zero, otherwise the
            value of "b" is returned. The "b" operand is NOT evaluated if
            "a" is zero.
    
        2)  The expression "a || b" returns the value of "a" if it is not 0,
            otherwise the value of "b" is returned. The "b" operand is NOT
            evaluated if "a" is non-zero.
    
    2.6.3 Other Operators
    
        ;           - Ends a statement.
        ,           - Allows several expressions in one statement.
                    + Separates symbol names in multiple declarations.
                    + Separates constants in multi-value initialization.
                    + Separates operands in function calls.
        ?           - Conditional expression.
        :           - Delimits labels, ends CASE and separates conditionals.
        { }         - Defines a block of statements.
        ( )         - Forces priority in expression, indicates function calls.
        [ ]         - Indexes arrays. If fewer index values are given than the
                      number of dimensions which are defined for the array, the
                      the value returned will be a pointer to the appropriate
                      address.
    
                    Eg:
                        char a[5][2];
    
                        a[3] returns address of forth row of two elements.
                        (remember index's start from zero)
    
                        a[3][0] returns the character at index [3][0];

    MICRO-C                                                          Page: 12


       2.7 Preprocessor Commands
    
             The  MICRO-C  compiler  supports  the  following  pre-processor
          commands. These commands are recognized only if they occur at  the
          beginning of the input line.
    
             NOTE:  This  describes  the  limited  pre-processor  which   is
          integral to the  compiler,  see  also  the  section  on  the  more
          powerful external processor (MCP).
    
          2.7.1 #asm
    
                Causes the compiler to copy all subsequent lines directly to
             the output  file  without  translation.  This  allows  assembly
             language code to be included in the 'C' program.
    
          2.7.2 #endasm
    
                Terminates a "#asm",  and  causes  the  compiler  to  resume
             compiling from the input file.
    
          2.7.3 #define <name> <replacement_text>
    
                The "#define" command allows a global name  to  be  defined,
             which will be replaced with the indicated text whenever  it  is
             encountered in the input file. This occurs prior to  processing
             by the compiler.
    
          2.7.4 #include <filename>
    
                This command causes the indicated file to be opened and read
             in as the source  text.  When  the  end  of  the  new  file  is
             encountered, processing will continue with the  line  following
             "#include" in the original file.
    
          2.7.5 #ifdef <name>
    
                Processes the following lines (up to #else or  #endif)  only
             if the given name is defined.
    
          2.7.6 #ifndef <name>
    
                Processes the following lines (up to #else or  #endif)  only
             if the given name is NOT defined.
    
          2.7.7 #else
    
                Processes the following lines (up to  #endif)  only  if  the
             preceeding #ifdef or #ifndef was false.
    
          2.7.8 #endif
    
                Terminates #ifdef and #ifndef
    
                NOTE: The #ifdef and #ifndef contructs may not be nested.

    MICRO-C                                                          Page: 13


       2.8 Error Messages
    
             When MICRO-C detects an  error,  it  outputs  an  informational
          message indicating the type of problem encountered.
    
             The error message is preceeded by the  line  number(s)  of  the
          line containing the error in all files being processed.
    
                             eg: 5:3: Syntax error
    
             In the above example, the main input file "#included" a file at
          line 5, and a syntax error was discovered in that file at line 3.
    
             The following error messages are produced by the compiler:
    
          2.8.1 Compilation aborted
    
                The preceeding error was so severe than the compiler  cannot
             proceed.
    
          2.8.2 Constant expression required
    
                The compiler requires a constant  expression  which  can  be
             evaluated at compile time (ie: no variables).
    
          2.8.3 Declaration must preceed code.
    
                All local variables must be defined at the beginning of  the
             function, before any code producing statements are processed.
    
          2.8.4 Dimension table exhausted
    
                The compiler has encountered more  active  array  dimensions
             than it can handle.
    
          2.8.5 Duplicate local: 'name'
    
                You have declared the named  local  symbol  more  than  once
             within the same function definition.
    
          2.8.6 Duplicate global: 'name'
    
                You have declared the named global symbol more than once.
    
          2.8.7 Expected '<token>'
    
                The compiler  was  expecting  the  given  token,  but  found
             something else.
    
          2.8.8 Expression stack overflow
    
                The compiler has found a more complicated expression than it
             can handle. Check that it is of  correct  syntax,  and  if  so,
             break it up into two simpler expressions.

    MICRO-C                                                          Page: 14


          2.8.9 Expression stack underflow
    
                The compiler has made an error in  parsing  the  expression.
             Check that it is of correct syntax.
    
          2.8.10 Illegal indirection
    
                You have attempted to perform an indirect operation ('*'  or
             '[]') on an entity which is not a pointer or array. This  error
             will also result if you attempt to index  an  array  with  more
             indices than it has dimensions.
    
          2.8.11 Illegal initialization
    
                Local variables may not be initialized  in  the  declaration
             statement. Use assignments at the  beginning  of  the  function
             code to perform the initialization.
    
          2.8.12 Illegal nested function
    
                You may not declare a  function  within  the  definition  of
             another function.
    
          2.8.13 Improper #else/#endif
    
                A #else or #endif statement is out of place.
    
          2.8.14 Inconsistant re-declaration: 'name'
    
                You have attempted to redefine  the  named  external  symbol
             with a type which does not match its previously declared type.
    
          2.8.15 Incorrect declaration
    
                A statement occuring outside of a function definition is not
             a valid declaration for a function or global variable.
    
          2.8.16 Invalid '&' operation
    
                You have attempted to reference  the  address  of  something
             that has no address. This error also occurs when you attempt to
             take the address of an array without giving it a  full  set  of
             indicies. Since the address is already returned in  this  case,
             simply drop the '&'. (The error occurs because you  are  trying
             to take the address of an address).
    
          2.8.17 Macro expansion too deep
    
                The compiler has encountered a nested macro reference  which
             is too deep to be resolved.
    
          2.8.18 Macro space exhausted
    
                The compiler has encountered  more  macro  ("#define")  text
             than it has room to store.

    MICRO-C                                                          Page: 15


          2.8.19 No active loop
    
                A "continue" or "break" statement was  encountered  when  no
             loop is active.
    
          2.8.20 No active switch
    
                A "case" or "default"  statement  was  encountered  when  no
             "switch" statement is active.
    
          2.8.21 Not an argument: 'name'
    
                You have declared the named variable as an argument, but  it
             does not appear in the argument list.
    
          2.8.22 Non-assignable
    
                You have attempted an operation which results in  assignment
             of a value to an entity which cannot be assigned. (eg: 1 = 2);
    
          2.8.23 Numeric constant required
    
                The compiler requires a constant expression which returns  a
             simple numeric value.
    
          2.8.24 String space exhausted
    
                The compiler has encountered more literal  strings  than  it
             has room store.
    
          2.8.25 Symbol table full
    
                The compiler has encountered more symbol definitions than it
             can handle.
    
          2.8.26 Syntax error
    
                The statement shown does not follow syntax rules and  cannot
             be parsed.
    
          2.8.27 Too many active cases
    
                The compiler has run out of space  for  storing  switch/case
             tables. Reduce the number of active "cases".
    
          2.8.28 Too many defines
    
                The compiler has encountered more '#define' statements  than
             it can handle. Reduce the number of #defines.
    
          2.8.29 Too many errors
    
                The compiler is aborting because of excessive errors.

    MICRO-C                                                          Page: 16


          2.8.30 Too many includes
    
                The compiler has encountered more  nested  "#include"  files
             than it can handle.
    
          2.8.31 Too many initializers
    
                You have specified more initialization values than there are
             locations in the global variable.
    
          2.8.32 Type clash
    
                You  have  attempted  to  combine  values   which   are   of
             incompatible types.
    
          2.8.33 Unable to open: 'name'
    
                A "#include" command specified the named file,  which  could
             not be opened.
    
          2.8.34 Undefined: 'name'
    
                You have referenced a name which is not defined as  a  local
             or global symbol.
    
          2.8.35 Unreferenced: 'name'
    
                The named  symbol  was  defined  as  a  local  symbol  in  a
             function, but was never used in that function. This error  will
             occur at the end of  the  function  definition  containing  the
             symbol declaration. It is only a warning, and  will  not  cause
             the compile to abort.
    
          2.8.36 Unresolved: 'name'
    
                The named symbol was forward  referenced  (Such  as  a  GOTO
             label), and was never defined. This error will occur at the end
             of the function definition containing the reference.
    
          2.8.37 Unterminated conditional
    
                The end of file was encountered  when  a  "#if"  or  "#else"
             conditional block was being processed.
    
          2.8.38 Unterminated function
    
                The  end  of  the  file  was  encountered  when  a  function
             definition was still open.

    MICRO-C                                                          Page: 17


       2.9 Quirks
    
             In its effort to provide the maximum  amount  of  functionality
          with the minimum amount of code, MICRO-C  deviates  from  standard
          'C' in some areas. The following is a short summary of  the  major
          infractions and quirks:
    
             The operands to '#' commands are  parsed  based  on  separating
          spaces, and any portion of the line not required  is  ignored.  In
          particular, the '#define' command only accepts a definition up  to
          the next space or tab character.
    
            eg: #define APLUSONE A+1        <-- uses "A+1"
                #define APLUSONE A +1       <-- uses "A"
    
             Comments are stripped by the token scanner, which occurs  AFTER
          the '#' commands are processed.
    
            eg: #define NULL    /* comment */   <-- uses "/*"
    
             Note that since comments can therefore be included in "#define"
          symbols, you can use "/**/" to simulate spaces between tokens.
    
            eg: #define BYTE unsigned/**/char
    
             Include filenames are not delimited by '""'  or  '<>'  and  are
          passed to the operating system exactly as entered.
    
            eg: #include /mc/stdio.h
    
             NOTE:  The  above  quirks  do  not  apply  when  the   external
          pre-processor (MCP) is used.
    
             The appearance of a variable name in the argument  list  for  a
          function  declaration  serves  only  to  identify  that  variables
          location on the stack. MICRO-C will not define the variable unless
          it is explicitly declared (between the argument list and the  main
          function body). In other words, all arguments to a  function  must
          be explicitly declared.
    
             MICRO-C is more  strict  about  its  handling  of  the  ADDRESS
          operator ('&') than most other compilers. It will produce an error
          message if you attempt to take the address of  a  value  which  is
          already a fixed address (such as an array name without a full  set
          of indicies). Since an address is already produced in such  cases,
          simply drop the '&'.
    
             The 'x' in '0x' and '\x' is accepted in lower case only.

    MICRO-C                                                          Page: 18


             When operating on pointers, MICRO-C only scales  the  increment
          (++), decrement (--) and index ([]) operations to account for  the
          size of the pointer:
    
            eg: char cptr;      /* pointer to character */
                int  cptr;      /* pointer to integer */
                ++cptr;         /* Advance one character */
                ++iptr;         /* Advance one integer */
                cptr[10];       /* Access the tenth character */
                iptr[10];       /* Access the tenth integer */
                cptr += 10;     /* Advance 10 characters */
                iptr += 10;     /* Advance ONLY FIVE integers */
    
        NOTE: A portable way to advance "iptr" by integers is:
    
                iptr = &iptr[10];   /* Advance 10 integers */
    
             When using MICRO-C to create  a  function  which  will  contain
          assembly language code, remember that MICRO-C allocates all  local
          variables at the beginning of a function definition, and will  not
          generate the function entry code until a non-declarative statement
          is encountered. In particular, since  "#asm"  is  handled  by  the
          pre-processor and not seen as  a  statement  by  the  parser,  you
          should use a "null" statement (';') to ensure that the entry  code
          is generated prior to using "#asm" at the beginning of a function.
    
            eg: func()
                { ;     /* ensures "entry" code is generated */
                #asm
                    assembly statements
                #endasm
                }
    
             Also note, that MICRO-C will not output  external  declarations
          to the output file  for  any  variables  or  functions  which  are
          declared as "extern", unless that symbol is actually referenced in
          the 'C' source code. This prevents "extern" declarations in system
          header files (such as "stdio.h") which are used as prototypes  for
          some library functions from causing those functions to  be  loaded
          into the object file. Therefore, any "extern"  symbols  which  are
          referenced only by assembly code (using "#asm") must  be  declared
          in assembly code, not by the MICRO-C "extern" statement.

    MICRO-C                                                          Page: 19


             Unlike some  'C'  compilers,  MICRO-C  will  process  character
          expressions using only  BYTE  values.  Character  values  are  not
          promoted to INT unless there is  an  INT  value  involved  in  the
          expression. This results in much more efficent code  when  dealing
          with characters, particularily  on  small  processors  which  have
          limited 16 bit instructions. Consider the statement:
    
                                 return c + 1;
    
             On some compilers, this will sign extend the character variable
          'c' into an integer value, and then ADD an integer  1  and  return
          the  result.  MICRO-C  will  ADD  the  character  variable  and  a
          character 1, and then promote the result to INT  before  returning
          it (results of expressions as  operands  to  'return'  are  always
          promoted to int).
    
             Unfortunately, programs have been written  which  rely  on  the
          automatic promotion of characters to INTs to  work  properly.  The
          most common source of problems is code  which  attempts  to  treat
          CHAR variables as UNSIGNED values (older compilers did not support
          UNSIGNED CHAR). For example:
    
                                return c & 255;
    
             In a compiler which always evaluates character  expressions  as
          INT, the above statement will extract the value of 'c' as positive
          integer ranging from 0 to 255.
    
             In MICRO-C, ANDing a character with 255  results  in  the  same
          character, which gets promoted to an integer  value  ranging  from
          -128 to 127. To force the promotion  within  the  expression,  you
          could CAST the variable to an INT:
    
                              return (int)c & 255;
    
             The same objective can be achieved  in  a  more  efficent  (and
          correct) manner by declaring the variable 'c' as UNSIGNED CHAR, or
          by CASTing the variable to an UNSIGNED value:
    
                              return (unsigned)c;
    
             Note that this is not only more clearly shows the intent of the
          programmer, but also results is more efficent code generated.

    MICRO-C                                                          Page: 20


    3. ADVANCED TOPICS
    
          This section provides information on the more advanced aspects  of
       MICRO-C, which  is  generally  not  needed  for  casual  use  of  the
       language.
    
       3.1 Conversion Rules
    
             MICRO-C keep track of the "type" of  each  value  used  in  all
          expressions. This type identifies certain characteristics  of  the
          value,  such  as   size   range   (8/16   bits),   numeric   scope
          (signed/unsigned), reference (value/pointer) etc.
    
             When an  operation  is  performed  on  two  values  which  have
          identical "types", MICRO-C assigns that same "type" to the result.
    
             When the  two  value  "types"  involved  in  an  operation  are
          different, MICRO-C calculates the "type" of the result  using  the
          following rules:
    
          3.1.1 Size range
    
                If both values are  direct  (not  pointer)  references,  the
             result will be 8 bits only if  both  values  were  8  bits.  If
             either value was 16 bits, the result will be 16 bits.
    
                If one value is a pointer, and  the  other  is  direct,  the
             result will be a pointer to the same size value as the original
             pointer.
    
                If both values were pointers, the result will be  a  pointer
             to 16 bits only if both original  pointers  referenced  16  bit
             values. If either pointer referenced an 8 bit value, the result
             will reference an 8 bit value.
    
          3.1.2 Numeric Scope
    
                The result of an expression is considered to be signed  only
             if both original values were signed. If  either  value  was  an
             unsigned value, the result is unsigned.
    
          3.1.3 Reference
    
                If either of the original values was a pointer,  the  result
             will be a pointer.
    
             Note that this "calculated" result type  is  used  for  partial
          results within an expression. Whenever a symbol such as a variable
          or function is referenced, the type of that symbol is  taken  from
          its declaration, no matter what "type" of value  was  last  stored
          (variable) or returned (function).

    MICRO-C                                                          Page: 21


       3.2 Assembly Language Interface
    
             Assembly language programs may be called from 'C' functions and
          vice versa. These programs may be in the form of "#asm" statements
          in the 'C' source code, or separately linked modules.
    
             When MICRO-C calls any routine ('C'  or  assembler),  it  first
          pushes all arguments to the routine onto the processor  stack,  in
          the order in  which  they  occur  in  the  argument  list  to  the
          function. This means that the LAST argument  to  the  function  is
          LOWEST on the processor stack.
    
             Arguments are always pushed as 16 bit values. Character  values
          are extended to 16 bits, and arrays are passed as 16 bit  pointers
          to the array. (MICRO-C knows that arrays which are  arguments  are
          actually  pointers,  and  automatically  references  through   the
          pointer).
    
             After pushing the arguments, MICRO-C then generates  a  machine
          language subroutine  call,  thereby  executing  the  code  of  the
          routine.
    
             Since the compiler uses the ACCUMULATOR and INDEX REGISTER,  it
          will automatically save them (if necessary) during  processing  of
          the arguments to the function (even if no arguments are  present),
          and therefore these registers do not have to be preserved  by  the
          called routine.
    
             NOTE that any other  registers  used  by  the  code  generation
          routines (register variables etc) will not be  saved  by  MICRO-C,
          and should be preserved by called functions if their content is to
          be relied on between function calls.
    
             Once the called routine returns, the arguments are removed from
          the stack by the calling program. This usually consists of  simply
          adding the number of  bytes  pushed  as  arguments  to  the  stack
          pointer.
    
             When the called function executes, the first thing usually done
          is to push any registers which must be preserved, and  to  reserve
          space on the stack for any local variables which are required.  In
          some implementations, a "base" register may also be established to
          provide a stable reference to the local variables and arguments.
    
             It is the responsibility of the called function to  remove  any
          saved registers and local variable space from the stack before  it
          returns. If a value is to be returned to the calling  program,  it
          is expected to be in the ACCUMULATOR register.

    MICRO-C                                                          Page: 22


             Local variables in a  function  may  be  referenced  as  direct
          offsets from the "base" register or stack pointer.  Note  that  if
          the stack pointer is used, offsets must be adjusted for the number
          of bytes which are pushed and  popped  on  the  stack  during  the
          execution of the function.
    
             The address of a particular local variable is calculated as:
    
                                "base register"
                                       -
                     (Size of all local variables in bytes)
                                       + 
               (size of all preceeding local variables in bytes)
    
                                    -- OR --
    
                                "stack pointer"
                                       +
                   (# bytes pushed during function execution)
                                       +
               (size of all preceeding local variables in bytes)
    
             Arguments to a  function  may  also  be  referenced  as  direct
          offsets from the "base" register or stack  pointer,  in  much  the
          same way as local variables are.
    
             The address of a particular argument is calculated as:
    
                                "base register"
                                       +
        (# bytes pushed at entry of function to preserve registers etc.)
                                       +
                 (Size of return address on stack (usually 2))
                                       +
                      (# arguments from LAST argument) * 2
    
                                    -- OR --
    
                                "stack pointer"
                                       +
                   (# bytes pushed during function execution)
                                       +
                     (size of all local variables in bytes)
                                       +
        (# bytes pushed at entry of function to preserve registers etc.)
                                       +
                 (Size of return address on stack (usually 2))
                                       +
                      (# arguments from LAST argument) * 2
    
             NOTE: The (number of bytes pushed at entry of  function)  is  a
          function of the code generator,  and  depends  on  the  particular
          MICRO-C implementation. Examine  some  assembly  output  from  the
          compiler to determine the actual number on your system.

    MICRO-C                                                          Page: 23


             If a function has been declared  as  "register",  MICRO-C  will
          load the accumulator with  the  number  of  arguments  which  were
          passed, each time the function is called. This allows the function
          to determine the location of the first argument.
    
             The address of  the  first  argument  passed  to  a  "register"
          function may be calculated as:
    
                           (accumulator contents) * 2
                                       + 
                                "base register"
                                       +
        (# bytes pushed at entry of function to preserve registers etc.)
                                       +
                 (Size of return address on stack (usually 2))
    
                                    -- OR --
    
                           (accumulator contents) * 2
                                       +
                                "stack pointer"
                                       +
                   (# bytes pushed during function execution)
                                       +
                     (size of all local variables in bytes)
                                       +
        (# bytes pushed at entry of function to preserve registers etc.)
                                       +
                 (Size of return address on stack (usually 2))
    
             Global  variables  exist  at  absolute  addresses  and  may  be
          referenced directly by name from within assembler  programs.  Keep
          in mind however, that MICRO-C uses only the first 15 characters of
          a symbol's name. Also, many code generators will reduce  the  size
          of names even further, often using an algorithm  to  compress  the
          name rather than simply truncating it. For this reason,  it  is  a
          good idea to avoid using global symbol names which are longer than
          6 or 8 characters  if  they  are  to  be  referenced  from  within
          assembly language programs.

    MICRO-C                                                          Page: 24


       3.3 Compiling for ROM
    
             Assuming the code generator does not use such "nasty" things as
          self modifying code, the output  from  the  compiler  is  entirely
          "clean", and may be placed in Read Only Memory (ROM).
    
             The compiler places all initialized  global  variables  in  the
          output file as part of the code image. When the program is  stored
          in ROM, those variables are also stored in ROM, and  will  not  be
          modifiable.
    
             When the program is to be placed in ROM, you may not initialize
          any variables which you intend to modify  later.  Those  variables
          must be explicitly initialized by code executed at  the  beginning
          of the program.
    
             Initialized variables which you do not intend to  modify  (such
          as tables etc.) may be initialized in the declaration, and will be
          permanently saved in the ROM as part of the static code image.
    
             The  processor  stack  pointer  must  be  set  up  before   any
          expressions are evaluated, or any function  calls  are  performed.
          This may be performed via '#asm' statements.
    
             All non-initialized global variables must be  located  in  RAM.
          The compiler usually outputs all such variables at the very end of
          the compilation, just after dumping the literal pool.  The  global
          variables may be moved to RAM by  editing  the  output  file,  and
          placing an appropriate "ORG" statement at  the  beginning  of  the
          globals.
    
             If extensive compilation for ROM is being  performed,  you  may
          want to use a version of the compiler which uses  an  intermediate
          output file (see "PORTING THE COMPILER"). This allows  a  separate
          code generator to be customized for ROM applications,  which  will
          output the appropriate stack setup instructions (this can be  done
          in "def_module()"), and locate the global variables in  RAM  (this
          can be done at the end of "def_literal()").

    MICRO-C                                                          Page: 25


    4. PORTING THE COMPILER
    
          There are two major goals to accomplish when porting  the  MICRO-C
       compiler to a new machine. The first is to make the compiler  run  in
       the new environment, and the second is to make it  produce  code  for
       that environment.
    
          These two goals do not always go hand in hand. For example, it may
       be desirable to implement a CROSS COMPILER which generates code for a
       different system from that on which it runs.
    
          The usual method of porting a compiler to system A when a  version
       of the compiler is already running on system B, is to first create  a
       compiler which runs on system B, producing code for  system  A.  This
       "new" compiler may then be used to create a compiler  which  runs  on
       system A.
    
          The compiler consists of a module "compile"  which  contains,  the
       main compiler, input scanner, regular expression parser,  and  symbol
       table management routines.  This  is  the  "static"  portion  of  the
       compiler which does not change in different implementations.
    
          To create a working compiler, the above module  must  be  compiled
       and linked with an "io" module and "code"  module.  The  "io"  module
       performs the necessary initialization and I/O to allow  the  compiler
       to run in a particular  environment  (goal  #1).  The  "code"  module
       generates  the  assembly  language  output  code  for  a   particular
       environment (goal #2).
    
          The compiler uses NO system library functions, and  relies  on  NO
       system services (other  than  those  used  by  the  "io"  and  "code"
       modules). This allows the compiler to  be  ported  to  virtually  any
       system.
    
          All fixed compiler  parameters  (such  as  table  sizes  etc)  are
       contained in the header file "compile.h".  When  porting  to  systems
       with very limited RAM (less than 64k), you may have to reduce some of
       these sizes in order to get it to fit.
    
          Two additional modules are provided with the  compiler.  The  file
       "intercg.c", may be linked into the compiler in  place  of  the  code
       generator, and writes a "generic" intermediate  file  which  contains
       the pseudo operation and type tokens (See Code Generator).  The  file
       "genasm.c", may be linked with the regular "io" and  "code"  routines
       to produce a utility program which reads the  intermediate  file  and
       produces the assembly language code for a specific processor.
    
          NOTE: If your system makes a distinction between TEXT  and  BINARY
       files, the "io.c" routines must be modified for each program so  that
       the intermediate file will be accessed  in  BINARY  mode.  All  other
       files are accessed as TEXT.

    MICRO-C                                                          Page: 26


          Although this "split" compiling approach is slower than the  usual
       mode of direct assembly  language  production,  it  provides  several
       useful capabilities:
    
       1) The amount of ram required to  run  the  "separate"  compiler  and
          genasm programs can be considerably less than required to run  the
          "stand alone" compiler.
    
       2) A single parser may be used to generate code  for  several  target
          systems, by simply running a different  version  of  the  "genasm"
          utility, which is customized for each target.
    
       3) Use of the intermediate file  allows  distribution  of  "portable"
          programs which may be processed by "genasm" for different  targets
          WITHOUT distribution of the source code.
    
       4) A program may be written which processes this  intermediate  file,
          and "optimizes" the code. Additional "pseudo operation" codes  may
          be added to the output file if the target processor is capable  of
          operations which  the  more  "generic"  MICRO-C  output  does  not
          utilize.
    
       4.1 The "io" module
    
             The "io" module required  by  the  compiler  must  contain  the
          following function definitions:
    
             The function "main()" is called by the  operating  system  when
          the MICRO-C compiler is executed. It is  responsable  for  parsing
          any parmeters and command qualifiers, opening the input and output
          files,  performing  any  other  initializations  that   might   be
          required, and then  invoking  the  function  "compile()"  with  no
          arguments. The "compile" function is internal to  the  "compile.c"
          module, and will never return. For UNIX and  other  systems  which
          support I/O redirection, "stdin" and "stdout" are often  used  for
          the input and output files.
    
             The  function  "exit(rc)"  is  called  when  the  compiler  has
          finished all processing and wishes to terminate. The value "rc" is
          a return code: 0 = Success, program compiled without error,  -1  =
          Compile was aborted due to severe errors, n  =  Compile  finished,
          but had 'n' errors.
    
             The function "put_chr(chr, flag)"  is  passed  a  character  to
          output, as well as a flag. The flag will always be zero  when  the
          character is being sent to the console terminal, or non-zero  when
          the character is to be written to the output file.
    
             The function "put_str(*ptr, flag)" is passed  a  pointer  to  a
          zero terminated string, which is to be written to the  console  or
          output file as determined by "flag".
    
             The function "put_num(number, flag)" is passed a 16 bit number,
          which is to be written in printable form to the console or  output
          file as determined by "flag".

    MICRO-C                                                          Page: 27


          4.1.1 Compiler only routines
    
                The following I/O routines are required by the compiler, but
             not by the "genasm" program.
    
                The function  "get_lin(*ptr)"  is  passed  a  pointer  to  a
             character array,  and  should  read  a  single  line  from  the
             currently  open  input  file  into  that  array.  The  manifest
             definition "LINE_SIZE", found in "compile.h"  may  be  used  to
             determine the maximum line length acceptable to  the  compiler.
             Return of a non-zero value indicates the end of file condition.
    
                The  function  "f_open(*ptr)"  is  passed  a  pointer  to  a
             filename. The new file should be opened, and if successful, the
             old input file should remain open and be "stacked", so that  it
             can be later returned to. If the file was opened  successfully,
             a non-zero value should be returned. A zero value indicates  to
             the compiler that the file could not be opened.
    
                The function "f_close()"  is  responsible  for  closing  the
             currently open input  file,  and  returning  to  the  "stacked"
             previously open one. It receives no parameters. Note:  multiple
             "opens" may  be  stacked  -  see  the  manifest  definition  of
             "INCL_DEPTH" in the "compile.h" file.
    
          4.1.2 Genasm only routines
    
                The following  I/O  routine  is  required  by  the  "genasm"
             program, but not by the compiler.
    
                The function "get_char()" must  return  a  single  character
             from the input file as a 16 bit number with  a  positive  value
             between 0 and 255. A '-1' is  returned  for  the  end  of  file
             condition.
    
          4.1.3 Notes on I/O module
    
             1) It is the responsibility of the "put" routines to  translate
                the  NEWLINE  '\n'  (0x0a)  character  into  whatever   line
                termination  character(s)  are  required   by   the   target
                operating system.
    
             2) If unix "stdin"  and  "stdout"  are  not  used,  it  is  the
                responsibility  of  "main"  to  display  appropriate   error
                messages if the input or output files could not be opened.
    
                Refer to  the  sample  "io"  modules  distributed  with  the
             compiler.

    MICRO-C                                                          Page: 28


       4.2 The "code" module
    
             In order to insure that MICRO-C is portable  to  virtually  any
          environment,  the  compiler  makes  few  assumptions   about   the
          processor or system software of  the  target  system.  The  "code"
          module is  relied  on  to  produce  all  machine  instruction  and
          assembler directives written to the output file.
    
             The only two real "assumptions" made about the target processor
          are:
    
          1) It is assumed that the target processor  has  an  "accumulator"
             register in which all math operations are performed,  and  that
             the  lower  8  bits  of   this   register   may   be   accessed
             independantly.
    
          2) It is  assumed  that  the  target  processor  has  one  "index"
             register which may be loaded with a  16  bit  value,  and  that
             memory references may be made indirectly through this register.
    
             If the target processor does not support the above features, it
          may be possible to write a code generator for it using some  other
          features of the processor.
    
             For example, if an "index" register  does  not  exist,  it  may
          often be implemented using two bytes of reserved memory.
    
             The code  generation  module  required  by  the  compiler  must
          contain the following function definitions:
    
             The function "do_asm(*ptr)" is passed a pointer to a  character
          string, which it should  write  to  the  output  file  EXACTLY  as
          passed, followed by a '\n' NEWLINE  character.  This  function  is
          used by the "#asm" directive to write directly to the output file.
    
             The function "def_module()"  is  called  at  the  beginning  of
          compilation, before any other code generator functions are called.
          It is used to output any pre-amble needed by the assembler.
    
             The function "end_module()"  is  called  at  the  very  end  of
          compilation, and is the last code generator function called. It is
          used to output any post-amble needed by the assembler.
    
             The function "def_static(symbol)" is passed am index  into  the
          compiler symbol tables for a global variable, which is about to be
          initialized as static storage. The call to this function  will  be
          immediately followed by a call to "init_static" or "end_static".
    
             The "init_static(token, value,  word)"  function  is  passed  a
          token and value, with which it should initialize a single  element
          of static storage. The "word" flag will be non-zero if  the  value
          is a 16 bit element. Only the "constant" tokens  (NUMBER,  STRING,
          LABEL) need be handled by this routine.

    MICRO-C                                                          Page: 29


             The  "end_static()"  function  is  called  to   terminate   the
          definition of static storage.
    
             NOTE: "init_static"  should  not  rely  on  "def_static"  being
          called first,  since  it  is  also  called  immediately  following
          "def_label" to define "switch" tables (See "do_switch"). After the
          table  is  defined,  the  compiler  will  call  "end_static()"  to
          terminate the initialization and set up for the next.
    
             The function "def_global(symbol, size)" is called at the end of
          the compile, once for each non-static global  variable  which  was
          defined. The "size" paremeter indicates the  number  of  BYTES  of
          memory to be reserved for that variable.
    
             The function "def_extern(symbol)" is called at the end  of  the
          compile, once for each  non-resolved  external  symbol  which  was
          defined. This routine should examine the type of  the  symbol  and
          output the appriopriate assembler directives to  allow  it  to  be
          referenced in another module.
    
             The "def_func(symbol, size)"  routine  is  called  to  start  a
          function definition. The "symbol" parameter is an index  into  the
          compiler symbol tables for the function entry being  defined.  The
          "size" parameter indicates how many  bytes  of  memory  should  be
          allocated  on  the  stack  for  local  variables.  When   defining
          "register" functions, care must  be  taken  that  the  entry  code
          preserves the contents of the accumulator.
    
             The "end_func()" routine is  called  to  terminate  a  function
          definition.  It  should  remove  anything  placed  on  the   stack
          (including the local variable space allocated by "def_func"),  and
          terminate the function with a "return" instruction.
    
             The "def_label(label)" function is called whenever the compiler
          wants to generate a label in the output file. Each label generated
          by the compiler is identified by a 16 bit unsigned number.  It  is
          up to the code generator to generate a unique label  suitable  for
          the target assembler.
    
             The "def_literal(*ptr, size)" function is called at the end  of
          the  compile,  just  before  non-initialized  global  symbols  are
          generated. This routine is  given  a  pointer  to  the  compiler's
          "literal pool", which contains all the character strings  occuring
          during the compilation. The "size" parameter  indicates  how  many
          characters are in the pool. This pool must  be  generated  in  the
          output file as a string of byte constants.
    
             The "call(token, value,  type,  clean)"  function  is  used  to
          generate  a  machine  language  subroutine  call  to  the   entity
          indicated by the "token, value & type" parameters (See later). The
          "clean" parameter indicates how many entries were pushed onto  the
          stack as arguments, which should be removed following the function
          call.  Note:  Since  stack  entries  are   TWO   bytes   in   most
          implementations, the "clean" value must be multiplied  by  two  to
          get the actual number of bytes to be removed from the stack.

    MICRO-C                                                          Page: 30


             The function "jump(label,  ljmp)"  is  called  to  generate  an
          unconditional jump instruction to the indicated compiler generated
          label. The "ljmp" flag will be set to zero if the jump  references
          code within the same expression from which it  is  generated,  and
          non-zero if one or more statements may occur between the jump  and
          the destination label. This allows  the  code  generator  to  take
          advantage of "short" jumps if they are available on the target.
    
             The function "jump_if(cond, label, ljmp) is called to  generate
          a conditional jump to a compiler generated label. The "cond" value
          indicates the condition: FALSE = Jump if accumulator is zero, TRUE
          = jump if accumulator is non-zero. Remaining  parameters  are  the
          same as above.
    
             The function "do_switch(label)" is  passed  the  address  of  a
          "switch" table, which contains 16  bit  entries,  and  is  of  the
          following format:
    
                        label-1, value-1, label-2, value-2, ....
                        label-n, value-n, 0, default_label
    
             This routine should search the table for the value currently in
          the accumulator, and if found, it  should  proceed  to  the  label
          associated with that value. If the value is not found  before  the
          end of the table is encountered (identified by a  label  value  of
          zero), execution should  proceed  at  the  address  identified  by
          "default_label".
    
             The "index_ptr(token, value, type)"  routine  should  load  the
          index register with the value  of  the  entity  indicated  by  the
          "token, value & type" parameters. This will always  be  a  16  bit
          wide quantity.
    
             The "index_adr(token, value, type)"  routine  should  load  the
          index register with the 16 bit address of the  symbol  represented
          by "token, value & type".
    
             The routine "expand(type)" is called following  the  evaluation
          of expressions in "return" and "switch" statements, and is used to
          insure that the result is a 16 bit value.
    
             The routine "accop(oper, type)" is  called  to  perform  a  "no
          operand" operation on the accumulator. See "compile.h" for a  list
          of these operations. The "type" passed indicates the type of value
          expected as a result.
    
             The routine "accval(oper, rtype, token, value, type)" is called
          to perform a "one  operand"  operation  on  the  accumulator.  See
          "compile.h" for a list of these operations. "rtype" indicates  the
          type of value expected as a result. "token",  "value"  and  "type"
          indicate  the  location  and  type  of  operand  which  is   being
          processed.

    MICRO-C                                                          Page: 31


          4.2.1 Notes on code generation
    
                The meaning of the individual bits  in  the  16  bit  "type"
             value which is passed to many of the code generation  routines,
             is documented in the "compile.h" file.
    
                The meaning of "token"  is  documented  in  the  "compile.h"
             file. For  each  type  of  "token",  "value"  has  a  different
             meaning:
    
                Token           Meaning of "value"
                ----------------------------------------------------------
                NUMBER          The numeric value of the constant.
                STRING          The offset into the literal pool.
                LABEL           The value of the compiler generated label.
                SYMBOL          Index into global symbol tables.
                All others      Undefined.
    
                When token is a SYMBOL, the "value" passed is used to  index
             into the global symbol tables (contained within  the  "compile"
             module) to determine information about the variable:
    
                s_name[value]   - Name of symbol (up to SYMBOL_SIZE characters).
                s_type[value]   - Type of symbol (bits defined in "compile.h").
                s_index[value]  - Variable index:
                    Global:     Index indicates symbol was the n'th one defined.
                    Local:      Index is stack offset from def_func.
                    Argument:   Index is stack offset from last argument pushed.
    
                When calculating the stack offset for  ARGUMENTs,  you  must
             add the number of bytes placed on the stack when  the  function
             was called. This  includes  the  local  variables,  the  return
             address, and any other values that "def_func" might push.
    
                There are two popular ways of  providing  addressability  to
             local variables:
    
                If the processor has many registers, you can reserve one  as
             a "base" pointer, and point it at the top of the stack when the
             function  is  entered.  This  allows  local  variables  to   be
             referenced as negative offsets from that "base"  register,  and
             arguments to be referenced as positive offsets  from  it.  This
             approach also allows the stack to  be  restored  directly  from
             this base  register  when  the  function  terminates.  See  the
             section on assembly language interfacing.
    
                Another approach is to have the  code  generator  "remember"
             exactly how many bytes have been pushed onto  the  stack  since
             "def_func", and adjust the offsets it generates  based  on  the
             stack contents. This has  the  advantage  of  not  tying  up  a
             register.

    MICRO-C                                                          Page: 32


                If you intend to use the MICRO-C Source Linker (SLINK), then
             you have to insure that whatever variable you use to  reference
             the "literal pool" qualifies as a "compiler  generated"  label,
             allowing SLINK to adjust it when processing the  source  files.
             Compiler  generated  labels  normally  consist  of   a   single
             character (usually '?'), followed by a  decimal  number.  Since
             the compiler begins generating its labels with the  value  '1',
             you may safely use '0' as the literal pool variable (Ie: '?0').
    
                It is the responsibility of the code generator to keep track
             of the validity  of  the  upper  8  bits  of  the  accumulator.
             Appropriate sign extension or clearing of  high  bits  must  be
             performed as necessary to convert signed and unsigned character
             values when 16 bit results when required.
    
                To improve the effiency of conditional statements, the  code
             generator should keep track of the validity of the "zero"  flag
             in  the  processor's  condition  code  register,  and  generate
             appropriate  "test"  instructions  only  if  necessary  when  a
             conditional jump is compiled.
    
                For  processors  not  supporting   operations   with   stack
             contents, the "ON_STACK" and "ION_STACK" tokens may implemented
             by first popping the top of the  stack  into  a  register.  The
             "ISTACK_TOP" token is a special case, because  the  address  on
             the top of the stack must  not  be  lost.  This  token  may  be
             efficiently implemented, because "ISTACK_TOP" is only used  for
             read/write operations to  a  stacked  calculated  address.  For
             example:
    
                            array1[i] += array2[i];
    
                This statement calculates the address of "array1[i]" (in the
             index register). Since the "index" register is  again  used  in
             calculating the address of "array2[i]", the first "index"  will
             be placed on the stack. Once the contents  of  "array2[i]"  are
             retrieved, it  will  be  added  using  "ISTACK_TOP",  and  then
             re-stored using "ION_STACK".
    
                The "ISTACK_TOP" token may  thus  pop  the  address  into  a
             register, and set a flag indicating to the code generator  that
             the next "ION_STACK" token  is  to  go  through  that  register
             rather than the top of the stack. Note that since an arithmetic
             operation may be performed between the two references, you must
             not use a register which is  modified  in  code  generated  for
             arithmetic operations.
    
                Refer to the sample code  generators  distributed  with  the
             compiler.

    MICRO-C                                                          Page: 33


       4.3 The "compile" module
    
             The "compile" module  contains  the  main  statement  analyser,
          input  scanner,  expression  parser  and  symbol  table  managment
          routines for the MICRO-C compiler. This module is  common  to  all
          implementations, and should NOT require any  changes.  The  source
          code for this module is contained in the "compile.c" file on  your
          distribution diskette, and may be examined for  insight  into  the
          internal operation of the compiler.
    
             This module must be compiled and linked with your I/O and  code
          generation routines to  generate  a  complete  executable  MICRO-C
          compiler.
    
             To test your code generator,  the  file  "test.c"  is  provided
          which when compiled using the new compiler, performs a  number  of
          simple tests  to  verify  your  code  generator.  This  is  not  a
          comprehensive analysis, as  it  makes  no  assumptions  about  the
          processor, however, it provides a good indication that  your  code
          generator is on the right track.
    
             A number of fixed parameters to the  compiler  (such  as  table
          sizes etc.) are contained in the header file "compile.h". The most
          common reason for changing  these  parameters  is  to  reduce  the
          memory requirements, in order to get  MICRO-C  to  fit  into  very
          small systems.
    
             If any of the parameters in "compile.h" are to be changed,  you
          must  make  the  changes  BEFORE  compiling  any  of  the  modules
          (compile, io or codegen).
    
             The file  "tokens.h"  contains  symbolic  definitions  for  the
          tokens parsed by the  compiler,  the  text  of  which  is  in  the
          character array variable "tokens". If you make any changes to this
          token table, MAKE SURE that the contents of the "tokens"  variable
          and the "tokens.h" file agree, otherwise, you will end up  with  a
          compiler for a very strange language.

    MICRO-C                                                          Page: 34


       4.4 Porting without a compiler
    
             If you have the MICRO-C  distribution  files,  but  no  running
          compiler,  it  is  still  possible  to  port  MICRO-C,  using  the
          following steps:
    
          1) You must write the code generator and I/O routines  in  another
             language. Using assembly language is  preferable,  because  you
             can then follow the MICRO-C function calling  conventions  (See
             "Assembly Language Interface  under  "Advanced  Topics").  This
             allows you to use the same routines with the compiler later.
    
          2) The "genasm.c" program should then be re-written  in  the  same
             language as above. This should not be difficult, since it is  a
             fairly simple program.
    
          3) Link "genasm" with your code generator  and  I/O  routines,  to
             create the "genasm" utility which reads intermediate files  and
             produces assembly language output.
    
          4) The "intermediate"  file  for  the  main  "compile"  module  is
             provided in the file "compile.i". When this file  is  processed
             by "genasm", and the resultant file assembled,  you  will  have
             the "compile" module which may be  linked  with  the  "io"  and
             "code" modules to produce the final compiler.
    
       4.5 Porting without a linker
    
             It is possible to port MICRO-C using a system  which  does  not
          support a linker. To do this, you must concatinate all the  source
          files "compile.c", "code.c" and "io.c" into  one  large  file  (in
          that order), and compile them all as one program.
    
             When this is done, the ".h" include files need only be included
          once, and external definitions  of  variables  occuring  in  other
          source files should not  be  used.  The  source  programs  on  the
          distribution disk all contain conditional  compilation  statements
          (#ifndef), which only perform the necessary #include and  external
          definition statements when compiling as a single file.

    MICRO-C                                                          Page: 35


       4.6 Optimization Techniques
    
             The MICRO-C compiler performs the following machine independant
          optimizations of the output file:
    
          1) All constant expressions are evaluated  at  compile  time,  and
             expressed as a single constant value in the output code.
    
          2) Operations which are not sensitive to order (eg:  '+')  may  be
             reversed to take advantage of partial results  already  in  the
             accumulator.
    
          3) Redundant jumps as a result of "return" or  "break"  statements
             are suppressed.
    
          4) The sense of jumps in conditional statements are  reversed  for
             logically negated expressions, code for '!' is  only  generated
             if the value returned by that operator is actually used.
    
          5) Jumps between code generated within  a  single  expression  are
             flagged as "short".
    
             Although the MICRO-C compiler produces fairly  reasonable  code
          for the  processor  model  it  uses,  that  model  is  necessarily
          limited, in order that it might fit a  large  number  of  physical
          targets. There are  several  simple  optimizations  which  may  be
          performed to further enhance the code generated by the compiler in
          a specific implementation.
    
          4.6.1 Register Usage
    
                MICRO-C assumes a single accumulator,  and  a  single  index
             register.  Additional  terms  in  complicated  expressions  are
             handled by placing temporary results on  the  processor  stack,
             and re-using those registers. All data placed on the  stack  is
             accessed on a "last in - first out" basis.
    
                If the target processor has a  full  compliment  of  general
             purpose registers, an optimization may be performed  by  simply
             selecting another general purpose register as  the  accumulator
             or index register instead of placing the value  on  the  stack.
             The code generator must  keep  track  of  the  order  in  which
             registers are selected, and which register represents the "top"
             of the stack. If the number  of  values  "pushed"  exceeds  the
             number of available registers, the "oldest" register should  be
             placed on the stack, thereby allowing it to be re-used.

    MICRO-C                                                          Page: 36


          4.6.2 Jump Optimization
    
                Although MICRO-C identifies jumps to instructions which span
             more than one expression as "long",  often  the  addresses  are
             close enough together that short jumps may  actually  be  used.
             This optimization is particularily useful for  processors  such
             as the 8086, which does not support "long"  conditional  jumps,
             and therefore must simulate them with a short conditional  jump
             of the opposite sense around a long unconditional jump.
    
          4.6.3 Redundant Load Elimination
    
                Since  MICRO-C  evaluates  and  processes   each   statement
             individually, it  does  not  carry  partial  results  from  one
             statement to another.
    
                Consider the following statements:
    
                                 a = x;
                                 b = a + 1;
    
                MICRO-C generates the code:
    
                                 LOAD x
                                 STORE a
                                 LOAD a
                                 ADD 1
                                 STORE b
    
                An optimization may be performed  by  recognizing  that  the
             second "load" instruction is redundant, and can be  eliminated.
             Note: A more efficent (but less readable)  way  of  coding  the
             above statements which would result in the latter code  without
             optimization is:
    
                                 b = (a = x) + 1;

    MICRO-C                                                          Page: 37


          4.6.4 Peephole Optimization
    
                Consider the statement:
    
                                 a = *++ptr;
    
                MICRO-C generates the code:
    
                                 LOAD ptr
                                 INCREMENT
                                 STORE ptr
                                 MOVE ACCUMULATOR TO INDEX
                                 LOAD [INDEX]
                                 STORE a
    
                For a processor supporting  a  rich  set  of  direct  memory
             addressing modes, the above sequence can be shortened to:
    
                                 INCREMENT_MEMORY ptr
                                 LOAD [ptr]
                                 STORE a
    
                One of the most  successful  techniques  of  optimizing  the
             output code is also one of the simplest.  Known  as  "peephole"
             optimization, the method consists of keeping a  window  of  the
             last few instructions generated,  and  scanning  the  list  for
             known patterns every time a new instruction is added to it.
    
                As long as the instructions in the list at  least  partially
             match one or more  of  the  "predefined"  patterns,  additional
             instructions are collected  until  either  a  complete  pattern
             match occurs, or all known patterns are eliminated.
    
                If no matches occur, the "oldest" instruction is written  to
             the output file, and the next one  becomes  the  first  in  the
             "window".
    
                Whenever a pattern is discovered, it is replaced  by  a  new
             series of instructions which perform the same function, but  in
             a more efficent manner.
    
                The new instruction sequences  are  replaced  on  the  list,
             which may then be  again  scanned,  allowing  further  possible
             reductions to be discovered.
    
                Handling of labels in the "window" and  their  corresponding
             placement in the output file must be carefully done,  in  order
             to preserve the "logical" context of the original code.

    MICRO-C                                                          Page: 38


    5. THE MICRO-C PREPROCESSOR
    
          The MICRO-C Preprocessor is a source code filter,  which  provides
       greater capabilities than the preprocessor which is integral  to  the
       MICRO-C compiler. It has been implemented as a  stand  alone  utility
       program which processes the source code before it is compiled.
    
          Due to the higher complexity of  this  preprocessor,  it  operates
       slightly slower than the the integral MICRO-C preprocessor.  This  is
       mainly due to the fact that it reads each line from the file and then
       copies it to a new line while performing the macro substitution. This
       is necessary since each macro may contain parameters  which  must  be
       replaced "on the fly" when it is referenced.
    
          The integral MICRO-C preprocessor is very FAST,  because  it  does
       not copy the input line. When it encounters a '#define'd  symbol,  it
       simply adjusts the input scanner pointer to point to  the  definition
       of that symbol.
    
          Keeping the extended preprocessor as a stand alone utility  allows
       you  to  choose  between  greater   MACRO   capability   and   faster
       compilation. It also allows the system to continue  to  run  on  very
       small hardware platforms.
    
          The additional capabilities of the extended preprocessor are:
    
            - Parameterized MACROs.
    
            - Nested conditionals.
    
            - Ability to undefine MACRO symbols.
    
            - Library reference in include file names.

    MICRO-C                                                          Page: 39


       5.1 The MCP command
    
             The format of the MICRO-C Preprocessor command line is:
    
                    MCP [input_file] [output_file] [options]
    
             [input_file] is the name of  the  source  file  containing  'C'
          statements to read. If no filenames are given, MCP will read  from
          standard input.
    
             [output_file] is the name of the file to  write  the  processed
          source code to. If less than two filenames are specified, MCP will
          write to standard output.
    
          5.1.1 Command Line Options
    
                MCP accepts the following command line [options]:
    
                -c      - Instructs MCP to keep comments from  the input
                          file (except for those in '#' statements which
                          are always removed). Normally, MCP will remove
                          all comments.
    
                l=path  - Defines the directory path which will be taken
                          to reference  "library"  files when  '<>'  are
                          used around an  '#include'  file name.  Unless
                          otherwise specified, the path defaults to:
                                        '/mc'
    
                -q      - Instructs MCP to be quiet, and not display the
                          startup message when it is executed.
    
        <name>=<text>   - Pre-defines a non-parameterized macro  of  the
                          specified <name> with the string value <text>.

    MICRO-C                                                          Page: 40


       5.2 Preprocesor Commands
    
             The following commands are recognized by the MCP utility,  only
          if they occur at the beginning of the source file line:
    
          5.2.1 #define <name>(parameters) <replacement text>
    
                Defines a global macro name which will be replaced with  the
             indicated <replacement text> wherever it occurs in  the  source
             file.
    
                Macro  names  may  be  any  length,  and  may  contain   the
             characters 'a'-'z', 'A'-'Z', '0'-'9' and '_'.  Names  must  not
             begin with the characters '0'-'9'.
    
                If the macro name is IMMEDIATELY followed by a list of up to
             10 parameter names contained in brackets, those parameter names
             will be substituted with parameters passed to the macro when it
             is referenced. Parameter names follow the same rules  as  macro
             names.
    
                     eg: #define min(a, b) (a < b ? a : b)
    
                If any spaces exist between the macro name and  the  opening
             '(', the macro will not be  parameterized,  and  all  following
             text (including '(' and ')') will be  entered  into  the  macro
             definition.
    
          5.2.2 #undef <symbol>
    
                Undefines the named macro symbol. further references to this
             symbol will not be replaced.
    
                NOTE: With MCP, macro definitions operate on a STACK. IE: If
             you define a macro  symbol,  and  then  re-define  it  (without
             '#undef'ing it first), subsequently '#undef'ing it  will  cause
             it to revert to its  previous  definition.  A  second  '#undef'
             would then cause it to be completely undefined.
    
          5.2.3 #forget <symbol>
    
                Similar  to  '#undef',  except  that  the  symbol  and   ALL
             SUBSEQUENTLY DEFINED SYMBOLS will be undefined.
    
                Useful for releasing any local symbols (used only  within  a
             single include file).
    
                For example:
    
                        #define GLOBAL "xxx"    /* first global symbol */
                            ...                 /* more globals */
                        #define LOCAL   "xxx"   /* first local symbol */
                            ...                 /* more locals */
                        /* body of include file goes here */
                        #forget LOCAL           /* release locals */

    MICRO-C                                                          Page: 41


          5.2.4 #ifdef <symbol>
    
                Causes the following lines (up to '#else' of '#endif') to be
             processed and included in the source file  only  if  the  named
             symbol is defined as a macro.
    
          5.2.5 #ifndef <symbol>
    
                Causes the following lines (up to '#else' of '#endif') to be
             processed and included in the source file  only  if  the  named
             symbol is NOT defined as a macro.
    
                NOTE: '#ifdef/#ifndef#else/#endif' may be nested.
    
          5.2.6 #else
    
                Toggles the state of the "if_flag", controlling  conditional
             processing. Only has effect in the highest level  of  suspended
             processing. IE: Nested conditionals will work properly.
    
                If the previous  '#ifdef/#ifndef'  failed,  processing  will
             begin again following the '#else'.
    
                If the previous '#ifdef/#ifndef' passed, processing will  be
             suspended until the '#endif' is encountered.
    
                NOTE: Since '#else' acts as a toggle, it may be used outside
             of any '#ifdef/#ifndef' to unconditionally  suspend  processing
             up to '#endif'.
    
          5.2.7 #endif
    
                Resets  the  "if_flag"  controlling  conditionals,   causing
             processing to resume. Only has effect in the highest  level  of
             suspended  processing.  IE:  Nested  conditionals   will   work
             properly.

    MICRO-C                                                          Page: 42


          5.2.8 #include <filename>
    
                Causes MCP to open the named file and include  its  contents
             as part of the input source.
    
                If the filename is contained within '"' characters, it  will
             be opened exactly as  specified,  and  (unless  it  contains  a
             directory path) will reference a file in the current directory.
    
                If the filename is contained within the characters  '<'  and
             '>', it will be  prefixed  with  the  library  path  (See  'l='
             option), and will therefore reference a file  in  that  library
             directory. The default  library  directory  is  assumed  to  be
             '/mc'.
    
                For example:
    
                        #include "header.h"     /* from current directory */
                        #include <stdio.h>      /* from library directory */
    
          5.2.9 #asm / #endasm
    
                The  '#asm'  and  '#endasm'  statements  are  not   actually
             recognized by MCP. They are passed through unchanged,  allowing
             them to be recognized and acted upon by  the  integral  MICRO-C
             preprocessor.

    MICRO-C                                                          Page: 43


       5.3 Error messages
    
             When MCP detects an error during processing of an include file,
          it displays an error message,  which  is  preceeded  by  the  line
          numbers of the files in which the error occurs. If  more  than  10
          errors are encountered, MCP will terminate.
    
             The following error messages are reported by MCP:
    
          5.3.1 Cannot open include file
    
                A '#include' statement on the  indicated  line  specified  a
             file which could not be opened for reading.
    
          5.3.2 Invalid include file name
    
                A '#include' statement on the  indicated  line  specified  a
             file  name  which  was  not  contained  within  '"'   or   '<>'
             characters.
    
          5.3.3 Invalid macro name
    
                A '#define' statement on the indicated line contains a macro
             name which does not follow the name rules.
    
          5.3.4 Invalid macro parameter
    
                A '#define' statement on the indicated line contains a macro
             parameter name which does not follow the name rules.
    
                A reference to a macro does not have a proper ')'  character
             to terminate the parameter list.
    
          5.3.5 Too many errors
    
                More  than  10  errors  has  been  encountered  and  MCP  is
             terminating.
    
          5.3.6 Too many macro definitions
    
                MCP has encountered more '#define' statements  than  it  can
             handle.
    
          5.3.7 Too many macro parameters
    
                A '#define' statement on the indicated line  specifies  more
             parameters to the macro than MCP can handle.
    
          5.3.8 Too many include files
    
                MCP has encountered more nested '#include'  statements  than
             it can handle.

    MICRO-C                                                          Page: 44


          5.3.9 Undefined macro
    
                A '#undef' or '#forget'  statement  on  the  indicated  line
             references a macro name which has not been defined.
    
          5.3.10 Unterminated comment
    
                The END OF FILE has  been  encountered  while  processing  a
             comment.
    
          5.3.11 Unterminated string
    
                A quoted string on the indicated line has no end.

    MICRO-C                                                          Page: 45


    6. THE MICRO-C OPTIMIZER
    
          The MICRO-C optimizer is an output code filter which examines  the
       assembly code produced by the compiler, recognizing known patterns of
       inefficent code (using the "peephole" technique), and  replaces  them
       with more optimal code  which  performs  the  same  function.  It  is
       entirely table driven, allowing it to be modified for  virtually  any
       processor.
    
          Due its many table lookup operations, the  optimizer  may  perform
       quite slowly when processing a large  file.  For  this  reason,  most
       people prefer not to optimize during the debugging of a program,  and
       utilize the optimizer only when creating the final copy.
    
       6.1 The MCO command
    
             The format of the MICRO-C Optimizer command line is:
    
                    MCO [input_file] [output_file] [options]
    
             [input_file] is the name of the source file containing assembly
          statements to read. If no filenames are given, MCO will read  from
          standard input.
    
             [output_file] is the name of the file to  which  the  optimized
          assembly code is to be written. If less  than  two  filenames  are
          specified, MCO will write to standard output.
    
          6.1.1 Command Line Options
    
                MCO accepts the following command line [options]:
    
                -d      - Instructs MCO to produce a  'debug' display on
                          standard output showing the source code  which
                          it is removing and replacing in the input file.
                          NOTE: If you do not specify an explict  output
                                file, you will get the debug  statements
                                intermixed with the  optimized  code  on
                                standard output.
    
                -q      - Instructs MCO to be quiet, and not display the
                          startup message when it is executed.

    MICRO-C                                                          Page: 46


       6.2 Porting to a new processor
    
             The MICRO-C Optimizer is completely table driven, and should be
          fairly easy to port to a new processor.
    
             The peephole optimization table  is  called  'peep_table',  and
          consists of two  sequential  character  string  entries  for  each
          optimization.
    
             The first is the "take" entry, and  represents  an  instruction
          sequence which (if found) is to be removed from the  output  file.
          The second  is  the  "give"  entry,  and  defines  a  sequence  of
          instructions to be placed in the output file at that  point.  NOTE
          that due to the way the optimizer removes and replaces instruction
          in the circular "peephole" buffer, the instructions in the  "give"
          entry ARE CODED IN REVERSE ORDER.
    
             Characters in the "take" entry  with  the  high  bit  set  (eg:
          '\200','\201') are special characters which represent any variable
          string which may occur in the instruction sequence,  and  will  be
          replaced with the same string wherever that  character  occurs  in
          the "give" entry. If  the  same  special  character  (eg:  '\200')
          occurs more than once  in  the  "take"  entry,  the  corresponding
          strings must be exactly the same or else the entire sequence  will
          not be matched.
    
             The processor will stop scanning  a  variable  string  when  it
          encounters the character which  immediately  follows  the  special
          character in the "take" entry, or at the end of the input line.
    
             The  manifest  SYMBOLS  defines  how  many  different   special
          characters are allowed in a peephole entry. You must not  use  any
          special characters which have  a  value  greater  than  ('\200'  +
          SYMBOLS - 1).

    MICRO-C                                                          Page: 47


    7. THE COMMAND CO-ORDINATOR
    
          'CC' is a program which co-ordinates the other commands (MCP, MCC,
       MCO, ASM and LINK),  to  provide  a  simple  "one  step"  compilation
       command.
    
       7.1 The CC command
    
             The format of the Command Co-ordinator command line is:
    
                              CC <name> [options]
    
          7.1.1 Command line options
    
                -a      - produce ASSEMBLER (.ASM) output file
                -l      - produce LINKABLE  (.OBJ) output file
                -o      - OPTIMIZE the output file (using MCO)
                -p      - use the extended PRE-PROCESSOR (MCP)
                -q      - QUIET mode (suppress informational messages)
                -s      - produce SMALL-MODEL (.EXE) output file
                m=mcdir - specify MICRO-C home directory
                t=mctmp - specify prefix for TEMPORARY files
    
                When executing the sub-commands, CC will search the  MICRO-C
             home directory, as well as any  directories  specified  in  the
             'PATH' environment variable. Libraries are  accessed  from  the
             MICRO-C home directory only.
    
                The environment variable 'MCDIR' is  examined  to  determine
             the path to  the  MICRO-C  home  directory.  If  MCDIR  is  not
             defined, CC will assume the string '\MC'. You may override this
             directory by using the 'm=' option on the command line.
    
                Intermediate  results  from  each  command  are  stored   in
             "temporary" files, which are fed as input to the next  command.
             Temporary files will be deleted once they are no longer needed,
             except in the case where a command fails.  When  this  happens,
             any temporary file which  was  being  used  as  input  to  that
             command will not be deleted, allowing you to examine it for the
             cause of the error.
    
                The environment variable 'MCTMP' is examined to determine  a
             prefix to prepend to temporary file  names.  If  MCTMP  is  not
             defined, CC assumes the default prefix of '$'. You may override
             this prefix by using the 't=' option on the command line.
    
                Here are example 'SET' commands suitable  for  inclusion  in
             the AUTOEXEC.BAT file, of an IBM/PC based MICRO-C system  which
             has the home directory in 'C:\MC', and a RAMDISK as drive 'D':
    
                    SET MCDIR=C:\MC
                    SET MCTMP=D:\$

    MICRO-C                                                          Page: 48


                The '-p' option causes the extended pre-processor  (MCP)  to
             be used. This provides greater pre-processor capability, at the
             expense of longer compile time.
    
                NOTE: If any compiler errors occur when using  this  option,
             the line numbers contained in the error messages will refer  to
             the temporary file containing the output from the pre-processor
             ($<name>.CP). You must examine this file in order to  determine
             the actual cause of the error.
    
                The '-o' option causes the optimizer (MCO) to be used, which
             results in more efficent code, at the expense of longer compile
             time.
    
                The '-a' option  causes  CC  to  bypass  the  assembler  and
             linker, and produce an assembly source file (<name>.ASM) as the
             output file.
    
                The '-l' option causes CC to  bypass  the  link  stage,  and
             produce a linkable object module  (<name>.OBJ)  as  the  output
             file.
    
                The '-s' option causes CC to  link  the  program  using  the
             SMALL  memory  model,   and   produce   an   executable   image
             (<name>.EXE) as the output file. This option  applies  only  to
             those  processors  which  have  a  segmented  architecture  and
             multiple memory models such as the 8086.
    
                If none of '-a', '-l' or '-s' is specified, CC will link the
             program using the TINY memory  model,  and  produce  a  command
             image (<name>.COM) as the output file.
    
       7.2 Using multiple object modules
    
             The 'LC' command file takes one or more object modules produced
          by 'CC' with the '-l' option, and links them with the libraries to
          produce an executable module. This module will be given  the  name
          of the first file specified in the argument list.
    
             When compiling large programs which have more than  one  source
          file, you must first compile all modules using 'CC' with the  '-l'
          option, and the use 'LC' to link the resultant object  files  into
          the final executable program.
    
             The '-s' option may be used as the FIRST argument, to cause  LC
          to link in the SMALL model (8086 only).
                eg: CC FIRST -l
                    CC SECOND -l
                    LC FIRST SECOND         <-- TINY  Model
                    LC -s FIRST SECOND      <-- SMALL Model
    
             The exact syntax and options available for 'CC'  and  'LC'  may
          differ in different  implementations  of  the  compiler.  See  the
          'READ.ME' file on your distribution disk for details.

    MICRO-C                                                          Page: 49


    8. THE MAKE UTILITY
    
          The MAKE utility provides a method of automating the  building  of
       larger programs consisting of more that one object module.  The  main
       benefit of MAKE is that it keeps track of the files that each  module
       is dependant on, and will rebuild a module if any of those files have
       been modified since  the  module  was  last  built.  This  frees  the
       programmer from  the  task  of  remembering  which  files  have  been
       changed, and the commands needed to rebuild the dependant modules.
    
       8.1 MAKEfiles
    
             To use MAKE, you must first create a MAKEFILE, which is a  text
          file containing entries for each module in the program. Each entry
          consists of a DEPENDANCY list, and a series of COMMANDS.
    
          8.1.1 MAKEfile Entries
    
                A dependency list in MAKE is a line which contains the  name
             of the module, followed by a ':', followed by the names of  any
             files on which it depends. The module name MUST begin in column
             1.
    
                When MAKE is invoked, it will process each dependancy  list,
             and  will  execute  any  following  commands  (up  to   another
             dependancy list) if (1) the module does not exist,  or  (2)  if
             any of the files to the right of the ':' have a timestamp which
             is later than that of the module. For example:
    
                main.obj : main.c main.h \\mc\\stdio.h
                    \\mc\\mcc main.c main.asm
                    masm/ml main;
                    -del main.asm
    
                In the above example, the  'main.obj'would  be  rebuilt  (by
             compiling and assembling 'main.c') if either it did not already
             exist, or any of 'main.c', 'main.h' or '\mc\stdio.h' was  found
             to have a later timestamp.
    
                The '-' preceeding the 'del' command prevents it from  being
             displayed. Unless the '-q' option is enabled, MAKE will display
             any commands not preceeded by '-' as they are executed.
    
                NOTE: To enter a single '\' in the MAKEFILE,  you  must  use
             '\\', this is because like 'C',  MAKE  uses  '\'  to  "protect"
             special  characters  which  otherwise  are  used  for   special
             functions (such as '\', '$' and '#'). The first '\'  "protects"
             the second one, allowing it to pass through as source text.

    MICRO-C                                                          Page: 50


          8.1.2 Macro Substitutions
    
                Sometimes in a MAKEFILE, you have a single file or directory
             path that you use  over  and  over  again.  If  it  is  a  long
             directory path, this may  involve  a  lot  of  typing,  and  it
             becomes inconvenient to change that name (if you want to use  a
             different directory etc.) because it is repeated many times.
    
                MAKE includes a MACRO facility, which allows you  to  define
             variable names which will be replaced with a text  string  when
             used in subsequent MAKEfile lines. Names are defined by placing
             them in the MAKEfile, followed by '=',  and  the  text  string.
             Macro names being defined MUST begin in  column  one,  and  may
             consist of the characters ('a'-'z', 'A'-'Z', '0'-'9', and '_').
    
                Whenever MAKE encounters a '$' in the  file,  it  takes  the
             name immediately following, and performs the macro replacement:
    
                mcdir = \\mc
                main.obj : main.c main.h $mcdir\\stdio.h
                    $mcdir\\mcc main.c main.asm
                    masm/ml main;
                    del main.asm
    
    
                When a macro name is immediately  followed  by  alphanumeric
             text, use a single '\' to  separate  it  from  the  text.  This
             "protects"  the  first  character  of  the  text   from   being
             interpreted as part of the macro name:
    
                mcdir = \\mc\\
                main.obj : main.c main.h $mcdir\stdio.h
                    $mcdir\mcc main.c main.asm
                    masm/ml main;
                    del main.asm
    
                There  are  several  predefined  macro  symbols  which   are
             available:
    
    
                $*      = The full name of the dependant module (name.type).
                $@      = The name only of the dependany module.
                $.      = The full name of each file in the dependancy list,
                          separated from each other by a single space.
                $,      = The full name of each file in the dependancy list,
                          separated from each other by a single comma.
                $:      = The name only of each file in the dependancy list,
                          separated from each other by a single space.
                $;      = The name only of each file in the dependancy list,
                          separated from each other by a single comma.

    MICRO-C                                                          Page: 51


                File names in the dependancy list which are preceeded by '-'
             will not be included in the '$. $, $: $;' macro expansions:
    
                mcdir = \\mc
                main.obj : main.c -main.h -$mcdir\\stdio.h
                    $mcdir\\mcc $. $@.ASM
                    masm/ml $@;
                    del $@.ASM
    
          8.1.3 MAKEfile Comments
    
                Whenever MAKE encounters the '#' character in the  MAKEFILE,
             it treats the remainder of the line as a comment, and does  not
             process it:
    
                # Define Directories
                mcdir = \\mc
    
                # Build the MAIN module
                main.obj : main.c -main.h -$mcdir\\stdio.h  # Dependants
                    $mcdir\\mcc $. $@.ASM                   # Compile
                    masm/ml $@;                             # Assemble
                    del $@.ASM                              # Delete tmp
    
          8.1.4 Ordering the MAKEfile
    
                MAKE processes the MAKEfile is sequential fashion, with  the
             entries near the top being processed before  the  entries  near
             the bottom. To insure that each module is built  properly,  any
             files appearing in the dependancy list for a module  which  are
             themselves dependant  on  other  files,  should  have  MAKEfile
             entries which occur BEFORE the entries for  the  modules  which
             are dependant on them:
    
                # Define Directories
                mcdir = \\mc
                # Build the MAIN module
                main.obj : main.c -main.h -$mcdir\\stdio.h
                    $mcdir\\mcc $. $@.ASM
                    masm/ml $@;
                    del $@.ASM
                # Build the SUB module
                sub.obj : sub.c -sub.h
                    $mcdir\\mcc $. $@.ASM
                    masm/ml $@;
                    del $@.ASM
                # Bind the executable file
                # NOTE: If either of the above modules is rebuilt,
                #       this entry will be guarenteed to execute.
                main.exe : main.obj sub.obj
                    LINK $:;

    MICRO-C                                                          Page: 52


       8.2 Directives
    
             Like 'C', MAKE recognizes several "directives" in the MAKEfile.
          These  directives  are  only  recognized  if  they  occur  at  the
          beginning of the input line:
    
          8.2.1 @include <filename>
    
                This command causes the indicated file to be opened and read
             in as the source  text.  When  the  end  of  the  new  file  is
             encountered, processing will continue with the  line  following
             "@include" in the original MAKEfile.
    
          8.2.2 @ifdef <name>
    
                Processes the following lines (up to @else of  @endif)  only
             if the given MACRO name is defined. NOTE: <name> should not  be
             preceeded by '$', otherwise its CONTENTS will be tested.
    
          8.2.3 @ifndef <name>
    
                Processes the following lines (up to @else of  @endif)  only
             if the given MACRO name is NOT defined.
    
          8.2.4 @ifeq <word1> <word2>
    
                Processes the following lines (up to @else of  @endif)  only
             if the following two words match exactly. This  is  useful  for
             testing the value of a defined MACRO symbol.
    
          8.2.5 @ifne <word1> <word2>
    
                Processes the following lines (up to @else or  @endif)  only
             if the following two words do not match.
    
          8.2.6 @else
    
                Processes the following lines (up to  @endif)  only  if  the
             preceeding @ifdef, @ifndef, @ifeq or @ifne was false.
    
          8.2.7 @endif
    
                Terminates @ifdef, @ifndef, @ifeq and @ifne.
    
          8.2.8 @type <text>
    
                Displays the following text.
    
          8.2.9 @abort [text]
    
                Terminates MAKE with an 'Aborted!' message. Any text on  the
             remainder of the line will be appended to the message.

    MICRO-C                                                          Page: 53


       8.3 The MAKE command
    
             The format of the MAKE command line is:
    
                           MAKE [makefile] [options]
    
             [makefile] is the name of the MAKEfile to process. If  no  name
          is given, MAKE assumes the default name 'MAKEFILE'.
    
          8.3.1 Command Line Options
    
                MAKE accepts the following command line [options]:
    
                -d      - Instructs MAKE to operate in "debug" mode, and
                          display the commands which it  would  execute,
                          without actually executing them. This provides
                          a method of quickly testing the MAKEFILE.
    
                -q      - Instructs MAKE to be quiet, and not display the
                          informational messages and commands executed as
                          it progresses.
    
        <name>=<text>   - Pre-defines a macro  of  the  specified  <name>
                          with the string value  <text>.  This  OVERRIDES
                          any definition within the MAKEfile,  which  may
                          be used to establish a "default" value.

    MICRO-C                                                          Page: 54


       8.4 The TOUCH command
    
             TOUCH is a small utility program which sets  the  timestamp  of
          one or more files to the current or  specified  time/date.  It  is
          useful as a  method  of  forcing  MAKE  to  recognize  a  file  as
          "changed", even when it has not.
    
             For example, if  you  had  decided  to  "undo"  several  recent
          changes by restoring a backup of "main.c", the restored file  will
          probably have a timestamp which is  older  than  the  last  module
          which was built. In this case, MAKE would be unaware that the file
          has changed, and would therefore not rebuild the module.
    
             The TOUCH command could then be used to "update" the  timestamp
          of 'main.c' to the current time, causing MAKE to recognize it as a
          changed file.
    
                                  TOUCH main.c
    
             You could also use TOUCH to force rebuilding of several files:
    
                           TOUCH main.c sub1.c sub2.c
    
             Or even ALL '.C' files:
    
                                   TOUCH *.c
    
             TOUCH can also be used to set the timestamp of  a  file  to  an
          arbritrary value, this may be useful  to  PREVENT  a  change  from
          causing an update:
    
                         TOUCH main.c t=0:00 d=31/10/80
    
             NOTE: Use of the 't=' or 'd=' parameters to  TOUCH  allows  the
          possibility that a changed file  will  go  unnoticed.  CAUTION  is
          advised.

    MICRO-C                                                          Page: 55


    9. THE SOURCE LINKER
    
          Many small development environments have assemblers which  do  not
       directly support an object linker. This causes  a  problem  with  'C'
       development, because the library functions must be  included  in  the
       source code, with several drawbacks:
    
        1)  There is no way to tell which library functions to include,
            therefore, you must to it manually.
    
        2)  'C' library functions must be  re-compiled every  time,  in
            order to avoid conflict between compiler generated labels.
    
        3)  Assembly language library functions must be modified to
            include the "#asm" and "#endasm" directives.
    
          The MICRO-C Source Linker (SLINK) helps overcome  these  problems,
       by automatically  joining  previously  compiled  (assembly  language)
       source code from the library to your programs compiler  output.  Only
       those files containing  functions  which  you  reference  are  joined
       (Taking into consideration of course  any  functions  called  by  the
       included library functions etc...). As the files are joined, compiler
       generated labels are automatically adjusted to be unique within  each
       file.
    
       9.1 The SLINK Command
    
             The format of the SLINK command line is:
    
                   SLINK [input_file] [output_file] [options]
    
             [input_file] is the name of  the  source  file  containing  the
          compiler output from your program. If no filenames is given, SLINK
          will read from standard input.
    
             [output_file] is the name of  the  file  to  write  the  linked
          source code to. If less that two filenames are given,  SLINK  will
          write to standard output.
    
          9.1.1 Command line options
    
                SLINK accepts the following command line [options]:
    
                g=char  - Informs SLINK of the lead-in character for
                          compiler generated symbols.  This defaults
                          to '?' unless otherwise specified.
    
                -l      - Instructs SLINK to list each  library  file
                          being included in your program.
    
                l=path  - Identifies the directory path which will be
                          taken to reference "library" files. If this
                          path is not specified, it defaults to:
                                        '/mc/slib'
    
                -q      - Instructs SLINK to be quiet, and not display
                          the startup message when it is executed.

    MICRO-C                                                          Page: 56


       9.2 The External Index File
    
             SLINK uses a special file from the library to  determine  which
          sysmbols are in which files. This files  is  called  the  EXTERNAL
          INDEX FILE, and is  found  in  the  library  directory  (see  'l='
          option), under the name "EXTINDEX.LIB".
    
             This  file  contains  entries  which  cross-reference  external
          symbols to files. Each entry is as follows:
    
            1)  Any lines beginning with '+' contain the names of files
                which are to be processed and included at the beginning
                of the program (Before your source file). This the best
                way to include the startup code and any runtime library
                routines which are required at all times. The files are
                included in the order in which they appear in the index
                file.
                    eg: +6809rl.asm
    
            2)  Any lines beginning with '-' contain the names of files
                which are to  be  included  if  any  of  the  following
                symbols (Up to another '+' or '-') are referenced.
                    eg: -printf.asm format.asm fput.asm
    
                NOTE: In most cases, the library functions will contain
                indications of any external references that they do, in
                which case SLINK will automatically include those files
                even of the names are not mentioned on the '-' line. In
                the example above, the following would suffice:
                        -printf.asm
    
            3)  The names  of  each  symbol  which  may  be  referenced
                externally must follow the '+'  or  '-' entry.  Symbols
                must occur one per line, with no  leading  or  trailing
                spaces.
                    eg: printf
                        fprintf
                        sprintf
    
            4)  A line beginning with '$' is used to define the pseudo-
                opcode used by SLINK to reserve uninitialized  data  at
                the end of the output file. One one line beginning with
                '$' should be entered into the EXTINDEX.LIB  file.  The
                remainder of this line, including all  spaces  etc.  is
                entered between each symbol name, and the decimal  size
                (in bytes) which is written to the output file.
                    eg: '$ RMB '    <- Quotes are for clarity

    MICRO-C                                                          Page: 57


            A complete example:
    
                    +6809rl.asm
                    -printf.asm
                    printf
                    fprintf
                    sprintf
                    -scanf.asm
                    scanf
                    fscanf
                    sscanf
                    $ RMB
    
       9.3 Multiple source files
    
             SLINK processes only one source  file,  and  resolves  external
          references only to the library files. This is because  the  public
          symbol information is available in the EXTINDEX.LIB  files,  which
          contains no entries for the user supplied programs.
    
             If you wish to use source code  linking  for  a  program  which
          contains multiple source files, use "#include" statements  at  the
          end if your main program to include all of the other parts into  a
          single source file.
    
       9.4 Source file information
    
          9.4.1 Special Comments
    
                SLINK  identifies  external  symbol  references  by  special
             comments in the input source file. These comments must begin in
             column one, and are of the form:
    
                                 *EXT*<symbol>
    
             where <symbol> is the name  of  the  symbol  being  referenced.
             These  comments  are  placed  into  the  source  file  by   the
             "def_extern" routine in the MICRO-C code generator.

    MICRO-C                                                          Page: 58


                SLINK also identifies uninitialized  data  area  by  special
             comments placed in the input source  file.  The  comments  must
             begin in column one, and are of the form:
    
                              *DAT*<symbol> <size>
    
             where <symbol> is the name of the symbol used to reference  the
             data area, and <size> is the number of bytes  to  be  reserved.
             SLINK will output statements to allocate the data area  at  the
             very end of the assembly language output  file.  This  prevents
             the uninitialized data from occupying space within  the  bounds
             of executable code generated, and thus allows it to be excluded
             from the image when it is saved to  disk.  These  comments  are
             placed into the source file by the "def_global" routine in  the
             MICRO-C code generator.
    
                The reserved data area are  allocated  at  the  end  of  the
             output file, in the REVERSE order of which they are encountered
             in the input files. This insures that the FIRST "*DAT*" comment
             found the LAST symbol name output. This allows you to  place  a
             "*DAT*" comment at the beginning of the startup file,  and  use
             it to allocate heap space at the end of all other data.
    
                If you  are  writing  assembly  language  programs  for  the
             library, be  sure  include  "*EXT*<symbol>"  comments  for  any
             symbols which  you  externally  reference,  and  "*DAT*<symbol>
             <size>" comments for any uninitialized data area you  may  wish
             to allocate. If you wish to place an assembly language  comment
             on the same line, make sure it is separated from the  remainder
             of the special comment line  by  at  least  one  space  or  tab
             character.
    
                Note that since SLINK removes these "special" comments  from
             the output file, they do not have to be in a form acceptable to
             the assembler. Ie: if your assembler uses ';' for comments, you
             don't not have to change the code generator  and  SLINK,  since
             the assembler will not see the special comments it generates.
    
          9.4.2 Compiler generated labels
    
                As it processes each source file, SLINK scans each line  for
             symbols which consist of the '?' character (See  'g='  option),
             followed by a number. If it finds such as symbol, it inserts  a
             two character sequence ranging from 'AA' to  'ZZ'  between  the
             '?', and the number. This sequence will be incremented for each
             source file processed,  and  thus  insures  that  the  compiler
             generated symbols will be unique for each file.
    
                If you  are  writing  assembly  language  programs  for  the
             library, you must be careful to  avoid  using  identical  local
             symbols in any of the library files, one way to do this  is  to
             use symbols which meet the above criteria.

    MICRO-C                                                          Page: 59


       9.5 The SINDEX utility
    
             SINDEX is a utility  which  assists  in  the  creation  of  the
          EXTINDEX.LIB file used by SLINK. When you run SINDEX, it  examines
          all of the '.ASM' files in the current  directory,  and  writes  a
          EXTINDEX.LIB file which contains a '-' type entry for  each  file,
          and  external  symbol  entries  for  any  labels  which  it  finds
          conforming to the 'C' naming conventions (Starts with 'a-z', 'A-Z'
          or '_', and contains only 'a-z', 'A-Z', '0-9' or '_').
    
             Once  you  have  run  SINDEX,  you  must  manually   edit   the
          EXTINDEX.LIB file, and remove any file or symbol entries which you
          do not wish to have available as external references, as  well  as
          change any necessary entries to the '+' type.
    
             NOTE: There is no information recorded in the  assembly  source
          file which indicates that a symbol was  declared  as  "static"  in
          'C'. For this reason, you must manually remove any  symbols  which
          you do not want to be accessable as external references,  EVEN  IF
          THEY WERE ORIGINALLY DECLARED AS "static" IN 'C'.
    
             You may instruct SINDEX to search for a file pattern other than
          '*.ASM' by passing it as a command line parameter.
    
                                eg: SINDEX *.A86

    MICRO-C                                                          Page: 60


    10. LIBRARY FUNCTIONS
    
          The MICRO-C distribution disk includes the 'C'  and  'ASM'  source
       code for a number of useful "library" functions. These  routines  may
       be also be used as "example" programs, providing insight into MICRO-C
       programming techniques.
    
          All functions except for the lowest level I/O routines  are  coded
       in 'C', and should compile on any MICRO-C system. Note that some  low
       level functions in the library are written in 'C' using  still  lower
       level routines. Although this makes the library highly  portable  and
       reduces the number of routines you have to re-write  for  a  specific
       system, the resultant function will be less efficent than  one  which
       directly uses the operating system services.
    
          If you are implementing MICRO-C an a small system  and  intend  to
       use it for serious programming, I strongly recommend that you re-code
       all of the low level library functions in assembly language.
    
          Note that since library routines are often used,  in  applications
       where code size and execution speed are of primary importance, it may
       be desirable to recode some or all of the other library  routines  in
       assembly language as well.
    
          For those who intend to make only casual use of  MICRO-C,  or  who
       wish to experiment with it simply for the  learning  experience,  the
       'C' versions of the low level library functions should be  more  than
       sufficient.
    
       10.1 Standard Library Functions
    
             These routines are currently available in the  MICRO-C  library
          as  "standard"  functions  which  should  be  available   in   all
          implementations.
    
             The exact syntax and capabilities of the  system  or  processor
          dependant functions may vary  in  different  implementations,  see
          your  implementation  notes  (READ.ME)  for   details.   Different
          possible forms of such functions are shown using (1), (2), ...

    ABORT                                                             ABORT
    
    
    
    PROTOTYPE:
    
        abort(char *message)
    
    
    ARGUMENTS:
    
        message - Pointer to message to display
    
    
    RETURN VALUE:
    
        N/A - Function never returns
    
    
    DESCRIPTION:
    
          This function writes the string passed as an argument to  standard
       error, and then terminates the program with a  return  code  of  '-1'
       (Indicating general  failure).  This  provides  a  simple  method  of
       terminating a program on an error condition with a message explaining
       why.
    
    
    EXAMPLES:
    
        abort("Invalid operand\n");

    ABS                                                                 ABS
    
    
    
    PROTOTYPE:
    
        int abs(int number)
    
    
    ARGUMENTS:
    
        number  - Any integer value
    
    
    RETURN VALUE:
    
        The absolute value of "number"
    
    
    DESCRIPTION:
    
          The "abs" function returns the absolute value of the argument.  If
       "number" is a positive value, it is returned unchanged. If  negative,
       the negate of that value is returned (giving a positive result).
    
    
    EXAMPLES:
    
        difference = abs(value1 - value2);

    ATOI                                                               ATOI
    
    
    
    PROTOTYPE:
    
        int atoi(char *string)
    
    
    ARGUMENTS:
    
        string  - Pointer to a string containing a decimal number
    
    
    RETURN VALUE:
    
        16 bit integer value
    
    
    DESCRIPTION:
    
          The "atoi" function converts an ASCII string containing  a  signed
       decimal number (-32768 to 32767) to a 16 bit value which is returned.
       An unsigned number of the range (0 to 65535) may also  be  used,  and
       the result if assigned to an "unsigned" variable will be correct.
    
    
    EXAMPLES:
    
        value = atoi("1234");
        value = atoi("-1");

    CD                                                                   CD
    
    
    
    PROTOTYPE:
    
        int cd(char *pathname)
    
    
    ARGUMENTS:
    
        pathname- Name of directory to make current
    
    
    RETURN VALUE:
    
        0 if successful, otherwise an operating system error code
    
    
    DESCRIPTION:
    
          This function sets the "current" directory, causing all subsequent
       file references which do not explicitly indicate a directory path  to
       access the path specified by "pathname".
    
    
    EXAMPLES:
    
        cd("/mc/c_source");     /* UNIX */
        cd("\\mc\\l_source");   /* MS-DOS */

    CONCAT                                                           CONCAT
    
    
    
    PROTOTYPE:
    
        register concat(char *dest, char *source, ...)
    
    
    ARGUMENTS:
    
        dest    - Pointer to destination string
        source  - Pointer to source string
        ...     - Additional sources may be given
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          The "concat" function concatinates the given source  strings  into
       one destination string. The destination string must be  large  enough
       to hold all of the source strings plus the string  terminator  (zero)
       byte. No value is returned.
    
          NOTE: This function uses a variable number of arguments, and  must
       be declared as "register" (See "stdio.h").
    
    
    EXAMPLES:
    
        concat(filename,"/tmp/", input_name);

    CREATE                                                           CREATE
    
    
    
    PROTOTYPE:
    
        int create(char *pathname, int attrs)
    
    
    
    ARGUMENTS:
    
        pathname- Name of file to create
        attrs   - Attributes for new file
    
    
    RETURN VALUE:
    
        0 if successful, otherwise an operating system error code
    
    
    DESCRIPTION:
    
          The "create" function creates a new file with the specified system
       attributes.
    
          The meaning of the individual bits in the "attrs" value is  system
       dependant, and is defined in the "file.h" header file.
    
    
    EXAMPLES:
    
        create("temp", HIDDEN);

    DELETE                                                           DELETE
    
    
    
    PROTOTYPE:
    
        int delete(char *pathname)
    
    
    
    ARGUMENTS:
    
        pathname- Name of file to delete
    
    
    RETURN VALUE:
    
        0 if successful, otherwise an operating system error code
    
    
    DESCRIPTION:
    
          The "delete" function removes an existing file from the disk.  Any
       disk space occupied by the file is released.
    
    
    EXAMPLES:
    
        delete("temp");

    EXIT                                                               EXIT
    
    
    
    PROTOTYPE:
    
        exit(int rc);
    
    
    ARGUMENTS:
    
        rc      - Termination return code
    
    
    RETURN VALUE:
    
        N/A - Function never returns
    
    
    DESCRIPTION:
    
          This function terminates the execution of the program and passes a
       specific return code back to the  operating  system.  A  return  code
       value of zero is used  to  indicate  successful  program  completion.
       Non-zero return code values may be used to indicate a particular type
       of failure. A value of '-1' is often used to indicate a  non-specific
       failure. Note that  the  "rc"  value  is  very  system  specific,  in
       particular, some systems support only 8 bit return codes,  so  values
       which are greater than 255 should be avoided.
    
    
    EXAMPLES:
    
        exit(0);        /* success */
        exit(-1);       /* failure */

    FCLOSE                                                           FCLOSE
    
    
    
    PROTOTYPE:
    
        fclose(FILE *fp);
    
    
    ARGUMENTS:
    
        fp      - File pointer to an open file
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          This function closes a file  which  was  previously  opened  using
       "fopen". The I/O buffer space used by the file is  released.  In  the
       case of a file open for write ('w'), the last disk buffer is  flushed
       and written to disk.
    
    
    EXAMPLES:
    
        fclose(fp);

    FGET                                                               FGET
    
    
    
    PROTOTYPE:
    
        int fget(char *buffer, int size, FILE *fp)
    
    
    ARGUMENTS:
    
        buffer  - Pointer to buffer to receive data
        size    - Number of bytes to read
        fp      - File pointer to an input file
    
    
    RETURN VALUE:
    
        Number of bytes read from file
    
    
    DESCRIPTION:
    
          This function reads a block of data from a file and places  it  in
       memory at the address of "buffer". Data is read in "raw"  form,  with
       no interpretation of "newline" characters etc. If the number of bytes
       returned is less than the number of bytes requested, either  the  end
       of the file was encountered or an error condition occured  (in  which
       case the value will be zero).
    
    
    EXAMPLES:
    
        fget(block, 512, input_fp);

    FGETS                                                             FGETS
    
    
    
    PROTOTYPE:
    
        char *fgets(char *buffer, int size, FILE *fp)
    
    
    ARGUMENTS:
    
        buffer  - Pointer to string to receive line
        size    - Maximum size of line to read
        fp      - File pointer to an input file
    
    
    RETURN VALUE:
    
        Pointer to "buffer", or 0 if end of file
    
    
    DESCRIPTION:
    
          The "fgets" function reads characters  from  the  specified  input
       file, and places them in the character  buffer  until  one  of  three
       things happens:
    
          1) A NEWLINE character is encountered.
    
          2) The END of the file is encountered.
    
          3) The limit of "size" character is read.
    
          The string is terminated with the standard  NULL  (00)  character.
       The trailing NEWLINE '\n' character is NOT  included  in  the  output
       buffer.
    
    
    EXAMPLES:
    
        fgets(input_line, 80, input_file);

    FIND_FIRST                                                   FIND_FIRST
    
    
    
    PROTOTYPE:
    
        int find_first(char *pattern, int mattrs, char name[], int &sizeh,
                       int &sizel, int &attrs, int &time, int &date)
    
    
    ARGUMENTS:
    
        pattern - File name pattern to match
        mattrs  - File attributes to match
        name    - Address of string to receive file name
        &sizeh  - Address of int to receive high word of size
        &sizel  - Address of int to receive low word of size
        &attrs  - Address of int to receive attributes
        &time   - Address of int to receive time stamp
        &date   - Address of int to receive date stamp
    
    
    RETURN VALUE:
    
        0 if successful, otherwise an operating system error code
    
    
    DESCRIPTION:
    
          This function locates the first file on the disk which matches the
       given pattern. The "mattrs" field specifies  any  special  attributes
       the files must have  in  order  to  be  matched,  use  0  for  normal
       directory searches.
    
          Subsequent files may be located using the "find_next" function.
    
          The above function prototype describes the  MS-DOS  implementation
       of the function. With other operating systems, the function may  have
       slightly  different  parameters,   due   to   differing   information
       available. See your implementation notes.
    
    
    EXAMPLES:
    
        if(find_first(pattern, 0, name, &sh, &sl, &a, &t, &d))
            abort("No matching files found\n");

    FIND_NEXT                                                     FIND_NEXT
    
    
    
    PROTOTYPE:
    
        int find_next(char name[], int &sizeh, int &sizel, int &attrs,
                      int &time, int &date)
    
    
    ARGUMENTS:
    
        name    - Address of string to receive file name
        &sizeh  - Address of int to receive high word of size
        &sizel  - Address of int to receive low word of size
        &attrs  - Address of int to receive attributes
        &time   - Address of int to receive time stamp
        &date   - Address of int to receive date stamp
    
    
    RETURN VALUE:
    
        0 if successful, otherwise an operating system error code
    
    
    DESCRIPTION:
    
          The function must be preceeded by a call to "find_first", and will
       locate the next file on  the  disk  which  matches  the  pattern  and
       attributes given to that function call.
    
          The above function prototype describes the  MS-DOS  implementation
       of the function. With other operating systems, the function may  have
       slightly  different  parameters,   due   to   differing   information
       available. See your implementation notes.
    
    
    EXAMPLES:
    
        do
            printf("%s\n", name);
        while(!find_next(name, &sh, &sl, &a, &t, &d));

    FOPEN                                                             FOPEN
    
    
    
    PROTOTYPE:
    
        FILE *fopen(char *filename, char *options)
    
    
    ARGUMENTS:
    
        filename- Name of the file to open
        options - String containing open options, valid modes are:
                    "r"  - Open file for read
                    "w"  - Open file for write
                    "rw" - Open for read/write update
                    "wa" - Open for write & append
    
    
    RETURN VALUE:
    
        File pointer to the file buffer for the open file
        Zero (0) if file could not be opened
    
    
    DESCRIPTION:
    
          This function opens a  file  for  input  ('r')  or  output  ('w'),
       allowing subsequent I/O operations to read or write the file.
    
    
    EXAMPLES:
    
        fp = fopen("input_file", "r");

    FPRINTF                                                         FPRINTF
    
    
    
    PROTOTYPE:
    
        register fprintf(FILE *fp, char *format, arg, ...)
    
    
    ARGUMENTS:
    
        fp      - File pointer to an output file
        format  - Pointer to format string
        arg     - Argument as determined by format string
        ...     - Additional arguments may be required
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          This routine performs a formatted print to  a  file  specified  by
       "fp". The "format" string is written to the file with  the  arguments
       substituted for special "conversion  characters".  These  "conversion
       characters" are identified by a preceeding '%', and may be one of the
       following:
    
                    b       - Binary number
                    c       - Character
                    d       - Decimal (signed) number
                    o       - Octal number
                    s       - String
                    u       - Unsigned decimal number
                    x       - Hexidecimal number
                    %       - A single percent sign (No argument used)
    
          A numeric "field width" specifier may be placed in between the '%'
       and the conversion character, in which case the value will be  output
       in a field of that width. If the "field width" is a negative  number,
       the output will be left justified in the field, otherwise it is right
       justified. If the field width contains a leading '0', then the output
       field will be padded with zero's, otherwise spaces are used.
    
          If no "field width" is given, the output  is  free  format,  using
       only as much space as required.
    
          NOTE: This function uses a variable number of arguments, and  must
       be declared as "register" (See "stdio.h").
    
    
    EXAMPLES:
    
        fprintf(stderr,"Filename='%s'\n", filename);
        fprintf(stdout,"Address=%04x\n", address);
        fprintf(outfile,"Amount: $%3u.%02u\n", amount / 100, amount % 100);

    FPUT                                                               FPUT
    
    
    
    PROTOTYPE:
    
        int fput(char *block, int size, FILE *fp)
    
    
    ARGUMENTS:
    
        block   - Pointer to a block of data to write
        size    - Number of bytes to write
        fp      - File pointer to an output file
    
    
    RETURN VALUE:
    
        0 if successful, otherwise an operating system error code
    
    
    DESCRIPTION:
    
          This function writes a block of data to the  indicated  file  from
       memory at the specified address. Data is written in "raw" form,  with
       no translations of "newline" characters etc. If the value returned is
       less than the value of the "size" parameter, some error condition has
       occured (Such as disk full).
    
    
    EXAMPLES:
    
        if(fput(buffer, 100, fp) < 100)
            abort("File write error\n");

    FPUTS                                                             FPUTS
    
    
    
    PROTOTYPE:
    
        fputs(char *string, FILE *fp)
    
    
    ARGUMENTS:
    
        string  - Pointer to a character string
        fp      - FIle pointer to output file
    
    
    RETURN VALUE:
    
        0 if successful, otherwise an operating system error code
    
    
    DESCRIPTION:
    
          The "fputs" function writes the specified string to the  indicated
       output file. The zero terminating the string is NOT written.
    
    
    EXAMPLES:
    
        fputs("Text message", output_file);

    FREE                                                               FREE
    
    
    
    PROTOTYPE:
    
        free(char *ptr)
    
    
    ARGUMENTS:
    
        ptr     - Pointer to a previously allocated memory block
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          The "free" function releases (de-allocates) a block of memory that
       was obtained via a call to "malloc", and returns it to the heap. This
       makes it available for use by other memory allocations.
    
    
    EXAMPLES:
    
        if(!(ptr = malloc(BUFSIZ)))     /* Allocate a temporary buffer */
            abort("Not enough memory");
        do {                            /* Copy the file over */
            size = fget(ptr, BUFSIZ, in_fp);
            fput(ptr, size, out_fp); }
        while(size == BUFSIZ);
        free(ptr);                      /* Release temporary buffer */

    FSCANF                                                           FSCANF
    
    
    
    PROTOTYPE:
    
        register int fscanf(FILE *fp, char *format, &arg, ...)
    
    
    ARGUMENTS:
    
        fp      - File pointer to an input file
        format  - Pointer to format string
        arg     - Argument as determined by format string
        ...     - Additional arguments may be required
    
    
    RETURN VALUE:
    
        The number of successful matches
        EOF (-1) if end of file or an error condition occurs
    
    
    DESCRIPTION:
    
          This routine reads a line from the specified file and scans it for
       specific values which  are  then  assigned  to  the  passed  argument
       addresses. The types of values  scanned  are  determined  by  special
       "conversion characters" within the "format" string. These "conversion
       characters" are identified by a preceeding '%', and may be one of the
       following:
    
                    b       - Binary number
                    c       - Character
                    d       - Decimal (signed) number
                    o       - Octal number
                    s       - String
                    u       - Unsigned decimal number
                    x       - Hexidecimal number
                    %       - A single percent sign (No argument used)
    
          Before scanning for  any  value,  any  leading  "space"  or  "tab"
       characters in the input line are automatically flushed.
    
          Scanning of a particular value type will terminate when either the
       end of  the  line  or  a  non-applicible  character  is  encountered.
       Scanning of strings (%s) stops with a "space" or "tab" character, and
       the stored string will be zero terminated.
    
          A numeric "field width" specifier may be placed in between the '%'
       and the conversion character, in which case  scanning  of  the  value
       will  also  terminate  if  that  many  input  characters  have   been
       processed.
    
          Scanning  for  characters  (%c)  assumes  a  "field  width"  of  1
       character (%1c) unless it is otherwise specified.

    
    
    
    
    
    
    
    
    
    
          Any other (non-conversion) characters in the  format  string  will
       cause the next character in the input string which is not  a  "space"
       or "tab" to be skipped if it matches that character.
    
          Any variable values from the input line  which  are  not  required
       must be cleared by scanning them into a "dummy" variable.
    
          The most common mistake when using "fscanf" is forgetting  to  use
       the '&'  operator  with  a  simple  variable  argument.  This  causes
       "fscanf" to store the value INDIRECTLY at the  address  contained  in
       that variable (Similar to  using  '*'  with  a  pointer)  instead  of
       storing the value into the actual variable  itself.  Arguments  which
       are array names do not require the '&' operator, since the address of
       the array is already generated by reference to its name.
    
          Unlike "fscanf" in most  other  compiler  libraries,  the  MICRO-C
       function always reads and scans a single line from the input file.
    
          NOTE: This function uses a variable number of arguments, and  must
       be declared as "register".
    
    
    EXAMPLES:
    
        if(fscanf(infile,"%s %s %u", first_name, last_name, &age) != 3)
            abort("Error in user record\n");

    FSEEK                                                             FSEEK
    
    
    
    PROTOTYPE:
    
        (1) int fseek(FILE *fp, int h_offset, unsigned l_offset, int mode)
        (2) int fseek(FILE *fp, int offset, mode)
    
    
    ARGUMENTS:
    
        fp      - File pointer to an open file
        h_offset- Highest 16 bits of offset value
        l_offset- Lowest 16 bits of offset value
        offset  - 16 bit offset value
        mode    - Type of seek
                    0 = Absolute from start of file
                    1 = Signed offset from current position
                    2 = Signed offset from end of file
    
    
    RETURN VALUE:
    
        0 if successful, otherwise an operating system error code
    
    
    DESCRIPTION:
    
          This function positions the operating system internal pointer into
       a file so that any read or write will take  place  at  the  specified
       position in the file.
    
          Most operating systems which support files of > 64K bytes in  size
       will support form (1) of the function, using both high and low offset
       values.
    
          Smaller operating  systems  may  only  support  form  (2)  of  the
       function, allowing seeking of only +/- 32K bytes.
    
          Also, some implementations may not support  all  "modes",  or  may
       only allow unsigned (positive) offsets.
    
    
    EXAMPLES:
    
        fseek(in_file, 0, 2);   /* Advance to end of file */

    FTELL                                                             FTELL
    
    
    
    PROTOTYPE:
    
        (1) int ftell(FILE *fp, int &h_offset, unsigned &l_offset)
        (2) int ftell(FILE *fp, int &offset)
    
    
    ARGUMENTS:
    
        fp      - File pointer to an open file
        h_offset- Address of int to receive high word of offset
        l_offset- Address of int to receive low word of offset
        offset  - Address of int to receive offset
    
    
    RETURN VALUE:
    
        0 if successful, otherwise an operating system error code
    
    
    DESCRIPTION:
    
          This function gets the current read/write position within a  file.
       The position returned indicates the absolute character (byte)  offset
       from the start of the file where the next read  or  write  will  take
       place.
    
          Most operating systems which support files of > 64K bytes in  size
       will support form (1) of the function, returning both  high  and  low
       offset values.
    
          Smaller operating  systems  may  only  support  form  (2)  of  the
       function,  allowing  access  to  only  the  first   65535   character
       positions.
    
    
    EXAMPLES:
    
        ftell(fp, &oldh, &oldl);    /* Save file position */
            . . .                   /* Perform some operations on the file */
        fseek(fp, oldh, oldl, 0);   /* Return to previous position */

    GETC                                                               GETC
    
    
    
    PROTOTYPE:
    
        int getc(FILE *fp)
    
    
    ARGUMENTS:
    
        fp      - File pointer to an input file
    
    
    RETURN VALUE:
    
        Value of a character read from the file (0-255)
        EOF (-1) if end of file or an error condition occurs
    
    
    DESCRIPTION:
    
          This function reads a single character from  an  input  file,  and
       returns it as a positive value in the range of 0 to 255.  A  full  16
       bit value is returned, allowing the  end  of  file  condition  to  be
       distinct from the character value 255.
    
    
    EXAMPLES:
    
        if((c = getc(input_file)) < 0)
            abort("End of file encountered\n");

    GETDIR                                                           GETDIR
    
    
    
    PROTOTYPE:
    
        int getdir(char pathname[])
    
    
    ARGUMENTS:
    
        pathname- Address of string to receive directory path
    
    
    RETURN VALUE:
    
        0 if successful, otherwise an operating system error code
    
    
    DESCRIPTION:
    
          This function retreives from the system the name of the  "current"
       directory path.
    
          The "pathname" string must be long  enough  to  hold  the  largest
       pathname supported by the system, as  indicated  by  the  "PATH_SIZE"
       definition in the "file.h" header file.
    
    
    EXAMPLES:
    
        getdir(&current_dir);

    GETENV                                                           GETENV
    
    
    
    PROTOTYPE:
    
        int getenv(char *ename, char *dest)
    
    
    ARGUMENTS:
    
        ename   - String containing name of environment variable
        dest    - Buffer to receive variable string value
    
    
    RETURN VALUE:
    
        1 if environment variable was found, 0 if not.
    
    
    DESCRIPTION:
    
          The GETENV function gets the value of a variable in  the  programs
       environment, and returns it as a string. If the environment  variable
       is not found, zero is returned, and the destination buffer is set  to
       a null (zero length) string.
    
          Use of this  function  allows  a  programs  fixed  parameters  and
       options to be specified once in environment variables, which may then
       be extracted by the program, eliminating the need  to  specify  those
       values every time the program is executed.
    
          When operating  MICRO-C  under  operating  systems  which  do  not
       support environment variables, this function will not be available.
    
    
    EXAMPLES:
    
        if(!getenv("COMSPEC", command))
            abort("No command processor defined\n");

    IN                                                                   IN
    
    
    
    PROTOTYPE:
    
        int in(unsigned port)
    
    
    ARGUMENTS:
    
        port    - I/O port address
    
    
    RETURN VALUE:
    
        The 8 bit value read from the given I/O port address
    
    
    DESCRIPTION:
    
          The "in" function reads and returns a byte (8 bits)  from  an  I/O
       port as an integer value between 0 and 255.
    
          The valid range of values for "port" depends on  the  I/O  address
       space of the processor.
    
          This function is not provided for processors which do not  support
       a separate I/O address space.
    
    
    EXAMPLES:
    
        while(in(0));   /* Wait for flag to clear */

    INW                                                                 INW
    
    
    
    PROTOTYPE:
    
        int inw(unsigned port)
    
    
    ARGUMENTS:
    
        port    - I/O port address
    
    
    RETURN VALUE:
    
        The 16 bit value read from the given I/O port address
    
    
    DESCRIPTION:
    
          The "inw" function reads and returns a word (16 bits) from an  I/O
       port as an integer value between 0 and 65535 (-1).
    
          The valid range of values for "port" depends on  the  I/O  address
       space of the processor.
    
          This function is not provided for processors which do not  support
       a separate I/O address space.
    
    
    EXAMPLES:
    
        var = inw(0);

    ISALNUM                                                         ISALNUM
    
    
    
    PROTOTYPE:
    
        int isalnum(char c)
    
    
    ARGUMENTS:
    
        c       - Any character value
    
    
    RETURN VALUE:
    
        1 if 'c' is alphabetic or numeric
        0 if 'c' is not alphabetic or numeric
    
    
    DESCRIPTION:
    
          Returns  TRUE  (1)  if  the  passed  character  'c'  is  an  ASCII
       alphabetic letter in either upper or  lower  case  or  if  'c'  is  a
       numeric digit, otherwise FALSE (0) is returned.
    
    
    EXAMPLES:
    
        while(isalnum(*ptr))        /* Copy over symbol name */
            *name++ = *ptr++;

    ISALPHA                                                         ISALPHA
    
    
    
    PROTOTYPE:
    
        int isalpha(char c)
    
    
    ARGUMENTS:
    
        c       - Any character value
    
    
    RETURN VALUE:
    
        1 if 'c' is alphabetic
        0 if 'c' is not alphabetic
    
    
    DESCRIPTION:
    
          Returns  TRUE  (1)  if  the  passed  character  'c'  is  an  ASCII
       alphabetic letter in either upper or lower case, otherwise FALSE  (0)
       is returned.
    
    
    EXAMPLES:
    
        flag = isalpha(input_char);

    ISCNTRL                                                         ISCNTRL
    
    
    
    PROTOTYPE:
    
        int iscntrl(char c)
    
    
    ARGUMENTS:
    
        c       - Any character value
    
    
    RETURN VALUE:
    
        1 if 'c' is a "control" character
        0 if 'c' is not a "control" character
    
    
    DESCRIPTION:
    
          Returns TRUE (1) is the passed character 'c' is an ASCII "control"
       character (0x00-0x1F or 0x7F), otherwise FALSE (0) is returned.
    
    
    EXAMPLES:
    
        putc(iscntrl(c) ? '.' : c, stdout); /* Display controls as '.' */

    ISDIGIT                                                         ISDIGIT
    
    
    
    PROTOTYPE:
    
        int isdigit(char c)
    
    
    ARGUMENTS:
    
        c       - Any character value
    
    
    RETURN VALUE:
    
        1 if 'c' is numeric
        0 if 'c' is not numeric
    
    
    DESCRIPTION:
    
          Returns TRUE (1) is the passed character 'c'  is  an  ASCII  digit
       ('0'-'9'), otherwise FALSE (0) is returned.
    
    
    EXAMPLES:
    
        value = 0;
        while(isdigit(*ptr))
            value = (value * 10) + (*ptr++ - '0');

    ISGRAPH                                                         ISGRAPH
    
    
    
    PROTOTYPE:
    
        int isgraph(char c)
    
    
    ARGUMENTS:
    
        c       - Any character value
    
    
    RETURN VALUE:
    
        1 if 'c' is a non-space printable character
        0 if 'c' is a space or not printable
    
    
    DESCRIPTION:
    
          Returns TRUE (1) if the passed character 'c' is a printable  ASCII
       character other than  a  space  character,  otherwise  FALSE  (0)  is
       returned.
    
    
    EXAMPLES:
    
        putc(isgraph(c) ? c : '.', stdout);

    ISLOWER                                                         ISLOWER
    
    
    
    PROTOTYPE:
    
        int islower(char c)
    
    
    ARGUMENTS:
    
        c       - Any character value
    
    
    RETURN VALUE:
    
        1 if 'c' is lower case alphabetic
        0 if 'c' is not lower case alphabetic
    
    
    DESCRIPTION:
    
          Returns  TRUE  (1)  if  the  passed  character  'c'  is  an  ASCII
       alphabetic letter of lower case, otherwise FALSE (0) is returned.
    
    
    EXAMPLES:
    
        flag = islower(input_char);

    ISPUNCT                                                         ISPUNCT
    
    
    
    PROTOTYPE:
    
        int ispunct(char c)
    
    
    ARGUMENTS:
    
        c       - Any character value
    
    
    RETURN VALUE:
    
        1 if 'c' is a printable non-alphanumeric character
        0 if 'c' is not printable or alphanumeric
    
    
    DESCRIPTION:
    
          Returns TRUE (1) if the passed character 'c' is a printable  ASCII
       character which is not a letter of the alphabet or a  numeric  digit,
       otherwise FALSE (0) is returned.
    
    
    EXAMPLES:
    
        while(ispunct(*ptr))
            ++ptr;

    ISSPACE                                                         ISSPACE
    
    
    
    PROTOTYPE:
    
        int isspace(char c)
    
    
    ARGUMENTS:
    
        c       - Any character value
    
    
    RETURN VALUE:
    
        1 if 'c' is a space character (space, tab or newline)
        0 if 'c' is not a space character
    
    
    DESCRIPTION:
    
          Returns TRUE (1) if the passed character 'c' is one  of  a  space,
       tab or newline, otherwise FALSE (0) is returned.
    
    
    EXAMPLES:
    
        while(isspace(*ptr))
            ++ptr;

    ISUPPER                                                         ISUPPER
    
    
    
    PROTOTYPE:
    
        int isupper(char c)
    
    
    ARGUMENTS:
    
        c       - Any character value
    
    
    RETURN VALUE:
    
        1 if 'c' is upper case alphabetic
        0 if 'c' is not upper case alphabetic
    
    
    DESCRIPTION:
    
          Returns  TRUE  (1)  if  the  passed  character  'c'  is  an  ASCII
       alphabetic letter of upper case, otherwise FALSE (0) is returned.
    
    
    EXAMPLES:
    
        flag = isupper(input_char);

    LONGJMP                                                         LONGJMP
    
    
    
    PROTOTYPE:
    
        longjmp(int savenv[3], int rvalue)
    
    
    ARGUMENTS:
    
        savenv  - Save area for program context
        rvalue  - Value to be returned by "setjmp"
    
    
    RETURN VALUE:
    
        N/A - Function never returns
    
    
    DESCRIPTION:
    
          The  "longjmp"  function  causes  execution  to  transfer  to  the
       "setjmp" call which  set  up  the  "savenv"  variable.  The  "setjmp"
       function will appear to return the value of "rvalue".
    
          NOTE-1: "longjmp" may  only  be  used  from  within  the  function
       calling "setjmp" or a function which has been called  "beneath"  that
       function. IT MUST NOT BE USED AFTER THE FUNCTION CALLING "SETJMP" HAS
       TERMINATED.
    
          NOTE-2: If "rvalue" is zero, the function  calling  "setjmp"  will
       assume that it is returning from initialization. Unless you want this
       unusual behavior, you should not pass  a  return  value  of  zero  to
       "longjmp".
    
          See also SETJMP.
    
    
    EXAMPLES:
    
        if(getc(stdin) == ('C'-'@'))    /* If Control-C entered... */
            longjmp(savearea, 1);       /* Return to main function */

    MALLOC                                                           MALLOC
    
    
    
    PROTOTYPE:
    
        char *malloc(int size)
    
    
    ARGUMENTS:
    
        size    - Size of memory block to allocate (in bytes).
    
    
    RETURN VALUE:
    
        0       - Memory allocation failed
        !0      - Pointer to allocated memory block
    
    
    DESCRIPTION:
    
          The "malloc" function allocates a block of memory of the specified
       size from the heap, and returns a pointer to  it.  This  memory  will
       remain allocated until it is  explicitly  releases  with  the  "free"
       function.
    
    
    EXAMPLES:
    
        if(!(ptr = malloc(BUFSIZ)))     /* Allocate a temporary buffer */
            abort("Not enough memory");
        do {                            /* Copy the file over */
            size = fget(ptr, BUFSIZ, in_fp);
            fput(ptr, size, out_fp); }
        while(size == BUFSIZ);
        free(ptr);                      /* Release temporary buffer */

    MAX                                                                 MAX
    
    
    
    PROTOTYPE:
    
        int max(int value1, int value2)
    
    
    ARGUMENTS:
    
        value1  - Any integer value
        value2  - Any integer value
    
    
    RETURN VALUE:
    
        The greater of "value1" or "value2"
    
    
    DESCRIPTION:
    
          The "max" function returns the higher of its two argument values.
    
    
    EXAMPLES:
    
        biggest = max(a, b);

    MEMCPY                                                           MEMCPY
    
    
    
    PROTOTYPE:
    
        memcpy(char *dest, char *source, unsigned size)
    
    
    ARGUMENTS:
    
        dest    - Pointer to the destination
        source  - Pointer to the souce
        size    - Number of bytes to copy
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          The "memcpy" function will copy the specified number of bytes from
       the source to the destination.
    
    
    EXAMPLES:
    
        memcpy(buffer1, buffer2, 256);

    MEMSET                                                           MEMSET
    
    
    
    PROTOTYPE:
    
        memset(char *block, char value, unsigned size)
    
    
    ARGUMENTS:
    
        block   - Pointer to a block of memory
        value   - Value to initialize memory with
        size    - Number of bytes to initialize
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          Sets a block of memory  beginning  at  the  pointer  "block",  for
       "size" bytes to the byte value "value".
    
    
    EXAMPLES:
    
        memset(buffer, 0, 100);

    MIN                                                                 MIN
    
    
    
    PROTOTYPE:
    
        int min(int value1, int value2)
    
    
    ARGUMENTS:
    
        value1  - Any integer value
        value2  - Any integer value
    
    
    RETURN VALUE:
    
        The smaller of "value1" or "value2"
    
    
    DESCRIPTION:
    
          The "min" function returns the lower of its two argument values.
    
    
    EXAMPLES:
    
        least = min(a, b);

    MKDIR                                                             MKDIR
    
    
    
    PROTOTYPE:
    
        int mkdir(char *pathname)
    
    
    ARGUMENTS:
    
        pathname- Name of directory to create
    
    
    RETURN VALUE:
    
        0 if successful, otherwise an operating system error code
    
    
    DESCRIPTION:
    
          The "mkdir" function create a new directory on the disk under  the
       specified path name.
    
    
    EXAMPLES:
    
        mkdir("subdir");

    NARGS                                                             NARGS
    
    
    
    PROTOTYPE:
    
        int nargs()
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        The number of arguments passed to the calling function
    
    
    DESCRIPTION:
    
          Returns the number of arguments passed to a "register" function.
    
          NOTE: When  calling  a  "register"  function,  MICRO-C  loads  the
       accumulator with the number of arguments just prior  to  calling  the
       function. This "nargs" routine is  simply  a  null  definition  which
       returns with the same value in the accumulator as was there  when  it
       was called. Therefore "nargs" MUST BE  THE  FIRST  ARITHMETIC  ENTITY
       EVALUATED WITHIN  THE  REGISTER  FUNCTION  or  the  contents  of  the
       accumulator will be lost. Some examples of "register" definitions and
       the use of "nargs" may be found in the library source code.
    
    
    EXAMPLES:
    
        first_arg = nargs() * 2 + &arguments;

    OUT                                                                 OUT
    
    
    
    PROTOTYPE:
    
        out(unsigned port, int value)
    
    
    ARGUMENTS:
    
        port    - I/O port address
        value   - Value to write to I/O port
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          The "out" function writes a byte (8 bit) value to an I/O port.
    
          The valid range of values for "port" depends on  the  I/O  address
       space of the processor.
    
          This function is not provided for processors which do not  support
       a separate I/O address space.
    
    
    EXAMPLES:
    
        out(0, 0);      /* Output 0 to I/O port 0 */

    OUTW                                                               OUTW
    
    
    
    PROTOTYPE:
    
        outw(unsigned port, int value)
    
    
    ARGUMENTS:
    
        port    - I/O port address
        value   - Value to write to I/O port
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          The "outw" function writes a word (16 bit) value to an I/O port.
    
          The valid range of values for "port" depends on  the  I/O  address
       space of the processor.
    
          This function is not provided for processors which do not  support
       a separate I/O address space.
    
    
    EXAMPLES:
    
        outw(0, 0);     /* Write 0 to I/O ports 0 and 1 */

    PEEK                                                               PEEK
    
    
    
    PROTOTYPE:
    
        (1) int peek(unsigned address)
        (2) int peek(unsigned h_addr, unsigned l_addr)
        (3) int peek(unsigned segment, unsigned offset)
    
    
    ARGUMENTS:
    
        segment - Memory segment
        offset  - Offset into segment
        h_addr  - High word of memory address
        l_addr  - Low word of memory address
        address - 16 bit memory address
    
    
    RETURN VALUE:
    
        The 8 bit value read from the given memory address
    
    
    DESCRIPTION:
    
          The "peek" function reads and returns a byte (8 bits) from  memory
       as an integer value between 0 and 255.
    
          Processors such as the 8080 or 6809 which address 64K of memory or
       less use form (1) of the function.
    
          Non-segmented processors addressing more  than  64K  such  as  the
       68000 use form (2) of the function.
    
          Processors employing a "segmented" architecture such as  the  8086
       use form (3) of the function.
    
    
    EXAMPLES:
    
        while(peek(0)); /* Wait for flag to clear */

    PEEKW                                                             PEEKW
    
    
    
    PROTOTYPE:
    
        (1) int peekw(unsigned address)
        (2) int peekw(unsigned h_addr, unsigned l_addr)
        (3) int peekw(unsigned segment, unsigned offset)
    
    
    ARGUMENTS:
    
        segment - Memory segment
        offset  - Offset into segment
        h_addr  - High word of memory address
        l_addr  - Low word of memory address
        address - 16 bit memory address
    
    
    RETURN VALUE:
    
        The 16 bit value read from the given memory address
    
    
    DESCRIPTION:
    
          The "peekw" function reads and  returns  a  word  (16  bits)  from
       memory as an integer value between 0 and 65535 (-1).
    
          Processors such as the 8080 or 6809 which address 64K of memory or
       less use form (1) of the function.
    
          Non-segmented processors addressing more  than  64K  such  as  the
       68000 use form (2) of the function.
    
          Processors employing a "segmented" architecture such as  the  8086
       use form (3) of the function.
    
    
    EXAMPLES:
    
        var = peekw(0));

    POKE                                                               POKE
    
    
    
    PROTOTYPE:
    
        (1) poke(unsigned address, int value)
        (2) poke(unsigned h_addr, unsigned l_addr, int value)
        (3) poke(unsigned segment, unsigned offset, int value)
    
    
    ARGUMENTS:
    
        segment - Memory segment
        offset  - Offset into segment
        h_addr  - High word of memory address
        l_addr  - Low word of memory address
        address - 16 bit memory address
        value   - Value to be written to memory
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          The "poke" function writes a byte (8 bit) value to memory.
    
          Processors such as the 8080 or 6809 which address 64K of memory or
       less use form (1) of the function.
    
          Non-segmented processors addressing more  than  64K  such  as  the
       68000 use form (2) of the function.
    
          Processors employing a "segmented" architecture such as  the  8086
       use form (3) of the function.
    
    
    EXAMPLES:
    
        poke(0, 0);     /* Write 0 to location 0 */

    POKEW                                                             POKEW
    
    
    
    PROTOTYPE:
    
        (1) pokew(unsigned address, int value)
        (2) pokew(unsigned h_addr, unsigned l_addr, int value)
        (3) pokew(unsigned segment, unsigned offset, int value)
    
    
    ARGUMENTS:
    
        segment - Memory segment
        offset  - Offset into segment
        h_addr  - High word of memory address
        l_addr  - Low word of memory address
        address - 16 bit memory address
        value   - Value to be written to memory
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          The "pokew" function writes a word (16 bit) value to memory.
    
          Processors such as the 8080 or 6809 which address 64K of memory or
       less use form (1) of the function.
    
          Non-segmented processors addressing more  than  64K  such  as  the
       68000 use form (2) of the function.
    
          Processors employing a "segmented" architecture such as  the  8086
       use form (3) of the function.
    
    
    EXAMPLES:
    
        pokew(0, 0);    /* Write 0 to locations 0 and 1 */

    PRINTF                                                           PRINTF
    
    
    
    PROTOTYPE:
    
        register printf(char *format, arg, ...)
    
    
    ARGUMENTS:
    
        format  - Pointer to format string
        arg     - Argument as determined by format string
        ...     - Additional arguments may be required
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          The "printf" routine performs a formatted print  to  the  standard
       output device  (usually  system  console).  The  "format"  string  is
       written  with  the  arguments  substituted  for  special  "conversion
       characters".
    
          See "fprintf" for more information on format strings.
    
          NOTE: This function uses a variable number of arguments, and  must
       be declared as "register" (See "stdio.h").
    
    
    EXAMPLES:
    
        printf("Hello world!!!\n");
        printf("File '%s', has %u lines\n", filename, num_lines);

    PUTC                                                               PUTC
    
    
    
    PROTOTYPE:
    
        putc(char c, FILE *fp)
    
    
    ARGUMENTS:
    
        c       - Any character value
        fp      - File pointer to an output file
    
    
    RETURN VALUE:
    
        0 if successful, otherwise an operating system error code
    
    
    DECRIPTION:
    
          This function writes the character 'c' to the  file  indicated  by
       "fp". The "newline" (\n) character will be translated  into  whatever
       character(s) are required by the operating system to separate records
       in the file.
    
    
    EXAMPLES:
    
        putc('*', fp);
        putc('\n', stderr);

    RAND                                                               RAND
    
    
    
    PROTOTYPE:
    
        unsigned rand(unsigned limit)
    
    
    ARGUMENTS:
    
        limit   - Maximum value to return
    
    
    RETURN VALUE:
    
        A pseudo-random number in the range of 0 to (limit-1)
    
    
    DESCRIPTION:
    
          The "rand" function calculates the next value of  a  pseudo-random
       sequence, based on a 16 bit unsigned "seed" value, which it maintains
       in the global variable "RAND_SEED". The new value is  stored  as  the
       new seed value, and is then divided  by  the  "limit"  parameter,  to
       obtain the remainder, which is returned. This  results  in  a  random
       number in the range of zero (0) to (limit - 1).
    
          Any  particular  sequence  may  be  repeated,  by   reseting   the
       "RAND_SEED" value.
    
    
    EXAMPLES:
    
        value = rand(52);

    RENAME                                                           RENAME
    
    
    
    PROTOTYPE:
    
        int rename(char *pathname, char *newname)
    
    
    ARGUMENTS:
    
        pathname- Name of file to rename
        newname - New name for file
    
    
    RETURN VALUE:
    
        0 if successful, otherwise an operating system error code
    
    
    DESCRIPTION:
    
          This function changes the name of an existing file  to  the  ASCII
       string specified by newname.
    
    
    EXAMPLES:
    
        rename("output.dat", "output.bak");

    REWIND                                                           REWIND
    
    
    
    PROTOTYPE:
    
        int rewind(FILE *fp)
    
    
    ARGUMENTS:
    
        fp      - File pointer to an open file
    
    
    RETURN VALUE:
    
        0 if successful, otherwise an operating system error code
    
    
    DESCRIPTION:
    
          This function resets the operating system internal file pointer so
       than any subsequent read or writes will be at the  beginning  of  the
       file.
    
    
    EXAMPLES:
    
        rewind(input_file);

    RMDIR                                                             RMDIR
    
    
    
    PROTOTYPE:
    
        int rmdir(char *pathname)
    
    
    ARGUMENTS:
    
        pathname- Name of directory to delete
    
    
    RETURN VALUE:
    
        0 if successful, otherwise an operating system error code
    
    
    DESCRIPTION:
    
          This function removes a directory from the disk. On most  systems,
       the directory  must  be  empty  (contains  no  files)  otherwise  the
       function will fail.
    
    
    EXAMPLES:
    
        rmdir("subdir");

    SCANF                                                             SCANF
    
    
    
    PROTOTYPE:
    
        register int scanf(char *format, arg1, arg2, ...)
    
    
    ARGUMENTS:
    
        format  - Pointer to format string
        arg     - Argument as determined by format string
        ...     - Additional arguments may be required
    
    
    RETURN VALUE:
    
        The number of successful matches
        EOF (-1) if end of file or an error condition occurs
    
    
    DESCRIPTION:
    
          The "scanf" function reads and scans  a  line  from  the  standard
       input device (usually system console) for specific values. Values are
       read and assigned to  the  passed  argument  addresses  according  to
       special "conversion characters" in the "format" string.
    
          See "fscanf" for more information on format strings.
    
          NOTE: This function uses a variable number of arguments, and  must
       be declared as "register".
    
    
    EXAMPLES:
    
        do
            printf("Please enter your First & Last names, and your age?");
        while(scanf("%s %s %u", first_name, last_name, &age) != 3);

    SETJMP                                                           SETJMP
    
    
    
    PROTOTYPE:
    
        int setjmp(int savenv[3])
    
    
    ARGUMENTS:
    
        savenv  - Save area for program context
    
    
    RETURN VALUE:
    
        0 is returned when actually called
        Value passed to "longjmp" is returned otherwise
    
    
    DESCRIPTION:
    
          When called, the "setjmp" function stores  the  current  execution
       state of the program into the passed integer array, and  returns  the
       value zero.
    
          The "longjmp" function may then be used to return the  program  to
       the "setjmp" call. In this case, the value returned by "setjmp"  will
       be the value which was passed to "longjmp". This allows the  function
       containing "setjmp" to determine which call to  "longjmp"  transfered
       execution to it.
    
          See also LONGJMP.
    
    
    EXAMPLES:
    
        switch(setjmp(savearea)) {
            case 0 : printf("Longjmp has been set up"); break;
            case 1 : printf("Control-C Interrupt");     break;
            case 2 : printf("Reset command executed");  break;
            default: printf("Software error trap");     break; }

    SPRINTF                                                         SPRINTF
    
    
    
    PROTOTYPE:
    
        register sprintf(char *dest, char *format, arg, ...)
    
    
    ARGUMENTS:
    
        dest    - Pointer to destination string
        format  - Pointer to format string
        arg     - Argument as determined by format string
        ...     - Additional arguments may be required
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          The "sprintf" routine performs a formatted print to  a  string  in
       memory. The "format" string is written to the destination string with
       the arguments substituted for special "conversion characters".
    
          See "fprintf" for more information on format strings.
    
          NOTE: This function uses a variable number of arguments, and  must
       be declared as "register" (See "stdio.h").
    
    
    EXAMPLES:
    
        sprintf(header_file, "/lib/%s.h", header_name);

    SQRT                                                               SQRT
    
    
    
    PROTOTYPE:
    
        int sqrt(unsigned value)
    
    
    ARGUMENTS:
    
        value   - Number for which to calculate square root
    
    
    RETURN VALUE:
    
        The integer square root (rounded up) of the argument value
    
    
    DESCRIPTION:
    
          The  SQRT  function  returns  the  smallest  number   which   when
       multiplied by itself will give a number equal to or larger  that  the
       argument value.
    
    
    EXAMPLES:
    
    /*
     * Draw a circle about point (x, y) of radus (r)
     */
    circle(x, y, r)
        int x, y, r;
    {
        int i, j, k, rs, lj;
    
        rs = (lj = r)*r;
        for(i=0; i <= r; ++i) {
            j = k = sqrt(rs - (i*i));
            do {
                plot_xy(x+i, y+j);
                plot_xy(x+i, y-j);
                plot_xy(x-i, y+j);
                plot_xy(x-i, y-j); }
            while(++j < lj);
            lj = k; }
    }

    SSCANF                                                           SSCANF
    
    
    
    PROTOTYPE:
    
        register int sscanf(char *input, char *format, arg1, arg2, ...)
    
    
    ARGUMENTS:
    
        input   - Pointer to input string
        format  - Pointer to format string
        arg     - Argument as determined by format string
        ...     - Additional arguments may be required
    
    
    RETURN VALUE:
    
        The number of successful matches
    
    
    DESCRIPTION:
    
          The "sscanf" function  scans  a  string  in  memory  for  specific
       values. Values are read and assigned to the passed argument addresses
       according to special "conversion characters" in the "format" string.
    
          See "fscanf" for more information on format strings.
    
          NOTE: This function uses a variable number of arguments, and  must
       be declared as "register".
    
    
    EXAMPLES:
    
        sscanf(pathname,"/%s/%s", directory, filename);

    STRBEG                                                           STRBEG
    
    
    
    PROTOTYPE:
    
        int strbeg(char *string1, char *string2)
    
    
    ARGUMENTS:
    
        string1 - Pointer to character string to test
        string2 - Pointer to character string to check for
    
    
    RETURN VALUE:
    
        0   - String1 does not begin with string2
        1   - String1 begins with string2
    
    
    DECRIPTION:
    
          Tests the passed "string1" to determine if it begins with the same
       data as is contained within "string2".
    
    
    EXAMPLES:
    
        if(strbeg(command, "delete"))
            delete_file(&command[6]);

    STRCAT                                                           STRCAT
    
    
    
    PROTOTYPE:
    
        char *strcat(char *dest, *source)
    
    
    ARGUMENTS:
    
        dest    - Pointer to destination string
        source  - Pointer to source string
    
    
    RETURN VALUE:
    
        Pointer to zero terminating destination string
    
    
    DESCRIPTION:
    
          This function concatinates the source string onto the tail of  the
       destination string. The destination string must be  large  enough  to
       hold the entire contents of both strings.
    
    
    EXAMPLES:
    
        strcat(program_name, ".c");

    STRCHR                                                           STRCHR
    
    
    
    PROTOTYPE:
    
        char *strchr(char *string, char chr)
    
    
    ARGUMENTS:
    
        string  - Pointer to a character string
        chr     - Character to look for
    
    
    RETURN VALUE:
    
        Pointer to the first occurance of 'chr' in 'string'
        Zero (0) if character was not found
    
    
    DECRIPTION:
    
          Searches  the  passed  string  got  the  first  occurance  of  the
       specified character. If the character is  found,  a  pointer  to  its
       position in the string is returned. If the character is not found,  a
       null pointer is returned.
    
          The null (0) character is treated as valid data by this  function,
       thus:
          strchr(string,  0);  would  return  the  position  of   the   null
       terminator of the string.
    
    
    EXAMPLES:
    
        comma = strchr(buffer, ',');

    STRCMP                                                           STRCMP
    
    
    
    PROTOTYPE:
    
        int strcmp(char *string1, char *string2)
    
    
    ARGUMENTS:
    
        string1 - Pointer to first string
        string2 - Pointer to second string
    
    
    RETURN VALUE:
    
        0   - Strings match exactly
        1   - String1 is greater than string2
        -1  - String2 is greater than string1
    
    
    DESCRIPTION:
    
          This function compares two strings character by character. If  the
       two strings are identical, a zero  (0)  is  returned.  If  the  first
       string is greater than the second (as far as ASCII is  concerned),  a
       one (1) is returned. If the second string is greater, a negative  one
       (-1) is returned.
    
    
    EXAMPLES:
    
        if(!strcmp(command, "quit"))
            exit(0);

    STRCPY                                                           STRCPY
    
    
    
    PROTOTYPE:
    
        char *strcpy(char *dest, char *source)
    
    
    ARGUMENTS:
    
        dest    - Pointer to destination string
        souce   - Pointer to source string
    
    
    RETURN VALUE:
    
        Pointer to zero terminating destination string
    
    
    DESCRIPTION:
    
          This function copies the source string to the destination  string.
       All data is copied up to and including the zero byte which terminates
       the string. The destination string must be large enough to  hold  the
       entire source.
    
    
    EXAMPLES:
    
        strcpy(filename, argv[1]);

    STRLEN                                                           STRLEN
    
    
    
    PROTOTYPE:
    
        int strlen(char *string)
    
    
    ARGUMENTS:
    
        string  - Pointer to a character string
    
    
    RETURN VALUE:
    
        The length of the string
    
    
    DECRIPTION:
    
          Returns the length in character of the passed string.  The  length
       does not include the zero byte which terminates the string.
    
    
    EXAMPLES:
    
        length = strlen(command);

    STRNCAT                                                         STRNCAT
    
    
    
    PROTOTYPE:
    
        char *strncat(char *dest, *source, unsigned length)
    
    
    ARGUMENTS:
    
        dest    - Pointer to destination string
        source  - Pointer to source string
        length  - Maximum number of characters to copy
    
    
    RETURN VALUE:
    
        Pointer to zero terminating destination string
    
    
    DESCRIPTION:
    
          This function concatinates the source string onto the tail of  the
       destination string. If the source string exceeds  "length"  bytes  in
       size, only that many characters are copied.
    
    
    EXAMPLES:
    
        strncat(path, filename, 64);

    STRNCMP                                                         STRNCMP
    
    
    
    PROTOTYPE:
    
        int strncmp(char *string1, char *string2, unsigned length)
    
    
    ARGUMENTS:
    
        string1 - Pointer to first string
        string2 - Pointer to second string
        length  - Number of bytes to compare
    
    
    RETURN VALUE:
    
        0   - Strings match exactly
        1   - String1 is greater than string2
        -1  - String2 is greater than string1
    
    
    DESCRIPTION:
    
          This function compares two strings character  by  character  until
       either a difference is detected, or  "length"  characters  have  been
       compared. If the two string portions are identical,  a  zero  (0)  is
       returned. If the first string is greater than the second (as  far  as
       ASCII is concerned), a one (1) is returned. If the second  string  is
       greater, a negative one (-1) is returned.
    
    
    EXAMPLES:
    
        len = strlen(buffer) - 3;
        for(i=1; i < len; ++i)
            if(strncmp(&buffer[i], "***", 3)
                abort("Found three stars\n");

    STRNCPY                                                         STRNCPY
    
    
    
    PROTOTYPE:
    
        strncpy(char *dest, char *source, unsigned length)
    
    
    ARGUMENTS:
    
        dest    - Pointer to destination string
        souce   - Pointer to source string
        length  - Number of bytes to copy
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          This function copies "length" characters from the source string to
       the  destination  string.  If  the  source  string  is  shorter  than
       "length", the destination string is padded with nulls. If the  source
       string is longer than "length", only that many characters are copied,
       and the destination string is NOT zero terminated.
    
    
    EXAMPLES:
    
        strncpy(filename, argv[1], 64);

    STRSTR                                                           STRSTR
    
    
    
    PROTOTYPE:
    
        char *strstr(char *string1, char *string2)
    
    
    ARGUMENTS:
    
        string1 - Pointer to character string to test
        string2 - Pointer to substring to search for
    
    
    RETURN VALUE:
    
        Pointer to substring, or 0 if not found
    
    
    DECRIPTION:
    
          Searches the passed "string1"  for  the  first  occurance  of  the
       passed "string2". If found,  a  pointer  to  the  beginning  of  that
       substring within "string1" is returned.
    
    
    EXAMPLES:
    
        if(ptr = strstr(command, "delete"))
            delete_file(&ptr[6]);

    SYSTEM                                                           SYSTEM
    
    
    
    PROTOTYPE:
    
        int system(char *command)
    
    
    ARGUMENTS:
    
        command - A system command to be executed
    
    
    RETURN VALUE:
    
        0 if successful, otherwise an operating system error code
    
    
    DESCRIPTION:
    
          The SYSTEM function accepts any  operating  system  command  as  a
       string parameter, and passes that command to the operating system  to
       be executed.
    
          When the command has terminated,  execution  will  resume  in  the
       MICRO-C program, with the statement following the call to SYSTEM.
    
    
    EXAMPLES:
    
        system("DEL *.TMP");

    TOLOWER                                                         TOLOWER
    
    
    
    PROTOTYPE:
    
        char tolower(char c)
    
    
    ARGUMENTS:
    
        c   - Any character value
    
    
    RETURN VALUE:
    
        The value of 'c', converted to lower case
    
    
    DESCRIPTION:
    
          Returns the value of 'c' converted to lower case. If 'c' is not  a
       letter of upper case, no change is made, and the  original  value  of
       'c' is returned.
    
    
    EXAMPLES:
    
        input_char = tolower(getc(stdin));

    TOUPPER                                                         TOUPPER
    
    
    
    PROTOTYPE:
    
        char toupper(char c)
    
    
    ARGUMENTS:
    
        c   - Any character value
    
    
    RETURN VALUE:
    
        The value of 'c', converted to upper case
    
    
    DESCRIPTION:
    
          Returns the value of 'c' converted to upper case. If 'c' is not  a
       letter of lower case, no change is made, and the  original  value  of
       'c' is returned.
    
    
    EXAMPLES:
    
        putc(toupper(output_char), stdout);

    MICRO-C                                                          Page: 61


    10.2 IBM-PC/MS-DOS Library Functions
    
        The following functions are available only under the MS-DOS operating
    system, on IBM-PC or compatible systems.
    
        These routines perform operations which are closely tied to the 8086
    family of processors, the IBM-PC hardware, or the MS-DOS operating system,
    and are therefore impractical to implement on a "general" basis.

    ALLOC_SEG                                                     ALLOC_SEG
    
    
    
    PROTOTYPE:
    
        int alloc_seg(int size)
    
    
    ARGUMENTS:
    
        size    - Number of 16 byte paragraphs to allocate
    
    
    RETURN VALUE:
    
    
        0       - Not enough free memory available
        !0      - The segment address of the allocated memory
    
    
    DESCRIPTION:
    
             The "alloc_seg" function allocates a 'segment' of  memory  from
          DOS. The size is given in  16  byte  "paragraphs".  The  allocated
          memory will be outside of the data memory available to the MICRO-C
          program, and therefore must  be  accessed  via  assembly  lenguage
          functions, or with the "peek" and "poke" library functions.
    
    
    EXAMPLES:
    
        if(!(aseg = alloc(4096)))   /* Get a 64K data segment */
            abort("Not enough memory!!!");
        set_es(aseg);               /* Set up extra segment */
        asm_func();                 /* Invoke assembler function */

    CCLOSE                                                           CCLOSE
    
    
    
    PROTOTYPE:
    
        Cclose()
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
             This function closes the communications port previously  opened
          using "Copen". The system interrupt vectors and all other hooks to
          the comm port are restored.
    
             This function must be called before any program  using  "Copen"
          terminates, otherwise the communications port will be left  in  an
          indeterminate state.  If  this  is  not  done,  there  will  be  a
          possibility of system crash if an interrupt is received  from  the
          port after the program has terminated.
    
    
    EXAMPLES:
    
        Cclose();       /* Close comm port */
        exit(0);        /* And terminate */

    CGETC                                                             CGETC
    
    
    
    PROTOTYPE:
    
        int Cgetc()
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        Character read from the communications port
    
    
    DESCRIPTION:
    
             This function reads a single character from the  communications
          port previously opened with "Copen". If no character is available,
          "Cgetc" will wait for one.
    
    
    EXAMPLES:
    
        /* Get a string from the comm port */
        while((c = cgetc()) != '\r')
            *ptr++ = c;
        *ptr = 0;

    COPEN                                                             COPEN
    
    
    
    PROTOTYPE:
    
        int Copen(int port, int speed, int mode, int modem)
    
    
    ARGUMENTS:
    
        port    - Comm port to use (1 or 2)
        speed   - Baudrate divisor to set
        mode    - Communications parameters to set
        modem   - Modem control lines to set
    
    RETURN VALUE:
    
        0       - Successful open
        !0      - Requested comm port is not available
    
    
    DESCRIPTION:
    
             The "Copen" function opens a serial communications port on  the
          IBM PC for  access.  An  independant  interrupt  handler  and  I/O
          drivers  are  installed,  which  allow  high  speed  full   duplex
          operation of the serial port with optional XON/XOFF  flow  control
          of both receive and transmit streams.
    
             Only one serial port may be accessed  at  a  time  using  these
          functions,  If  "Copen"  is  called  more  than  once,   it   will
          automatically close the last port before opening the new one.
    
             The meaning of the "speed", "mode", and "modem"  parameters  if
          documented in the "comm.h" header file.
    
             An external "char" variable "Cflags" may be accessed to  enable
          or disable transparency of the serial channel. When  "transparent"
          is selected, XON/XOFF flow control is disabled, and  all  data  is
          sent and received with no changes. When operating  in  this  mode,
          you must insure that "Cgetc" is called frequently enough that  the
          256 byte internal receive buffer will not overflow.
    
             Since "Cflags" is used by the  interrupt  handler,  you  should
          disable and enable interrupts around any accessed to it.

    
    
    
    EXAMPLES:
    
        #include comm.h     /* Get comm port defintions */
    
            extern char Cflags;
    
        /*
         * Program to read & echo characters on the serial port
         * in transparent mode. (Until ESCAPE char is received)
         */
        main()
        {
            char c;
    
            if(Copen(1, _2300, PAR_NO|DATA_8|STOP_1, SET_RTS|SET_DTR))
                abort("Cannot access COM1");
    
            disable();                  /* Disable interrupts */
            Cflags |= TRANSPARENT;      /* Set transparency */
            enable();                   /* Re-enable interrupts */
    
            while((c = Cgetc()) != 0x1B)    /* Do until ESCAPE */
                Cputc(c);
    
            Cclose();                   /* Close the serial port */
        }

    COPY_SEG                                                       COPY_SEG
    
    
    
    PROTOTYPE:
    
        copy_seg(int dseg, int doffset, int sseg, int soffset, int size)
    
    
    ARGUMENTS:
    
        dseg    - Destination segment
        doffset - Destination offset
        sseg    - Source segment
        soffset - Source offset
        size    - Number of bytes to copy
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
             This function perform a copy  between  80X86  processor  memory
          segments. A number of bytes equal to "size"  is  copied  from  the
          source segment and offset to the destination segment and offset.
    
    
    EXAMPLES:
    
        /* Save the video display contents */
        copy_seg(get_ds(), buffer, _V_BASE, 0, (25*80)*2);

    CPU                                                                 CPU
    
    
    
    PROTOTYPE:
    
        int cpu()
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        0       - CPU is 8088 or 8086
        1       - CPU is 80188 or 80186
        2       - CPU is 80286
        3       - CPU is 80386 or 80486
    
    
    DESCRIPTION:
    
             This function returns a simple  integer  which  identifies  the
          processor type on which the program is currently executing.
    
    
    EXAMPLES:
    
        if(cpu() < 2)
            abort("This program requires at least an 80286");

    CPUTC                                                             CPUTC
    
    
    
    PROTOTYPE:
    
        Cputc(char c)
    
    
    ARGUMENTS:
    
        c       - Character to write to communciation port
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
             The  "Cputc"  function  writes  the  given  character  to   the
          communcinations port previously opened by "Copen".
    
    
    EXAMPLES:
    
        while(*ptr)         /* Write a string to comm port */
            Cputc(*ptr++);

    CSIGNALS                                                       CSIGNALS
    
    
    
    PROTOTYPE:
    
        int Csignals()
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        The modem input signals read from the open comm port
    
    
    DESCRIPTION:
    
             This function reads the modem input signals (DSR, CD,  RI  etc)
          from the serial communication port previously opened  by  "Copen",
          and returns them as an integer value.
    
             The meaning of the individual bits in  the  value  returned  by
          "Csignals" is documented in the "comm.h" header file.
    
    
    EXAMPLES:
    
        if(!(Csignals() & DSR)) {
            Cclose();
            abort("Modem not ready"); }

    CTESTC                                                           CTESTC
    
    
    
    PROTOTYPE:
    
        int Ctestc()
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        0-255   - Character read from comm port
        -1      - No character available
    
    
    DESCRIPTION:
    
             This function tests for a  character  from  the  communications
          port previously opened with "Copen", and returns that character if
          one if found. If no character is available, "Ctestc" returns -1.
    
    
    EXAMPLES:
    
        if((c = Ctestc()) == -1) {
            Cclose();
            abort("No character available"); }

    DISABLE                                                         DISABLE
    
    
    
    PROTOTYPE:
    
        disable();
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
             The "disable" function  disables  the  8086  interrupt  system,
          preventing the processor from servicing  interrupts.  It  is  used
          whenever the execution of an interrupt handler may interfere  with
          a particular operation.
    
             When this function is used, the  "enable"  function  should  be
          called as soon as possible after "disable". Failure to do this may
          result in loss of system  functions  performed  under  interrupts,
          such as timekeeping, and serial communications (Via MICRO-C serial
          drivers).
    
    
    EXAMPLES:
    
        disable();                  /* Disallow interrupts */
        Cflags &= ~TRANSPARENT;     /* Remove transparency */
        enable();                   /* Re-allow interrupts */

    ENABLE                                                           ENABLE
    
    
    
    PROTOTYPE:
    
        enable();
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
             The  "enable"  function  enables  the  8086  interrupt  system,
          allowing the processor to service interrupts. It should be  called
          as soon as possible following the use of the "disable" function.
    
    
    EXAMPLES:
    
        disable();                  /* Disallow interrupts */
        Cflags |= TRANSPARENT;      /* Force  transparency */
        enable();                   /* Re-allow interrupts */

    EXEC                                                               EXEC
    
    
    
    PROTOTYPE:
    
        int exec(char *exefile, char *args)
    
    
    ARGUMENTS:
    
        exefile - Full pathname of a '.COM' or '.EXE' file
        args    - Command tail containing arguments
    
    
    RETURN VALUE:
    
        0 if successful, otherwise an MS-DOS error code
    
    
    DESCRIPTION:
    
             The "exec" function causes MS-DOS to suspend the  execution  of
          the MICRO-C program, and then to execute the indicated  '.EXE'  or
          '.COM' program file. When that program  terminates,  execution  of
          the MICRO-C program will resume.
    
             This is a low level interface to the  MS-DOS  'EXEC'  function,
          and as such, it does not search your PATH, does not process '.BAT'
          files, nor provide any I/O redirection facilities. If you want  to
          make use of these features (which are provided by  'COMMAND.COM'),
          use the higher level 'SYSTEM' function.
    
    
    EXAMPLES:
    
        printf("Type 'EXIT' to return to the MICRO-C program\n");
        exec("C:\\COMMAND.COM", "");    /* Start up a sub-shell */

    FREE_SEG                                                       FREE_SEG
    
    
    
    PROTOTYPE:
    
        int free_seg(int segment)
    
    
    ARGUMENTS:
    
        segment - A previously allocated segment of memory
    
    
    RETURN VALUE:
    
        0       - The segment was released
        !0      - DOS error code
    
    
    DESCRIPTION:
    
             The "free_seg" function releases a segment of memory previously
          allocated by "alloc_seg", and returns it to the operating  system.
          This should be used whenever your  program  has  finished  with  a
          segment of extra memory which it has allocated.
    
    
    EXAMPLES:
    
        aseg = alloc_seg(4096);         /* Allocate a 64K segment */
        set_es(aseg);                   /* Set up extra segment */
        asm_func();                     /* Call assembler function */
        free_seg(aseg);                 /* Releas the memory */

    GET_ATTR                                                       GET_ATTR
    
    
    
    PROTOTYPE:
    
        int get_attr(char *pathname, int &attrs)
    
    
    ARGUMENTS:
    
        pathname- Name of file to get attributes of
        attrs   - Integer to receive attributes
    
    
    RETURN VALUE:
    
        0 if successful, otherwise an operating system error code
    
    
    DESCRIPTION:
    
             This function retreives the attributes of the specified file.
    
             The meaning of the individual bits  in  the  "attrs"  value  is
          defined in the "file.h" header file.
    
    
    EXAMPLES:
    
        get_attr("tempfile", &attributes);

    GET_CS                                                           GET_CS
    
    
    
    PROTOTYPE:
    
        int get_cs()
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        The current processor CODE segment
    
    
    DESCRIPTION:
    
             This  function  is  available  only  on  the  8086  family   of
          processors, and returns the current processor CODE segment.
    
    
    EXAMPLES:
    
        code_seg = get_cs();

    GET_DATE                                                       GET_DATE
    
    
    
    PROTOTYPE:
    
        get_date(int &day, int &month, int &year)
    
    
    ARGUMENTS:
    
        &day    - Address of integer to receive day (1-31)
        &month  - Address of integer to receive month (1-12)
        &year   - Address of integer to receive year (1980-2099)
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
             This function gets the current system date in day,  month,  and
          year.
    
    
    EXAMPLES:
    
        get_date(&day, &month, &year);
        printf("%s %u, %u", months[month], day, year);

    GET_DRIVE                                                     GET_DRIVE
    
    
    
    PROTOTYPE:
    
        int get_drive()
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        The currently active (default) disk drive (0=A, 1=B, 2=C, ...)
    
    
    DESCRIPTION:
    
             The "get_drive" function returns the drive index (0-n)  of  the
          currently active or "default" MS-DOS disk drive.
    
    
    EXAMPLES:
    
        old_drive = get_drive();
        set_drive(new_drive);

    GET_DS                                                           GET_DS
    
    
    
    PROTOTYPE:
    
        int get_ds()
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        The current processor DATA segment
    
    
    DESCRIPTION:
    
             This  function  is  available  only  on  the  8086  family   of
          processors, and returns the current processor DATA segment.
    
    
    EXAMPLES:
    
        data_seg = get_ds();

    GET_ES                                                           GET_ES
    
    
    
    PROTOTYPE:
    
        int get_es()
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        The current processor EXTRA segment
    
    
    DESCRIPTION:
    
             This  function  is  available  only  on  the  8086  family   of
          processors, and returns the current processor EXTRA segment.
    
    
    EXAMPLES:
    
        code_seg = get_es();

    GET_TIME                                                       GET_TIME
    
    
    
    PROTOTYPE:
    
        get_time(int &hour, int &minite, int &second)
    
    
    ARGUMENTS:
    
        &hour   - Address of integer to receive hour (0-23)
        &minite - Address of integer to receive minite (0-59)
        &second - Address of integer to receive second (0-59)
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
             This function gets the current system time  in  hours,  minites
          and seconds.
    
    
    EXAMPLES:
    
        get_time(&hour, &minite, &second);
        printf("%02:%02:%02", hour, minite, second);

    RESIZE_SEG                                                   RESIZE_SEG
    
    
    
    PROTOTYPE:
    
        int resize_seg(int segment, int size)
    
    
    ARGUMENTS:
    
        segment - A previously allocated segment of memory
        size    - Desired size (in 16 byte paragraphs)
    
    
    RETURN VALUE:
    
        0       - The segments size has been adjusted
        !0      - DOS error code
    
    
    DESCRIPTION:
    
             The "resize_seg" function provides a  method  of  changing  the
          size of a segment of memory previously allocated via  "alloc_seg".
          If not enough memory is available, the function will fail  with  a
          ono-zero return value.
    
             This function may also be used to adjust the memoey  allocation
          of the programs image, by passing it the segment  address  of  the
          programs own PSP. This value is available in the external variable
          "PSP".
    
             MICRO-C normally allocates 64K for  programs  compiled  in  the
          TINY model, and (64K + (256 byte PSP) + (size of executable code))
          for programs compiled in the SMALL model. This  allocation  should
          NEVER be reduced, however you  may  enlarge  it  if  your  program
          wishes to access additional data  immediately  following  its  own
          DATA/STACK segment.
    
    
    EXAMPLES:
    
        extern int PSP;
    
        main()
        {
            if(resize_seg(PSP, 8192))   /* Append 64K buffer */
                abort("Not enough memory!!!");
            ...     /* Remainder of program */
        }

    RESTORE_VIDEO                                             RESTORE_VIDEO
    
    
    
    PROTOTYPE:
    
        restore_video(char buffer[4006]);
    
    
    ARGUMENTS:
    
        buffer  - Video save area.
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
             The RESTORE_VIDEO function restores the contents and  state  of
          the  IBM  P.C.  video  display  to  the  state  it  was  in   when
          "SAVE_VIDEO" was executed. At the present time,  the  function  is
          effective only for  text  modes.  Graphics  screens  will  not  be
          restored, due to the high memory requirements.
    
             Although this function is useful in ANY program (to restore the
          DOS screen before termination), it is most useful in "POP-UP"  ram
          resident programs (See "TSR" function), to save the screen of  any
          application which may be running when you pop up.
    
             The video state is restored from the passed "buffer"  argument,
          which is 4006 bytes in size, and  must  have  been  filled  in  by
          "SAVE_VIDEO". It has the following format:
    
                  buffer[0]         - Video mode
                    "   [1]         - Video page
                    "   [2]         - 'X' cursor position
                    "   [3]         - 'Y' cursor position
                    "   [4]         - Ending line for cursor
                    "   [5]         - Starting line for cursor
                    "   [6-4005]    - Saved video screen contents
    
    
    EXAMPLES:
    
        popup_func()
        {
            save_video();
            perform_function();
            restore_video();
        }

    SAVE_VIDEO                                                   SAVE_VIDEO
    
    
    
    PROTOTYPE:
    
        save_video(char buffer[4006]);
    
    
    ARGUMENTS:
    
        buffer  - Video save area.
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
             The SAVE_VIDEO function saves the current contents and state of
          the IBM P.C. video display. The screen may be restored at any time
          using "RESTORE_VIDEO".  At  the  present  time,  the  function  is
          effective only for text modes. Graphics screens will not be saved,
          due to the high memory requirements.
    
             Although this function is useful in ANY program (to restore the
          DOS screen before termination), it is most useful in "POP-UP"  ram
          resident programs (See "TSR" function), to save the screen of  any
          application which may be running when you pop up.
    
             The video state is saved in the passed "buffer" argument, which
          is 4006 bytes in size, and has the following format:
    
                  buffer[0]         - Video mode
                    "   [1]         - Video page
                    "   [2]         - 'X' cursor position
                    "   [3]         - 'Y' cursor position
                    "   [4]         - Ending line for cursor
                    "   [5]         - Starting line for cursor
                    "   [6-4005]    - Saved video screen contents
    
    
    EXAMPLES:
    
        popup_func()
        {
            save_video();
            perform_function();
            restore_video();
        }

    SET_ATTR                                                       SET_ATTR
    
    
    
    PROTOTYPE:
    
        int set_attr(char *pathname, int attrs)
    
    
    ARGUMENTS:
    
        pathname- Name of file to get attributes of
        attrs   - New attributes
    
    
    RETURN VALUE:
    
        0 if successful, otherwise an operating system error code
    
    
    DESCRIPTION:
    
             This function sets the system attributes of the specified file.
    
             The meaning of the individual bits  in  the  "attrs"  value  is
          defined in the "file.h" header file.
    
    
    EXAMPLES:
    
        set_attr("tempfile", READONLY|HIDDEN);

    SET_DATE                                                       SET_DATE
    
    
    
    PROTOTYPE:
    
        set_date(int day, int month, int year)
    
    
    ARGUMENTS:
    
        day     - New day (1-31)
        month   - New month (1-12)
        year    - New year (1980-2099)
    
    
    RETURN VALUE:
    
        0       - Success
        -1      - Invalid date given
    
    
    DESCRIPTION:
    
             This function sets the current system date to day,  month,  and
          year.
    
    
    EXAMPLES:
    
        set_date(1, 1, 1980);   /* Set to Jan 1, 1980 */

    SET_DRIVE                                                     SET_DRIVE
    
    
    
    PROTOTYPE:
    
        int set_drive(int drive)
    
    
    ARGUMENTS:
    
        Drive   - New drive index (0=A, 1=B, 2=C ...)
    
    
    RETURN VALUE:
    
        The total number of "logical" disk drives in the system
    
    
    DESCRIPTION:
    
             The "set_drive" function sets the disk drive indicated  by  the
          "drive" index (0-x) to be the currently active or "default" MS-DOS
          disk drive.
    
    
    EXAMPLES:
    
        old_drive = get_drive();
        set_drive(new_drive);

    SET_ES                                                           SET_ES
    
    
    
    PROTOTYPE:
    
        int set_es(int segment)
    
    
    ARGUMENTS:
    
        segment - The 16 bit new segment value
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
             This  function  is  available  only  on  the  8086  family   of
          processors, and sets the processors EXTRA segment to the indicated
          value.
    
    
    EXAMPLES:
    
        set_es(get_ds());       /* Copy DATA to EXTRA segments */

    SET_TIME                                                       SET_TIME
    
    
    
    PROTOTYPE:
    
        set_time(int hour, int minite, int second)
    
    
    ARGUMENTS:
    
        hour    - New hour (0-23)
        minite  - New minite (0-59)
        second  - New second (0-59)
    
    
    RETURN VALUE:
    
        0       - Success
        -1      - Invalid time given
    
    
    DESCRIPTION:
    
             This function sets the current system time to "hour",  "minite"
          and "second".
    
    
    EXAMPLES:
    
        set_time(0, 0, 0);  /* Set to 00:00:00 (midnight) */

    TSR                                                                 TSR
    
    
    
    PROTOTYPE:
    
        tsr(&func, int hotkey, int alloc)
    
    
    ARGUMENTS:
    
        func    - Address of function to execute
        hotkey  - POP-UP activation hotkeys
        alloc   - Memory allocation
    
    
    RETURN VALUE:
    
        Function normally never returns, but if it does, an
        operating system error code is passed back.
    
    
    DESCRIPTION:
    
             The TSR function terminates the MICRO-C program, but leaves  it
          resident in memory. When the specified "HOT KEYS" are detected  on
          the IBM PC keyboard, the context of whatever program is running is
          saved, and the specified MICRO-C function  is  called.  When  that
          function returns, the interrupted program is resumed.
    
             When activated this way, THE "func" FUNCTION MUST NOT TERMINATE
          WITH "exit" or one of its related functions (abort etc.). THE ONLY
          WAY IT MAY TERMINATE IS TO "return" NORMALLY.
    
             The meaning of "hotkey" is defined in the "tsr.h" header file.
    
             The "alloc" paremeter specifies how much extra memory is to  be
          retained in the TSR image for use by the MICRO-C  stack  and  heap
          memory allocation functions. The "func"  function(s)  must  insure
          that the total amount of memory used by the  stack  and  calls  to
          "malloc" does not exceed this value.
    
             NOTE: "malloc" will fail if the heap grows to within 1K of  the
          stack pointer.
    
             All memory used by code, global variables,  string  space,  and
          "malloc"  calls  prior  to  the  use  of  "tsr"  is  automatically
          retained, and should not be included in the "alloc" value.
    
             TSR programs which perform screen I/O should take care to  save
          and restore the screen contents when popping up and down.
    
    
    EXAMPLES:
    
        tsr(&popup_func, ALT+L_SHIFT, 1024);

    VCLEAR_BOX                                                   VCLEAR_BOX
    
    
    
    PROTOTYPE:
    
        vclear_box(int x, int y, int w, int h)
    
    
    ARGUMENTS:
    
        x       - COLUMN of top left corner of box
        y       - ROW of top left corner of box
        w       - Width of box (columns)
        h       - Height of box (rows)
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
             This function clears a box of the specified height  and  width,
          at the indicated 'X' and 'Y'  coordinates,  on  the  IBM-PC  video
          screen using the block graphics  characters.  The  entire  box  is
          cleared to spaces.
    
             "VOPEN" MUST be called prior to using this function.
    
    
    EXAMPLES:
    
        vclear_box(21, 11, 8, 3);   /* Clear a BOX */

    VCLEOL                                                           VCLEOL
    
    
    
    PROTOTYPE:
    
        vcleol()
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
             This function clears the IBM PC video screen from  the  current
          cursor position to the end of a line.
    
             You must "#include video.h", and execute "VOPEN" prior to using
          this function.
    
    
    EXAMPLES:
    
        vprintf("Input> ");     /* Display a prompt */
        vcleol();               /* Clear remainder of input line */

    VCLEOS                                                           VCLEOS
    
    
    
    PROTOTYPE:
    
        vcleos()
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
             This function clears the IBM PC video screen from  the  current
          cursor position to the end of a screen.
    
             "VOPEN" MUST be called prior to using this function.
    
    
    EXAMPLES:
    
        vgotoxy(0, 10);         /* position at line 11 */
        vcleos();               /* Clear lower part of screen */

    VCLSCR                                                           VCLSCR
    
    
    
    PROTOTYPE:
    
        vclscr()
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
             This function clears the entire IBM PC video screen and  resets
          the cursor position to the top left hand corner.
    
             "VOPEN" MUST be called prior to using this function.
    
    
    EXAMPLES:
    
        if(c = 0x1b) {          /* Escape command */
            vclscr();       /* Clear the screen */
            vprintf("%s has terminated\n", argv[0]);
            exit(-1); }

    VCURSOR_BLOCK                                             VCURSOR_BLOCK
    
    
    
    PROTOTYPE:
    
        vcursor_block()
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
             This function enables (turns on) display of the cursor  on  the
          IBM PC video display. The  cursor  is  shown  as  flashing  block,
          occupying the entire character window.
    
             "VOPEN" MUST be called prior to using this function.
    
    
    EXAMPLES:
    
        if(insert)              /* Test insert mode flag */
            vcursor_block();    /* Indicate inserting with block cursor */
        else
            vcursor_line();     /* Indicate overwrite with line cursor */

    VCURSOR_LINE                                               VCURSOR_LINE
    
    
    
    PROTOTYPE:
    
        vcursor_line()
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
             This function enables (turns on) display of the cursor  on  the
          IBM PC video display. The cursor is shown  as  a  single  flashing
          line, at the bottom of the character window.
    
             "VOPEN" MUST be called prior to using this function.
    
    
    EXAMPLES:
    
        vcursor_line();     /* Re-enable the cursor */
        exit(0);            /* And terminate */

    VCURSOR_OFF                                                 VCURSOR_OFF
    
    
    
    PROTOTYPE:
    
        vcursor_off()
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
             This function inhibits (turns off) display of the cursor on the
          IBM PC video display. This affects the cursor display only, screen
          output will  continue  to  be  displayed  at  the  correct  cursor
          position.
    
             "VOPEN" MUST be called prior to using this function.
    
    
    EXAMPLES:
    
        vclscr();           /* Clear screen */
        vcursor_off();      /* Inhibit cursor */
        vmenu(10, 10, main_menu, 0, &index);    /* Present main menu */

    VDRAW_BOX                                                     VDRAW_BOX
    
    
    
    PROTOTYPE:
    
        vdraw_box(int x, int y, int w, int h)
    
    
    ARGUMENTS:
    
        x       - COLUMN of top left corner of box
        y       - ROW of top left corner of box
        w       - Width of box (columns)
        h       - Height of box (rows)
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
             This function draws a box of the specified height and width, at
          the indicated 'X' and 'Y' coordinates, on the IBM-PC video  screen
          using the block graphics characters.
    
             "VOPEN" MUST be called prior to using this function.
    
    
    EXAMPLES:
    
        vdraw_box(20, 10, 10, 5);   /* Draw a BOX */

    VERSION                                                         VERSION
    
    
    
    PROTOTYPE:
    
        int version()
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        MS-DOS operating system version number
    
    
    DESCRIPTION:
    
             The "version" function is  available  only  under  MS-DOS,  and
          returns the version number of the operating system.
    
             The higher 8 bits of the returned  value  indicates  the  MAJOR
          version number ('3' in DOS 3.1)
    
             The lower 8 bits of the  returned  value  indicates  the  MINOR
          version nuber ('1' in DOS 3.1).
    
    
    EXAMPLES:
    
        if(version() < 0x031E)
            abort("Requires DOS 3.30 or higher\n");

    VGETC                                                             VGETC
    
    
    
    PROTOTYPE:
    
        int vgetc()
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        0-127   - ASCII value of key pressed
        < 0     - Special function key as defined in "video.h"
    
    
    DESCRIPTION:
    
             The "vgetc" function waits until a key is pressed on the system
          console, and returns its value.
    
             Note that due to the buffering of the  IBM-PC  keyboard,  every
          keypress will be reported, even if the VGETC  function  is  called
          after a key is pressed and released.
    
    
    EXAMPLES:
    
        switch(vgetc()) {       /* Handle input keys
                . . .
        }

    VGETS                                                             VGETS
    
    
    
    PROTOTYPE:
    
        int vgets(int x, int y, char *prompt, char *field, int width)
    
    
    ARGUMENTS:
    
        x       - COLUMN of top left corner of input box
        y       - ROW of top left corner of input box
        prompt  - String to prompt with
        field   - String to receive the data
        width   - Width in characters of input field
    
    
    RETURN VALUE:
    
        0   - Selection was made and ENTER pressed.
        !0  - Input was aborted via ESCAPE key.
    
    
    DESCRIPTION:
    
             The "vgets" function draws a box on the  video  screen  at  the
          specified X and Y coordinates, then prompts for  and  receives  an
          input string in the box. The box is drawn large enough to  contain
          the prompt and the specified width of input field. The  prompt  is
          displayed at the left hand side of the  box,  and  the  cursor  is
          positioned immediatly following it, at  the  start  of  the  input
          field.
    
             The "field" parameter is the address of a  character  array  to
          receive the input string. The previous value of the "field"  array
          is inserted into the input box when VGETS is invoked.  If  you  do
          not want to display  an  old  value,  you  should  set  the  first
          character pointed to by field to zero, before calling VGETS.
    
             When entering the  string,  the  user  may  use  the  following
          special keys to edit the input field:
    
                Right Arrow - Move forward one character
                Left  Arrow - Move backward one character
                Delete      - Delete the character under the cursor
                Backspace   - Move backward one character and delete.
                Home        - Move to beginning of string
                End         - Move to end of string
                PgUp        - Clear (erase) entire string
                PgDn        - Clear from cursor to end of string
                Enter       - Accept (enter) the string
                ESC         - Abort the input request
    
             All data entered in the input box is  inserted  into  any  data
          which is already present.

    
    
    
    EXAMPLES:
    
        name[0] = 0;
        if(vgets(10, 10, "Your name?", name, 30))
            return;     /* Aborted, exit to higher level */

    VGOTOXY                                                         VGOTOXY
    
    
    
    PROTOTYPE:
    
        vgotoxy(int x, int y)
    
    
    ARGUMENTS:
    
        x       - New COLUMN (0-79)
        y       - New ROW    (0-24)
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
             The "vgotoxy" function positions the cursor on the IBM-PC video
          screen. Any further display output will occur at the new  ROW  and
          COLUMN on the screen.
    
             The extern "int" variable "V_XY" may be referenced to  read  or
          set the current X/Y position. The higher 8 bits  contain  the  'Y'
          coordinate, and the lower 8 bits contain the  'X'  coordinate.  If
          this variable is  used  to  set  (restore)  the  cursor  position,
          "vupdatexy" must then be called to position the physical cursor.
    
             "VOPEN" MUST be called prior to using this function.
    
    
    EXAMPLES:
    
        for(i=0; i<24; ++i) {   /* Draw a diagonal line of 'X's */
            vgotoxy(i, i);
            vputc('X'); }

    VMENU                                                             VMENU
    
    
    
    PROTOTYPE:
    
        vmenu(int x, int y, char *names[], char erase, int &index)
    
    
    ARGUMENTS:
    
        x       - COLUMN of top left corner of menu box
        y       - ROW of top left corner of menu box
        names   - Array to menu selection text (last entry = 0)
        erase   - 1=Erase BOX after selection is made
        index   - Address of message selection index variable
    
    
    RETURN VALUE:
    
        0   - Selection was made and ENTER pressed.
        !0  - Menu was aborted via ESCAPE key.
    
    
    DESCRIPTION:
    
             The "vmenu" function displays a list of menu items enclosed  in
          a box on the IBM-PC video screen at the specified ROW  and  COLUMN
          address. The user may use the UP,  DOWN,  HOME  and  END  keys  to
          select an entry by moving the INVERSE VIDEO selection cursor.
    
             When the desired selection is under the cursor,  the  selection
          is made by pressing the ENTER key.
    
             At any time the menu selection may be canceled by pressing  the
          ESCAPE key.
    
             The "names" argument must be a pointer to an array of character
          strings which are the selections to display. This array  MUST  end
          with a zero (0) element to indicate the end of the list.
    
             The "erase" flag indicates that the menu box should be  cleared
          to blanks when the selection is made. If "erase=0", the  menu  box
          is left on the screen, WITHOUT  the  selection  cursor,  with  the
          selected entry marked by '>' and  '<'.  The  menu  box  is  always
          erased when the menu is aborted with the ESCAPE key.
    
             The "index" argument is the address of an "int" variable  which
          contains the position of the selection cursor. It  controls  where
          the selection cursor  will  appear  when  the  function  is  first
          invoked (0 = first entry), and also is assigned  the  position  of
          the selection cursor when the selection is made.

    
    
    
    EXAMPLES:
    
        char *names[] = { "One", "Two", "Three", "Four", "Five", 0 };
            . . .
        index = 0;
        if(vmenu(10, 10, names, 0, &index))
            return;         /* Aborted, exit to higher level */
        switch(index) {     /* Handle selection */
            . . .
        }

    VMESSAGE                                                       VMESSAGE
    
    
    
    PROTOTYPE:
    
        vmessage(int x, int y, char *string)
    
    
    ARGUMENTS:
    
        x       - COLUMN of top left corner of message box
        y       - ROW of top left corner of message box
        string  - Message to display
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
             The "vmessage" function displays a text string surrounded by  a
          BOX, on the IBM-PC video screen, at the specified ROW  and  COLUMN
          address.
    
             "VOPEN" MUST be called prior to using this function.
    
    
    EXAMPLES:
    
        vmessage(20, 20, "Press any KEY to continue");
        get_key();
        vclear_box(20, 20, 26, 2);

    VOPEN                                                             VOPEN
    
    
    
    PROTOTYPE:
    
        vopen()
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
             This function initializes the IBM-PC video display adapter  for
          use with the MICRO-C video library functions.  It  determines  the
          adapter type (COLOR ot MONOCHROME),  sets  up  internal  variables
          with information required by the other video functions, and clears
          the video screen.
    
             This function MUST be called before  any  of  the  other  video
          functions in the library are used.
    
             After "vopen" is called, the extern "int" variable "V_BASE" may
          be referenced to determine the memory segment of the video display
          (B000 for monochrome, B800 for color).
    
             Any program using the video library functions must include  the
          "video.h" header file.
    
    
    EXAMPLES:
    
        vopen();

    VPRINTF                                                         VPRINTF
    
    
    
    PROTOTYPE:
    
        register vprintf(char *format, arg, ...)
    
    
    ARGUMENTS:
    
        format  - Pointer to format string
        arg     - Argument as determined by format string
        ...     - Additional arguments may be required
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
             This function performs exactly as the "PRINTF" function in  the
          standard function library, except that it outputs directly to  the
          video screen using the video interface library routines.
    
             This function should be used in  preference  to  "PRINTF"  when
          using the video function library since "PRINTF" will not move  the
          video librarys cursor.
    
             NOTE: This function uses a variable number  of  arguments,  and
          must be declared as "register" (See "video.h").
    
             "VOPEN" MUST be called prior to using this function.
    
    
    EXAMPLES:
    
        vgotoxy(0, 0);
        vprintf("Screen %u", screen);

    VPUTC                                                             VPUTC
    
    
    
    PROTOTYPE:
    
        vputc(char chr)
    
    
    ARGUMENTS:
    
        chr     - Character to display
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
             This function displays a character on the video screen  at  the
          current cursor position.
    
             Characters are output in "tty" fashion, with proper handling of
          control codes such as CARRIAGE-RETURN,  LINE-FEED  and  BELL.  The
          screen will scroll upwards when a NEWLINE is printed on the bottom
          line of the screen, or when the bottom line wraps  around  to  the
          next.
    
             Although only the lower 8 bits of  a  passed  value  are  used,
          "vputc" will not perform ANY output translations  if  any  of  the
          upper 8 bits are set. This provides a  method  of  displaying  the
          video characters represented by control codes such as NEWLINE, and
          BACKSPACE.
    
             The external "char" variable "V_ATTR" may be used  to  set  the
          video attribute used by "VPUTC" to  display  the  character.  This
          value is written to the attribute  location  associated  with  the
          character on the video display hardware. Its effect  is  dependant
          on the video adapter in use. The "video.h"  header  file  contains
          definitions of the attribute bits for use on "standard" monochrome
          and color displays.
    
    
             "VOPEN" MUST be called prior to using this function.
    
    
    EXAMPLES:
    
        vputc(0x0A);            /* Line-feed, advance cursor */
        vputc(0x0A | 0xff00);   /* Display 0x0A character code */

    VPUTF                                                             VPUTF
    
    
    
    PROTOTYPE:
    
        vputf(char *string, int width)
    
    
    ARGUMENTS:
    
        string  - Pointer to character string
        width   - Width of output field
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
             The "vputf" function outputs a character string to  the  IBM-PC
          video screen using the video library functions.
    
             The string is left justified in a field of the specified width.
          If the string is shorter than "width", the field  is  padded  with
          blanks. If the string  is  longer  than  "width",  the  output  is
          truncated.
    
             "VOPEN" MUST be called prior to using this function.
    
    
    EXAMPLES:
    
        vputf(message, 10); 

    VPUTS                                                             VPUTS
    
    
    
    PROTOTYPE:
    
        vputs(char *string)
    
    
    ARGUMENTS:
    
        string  - Pointer to character string
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
             The "vputs" function outputs a character string to  the  IBM-PC
          video screen using the video library functions.
    
             "VOPEN" MUST be called prior to using this function.
    
    
    EXAMPLES:
    
        vputs(message);

    VTSTC                                                             VTSTC
    
    
    
    PROTOTYPE:
    
        int vtstc()
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        0       - No key pressed
        1-127   - ASCII value of key pressed
        < 0     - Special function key as defined in "video.h"
    
    
    DESCRIPTION:
    
             The "vtstc" function tests for a  key  pressed  on  the  system
          console, and returns its value.  A  returned  value  of  zero  (0)
          indicates that no key was found to be pressed.
    
             Note that due to the buffering of the  IBM-PC  keyboard,  every
          keypress will be reported, even if the VTSTC  function  is  called
          after a key is pressed and released.
    
    
    EXAMPLES:
    
        if(vtstc() == 0x1B) /* exit loop on ESCAPE key */
            break;

    VUPDATEXY                                                     VUPDATEXY
    
    
    
    PROTOTYPE:
    
        vupdatexy()
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
             This function updates the real X/Y cursor position on the video
          screen to reflect the "logical" position where the next  character
          will be output.
    
             The MICRO-C video library uses a BIOS  interrupt  (INT  10)  to
          position the cursor, which is quite slow, compared to the speed of
          the library video routines. To prevent this from slowing down  the
          video output, the cursor is only physically re-positioned  when  a
          "vgotoxy" or a "vgetc" is executed.
    
             This allows the library routines to  run  at  full  speed,  and
          still put the cursor in the right place when output stops  and  an
          input request is made.
    
             A side effect of this is that the cursor on the screen will not
          appear to move unless you call "vgotoxy"  or  "vgetc".  This  only
          affects the physical cursor on the screen, MICRO-C  maintains  its
          own internal cursor location which it uses to determine  where  on
          the screen the next write will occur.
    
             Some applications which run in real time (Such  as  a  terminal
          emulator) do not  call  "vgetc",  but  use  "vtstc"  to  poll  the
          keyboard on a regular basis. In this case, the "vupdatexy" routine
          should be called any time that the visual position of  the  cursor
          is important.
    
             "VOPEN" MUST be called prior to using this function.
    
    
    EXAMPLES:
    
        vupdatexy();        /* position the cursor *
        c = vtstc();        /* Test for a character */




                                    MICRO-C

                               TABLE OF CONTENTS


                                                                         Page

     1. INTRODUCTION                                                        1

        1.1 Code Portability                                                2
        1.2 Compiler Portability                                            2
        1.3 The MCC command                                                 3

     2. THE MICRO-C PROGRAMMING LANGUAGE                                    4

        2.1 Constants                                                       4
        2.2 Symbols                                                         4
        2.3 Arrays & Pointers                                               7
        2.4 Functions                                                       7
        2.5 Control Statements                                              8
        2.6 Expression Operators                                           10
        2.7 Preprocessor Commands                                          12
        2.8 Error Messages                                                 13
        2.9 Quirks                                                         17

     3. ADVANCED TOPICS                                                    20

        3.1 Conversion Rules                                               20
        3.2 Assembly Language Interface                                    21
        3.3 Compiling for ROM                                              24

     4. PORTING THE COMPILER                                               25

        4.1 The "io" module                                                26
        4.2 The "code" module                                              28
        4.3 The "compile" module                                           33
        4.4 Porting without a compiler                                     34
        4.5 Porting without a linker                                       34
        4.6 Optimization Techniques                                        35

     5. THE MICRO-C PREPROCESSOR                                           38

        5.1 The MCP command                                                39
        5.2 Preprocesor Commands                                           40
        5.3 Error messages                                                 43

     6. THE MICRO-C OPTIMIZER                                              45

        6.1 The MCO command                                                45
        6.2 Porting to a new processor                                     46

     7. THE COMMAND CO-ORDINATOR                                           47

        7.1 The CC command                                                 47

    MICRO-C                                                Table of Contents

                                                                         Page
        7.2 Using multiple object modules                                  48

     8. THE MAKE UTILITY                                                   49

        8.1 MAKEfiles                                                      49
        8.2 Directives                                                     52
        8.3 The MAKE command                                               53
        8.4 The TOUCH command                                              54

     9. THE SOURCE LINKER                                                  55

        9.1 The SLINK Command                                              55
        9.2 The External Index File                                        56
        9.3 Multiple source files                                          57
        9.4 Source file information                                        57
        9.5 The SINDEX utility                                             59

     10. LIBRARY FUNCTIONS                                                 60

        10.1 Standard Library Functions                                    60
        10.2 IBM-PC/MS-DOS Library Functions                               61