HPSORT

                           Pen Plotter Pen Motion Optimizer
                                         and
                                   File Compressor 
                            for HPGL Compatibile Plotters



                                     CNT Software
                                  1615 Highland Ave.
                                Janesville, Wis 53545


                        Copywrite 1991.  All Rights Reserved.




          Any trademarks metioned in this document are the property of
          there respective companies.




























                                                                          1









                                  Table of Contents


          1.0 Introduction  . . . . . . . . . . . . . . . . . . . . . .   3

          1.1 Will HPSORT work with my software?  . . . . . . . . . . .   3

          2.0 Legal Stuff . . . . . . . . . . . . . . . . . . . . . . .   4
               2.1 Warranty . . . . . . . . . . . . . . . . . . . . . .   4
               2.2 License  . . . . . . . . . . . . . . . . . . . . . .   5
               2.3 Ordering Information . . . . . . . . . . . . . . . .   5

          3.0 Installation  . . . . . . . . . . . . . . . . . . . . . .   6
               3.1 System Requirements  . . . . . . . . . . . . . . . .   6
               3.1 Installation . . . . . . . . . . . . . . . . . . . .   6

          4.0 Configuration . . . . . . . . . . . . . . . . . . . . . .   6
               4.1 Control Keys   . . . . . . . . . . . . . . . . . . .   7
               4.2 Opening Configuration Menu . . . . . . . . . . . . .   8
                    4.2.1 Edit Configuration Data . . . . . . . . . . .   9
                    4.2.2  General Data Editing . . . . . . . . . . .    10
                    4.2.3 Swapping Polylines to Disc  . . . . . . . .    16
                    4.2.4 Label commands  . . . . . . . . . . . . . .    17
                    4.2.5 Serial Input / Output Communication Parame-
                         ters . . . . . . . . . . . . . . . . . . . .    20
                    4.2.6  Disc Parameters  . . . . . . . . . . . . .    21
               4.3 Default Settings . . . . . . . . . . . . . . . . .    23

          4.4 Sort / Compress . . . . . . . . . . . . . . . . . . . .    24
               4.5 Save . . . . . . . . . . . . . . . . . . . . . . .    24
               4.6 Quit . . . . . . . . . . . . . . . . . . . . . . .    24

          5.0 Operation . . . . . . . . . . . . . . . . . . . . . . .    24
               5.1 Theory of Operation  . . . . . . . . . . . . . . .    25
               5.2 HPSORT & Desqview  . . . . . . . . . . . . . . . .    26

          6.0 problems  . . . . . . . . . . . . . . . . . . . . . . .    26
               6.1 Error Messages . . . . . . . . . . . . . . . . . .    26
               6.2 Incompatibilities  . . . . . . . . . . . . . . . .    27
               6.3 How to contact CNT Software  . . . . . . . . . . .    27

          Order Form  . . . . . . . . . . . . . . . . . . . . . . . .    28










                                                                          2










          1.0 Introduction


          HPSORT sorts and compresses plot files for Hewlett Packard and
          compatible pen plotters using the HPGL (Hewlett Packard Graphics
          Language) language.  The sorting function initially analyzes the
          plot file produced by a CAD package.  Then it creates a new file
          of the same plot that saves 10% to 30% of the plotting time. 
          While creating this file, HPSORT writes a "denser" sequence of
          instructions reducing the file to about 50% to 60% of it's
          original size.

          For those persons communicating with a plotting service bureau,
          the output files may be automatically compressed using PKZIP, ARC
          or other similar program.  The resulting output files are typic-
          ally be 15% of original file size.  Service bureau's will supply
          compression program information to use.

               How does HPSORT perform this magic on the plot files?  

          Most CAD packages do not sort plotter files for minimum pen
          motion and plot time.  They typically create the plot in the
          order that the operator created the file.  Most CAD packages do
          not optimize pen motion because this procedure requires a sig-
          nificant amount of processing time and RAM memory in the proces-
          sor.  

          HPSORT works well with software that are capable of producing
          HPGL plot files.  It will be a judgement call for each user if
          the benefits of HPSORT are worth the computing time costs.  It
          will depend on the size of the plot files, the speed of your
          plotter and the speed of your computer.  

          1.1 Will HPSORT work with my software?

          HPSORT does not work equally well with all software that is
          capable of generating a plot file.  It is optimized to work with
          those instructions that are commonly used by CAD and other
          Graphics software.  

          Most of these packages only use a subset of the full instruction
          set available.  It is this instruction set the HPSORT uses.  For
          instructions outside of this subset, HPSORT outputs all of the
          data it has read in, then copies that instruction to the output. 
          It then begins the sorting the rest of the input file.






                                                                          3








          HPSORT does not work the following two types of software:

            o  If the software does a lot of pen changing,  HPSORT probably
               will not work very well (although try it).

            o  It does not work with Microsoft Windows 3.x.  Microsoft uses
               features of the HPGL language that work with the plotters,
               but are contrary to the documentation in HP's manuals. 
               HPSORT does not understand the syntax as of yet.

          Future versions will correct these exceptions.

          For a list of software the HPSORT works with, run the config-
          uration utility HP_CFG.  If the list does not contain your
          software, try using the generic settings.  For well behaved pack-
          ages, you should have no problems.  Either way, if either it
          works or not, please let the author know of your experience.  We
          will update the list of packages.

          If it does not,  it is usually a very simple thing to correct
          (and I will).  Refer to Section 6.3 of this document on how to
          contact the author.  If HPSORT does not work, we would appreciate
          getting a sample of your more complicated drawings to test rather
          than just a single drawing.


          2.0 Legal Stuff


          2.1 Warranty

          The CNT Software makes no warranty of any kind, express or
          implied,including without limitation, any warranties of merchan-
          tability and/or fitness for a particular purpose.  CNT Software
          shall not be liable for any damages, whether direct, indirect,
          special or consequential arising from a failure of this program
          to operate in the manner desired by the user.  CNT Software shall
          not be liable for any damage to data or property which may be
          caused directly or indirectly by the use of this program.

               IN NO EVENT WILL CNT SOFTWARE BE LIABLE TO YOU FOR ANY
               DAMAGES, INCLUDING ANY LOST PROFITS, LOST SAVINGS OR
               OTHER INCIDENTAL OR CONSEQUENTIAL DAMAGES A RISING OUT
               OF YOUR USE OR INABILITY TO USE THE PROGRAM, OR FOR ANY
               CLAIM BY ANY OTHER PARTY.








                                                                          4








          2.2 License

          HPSORT is not, and has never been in the Public Domain.  HPSORT
          is not free.

          Non-registered users are granted a limited, 90-day  license to
          determine whether or not the program meets their needs.  Con-
          tinued use of HPSORT beyond the 90-day evaluation time period
          requires registration of the program.  Use of non-registered
          copies of HPSORT beyond the original evaluation period is strict-
          ly prohibited.

          Copying and distributing HPSORT to others, is subject to the
          above restrictions and the following:

               o    HPSORT must be copied in unmodified form, including the
                    file containing this license information.

               o    No copying fee of any type may be assessed other than
                    basic charges for the cost of the copying medium.

               o    Distribution of HPSORT  with any other software or
                    hardware product(s) without the express written permis-
                    sion of CNT Software.

               o    Sysops (bulletin board SYStem Operators) may make
                    HPSORT available for downloading by their users as long
                    as all above conditions are met.  

               o    Commercial Distributors of Public Domain, Shareware, or
                    User-Supported software may distribute HPSORT subject
                    to the above conditions only after getting written
                    permission from CNT Software and filling out a regis-
                    tration form for upgrade notifications.  

          2.3 Ordering Information

          When you register your copy of HPSORT, you are granted a license
          to use the program as you desire.  There are several advantages
          to registering your copy of HPSORT:

               o    Copy of the latest version of HPSORT
               o    Printed Manual
               o    E-Mail Support   No problem is too big or small, but
                    you must be a registered user to get support.
               o    Notification of major releases with reduced upgrade
                    costs.
               o    You are contributing towards user supported software.

          To register HPSORT, please send the completed registration form
          at the end of this document.


                                                                          5








          3.0 Installation


          3.1 System Requirements

               o    HPSORT requires an IBM PC,XT,AT,PS/2 or IBM
                    compatible computer with at least 384K RAM.
               o    Math coprocessor is highly recommended.  A 12mhz 286 
                    287 processor combination will preform equal to a 25mhz
                    386 processor without a coprocessor.


          3.1 Installation 


          HPSORT is distributed with the following files -

               o    README.HST     Read me first file
               o    HPSORT.EXE     Sorting and Compression Program
               o    HP_CFG.EXE     Configuration Program for HPSORT
               o    HPSORT.HLP     Help file for HP_CFG.EXE
               o    HPSORT.DOC     This document

          Any missing files constitutes an incomplete copy.

          Copy the files into either a separate directory or the current
          CAD program's directory on your hard drive.

          Run HP_CFG  to create the configuration file (HPSORT.CFG) that
          HPSORT requires for execution.  The configuration file can either
          be in the same directory as HPSORT or your current directory.  

          It is possible to have multiple configurations for different
          applications.  Do this by copying the "master" or "initial"
          configuration file into the directory of the current application. 
          While in this directory, run HP_CFG to edit the parameters.

          4.0 Configuration

          HP_CFG is the configuration utility for HPSORT.  This config-
          uration program "tunes" HPSORT to your preferences.  It stores
          your choices in the file HPSORT.CFG.   This configuration file
          can be anywhere on your system as long as it is either in the
          current directory or in a directory listed in the path.

          All screens contain two status lines that appear on lines 23 and
          25 of the display.  Line 23 is a message that explains the menu
          option or the data field that the cursor is at.  Line 25 is the
          current "sort & compress" or "compress only" mode (see section
          4.4).



                                                                          6








          4.1 Control Keys 

          HP_CFG uses the following control keys:

          Arrow Keys Moves the cursor between different menu or data items.

          BACKSPACE Deletes the character to the left of the cursor and
                    moves the cursor one space to the left.

          DELETE    When editing data, deletes the character the cursor is
                    on.

          ENTER     When on a menu item, it executes the item.  When on a
                    data field, stores that data in the field, then moves
                    the cursor to the next field.  

          ESC       Exits the active data, help or menu screen.

          F1        Displays a help message.

          INSERT    Toggles Insert Mode.  In insert mode, characters are
                    inserted at the current cursor location.  Any trailing
                    characters are pushed to the right and may be pushed
                    out of the field and lost.

          PAGE UP   Used on help screens to look at the previous page.

          PAGE DOWN Used on help screens to look at the next page.

























                                                                          7









          4.2 Opening Configuration Menu

          Start this program  by typing HP_CFG and pressing the ENTER key
          from the DOS prompt.

          After the HP_CFG opening screen, the following screen will
          appear:



            ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄHPSORT Configuration MenuÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
            ³Edit  Default  Sort  Compress  Save  Quit                ³
            ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ







            Select Data to Edit

            Sort and Compress Output






          This is the primary menu.  Use the arrow keys, to select the
          desired option, then press ENTER.  

          Warning:  Pressing ESC key from this menu causes HP_CFG
                    to abort to MS-DOS.  Changes are not saved.

          EDIT      This selects a menu that permits editing of the para-
                    meters. Refer to Page #8

          DEFAULT   For the listed CAD packages, HP_CFG can preconfigure
                    most parameters for you.  This option selects the menu
                    that chooses which package.

          SORT      Configures HPSORT to sort and compress plot files. 
                    This is the default mode.

          COMPRESS  Configures HPSORT to compress a plot file.  The out-
                    putted file is not an exact representation of the input
                    file.  HPSORT draws text using the built in plotter
                    fonts and lines separately.



                                                                          8








          SAVE      Saves the configuration to file HPSORT.CFG in the
                    current directory.

          QUIT      Exits HP_CFG without performing a save.


          4.2.1 Edit Configuration Data

          After selecting EDIT on the opening menu, the following menu will
          appear:


            ÚÄÄÄÄÄÄÄÄÄÄÄÄHPSORT Configuration MenuÄÄÄÄÄÄÄÄ¿
            ³Edit  Default  Sort  Compress  Save  Quit    ³
            ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
            ³General Data   ³
            ³Swap File      ³
            ³Labels         ³
            ³Serial Port    ³
            ³Disc Parameters³
            ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ








          Options are


          General Data   Controls the processing of lines.  Adjust entries
                         here with care.

          Swap File      HPSORT can use a disc to expand its sorting capa-
                         city.

          Labels         Controls drawing of text using the built in plot-
                         ter fonts.

          Serial Port    Controls how HPSORT buffers and/or configures COM
                         ports.

          Disc Parameters Controls miscellaneous disc and compression op-
                         tions.







                                                                          9








          4.2.2  General Data Editing

          These parameters control how the HPSORT draws lines, arcs and
          circles.  They can directly affect plot quality, so adjust values
          with care.



            ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍHPSORT Vector Parameter SettingÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
            º                                                           º
            ºNear Zero Move Delta......  0.010mm                        º
            ºPen Width Move Delta......  0.030mm                        º
            ºShort Near Zero Length.....   5.00mm                       º 
            ºMax. Numb Relative Moves.    5                             º
            ºCircle Check Radius.......  5.000mm                        º
            ºMax. Relative Move.......  16000                           º
            º  The following two lines are primarily for persons using  º
            º  ORCAD.  This has to do with how dashed lines are         º
            º  implemented.  Refer to the manual for proper settings.   º
            º                                                           º
            ºLine Type Divider.........  3.500                          º
            ºIgnore IP Commands..Y/N...  YES                            º
            º                                                           º
            º                                                           º
            ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼









          Parameters

          Near Zero Move Delta

               This parameter drops unnoticeable short moves.  It controls
               the pen motion from the end of one vector to the start of
               the next.  The parameter states: 

                    When the end of the vector just drawn is closer
                    than this distance from the starting point of the
                    next vector, the pen will not move to the starting
                    point of the next vector.







                                                                         10








               As an example consider the following sequence:

               a.   Move with pen up to position #1.
               b.   Lower the pen and draw a line from point #1 to #2.
               c.   Raise the pen up and move to position #3.
               d.   Lower the pen and draw a line from point #3 to #4.

               The two lines from #1 to #2






                                             Example Plot of Two Lines
                                             Close Together#1--------------------#2
                                                     

                                                                          
                                                                #4---#3and from #3 to #4 would be
               drawn as shown in figure to
               the right.

               This is how they will appear
               when the distance from
               Points #2 to #3 is larger
               than this parameter.



               When the distance between points #2 and #3 is less than or
               equal to this parameter, then above example would generate
               the following sequence:

               a.   Move with pen up to position #1.
               b.   Lower the pen and draw a line from point #1 to #(2&3).
               d.   Lower the pen and draw a line from point #(2&3) to #4.

               Note in figure to right
                                          #1-------------------+#(2&3)
                                                              /
                                                             /
                                                            #4that a single point
               replaces points #2 and
               #3.  This effect
               noticed on parallel
               lines drawn close
               together, but still
               separate.
                
               Typical value is 1/10 smallest pen size used.  For 0.35mm
               pen would be 0.035mm.  Range is 0 to 1.5mm.

          Pen Width Move Delta

               This parameter removes pen up/down motions that are so short
               that they are unnoticeable.  Plotting speed is increased
               because the pen is not lifted as much.  HPSORT does this by
               drawing a line between the two points that should not be
               there.   When this parameter is set correctly, the line is
               unnoticeable.   This parameter says: 

                    When the end of the vector just drawn is closer
                    than this distance from the starting point of the
                    next vector, a line  connects the points without
                    the pen lifting from the paper.

                                                                         11








               As an example consider the following sequence:

               a.   Move with pen up to position #1.
               b.   Lower the pen and draw a line from point #1 to #2.
               c.   Raise the pen up and move to position #3.
               d.   Lower the pen and draw a line from point #3 to #4.

               The two lines from #1 to #2






                                             Example Plot of Two Lines
                                             Close Together#1--------------------#2
                                                     

                                                                          
                                                                #4---#3and from #3 to #4 would be
               drawn as shown in figure to
               the right.

               This is how they will appear
               when the distance from
               Points #2 to #3 is larger
               than this parameter.

               When the distance between
               points #2 and #3 is less than or equal to this parameter,
               then above example would generate the following sequence:

               a.   Move with pen up to position #1.
               b.   Lower the pen and draw a line from point #1 to #2.
               c.   Lower the pen and draw a line from point #2 to #3.
               d.   Lower the pen and draw a line from point #3 to #4.

               The figure to right is how
                                               #1-------------------+#2
                                                                    | 
                                                                    |
                                                                    |     
                                                               #4---+#3the above example would be
               drawn.  Note the line
               appearing between points #2
               and #3 that was not in the
               original sequence.

               Typical values are 1/2 to
               1/4 smallest pen size used.  
                Range is 0 to 1.5mm.

          Short Near Vector Length

               Before sending a vector to the output device, HPSORT checks
               to see if a "short" vector touches it.  If yes, then HPSORT
               draws the "short" vector first.  Range is 0 to 99.99mm, with
               5 to 10mm being a good value.  If this value is too large,
               it is counter productive towards sorting.  









                                                                         12








               Consider the lines in the
                                            #1
                                              \
                                               \
                                                \
                                              #2 +--------------------#3figure to the right.
               During the sorting
               process,  HPSORT decides
               the next line to draw is
               from points #2 to #3.

               This parameter instructs
               HPSORT to check to see if
               a "short" line is connected to the line about to be drawn. 
               In this case, it is the line from points #1 to #2.  If the
               length of the line from points #1 to #2 is less than or
               equal to the value of this parameter, then HPSORT will
               output the following sequence:

               a.   Move with the pen up to position #1.
               b.   Lower the pen and draw a line from point #1 to #2.
               c.   Lower the pen and draw a line from point #2 to #3.


          Maximum Number of Relative Moves

               HPSORT uses primarily "relative" positioning.  This is one
               of the major techniques used to reduce file size.  In this
               mode, each pen move is the delta x, delta y from the end of
               the last pen move.  When positioning in relative mode, this
               parameter controls how often an absolute positioning command
               is issued to correct for any positioning errors in the
               plotter.

                      What is "absolute" and "relative" positioning?

               Absolute positioning is where each command tells the plotter
               exactly where to position the pen on the paper independent
               of any other move.  Therefore, the pen is always in the
               position where the CAD program expects it to be.  An example
               would be -

                    Move Pen Up to 1000,1000
                    Place Pen Down
                    Move to 1400,1000
                    Move to 1400,1400
                    Move to 1000,1400
                    Move to 1000,1000

               The numbers are in plotter units and draw a square 1 cm on a
               side.






                                                                         13








                Using the same example as above, HPSORT would output 

                    Move Pen Up to 1000,1000 in absolute mode
                    Place Pen Down
                    Shift to relative mode 
                    Move right 400 units
                    Move up 400 units
                    Move left 400 units
                    Move down 400 units

               Notice that in the relative example, there is only one
               command to tell the plotter exactly where to move.  The rest
               of the commands are move left, right, up or down commands. 
               They assume that the plotter pen is where it is suppose to
               be.  Due to cumulative errors in both calculations and
               mechanical positioning in the plotter, every once in a
               while, a absolute positioning command must be done. 

               The larger this parameter, the more the file size is
               reduced.  But the larger the chance of plotting errors. 
               Legal values range from 2 to 999.  Values of 5 to 20 are
               effective.

          Check Circle Radius

               Circles are a special case when compared to all of the other
               types of line drawing commands.  When at a start or end of a
               line, HPSORT checks to see if a circle is either touching or
               centered on the current position.  If yes, then send the
               circle to the output device.  

               This parameter controls how close the circle be in order to
               be checked.  If it is too small, HPSORT misses the circle
               during the normal processing and is outputted during the
               cleanup phase.  If it is too large, then it will slow down
               normal vector processing by needlessly checking too many
               circles.  A good value is dependant upon the average circle
               size.  Range of legal values is 0.01 to 99.99mm.  Values of
               5 to 10mm are effective.

               If HPSORT draws too many circles during the cleanup phase of
               the processing, try increasing this value.











                                                                         14








          Max. Relative Move

               This defines the maximum move size in relative mode in
               plotter units.  Some plotters ignore large relative moves,
               such as the HP 7450 DraftPro.  For moves larger than this
               parameter,  HPSORT uses absolute moves instead of relative
               moves.  For most plotters, 16,000 is a good value. 

          Line Type Divider

               When not using ORCAD, set value to 1.00.

               The method ORCAD uses to draw dashed lines is not compatible
               with the internal structure HPSORT uses to represent draw-
               ings internally.  See "Ignore IP Command" (next parameter)
               for details.  This parameter is a compromise that scales the
               "dash" in the dashed line to fit the paper.  Values are
               dependant upon the normal drawing size:

                                    Paper Size   Value
                                    ----------   -----
                                     A to B       1.5
                                     B to C       2.5
                                     C to D       3.5
                                     D to E       4.5
                                     B to D       3.0

          Ignore IP Command

               When not using ORCAD, set value to NO.  

               The IP is the "Input P1 and P2" command.  This permits the
               computer to redefine the meaning of P1 and P2 (refer to the
               plotter manual for definition of P1 and P2).

               The method ORCAD uses to output dashed lines is different
               other packages.  The HP plotter language defines dashed
               lines is as a percentage of the distance from the opposite
               corners of the paper.  ORCAD, "redefines" the corners of the
               paper, using the "IP" command to an "A" size drawing, draws
               the dashed line and then redefines the paper size back to
               normal.

               Normally, when HPSORT finds an IP command, it outputs the
               contents of the label and vector buffers, then outputs the
               IP command.  ORCAD uses this command for dashed lines. This
               stops the pen motion optimization process whenever dashed
               lines are encounter.  When using ORCAD, set value to YES.





                                                                         15








          4.2.3 Swapping Polylines to Disc

          This option controls how HPSORT handles a series of connected
          lines (polylines)1  When these polylines are found, the only
          where the starting and ending points are needs to be stored.  The
          rest of the information can be stored elsewhere while the program
          is running.  If this information is swapped to the disc, HPSORT's
          effective capacity is increased.

          If more than 4,000 vectors on a machine with 450k or more of free
          RAM memory are normally processed in a single pass by HPSORT,
          then these parameters will aid in performance.

          When this option is selected, the following edit screen will
          appear -


            ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍVector Buffering to DiscÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
            º                                                           º
            ºSwap Polylines to Disc................Y/N. YES             º
            º                                                           º
            ºCollapse Rectangles to Single Command.Y/N. NO              º
            º                                                           º
            º       -----------  Swapping Options  --------------       º
            ºDrive to swap to.................  C                       º
            ºSwapping Threshold...............  005                     º
            ºPrint Swapping Statistics....Y/N.  NO                      º
            º                                                           º
            º                                                           º
            º                                                           º
            ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼







          Swap Polylines to Disc

               This parameter enables the rest of the options on this
               screen.  If YES, the swapping is enabled.

               Electrical schematics usually do not benefit significantly
               from this option.  Mechanical drawings, particular drawings
               by AUTOCAD, and PCB Layouts benefit significantly by setting
               this parameter to YES.

                                   

               1    In HPSORT, a polygon can be either close line a rec-
                    tangle or open like the line segments in the letter M.

                                                                         16








          Collapse Rectangles to Single Command

               Set to NO.  Current version does not support this option.


          Drive to Swap To

               Letter of the drive to use for buffering to disc.  HPSORT
               uses the current drive and directory if this field is blank. 
               If more than one hard drive is available, use the fastest
               one available.

               If a RAAM drive is present, size of 400kb is usually enough. 
               If running from a network, using the local hard drive will
               give better performance rather that a drive on the file
               server.

          Swapping Threshold

               This sets the minimum number of connected line segments
               before swapping them to the disc.  Swapping all connected
               segments does not significantly give a better sort, but can
               have a significant increase in plotting time.   A good value
               is one that is slightly less than the average number of
               connected segments.  For a starting value, 5 works well. 
               Range of values is 1 to 999.

          Print Swapping Statistics

               This parameter turns on the printing of the swapping statis-
               tics.  These statistics are useful in adjusting the other
               parameters towards optimal values.


          4.2.4 Label commands

          These parameters control how HPSORT handles text plotted with the
          built in plotter fonts2.  The HPGL documentation refer to this
          as a label command.  One of the first questions that you should
          ask is "Does my CAD program use built in fonts?".  HP_CFG knows
          the correct settings for those CAD programs listed in the Default
          option (see section 4.3) on the opening menu.  

          If your program was not listed in the default settings, HPSORT
          can make the determination.  Set the "Label Commands Processed"
          parameter to NO.  If HPSORT finds a label command, HPSORT will
          exit with a configuration error.  Set the parameter to YES then. 

                              

               2    What is a font.  Font is the term used to describe the
                    shape of the letters as they are drawn.

                                                                         17








          Then set the "Print Labels Stats" command to yes to determine the
          correct buffer sizes.

            ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍHPSORT Label ParametersÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
            º                                                           º
            ºLabel Commands Processed.....Y/N..... YES                  º
            ºIgnore Single Space Labels...Y/N..... YES                  º
            ºPrint Labels Stats...........Y/N..... NO                   º
            ºMap Font 0 to Font 99........Y/N..... YES                  º
            º                                                           º
            º    --- Relative Label Positioning Commands ---            º
            ºPosition Labels in Relative Mode..Y/N. YES                 º
            ºMax Number Relative Moves............. 20                  º
            º                                                           º
            º               ------- Label Buffer Sizes --------         º
            ºMax Number Labels in Memory at one time..... 1000          º
            ºMax kb to store labels...................... 48            º
            º                                                           º
            º                                                           º
            ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼






          Label Commands Processed

               This flag controls how HPSORT supports the Label command. 
               There are two methods of printing text on a drawing.  Pro-
               grams such as AUTOCAD, output all text as a series of line
               segments.  This permits the program to support a variety of
               fonts.  Some programs such as ORCAD or SCHEMA, use only
               those fonts built into the plotter.  Some programs such as
               Point Line CADD, use both methods.  

               Setting this parameter to NO effectively increases the
               amount of memory available for sorting lines.

          Ignore Single Space Labels

               If the CADD program is try to plot a single space character
               using the built in plotter fonts, ignore the command.  This
               parameter normally should be to YES.  

          Print Label Stats

               This parameter turns on the printing of the labels statis-
               tics.  These statistics are useful in adjusting the other
               parameters towards optimal values.



                                                                         18








          Map Font 0 to Font 99
               This parameter when YES will change the appearance of some
               or all the text on your drawing for those CAD programs that
               use the built in plotter fonts.  Normally font 0 is used. 
               While this font is okay, the 5, 6 & S and 8 & B characters
               are difficult to tell apart.  HPSORT can substitute plotter
               font 99 which is designed to make telling these characters
               apart easier.  

          Position Labels in Rel Mode 

               This parameter controls positioning of labels using relative
               instead of absolute positioning.  For a discussion on the
               difference between the positioning mode, refer to "Maximum
               Number of Relative Moves" on page #? for more details. This
               results in smaller output files.  

          Max Number Relative Moves

               When positioning labels in relative mode, this controls how
               often an absolute positioning command is issued to correct
               for any positioning errors in the plotter.

               The net effect of this parameter is that the larger the
               value, the more the file size compression, but the larger
               the chance of plotting errors.  Legal values range from 2 to
               999.  Values of 5 to 20 are effective.

          Max Number Labels in Memory at one time

               This is the maximum number of labels to reserve space for
               before outputing the buffer.  Use label statistics to deter-
               mine a good value.  If the maximum value printed on the
               stat's is "close" to the current value, try increasing this
               value by 10%.  Range of values are 30 to 2,0000.

          Max kb to store labels

               Number of kilobytes of memory to reserve for the to store
               the actual text of the labels.  Range of values is 3 to 64. 
               Use label statistics to determine a good value.  If the
               maximum value printed on the stat's is "close" to the cur-
               rent value, try increasing this value by 10%.










                                                                         19








          4.2.5 Serial Input / Output Communication Parameters


          HPSORT has full control over serial ports.  HPSORT can set all of
          the serial port parameters without the use of the DOS MODE
          command.  

          HPSORT has a simple built in spooler to the serial port.  This
          permits HPSORT to output to a plotter while performing it's
          calculations.  

          When you select this option, the following edit screen will be
          displayed:



            ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍHPSORT Serial Port ParametersÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
            º                                                           º
            ºBuffer Serial Output..............Y/N. NO                  º
            ºBuffered Serial Output Buffer Size.... 32kb                º
            º                                                           º
            º----------  Serial Communication Parameters ------------   º
            ºHave HPSORT set serial parameters.Y/N.. NO                 º
            ºWord size.............................. 8                  º
            ºBaud Rate.............................. 9600               º
            ºParity 0-NONE  1-EVEN, 2-ODD........... NONE               º
            ºNumber Stop Bits (1 or 2).............. 1                  º
            º                                                           º
            º                                                           º
            ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼





          Buffered Serial Output

               HPSORT contains a simple serial port spooling program when
               the output device is either COM1, COM2, COM3 or COM4.  This
               exists so  if you do not already have a spooling program on
               your system, HPSORT can send data to the plotter while it is
               processing.  

               There are two restrictions on this function:

               1 -  The plotter must use the hardware same style of
                    handshaking as used by MS-DOS.  If you can copy your
                    file to the plotter using the MS-DOS "COPY" command,
                    there will be no problems with the built in spooler. 

               2 -  HPSORT will not exit until the plotter has received all
                    of the data.

                                                                         20








          Buffered Serial Output Buffer Size

               When enabling the serial port buffering, this is the number
               of kilobytes of memory to reserve.   Value can be from 3kb
               to 32kb.

          Have HPSORT set serial parameters

               This parameter has meaning only when the output file is
               either COM1, COM2, COM3 or COM4.  When this parameter is 
               NO, HPSORT does not change the parameters from when it 
               begins.  If YES, then the parameters are set to the
               parameters in this section.

          Word Size

               Number of bits in each data byte sent.  Must be the same as
               the plotter.  Normally, will be 8, but can be 7.

          Baud Rate

               Baud Rate to set serial port to.  Must be  the same value as
               the plotter.  Legal values are only those values displayed.


          Parity 0-NONE  1-EVEN, 2-ODD

               Can be only one of the three values listed in the options
               menu.  Must be the same value as the plotter.

          Number Stop Bits (1 or 2)

               Legal values are 1 or 2.  Must be the same value as the
               plotter. Normally, will be 1 unless sending at 110 baud.


          4.2.6  Disc Parameters

          HPSORT has two groups of parameters that control the output file
          name.  The first group has to do with the default output file
          name.  These are the first two parameters.

          The second is to automatically invoke the file compression
          program of your choice.  For those users that communicate with a
          plotting service bureau, HPSORT can automatically invoke your
          compression program. 

          When you select this option, the following edit screen will be
          displayed:




                                                                         21









            ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍHPSORT Disc I/O ParametersÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
            ºDefault Output File Name..................HPSORT.OUT       º
            ºRename Output file to Input file name.Y/N.YES              º
            º                                                           º
            ºIf you use data compression programs to shrink the size of º
            ºthe plot files before they are sent to a plotting service  º
            ºbureau, HPSORT can automatically invoke your favorite      º
            ºcompression program.  Please refer to the manual for full  º
            ºdetails as to how to use this option.                      º
            º                                                           º
            º                                                           º
            ºAdd Output File to Compressed file........Y/N.. NO         º
            ºCompression File Name (must be pathed in)......            º
            ºCompression File Program parameters............            º
            ºCompression File to add output to..............            º
            º                                                           º
            ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼







          Default Output File Name

               Default name of file to send output.  When HPSORT runs, this
               is the file name used if no output file is present.  The
               default value is HPSORT.OUT.  

               This field can contain a device name.  For example if the
               value is COM1:, all output would by default goes to serial
               port #1.

               NOTE:     If the parameter to "Rename Output to Input" is
                         YES, then this parameter has no meaning.

          Rename Output file to Input file name

               If set to YES, HPSORT sends it's output  to a temporary
               file.  When HPSORT completes, the input file is renamed with
               a ".BAK" extension and the temporary output file will be
               renamed to the input file name.









                                                                         22








          Add Output File to Compressed file

               If you routinely use service bureaus to plot your drawings,
               these can be compressed by a programs such as ARC, PKXARC,
               LHARC, etc.  By setting this parameter to YES, HPSORT will
               automatically send the output file to the compression pro-
               gram.  The rest of the parameters, define how to pre-form
               this operation.

               WARNINGS: The output file name must be unique.  If
                         not, then the compressed file will con-
                         tain only the last file processed.  

          Compression File Name (must be pathed in)

               Name of you compression program to use.  Examples would be
               PKZIP, ARC or LHARC.  The program must be either in the
               current directory or path.

          Compression File Program parameters

               List of any commands required by the compression program to
               process the file.

          Compression File to add output to

               Name of compressed file to store data in.  This cannot be
               selected from the command line.
              
          4.3 Default Settings

          HP_CFG can automatically configure HPSORT for the listed software
          on the menu.  If the software that you use is not listed, then
          choose "Default CAD".  The settings should work for most
          packages.

          The "Default Serial Parameters" option configures the serial port
          for 9600 baud, no parity, 8 data bits and 1 stop bit.















                                                                         23









             ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄHPSORT Configuration MenuÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
                ³Edit  Default  Sort  Compress  Save  Quit                            ³
                ÀÄÄÄÄÄÄÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
                       ³AutoCad                  ³
                       ³ORCAD                    ³
                       ³Point Line CADD          ³
                       ³Schema                   ³
                       ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
                       ³Default CAD              ³
                       ³Default Serial Parameters³
                       ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ





          4.4 Sort / Compress

          The primary purpose of HPSORT is the pen motion optimizing.  If
          your CAD package does do pen motion optimizing and wish only to
          compress the plot file, then select the "Compress" option on the
          menu.  

          In Compress mode, the plot file is not sorted.  It is split into
          lines and label commands.  Then each of these two sections are
          separately outputed in the order that the commands were read in.

          4.5 Save

          Stores parameters to file "HPSORT.CFG" in the current directory.

          4.6 Quit

          Exits configuration utility without save any parameters.  Use the
          "Save" command to save the parameters.


          5.0 Operation

          To execute HPSORT, type the following command line:

                     HPSORT "INPUT FILE NAME" "OUTPUT FILE NAME"

          INPUT FILE NAME     This is the name of the file to be processed.

          OUTPUT FILE NAME    This is an optional parameter that specifies
                              the where the sorted file is to be placed. 
                              Note if this value is not specified, then the
                              parameters in section 4.8 control output file
                              name.


                                                                         24








          HPSORT displays the following status messages when running -

          "Vector Buffer Full - XX%     How much memory is used while
                                        reading in the source file.

          "Number of Vectors - x,xxx"   This is the number of vectors that
                                        HPSORT is processing.

          "Vector Buffer Left - XX%"    Percentage of buffers left to sort
                                        and output.  Percent is comparing
                                        the number of vectors (lines) left
                                        with the number of vectors when
                                        this phase started..

          "Label Buffer Left - XX%"     Percentage of the label buffer left
                                        to sort and output.  Percent is
                                        comparing number of labels left
                                        with the number of labels when this
                                        phase was started.

          "Waiting for Output Queue to Empty"       This message appears only
                                        when Serial Port Output Buffer
                                        (Section 4.2.5) has been enabled
                                        and the output file was a COM port. 
                                        The next line contains the number
                                        of bytes left in the buffer to
                                        output.
          5.1 Theory of Operation

          The technical description of how HPSORT works is that it preforms
          a topological sort.  What this means is that it tries to minimize
          the overall pen motion.  HPSORT does not attempt to do the best
          possible sort.  What it does do is do, is a good sort quickly.

          HPSORT works under a self imposed time restriction.  The bench-
          mark time is a system where the plotter is directly connected to
          20mhz 386/387 computer system with 500kb free RAM.  HPSORT has
          perform the sort and send the results to the plotter in same
          amount of time than it takes MS-DOS COPY command to perform the
          same operation.  

          Doing the sort that it does do, plots will generally plot in 10%
          to 30%  (had one case of 54%) less time.  It was our judgement,
          that the processing time to get the best possible sort was not
          worth the plotting time saved.  Future versions of HPSORT will
          have improved routines both for processing speed and plotting
          speed.






                                                                         25








          In operation HPSORT has three separate phases:

               1    Read in the input plot file and decode it.
               2    Sort and output the lines, circles and arcs.
               3    Sort and output any text that uses the built in
                    plotter fonts.

          These three phases generally run in the order displayed. 
          Commands that flush the internal buffers (e.g., a pen change) or
          if the label or vector buffer fills up disrupt this order.


          5.2 HPSORT & Desqview

          When running HPSORT with Desqview, having a partition size of at
          least 320kb is required.  The more ram available to HPSORT the
          faster it will run.

          The only problem noticed is when HPSORT is running at the same
          time as your CAD package is.  As HPSORT is a compute intensive
          program, your CAD package will appear to slow down while HPSORT
          is running.


          6.0 problems


          Refer to the README file for a the list of known problems with
          this version.

          6.1 Error Messages

          HPSORT has three types of error messages.  In the first tow
          cases, the message includes text as to how to fix or work around
          the problem.

          CONFIGURATION -These messages occur when the HPSORT.CFG file and
                         the input file contain values that are in conflict
                         with each other.

          RUNTIME -      These messages occur when HPSORT cannot do some
                         operation.

          INTERNAL -     These messages occur when HPSORT detects an
                         internal error.  If you get one of these messages,
                         please contact the author (section 6.2).







                                                                         26








          6.2 Incompatibilities

          If HPSORT is not buffering serial output, there are no known
          incompatibilities.

          HPSORT may not operate properly when other background software is
          running and it is buffering serial output.  By other background
          software, we mean programs that are loaded in the CONFIG.SYS,or
          by a BAT file and remain in memory.  Certain screen clock pro-
          grams, for example, are known to interfere with serial port
          operations.

          Conflicts with HPSORT may not be caused by a single program, but
          by a combination of programs, which, taken singly, cause no
          problems.  Therefore, if you suspect some conflict, you should
          boot your system with only absolutely necessary device drivers
          and resident programs (i.e. a partitioned disk device driver). 
          Then add programs back in one at a time.


          6.3 How to contact CNT Software

          We have support for messages and technical support on JADE BBS at
          (608) 752-7840 When calling, set your modem up for 8 data bits,
          no parity and 1 stop bit.  Leave a private message for "Tom
          Thorp".

          If you need to send us your plot file for analysis, please send
          to:
                         CNT Software
                         1615 Highland Ave.
                         Janesville, Wis.  53545

          We use both 5 1/4 & 3 1/2 inch diskettes. Please include the
          following information:

               o    Version of HPSORT
               o    CAD or Graphics Program 
               o    Make and model of Plotter
               o    Version of DOS













                                                                         27








                                              Order Form

            INVOICE # 91-0331

            Remit To:
                        CNT Software
                        1615 Highland Ave
                        Janesville, Wisw3545


            Qty. Description                             Amount

            ____ HPSORT Registration                        $50.00 ea   __________

            ____ HPSORT Printed Manual                      $19.95 ea   __________

                 Shipping (see below)                                   __________

                 (Wis. residents add 5% sales tax)       Tax            __________
             
                                                                  Total __________

                           Purchase Orders less than $100 must be pre-paid.

            Name:       _____________________________________________________

            Company     _____________________________________________________

            Address:    _____________________________________________________ 

                        _____________________________________________________

                        _____________________________________________________

            Work Phone: (____)  ________________     

            Home Phone: (____)  ________________

            Comments:   ____________________________________________________

                        ____________________________________________________

                        ____________________________________________________

                        ____________________________________________________

            Note: Shipping to 48 continental states is $5.00.  Alaska, Hawaii, and Canada
                  is $10.00.  Other countries, please call before ordering. 





                                                                                        28









            Site License Information

            If you plan on using HPSORT in a corporation, government office, or for any
            business purpose whatsoever, registration is mandatory and the 90 day limited
            license is strictly enforced.  Quantity discounts are available under a Site
            License agreement:


                  One MASTER copy of HPSORT disc per site is supplied and one copy
                  of the manual is supplied per user.

                  For all site licenses, the customer must appoint a single contact
                  person with whom all HPSORT related dealings will take place. 
                  Should a problem occur, that person, must  report the problem and
                  arrange for its resolution.  All HPSORT program updates will be
                  forwarded to the contact person.  When filling out the order form,
                  please use the contact person's name to prevent any later
                  misunderstandings.

                                   Site license discount rates are:


                                Total Copies         Discount per Unit
                                   2 to 10                  20%

                                  11 to 50                  40%

                                     51+                    50%



            NOTE:       All prices and discounts are subject to change without notice.
                        Discounts are not cumulative.  They apply to separate orders only.
              

              
              















                                                                                        29