PROGRAM: PRINTER.COM

GENERAL FUNCTION: To send commands to the printer.

WHY IS IT NEEDED?  The many different printers that run on PCs
each have different commands.  It is often necessary to vary how 
the output is printed; to get italics, compressed print, a higher
quality, etc.

INSTALLATION: This program is driven by a configurable data file
which must be created by the user.  The file consists of three
fields in the format

             <prompt>[#n]$<decimal code><decimal code>

There can be up to 10 such lines in the file.  The program will read
the file, label the prompts from 0 up to a maximum of 9, add Esc as
an option to end processing.  For the option selected, the program
will send the two characters to the printer whose ASCII code in decimal
is given.  Each code consists of exactly 3 digits.  The appropriate
printer codes for each function will have to be gotten from the user's
printer manual.  If only one character need to send to the printer,
then the second code should be three zeros.  If more than two characters
need to be send to the printer, use two lines in the file, and put #1 in
the first line and #2 in the second; for two or fewer characters the #n
should be omitted entirely.  Examples of lines in such a file are

           Compressed Print$029000         [sends 029 to printer to get
                                            compressed print]
           Double Width Print #1$027087    [to get double width, sends
           Double Width Print #2$001000     Esc(027),W(087),(001) to
                                            printer]

The last option in the file must have an ampersand ("&") at the end 
of the line.  This file must be named PRINTER.DAT.  An example for the
Epson printer is

            Set Printer to Power Up Mode$027064
            Compressed Print$027015
            Italics Print$027052
            Emphasized Print$027069
            Double Strike Print$027071
            1/8th Inch Spacing$027048
            Turn on Paper Out Sensor$027057
            Turn off Paper Out Sensor$027056
            Double Width Print #1$027087
            Double Width Print #2$001000&

When PRINTER is run, the user will see the screen

             Printer (1.1) - Special Print Functions

             0   -  Set Printer to Power Up Mode
             1   -  Compressed Print
             2   -  Italics Print
             3   -  Emphasized Print
             4   -  Double Strike Print
             5   -  1/8th Inch Spacing
             6   -  Turn on Paper Out Sensor
             7   -  Turn off Paper Out Sensor
             8   -  Double Width Print #1
             9   -  Double Width Print #2
             Esc -  Exit

             Your choice 

The user can select as many items as many times as desired.  After a
selection, the prompt "Choose again?" will appear, and the user can select
0-9,Esc or Y/N as a response.

FORMAT:                 PRINTER [drive letter]

EXAMPLES:               PRINTER B        [Look to drive B for 
                                          PRINTER.DAT]

HOW TO USE IT:  Prepare the list of options in PRINTER.DAT in
advance.  Before you start to print, run PRINTER first.  You may
for example need more than 80 columns, and therefore will have to
use more than 10 characters per inch.  You may need a higher
quality print and therefore use a double strike or emphasized
print mode.  Select the needed options, press ESC to get back to
DOS, then do your printing.

OTHER EFFECTS: The printer will be left in whatever mode you
select.  Either turn the printer off, then back on, to restore
its default mode, or else restore the printer to the desired state
by rerunning PRINTER again.

SYSTEM REQUIREMENTS:  Works with DOS 1.1 and 2.X.

COMMENTS:  Application programs that reset the printer when they are
invoked nullify any prior use of this program.  WordStar users can
run PRINTER from within WordStar using the R option.  The output of
PRINTER goes to LPT1.

SOURCE OF PROGRAM:  John Petrey