Responsible:  Remco Treffkorn CompuCom.


	This is an informal document. The information contained herein
	is hoped to be accurate. If you find anything you want to have
	changed or corrected please contact me at the HQ BBS.


	CCSP.EXE: the CSP3 protocoll.
	=============================

	Status:
		Version 1.00

	Useage:
		You must initialize CSP3 before you can use it. That has to
		be done only once. Type:
		  CCSP -b<baudrate> -p<port number> -i


	Known bugs:
		None so far...

	Hardware required:
		A SpeedModem.
		At least a '286/12, slower machienes might work,
		but with a performance penalty.
		The program needs ~150 Kbyte for itself.

	Description:
		CCSP.exe is an external protocoll to be used with
		BBSs and communication packages like PROCOM(+),
		Boyan, Telix, Qmodem...
		The installation depends on the package you are using.

		CCSP uses data compression to get your file over the
		the line faster. It does not rely on the error correction
		feature of the SpeedModem. It can (and should) be used
		with the *H1 setting for comm programs, BBSs use *h2.


		CSP3 is able to achieve up to a 4 to 1 data compression
		ratio, but only on certain ASCII files and some data files.
		If something is VERRY compressable using a program like
		PKARC or PKZIP then CSP3 will archieve excelent results.
		Already compressed files will not be compressed any more
		and CSP3 will not gain any speedup in these cases.

		Generally spoken: In cases where  V.42bis will not
		compress the data any more, don's expect CSP3 to do so.
		In cases where MNP5 is used to some advantage expect a
		much higher compression rate from CSP3.

		A word of caution: CSP3 uses a lot of 'coputer muscle'
		to compress the data. If you have not at least a '286/12
		the compression might actually take longer than the
		transfer of data. You will not get the full performance.
		Receiving data on a slow machiene (downloading) should
		work fine, since the decompression is much less demanding.

	Usage:
		Initialisation:
		  CCSP -b<baudrate> -p<port number> -i
		   This has to be done only once! It registers
		   CSP3 with the SpeedModem.

		Upload:
		  CCSP -b<baudrate> -p<port number> -t <filename>

		Download:
		  CCSP -b<baudrate> -p<port number> -r <filename>

		Baudrates:      9600 / 19200

		Port Numbers:   1-4
		Filename:       The name of the file to send/receive.
				On downloading the <filename> is
				optional. If no name is given, the
				file will get the name the sender
				supplied. In case of a name conflict
				the already existing file will not be
				overwritten, but the newly received file
				gets a filename with the last character
				changed to a numeric value.

		Examples:
				ccsp -b19200 -p2 -t c:\ul\test.txt
				This line will upload the file
				'test.txt' on the c: drive in the
				directory \ul using com port 2 and set
				the baudrate to 19200.

				ccsp -b19200 -p4 -r
				This line will receive a file using
				com port 4 at 19200 baud. The name of
				the file will be the same as on the
				senders side.


	Setup for various communication packages:
		Help!!
		If you have set up CSP3 for ANY software, please
		share your wisdom. Drop me a message at the
		HQ BBS.


	Good Luck! and thanks for your help in beta testing CCSP.

	Remco Treffkorn.