ICOM Programmer

			written in TURBO C 1.5

			by John Lundy - N5MHZ


	This program is my answer to an online radio control program for
my IC735.  Although specifically written for the 735 it should be fairly
easy to modify this code for many other rigs.  But that task is left to
the more advanced user.  For those of us who just want to load-and-run,
this program may be your answer.

	There are 2 modes of operation for this program: stand alone and
memory resident.  Be sure your radio is hooked to the COM port.

	Stand alone mode: at the DOS prompt type ICOM.  You then get a
menu and a display of your radio's status (i.e Frequency and Mode).

	Memory resident mode: at the DOS prompt type ICOM R.  After an
identification is printed on the screen, you're back at the DOS prompt.
The ICOM programmer is now memory resident and can be called up by pressing
the CTRL and Right-Shift keys at the same time.  Otherwise, the function of
the two modes is the same.

	Play around with the program.  It's really simple to use.  Select
from the memu items and see what they do.  The only place a little more info
might be helpful is in the Frequency option.  This option has the ability
to change the frequency by an offset.  When prompted for the frequency,
enter +/- and the offset in KHz.  In this way you can move around by a
few KHz without typing the whole frequency.

	You might ask, "How does the program know what COM port my rig
is hooked to?"  Well, it doesn't.  It assumes COM1.  To change this and
some other options do the following:  Enter the program as outlined above,
Use the "Save List Disk" option to create the ICOM.INI file, and then Edit
this file changing the parameters in the file to your preferences.  This
ICOM.INI file will be created in whatever directory ICOM.COM was loaded
from by DOS.  So, if you run ICOM.COM and the DOS PATH is used to find the
executable, ICOM.INI will be created in the same directory.

	Some other special features that you might like to know about are:

1) 64 frequency/mode memories that are accessed sequentially in a round-robin
   method, both forward (-->) and backward (<--).  These memories are saved
   with the setup info by using the the "Save List Disk" option.  They are
   automatically reloaded the next time the program is run or by using the
   "Load List Disk" option.
2) frequency rounding, round the present frequency to the nearest 1KHz
   boundary (.)
3) up and down frequency stepping in .1KHz, .5KHz and 1KHz steps
4) up and down frequency scanning with selectable increments
5) next and previous band selection of all HF amateur and MARS bands
6) top and bottom commands for the present band
7) hitting Enter will reset the COM port to present desired values and
   refresh the screen

	Release revision information

1.0	Initial release

1.1	Found problem with interaction with some programs and the use
	of keyboard interrupt trapping.  Had to change the method of
	exiting and memory resident entry to Ctrl-RShift.  No longer trap
	keyboard interrupts.

	If you have any difficulties, please let me know about them.  I'm
always tinkering with programs and would appreciate useful feedback I can
incorporate into future programs.

vy 73, John