WHATPORT.COM 
 
                           Version 3.4 
                          January 8, 1989 
 
     For detecting installed serial ports and type of mouse 
 
        Copyright 1989, Life Sciences Editorial Services 
                       1236 River Bay Road 
                    Annapolis, Maryland 21401 
 
 
 
AUTHOR: Peter Petrakis 
 
 
IMPROVEMENTS IN THIS VERSION: 
 
    Version 3.4 of WHATPORT.COM provides a more graphic 
    display of installed COM ports and their associated interrupt 
    request (IRQ) lines.  In addition, it displays the IRQ line 
    being used by any installed mouse (except PS/2), not just a 
    serial mouse, thus increasing the usefulness of the program for 
    avoiding IRQ line conflicts.  If IRQ line conflicts exist, it 
    notifies you.  Finally, the program disk file size has been 
    substantially reduced and color has been added. 
 
 
DESCRIPTION: 
 
    This program detects what serial ports are installed in an 
    MS/DOS or PC/DOS system.  The type of mouse, if installed, 
    is also shown (serial, bus, InPort, PS/2, HP) together with the 
    interrupt request (IRQ) line it's using (unless it's a PS/2).
    The program warns of potential IRQ line conflicts between the
    mouse and serial ports.


PRINCIPLE:

    Because PCs have only two IRQ lines for serial communications,
    COM3 must share COM1's IRQ line and COM4 must share COM2's 
    IRQ line.  Unfortunately, two devices using the same IRQ 
    line can't be active at the same time.  COM3 can't be used for 
    a printer or modem if a serial mouse is active on COM1, for 
    example.  Likewise, COM4 can't be used if a serial mouse is 
    active on COM2.  In other words, if you have four COM 
    ports and a mouse is attached to one of them, you do not 
    have three COM ports available for other devices, you only 
    have two.  The COM port that shares the IRQ line being 
    used by the mouse is not usable.  WHATPORT detects and
    reports such conflicts.
 

    The following table shows what ports are available for other 
    devices when a serial port mouse is present on a multiple-port 
    system:

    Serial port mouse on     Ports available for other devices 
    ---------------------    ---------------------------------
    COM1 or COM3 (IRQ4)          COM2 or COM4 (IRQ3) 
    COM2 or COM4 (IRQ3)          COM1 or COM3 (IRQ4) 
 

    Conflicts with serial ports are also possible in the case of a
    bus mouse.  For example, if a bus mouse is configured to use
    IRQ3, there will be a conflict with with both COM2 and COM4.  If
    it is configured to use IRQ4, there will be a conflict with both
    COM1 and COM3.  WHATPORT also detects and reports these conditions
    so a different IRQ can be selected for the bus mouse.
 
 
HOW TO USE THE PROGRAM:

    Just run it and read the results.  Adjustment for color or
    monochrome display is automatic in this version, but monochrome
    can be forced by putting /m on the command line.
 
 
DISTRIBUTION: 
 
    WHATPORT.COM and this document are provided free by 
    Life Sciences Editorial Services, Annapolis, Maryland.  They 
    may be copied and distributed promiscuously provided no 
    money is charged for them, they are not modified, and they 
    are not separated.  Although the program has been extensively 
    tested, Peter Petrakis makes no warranty concerning its 
    usefulness on all systems and he accepts no responsibility or 
    liability for any mishap resulting from its use.