Ymodem Batch / Ymodem-G

         Ymodem   has  a built in communications manager  and  doesn't
         need  any  type of fossil, in fact you should make  sure  you
         turn  the  fossil  OFF if running it on a  BBS  that  uses  a
         fossil.

         Ymodem requires a number of command line switches:
                              -B, -P, {-R or -S}
         -Bxxxx <Baud Rate>
         -R Receive files
         -UDrive:path,    directs that all files  received  should  be
                          stored on this drive and in this  directory.
                          This  switch  is primaryly  for  NON-OSIRIS,
                          NON-QT  systems. Osiris takes care  of  this
                          internally  and  this switch should  NOT  be
                          used.

         Example: -UC:\uploads
                  -UD:\files\temp

         Do NOT end the path with a backslash "\"

         Illegal -U settings would be C:\
                                      C:\uploads\
                                      D:\files\temp\
                                      C:

         -G , Use Ymodem-G.

         -O, use Ymodem Overdrive/Overthrust. This is compabible with
             the DSZ Ymodem Overthrust.

             The switch should never be used with the -G switch.

         -Nx, with x being the node number in use. For use on Osiris
               CBIS  systems only.  Ymodem will show the name  of  the
               caller as well as where he's from if this switch is used.

         -Px,  Supported  Com  Ports, COM 1, COM  2, COM 3, and COM 4.
                         (COM1-8 if used with OSIRIS.)
         -S,  <Filenames> as  many as DOS allows. Full drive,
                         path,  and  filename supported.

         e.g. -S File1.Zip File2.Zip

                   NOTE:   -R  or   -S  MUST  be  the   last
                   parameter on the command line. As soon as
                   Ymodem encounters either one of these two
                   switches, it will begin to either Receive
                   or Send.


         The -L switch is only for those that do not have COMx= set in
         the environment. If your running Osiris then Ymodem will  use
         the COMx= automatically.

         Sample Osiris Command line (protocol control file)

         (Ymodem)
         Send : -N*N -B*B -P*P -@*U
         RCV  : -N*N -B*B -P*P -R

         (Ymodem-G)
         Send : -G -N*N -B*B -P*P -@*U
         RCV  : -G -N*N -B*B -P*P -R


                                  Infomation

         This  driver supports Ymodem Batch and Ymodem-G. Use  -G  for
         Ymodem-G.

         It  has  been tested against DSZ in both modes and  seems  to
         function just fine.

         The Ymodem-G documentation is rather swallow on just  exactly
         what  to  do if an error occurs. The receiver is  suppose  to
         abort  the  transfer but it doesn't say if  it's  suppose  to
         abort  out the entire BATCH session.


         We would  recommend  Ymodem-G ONLY be used  if  the  call  is
         local  or your using an HST, Telebit, or another other  modem
         with MNP or ARQ type error correction.


         Ymodem  may be freely used by Osiris Owners.  If you do NOT
         own Osiris, Ymodem must be purchased.

         The price is 15 dollars (US Currency).

                                   Mail to :

                              Micro TECH Systems
                             555 North Spring, #39
                           Cape Girardeau Mo. 63701