____________________________
                          |                            |
                          |       CBEEP - DBEEP        |
                          | Replace BEEP With a Flash! |
                          |____________________________|

                                Copyright (C)  1991
                                  >>-Swift-Ware->



























                                   Version  1.2
                                    April 1991




                                 I. Introduction

        CBEEP, DBEEP, and the associated files were designed to allow the
        replacement  of the usual beep sound (which many programs use  to
        get  the user's attention) with a visual flash.   Potential  uses
        for  such a capability are to allow a hearing-impaired person  to
        sense  the beep or to avoid disturbing normal-hearing people  yet
        allow  the program to signal the user.  This is  accomplished  by
        replacing  the  code  which generates the  beep  sound  with  new
        program  instructions  which  replace the beep with  a  flash  of
        selectable  size and duration.  Although the copyright  has  been
        retained,  there is no charge for use of these programs and  they
        may  freely be copied and distributed to others as long  as  they
        are not modified and all files, including this documentation, are
        included.


                             II.  Installation and Use

        The primary programs in this package are CBEEP.COM and DBEEP.COM.
        They  will usually be referred to without their  .COM  extensions
        for  convenience.  DBEEP is first used to produce a  new  renamed
        version  of any program which has the beep replaced by  a  flash.
        Then  CBEEP is loaded into the computer's memory.  CBEEP  is  the
        program which actually makes the flash when called upon to do  so
        by  the  debeeped program.  Finally the debeeped version  of  the
        program  is loaded and run.  After some initial preparation,  the
        use  of the debeeped version of a program can be made  completely
        automatic and transparent to the user.

        First, the program to be debeeped must be selected.  Programs can
        be  recognized  by their file extension of  .COM  (for  "command"
        or .EXE (for "executable").  DBEEP, CBEEP, and the program to  be
        debeeped  should  all be placed in the  same  subdirectory.   For
        simplicity, this may be the subdirectory in which the program  to
        be debeeped was initially located.  That subdirectory should next
        be  made  the current subdirectory.  Then the  debeeping  program
        DBEEP should be started by entering its name from the DOS command
        line. If the program to be debeeped was NOISY.EXE in subdirectory
        C:\PROGRAMS,  and  if  CBEEP  and DBEEP were  on  a  floppy  disk
        inserted in floppy disk Drive A:, this might be done by something
        like

                  C:
                  CD \PROGRAMS
                  COPY A:CBEEP.COM
                  COPY A:DBEEP.COM
                  DBEEP

        This  will start execution of the debeeping program.  DBEEP  will
        display  a  menu  where <F1> may be pressed  to  display  a  help
        screen,  <F2> may be pressed to start the debeeping process,  and
        <F3>  may be pressed to install CBEEP in the computer.  For  now,
        let's wait a bit before installing CBEEP and go on to create  the
        debeeped  version  of the program.  Press <F2> and  you  will  be


        _________________________________________________________________
                                 CBEEP - DBEEP                     Page 2




        prompted to enter the name of the program to be debeeped.  In our
        example,  the program was NOISY.EXE in subdirectory  PROGRAMS  on
        Drive C:, so enter

                  C:\PROGRAMS\NOISY.EXE

        If   you   followed  the  previous  instructions,   the   current
        subdirectory  would  have  been C:\PROGRAMS,  so  the  full  path
        reference would not have been necessary, just entering  NOISY.EXE
        would have been ok. Next you will be prompted for the name of the
        new  (debeeped) version of the program which you want to  create.
        Select  any name with no more than eight letters in the name  and
        use the same extension (the ".COM" or ".EXE") as was used in  the
        original program.  It is very important to use the same extension
        but the name should be different from the original name.  In  our
        case  we might select the name NOTNOISY.EXE as our  new  program.
        After  you  enter  the new program name,  DBEEP  will  begin  the
        debeeping  process. You will see from the display on  the  screen
        that the process has begun and the display will indicate when the
        debeeping  process  has finished; this may take a minute  or  so.
        After DBEEP has finished, you may  press <F3> to "launch"  CBEEP.
        This places into the computer's memory the program which produces
        the  flash when called upon to do so by the debeeped  version  of
        the  program.  As part of the process of installing or  launching
        CBEEP,  the  CBEEP  menu  will  be  displayed  which  will  allow
        selecting  the size and duration of the flash.  Press the  number
        keys  as  indicated to select your  preferred  choice.   Finally,
        after completing the creation of the debeeped program (which  you
        have  given  a new name) and installing CBEEP, you are  ready  to
        exit from DBEEP which may be done by pressing the <Esc> key.  You
        will now be back at the DOS prompt and may run your new  debeeped
        version of the program by entering its new name.  In our example,
        merely enter NOTNOISY.  That's all there is to it.

        In  some cases, you may see the message "NO BEEPERS  FOUND"  even
        though you know that the program produces beeps.  In most  cases,
        this  will  not cause a problem and the beeps  will  properly  be
        intercepted  and  replaced by flashes.  A further  discussion  of
        this will be found in the section for Advanced Topics.

        Once  it has been created, it is not necessary to go through  all
        the  previous steps to run the debeeped program again.   Normally
        CBEEP will stay in memory ready to do its job until the  computer
        is rebooted or the power is turned off.  The debeeped version  of
        your program (i.e. NOTNOISY.EXE in the example above) will remain
        available  for  use.   All you have to do to run  the  program  a
        second  time is to move to the proper subdirectory and enter  the
        debeeped program's name again.  In our example,

                  C:
                  CD \PROGRAMS
                  NOTNOISY

        If  the computer has been rebooted or the power has  been  turned
        off,  it  will  be necessary to reload CBEEP  in  the  computer's


        _________________________________________________________________
                                 CBEEP - DBEEP                     Page 3




        memory. This can be done by entering DBEEP from the command  line
        and  then  pressing <F3> and continuing to install CBEEP  as  was
        done  before.  A shortcut which can be used if you  remember  the
        number  of  the menu item you used to select the flash  size  and
        duration is to skip the use of DBEEP and just enter CBEEP /n from
        the  DOS  command  line, where for "n" you enter  the  menu  item
        selection.   For example, to get a large, 1/2 sec.  flash,  enter
        CBEEP /2.

        If you use the debeeped versions of your programs frequently, you
        may want to place the CBEEP /n command in your AUTOEXEC.BAT  file
        where it will cause CBEEP to be automatically installed each time
        you reboot or power up your computer.

        The  previous instructions were written for use with  a  computer
        with  a  hard disk.  If you have two floppy  disks  instead,  the
        instructions  will generally be the same except that  you  should
        replace  "C:" with "B:" wherever it appears.  You will,  however,
        have to be sure there is enough room on the floppy in Drive B: to
        hold CBEEP, DBEEP, and the new debeeped version of your program.

        If  you have only a single floppy disk, it is still  possible  to
        follow  a similar process.  If you are a  reasonably  experienced
        DOS  user,  you can probably figure out how to modify  the  above
        instructions.   If you are not sufficiently experienced, it  will
        probably be best to get help from a more experienced friend.


                                   III.  History

        The idea for this program came from a Letter to the Editor in the
        January  1991 issue of Consumer Reports magazine where  a  father
        complained about the beep from his son's word processor not being
        useful  as his son was hearing-impaired.  Dave Hickman  posted  a
        notice  on  CompuServe,  an  international  computer  information
        network,  in  the  IBMSYS  forum, a  section  devoted  to  system
        utilities  for IBM-compatible computers, asking if  anyone  might
        want  to develop a program to replace a beep with a flash.   Bill
        Cravener  responded  that he had previously developed  a  similar
        program  as  a  programming  exercise.   After  some  significant
        refinement  and  extension of the original program by  Bill,  the
        current  versions  of CBEEP and DBEEP were born.   Bill  Cravener
        contributed all of the programming and Dave Hickman provided some
        testing, comments, and this user documentation.

        Several  useful  comments were contributed  by  other  CompuServe
        members  which helped to improve the programs.  There was also  a
        discussion  of  doing  the same thing  in  hardware  rather  than
        software.   Although a hardware approach has some advantages,  it
        has  some  significant  drawbacks too, and as  it  would  require
        disassembly  and (very minor) modification of the  computer,  the
        software approach chosen here was considered to be useful.   Once
        a  debeeped  version  of a program has been created,  it  can  be
        easily transported to any other computer.  The hardware  approach
        is  less readily portable.  For those wishing to contact Dave  or


        _________________________________________________________________
                                 CBEEP - DBEEP                     Page 4




        Bill,  the  easiest way is through  CompuServe's  E-Mail  system.
        Their CompuServe account numbers are

                  Bill Cravener [72230,1306]
                  Dave Hickman [72611,2106]



                               IV.  Advanced Topics

        The previous sections have been written assuming some familiarity
        with  DOS  on  the part of the user, but that he  does  not  have
        advanced  knowledge.   For  the more  advanced  user,  additional
        information,  not  usually  needed,  will  be  included  in  this
        section.

        CBEEP.COM is a terminate-and-stay-resident (TSR) program which is
        called by the debeeped program.  DBEEP.COM searches the  original
        user's  program and replaces all code which generates beeps  with
        code  which generates a software interrupt.   Normally  interrupt
        60H  is  used,  but  CHGINT.COM may be  used  to  select  another
        interrupt if 60H causes interference with other users of the same
        interrupt. CBEEP, DBEEP, and CHGINT should be placed in the  same
        subdirectory, and CHGINT run.  That will display a menu  allowing
        selection  of an alternate interrupt number in the range  60H  to
        66H.  You should be very careful about using interrupt 67H as  it
        is used for LIM EMS (an Expanded Memory manager) in all  versions
        of  DOS beginning with DOS 2.0 although only officially  reserved
        by DOS in DOS 4.0 and above.

        C/DBEEP  should be compatible with all versions of DOS  from  DOS
        2.0  on  and should work with MDA, Hercules, CGA,  EGA,  and  VGA
        display adapters.

        If  the space taken up by CBEEP is needed in order to  run  large
        applications or if there are conflicts with other TSRs, CBEEP may
        be  uninstalled by entering CBEEP /U from the DOS  command  line.
        This  can  be done only if no other TSRs have been  loaded  after
        CBEEP.   If  you  need to load additional TSRs  after  CBEEP  and
        unload  them  (as  well as CBEEP), you may want to  look  at  TSR
        control programs such as PC Magazine's INSTALL and REMOVE or  the
        well  known MARK and RELEASE (usually contained in  a  compressed
        archive  called  TSRCOM.ARC or TSRCOM.ZIP)  or  their  commercial
        equivalents such as POPDROP.

        If  you  want to suppress the messages output by  CBEEP  when  it
        loads  and  unloads,  you can redirect the output  to  NUL.   For
        example  CBEEP /1 > NUL will result in no output to  the  screen.
        The installation message can also be suppressed by adding "x"  to
        the size/duration switch, CBEEP /1x.

        Beeps can be generated in several ways.  The best-behaved  method
        is to use DOS' BIOS services to send a BEL (character code 7)  to
        the  screen.  An alternate method is directly to  manipulate  the
        hardware  which controls the speaker.  This is done by using  the


        _________________________________________________________________
                                 CBEEP - DBEEP                     Page 5




        OUT  instruction to change the two low order bits of port 61H  to
        turn  the  speaker on and off.  DBEEP looks for  the  code  which
        generates  such  instructions  and replaces it  with  a  software
        interrupt (using either the default interrupt number of 60H or an
        alternate  interrupt  number  selected via  CHGINT),  padding  as
        needed  with NOPs. A reasonableness check of surrounding data  is
        made  in order to distinguish code from data prior  to  replacing
        the  beep codes.  This technique for handling direct port  writes
        was suggested by Dave Fallen's SILENCER program code.

        In some cases the message "NO BEEPERS FOUND" is produced by DBEEP
        even  though the code being debeeped is known to  produce  beeps.
        This is generally caused by code which does not write directly to
        hardware ports but merely uses DOS or BIOS services to produce  a
        beep by sending the BEL character to the screen.  The  interrupts
        used  by these services are trapped by CBEEP and thus  the  beeps
        are  properly  converted  into flashes even  though  no  code  is
        modified by DBEEP.  The message "NO BEEPERS FOUND" thus indicates
        that  no  code  replacement was necessary rather  than  that  the
        program being debeeped doesn't have any beep-producing code.

        There are a few known limitations to this procedure.   Compressed
        executable  code will not generally allow the instructions to  be
        properly identified.  If the compression technique which has been
        used  is known, it may be possible to uncompress the code,  apply
        the  debeeping  program  to the uncompressed  version,  and  then
        recompress  the  debeeped version.  Microsoft  Windows  code  may
        cause  problems.   Programs  which have been  compressed  can  be
        identified  (along  with the compression technique used)  by  the
        utility   CHK4COMP.EXE.   Many  commercial  programs  have   been
        compressed by Microsoft's EXEPACK; these may be unpacked by using
        UPACKEXE.EXE.   As  of this writing, CHK4COMP could  be  obtained
        from  CompuServe IBMSYS in CKH4.ZIP; UPACKEXE was also  available
        from CompuServe IBMSYS in LZEX91.ZIP.

        C/DBEEP  has not been tested for use on overlays.   For  standard
        overlays  it  may be possible to debeep the  overlays  just  like
        a .COM or .EXE file.  Borland's VROOMM (TM) overlays are known to
        cause problems (they are identifiable by the .VRM extension).  In
        particular, the file Q.VRM in Quattro Pro 1.0 may not be debeeped
        using the standard method.

        Generally  it  is anticipated that for a  hearing-impaired  user,
        CBEEP  will be installed by a line in AUTOEXEC.BAT and  that  the
        debeeped program will be called instead of the standard  version,
        either  through use of batch files or by renaming.  In  case  the
        application  program  needs  to be used in both a  normal  and  a
        debeeped  mode, both versions (with different names,  of  course)
        may be used at any time. The original code is never modified.


                                 V.  Disclaimer

        The  software and documentation in this packare are provided  "As
        Is"  without  warranty  of any kind.   >>-Swift-Ware->  does  not


        _________________________________________________________________
                                 CBEEP - DBEEP                     Page 6




        warrant,  guarantee,  or make any representations  regarding  the
        use, or the results of use, of this software.  All risk taken  in
        the use of this software is assumed by you, the user, and not  by
        >>-Swift-Ware->,  nor  by  any person  or  organization  who  may
        distribute this product.


                              VI.  Revision History

        1.0 - January, 1991 - Original release.
        1.1 - Removed autoloading of CBEEP
        1.2 - April, 1991 - Code same as 1.1, documentation updated

OTHER PROGRAMS by the AUTHOR:

BOBCAT ($15.00) ....... Lets anyone manage their Files and Directories,
                        with an easy press of a key you can copy, move
                        delete, view, mark, create, edit, compress, -
                        uncompress, format - plus enables the user to
                        assign up to 20 of his or her commands or favorite
                        programs to the menuing system and many more -
                        features from within a window environment...


MENU MAKER ($10.00) ... Makes it easy for anyone to create beautiful
                        stand alone - 3D Text mode graphic shadow box
                        window menus. Create up to 4 windows you can pop
                        down by the press of a function key then highlight
                        your commands or program names via menu bar or -
                        mouse to activate them.


REDEFINE ($10.00) ..... Enables assigning up to 20/60 character command -
                        strings to any of the Alt + Number keys or function
                        keys F1 to F10 plus recall your last 10 DOS commands.

                        Also includes many utilities - View files, Copy,
                        Delete, Rename, Show All Paths, NotePad, and many
                        more in an easily Deactivated Pop Down TSR.
                           

 GRAB4 ($10.00) ....... TSR that makes it an easy task to capture text
                        mode screens from within most any running program.
                        Enables saving screens as Executables including -
                        their color values, or save as a readable text mode
                        ASCII file, you can also edit any current or saved
                        screen and capture or append to another file.
                        Easily Deactivated.

------------------------------- END OF DOCUMENT --------------------------------