COREtest - Disk Performance Test Program v2.91

    This program will measure the performance of one or two hard disk
    drives.  The evaluation is made using three tests:  data transfer,
    random seek, and track-to-track seek.  The program will not destroy any
    data on the disk and may be run as many times as desired.

    The data transfer test measures the performance of the computer, disk
    controller, and drive functioning as a combined unit.  This is
    accomplished by reading repeatedly a specific block of data and timing
    each transfer.  The resulting effective transfer rate is produced from
    the combined relationship of the computer bus structure (8, 16, or 32
    bits), the transfer rate of the controller with the drive, the
    interleave factor for which the drive was formatted, and the size of the
    data block transferred.

    The block size is automatically calculated or may be explicitly set from
    1 to 64K in 1K increments.  If automatically calculated, the block size
    will be set to 64K or the amount of data stored on one cylinder,
    whichever is less.  The transfer rate is displayed in units of kilobytes
    per second (KB/sec).  This indicates how much data will be moved from
    the disk to memory in one second.

    The next two tests measure the time required to position the read/write
    heads to a specific location where data is stored.  The first of these
    tests will measure what is referred to as the "average access time" by
    moving the heads across one-third of the cylinders, simulating true
    random access.  The final test will measure the time to move the heads
    from one track to an adjacent track, measuring the "track-to-track
    access time." Both these results are reported in milliseconds (ms =
    thousandths of a second).  The smaller the access time, the faster the
    data may be located and transferred to the computer.

    After the tests are complete, a "performance index" is calculated for
    the tested system.  This number measures the overall performance of a
    given computer, the disk controller, and its hard disk.  It may be used
    to evaluate the performance of different computer systems on a
    comparable scale.  For example, a standard IBM 10MB XT system will
    typically report an index of one while an IBM 20MB AT will yield an
    index of approximately 2.4.  The higher the index, the more powerful the
    computer system.  It can generally be said that a computer with a
    performance index of two is twice as fast as a computer with an index of
    one.

                             Caching  Information
    If COREtest detects that a cache program is installed, it will display
    a message indicating same.  The presence of a cache program can mis-
    represent the actual drive performance.  When comparing the performance
    of disk drives, you should do so without any cache programs installed.
    This will give a true representation of the actual drive performance.

                               Ranking screen
    The final screen displays where your drive(s) rank compared to others
    in the industry.

    Various options are available to change the test parameters to better
    compare performance across a wide variety of applications.  These
    options must be placed on the command line when program execution is
    started.  The format of the command line and the option descriptions are
    given below:

    CORETEST [?] [HELP] [/B:xx] [/C:xxx] [/D:n[="xxx"]] [/P:xx] [/T:xxx]

    Format  Description
    ------  -----------
    /B:xx   Use a block size of xxK.  The block size may be up to
            64K.  Default is the largest transfer possible without
            moving the disk heads.
    /C:xxx  Set maximum seek stroke to xxx.  This is used to set drives to
            equal cylinder comparisons. If not specified, then the full
            cylinder range of the drive will be used (default).
    /D:n[="xxx"]  Test disk number n (n = 0-7).  This parameter may appear
            up to two times. If a string is enclosed in quotes, then this
            string will be used to identify the drive on the display.  If
            omitted, up to the first two drives will be tested.
    /P:xx   Pause for xx seconds when test complete (for batch files).
    /T:xxx  Perform transfer test for xxx seconds (default = 4 seconds).