ALIGN
                 Version 2.9 for IBM Personal Computers
                             11/26/87

    (c) Copyright John L. Dickinson 1983, 1987.  All rights reserved.

DISCLAIMER

   This program is provided "as-is" without warranty of any kind,
   either expressed or implied, including, but not limited to the
   implied warranties of merchantability and fitness for a particular
   purpose.  The entire risk as to the quality and performance of the
   program is with you.

   In no event will I be liable to you for any damages, including any
   lost profits, lost savings or other incidental or consequential
   damages arising out of the use or inability to use this program
   even if I have been advised of the possibility of such damages, or
   for any claim by any other party.


COPYING PROVISIONS

   This program and documentation may be freely copied and shared
   provided it is not modified in any manner and this notice is not
   bypassed or removed.  Please register by sending your name,
   address and any comments to the author.  There is no charge.

                        John L. Dickinson
                        2470 N. Tierra Verde Pl.
                        Tucson, Arizona 85749-9315


OVERVIEW

   The ALIGN program allows you to move a diskette drive head to
   absolute track locations and operate the drive while checks and
   adjustments are made.  48, 96, and 135 tracks per inch (TPI)
   diskette drives are supported.  These include 40 and 80 track 5
   1/4 inch drives as well as 80 track 3 1/2 inch drives.  The PC-AT
   High Capacity drive and Personal System/2 High Density drives are
   also supported.

   You may also be interested in a companion program called DRIVECHK
   which is a diskette drive diagnostic program that uses the
   Xidex/Dysan Digital Diagnostic Disk (DDD).

   ALIGN is one of several tools needed to adjust and service
   diskette drives.  The ALIGN program does not attempt to teach you
   how to do an alignment, but it isn't difficult if you have what
   you need.

   In addition to this program, you should have:

     The drive manufacturer's alignment and service procedures.

     An oscilloscope (dual trace with triggered sweep).

     A XIDEX/DYSAN double-sided Analog Alignment Diskette (AAD) for
     the drive to be serviced (not required for SPEED test):

                           Xidex-      Xidex-
       Size   TPI Tracks Dysan Model Dysan P/N Current Price Each
       ------ --- ------ ----------- --------- ------------------
       5 1/4"  48   40     224/2A     800180        $50.00
       5 1/4"  96   80     206-31     802166        $50.00
       3 1/2" 135   80     350/2A     810234        $50.00

     The above disks are double-sided.  224/2A is used for the
     majority of PC drives which are 40 track.  206-31 can be used
     for either the PC-AT's High Capacity drive or a user attached 80
     track drive.  350/2A is for 3 1/2 inch drives.  Xidex/Dysan also
     makes Analog Alignment Diskettes for other drives, but they
     aren't directly supported by ALIGN.  You may still be able to
     use ALIGN to step the drive.

     Extension or external diskette drive signal and power cables are
     very helpful.

   See the notes at the end of this document for possible sources for
   these items.

   An Analog Alignment Diskette contains NO data, just special
   waveforms and can't be copied.  (It's really copy protected!) You
   can try the program using any diskette.  The ALIGN program does
   not write on diskettes.


SYSTEM AND DISKETTE DRIVE REQUIREMENTS

   ALIGN runs under IBM PC-DOS version 2.0 or later on a PC, PC-XT,
   PC-AT, PC Convertible or Personal System/2 with at least 128K.  An
   80 column display, either monochrome or color is required.

   Since ALIGN uses standard BIOS interfaces for all I/O, it should
   also work on most IBM compatibles.  It does not work properly on
   the PCjr.

   The diskette drives to be adjusted are connected to the PC in the
   usual manner.  The ALIGN program works with standard IBM diskette
   drives and should work with others that use the same electrical
   interface.  ALIGN has no provisions for changing the BIOS diskette
   parameter tables - step time, settle time, etc.


USING THE ALIGN PROGRAM

   The ALIGN program consists of the single file ALIGN.EXE.  There is
   no installation other than copying it to your program diskette.

   Boot DOS and insert the ALIGN program disk in any working drive.

   After the DOS prompt, enter ALIGN (preceded by a drive specifier,
   if necessary) and press Enter.  Once ALIGN is loaded, the program
   disk is no longer needed in the system.

   Press any key to get past the initial screen to the main command
   menu.

   Commands are entered one at a time in ALIGN's command area to
   control the diskette drive under test.  All commands may be
   abbreviated and the first letter is sufficient for most commands.
   (INFO, TYPE and TPI require more.)

   If you are testing the "A" drive, ALIGN's default of DRIVE 0 is
   correct.  If you are testing the "B" drive enter DRIVE 1 to select
   it.  See the DRIVE command description for more information or if
   you are testing an external diskette drive.

   Chances are, you'll be able to use the program without reading any
   more of this documentation.

   Some commands require operands as listed on the menu.  Numeric
   operands, such as track number or seconds, are decimal.  The first
   track is track 0, not track 1.

   If the diskette drive under test is running, pressing (almost) any
   key will cause it to stop in about 2 seconds.  This key may be the
   first letter of the next command or any key such as the Enter key.
   The drive will stop by itself after 60 seconds.

   To increment or decrement the current track number, use the cursor
   up and cursor down keys on the numeric keypad.  If the drive is
   not running, it will start.

   If the drive is stopped and and you want to continue the previous
   motion command, simply press the Enter key.  This enters a null
   command which is interpreted just like a GO command.

   Commonly used commands may also be entered using the program
   function keys as shown on the command menu.

   When finished, enter Q or QUIT to return to DOS.


ALIGN COMMAND MENU

|-----------| |----------------------------------------------------------------|
|     |     | | Altseek trk trk     Alternate seek between two tracks          |
| IN  | OUT | | Cycle               Cycle tracks 3,2,1,0,3,2,1,0,3,2,1...      |
| (1) | (2) | | Drive   <0,1,2,3>   Selects a drive number  (default 0)        |
|-----|-----| | Go or (null)        Start drive motion                         |
|     |     | | Head    0..1        Set head                                   |
| T 0 | H 1 | | In                  Move to track 0, then to cat's eye.        |
| (3) | (4) | | INFo                Display alignment disk track information   |
|-----|-----| | Max     39..255     Set maximum track allowed.                 |
|     |     | | Out                 Move toward center hub, then to cat's eye. |
| T 1 | H 0 | | Pause   0..180      Set seconds to pause at second ALTSEEK trk |
| (5) | (6) | | Quit                Quit and return to DOS                     |
|-----|-----| | Reset               Reset diskette system                      |
|     |     | | Seconds 3..999      Set length of time to run drive            |
|T 34 |CYCLE| | Speed               Display spindle speed. (Use DOS diskette)  |
| (7) | (8) | | TPi     <48,96,135> Specifies track density of diskette        |
|-----|-----| | Track   0..max      Set track and run drive                    |
|STOP/|     | | TYpe    <REG,HC,X2> 'regular', High Capacity or double-step    |
| GO  |RESET| |----------------------------------------------------------------|
| (9) |(10) |       DRIVE  TPI  TYPE  HEAD  TRACK  MAX  SECONDS  PAUSE
|-----------|         0     48   REG    0     16    39     60       0
Function Keys
-------------  Enter command:
up= Incr. Trk
dn= Decr. Trk

(up and dn are the cursor keys)



DETAILED COMMAND DESCRIPTIONS (in alphabetical order)

   ALTSEEK trk trk

     The ALTSEEK (alternate seek) command causes the drive to start
     and do a head seek back and forth between the two specified
     tracks.

     Since ALIGN provides the CYCLE command to test and adjust the
     track 0 switch, there really isn't any particular reason for
     using the ALTSEEK command.  It might be useful if you have some
     special tests or just enjoy watching the head move.

     Normally, the head moves back and forth as fast as ALIGN, the
     system BIOS and the disk drive hardware can go.  The PAUSE
     command can be used before the ALTSEEK command to cause the head
     to pause at the second specified track.  If you want the pause
     to be at the first specified track, reverse the the two tracks
     in the ALTSEEK command line.

     Examples:
                        ALTSEEK 5 15
                        A 0 1
                        A 26 16


   CYCLE

     The CYCLE command starts the drive and cycles the head through
     tracks 0 through 3 in the following order 3,2,1,0,3,2,1,0,3,2...
     and so on for the purpose of checking the track 0 switch.  The
     drive changes tracks every few seconds so you have time to see
     if the track 0 switch has switched.  In between each track
     (0,1,2 or 3) the CYCLE command moves the head to track 16 so
     there is a seek similar to that when a drive is first used after
     power-on.

     Believe it or not, on Tandon TM-100 series drives, the track 0
     switch should switch between tracks 1 and 2.  (It's NOT supposed
     to switch at track 0!)  This is a position in the middle of the
     first four tracks.  The actual track 0 signal on the drive
     interface is a combination of the track "0" switch and other
     indications in the drive electronics.

                            Switch here
                                 |
                                 V
                        0     1     2     3

     While the CYCLE command is active, the PC's speaker sounds rapid
     beeps equal to the current track number, 1 to 3, each time it
     changes tracks.  Track 0 is a single longer beep.  These beeps
     allow you to know what track the drive is on without trying to
     watch a meter or test light and the PC's display at the same
     time.  A higher pitch sounds in addition to the track beeps when
     the switch should switch.  After a little practice, the sound
     eliminates the need to watch the screen.  As you watch your
     meter or light, don't be confused by the very brief switch
     changes when the head moves to track 16 and then back toward
     track 0.

     While it's always nice to set things "right on," the track 0
     switch adjustment isn't critical and the drive operates fine
     even when it switches a whole track off from the ideal point
     between tracks 1 and 2.


   DRIVE  <0,1,2,3>

     The DRIVE command specifies which physical drive is under test
     using a drive address number of 0, 1, 2 or 3.  The default is
     drive 0 which is the first internal diskette drive.  The DRIVE
     command does not cause the drive to start.  Examples:

                        DRIVE 0         (Set drive 0)
                        D 2             (Set drive 2)

     The drive number designates a physical drive address and not a
     DOS drive letter or a drive letter associated with a special
     device driver such as DOS 3.2's DRIVER.SYS.  (DRIVER.SYS may
     be installed for any diskette drive, but it is not used or
     needed by the ALIGN program.)

     Drive address numbers are:

      0  First internal diskette drive.  Identified by DOS as
         as "A" (or "A" and "B" when only one internal diskette
         drive is installed.)

      1  Second internal diskette drive.  Identified by DOS as "B".

      2  First external diskette drive.

      3  Second external diskette drive.

     The drive letter that DOS assigns to external drives varies and
     depends on the number of fixed disks, system board switch
     settings and device drivers.  ALIGN doesn't care what letter DOS
     uses.


   GO

     If the drive is stopped, the GO command simply starts the drive
     at whatever track it happens to be on.  A null entry does the
     same thing, so you can just press the Enter key with nothing on
     the command line to start the drive.


   HEAD  0..1

     The HEAD command selects the lower or upper head (diskette side)
     and starts the drive.  HEAD 0 is the lower head and the only
     head on a single-sided drive.  HEAD 1 specifies the upper head
     on a double-sided drive.

     It may seem strange that the HEAD command starts the drive.
     This allows rapid switching to compare heads by simply
     alternating the two HEAD command program function keys.

     Examples:

                        HEAD 0          (Set head 0, the lower head)
                        HEAD 1          (Set head 1, the upper head)
                        H 1             (Set head 1, the upper head)


   IN
   OUT

     The IN command moves the head first to track 0 and then "in"
     towards the center, stopping on the radial alignment (cat's eye)
     track.

     The OUT command is similar, but moves the head first toward the
     center spindle and then immediately moves it "out" away from the
     center, stopping on the radial alignment track.

     IN and OUT each have the same effect as entering two TRACK
     commands.

     Both commands end up on the radial alignment track with the
     drive running.  The ending track depends on the Analog Alignment
     Diskette specified with the TPI command:

                 TPI   Radial alignment track
                 ---   ----------------------
                  48           16
                  96           32
                 135           40

     After making a head adjustment it's a good idea to re-seek to
     the radial alignment track and check the cat's eye pattern
     again.  Both the IN and OUT commands cause a re-seek to this
     track.  The two commands also allow checking the accuracy of
     seeks (and the resulting head alignment) in both directions.  If
     there is a difference in the cat's eye patterns in the two
     directions, you may want to re-adjust the alignment to split the
     difference.  A difference indicates play in the mechanism or an
     imprecise head stepper motor.


   INFO

     The INFO command causes another screen to be displayed with a
     brief description of each track on the Xidex/Dysan Alignment
     Disk.  It's simply for reference.

     The information displayed depends on the Analog Alignment
     Diskette specified with the TPI command.

     Pressing any key returns you to the ALIGN command menu screen.


   MAX 39..255

     The MAX command sets the maximum track allowed with the TRACK
     command.

     Normally, the TRACK and ALTSEEK commands accept track numbers
     from 0 through 39 or 79 depending on the current value specified
     with the TPI command.  The MAX command allows you to change the
     high track limit all the way up to 255.  The MAX command does
     not cause the drive to start.

     There really isn't much occasion to use the MAX command.  Maybe
     you're looking for the track 39 signal on the XIDEX/DYSAN
     alignment disk.  If it doesn't appear on what the system thinks
     is track 39, maybe it will show up at what the system thinks is
     track 40, or 41 or....

     Actually, there is a limit to how far the head will go past
     track 39.  You may want to use the MAX command to allow you to
     investigate just how much further the head will go.  (A copy
     protection scheme might use one track past the "end" of the
     disk.)

     However, before you go charging off into the stratosphere of
     track addressing, realize that when the head hits the upper
     limit, it does so with the full force of the stepper motor.
     This alone could knock a drive out of alignment or possibly
     cause permanent damage.  Use the MAX command at your own risk.


   OUT

     See IN command description.


   PAUSE  0..180

     The PAUSE command can be used before the ALTSEEK command to
     cause the head to pause at the second track specified on the
     ALTSEEK command line.  The PAUSE operand specifies the number of
     seconds to wait.  The PAUSE command does not cause the drive to
     start.

     The pause is approximate and may vary by up to about a second
     from that specified.  Note too that the SECONDS command value
     should be larger than the PAUSE value for PAUSE to be useful.
     Otherwise the drive may stop during the PAUSE period.

     See the ALTSEEK command description.

     Examples:
                        P 5                        (5 seconds)
                        PAUSE 60                   (1 minute)

   QUIT

     The QUIT command ends the ALIGN program and returns to DOS.


   RESET

     The RESET command causes a reset of the diskette system (via
     BIOS INT 13 with AH=0).  RESET does not cause the drive to
     start.

     After entering RESET, the next time any drive is accessed it
     will then be "recalibrated."  This means that the diskette
     controller makes no assumptions about which track the head is
     on, moves the head until track 0 is located as indicated by the
     drive, and then proceeds with the requested operation.  Once
     this recalibration process is complete, the diskette controller
     keeps it's own head position register and simply pulses the head
     forward or back, one step at a time to get to a desired track.
     If one pulse is missed or the head is moved manually with
     power-on, then the controller's track register won't agree with
     the physical position of the head.

     "Recalibration" is not an adjustment, but rather a normal
     operation done by the diskette controller so it can get in sync
     with the physical head position.  Every drive is "calibrated" by
     the controller the first time you use it after power-on or boot.

     The RESET command allows you to recalibrate during the drive
     adjustment procedure.  For instance, assume the the drive is on
     track 16 (or what you think is track 16).  If you issue a RESET
     command and then simply start the drive motion (null entry), you
     will hear the drive move to track 0 and then back out to track
     16 as the drive is recalibrated.

     The RESET command is useful when servicing drives and you think
     the drive is not seeking to the correct track.  This could
     happen while adjusting the track 0 switch.  Also, the drive
     won't seek to the correct track anytime the head has been moved
     against the stepper's electrical hold.  This could occur when
     the head assembly hits it's travel limit at either end.  This
     isn't normal operation, but when the adjustments are wrong it
     can (and does) happen.

     If you don't find an alignment disk signal where you think it
     should be, try the RESET command.  It is also a good idea to use
     the RESET command just before the final checks on radial head
     alignment to be sure you're not exactly 1 or 2 tracks off.
     ALIGN does an automatic RESET between every CYCLE command seek
     to make track 0 switch adjustment easier.

     Without the RESET command, it would otherwise be necessary to
     re-boot or turn the machine off-and-on to force a recalibrate
     operation.


   SECONDS  3..999

     Normally, each time you start the drive using ALIGN, the drive
     runs for 60 seconds if not stopped by pressing any key.  This is
     usually enough time to make a check or adjustment and prevents
     the drive from running "forever".

     The SECONDS command allows you to change this 60 second limit
     anywhere from 3 to 998 seconds.  A value of 999 means there is
     no limit and the drive will run continuously until stopped by
     pressing a key.

     The SECONDS command does not cause the drive to start.
     Examples:

                        SECONDS 120                (2 minutes)
                        S 10
                        S 999                      (no limit)


   SPEED command

     The SPEED command measures diskette drive spindle speed which is
     the speed the diskette rotates.  It also gives and indication of
     the Instantaneous Speed Variation or ISV.  ISV is a short term
     speed variation which doesn't show in the average speed.
     Possible causes of high ISV are things such as incorrect belt
     adjustment, binding, motor cogging or poor brush contact.

     SPEED requires a regular DOS formatted diskette and does not work
     with the Xidex/Dysan AAD, Analog Alignment Diskette used with
     most other ALIGN commands.  The SPEED command does not write on
     the diskette (nor does any ALIGN program command.)

     The SPEED command has no operands, but the drive should be
     properly specified with the DRIVE, TPI and TYPE commands first,
     if necessary.  SPEED also uses current values as displayed for
     the track and head, either by default or from prior ALIGN
     commands.  The track and head should not affect the measured
     speed, although SPEED must find a valid sector on the indicated
     track and head.  ALIGN determines the speed by measuring the time
     between successive reads of sector 1.

     To use the SPEED command, insert a DOS formatted diskette and
     simply enter SPEED.  Let it run for a few seconds, stopping it
     with any key.  It you don't stop it, it runs for 60 seconds or
     whatever time has been set with the SECONDS command.

     Nearly all diskette drives have a nominal speed of 300 RPM.  The
     only IBM exception at this time is the PC-AT's High Capacity
     drive which has a nominal speed of 360 RPM.  The PC-AT High
     Capacity drive runs at 360 RPM regardless of the type of media it
     is using.

     Spindle speed accuracy is not as critical as the displayed
     numbers might suggest.  Most drives allow a speed tolerance of 1
     or 1.5 percent which is about plus or minus 3 or 4 RPM.  The
     actual speed also varies a bit due to the drag of different
     diskettes.  Some people over-emphasize spindle speed because it's
     about the only thing they can adjust without extra equipment.
     The SPEED command dumps out all those numbers more for
     entertainment than necessity.

     The measured speed will always be within the displayed range of
     approximately 280 to 320 RPM for 300 RPM drives and 330 to 390
     RPM for 360 RPM drives.  This is true even if the actual speed is
     outside that range and is the the result of the measurement
     method used by the program.  In practice, a drive whose speed is
     outside the range probably won't be working anyhow and may also
     show an erratic speed.  If there's any question, a look at the
     strobe on most drives will tell you very quickly if the drive is
     anywhere near the correct speed.

     There is another way to measure the speed if you think the
     actual speed is outside the displayed range and the drive reads
     without error.  Check to see that SECONDS had the default value
     of 60.  If not, enter SECONDS 60.  Then enter SPEED and let the
     drive run for the full minute.  The displayed "Measurement
     Number" at the end of the minute is the speed in RPM.  This is
     only accurate if there are no read errors.

     SPEED example:

           Current  Average  Maximum  Minimum  Percent  Measurement
             RPM      RPM      RPM      RPM      ISV      Number
            298.40   298.40   298.40   298.40    0.00       1
            298.37   298.38   298.40   298.37    0.01       2
            298.38   298.38   298.40   298.37    0.01       3
            298.40   298.39   298.40   298.37    0.01       4
            298.37   298.39   298.40   298.37    0.01       5
            298.38   298.38   298.40   298.37    0.01       6
            298.40   298.39   298.40   298.37    0.01       7
            298.37   298.38   298.40   298.37    0.01       8
            298.39   298.39   298.40   298.37    0.01       9
            298.41   298.39   298.41   298.37    0.01      10

            298.39   298.39   298.44   298.34    0.03      38

               280  285  290  295  300  305  310  315  320
     ÀÄÄÄÄÄÄÄÄÄ |....|....|....|....|....|....|....|....| ÄÄÄÄÄÄÄÄÄÙ
                                  ^

     The easiest part of the display to read is the speed meter on the
     bottom.  It indicates the current RPM and changes whenever the
     actual drive speed changes.  (It is not the average drive speed.
     However, if it doesn't move much, then the current and average
     will be the same thing.)  The arrow on the meter moves in one RPM
     increments, displaying the "Current RPM" rounded to the nearest
     whole RPM value, which is plenty close enough.

     You can probably ignore the rest of the SPEED display.  The first
     10 lines show individual statistics for the first 10 measured
     revolutions.  (SPEED lets the drive come up to operating speed
     and stabilize before starting measurement.)  "Current RPM" is for
     just one revolution.  All the other statistics are cumulative.
     The last line of statistics, separated with a blank line, is the
     data for the last revolution measured.  It is updated every
     revolution until the SPEED command is stopped or times out.  As
     all the values except "Current RPM" are cumulative, they tend to
     stabilize as the test progresses.

     "Current RPM" is the measured spindle speed for one revolution.

     "Average RPM" is the average of the spindle speed RPM
     measurements so far and is the best overall indication of spindle
     speed.

     "Maximum RPM" and "Minimum RPM" are the highest and lowest
     spindle speeds encountered during the test.

     "Percent ISV" is an indication of Instantaneous Speed Variation.
     It is calculated by taking the difference between the maximum and
     minimum speeds, dividing by the average speed and multiplying by
     100 to get a percentage value.  Drive factors are usually the
     cause of ISV problems.  However, keep in mind that the diskette
     and its jacket are part of the system which contributes to ISV,
     possibly by binding, buckling or other irregularities.

     The "Measurement Number" is the revolution number since the drive
     came up to speed and measurements started.


   TPI     <48,96,135>

     The TPI command specifies the track density of the Analog
     Alignment Disk (AAD) you are using.  48 is the default.  You may
     prefer to think in terms of the number of tracks instead.

                    TPI   Size    Tracks
                    ---   ------   ------
                     48   5 1/4"     40
                     96   5 1/4"     80
                    135   3 1/2"     80

     The TPI command does not cause the drive to start.

     Normally, you set TPI to match the physical drive to be tested.

     You can test the High Capacity drive on the PC-AT with either a
     96 TPI AAD or a 48 TPI AAD.  Testing it at 80 tracks with the
     model 206-31 96 TPI AAD certainly gives the best results.  But,
     if you only have the model 224/2A AAD for 48 TPI drives, you can
     still get useful displays by using it and specifying TPI 48 and
     TYPE REG.  The PC-AT will then double-step the High Capacity
     drive as it always does with 40 track diskettes.

     As with a High Capacity drive, a "regular" 80 track drive can be
     tested with either a 96 TPI AAD or 48 TPI AAD.  To use a 48 TPI
     AAD on an 80 track drive, specify TPI 48 and TYPE X2.  ALIGN
     will then double-step, multiplying all track numbers by 2 before
     all seeks.

     Don't do the reverse and specify TPI 96 or 135 on a 40 track
     drive as ALIGN will try to use tracks that aren't there and bang
     the head assembly against its travel limit.

     Examples:
                    TPI 48               (Set 48 tracks per inch AAD)
                    TP 96                (Set 96 tracks per inch AAD)


   TRACK  0..max

     The TRACK command moves the head to a specified track and starts
     drive motion.  The drive will continue to run until a key is
     pressed or for 60 seconds.  (The 60 second run time may be
     changed using the SECONDS command.)

     The track number that may be specified is in the range 0 through
     39 for 48 TPI drives and 0 through 79 for 96 TPI or 135 TPI
     drives.  The upper track limit may be extended using the MAX
     command.  Examples:

                        TRACK 0      (Move to track 0 and run drive)
                        T 34         (Move to track 34 and run drive)
                        T 16         (Move to track 16 and run drive)

     The track number can be incremented or decremented by one track
     using the cursor up and cursor down keys on the numeric keypad.
     This is easier than specifying the tracks one at a time with the
     TRACK command.  Use the TRACK command to move to the first
     desired track and use the cursor keys from that point.  Or,
     simply hold the cursor key until the desired track is reached.


   TYPE     <REG,HC,X2>

     The TYPE command specifies a "regular" diskette drive, the
     PC-AT's High Capacity drive or a "regular" drive that is to be
     double-stepped.  The Personal System/2 High Density drive is
     also considered a "regular" drive.  TYPE REG is the default.

         REG           Specifies a "regular" drive      (default)
         HC            Specifies a PC-AT High Capacity drive
         X2            Have ALIGN double-step a "regular" drive

     The TYPE command does not cause the drive to start.

     TYPE HC is only valid on the PC-AT.  (It attempts to run the
     drive at a 300 KBS data transfer rate, not the 500 KBS rate used
     with the special high capacity media.)

     While it's best to test the High Capacity drive as TYPE HC and
     TPI 96, if you only have a 48 TPI AAD diskette, you can use TYPE
     REG and TPI 48.  Similarly, an 80 track "regular" drive is best
     tested as TYPE REG and TPI 96, but you can use a 48 TPI AAD
     diskette by specifying TYPE X2 and TPI 48.  See the TPI command
     description.

     TYPE X2 is really only useful with TPI 48 and an 80 track
     regular drive.  However, ALIGN does no checking and will gladly
     attempt to double-step with TPI 96 or TPI 135 and bang the head
     carriage at its travel limit.  Be sure you understand X2 and
     what it means before you try it.

     Examples:
                   TYPE REG           (Specify "regular" drive)
                   TY HC              (Specify High Capacity drive)
                   TYPE X2            (Double-step a "regular" drive)


INSTANTANEOUS SPEED VARIATION TESTING

   ALIGN's SPEED command gives an indication of Instantaneous Speed
   Variation, ISV.  Since the SPEED command only checks the speed
   once per revolution, it is not a true ISV test.

   To test ISV with an oscilloscope, the Tandon manual says to first
   "write a 2F (all ones) pattern on any track." The ALIGN program
   won't write this or anything else on your diskettes.  A totally
   satisfactory substitute is to simply use the DOS FORMAT command to
   format a work diskette in the drive under test.  This puts a
   pattern on every track.  Admittedly, it's not "all ones" but
   you'll hardly know the difference as you observe the pulse jitter
   on the oscilloscope.  Also, while Tandon says to use "any" track,
   the jitter is much worse on the inside (high) tracks.  Use a
   middle track, such as the radial alignment track, to check the
   specification.  Get to know what normal jitter looks like on track
   0 and in towards the hub too (39 or 79).



MESSAGES

   (operand name) operand is too large.  Range=(min)...(max)

     Explanation:  The value you specified as a parameter is too
     large for the command you entered.

     Action:  Choose a value within the specified range and retry the
     command.

   (operand name) operand is too small.  Range=(min)...(max)

     Explanation:  The value you specified as a parameter is too
     small for the command you entered.

     Action:  Choose a value within the specified range and retry the
     command.

   (operand name) operand must be a numeric integer

     Explanation:  The value you specified as a parameter is not a
     valid numeric constant.

     Action:  Check the characters you entered and retry the command
     using numeric characters only for the operand value.  Decimal
     points, plus and minus signs are not permitted.

   Can't process.  HC is only correct with 96 TPI

     Explanation: A High Capacity drive has been specified with the
     TYPE command, but the current TPI (tracks per inch) is incorrect
     for a High Capacity drive.

     Action:  Either enter TPI 96 or change the drive type with the
     TYPE command.

   Diskette system has been reset

     Explanation:  This is an informational message displayed every
     time the RESET command is executed.  It indicates that the next
     time the drive is started, the diskette controller will
     re-calibrate the drive by seeking to track 0 before seeking to
     the current track.

     Action: None.

   Drive operand is not 0, 1, 2 or 3

     Explanation:  The specified diskette drive number must be 0, 1,
     2, or 3.

     Action:  Retry the command using the correct drive number.

   Error reading diskette

     Explanation:  The program encountered a disk error while reading
     the diskette for spindle speed testing.  Testing and measurement
     continues, although some of the calculated results may lose
     accuracy.  If you just get a single error, you can restart the
     speed test.  If you get this error continuously, then you are
     either using the wrong diskette or may have a solid diskette
     drive failure.

     Action:  Make sure you are using a regular DOS formatted
     diskette and that the DRIVE, TYPE and TPI values are properly
     set.  The ALIGN speed test only works with ordinary DOS
     formatted diskettes.

   Missing operand(s)

     Explanation:  Not enough operands were entered on the command
     line for the specified command.

     Action:  Re-enter the command with the proper number of operands
     as indicated in the command description.

   Running continuously

     Explanation:  The selected drive is running and will run until
     stopped.  This is the result of specifying SECONDS 999
     previously.

     Action: Press any key to stop the drive when you want it to
     stop.

   Running:  nnn seconds left

     Explanation:  The selected drive is running and will run for the
     specified number of seconds.

     Action:  Either let the drive run until the timer is up or press
     any key to stop the drive when you want it to stop.  If the
     drive isn't running long enough for you, increase the time it
     runs with the SECONDS command.

   Too many operands

     Explanation:  More operands were entered on the command line
     than the specified command can accept.

     Action:  Re-enter the command with the proper number of operands
     as indicated in the command description.  Many commands do not
     have any operands.

   TPI operand is not 48, 96 or 135

     Explanation:  The specified TPI (tracks per inch) must be
     48, 96 or 135.

     Action:  Retry the command using the correct track density.

   TYPE operand is not REG, HC or X2

     Explanation:  The specified TYPE value must be REG, HC or X2.
     See the TYPE command description for an explanation.

     Action:  Retry the command using the correct TYPE value.

   Unknown command

     Explanation:  The specified command is not recognized by ALIGN.

     Action:  Check the command spelling and re-enter it.

   Warning: TYPE HC is intended for PC-AT

     Explanation:  You specified a High Capacity drive and ALIGN is
     not running on a PC-AT which is the only IBM Personal Computer
     that supports a High Capacity drive.

     Action:  If you are not testing a High Capacity drive, then
     re-enter the TYPE command specifying a type that is appropriate
     for your Personal Computer model and diskette drive type.  If
     you are testing a High Capacity drive on a machine other than a
     PC-AT, then you may continue.  However, High Capacity support in
     ALIGN has only been tested on a PC-AT.  Operation with other
     machines and non-IBM hardware may not be successful.



TANDON TM-100 SERIES REPAIR TIPS

   LOOSE SCREWS AND NUTS - HEAD MISALIGNMENT

   In my experience, the most frequent cause of head misalignment and
   drive failure on Tandon TM-100 series drives is a loose Allen head
   screw on the stepper motor shaft.  This allows the motor shaft to
   slip where it connects to the split band positioner pulley.
   Tighten this Allen head screw before doing an alignment.  It's not
   unusual to tighten it one-half turn holding the short end of an
   Allen wrench with just your fingers.  Don't over-do it, however,
   as you could strip the threads.

   The stepper motor shaft is smooth and has no flats or keys.  As
   long as you are doing an alignment and the Allen screw is tight,
   the exact pulley position on the shaft usually doesn't matter.
   But sometimes it can be out of the head alignment cam screw
   adjuster range.  If this happens, loosen the Allen screw, rotate
   the pulley a bit, tighten it, and try again.

   While you're at it, check the two nuts that hold the track stepper
   motor to the casting.  Also, remove the clear plastic cover on the
   bottom of the head assembly and carefully tighten the little
   Phillips screw that holds the split band on the pulley.

   If you're not going to do an alignment, don't tighten these screws
   since just tightening them might change the alignment some.


   TRACK 00 SWITCH PROBLEMS - BOOT FAILURE

   The track 0 microswitch frequently becomes intermittent or fails.
   You can easily check this by powering-off the system and removing
   plug 11 on the back of the drive.  Push a few pieces of bare wire
   into the connector and check the switch contacts with an analog
   ohm meter.  The switch is single pole, double throw (SPDT).

               |     |  |
               |     |  |  <- wires to switch
              ------------
              |          |         COM - common center contact
              | Plug     |         NC  - normally closed
              |          |         NO  - normally open
              |          |
    Pin # ->  |4  3  2  1|
              ------------
             COM     NC NO  <- Switch contacts

   Operate the switch manually.  It is a little hard to get to and
   you may want to remove the logic board first.  Check to see that
   contact closure is positive, occurs when the switch clicks,
   and without any wavering around.

   If the switch is not operating properly, the problem is usually
   just a very small amount of corrosion or oxidation on the switch
   contacts.  Rather than replacing the switch, the easy and
   effective repair is to pass some reasonable current through the
   switch and operate the switch a few times.  Be sure that plug 11
   is disconnected from the logic board and that you make connections
   to just the plug.  Use an external CURRENT LIMITED low voltage
   supply to burn off the little bit of oxidation.  I don't know how
   much current to recommend.  I use just enough to cause a little
   spark when the power supply leads are touched, probably 0.5 or
   1.0 amp.  Be sure to use a current limited supply or put an
   appropriate current limiting resistor in series.  If you don't
   know how to do this, then find someone who does rather than risk
   any harm or damage.


POSSIBLE SOURCES FOR SUPPLIES

   For the type of drive used in the original PC, the alignment and
   service procedures are in the Tandon "OEM Operating and Service
   Manual TM-100-1 and -2 Disk Drives, 48 Tracks per Inch."

   Priority One Electronics has sold this as part number
   07TND179022001, for $36.00.

                     Priority One Electronics
                     9161 Deering Ave.
                     Chatsworth, CA 91311
                     Telephone (800) 423-5922
                               (818) 709-5111

   It is also Tandon part number 179022-001, listed at $25.00 on a
   December 1982 Tandon price list.  I don't know if they will sell
   it directly to end users.

                     Tandon Corporation
                     20320 Prairie Street
                     Chatsworth, CA 91311
                     Telephone (213) 993-6644


   Analog Alignment Disks (AAD's) are no longer available directly
   from Xidex/Dysan Corporation.  Their regional sales offices or
   main office should be able to give you the name of a dealer who
   stocks them or can get them for you.  Xidex/Dysan says that any
   Xidex/Dysan dealer can order them.

           Xidex/Dysan Corporation
           5100 Patrick Henry Drive
           Santa Clara, CA 95050
           Telephone (408) 988-3472

   One mail order dealer with a range of Xidex/Dysan products is

           Supply Line, Inc.
           2909 Oregon Court, Suite A4
           Torrance, California 90503
           Telephone (800) 422-3392  outside of California
                     (800) 648-7376  inside California
                     (213) 212-7376

   Extension or external diskette drive signal and power cables may
   be difficult to locate or you may have to make your own.