==============================================================================
=                                                                            =
=                                 VHARD.DOC                                  =
=                                                                            =
=           Documentation for VHARD.SYS and associated utilities             =
=                                                                            =
=                          Public Domain Software                            =
=                                                                            =
=                                    by                                      =
=                                                                            =
=                             Aaron L. Brenner                               =
=                                 July 1990                                  =
=                                                                            =
=                            BIX user albrenner                              =
=                       GEnie mail address A.BRENNER                         =
==============================================================================

=Dedication=
	This documentation and all the accompanying software (VHARD.SYS,
VHPREP.EXE, VHCACHE.EXE, and all associated source code) are hereby released
to the public domain.

=Background=
        I hate doing backups. Since I don't have a commercial backup program
(and I refuse to use the brain-damaged BACKUP that comes with DOS), I have to
split large files to fit on my 360KB diskettes. That gets to be a real pain.

        One day, I got an idea: how about a device driver that makes my A:
drive look like a small (and very slow) hard disk? It would allow me to easily
backup those big files without the hassle of manually splitting them up. With
that idea in mind, I sat down and wrote VHARD.


=VHARD.SYS=

        VHARD.SYS is a device driver that provides another drive to DOS.
Version 1.00 allows for 13 360KB diskettes, giving 5,304,320 bytes of space.
Later versions will allow for different diskette formats.

        To install VHARD.SYS, you need to put a line in your CONFIG.SYS like
this
        DEVICE=VHARD.SYS

and reboot. At that point, you will have another drive recognized by DOS. You
can copy files to and from the drive, run CHKDSK on the drive, list the
directory of the drive, and so on. As far as DOS is concerned, it's a
removable 5MB disk.


=VHPREP.EXE=

        Before you can actually use a set of floppies with VHARD, they must be
prepared by VHPREP. Each floppy will be formatted and stamped with a disk ID
and serial number.

        The command syntax for VHPREP is

        VHPREP [<disk ID> [<disk number>]]

        <disk ID> is an optional 8-character identification tag that will be
        put on each diskette in the set.

        <disk number> is the optional disk number. It can only be used in
        conjuction with the <disk ID> option, and indicates to VHPREP that you
        only want to prepare 1 diskette.

        If you don't give VHPREP a specific disk ID to use, it will build a
        funny-looking one based on the current system time (VH0BF10D, for
        instance).

        When run, VHPREP will prompt you to put a diskette in drive A:, then
press a key. VHPREP will then format the diskette, and write the disk ID and
disk number. Also, if it is the first disk of the set (disk 0), VHPREP will
also write a DOS boot sector, 2 empty FATs, and a root directory containing
the disk ID as the volume label. Once the diskette has been prepared, VHPREP
will tell you how to label it.


=VHCACHE.EXE=

        To minimize floppy-swapping when copying files to the VHARD drive, 
VHCACHE provides a read/write cache of the FAT and root directory.

        The command syntax for VHCACHE is

        VHCACHE [? | INFO | ON | OFF | MANUAL | AUTO | FLUSH]

        ? and INFO will cause VHCACHE to display information about the cache.

        ON will install and enable the cache.

        OFF will disable the cache and remove it from memory.

        AUTO will cause the cache to be written to disk automatically if the
        DOS version is 3.00 or greater AND SHARE is installed. In this case,
        DOS will tell the VHARD driver when it is opening and closing files,
        so the driver can know when it needs to update the FAT and root
        directory.

        MANUAL will disable AUTO, forcing you to tell VHARD when to write the
        cache to disk.

        FLUSH is how you tell VHARD to write the cache to disk.

        If you don't give VHCACHE any parameters, it will display a brief
        usage message.

        * * * * * * * * * * * * * WARNING!!! * * * * * * * * * * * * *

        If you intend to run a program that will be using absolute disk
        sectors (a defragger, for instance) with the VHARD drive, DISABLE THE
        CACHE FIRST! The cache-handling code in VHARD.SYS is *very* simple-
        minded. DOS only reads and writes the FATs and root directory a few
        sectors (at most) at a time, so VHARD will only work properly if the
        data to be read or written fall entirely within or outside tha cache.
        This warning applies to reading or writing absolute sectors from
        within DEBUG and SYMDEB as well.

        If you don't know what I'm talking about, that's all right. Just
        remember: if you're going to do something that could be dangerous with
        a normal disk, disable the cache first.


=Technical info=

    *   Each diskette in the set is formatted to 10 sectors per track, 40
        tracks, 512 bytes per sector. This gives 799 usable sectors on each
        diskette.

    *   VHARD.SYS actually contains 2 device drivers - a block driver that
        provides the support for the virtual hard drive, and a character
        driver that provides functions for dealing with the non-standard
        diskettes. This driver is named VHARDCTL. The provided source code
        fully describes the operation and use of this driver, but I'll repeat
        some of it here.

        All commands are sent to VHARDCTL via DOS' IOCTL function (44h). The
        usual sequence of operations is something like this:

        vhctl_name      db      'VHARDCTL',0    ; Name of the driver
        vhctl_command   VH_CMD <>               ; Defined in VHARD.INC
        our_drive       db      0ffh            ; Drive assigned (DOS 3.10+)
        vhard_version   dw      0               ; VHARD.SYS version
        vhard_BPB       DOS_BPB <>              ; Defined in DD_DEFS.INC

                . . . . .

                mov     dx,offset vhctl_name    ; Tell DOS to open it
                mov     ax,3d02                 ;  for read/write
                int     21h                     ;
                jc      not_there               ; If it fails, driver isn't
                                                ;  loaded
                mov     bx,ax                   ; Get the handle DOS returned
                mov     ax,4400h                ; IOCTL - Get Device Info
                int     21h                     ;
                test    dl,80h                  ; Test the "ISDEV" bit
                jz      not_there               ; If it isn't a device, the
                                                ; driver isn't loaded
                . . . . .

                mov     vhctl_command.VC_cmd_code,CMD_GETDATA
                mov     word ptr vhctl_command.VC_buffer[0],offset our_drive
                mov     word ptr vhctl_command.VC_buffer[2],ds
                mov     dx,offset vhctl_command ; Data to write (BX = handle)
                mov     cx,size VH_CMD          ; Number of bytes to write
                mov     ax,4403h                ; IOCTL write
                int     21h                     ;

        VHARDCTL supports the following commands:

        Format Track command
        byte    0
        byte    track to format (head in bit 7, cylinder in low 7 bits)
        byte    return status
        dword   pointer to format parameter buffer (see details of INT 13H)

        Read Track command
        byte    1
        byte    track to read (head in bit 7, cylinder in low 7 bits)
        byte    return status
        dword   pointer to buffer to read into

        Write Track command
        byte    2
        byte    track to write (head in bit 7, cylinder in low 7 bits)
        byte    return status
        dword   pointer to buffer to write from

        Verify Track command
        byte    3
        byte    track to verify (head in bit 7, cylinder in low 7 bits)
        byte    return status

        Set FAT cache buffer
        byte    4
        byte    0, disable cache
                1, enable cache
                2, flush cache
                3, disable cache autoflush
                4, enable cache autoflush (DOS 3+, SHARE installed)
		5, return cache information
        byte    return status
        dword   pointer to cache buffer

        Retrieve Driver Data
        byte    5
        byte    unused
        byte    set to 0 by VHARD
        dword   pointer to buffer to receive the following data:
                byte            drive number assigned by DOS (3.10+)
                word            VHARD version
                19 bytes        BPB for VHARD

[EOF]