This Directory contains the OmniKey/Ultra SF utility program.  With
it, the top row of the Ultra's SF (Special Function) keys marked SF1 
through SF12 can be set to operate in one of four modes: 

Normal/SF; Shift/SF; Alt/SF and Ctrl/SF.

Selection can be made at the DOS prompt or as part of a Batch file.  
Here are the commands for inclusion in your Autoexec.Bat file:

SFSET N    - Normal (same as the left function keys)
SFSET A    - Alt    (sends Alt   + function key)
SFSET S    - Shift  (sends Shift + function key)
SFSET C    - Ctrl   (sends Ctrl  + function key)

SF Key functions can be set in the DOS mode using the SF Select Key
(located to the left of the CapsLock LED on the top righthand side 
of the keyboard) and the appropriate control key -- Shift, Ctrl, Alt. 
Hold down the SF Select key and press the desired control key.  

Next time you use the SF 1-12 keys, they will register as Shift/F, Ctrl/F
or Alt/f.  

Using macro software programs, macros may be assigned to 
any SF key with any associated control key.  Hence you could have as
many as 48 distinct macros assigned to the SF keys.