GAMMA.IXP
           Autodesk 3D Studio Gamma Correction Process
                           Version 1.0
        Copyright 1993 Dan Silva.  From Yost Group, Inc.
     This is a Public Domain IPAS routine.  Not for Resale.


Gamma is an image process that corrects the gamma values of an
image within Video Post.  It's primary use is to modify the gamma
(brightness curve) of scenes that will be recorded on videotape.

A brief explanation of what gamma is:

Color calculations in 3D Studio (and most other 3D renderers) are
based on linear intensity values.  For example, an RGB color of
(0.5,0.5,0.5) has exactly half the intensity of an RGB color of
(1,1,1).  Traditionally, images produced by computer graphics
applications are written into files of linear intensity byte data
with one byte for each of red, green and blue at every pixel. 
Thus, a pixel value of (127,127,127) has half the intensity of a
pixel value of (255,255,255).

Unfortunately, the response of typical video color monitors and
of the human visual system is nonlinear.  A typical monitor
luminance curve shows a dip in the middle of the response range. 

Since the default Targa file or frame buffer contents is linear,
the RGB values aren't being displayed "correctly" for the video
device.  The effect of this is that the colors in the middle of
the luminance curve are darker than they should be, and
antialiasing techniques aren't utilized in an optimal way.

Therefore, in order to correct for the non-linearity of the
monitor, a monitor gamma correction function must be performed.  

The monitor correction function is an exponential function of the
form:

     lookup value = intensity 1.0/y

Gamma (y) represents the nonlinearity of the monitor.  Monitors
normally have a gamma value that is in the range of 2.0 to 3.0. 
A gamma of 1 represents a linear device.  A gamma of 2.2 is the
NTSC standard.  3D Studio outputs all images with linear gamma
(1.0), so in order to take advantage of gamma correction, this
GAMMA.IXP program has been provided.

Using an incorrect gamma value results in incorrect image
contrast and chromacity shifts.  A gamma that is too large
results in intensities being mapped brighter than they should be.
A gamma that is too small results in intensities being mapped
dimmer than they should be.  The pure black and white
intensities, however, are always correctly mapped.  Incorrect
gamma either increases or decreases only the intensity of the
mid-range of the image.  Consider a color of (0,127,255).  If the
gamma is too high, the green component will be too intense,
resulting in a color shift towards green.  If the gamma is too
low, the green value is too low, resulting in a shift towards
blue.  The red and blue intensities are not affected by an
incorrect gamma because they represent the extreme values of 0
and 255.

One effect of increasing gamma is that the darkest portion of the
intensity values in the image are stretched into a much greater
range of intensity values.  Therefore, the higher the gamma, the
more possible banding/quantizing you'll see in the darkest part
of the image.

Gamma.ixp is used like any other IXP in Video Post; it is added
to the image queue, and its gamma value field is accessed through
the Setup button in the Queue Item dialog box.  Any floating
point number can be used in the gamma value field, but the only
relevant range is from 1.5 to 3.0 (with NTSC standard being 2.2). 
Gamma affects all queue items above it, and it should always be
placed at the bottom (end) of the queue.

It's only recommended to use gamma correction as the final step
of your entire image chain.  Do not gamma correct any other
elements of your queue, texture maps, backgrounds, etc.

Unfortunately, since your scenes were all designed with linear
(1.0) gamma, when you gamma correct them to higher values, they
will appear much brighter.  This means that, if you want to take
advantage of gamma correction, you'll have to adjust/darken all
of your materials and your scene lighting (which can be a BIG
job).  Oh well...

How can you tell if you're using the best gamma value for your
monitor?  Well, if you're doing NTSC output, a gamma of 2.2 is
standard, but you can visually check the optimal gamma for your
particular output device using the following method.

1.   Set up a Video Post sequence with the supplied GAMMA.GIF
file as the first item in the Queue, and with GAMMA.IXP as the
second (bottom/last) item in the Queue.

     GAMMA.GIF is a test file that is composed of two halves. 
The right half of the image is a black/white checkerboard
pattern.  This pattern, since it's made of pure black and white
pixels, will not be affected by changes in gamma.  Since it's a
50/50 mix of pixels, it will always appear 50% grey, no matter
what the gamma setting.  The left half of the image contains
solid grey (127,127,127) pixels.  When you gamma correct this
image, the left half will change, since it's in the middle of the
luminance scale.  

2.   Render the VP sequence.  At a gamma of 1.0, the left half
will appear MUCH darker than the right half.  This is proof that
the monitor gamma is nonlinear, since the 50% grey image is so
much darker than the 50/50 black/white pixel field.  As you bring
the gamma up to the 2.2 range, and test render the image, the
left half will match the luminance/grey value of the right half
(you may have to stand back a few feet from the monitor to blend
the right halve's 50/50 pixels into one grey field).  When the
left half most-closely approximates the luminance of the right
half, the gamma value is perfect for your monitor.  (Note that
what might be perfect for your monitor is not necessarily the
correct 2.2 value for NTSC, so if you're going to be outputting
to videotape, just use 2.2, and leave it at that.)

Note that the GAMMA.GIF file is set up for 512x482 pixel
resolution.  If your frame buffer does not support that
resolution, you may have to modify GAMMA.GIF for your particular
resolution in Animator Pro, since you optimally don't want to
rescale it in Video Post.  (rescaling will stretch the 50/50
black/white pixels and they'll lose their optimal pseudo-grey
characteristics when stretched)

[end]