Doc for BENCH12.SCR 12/21/92

How to run.---------------------------------------------------

First, completely configure AutoCAD for the driver environment
to be tested.  Use either the drivers configuration program
and/or AutoCAD video configuration to set this up.  Ensure that
32 bit display space operation is enabled in the driver, if it
has this option.

NOTE:  This benchmark will not work with any driver that only
supports 16 bit display space, as that these drivers are not
true ADI 4.2 drivers.

After configuration, return back to DOS.

All of the Autodesk supplied drivers will execute this
benchmark.  The ACAD.DWG prototype drawing should be the default
one shipped by Autodesk.

Starting from the directory where ACAD.EXE is located, enter
ACAD.  You might want to use the STATUS command to see how much
memory is available, and to see how much memory is used by the
driver without any drawing loaded.

Use the SCRIPT command to invoke BENCH12.SCR.  Depending on your
system speed, amount of memory, and driver, this benchmark will
take anywhere from under 2 minutes up to A LONG TIME.  On a
486/66 DX/2 with 16 meg, Autodesk VGA driver takes a little
under 5 minutes, and about 11 meg of memory.

The files used.--------------------------------------------------

This script file benchmarks driver performance using 32 bit
display list with Release 12.  It must be run from the ACAD
directory (or the main directory where ACAD.EXE is located).  It
assumes the standard AutoCAD installation to find the following
files:

	SAMPLE\PSSHADOW.DWG
	SAMPLE\HOUSEPLN.DWG
	SUPPORT\CHROMA.DWG

You must have read-write access to the directory where the
script was started from, because its creates a temporary file
$$$TEMP.EPS for the postscript output/input functions.  The
TEMPPREFIX SETVAR variable cannot be used because the PSIN
function cannot be used from LISP due to an AutoCAD bug.

The only place any files are used is at the top of the script
file, so you may easily change the path names to enable this to
work on a network.

You should have at least 11 meg of free memory for AutoCAD to
use run this benchmark.  The Autodesk STANDARD VGA 640x480 16
color driver uses about 11 meg to run the script.

The amount of extra memory required by the display driver will
make a difference in the performance of this benchmark.

What this benchmark measures.----------------------------------

This benchmark was developed due to requests by many users,
customers, graphics board manufacturers, users groups, and
reviewers to design a benchmark that shows actual AutoCAD
performance as affected by a display list driver.  Traditional
benchmarks only show the benefits of faster zoom and pan
operations, but they ignored the side-effects that a driver may
bring to the system, caused by normal editing operations.

The main objective was to never generate a regen.  Autodesk is
promoting that 32 bit display space built into AutoCAD R12
dramatically reduces the need for a regen, so this script will
not generate a regen on any driver that is fully ADI 4.2 and
supports 32 bit display space, after the initial Zoom Extents.

The second objective was to show the performance gains or losses
because a display list driver is installed.  Many edits are
performed which typically cause display list drivers to
dramatically increase their memory usage.  We received many
requests that the benchmark show when a driver does not
effectively manage display list editing and memory management.
Typical display list operations are also performed (zooming and
panning) to show traditional display list gains.

The third objective was to test the driver with 32 bit display
list objects, to ascertain if the driver performs correct
scaling and clipping.

About the Script.----------------------------------------------

This script file first inserts PSSHADOW.DWG, PSOUT it to an .EPS
file, and then imports it with PSIN, to get the shaded image.
This portion is not timed since it is virtually 100% CPU and
Hard disk related.

The drawing is generated by moving the shaded image, importing
the HOUSEPLN.DWG drawing, importing the HOUSEPLN.DWG drawing at
a reduced scale, importing the CHROMA drawing, and importing the
CHROMA drawing at a reduced scale.  The total time for this
section is reported at the end.

A ZOOM E is performed (which will cause a regen) and a donut is
created in the corner, and this time is reported at the end.

A series of ZOOM and PAN are used to test the classic display
list benefits, and its time is reported at the end.  Accelerated
boards should benefit from this section and should have smaller
times than non-accelerated boards.  About 28 bits of display
list space (out of 31) are used to prevent regens at very high
resolutions and other aspect ratio considerations.  The donut
created in the Zoom E section is used to check polygon clipping.

A number of edits are performed such as rotations, UNDO,
changing of PLINE widths, DONUT, and circles.  This section
contains redraws after most edits, simulating a typical user
cleaning up the pick blips, which shows the effect of edits on
display list performance.  This time is reported at the end.

The final section tests MOVE and ERASE of large items, and is
reported at the end.

At this point, the original drawing is completely erased, and a
small drawing is created tallying the results.

A STATUS command is execute to show the amount of virtual memory
used by AutoCAD and the driver.

What to look for.-----------------------------------------------

If a regen occurs, most likely the driver does not implement the
full 32 bit display space, and is an ADI 4.1 driver (Release 11)
pretending to be an ADI 4.2 driver.

During the edits, check to see if redraws are showing the
previous edits.  These may appear as "temporary or flashing
ghosts".  If so, then the driver is not performing real-time
display list editing.  If the Virtual Memory Allocated to
Program grows  more then a couple of meg, then the driver is not
re-using erased display list memory.  Some drivers may cause the
system to page to the hard disk excessively due to the amount of
memory they are using.

If you "hang", reboot, get "Divide by zero", "Abnormal Program
Termination", "Fatal Error", or other messages (or lack of),
then it is the driver that caused the problem.

In general, run the benchmark with the Autodesk supplied VGA
driver to get a feel for what the display should look like
during the execution, then run with the driver to test, to see
if the driver is operating correctly.

The future.---------------------------------------------------

Some of the areas that this script does not address are:
Multiple Viewports, Paper Space, AVE Render, Grid, Command Area
text speed, dialog-box speed, and others.

We are more than open to any comments, and we plan on enhancing
this over time.  If you have any feelings, either positive or
negative, please let us know so that this script will continue
develop to test your needs.


Enjoy,

Vibrant Graphics, USA.
Tel: 512-250-1711, Fax: 512-250-5811

Vibrant Graphics produces high-performance display drivers for
AutoCAD 10/386, AutoCAD 11/386, AutoCAD 12, AutoSHADE,
3D-Studio, CADKEY, and MicroStation.