SFRBBSDR
                   RBBS Door To SPITFIRE Conversion Program     
                                Version 1.5
                       Copyright (C) By Mike Woltz, 1990
                             Buffalo Creek Software
                                  A Member Of 
                   The Association Of Shareware Professionals

    
    INTRODUCTION
    ------------                         

         SFRBBSDR is a companion SPITFIRE Bulletin Board System program 
    which can be used to convert door programs written specifically for 
    RBBS (Remote Bulletin Board Service System) software so they are 
    compatible with SPITFIRE.  Using the SFRBBSDR conversion utility, 
    RBBS door programs can be set up and run in SPITFIRE either as a 
    SPITFIRE door program or as one of the optional SPITFIRE Sysop 
    configurable commands available from the Main, Message or File Menu.


     HOW IT WORKS
     ------------
     
         When a caller is logged on a SPITFIRE BBS and elects to utilize 
     a Door, SPITFIRE creates a file named SFDOORS.DAT.  This file
     contains necessary user information and must exist for the user to 
     be able to return to SPITFIRE after running the Door program.
     Similarly, when a caller uses one of the Sysop configurable 
     commands, a SFMAIN.DAT, SFMESS.DAT or SFFILE.DAT is created 
     corresponding to the menu from which the configurable command 
     is being executed.    Once the caller has returned to SPITFIRE, 
     the SFDOORS.DAT, SFMAIN.DAT, SFMESS.DAT or SFFILE.DAT file is 
     erased from the drive.
          
         SFRBBSDR reads the information from SFDOORS.DAT, SFMAIN.DAT,
    SFMESS.DAT or SFFILES.DAT and then writes the information to 
    DORINFO[x].DEF.  SFRBBSDR reads the SFDOORS.DAT, SFMAIN.DAT,
    SFMESS.DAT or the SFFILES.DAT and determines the node number for
    the DORINFO[x].DEF file.  DORINFO1.DEF is written for single node
    systems.  DORINFO2.DEF through DORINFO9.DEF is written for multi-
    node systems.  SFRBBSDR will automatically create this file to
    correspond to the appropriate node from which it is being run;
    up to the nineth node.  Due to DOS's eight character file name
    limit, it is not possible to create a DORINFO[x].DEF file for
    nodes ten or higher.
    
       DORINFO[x].DEF is a file that RBBS writes when a caller
    logged on a RBBS BBS elects to utilize a door.  There are many Door
    programs written to be used with RBBS that are dependent on the 
    DORINFO[x].DEF file for their operation.  By using SFRBBSDR, the 
    DORINFO[x].DEF can be created to allow Door programs written for 
    RBBS to be used with SPITFIRE.

       SFRBBSDR requires the path to where the DORINFO[x].DEF file will
    be written be included as a command line parameter.  For instance,
    if you are running an RBBS door in a directory, DOOR_A, directly 
    beneath your SF directory on drive C:, your command line would look
    like this:
              
         SFRBBSDR C:\SF\DOOR_A

    Notice, a space is left between the SFRBBSDR and the path to where
    the DORINFO[x].DEF file will be written.
     

    USING SFRBBSDR TO RUN AS A SPITFIRE DOOR
    ----------------------------------------
       
       The first thing you will need to be concerned with when using
    SFRBBSDR to run a SPITFIRE door will be to create or modify an existing
    SFDOOR.MNU.  Using your favorite text editor you will need to
    include a line that contains a brief description of the door program
    you intend to run, a comma, and the security level required by the
    user to access this SPITFIRE door.  (The line number should correspond 
    to the door number you are running your door program in.  For this 
    example we will be using Door A so it should appear on line number 1.
    For more detailed information refer to the SPITFIRE manual.)  A typical
    line of your SFDOOR.MNU might look like this:
    
    The Door Description,10
    
    If you are using SFDR[x].BBS/CLR sysop created non-ansi and ansi
    menus these will need to be modified also.
    
       Next you will also need to modify your SF.BAT file with your 
    favorite text editor.  Locate the line which contains :DOOR_A.
    You will need to place your door #1 commands (valid DOS commands,
    program execution, etc.) between :DOOR_A and GOTO LOOP.  A typical
    example of this portion of your SF.BAT might be changed to read as
    listed below:
    
         :DOOR_A
         SFRBBSDR C:\SF\DOOR_A
         CD\SF\DOOR_A
         PROGRAM NAME  
         DEL DORINFO[x].DEF         (where x refers to the node number)
         CD\SF
         GOTO LOOP
         :DOOR_B
         
    If the RBBS door program you are using requires the use of a
    configuration file, the name of the configuration file would be
    added on the same line as, and after the PROGRAM NAME.  For instance,
    instead of PROGRAM NAME you would need PROGRAM NAME and a blank
    space followed by the name of the configuration file.      
     
    
    USING SFRBBSDR FROM A SPITFIRE MENU
    -----------------------------------
    
       SPITFIRE has a sysop configurable command for the Main, Message 
    and File menus.  The sysop configurable command is executed through 
    a batch file which corresponds to the menu it is being run from.  In
    other words, SFMAIN.BAT runs the sysop configurable command from the
    Main Menu, SFMESS.BAT runs the one from the Message Menu and SFFILE.BAT 
    the one from the File Menu.  The commands necessary to execute SFRBBSDR 
    and run the RBBS door program are set up in the batch file which 
    corresponds to the menu you wish to have program run from.

       The first thing you will need to establish is which of these menus
    you wish to use to run the RBBS door program.  For this purpose, 
    let's assume that it is going to be set up so it can be run from the 
    Main Menu.  (It should be noted the set up procedure will be the same 
    regardless of which Menu you are running SFRBBSDR and the RBBS door
    program from.)

       Next, you will need to decide what you wish to name the command
    option and establish what security level will be required for
    users of your system to be able to access this option.  Once this
    is determined you will need to modify the SFMAIN.MNU file using
    your favorite text editor, as long as it saves in ASCII format.
    (Refer to the SPITFIRE manual for further documentation on this
    if needed.  It should also be noted that if SFRBBSDR was being
    set up to run from the File Menu, you would need to modify the
    SFFILE.MNU file and if it was being set up to be run from the
    Message Menu you would need to modify the SFMSG.MNU file.)

       Examining the default SFMAIN.MNU file, you will notice the sysop
    configurable command appears as:
 
       <K>............. Add Your Own,,1000,@

       This will need to be replaced with a Command Character that will
    be used to select the option from the menu.  It is ABSOLUTELY IMPERATIVE
    that the Command Character must not duplicate an existing Command
    Character for another menu option.  You will then need to include
    a brief description of the RBBS door program you are running, two
    commas, the security level required to access this feature, and another
    comma followed by the a @.  The @ must not be changed! (For more detailed
    information on modifying your SFMAIN.MNU, SFMSG.MNU or SFFILE.MNU refer
    to your SPITFIRE manual.)
    
       <K>.... Brief Program Description,,10,@

       Now you will need to modify the corresponding batch file, SFMAIN.BAT,
    so that it can be executed from the Main Menu.  Do this using your
    favorite text editor, as long as it saves in ASCII format.  (Again, it
    should be noted that if SFRBBSDR and the RBBS door program were being 
    set up to run from the File Menu, you would need to modify the SFFILE.BAT 
    file and if it was being set up to be run from the Message Menu you would 
    need to modify the SFMESS.BAT file.)

       The commands you will need to include in your SFMAIN.BAT to run 
    SFRBBSDR and the RBBS door program might look similar to this:
   
       ECHO OFF
       BRK OFF
       SFRBBSDR C:\SF\DIRNAME
       CD\SF\DIRNAME
       PROGRAM NAME 
       DEL DOORINFO[x].DEF     (where x refers to the node number)
       :END
       CD\SF
       BRK ON

       (BRK is written and copyrighted by Solid Systems, 1985, but can 
    be downloaded from Buffalo Creek's BBS as well as a number of other 
    BBS systems.  BRK is not required, however, it is recommended since it
    will prevent a caller using the CTRL BRK command to terminate the batch 
    file, gaining access to your system at the DOS level.)

      In the above example, C:\SF\DIRNAME refers to the drive and the 
    directory in which the RBBS door program files reside.  The actual
    RBBS door program name would be entered where PROGRAM NAME is 
    currently.   If the RBBS door program you are using requires the 
    use of a configuration file, the name of the configuration file would 
    be added on the same line as and after the program.  For instance,
    instead of PROGRAM NAME you would need PROGRAM NAME and a blank
    space followed by the name of the configuration file.      


    FILES REQUIRED BY SFRBBSDR
    --------------------------
    
       SFRBBSDR must find either the SFDOORS.DAT, SFMAIN.DAT, SFMESS.DAT
    or SFFILE.DAT in order to run.  If the appropriate file is not
    found (depending upon where SFRBBSDR is being executed from) a
    message will display that the file was not found and operation is
    halting.
    
       SFRBBSDR will next look for the SFNODE.DAT file.  If not found
    the following message displays:
    
    Unable to find SFNODE.DAT!
    Operation halting!
    
       SFRBBSDR will next look for the SFUSERS.DAT file.  If not found
    the following message displays:
    
    Unable to find SFUSERS.DAT!
    Operation halting!

       Lastly, SFRBBSDR will look for the SFSYSTEM.DAT file.  If not found
    the following message displays:
    
    Unable to find SFSYSTEM.DAT!
    Operation halting!

   
    LOCAL OPERATION
    ---------------
    
       SFRBBSDR can be used to execute a RBBS door in local mode.  If
    the door is being used during a local log on, SFRBBSDR writes
    COM0 to the DORINFO[x].DEF file.  Otherwise, it will write the
    appropriate COM port, i.e. COM1, COM2, etc.
    
    
    SFRBBSDR ON A MULTI-NODE SYSTEM
    -------------------------------
   
       SFRBBSDR is fully compatible for operation on a multi-node BBS.
    It automatically handles any file locking and file sharing 
    required during program execution.   However, the RBBS door being
    used with SFRBBSDR may not have this capability.  Please refer
    to the RBBS door's documentation in regard to it's multi-node
    capability.  The section HOW IT WORKS of this documentation
    explains how SFRBBSDR works in a multi-node environment.
    
    
    SFRBBSDR AND DTE LOCK
    ---------------------
        
       SFRBBSDR.EXE uses a second command line parameter, /S, that is 
    used under the following conditions:
    
       1)  the BBS is operating at a locked baud rate
       2)  SPITFIRE is configured so that the hardware data flow control
           is on
       3)  the RBBS door will operate on a BBS with a locked DTE
       
       When the /S parameter is used on the command line, the following
    line of the DORINFO[x].DEF file,
    
    2400 8 N 1
    
    is modified so the baud rate is replaced with that at which the
    BBS is locked.  In other words, if the BBS is locked at 19200 
    and a 2400 baud caller attempts to use a RBBS door, SFRBBSDR would
    write this line as:
    
    19200 8 N 1
    
    If the /S parameter is not used, the baud rate of the above line
    is modified so that it is replaced with the baud rate of the
    caller.  If the BBS is not operating at a locked baud rate, the
    /S should not be used.  Or if an unlocking utility is used, the
    /S should not be used.  In such instances, if a 1200 baud caller
    attempts to use a RBBS door, SFRBBSDR would write this line
    as:
    
    1200 8 N 1
   
    Refer to the actual door's documentation as to whether the
    individual door will run under a locked DTE environment.
    
       When using the /S parameter on the command line, it should appear
    after the path to the door.  Using the previous example, your command
    line would look similar to this:
    
       SFRBBSDR C:\SF\DIRNAME /S
       

    DISTRIBUTION
    ------------

       SFRBBSDR is distributed under the shareware concept.  You are
    free to distribute the SFRBBSDR program as long as it remains
    unmodified and no fee is charged.  If you use this program and
    find it beneficial, a fee is required.  A $1.00 fee is required
    of registered SPITFIRE Sysops and a $5.00 fee is required of
    all others.  
    
    
    DISCLAIMER
    ----------
        
         Mike Woltz and/or Buffalo Creek Software shall in no way be held 
     responsible for any damage incurred while operating SFRBBSDR.  All 
     responsibility lies with the user of the software.


       The documentation for SFRBBSDR is contributed by Jacque Shipley
    and The Mother Board BBS.  The shareware version of SPITFIRE 
    and other SPITFIRE utilities are available for download from:

         Buffalo Creek's BBS              The Mother Board BBS
          Mike Woltz, Sysop               Jacque Shipley, Sysop
           (515) 225-8496                    (515) 986-3464
    38000/19200/9600/2400/1200 Baud     19200/9600/2400/1200 Baud