____________________________________________________________


IBM AT or Compatible
Adaptec AHA-1540/1540A/1542A/1540B/1542B/1640/1740  SCSI  Adapter
Board
SCSI Hard Drive/Tape Drive
MS-DOS 3.3

This utility will not operate while the 80386 is in virtual mode.
Attempting  to  do  so  will  cause  the  program  to  abort.  In
addition, this program will not run when  another  device  driver
has  been  loaded  that talks directly to the adapter such as the
ASW-1410 ASPI Manager.
NOTE:  The 1740 must be  in  standard  mode  in  order  for  this
utility to function.

SCSICNTL is a program that runs  under  MS-DOS  allowing  you  to
reprogram your SCSI device to meet the needs of your environment.
Reprogramming your SCSI device allows you to achieve the  highest
possible  throughput for the given operating environment you will
be working in.

This program assumes a basic  knowledge  of  SCSI  and  makes  no
attempt  to  teach  you  about  SCSI.   Although,  there  is help
available for all options in each submenu window, it  is  advised
that   you  obtain  the  programmers  reference  guide  for  your
particular device, or get the ANSI SCSI Standard Rev 17B document
to  gain full knowledge of the parameters in each window.  If you
do not have access to either of these documents, read this manual
carefully and use the help system that is built into the program.

Through the mode sense pages you can  reprogram  a  SCSI  device.
This  program  does  have a knowledge of certain SCSI devices and
for those devices,  the  defaults  are  listed  in  each  program
window.   For  those devices that are not known, the defaults are
listed as "Unknown".  Unknown devices can  still  be  programmed,
but  it is up to you to have the necessary documentation relating
to the device you are attempting to re-program.

With some experimentation, you can find  the  best  settings  for
your  environment.   All  but two of the menu options may be used
without risk to data stored on a SCSI device.  Where options that
could effect data integrity, there are many warnings.  In some of
the menus,  helpful  recommendations  for  a  specific  operating
environment   are  available.   Take  these  recommendations  for
starters  and  tune  them  to  meet  your  needs.   Some  options
available  can  reduce  the throughput of your device, but give a
higher level of data integrity.  While others will  yield  higher
throughput  and  reduce  the  data  integrity.  Reduction of data
integrity is up to you.  If you have a high level  of  confidence
in your SCSI device, this is not a risk, but it is your option.

If you have very little understanding of  SCSI,  study  the  menu
choices  and  take the time to go through each option and ask for
help.  The help provided is sometimes technical  in  nature,  but
what you are doing is highly technical in nature.  If you are not
comfortable with this program, it is advised that you do not  use
it.   But  keep  in  mind  that the program will not allow you to
destroy data unless you make the effort to do so.



The program may be run off of a floppy drive or  off  of  a  hard
drive.   The disk does not have any copy-protection.  Use the MS-
DOS 'copy' utility to install the programs on to your hard  drive
or another floppy drive.  See your MS-DOS documentation for usage
of the 'copy' command.


To run this program on the in your CPU, you must  have  the  host
adapter base I/O address set to 0x330h.  This is the default, but
if you have changed this default it will be necessary for you  to
change   it  back.   Please  refer  to  your  SCSI  Host  Adapter
Installation guide for help.

To start the program, type SCSICNTL <ENTER>.

You will be presented with a window that  contains  a  disclaimer
which  will require you to press ENTER to continue, next a window
with Copyright information and the version number of the  program
is displayed.  You will asked to press ENTER to continue again.

The screen will clear and you will be  presented  with  a  window
along with a window that states, "Looking for devices on the SCSI
bus".  If you have a SCSI tape drive in the system and  the  tape
is not loaded in the tape drive (Tape drive LED is off), an error
message window pops up at the bottom of  the  display  showing  a
"Not Ready" message.  This message can be ignored as it is simply
stating that the tape drive does not have  a  tape  in  it.   For
almost  all  the  options  available  a  tape does not need to be
loaded in the drive.  If any other error appears,  there  may  be
something wrong with the device that was being reviewed.



































After the search for SCSI  devices  is  complete  the  main  menu
window  pops  up,  shown below.
Drive 0                         MAIN MENU               [Modify]
  1.  Select Device
  2.  Format Utility
  3.  Read Device Defect List
  4.  Read/Write Error Recovery Page
  5.  Disconnect/Reconnect Control Page
  6.  Direct Access Device Format Page
  7.  Rigid Disk Drive Geometry Page
  8.  Cache Control Page
  9.  Unique Control Page
  10. Set mode of operation (View/Modify)
  11. SCSI Adapter Configuration
  12. Additional SCSI Device Information
  13. Exit

  Enter Selection:




The program uses menus to guide you  through  the  programmable
pages  of a SCSI device.  Along with the listed options, as shown
above, is a window that contains the information about  the  SCSI
device that is currently selected.  The program defaults the SCSI
device to drive 0 as displayed in the upper left hand  corner  of
the  main  menu  window.   If  device  zero is not available, the
program will find the first available device on the SCSI bus  and
use that device as the default.

The information, in the window to  the  left  of  the  main  menu
selections  contains  the  manufacturer, model number of the SCSI
device, part number, firmware level, firmware  date,  and  serial
number.   Take  note  that  not  all  SCSI  devices have all this
information available and those fields will be blank.

In the upper right hand corner of  the  window,  is  the  current
state  the  program is in.  It defaults to "Modify".  You can use
option 10 to change it to "View" if you like.

Options 4 through 9 have  a  similar  window  format.   The  menu
heading  will  reflect  the  option you have chosen from the main
menu.  Like the main menu, the drive that has  been  selected  is
displayed  in  the  upper  left  hand corner of the display.  The
sub-menu  headings  or  fields  are,  "Parameters",   "Defaults",
"Current",  "Options", and "Selected".

Parameters
This  field  is  a  listing  of  descriptions  for  the  possible
programming options.

Defaults
This field contains a listing of defaults for the  known  device,
if  the  device is of an unknown type, the word "Unknown" appears
for all of the parameters.

Current
This field lists all of the parameters that are currently set for
the selected device.

Options
This field lists all of the available options for a known device.
If  the  device is not known, the word "Unknown" is displayed for
all the parameters.

Selected
This field is where the cursor is placed for you  to  enter  your
choice for each programmable option that is supported for a known
device.  Not all devices support all the parameters  of  a  given
main menu selection.  If the device is an unknown type of device,
you will need to have the SCSI Reference manual for  that  device
in order to select the correct options for that device.

For a given device, the cursor will be placed in  the  "Selected"
field.  Some options are not available for some devices.  In this
case, the cursor will be placed accordingly.  If the device is  a
known  device,  the  options  available  for  that device will be
listed and the cursor will be placed in the "Selected" field  for
you  to  enter the option.  Unless you are in 'view' mode.  If in
'view' mode, all the  current  settings  for  a  device  will  be
displayed  and  you will be asked to "Press <ENTER> to continue",
doing so will return you to the main menu.

When in 'Modify' mode, you may enter the listed option  for  that
parameter,  press  a  '?' to get help, or press <ENTER> to select
the current setting.  If you press the '?', a  help  window  will
describe  each option for the field you are currently in and what
the effect of each option is.  If the program is only expecting a
single  character  response,  you will not have to press <ENTER>.
For instance, if the option for the field you are in is  (E)nable
or  (D)isable,  pressing  '?',  'e',  or 'd' will not require the
<ENTER> key to be pressed, but if the field is expecting a  range
of  values  such  as  0-65535,  pressing  the <ENTER> key will be
required before action will occur.

At the end of each page, you will receive another  prompt  asking
if  you  wish to 'S'tore, or make 'A'ctive, or 'C'ancel the above
changes.

If you choose to 'S'tore the parameters as they appear under  the
'Selected'  field,  these  parameters  will  become the 'current'
parameters until you use this program to change them again.

If you choose 'A' to make the page  active  only,  the  currently
selected  parameters  will  be sent to the drive and will stay in
effect until the system is re-booted.  This  is  helpful  if  you
only  wish  to  make changes, for instance, under MS-DOS and when
you reboot the system, you may enter  XENIX  and  the  parameters
that were previously installed will take effect.  This allows you
to reprogram a device for one environment, while you are in  that
environment,   and  reboot  the  system  to  return  to  the  old
parameters for another environment.

Answering 'C' will simply return you to the  main  menu  aborting
any changes you have made.

Options '6' and '2' from the main menu are the only options  that
could  have  any  effect  on data you have on the hard drive.  Be
sure you have selected the correct device before using either  of
these options.

The options available at the main menu are as follows:

This allows you to select the device that will be used during the
program.   You  may  choose from any of the devices in the window
and you may reselect devices as often as you like.   The  default
device is zero.

Selecting this option will open a  window  on  the  display  that
shows a warning about the device that is currently selected and a
prompt that asks, "DO YOU REALLY WANT TO  CONTINUE?".   Answering
this  prompt with anything other than a 'Y' will abort the format
and you will be returned to the main  menu.   If  you  choose  to
continue  (answering with a 'Y'), the drive will be formatted and
ALL USER DATA ON THE DRIVE WILL BE DESTROYED.   While  formatting
the  drive the system will appear as if it is doing nothing.  The
only message that will be displayed will  be,  "Formatting  Drive
x",  where 'x' is the drive you have selected.  If the drive is a
tape drive, the message, "Erasing Drive x",  will  be  displayed.
If you are erasing a tape, you will need to have a tape loaded in
the drive, or you will get a "Not Ready" error message displayed.

Some devices are hard sectored and  will  only  check  for  added
media flaws when the format command is issued.  In this case, the
format will be done in a matter of seconds.  This is due  to  the
fact that these devices keep track of potentially bad sectors and
only reassign those  sectors  for  a  low-level  format.   If  no
sectors  are  found  to be defective, a low-level format of these
devices will not result in loss  of  user  data.   In  all  other
cases, user data will be lost for any SCSI device.

When you use this option, you will be  presented  with  a  window
that  asks,  "Which list do you want (P,G,A)?".  In the middle of
the screen is a window that outlines each of  the  options.   The
"P"  list  contains  the original manufacturers defect list.  The
"G" list contains a list of defects that  have  been  mapped  out
during a format command.  Choosing "A" will display both lists on
the screen.

This window allows you to alter the error recovery parameters  of
a  SCSI  device.   You  can control things like ECC and Automatic
Read/Write  Reallocation;  which  allows  the  SCSI   device   to
automatically reallocate bad sectors dynamically.

This  window  allows  you  to  set  the  levels  that  SCSI   bus
arbitration  will  occur, based on how full/empty the SCSI buffer
is for the device  that  you  have  selected.   These  parameters
really only effect the XENIX/OS2 operating environments.

This page allows you to set the SCSI sparing scheme for a device.
SCSI  devices  have  spare  sectors  and tracks that are used for
replacing bad sectors and tracks.   By  reducing  the  number  of
spares  in  this page you can increase your storage, but you lose
the spares that may be required someday.  Increasing  the  number
of  spares will decrease the total storage available on your SCSI
device, but will allow the device to have  a  greater  number  of
spare  sectors  to  use  for  replacing  bad  ones.  Not all SCSI
devices allow these parameters to be altered.

You will be warned that altering this information will require  a
low-level  format  to  be  done.   Also  the only storage options
available are 'S'tore and  'C'ancel.   You  have  the  option  of
aborting  the  format,  but  if  you  leave  the  program without
formatting the device, the parameters you have  altered  will  be
changed back to thier original values.

This page is available for viewing only and  cannot  be  altered.
It  contains the physical specifications for a SCSI device.  Such
as the number of heads and cylinders for a SCSI hard drive.

This page is only available for devices that  this  utility  will
support.   If  the device is not supported, an error message will
be displayed in the center of the main window stating so.

If the device is a supported device, and the  drive  has  a  true
cache,   you   will   have   windows   appear   for  some  option
recommendations for specific  operating  environments.   You  can
choose   any   options   you   like,   but   if  you  follow  the
recommendations you will get the most you can out  of  your  SCSI
device.   Feel  free  to  experiment  with these options for your
application to get the most out the drive that you can.

For devices that only have a read ahead buffer, you will  not  be
presented  with  any suggestions for setting this option as it is
either on or off.  Drives such as CDC and Maxtor have read  ahead
buffers, that may or may not be enabled from the factory.

This page is only available for devices that  this  utility  will
support.   If  the device is not supported, an error message will
be displayed in the center of the main window stating  so.   This
window will display unique control parameters of a SCSI device.

This allows you to set the mode of operation for the utility.  If
you are in 'view' mode, you may view the current settings for the
device you have selected.  This option is a toggle and remains in
effect until you press it again.  For some SCSI devices, the mode
may be changed from Modify to  View  depending  on  if  the  SCSI
device  you  have  selected will actually allow the altering of a
page.

This will display information relating to  the  SCSI  adapter  in
your  system.   Under  the heading of the window will be the part
number of the SCSI  host  adapter  you  have  installed  in  your
system.   The rest of the window shows the base I/O port address,
DMA channel, Interrupt channel, and  the  SCSI  ID  of  the  host
adapter.   It  will  also  display  a  number associated with the
firmware level of the adapter board if you are using a  AHA-154xA
or latter.

If you  are  using  this  program  with  the  micro-channel  host
adapter,  the  DMA  channel will not be displayed.  This is not a
hardware configuration option, but is  instead  set  in  the  POS
registers of the system.

Another window  is  also  displayed  to  show  further  operating
information that is stored on the host adapter.  This window will
only  appear  for  the  AHA-154xA  or  latter.   The  information
indicates  whether  the  host  adapter  is  set  to negotiate for
synchronous or not, whether parity checking on the  SCSI  bus  is
enabled, the host adapter DMA write/read pulse widths, the strobe
off time, the bus on/off times.  The window next  to  this  shows
the  status regarding the synchronous negotiation per device.  If
the adapter succesfully negotiated for synchronous protocol,  the
synchronous  period  and  offsets  are  displayed.  If the device
could not support synchronous, the message asynchronus appears.

This window provides detailed information about the  SCSI  device
according  to  what  was  recieved  from  the device via the SCSI
INQUIRY command.  This information as displayed is in accord with
the SCSI-2 specification.

Used to return to MS-DOS.  A message is displayed indicating that
the SCSI is being cleaned up.  You may hear noises emanating from
your SCSI devics as they recalibrate.  This is due  to  the  SCSI
bus  being  issued  a reset, which forces the SCSI devices into a
power on state.































































SCSI:  Usually pronounced  'skuzzy'  stands  for  Small  Computer
Systems Interface.

SCSI Adapter:  This is the board that occupies a slot in the host
CPU.   It  is  not a SCSI controller.  It is a device on the SCSI
bus.

SCSI Bus:  This can be thought of as the cable that is  connected
between the SCSI adapter and the SCSI devices.

Target:  This is the device that a SCSI command has been sent to.

Target ID:  The actual ID of the SCSI controller on the SCSI bus.
The  SCSI  host adapter uses target ID 7, for instance.  All SCSI
controllers must have a unique target ID to work on the SCSI bus.
The  target  ID  ranges  from  0  to 7.  The higher the target ID
number, the higher the priority a device has  on  the  SCSI  bus.
This is akin to the drive select on ST-506 drives.

Initiator:  This the same as 'host'.  This  is  the  system  that
issued  the SCSI command.  While it is possible for more than one
computer to be on the SCSI bus, this  feature  is  currently  not
supported.

LUN:  This stands for Logical Unit Number.  All SCSI devices  are
accessed by the target/LUN of the device.  SCSI devices that have
a SCSI controller imbedded in them, like SCSI  hard  drives,  are
assigned  a  target ID and LUN ID of 0.  The LUN can be from 0 to
7.  This is used only if a SCSI  controller  has  more  than  one
device attached to it.

Mode Sense:  This is a  SCSI  command  that  allows  an  external
program call up and modify parameters for that device.

Page:  This refers to the page of the mode  sense  request.   The
programmable parameters of a SCSI device are kept in pages.  Each
page has a unique set of parameters associated  with  that  page.
Consider  a  page  like  a  small window into the heart of a SCSI
device.

Disconnect:  A SCSI device that has to seek  to  read/write  data
sent  to/from  the host system, will notify the host that it must
relinquish the SCSI bus to complete the requested command.   This
action allows the host system to issue another command to another
SCSI device while the other SCSI device is working  on  the  last
command  sent.   This  action  is  best  noticed in the XENIX/OS2
environments.

Reconnect:  This concerns the action of a SCSI  device  that  has
disconnected  from  the  SCSI  bus  due  to  a seek command being
issued.  Once the device has a certain percentage of data in  its
local  buffer, it will request access to the SCSI bus to send the
data to the host system.  This is best  noticed  in  a  XENIX/OS2
operating   environment.   These  operating  systems  are  multi-
threaded (multi-tasking) and do not have to wait for  a  specific
command to be completed before another command is issued.

Priority:  The priority of a SCSI device  is  determined  by  the
target  ID  of the device.  The higher the number, the higher the
priority a device has on the SCSI bus.  This is how SCSI  devices
arbitrate for the SCSI bus.

Bus   Arbitration:     This    refers    to    the    transparent
disconnection/reconnection  of  a SCSI device.  SCSI devices will
get off of the SCSI bus if they have to seek to get  data.   This
allows  the  SCSI adapter to issue other commands to another SCSI
device that is not doing anything.   Another  term  for  this  is
multi-threaded.   A  SCSI device that has data in the buffer will
ask for the SCSI bus again,  and  send  the  data  for  the  last
command that it received.  If two or more devices attempt to grab
the SCSI bus, it falls to the priority of the device to determine
who shall win the bus.

REQ:  The SCSI bus uses this signal for  the  synchronization  of
data  on  the  SCSI bus.  Broken down, it simply is a signal that
means a SCSI device is asking for a byte of data.

ACK:  This SCSI signal is the inverse  of  the  REQ  signal.   It
means  that  a SCSI device has received the byte of data that was
REQuested.

Asynchronous:  This is  a  term  that  applies  to  how  data  is
transmitted to/from the SCSI bus.  For each byte requested, a REQ
signal is generated, and once the byte  has  been  sent,  an  ACK
signal  is  generated.   This allows SCSI devices to send/receive
data at the fastest rate possible for each  given  device.   Data
rates  up  to  3MBytes/sec  are  allowed  for  this  type of data
transfer.  All SCSI devices support this type of operation.

Synchronous:  This is similar  to  asynchronous  data  transfers,
except the ACK and REQ signals are sent in groups.  For instance,
if the offset negotiated for is 7, then the SCSI device will send
seven REQ's and the seven bytes of data and then it will wait for
the 7 ACK's before sending more data.  The pulse  widths  of  the
REQ's/ACK's  can  be very short as there is no need for a ACK for
each REQ.  This allows the  highest  throughput  possible  for  a
SCSI-1 device.  Data rates up to 5MBytes/sec are allowed for this
method of data transfer.   Not  all  SCSI  devices  support  this
feature.

Automatic Read/Write Reallocation:  SCSI  devices  give  you  the
appearance  of  having  no flaws.  While in truth there are media
flaws,  SCSI devices hide  these  flaws  by  keeping  a  list  of
sectors that are not available to you.  These sectors are used by
the SCSI device to replace bad sectors.  If you have reallocation
turned on, the SCSI device will automatically map out bad sectors
as they are found.  This  is  accomplished  in  the  same  manner
during  a  low-level  format.   That  is  how  a  SCSI device can
maintain the same capacity after many years of use.   Degradation
of  the  capacity  will  not  occur  until  the  device  has  run
completely out of spares.

Firmware:  All SCSI devices have programs that interface with the
SCSI  bus  and  the  hardware  of a particular SCSI device.  This
program is contained in a ROM on the SCSI device and is  referred
to as firmware.

Sense Key:  This is referring to the main error code that a  SCSI
drive  will  send  to  the host system.  It is a single byte that
represents a number associated with the list of  error  codes  in
the back of your SCSI hard drive installation guide.

Sense Data:  This is the data associated with a sense key.   This
data  further  qualifies  the  error  that has occurred on a SCSI
device.

Message System:  SCSI uses a message system for initializing  the
device  as  well as action upon reconnecting/disconnecting.  This
message system is a well defined set of bytes in  the  SCSI  ANSI
standard.

Check Condition:  This data tells the host CPU that an error  has
occurred  on the previous command and the SCSI device expects the
host to ask for the sense key/data before  any  further  commands
can  be sent to the device.  Basically, the SCSI device is asking
the host, "Please check my condition?".

Zone:  Some  SCSI  devices  have  the  media  split  into  zones.
Consider  zones  to  be  partitions of the SCSI hard drive media.
Each partition may contain a  different  number  of  sectors  per
track.   These  partitions also contain spare sectors and tracks.
This keeps the SCSI device from putting  all  spare  sectors  and
tracks in one spot on the device.

Identify Message:  This  message  is  used  when  more  than  one
initiator  is  on the SCSI bus.  It allows multiple initiators to
know which device on the SCSI bus is asking for service from that
initiator.  This is usually disabled for SCSI devices as multiple
initiators are not a supported feature.

Prefetch:  This term is used in reference to  SCSI  devices  that
have  the  ability to get data into the local device buffer, that
has not actually been requested.   Some  SCSI  devices  have  the
ability  to  do  a  read  ahead,  while  others have a true cache
mechanism.  In both implementations, the device  will  read  more
data  into  the  device buffer than was actually requested.  This
helps only when data is requested in a sequential manner, as  may
be done in the MS-DOS/OS2 operating environments.

ECC:  ECC is a mechanism employed by many types of  devices  that
allows  the  device  to do error correction on data that has been
misread from the media.  This helps to ensure data integrity  for
a device.  It also adds some overhead.



































All SCSI error messages will be displayed at the  bottom  of  the
screen  in  a  window.  All other errors will be displayed in the
center of the screen with the appropriate error message.

Unknown:  An unknown error has occurred.

Recovered Error:  The last command  completed  successfully  with
some recovery action performed by the device.

Not Ready:  The device selected is not ready.  For a  tape  drive
it  may  indicate  that the tape is not loaded in the drive.  For
another type of removable media device it could indicate that the
device is not up to speed or the media is not loaded.

Media Error:  The last command terminated  with  a  non-recovered
error  condition  that  was  probably  caused by some flaw in the
media.

Hardware Error:  The device detected a  non-recoverable  hardware
failure while performing the command.

Illegal Request:  There was an illegal parameter in  the  command
or  in  the  additional data parameters supplied for the command.
The command will be terminated without altering the device.

Unit Attention:  The device has received a hard reset  since  the
last command has been issued.

Aborted Command:  The device has aborted the  command.   You  may
try the command again.

Miscompare:  The source data did not match the data read from the
media.

Could not get mode sense data from SCSI device:  The device  that
has  been  selected  did  not  return  the  requested information
related to the main  menu  choice.   This  error  indicates  that
either  the mode page selected is not supported by this device or
the device is in such a state that the data cannot be sent.



























Test Unit Ready:  This is used to test to  see  if  a  device  is
available.

Request Sense:  This command is used to get error  codes  from  a
SCSI device.

Format Unit:  This command is used to do a  low-level  format  of
the SCSI device.

Inquiry:  This command returns information about a  SCSI  device.
Such as the manufacturer, firmware level, and so on.

Mode Select:  This command returns the tunable information  about
a  SCSI  device  so  that it may be modified and sent back to the
device via the mode sense command.

Mode Sense:  This command is used to  send  information  about  a
particular section of tunable parameters to the device.

Start/Stop Unit:  This command is used to start a device that has
spun  down.   It is also used to load a tape when a tape drive is
present in the system.

Read Capacity:  This command  returns  the  capacity  of  a  SCSI
device.   The  capacity  is  returned  in  total  number  of user
accessible blocks on the device.

Read Defect List:  This command returns the  defect  list  for  a
SCSI hard drive only.  Tape drives have no defect list.