The Configuration Manager Version 1.00
               Configuration Selection and Boot Control Program
                   Copyright (C) 1992 by McAfee Associates.
                            All Rights Reserved.

                       Documentation by Aryeh Goretsky






























          McAfee Associates                      (408) 988-3832 office
          3350 Scott Blvd. Bldg. 14              (408) 970-9727 fax
          Santa Clara, CA  95054-3107            (408) 988-4004 BBS
          U.S.A.                                 USR HST/v.32/v.42bis/MNP1-5
                                                 CompuServe    GO VIRUSFORUM
                                                 Internet support@mcafee.COM















                              TABLE OF CONTENTS

          SYNOPSIS . . . . . . . . . . . . . . . . . . . . . . . . . 2
           - What is The Configuration Manager (TCM)?
           - Configuration Control Program (CCP)
           - Multiple Configuration Manager (MCONFIG)
           - System requirements

          AUTHENTICITY . . . . . . . . . . . . . . . . . . . . . . . 3
           - Verifying the integrity of TCM

          CCP OVERVIEW . . . . . . . . . . . . . . . . . . . . . . . 4
           - General description of CCP

          CCP INSTALLATION and OPERATION . . . . . . . . . . . . . . 5
           - Detailed description of CCP's options

          CCP EXTRA PRECAUTIONS. . . . . . . . . . . . . . . . . . . 7
           - Back up system before installation
           - Back up CCP restore disks
           - Disable caching hard disk controllers before installation

          MCONFIG OVERVIEW . . . . . . . . . . . . . . . . . . . . . 8
           - General description of MCONFIG

          MCONFIG INSTALLATION and OPTIONS . . . . . . . . . . . . . 9
           - Options for use with MCONFIG

          MCONFIG MENU ITEMS . . . . . . . . . . . . . . . . . . . . 10
           - How to insert Configuration Selection Menu items

          MCONFIG DISPLAY ITEMS. . . . . . . . . . . . . . . . . . . 12
           - How to change MCONFIG's colors

          MCONFIG SUPPLEMENTAL PROGRAMS. . . . . . . . . . . . . . . 13
           - How to use the ASK, PAUSE, and ECHO device drivers

          MCONFIG EXAMPLES . . . . . . . . . . . . . . . . . . . . . 15
           - Sample CONFIG.SYS and AUTOEXEC.BAT files

          MCONFIG TUTORIAL . . . . . . . . . . . . . . . . . . . . . 18
           - Learn how to use MCONFIG

          NOTES ON MCONFIG . . . . . . . . . . . . . . . . . . . . . 20
           - DOS 3.3 and DOS 5.0 considerations

          APPENDIX A: Advanced MCONFIG Features  . . . . . . . . . . 21
           - How to use the ENVIRON and SET device drivers
           - How to use the MCON-ERR, MCON-SET, and CREM programs


                                    Page 1


TCM Version 1.00                                    Page 2


          SYNOPSIS

               The Configuration Manager (TCM) is a suite of utilities
          designed to provide system access, boot, and configuration
          control while allowing multiple configurations for flexibility.
          TCM is for IBM PC and compatible computers using MS-DOS, PC-DOS
          operating systems.  TCM provides secure access, boot protection,
          configuration locking, optional hard disk password protection,
          and up to 14 different multiple configuration setups inside the
          CONFIG.SYS and AUTOEXEC.BAT files.

               TCM consists of two parts:  CCP (Configuration and Control
          Program) for access, boot, and configuration locking; and
          MCONFIG (for Multiple CONFIGuration Manager) for selecting
          multiple configurations.

              The CCP installation program installs a new master boot
          record (MBR or partition table) on the hard disk.  The original
          MBR is copied to a hidden file on the hard drive and to a
          floppy diskette for recovery purposes.

              The new MBR prevents access to the hard disk when the
          system is booted from a diskette, password-protects the hard
          disk on boot-up, and/or prevents booting if changes have been
          made to the CONFIG.SYS or AUTOEXEC.BAT files without supervisor
          approval -- a feature for standardizing configurations in
          corporate environments.  The supervisor selects which features
          the new MBR will have.

               MCONFIG is a device driver that loads through the
          CONFIG.SYS file.  MCONFIG presents the user with a menu of the
          different configurations available.  After selecting one,
          MCONFIG modifies the in-memory copy of CONFIG.SYS so that only
          the commands for the selected configuration are executed.

               TCM Version 1.00 works on any system with 256Kb of
          memory and DOS 3.3 or greater.  One floppy disk is required
          for each system CCP is installed on.  CCP is not compatible
          with DOS 2.nn systems or PC's with a 'dual boot' partition,
          such as DOS-Unix or DOS-OS/2.  MCONFIG requires MS-DOS or
          PC-DOS 3.30 or above.  It is not compatible with DR-DOS.












TCM Version 1.00                                    Page 3


          AUTHENTICITY

               TCM is packaged with the VALIDATE program to ensure the
          integrity of the TCM files.  The VALIDATE.DOC file tells how
          to use VALIDATE.  VALIDATE can be used to check subsequent
          versions of TCM for tampering.

               The validation results for Version 1.00 should be:

          FILENAME     SIZE       DATE         CHECK METHOD

          ASK.SYS      S:4,057    D:08-19-92   M1: 6E41  M2: 146B
          CCP.COM      S:9,499    D:07-21-92   M1: E5E3  M2: 17FC
          CCP.MBR      S:39,361   D:12-04-92   M1: e658  M2: 0BE5
          CREM.EXE     S:15,372   D:08-21-92   M1: 6D59  M2: 1EC8
          ECHO.SYS     S:1,700    D:08-19-92   M1: CE25  M2: 0C88
          ENVIRON.SYS  S:298      D:08-19-92   M1: AB32  M2: 1504
          MCONFIG.SYS  S:13,651   D:08-21-92   M1: 6CF3  M2: 1061
          MCON-ERR.COM S:71       D:07-23-92   M1: 51EE  M2: 1EEC
          MCON-SET.EXE S:10,098   D:07-23-92   M1: 935D  M2: 0400
          PAUSE.SYS    S:1,890    D:08-19-92   M1: 4D46  M2: 10AA
          SET.SYS      S:2,518    D:08-19-92   M1: 5ED3  M2: 17AF


          If your copy of TCM differs, it may have been damaged (or the
          CCP.MBR file may have been pre-configured by the system
          administrator).  Always obtain TCM from a known source, such as
          McAfee Associates, its Agents, or the person responsible for
          computer security in your organization.  The latest version of
          TCM and validation data for its programs can be obtained from
          McAfee Associates' bulletin board system at (408) 988-4004 or
          from the CompuServe Computer Virus Help Forum (GO VIRUSFORUM).

               All of McAfee Associates' programs have been archived
          with PKWare's PKZIP Authentic File Verification.  If you do
          not see an "-AV" after every file is unzipped and receive
          the "Authentic Files Verified! # NWN405 Zip Source: McAFEE
          ASSOCIATES" message then do not use them.

               If your version of PKUNZIP does not have verification
          ability, then this message may not be displayed.  Please
          contact us if you believe tampering has occurred to the .ZIP
          file.










TCM Version 1.00                                    Page 4


          CCP OVERVIEW

               CCP installs a custom Master Boot Record (partition table)
          onto the first five sectors on the hard disk, an area of the
          disk that typically remains unused.
               The MBR installed by CCP can be configured to perform
          several functions:  It can prevent access to the hard disk when
          the PC is booted from a floppy, prompt the user for a password
          when the system is booted from the hard disk, and lock the
          system when changes have been made to the CONFIG.SYS and
          AUTOEXEC.BAT files.
               The MBR will also prevent accesses to the first five (5)
          sectors of the hard disk which contain its code.  Access to
          this area while CCP is active will show the original (pre-CCP
          installation) MBR.  CCP will prevent any changes from being
          made to this part of the disk.

          NOTE:  When CCP's custom MBR is installed and running, it will
                 reduce the amount of total conventional memory available
                 to the system by 1,024 bytes.  Thus, a system with 640Kb
                 of memory (655,360 bytes) will report that it has 639Kb
                 of memory (654,336 bytes) available.

               When CCP is installed, it will save the original MBR to
          a floppy diskette as a backup.  The floppy disk should be
          clearly labeled as a CCP RECOVERY DISKETTE and write protected.
          Be sure to write the user's name, department, PC serial number
          and any other important information on the label.  CCP will
          also create a hidden file in the root directory of the disk
          containing the first five sectors of the hard disk.  The file
          is named ±ðDISKð±.IDN.


          NOTE:  Do not install or run CCP while disk caching software or
                 hardware is in use.  CCP performs direct writes to the hard
                 disk which may not be handled correctly by disk caching
                 algorithms.  Use of disk caches while installing CCP via
                 the CCP.COM program may result in the loss of all data on
                 the hard disk.  Disk caches can be used AFTER CCP has
                 been installed, reconfigured, or removed.













TCM Version 1.00                                    Page 5


          CCP INSTALLATION and OPERATION


          NOTE:  If MCONFIG and CCP are to be used together, then MCONFIG
                 must be installed first.  Please refer to the section on
                 installing MCONFIG for more information.

               To install CCP onto your hard disk, run the CCP.COM
          program.  The main menu will appear.  Main menu items are:

             Set Access - Configure CCP's functions
             Install - Install (or reinstall) CCP
             Recover - Restore CCP after virus infection or disk crash
             Remove - Remove CCP from hard disk
             Exit - Save configuration and return to DOS

          SET ACCESS
               Selecting 'Set Access' brings up the 'Access Password' and
          'Configuration' items.
               'Access Password' selects and changes the SuperUser's
          (system administrator) password.  After selecting a SuperUser
          password, be sure to write it down and store it in a safe
          location.  The SuperUser password is required to reconfigure
          CCP.
                 Selecting 'Configuration' brings up the Configuration
          menu.  This menu allows you to select which items require
          SuperUser approval.  Configuration Selection Menu items are:

             Recover hard disk protection
             Remove hard disk protection
             (Re)Install hard disk protection
             Set boot password

          Move between options with the cursor keys.  Select options with
          the space bar.  Options that have been selected will have a
          check-mark (ASCII 251) character in front of them.  All selected
          items will be set as "unavailable" to end users.  The SuperUser
          password will be required to gain access to these functions.

          INSTALL
               Selecting 'Install' brings up the 'Available Options' menu.
          This menu allows you to select which items the CCP MBR is
          installed with.  Available Options menu items are:

             Require password to boot the operating system
             Check CONFIG.SYS and AUTOEXEC.BAT at system boot
             Prevent access to hard disk if system booted from floppy disk

               Selecting 'Require password...' allows the user to select a
          password that will be requested by CCP each time the system is
          booted from the hard disk.


TCM Version 1.00                                    Page 6


          NOTE:  The 'Require password to boot the operating system' item
                 appears only if 'Set Boot Password' is not restricted by
                 the Set Access menu.

               Selecting 'Check CONFIG.SYS and AUTOEXEC.BAT at system
          boot' enables a check of the CONFIG.SYS and AUTOEXEC.BAT files
          when the system is booted from the hard disk.  Any changes made
          to these files will result in the message

             AUTOEXEC.BAT and/or CONFIG.SYS has been modified.
             Enter SuperUser password.

          being displayed when the system is booted.  The hard drive will
          be locked until the SuperUser enters the password and reinstalls
          CCP or replaces the original configuration files.

               Selecting 'Prevent access to hard disk if system booted
          from floppy disk' disables access to the hard disk when the
          system is booted from a floppy.  Attempts to access the hard
          disk will result in an "Invalid Media Specification" error
          being displayed.

          RECOVER
               Selecting 'Recover' allows you to restore CCP after a disk
          crash or virus infection that has corrupted the Master Boot
          Record.  After selecting 'Recover' CCP will prompt the user to
          insert the CCP MBR recovery disk to reload the CCP MBR from.
          When finished, CCP will reboot the system.

          REMOVE
               Selecting 'Remove' allows you to unload CCP from the hard
          disk and restore the original Master Boot Record.  After
          selecting 'Remove', CCP will restore the original MBR and
          reboot the system.

          EXIT
               Selecting 'Exit' allows you to return to DOS.  If CCP has
          been reconfigured, it will prompt the user to save changes
          before exiting.














TCM Version 1.00                                    Page 7


          CCP EXTRA PRECAUTIONS

          BACK UP
               Before installing CCP, it is recommended that the system be
          backed up.  After installing CCP, it is recommended that one or
          more backup copies of the CCP recovery diskette be made and
          stored in a safe location.  The DOS DISKCOPY command can be used
          to make copies of CCP MBR backup diskettes.

          NOTE:  The CCP recovery diskette will appear unreadable to
                 normal DOS programs, including the DIR command.  Only
                 CCP can access the diskette.

          CACHING HARD DISK CONTROLLER CARDS
               If you are installing CCP on a PC equipped with a caching
          hard disk controller card, it is recommended that you disable
          the disk cache before installing CCP.  After CCP has been
          installed, the disk cache can be returned to normal operation.



































TCM Version 1.00                                    Page 8


          MCONFIG OVERVIEW


               MCONFIG is a device driver that allows the selection of
          different configuration set ups.  At boot up, MCONFIG
          displays a menu listing available configurations.  After
          selecting a configuration, MCONFIG modifies the in-memory copy
          of the CONFIG.SYS file so that only the configuration selected
          will be used.  After the selected configuration has been
          executed, a single AUTOEXEC batch file or multiple AUTOEXEC
          files can be executed.

               MCONFIG comes with a number of supplementary device drivers
          to simplify the creation of multi-configuration environments.
          These device drivers are explained in appendix A.

               MCONFIG works by placing Menu Items within the CONFIG.SYS
          file, followed by the different "selection blocks" of CONFIG.SYS
          entries to be used when each Menu Item is selected.  Menu Items
          display the actual text to appear on the Configuration Selection
          menu; these are followed by the CONFIG.SYS entries associated
          with each Menu Item.































TCM Version 1.00                                    Page 9


          MCONFIG INSTALLATION and OPTIONS

               MCONFIG is normally placed at the beginning of the
          CONFIG.SYS file.  When initially executed, MCONFIG reads in
          the rest of the CONFIG.SYS file and displays a Configuration
          Selection menu based on the Menu Items found.

          NOTE:  There will be several entries for MCONFIG in the
                 CONFIG.SYS file:  one to initially load MCONFIG,
                 one for each Menu Item, plus an entry to signal where
                 MCONFIG stops processing the last menu entry.
                 Additional entries to set colors and other options may
                 also appear.

               Valid options for MCONFIG are listed below:

          DEVICE = MCONFIG.SYS CENTER DEFAULT=n END NOHIGHVIDEO NUMOFF
                   TIMEOUT=n PASSIVE {left shift key} {right shift key}

          Options are:

                     CENTER - center Menu Items in window
                  DEFAULT=n - use Menu Item 'n' as default
                        END - tells where last Menu Item finishes
                NOHIGHVIDEO - disable video attributes used on EGA/VGA
                              monitors
                     NUMOFF - turn off NumLock
                    PASSIVE - execute first Menu Item as default
                              (see below for specifics)
                  TIMEOUT=n - set delay time in seconds for DEFAULT
           {left shift key} - invoke Menu Item 1 at boot-up
          {right shift key} - invoke Menu Item 2 at boot-up

          NOTE:  Use the complete pathname for only the first MCONFIG
                 entry.  For other entries use the statement
                 "DEVICE = MCONFIG options" with a pathname.

               The CENTER switch tells MCONFIG to center Menu Items
          in the MCONFIG Configuration Selection menu window.  By
          default, all Menu Items are left-justified.

               The DEFAULT switch tells MCONFIG which Menu Item to
          select as the default menu selection.  It can be used with the
          TIMEOUT switch to invoke a default configuration.  Syntax is
          DEFAULT=n where 'n' is the Menu Item to select as the default
          OR place the DEFAULT switch on the MCONFIG Menu Item line to be
          selected as the default Menu Item.






TCM Version 1.00                                    Page 10


               The END switch tells MCONFIG to finish processing menu
           entries.  Any CONFIG.SYS entries after the END switch will be
           executed with all configurations.

               The NOHIGHVIDEO switch disables the "high video"
          attributes used on EGA and VGA monitors.  If you are using a
          different type of monitor, you may see blinking characters on
          the screen.  If so, use the NOHIGHVIDEO switch with MCONFIG.

               The NUMOFF switch turns off the NumLock key.

               The PASSIVE switch tells MCONFIG to use the first Menu
          Item unless you tell it to pop up the menu by pressing the
          left SHIFT key.  If the right SHIFT key is pressed, MCONFIG
          executes the second Menu Item.

               In non-passive mode, holding down the {LEFT SHIFT KEY}
          during boot-up will automatically start the first Menu Item
          without displaying the Configuration Selection Menu.

               Holding down the {RIGHT SHIFT KEY} during boot-up will
          automatically start the second Menu Item without displaying the
          Configuration Selection Menu.

          Key pressed ³ In ACTIVE Mode          ³ In PASSIVE mode
          at boot-up  ³ (default)               ³ (using PASSIVE switch)
          ÍÍÍÍÍÍÍÍÍÍÍÍØÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍØÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ
          none        ³ MCONFIG menu is always  ³ First Menu Item is
                      ³ displayed on screen.    ³ executed without
                      ³                         ³ displaying the menu.
          ÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          left SHIFT  ³ First Menu Item is      ³ MCONFIG menu is
          key         ³ executed.               ³ displayed on screen
          ÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          right Shift ³ Second Menu Item is     ³ Second Menu Item is
          key         ³ executed without        ³ executed without
                      ³ displaying the menu.    ³ displaying the menu.


          MCONFIG MENU ITEMS


               Menu Items tell MCONFIG what text to insert into the
          Configuration Selection Menu.  The syntax is:

          DEVICE = MCONFIG "text \TEXT\ \T\ext" DEFAULT TIMEOUT=n

          When MCONFIG sees the double quote in the CONFIG.SYS file
          after MCONFIG, it adds that Message Line to the Configuration
          Selection Menu.



TCM Version 1.00                                    Page 11


          The operating system displays all lines in the CONFIG.SYS in
          UPPER CASE.  To make messages more readable, MCONFIG switches
          between cases.  This is done by placing a backslash character
          "\" in the Message Line text.  Example:

          DEVICE = MCONFIG "T\his is a \TEST\ \M\essage."

          would be displayed on the screen as:

               "This is a TEST Message."

               The DEFAULT and TIMEOUT switches can be used with Message
          Lines (See MCONFIG INSTALLATION and OPERATIONS for more
          information).

               After each Menu Item, place the CONFIG.SYS entries to use
          with it.  At the end of the multi-configuration area of the
          CONFIG.SYS file, place a "DEVICE = MCONFIG End" statement.

               A commented example of a CONFIG.SYS:

              COMMENTS         ³             CONFIG.SYS Contents
          ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍØÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ
          invoke MCONFIG       ³  device = C:\MCONFIG\MCONFIG.SYS
                               ³
          option 1 on the menu ³  device = MCONFIG "M\enu entry number 1"
                               ³       ........
                               ³       statements to execute if selected
                               ³       ........
                               ³
          option 2 on the menu ³  device = MCONFIG "M\enu entry number 2"
                               ³       ........
                               ³       statements to execute if selected
                               ³       ........
                               ³
          mark the end         ³  device = MCONFIG End
                               ³
          These lines are used ³  DOS     = High, UMB
          with all selections  ³  Files   = 30
          since they are after ³  Stacks  = 0,0
          the MCONFIG = END    ³  Buffers = 10
          statement.           ³  Break   = OFF

                Using the above CONFIG.SYS file, the following
          Configuration Selection menu will be displayed:

                 ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                 º                                                º
                 º  Menu entry number 1                           º
                 º  Menu entry number 2                           º
                 º                                                º
                 ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

TCM Version 1.00                                    Page 12


          The first entry is highlighted by the "selection bar".
          Choosing Entry 1 causes the statements immediately following
          the first selection block to be executed, and statements in
          the other selection blocks will be ignored by the system.


          MCONFIG DISPLAY ITEMS


          NOTE:  MCONFIG automatically detects monochrome monitors
                 and will adjust screen colors appropriately.

               Display Items allow you to change MCONFIG's default
          colors.  Display items follow the following syntax:

               DEVICE = MCONFIG displayitem = color

          Where "displayitem" is the item to change the color of and
          "color" is the color to use.  Display Items are as follows:

               DISPLAY ITEM        COLOR
               ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÑÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ
               BannerBorder       ³top and bottom lines of screen
                                  ³
               BannerBackground   ³copyright background color
                                  ³
               BannerForeground   ³copyright foreground color
                                  ³
               BackgroundFill     ³background screen color
                                  ³
               DialogBorder       ³border color around Configuration
                                  ³Selection menu dialog box.
                                  ³
               DialogBackground   ³background color of Configuration
                                  ³Selection menu dialog box.
                                  ³
               DialogForeground   ³foreground color of Configuration
                                  ³Selection menu dialog box.
                                  ³
            SelectionBarBackground³background color used when displaying
                                  ³the moveable selection bar.
                                  ³
            SelectionBarForeground³foreground color used when displaying
                                  ³the moveable selection bar.









TCM Version 1.00                                    Page 13


          Valid color values are:
          ÍÍÍÍÍÍÍÍÍÍÍÍÍÑÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ
          Blue         ³  LightBlue (BrightBlue)
          Green        ³  LightGreen (BrightGreen)
          Cyan         ³  LightCyan  (BrightCyan)
          Red          ³  LightRed (BrightRed)
          Magenta      ³  LightMagenta (BrightMagenta)
          Brown        ³  Yellow (BrightBrown)
          DarkGray     ³  LightGray (BrightGray)
          White        ³


          MCONFIG SUPPLEMENTAL PROGRAMS

          ASK.SYS DEVICE DRIVER

               The ASK.SYS device driver is a device driver that can be
          used to ask simple, one-line Yes/No questions at boot-up and
          then selectively load other device drivers based upon the
          response.  Questions can be placed in Menu Item "selection
          blocks".  The syntax for ASK is:

          DEVICE = ASK.SYS "Question" DEFAULT=x TIMEOUT=n
             DEVICE = YES
               (lines to execute if YES)
               ...
             DEVICE = NO
               (optional lines to execute if NO)
               ...

          DEVICE = END

          For information on the DEFAULT and TIMEOUT switches, please
          refer to the MCONFIG INSTALLATION and OPERATIONS section.

               An example of the ASK.SYS device driver:

             device=c:\Ask.Sys "L\oad mouse driver?" default=Y timeout=10
             device=YES
                  device=c:\mouse\mouse.sys
             device=END

          The same caveats that apply to MCONFIG for DOS 3.3 and DOS 5.0
          exist for ASK (see NOTES ON MCONFIG for more information).


          PAUSE.SYS DEVICE DRIVER

               The PAUSE.SYS device driver performs identically to the
          DOS PAUSE batch file command.  It displays an optional message



TCM Version 1.00                                    Page 14


          and waits for any key to be pressed.  The syntax for PAUSE is:

               DEVICE = PAUSE.SYS message

          where "message" is an optional message to display.  If no
          message is given, PAUSE will display:

               Press any key when ready...

          Otherwise, PAUSE will display the optional message.

          An example of the PAUSE.SYS device driver:

               DEVICE = C:\PAUSE.SYS P\ress any to continue \CONFIG.SYS

          would display the following message:

               Press any key to continue CONFIG.SYS

          and pause until a key was pressed.


          ECHO.SYS DEVICE DRIVER

               The ECHO.SYS device driver performs identically to the
          DOS ECHO batch file command.  It is useful for debugging the
          CONFIG.SYS file.  The syntax for ECHO is:

               DEVICE = ECHO.SYS message

          where "message" is a message to display.

               An example of the ECHO.SYS device driver:

               DEVICE = C:\ECHO.SYS L\oading \MOUSE\ driver now.
               DEVICE = C:\MOUSE\MOUSE.SYS
               DEVICE = C:\ECHO.SYS MOUSE\ has loaded successfully.
               DEVICE = C:\PAUSE.SYS

          would display the message "Loading MOUSE driver now.", load
          the mouse driver into memory, display the message "MOUSE has
          loaded successfully." and pause until a key is pressed.











TCM Version 1.00                                    Page 15


          MCONFIG EXAMPLES


               Following are a sample CONFIG.SYS file and two sample
          AUTOEXEC.BAT files.  The CONFIG.SYS has three different
          configurations for booting without network drivers, booting
          with LAN Manager, and booting with Novell NetWare drivers.

          NOTE:  The first and last four lines of the CONFIG.SYS file are
                 outside of the "DEVICE=C:\MCONFIG.SYS" and "MCONFIG End"
                 lines are shared across all selections and will ALWAYS
                 be run.

          __ SAMPLE CONFIG.SYS FILE ______________________________________
          DOS     = high,umb
          device  = c:\dos\himem.sys
          device  = c:\emm386.exe ram noems i=b000-b7ff
          shell   = c:\command.com /p /e:512

          DEVICE  = c:\mconfig.sys Center NumOff
          device  = MCONFIG SelectionBarBackground=RED

          device = MCONFIG "N\o network" Default Timeout=30
            devicehigh = c:\mouse\mouse.sys /y /s30
            devicehigh = c:\dos\ansi.sys
            devicehigh = c:\dos\setver.exe
            device = c:\MCONFIG\Ask.Sys "L\oad the \MOUSE\ driver?"
            device = YES
            devicehigh = c:\mouse\mouse.sys /y /s30
            device = END

          device = MCONFIG "LAN M\anager \N\etwork"
            devicehigh = c:\netlib\dxma0mod.sys 001
            devicehigh = c:\netlib\dxmc0mod.sys
            devicehigh = c:\netlib\dxmt0mod.sys s=32 c=32
            devicehigh = c:\dos\ansi.sys
            devicehigh = c:\dos\setver.exe

          device = MCONFIG "N\ovell \N\etwork"
            devicehigh = c:\mouse\mouse.sys /y /s30
            devicehigh = c:\netlib\dxma0mod.sys 001
            devicehigh = c:\netlib\dxmc0mod.sys
            devicehigh = c:\netlib\dxmt0mod.sys s=32 c=32
            devicehigh = c:\dos\ansi.sys
            devicehigh = c:\dos\setver.exe

          device = MCONFIG End

          buffers   = 20
          files     = 50
          STACKS    = 0,0
          lastdrive = E

TCM Version 1.00                                    Page 16


              The first sample AUTOEXEC.BAT file shows how to use the
          MCONFIG environment variable to login to a Novell network from
          a single AUTOEXEC file, using the results from the sample
          CONFIG.SYS above.

          NOTE:  These SAMPLES make use of the MCON-SET.EXE program used
                 for setting DOS environmental variables from MCONFIG.
                 For information on using this and the MCON-ERR.COM DOS
                 ERRORLEVEL-setting program, please refer to APPENDIX A.

          __ SAMPLE FIRST AUTOEXEC.BAT FILE _____________________________
          REM Run the MCON-SET program to set the environment variable
          REM "MCONFIG" to the selection made from the menu.
          C:\MCONFIG\MCON-SET.EXE
          set comspec=c:\command.com
          path c:\dos;c:\bat;c:\utils
          set prompt=$p$g
          C:\MCAFEE\VSHIELD.EXE /CHKHI /CV /LH /M
          mode con rate=30 delay=1

          if NOT "%MCONFIG%" == "3" goto no_novell
            c:\netware\wsgen\ipx
            c:\netware\wsgen\route
            c:\netware\wsgen\netx
            f:
            C:\MCAFEE\VSHIELD.EXE /RECONNECT
            login mcafee_server_1/John_M
            path %path;c:\netware
          :no_novell
          ________________________________________________ END OF FILE __


               This example shows how to use the MCONFIG environment
          variable to have 3 separate AUTOEXEC files.  Depending upon
          the selection made from the MCONFIG menu, either AUTO-1.BAT,
          AUTO-2.BAT, or AUTO-3.BAT will execute.

          __ SAMPLE SECOND AUTOEXEC.BAT FILE ____________________________
          REM Call the MCON-SET program to set the environment variable
          REM "MCONFIG" to the selection made from the menu.  Then call
          REM the matching AUTO-n.BAT file.
          C:\MCAFEE\VSHIELD.EXE /CHKHI /CV /LH /M
          C:\MCONFIG\MCON-SET.EXE
          C:\AUTO-%MCONFIG%.BAT
          ________________________________________________ END OF FILE __








TCM Version 1.00                                    Page 17


          __ SAMPLE AUTO-1.BAT FILE _____________________________________
          set comspec=c:\command.com
          path c:\dos;c:\bat;c:\utils
          set prompt=$p$g
          mode con rate=30 delay=1
          ________________________________________________ END OF FILE __


          __ SAMPLE AUTO-2.BAT FILE _____________________________________
          set comspec=c:\command.com
          path c:\dos;c:\bat;c:\utils
          set prompt=$p$g
          mode con rate=30 delay=1
          ________________________________________________ END OF FILE __


          __ SAMPLE AUTO-3.BAT FILE _____________________________________
          set comspec=c:\command.com
          path c:\dos;c:\bat;c:\utils
          set prompt=$p$g
          mode con rate=30 delay=1
          c:\netware\wsgen\ipx
          c:\netware\wsgen\route
          c:\netware\wsgen\netx
          f:
          C:\MCAFEE\VSHIELD.EXE /RECONNECT
          login mcafee_server_1/John_M
          ________________________________________________ END OF FILE __

























TCM Version 1.00                                    Page 18


          MCONFIG TUTORIAL


               The easiest way to get familiarized with MCONFIG is to
          create a two-selection CONFIG.SYS file.  Option one is your
          existing CONFIG.SYS file.  Option two will be a minimum
          "bare-bones" configuration.

               Load the CONFIG.SYS file into your text editor or word
          processor and make the following changes to the current
          CONFIG.SYS file:

          NOTE:  When editing the CONFIG.SYS file with a word processor
                 be sure to save it as an ASCII text file, not a word
                 processor document.

          Add the following two lines to the top of the CONFIG.SYS file
          (change the pathname if MCONFIG is located elsewhere):

               device=C:\MCONFIG\MCONFIG.SYS CENTER
               device=MCONFIG "S\tandard \C\onfiguration" Default Timeout=30

          Next, go to the end of the CONFIG.SYS file and add:

               device=MCONFIG "M\inimal \C\onfiguration"
                 files   = 20
                 buffers = 30
               device=MCONFIG End

          Save the CONFIG.SYS file and re-boot the computer.  The MCONFIG
          Configuration Selection menu will appear with two configuration
          options.  Selecting the first option loads the original
          CONFIG.SYS.  Selecting the second option loads the minimal
          configuration.



















TCM Version 1.00                                    Page 20


          NOTES ON MCONFIG

          USING MCONFIG with DOS 3.30

               MCONFIG is designed to work seamlessly with DOS Version
          4.00 and above.  It can be used with DOS 3.3x with the
          following considerations:

          -    DOS 3.3x does not allow a "REMark" statement in the
               CONFIG.SYS file.  MCONFIG adds a REM to comment-out
               un-needed lines so this will cause a problem with DOS 3.3.
                    To get around this, MCONFIG precedes unwanted lines
               with "BREAK=OFF" statements.  This is done automatically
               by MCONFIG if run under DOS 3.3x.

          -    To set BREAK=ON in the CONFIG.SYS, place the "BREAK=ON"
               statement after the "DEVICE = MCONFIG End" statement.

          -    Lines with less than three characters after the equals "="
               sign will not be correctly proceeded with a "BREAK=OFF"
               statement.
                    For example, "BUFFERS = 5" is not long enough and
               will give an "Invalid Command?" error when executed in
               the CONFIG.SYS file.  This does not affect the operation
               of MCONFIG or the CONFIG.SYS file.
                    To get around this, add spaces to the right
               of short entries.  For example, changing "BUFFERS = 5" to
               "BUFFERS = 5     *" allows MCONFIG to change the line to
               a "BREAK = OFF" statement, removing the "Invalid Command?"
               error message from DOS.

          USING MCONFIG with DOS 5.00

               The only command that can NOT be selectably configured is
          the "DOS =" statement.  This is because DOS 5.0 checks the
          CONFIG.SYS file for "DOS =" entries before executing any device
          drivers and uses the last "DOS =" statement found to set itself
          up to load high.  This means that the following will NOT work:

               MCONFIG "L\oad \DOS\ \L\ow"
                  DOS=LOW
                  ...rest of configuration...

               MCONFIG "L\oad \DOS\ \H\igh"
                  DOS=HIGH,UMB
                  ...rest of configuration...

               MCONFIG End

          In the above example, the DOS=HIGH,UMB will always be used as
          this is the last setting DOS sees.  DOS will then load itself
          high before MCONFIG is executed.

TCM Version 1.00                                    Page 21


          APPENDIX A: Advanced MCONFIG Features


          ENVIRON.SYS DEVICE DRIVER


               The ENVIRON.SYS device driver, when used with the SET.SYS
          device driver, allows environmental variables to be set from
          within the CONFIG.SYS file.  Environmental variables set in
          this manner are retrieved by the MCON-SET program (normally run
          in the AUTOEXEC.BAT file).
               The ENVIRON.SYS device driver remains memory resident and
          stores up to 128 bytes of environmental variables.  The syntax
          for ENVIRON is as follows:

               DEVICE = ENVIRON.SYS

          There are no options.  The ENVIRON.SYS device driver uses 280
          bytes of RAM.


          SET.SYS DEVICE DRIVER


               The SET.SYS device driver stores an environmental variable
          and value for later retrieval by the MCON-SET program.  The
          syntax for SET is:

               DEVICE = SET.SYS variable = value

          where "variable" is the environmental variable to store and
          "value" is the value to store with it.

          NOTE:  ENVIRON.SYS must be loaded before SET.SYS is used.


          MCON-SET.EXE PROGRAM


               MCON-SET is a program that reads the environmental
          variables stored by SET and ENVIRON and places them into DOS
          environmental space.  There are no options for MCON-SET.  It is
          usually placed at or near the beginning of the AUTOEXEC.BAT
          file.


          MCON-ERR.COM PROGRAM

               MCON-ERR is a program that sets the DOS ERRORLEVEL to the
          same number as the Menu Item selected at boot-up.  For example,
          the first menu item would set the ERRORLEVEL to 1, the second
          to 2, and so forth.

TCM Version 1.00                                    Page 22


          CREM.EXE PROGRAM

               CREM (Configuration REMarker) prevents memory managers
          such as QEMM-386, 386^MAX, and BlueMAX from optimizing
          MCONFIG's Menu Item "Selection Blocks".  Memory managers may
          not recognize MCONFIG and change its settings so it no longer
          runs correctly.  CREM modifies the CONFIG.SYS file so that
          only one selection block is visible to the optimization
          program.

               Valid options for CREM are listed below:

          CREM block_number REMOVE

          Options are:

               block_number - REMark out MCONFIG-specific lines and
                              all selection blocks EXCEPT "block_number"
                     REMOVE - Restore MCONFIG-specific lines and all
                              selection blocks

               "Block_number" tells CREM to process the CONFIG.SYS file
          commenting out all MCONFIG-specific lines and all Menu Item
          "selection blocks" EXCEPT the specified "block_number".  This
          option is not compatible with REMOVE.

                REMOVE tells CREM to remove all REMarks from the
          CONFIG.SYS file placed there by a previous invocation of CREM
          (other comments will remain untouched).  This option is not
          compatible with "block_number".























TCM Version 1.00                                    Page 23


               An example of a CONFIG.SYS file before processing by
          CREM:

          __ SAMPLE CONFIG.SYS FILE _____________________________________
          DOS     = High
          device  = c:\qemm\qemm386.sys noems
          shell   = c:\command.com /e:512 /p

          device  = c:\utils\MCONFIG.SYS Center NumOff
          device  = MCONFIG SelectionBarBackground=RED

          device  = MCONFIG "C\onfiguration with cache"
            device = c:\mouse\mouse.sys /y /s30
            device = c:\cache\cache.sys 4096
            device = c:\DOS\ansi.sys
            device = c:\DOS\setver.exe

          device  = MCONFIG "C\onfiguration with \RAM\disk"
            device = c:\mouse\mouse.sys /y /s30
            device = c:\DOS\ramdrive.sys 4096
            device = c:\DOS\ansi.sys
            device = c:\DOS\setver.exe

          device = MCONFIG "M\inimal configuration"
            device = c:\DOS\ansi.sys
            device = c:\DOS\setver.exe

          device = MCONFIG End

          buffers   = 5
          files     = 60
          break     = on
          STACKS    = 0,0
          lastdrive = E
          ________________________________________________ END OF FILE __


















TCM Version 1.00                                    Page 24


               If CREM was invoked with "CREM 2", the CONFIG.SYS file
          would be modified as follows:


          __ SAMPLE CONFIG.SYS FILE AFTER CREM 2 PROCESSING _____________
          DOS     = High
          device  = c:\qemm\qemm386.sys noems
          shell   = c:\command.com /e:512 /p

          REM {!!}device  = c:\utils\MCONFIG.sys Center NumOff
          REM {!!}device  = MCONFIG SelectionBarBackground=RED

          REM {!!}device  = MCONFIG "C\onfiguration with cache"
          REM {!!}  device = d:\mouse\mouse.sys /y /s30
          REM {!!}  device = c:\cache\cache.sys 4096
          REM {!!}  device = c:\DOS\ansi.sys
          REM {!!}  device = c:\DOS\setver.exe
          REM {!!}
          REM {!!}device  = MCONFIG "C\onfiguration with RAMdisk"
            device = c:\mouse\mouse.sys /y /s30
            device = c:\DOS\ramdrive.sys 4096
            device = c:\DOS\ansi.sys
            device = c:\DOS\setver.exe

          REM {!!}device = MCONFIG "M\inimal configuration"
          REM {!!}  device = c:\DOS\ansi.sys
          REM {!!}  device = c:\DOS\setver.exe
          REM {!!}
          REM {!!}device = MCONFIG End

          buffers   = 5
          files     = 60
          break     = on
          STACKS    = 0,0
          lastdrive = E
          ________________________________________________ END OF FILE __


               Note that the second Menu Item "selection block" is
          available to DOS (and the optimization program).  Now that
          CREM has modified the CONFIG.SYS, the QEMM OPTIMIZE or
          386^MAX MAXIMIZE programs can be safely run.

               After optimization, execute the following:

               CREM REMOVE

          to remove the comments placed in the CONFIG.SYS file by CREM.
          This restores the MCONFIG Menu Item "selection blocks" (with
          an optimized second item).



TCM Version 1.00                                    Page 25


               There is no specific way to process the AUTOEXEC.BAT with
          CREM since there are many different ways AUTOEXEC.BAT files can
          be processed with MCONFIG.  Because of this, the AUTOEXEC.BAT
          files will have to be processed manually.
               If only one AUTOEXEC.BAT file is used, then processing is
          simplified.  For example, if the AUTOEXEC.BAT file is as
          follows:

          __ SAMPLE AUTOEXEC.BAT FILE __________________________________
          C:\MCONFIG\MCON_SET
          C:\MCAFEE\VSHIELD /CHKHI /CV /LH /M
          GOTO CONFIG_%MCONFIG%
          :CONFIG_1
             (first configuration)
          :CONFIG_2
             (second configuration)
          :CONFIG_3
             (third configuration)
          ________________________________________________ END OF FILE __


             Given the previous CONFIG.SYS example run with "CREM 2", edit
          the AUTOEXEC.BAT file as follows:


          __ SAMPLE AUTOEXEC.BAT FILE AFTER EDITING ___________________
          C:\MCONFIG\MCON_SET
          SET MCONFIG=2                        <--- add this line
          GOTO CONFIG_%MCONFIG%
          :CONFIG_1
             (first configuration)
          :CONFIG_2
             (second configuration)
          :CONFIG_3
             (third configuration)
          ________________________________________________ END OF FILE __

               After the optimization program has been run, edit the
          AUTOEXEC.BAT to remove the "SET MCONFIG=2" line.

          NOTE:  CREM will ALWAYS operate on C:\CONFIG.SYS.












TCM Version 1.00                                    Page 26


               Following are the steps necessary to optimize an MCONFIG
          configuration with three different Menu Item "selection
          blocks" using QEMM's OPTIMIZE in this example:


                 1.   run "CREM 1"
                 2.   Change AUTOEXEC.BAT for first configuration
                 3.   run "OPTIMIZE"

                 4.   run "CREM 2"
                 5.   Change AUTOEXEC.BAT for second configuration
                 6.   run "OPTIMIZE"

                 7.   run "CREM 3"
                 8.   Change AUTOEXEC.BAT for third configuration
                 9.   run "OPTIMIZE"
                 10.  run "CREM remove"