PrintCAD 1.30

                        printer driver for IBM/DOS CAD packages
                           including AutoCAD and Microstation

                      (C) Copyright Ravitz Software Inc. 1991,1993


         Ravitz Software Inc.                              BBS/FAX 606-268-0577
         P.O. Box 25068
         Lexington, KY  40524-5068
         USA                                  Compuserve Cary Ravitz [70431,32]


         Introduction ....................................................... 2
         License and Registration                                             3
         What Is New ........................................................ 3
         Operation                                                            4
         Installation ....................................................... 5
         Syntax                                                               6
         Example Setup Instructions ......................................... 7
         Overview of Options                                                  8
         /1, /2, /3, /4, /5 - Alternate Configurations ...................... 8
         /A - Location Option                                                 8
         /B - Tiling Option ................................................. 9
         /C - Pen Color Option                                                9
         /D - Output Destination Option .....................................10
         /F - Output Format Option                                           11
         /I - Scaling Point Location Option ................................ 13
         /J, /K - Printer Code Prefix, Suffix Options                        13
         /L - Page Layout Option ........................................... 14
         /M - Magnification Option (Scale, Size)                             15
         /O - Origin and Orientation Option ................................ 15
         /P - Intercept Mask Option                                          15
         /Q - Number of Copies Option ...................................... 16
         /R - Internal Resolution Option                                     16
         /S - Pen Shading Option ........................................... 16
         /T - Temporary File Option                                          16
         /W - Pen Width Option ............................................. 17
         /X - Control Option                                                 17
         /Y - D/Y and S/E Settings, ADI Handler Option ..................... 18
         /Z - Chord Angle and Enhanced Font Option                           18
         Large Paper ....................................................... 19
         Color Processing                                                    20
         DESQview and Windows .............................................. 20
         Answers                                                             21
         Useful Prefix and Suffix Codes .................................... 22
         Output Devices                                                      23
         Compatibility and Technical Information ........................... 28
         User Support                                                        28


                                                                            p-2
         Introduction ---------------------------------------------------------

           PrintCAD is a pen plotter emulator that acts as a printer driver for
           most IBM/DOS based CAD packages. It lets you print drawings directly
           from CAD programs, via the CAD program's pen plotter driver - either
           AutoCAD's ADI plotter driver or an HP-GL driver.

           PrintCAD  works  with  AutoCAD,  AutoSketch,  Microstation,  Cadkey,
           Generic CADD, Draft Choice, PC-Draft-CAD, and other CAD programs. It
           will  print on Epson  and IBM 9 pin  printers,  Epson, Fujitsu, IBM,
           NEC, and Toshiba  24 pin printers, HP LaserJet,  DeskJet,  PaintJet,
           QuietJet,  HP-GL/2  devices, and HP-GL plotters, Canon  LBP, BJ, and
           BJC printers, HI JetPro  printers,  IBM  LaserPrinter, ExecJet,  and
           Quietwriter  2  and  3,  Kodak  Color  4, PDP  ProTracer,  Tektronix
           ColorQuick, and PostScript printers, and it will generate PCX files.

           PrintCAD  prints  faster than  many native  CAD printer  drivers and
           provides  additional  flexibility, such as pen  width,  shading, and
           color   (with  color   mixing),   and   paper   size,   orientation,
           magnification, and  positioning.  PrintCAD  uses  the  best graphics
           modes available for each printer that it supports.

           PrintCAD  is a swapping resident program that uses 5K of base memory
           and  400K of EMS or XMS memory.  Either 400K of EMS or XMS memory is
           required.  EMS and  XMS are expanded and extended  memory management
           protocols that are typically set  up with memory management software
           such as HIMEM/EMM386, QEMM386, or  386MAX.  If you have  a  computer
           with extended  or expanded memory hardware, you need to install such
           a driver to use it as EMS or XMS memory.

           For  use with DOS extender based  programs such as  AutoCAD  386 and
           Microstation  4, a VCPI handler  needs to be present.  VCPI handlers
           are built into MS-DOS  5's  EMM386.EXE and  recent  versions of QEMM
           386, 386MAX, and other 386 memory managers.  If PrintCAD notes "VCPI
           not  present"  then you  need  to  upgrade  your  memory  management
           software.

           PrintCAD  has  been tested in  a variety of  environments.  However,
           because it  is a  swapping resident program, unusual  situations may
           cause  it to crash the system.  Please  test  it  thoroughly on your
           system before using it with unsaved data.  PrintCAD  will  generally
           work  with multitasking  systems  such as DESQview and  Windows, but
           this is not guaranteed. See DESQview and Windows for information.

           This program is produced by a member of the Association of Shareware
           Professionals (ASP).  ASP wants to  make  sure  that  the  shareware
           principle  works   for  you.   If  you   are  unable  to  resolve  a
           shareware-related  problem  with  an ASP  member  by  contacting the
           member directly, ASP may be able to help. The ASP Ombudsman can help
           you resolve a  dispute or problem  with an  ASP member, but does not
           provide technical support for members' products. Please write to the
           ASP  Ombudsman at  545  Grover Road,  Muskegon, MI 49442  or send  a
           CompuServe message via CompuServe Mail to ASP Ombudsman 70007,3536. 


                                                                            p-3
         License and Registration ---------------------------------------------

           PrintCAD is  provided  as is.  There are  no warranties expressed or
           implied.  PrintCAD  is  a  swapping resident  program that may  have
           problems with unusual environments.

           PrintCAD  is  copyrighted  by  Ravitz Software  Inc.  You  may  copy
           PrintCAD only for use under this license agreement.

           PrintCAD  is distributed as shareware.  You may use PrintCAD without
           charge on a trial basis to determine its suitability for you. If you
           continue to  use  it  after  your  evaluation,  you must  purchase a
           registered copy for $49.  This registration  covers use  by a single
           person (on multiple computers) or installation on  a single computer
           (may be used by a group of people).  There is no cost to use a later
           1.** version after registering any 1.** version.

           You may distribute PrintCAD as a stand alone product if you keep the
           entire   package  together,  unchanged,   including   this   license
           explanation, and do not charge more than $10. You may not distribute
           PrintCAD as part of another product.

           To purchase a registered copy of PrintCAD, send your name,  address,
           and $49 check to:

             Ravitz Software Inc.
             P.O. Box 25068
             Lexington, KY  40524-5068
             USA

           You will  be sent  a  printed manual  and  disk (always  the  latest
           version).  Please specify 3.5  or 5.25 inch disk.  If you previously
           registered  PrintCAD,  you may send $15 to  get a current  disk  and
           manual.

           The price for multiple licenses is $49 for the first copy (with disk
           and  manual) and thereafter $40 per copy with disk and manual or $25
           per copy without disk or manual.

           For users outside the USA, please make checks payable in US dollars,
           and except  for  Canada,  please  use  a  check  from  a US bank  if
           possible. Don't forget to include your country in your address.

           If you register through a business, be sure to include your name.

         What Is New ----------------------------------------------------------

           V 1.30 - Version number matches PrintGL. Supports Canon BJC880,
                    Canon LBP 8 Mk4, Canon BJC800 native mode, IBM 4029
                    LaserPrinter 600 dpi PPDS upgrade. PrintCAD can take binary
                    ADI data. The PCADDV function is built in to PCAD.EXE.

           V 1.18 - Supports HP DeskJet 500C, PaintJet XL 300, LaserJet 4. /XN
                    inhibits swapping for improved compatibility with DOS
                    extender based programs.                                   


                                                                            p-4
         Operation ------------------------------------------------------------

           PrintCAD is a resident program that intercepts plot data output from
           CAD software, processes the data, and prints the resulting  picture.
           When PrintCAD is first run it installs itself.  Subsequent runs look
           for the resident copy  and  send control information to it, updating
           the parameters.

           PrintCAD must  be installed before running the CAD software.  Do not
           install it from a DOS shell.  PrintCAD automatically loads high if a
           5K DOS or XMS upper memory block is available.  Do not use LOADHI or
           LOADHIGH.

           PrintCAD can only function as  a  plotter - it cannot  function as a
           ADI printer/plotter or as a rendering driver.

           PrintCAD  can intercept data from two  sources, DOS file  writes and
           AutoCAD/Sketch  ADI 4.0  interrupts.  With  the  option  /PADI,  ADI
           interrupts  are intercepted.  With /Pmask, for example  /P*.PLT, DOS
           file writes are intercepted.

           PrintCAD can interpret two  kinds of data, HP-GL  and AutoCAD/Sketch
           ADI  4.0 binary plotter data.  HP-GL data is always interpreted.  If
           you use /PADI or /YA then ADI plotter data is also interpreted.

           To use PrintCAD as an HP-GL interpreter, use /Pmask to tell it  what
           files to intercept.  Use /P*.PLT, /P*.DPF, /P*.HPG, /P*.000, etc. to
           match the names that the CAD software uses when writing HP-GL files.
           Configure the  CAD software for HP-GL (HP 7550 or  7585) output to a
           file.  Then plot (do  NOT print).  PrintCAD  intercepts the data and
           prints it.

           To  use PrintCAD with AutoCAD  or AutoSketch as an  ADI  interpreter
           that intercepts ADI binary files use /P*.PLT.  Configure AutoCAD for
           an  ADI 4.0 plotter, binary data output to a file, up to forty pens,
           1016 steps/inch, and six non-solid line types. Then plot.

           To use PrintCAD  with AutoCAD or  AutoSketch as an installed ADI 4.0
           plotter  driver  use  /PADI.  After  installing  PrintCAD  configure
           AutoCAD for an ADI 4.0 plotter, installed at interrupt hex 78, up to
           forty  pens,  1016 steps/inch, and  six non-solid  line types.  Then
           plot.

           After making PrintCAD resident, you can verfiy the installation with
           "pcad /xq". You can verify that it is functional by copying an HP-GL
           (or  ADI  if you  use /YA)  file to  "pcad.plt"  with  the  DOS COPY
           command.

           For COLOR output, the CAD package should be configured for a plotter
           with multiple pens, the CAD package's pen assignment table should be
           set up match screen colors to pen numbers, and PrintCAD's  /C option
           should set up to match.

           PrintCAD  causes a  high/low beep  the  first time that data is sent
           after a file open. If you turn on sound (/XS), it causes a high beep
           after swapping in its code and a low beep before swapping it out, to
           let you monitor its processing.                                     


                                                                            p-5
           When PrintCAD  is  running,  Esc stops processing at  the next  good
           stopping point.  Ctrl-B stops processing immediately and will likely
           leave the printer in need of a reset.

           Internally PrintCAD uses two  byte coordinates  on a 1016  dots/inch
           grid. This allows for plots with coordinates of over 30 inches - far
           larger  than  an HP  7475  can handle.  However, if  you  are  using
           PrintCAD to emulate  a large plotter, you may  overflow the internal
           coordinate system.  This condition is not checked, and it will cause
           garbage output.  You can change the  internal resolution to 508 dots
           per  inch (giving  60 inch maximum  plot sizes) with the  /R  option
           (/R508).  This only helps  store the original  plot internally.  The
           next  step in PrintCAD converts these  coordinates  to the requested
           size in the resolution  of the output device,  and these coordinates
           must also fit in the two byte coordinate list.

         Installation ---------------------------------------------------------

           Copy the file PCAD.EXE to your  working  disk or directory.  This is
           the PrintCAD  executable  file  and  is  all  that you  need  to run
           PrintCAD.

           In addition  to PCAD.EXE, these  files are included in  the package,
           and must be included if you distribute PrintCAD as shareware:

             PCAD.DOC   documentation
             ADD.DOC    additional documentation since last release
             ORDER.FRM  order form
             README.*   quick information                                      


                                                                            p-6
         Syntax ---------------------------------------------------------------

           The calling syntax of PrintCAD is:

             PCAD /option1 /option2 ...

           Spaces between parameters are not required.

           Except for the /X and  /P options, if a given option is entered more
           than once, only the last entry is used.  And if an option is invalid
           (but not incorrect), it is ignored. Only one /X and one /P option is
           allowed.

           If you do  not enter any  parameters, PrintCAD  displays  its option
           reminder screen.

           The DOS environment variable PRINTCAD is examined by PrintCAD and if
           it is nonblank  then  it  is  put  in  front  of  the  command  line
           parameters.  When you  need to exceed the 127  character DOS command
           line limit, put some of the parameters in the PRINTCAD variable, for
           example

             SET PRINTCAD=/CRGB... /S... /W...
             PCAD /P*.PLT ...

           Below, [  and ] enclose optional suboptions and | separates mutually
           exclusive suboptions. The options and suboptions may be in any order
           except  that  multiple  numeric suboptions are  ordered  and numeric
           suboptions must follow character suboptions where the characters may
           be digits.  "c"  refers to  a suboption character,  "x" and  "y"  to
           suboption  numbers,  "i"  and "j" to suboption  integers, "b"  to  a
           suboption byte, and "f" to a DOS file or device name.

           For numbers (x, y), a decimal point  is allowed but is not required,
           and scientific notation is not allowed.  "-" is allowed but not "+".
           For  integer  input (i, j),  only  base ten  integers from -32768 to
           32767 are allowed. "+" is not allowed. A byte (b) must be a base ten
           integer from 0 to  255 or a hexadecimal  number prefixed with $ from
           $00 to $FF.  Further range checking is done for most options to flag
           unreasonable input.  If an option  has multiple  numeric suboptions,
           these may be separated with commas or blanks.

           * It  is  very  important  to  choose  the right  output  format (/F
           * option).  It is likely that the default output format will work on
           * your  printer,  but it is equally likely that it will  not produce
           * optimal results.  Please  look carefully  at  the  entire list  of
           * output formats before choosing one, and do not assume that because
           * a format works that it is the best one to use.                    


                                                                            p-7
         Example Setup Instructions -------------------------------------------

           Below are instructions for  simple setups to  help  you get started.
           After you have PrintCAD running, there  are many additional  options
           that might be useful.

           To  use  AutoCAD (or AutoSketch)  with  an HP DeskJet  500C or 550C,
           install PrintCAD with  "pcad /padi  /fa!  /l7.9,10,0,.3  /crygcbmk".
           Configure  AutoCAD  for  an  ADI  4.0  vector  plotter  installed on
           interrupt 78h,  7  pens,  1016  steps/inch,  plot  area  10x7.9,  no
           calibration.  Set up  the AutoCAD pen  assignment table so  that the
           seven pens are assigned red, yellow, green, cyan, blue, magenta, and
           black. Set skip perforation off on the printer by setting DIP switch
           1-8 up. Then plot.

           To  use a Canon BJC800 or 820 with 11x17 paper with AutoCAD, install
           PrintCAD  with  "pcad  /p*.plt  /ya   /f&  /l10.5,16,0,0  /crygcbmk.
           Configure  AutoCAD for an ADI 4.0  vector plotter with binary output
           to  a   file,  7  pens,  1016  steps/inch,  plot  area  16x10.5,  no
           calibration.  Set up  the AutoCAD pen  assignment  table so that the
           seven pens are assigned red, yellow, green, cyan, blue, magenta, and
           black. Then plot.

           To  use  a Canon BJ330 with cut sheet  paper  with  AutoCAD, install
           PrintCAD with:

             pcad /ppcad#.plt/f7 1,1.01 /l8,10,0,.4 /j27,67,0,11
             pcad /2/f7 1,1.01 /l10.5,16,0,.4 /j27,67,0,17
             pcad /3/f7 1,1.01 /l13.5,21,0,.4 /j27,67,0,22

           Configure AutoCAD for an HP  7585 plotter with output to a file.  To
           print on 8.5x11 paper set the plot area to 10x8 and output  the plot
           to file PCAD1.  For 11x17  paper set  the  plot area to 16x10.5  and
           output to  PCAD2.  For 17x22  paper set the plot area to 21x13.5 and
           output to PCAD3.

           To  use the BJ330 with another CAD package, replace the  ".plt" with
           the  default  plotfile  extension  for  that  package.  AutoCAD  and
           AutoSketch  use  ".plt",  Microstation  uses  ".000",  GenCADD  uses
           ".dpf",  and EasyCAD  and  FastCAD uses  ".hpg".  DesignCAD  has  no
           default  extension - use ".plt" and enter  the entire file name when
           plotting (PCAD1.PLT for example).

           To  use a  LaserJet with Microstation,  install PrintCAD with  "pcad
           /p*.000  /fl /l7.9,10,0,.1".  Configure Microstation for an  HP 7585
           plotter, set  the plot  area to 10x7.9, and  plot.  Instead of  /fl,
           choose the best LaserJet driver from this list:

             /FL  any LJ
             /FL! any LJ2 and any LJ3 with less than 1.5 Meg
             /FI  any LJ3 with 1.5 Meg or more and the LJ4L
             /FI+ any 600 dpi LJ4

           For   manual  feed  legal  paper  use  "/p*.000  /fl   /l7.9,13,0,.1
           /J27,38,108,50,72,27,38,108,51,65" and set the plot area to 13x7.9. 


                                                                            p-8
         Overview of Options --------------------------------------------------

           PrintCAD's options fall into several categories.  The first is input
           and output  choices.  The input option  (/Pmask) lets you  choose an
           intercept filename mask, or you may select ADI interrupt 78 by using
           "adi". The output options are /F, the output format (printer model),
           and /D, the destination port, device, or file.

           The  second  category is the page layout.  /L controls  the size and
           location  of the print window (hard  clip limits) and the option  to
           box  the  window, not send a form feed, and reverse the image color.
           Tiling is set with /B and copies with /Q.

           The third category defines  how the  plot  looks  within  the  print
           window.  /M,  the  magnification,  sets  the size  of  the plot.  /A
           determines the location of the plot within the print window. /O sets
           the  origin  and  orientation, and  is used to rotate or  mirror the
           plot. /I sets the plotter's initial scaling points.

           The  fourth category defines the pens, /W for the width,  /C for the
           color, and /S for the shade.

           The fifth category determines how PrintCAD processes the plot.  This
           includes the temporary file  /T, the default and minimum chord angle
           /Z, the plotter Y/D and S/E switch position and ADI handling /Y, the
           internal  resolution /R, and prefix and suffix printer  codes /J and
           /K.

           The  last category is PrintCAD setup, /P sets the intercept mask, /X
           sets  up  the initial configuration, /1,  /2, /3, /4, and /5 set  up
           multiple configurations.

         /1, /2, /3, /4, /5 - Alternate Configurations ------------------------

           These options select up to 5 alternate configurations, labeled 1..5.
           /1 is  the  default.  The configuration used  for printing is chosen
           based on the file name and mask (/P option).

         /A - Location Option -------------------------------------------------

           /A[O][x,y] - location - default /A

           The A option determines the location of the plot in the print window
           via a point on  the plot that is  aligned with a point in  the print
           window.  You can specify the plot alignment point with x,y in inches
           from the  plot's origin (before  PrintCAD applies magnification), or
           let  it default to  the plot center.  For the print window alignment
           point, you can default to the center or specify the origin with O.

           /A      puts the center of the plot at the print window center
           /AO0,0  puts the plot 0,0 at the print window origin
           /A0,0   puts the plot 0,0 at the print window center                


                                                                            p-9
         /B - Tiling Option ---------------------------------------------------

           /B[i,j,x] - tiling parameters - default /B1,1,0

           /B  lets  you  specify tiling options that break a  large  plot into
           pages. Each page is defined by the page layout option (/L).  I and j
           specify  the number of tiles (pages) horizontally and vertically.  X
           specifies the overlap in inches.

           /B2,2,.5  breaks the plot into 4 pages with .5 inch overlap
           /B        is the same as /B1,1,0 and produces no tiling

         /C - Pen Color Option ------------------------------------------------

           /C[O|T]c.. - color - default /CK

           /C specifies the color of each pen. The colors are B for blue, C for
           cyan,  G for green, K for black,  M  for magenta,  R  for red, W for
           white, and Y  for  yellow.  Unspecified  pens use the  last selected
           color  (/CRGB  is the same as /CRGBBBBBB).  For  black/white  output
           formats, all nonwhite colors become black.

           Additional colors can be created with shade mixing. These colors use
           shading patterns  to  mix the eight  pure colors.  The  format for a
           mixed color is  .??  where  each ?  represents any of the eight pure
           colors.  The  first  color is printed with the pen's shading pattern
           (/S  option)  and the  second is printed  with the  inverse  shading
           pattern.  If the shade  value is 0 (solid) it is replaced by 2 (50%)
           which produces the most  uniform  mixed  colors.  On many  printers,
           using a shade of 1 (75%) or 3 (25%) gives a better color.  Here  are
           some useful mixed colors for inkjet printers. Use them with shade 1.

             color  description     color  description
             .cb    light blue      .yr    orange
             .mb    violet          .rk    brown
             .cg    blue-green      .ck    teal
             .yg    yellow-green    .kr    black on DeskJet 500C

           Mixed colors need line  widths  of at least  2 (4  for 2 dot shading
           patterns) to look good, and they may have  visual artifacts on edges
           near a 45 degree angle.  Multipass dot matrix formats may not handle
           color mixing well.

           By default, colors are  overwritten into the print,  so they  appear
           opaque.  You can  switch to translucent colors (ored into the print)
           with the  T suboption, and then back to opaque with the O suboption.
           Make  this  mode switch in front of the pen that you want to change.
           For PostScript devices and plotters, the color processing is done by
           the device, not PrintCAD.  PostScript  devices  use opaque lines and
           plotters use translucent lines.

           " means repeat the previous color.

           /COKR.MB""T.KY  sets pen 1     to opaque black
                                pen 2     to opaque red
                                pen 3..5  to opaque magenta on blue
                                pen 6..40 to translucent black on yellow       


                                                                           p-10
         /D - Output Destination Option ---------------------------------------

           /D[+]f - destination - default /D1

           The D option specifies the output printer port, device, or file. The
           + suboption causes files to  be appended rather than overwritten (it
           has no effect on device output). 1, 2, and 3 select the BIOS printer
           routines.  X1, X2, X3, and X4 select xon/xoff controlled serial port
           drive.  H1,  H2,  H3, and H4 select hardware controlled serial  port
           drive. You can also use the DOS devices LPT1, COM1, etc.

           PrintCAD cannot set up the serial ports. This is usually done in the
           AUTOEXEC.BAT with MODE (probably MODE COM1:9600,N,8,1,P).

           If you  specify a three digit number  for a file name extension (for
           example .000), and multiple pages are output via the multiple copies
           option or tiling, then rather than  appending the destination  file,
           additional files  are  created  with sequential extensions.  This is
           useful for PCX output.

           /D2          sends output to the second parallel port via BIOS
           /DLPT3       sends output to the DOS device LPT3
           /D+TEMP.PRN  appends output to file TEMP.PRN
           /DOUTPUT.000 sends output to OUTPUT.000, OUTPUT.001, ...            


                                                                           p-11
         /F - Output Format Option --------------------------------------------

           /Fc[-|+|*][!|­][~][`][x,y] - output format - default /FN~

           The F option specifies the output format. -, +, and * are resolution
           modifiers,  !  and  ­  select compression levels, ~ turns off  color
           processing, and ` switches four  plane color  processing on  or off.
           These suboptions are allowed even if they have no effect.

           For HP-GL (/F8),  HP-GL/2 (/F0), PostScript (/FS), and PCX (/FZ) you
           can append  the  nominal  device  resolution.  Matching the  nominal
           resolution to  the printer  may yield improvements in print quality.
           For PCX the nominal device resolution may be one or two numbers.

           For  output  formats  other  than  PCX,  you  can  append  the  true
           horizontal  and   vertical  resolution  of  the  output   device  in
           dots/inch.  This overrides the normal  output device resolution, but
           does not affect  the structure of the output.  These numbers  should
           follow all other suboptions. This lets you compensate for print size
           error. For example, a 360x360 dpi printer consistently under indexes
           so that a 6 inch high box comes  out  5.94 inches.  Using  360,363.6
           (6/5.94*360  = 363.6) removes the error.  For print size correction,
           you  also specify a number from .5 to 2 which is interpreted as  the
           nominal  resolution  times  this number.  For  example on  a 360 dpi
           printer, 1.0,1.01 is the same as 360,363.6.

           Each printer driver has a default level of  data compression, chosen
           to give maximum compatilibity among the different  printers that the
           driver supports.  Many  drivers have  an optional enhanced  level of
           compression, chosen with  !.  This  will be incompatible  with  some
           printers.  And  some drivers let you turn all compression off with ­
           (ASCII 173).  This is rarely of any use.  Where these suboptions are
           effective, they are marked in the table below.

           Drivers  marked below with  ~  can handle color.  Using ~ suppresses
           color processing, substituting black for all colors except white.  `
           switches between 4 and 3 plane color (see Color Processing).

           /F0[i]       ~ HP-GL/2 ................................ 600x600, ixi
           /F1          ~ IBM 9 pin                                      120x72
           /F1+         ~ IBM 9 pin (2 pass) .......................... 120x144
           /F1*         ~ IBM 9 pin (4 pass)                            240x144
           /F2            IBM Quietwriter 2 ........................... 240x240
           /F3            IBM Quietwriter 3                             240x240
           /F4-       !­  IBM LaserPrinter (PPDS mode) ................ 150x150
           /F4        !­  IBM LaserPrinter (PPDS mode)                  300x300
           /F4+       !­  IBM LaserPrinter (PPDS mode) ................ 600x600
           /F5        ! ~ IBM 24 pin alternate 1                        180x180
           /F5+       ! ~ IBM 24 pin alternate 1 (2 pass) ............. 360x180
           /F5*       ! ~ IBM 24 pin alternate 1 (4 pass)               360x360
           /F6        !   IBM Proprinter X24 .......................... 180x182
           /F6+       !   IBM Proprinter X24 (2 pass)                   360x182
           /F6*       !   IBM Proprinter X24 (4 pass) ................. 360x364


                                                                           p-12
           /F7         ­  Canon BJ IBM mode, IBM ExecJet .............. 360x360
           /F7+        ­  Canon BJ IBM mode, IBM ExecJet (2 pass)       360x360
           /F8[i]         HP-GL ................................ 1016x1016, ixi
           /F9        ! ~ NEC 24 pin                                    180x180
           /F9+       ! ~ NEC 24 pin (2 pass) ......................... 360x180
           /F9*       ! ~ NEC 24 pin (4 pass)                           360x360
           /F&          ~ Canon BJ/BJC native mode .................... 360x360
           /F@          ~ Canon BJC CaPSL mode                          360x360
           /FA-       ! ~ HP DeskJet 500C, Mannesmann Tally MT92C ..... 150x150
           /FA        ! ~ HP DeskJet 500C, Mannesmann Tally MT92C       300x300
           /FB         ­~ Canon BJ/BJC Epson mode ..................... 360x360
           /FB+        ­~ Canon BJ/BJC Epson mode (line overlap)        360x360
           /FD-       !­  Canon LBP (ISO/CaPSL mode) .................. 150x150
           /FD        !­  Canon LBP (ISO/CaPSL mode)                    300x300
           /FD+       !­  Canon LBP (ISO/CaPSL mode)................... 600x600
           /FF        ! ~ Fujitsu 24 pin                                180x180
           /FF+       ! ~ Fujitsu 24 pin (2 pass) ..................... 360x180
           /FF*       ! ~ Fujitsu 24 pin (4 pass)                       360x360
           /FG         ­  PDP Protracer (IBM mode) .................... 360x360
           /FI-           HP LaserJet 3, DeskJet                        150x150
           /FI            HP LaserJet 3, DeskJet ...................... 300x300
           /FI+           HP LaserJet 4                                 600x600
           /FJ            Canon BJ BJ130 mode ......................... 360x360
           /FK          ~ Kodak Diconix Color 4                         192x192
           /FL-       !­  HP LaserJet ................................. 150x150
           /FL        !­  HP LaserJet                                   300x300
           /FN          ~ Epson 9 pin .................................. 120x72
           /FN+         ~ Epson 9 pin (3 pass)                          120x216
           /FN*         ~ Epson 9 pin (6 pass) ........................ 240x216
           /FO        ! ~ Toshiba 24 pin                                180x180
           /FO+       ! ~ Toshiba 24 pin (2 pass) ..................... 360x180
           /FO*       ! ~ Toshiba 24 pin (4 pass)                       360x360
           /FP        ! ~ HP PaintJet ................................. 180x180
           /FQ            HP QuietJet (PCL mode)                        192x192
           /FR          ~ Tektronix ColorQuick ........................ 216x216
           /FS[i]       ~ PostScript                               600x600, ixi
           /FT        ! ~ Epson 24 pin ................................ 180x180
           /FT+       ! ~ Epson 24 pin (2 pass)                         360x180
           /FT*       ! ~ Epson 24 pin (4 pass) ....................... 360x360
           /FW          ~ Epson 9 pin alternate                          120x72
           /FW+         ~ Epson 9 pin alternate (3 pass) .............. 120x216
           /FW*         ~ Epson 9 pin alternate (6 pass)                240x216
           /FX        ! ~ IBM 24 pin alternate 2 ...................... 180x180
           /FX+       ! ~ IBM 24 pin alternate 2 (2 pass)               360x180
           /FX*       ! ~ IBM 24 pin alternate 2 (4 pass) ............. 360x360
           /FZ[i[,j]]   ~ ZSoft PCX                           100x100, ixi, ixj


                                                                           p-13
         /I - Scaling Point Location Option -----------------------------------

           /IA|R|W[N] - IP point location - default /IA

           This  option is not useful with AutoCAD or any software that outputs
           HP-GL that  does not use  scaling commands  or that initializes  the
           plotter or sets the scaling points.

           The  I option  sets the initial scaling points (P1, P2 - the scaling
           points  may  be set  in  the HP-GL  file  with  the IP  command).  A
           (absolute) sets the points  to the default  for  the paper size (see
           below).  R fits P1 and P2 to the print window with at least .25 inch
           margins  and an x/y ratio of 10/7.2 (the same ratio as  the HP  7475
           with small paper).  W fits P1 and P2  to the print window with a .25
           inch margin. N makes the margin 0 for R or W and is ignored with A.

           The  default scaling points depend on the print window  (/L  option)
           with the implied paper size and the plot orientation (/O option).

           paper    options            default scaling pts  with RO90 command
           7440 A   /O1 /L 7.54,10.14  250,279 10250, 7479  279,250  7479,10250
           7440 A4  /O1 /L 7.54,10.74  250,279 10250, 7479  279,250  7479,10250
           7475 A4  /O1 /L 7.84,10.20  250,596 10250, 7796  154,244  7354,10244
           7475 A4  /O1 /L 7.60,10.88  603,521 10603, 7721    0,610  7200,10610
           7475 B   /O1 /L10.20,16.38  522,259 15722,10259  283,934 10283,16134
           7475 A3  /O1 /L10.88,15.90  170,602 15370,10602  607,797 10607,15997
           7440 A   /O2 /L10.14, 7.54  250,279 10250, 7479  279,250  7479,10250
           7440 A4  /O2 /L10.74, 7.54  250,279 10250, 7479  279,250  7479,10250
           7475 A   /O2 /L10.20, 7.84  250,596 10250, 7796  154,244  7354,10244
           7475 A4  /O2 /L10.88, 7.60  603,521 10603, 7721    0,610  7200,10610
           7475 B   /O2 /L16.38,10.20  522,259 15722,10259  283,934 10283,16134
           7475 A3  /O2 /L15.90,10.88  170,602 15370,10602  607,797 10607,15997

           anything else               250,279 10250, 7479  279,250  7479,10250

           /O3 and /O4 gives the same default scaling points as /O1 and /O2.

           /IA   uses the default scaling points
           /IWN  sets the scaling points to fit the print window

         /J, /K - Printer Code Prefix, Suffix Options -------------------------

           /J[b,b,..] - printer code prefix - default /J
           /K[b,b,..] - printer code suffix - default /K

           /J lets you send codes to the  printer before  PrintCAD's usual data
           is  sent and /K lets you send codes  after PrintCAD's usual data  is
           sent.  This lets  you  set  up  and reset the  printer  for  special
           situations. For PostScript and HP-GL output, the /J codes follow the
           initialization commands.

           The  codes  are  specified  with  byte  values  (0..255 or  $0..$FF)
           separated by blanks or commas. There is a limit of 80 characters for
           any option, so long sequences must be handled outside of PrintCAD.

           /J27 79   sets skip perforation off  to allow plots  larger than one
                     page on most continuous form printers                     


                                                                           p-14
         /L - Page Layout Option ----------------------------------------------

           /L[B][F|N][R][x,y[,x,y]] - page layout - default depends on printer

           The L option defines the page layout.

           B boxes the plot at the print window edge using pen 40.

           F (the default) and N turn form  feed on  or off.  These are ignored
           for bit maps and display output.

           R  reverses the  colors on displays, bit maps, and output formats 4,
           D, I, and L  (Canon,  HP, and IBM  page  printers) and is  otherwise
           ignored. This gives the equivalent of a photographic negative.

           The first optional x and y are the print window width  and height in
           inches.  These define  the hard  clip  limits.  These values are not
           checked against the printer's capabilities.  If you specify  a print
           window  that  exceeds  the  output  device limits, the  results  are
           unknown.  You may need to reset the printer's margins or page length
           for large plots (see Large Paper). The size needed for a given width
           and height exceeds x and y by 8 dots to allow for line widths.

           The  second  optional x and y are the left and top margins, measured
           from the printer's  left margin and current vertical position to the
           print window. The margins for HP-GL and PostScript are measured from
           0,0 (left, bottom).  Margins are ignored for display output  and bit
           maps.

           THE PRINT WINDOW PLUS THE MARGINS MUST FIT WITHIN THE PRINTABLE AREA
           OF  THE PRINTER.  To find the largest printable area turn on the box
           and form feed  options  and set a  window and margins of 7.5,10,0,0.
           Any plotfile will do - the  only  concern  is the box.  Increase the
           window until you have the largest  box that fits on the paper.  This
           is the best that you can do. To improve centering you can reduce the
           print window and increase the corresponding margin.

           The default print window is 7.54x10.14 for printers and bit maps and
           10.14x7.54 for HP-GL and displays, corresponding to HP 7440 A paper.
           The  default  margins are printer  specific to compensate for  paper
           handling.

           /L7.5,3,.5,0   print window 7.5x3, left margin .5, top margin 0
           /L7.54,10.14   sets window equivalent to HP 7440 with A  paper
           /L7.54,10.74   sets window equivalent to HP 7440 with A4 paper
           /L7.84,10.20   sets window equivalent to HP 7475 with A  paper
           /L7.60,10.88   sets window equivalent to HP 7475 with A4 paper
           /L10.20,16.38  sets window equivalent to HP 7475 with B  paper
           /L10.88,15.90  sets window equivalent to HP 7475 with A3 paper      


                                                                           p-15
         /M - Magnification Option (Scale, Size) ------------------------------

           /M[F]x - magnification - default /M1

           The M option  sets the magnification.  F fits  the plot to the print
           window.  The default, /M1, prints at the same size as an HP 7440.

           /MF.9  prints at 90% the largest size that fits in the print window
           /M1    plots at the same size as an HP 7475

         /O - Origin and Orientation Option -----------------------------------

           /O[1|2|3|4[L]] - origin, orientation - default /O

           The O  option  sets  the print  window origin  and orientation.  The
           origin  is  one of four corners numbered 1..4  for upper left, lower
           left, lower right, and upper right, and implies a plot rotation. The
           L suboption specifies a left handed coordinate system, which mirrors
           the plot.  If no origin is specified then it is chosen so that the x
           axis is the longer dimension.

           Here are pictures of PrintCAD's view of the output media compared to
           an HP 7475's view. O marks the default origin.

           HP 7475                               PrintCAD
           A size           B size               printer        plotter

             yÚÄÄÄÄÄÄÄÄ¿    0,0ÚÄÄÄÄÄÄÄÄ¿y       ul oÄÄÄÄÄ¿ur   ul ÚÄÄÄÄÄÄÄÄ¿ur
              ³        ³       ³        ³         1 ³     ³4     1 ³        ³4
              ³        ³       ³        ³           ³     ³        ³        ³
           0,0ÀÄÄÄÄÄÄÄÄÙx      ³        ³           ³     ³     ll oÄÄÄÄÄÄÄÄÙlr
                               ³        ³           ³     ³      2           3
                               ³        ³        ll ÀÄÄÄÄÄÙlr
                               ³        ³         2        3
                              xÀÄÄÄÄÄÄÄÄÙ

           /O1  puts the print window's origin in the upper left corner
           /O2  puts the print window's origin in the lower left corner

         /P - Intercept Mask Option -------------------------------------------

           /PADI|mask - intercept mask

           /PADI sets up PrintCAD as an AutoCAD ADI plotter driver. /Pmask lets
           you  choose  a DOS file mask as PrintCAD's intercept mask.  The mask
           should not include disk  or directory information - PrintCAD ignores
           this information when looking at  file names.  The mask may  contain
           the character #.  This is the same as ?, but when a file matches the
           mask   the  character  that  matches  the  #  selects  the  PrintCAD
           configuration - 1..5  selects configurations 1..5  and anything else
           selects configuration 1.

           /Padi        sets up PrintCAD to take data from AutoCAD interrupt 78
           /P*.plt      intercepts data written to *.plt
           /Ppcad#.plt  intercepts data written to pcad1.plt, pcad2.plt, etc.     


                                                                           p-16
         /Q - Number of Copies Option -----------------------------------------

           /Qi - number of copies - default /Q1

           /Q  sets the number of copies of  each printed page.  The default is
           one.  Page printers  produce multiple  copies  faster using  the  "N
           copies" prefix code (see Useful Prefix and Suffix Codes).

         /R - Internal Resolution Option --------------------------------------

           /Ri - internal resolution - default /R1016

           /R sets the internal grid resolution  in dots/inch.  It is  normally
           1016 and rarely needs  to be changed.  To fit very large plots  into
           the   -32768..32767  coordinate  limit,  use   /R762.   Setting  the
           resolution to a multiple  of the output device  resolution times the
           magnification may yield a small improvement in print quality.

         /S - Pen Shading Option ----------------------------------------------

           /Sc.. - pen shading patterns - default /S0

           /S assigns a shading pattern to each pen.  Unspecified pens use  the
           last  specified  shade.  The shade values  are 0..8  and  A..F.  The
           percent coverage for  each shade is list below.  Narrow line  widths
           may not work well with some shade patterns.

             0 100%    1 75%      5 75%   coarse pattern    A 6.2%    D 87.5%
                       2 50%      6 50%   coarse pattern    B 3.1%    E 62.5%
                       3 25%      7 25%   coarse pattern    C 1.6%    F 37.5%
                       4 12.5%    8 12.5% coarse pattern

           Some printers, especially dot matrix printers  in  multipass  modes,
           wash out shading because they have a dot size that is large relative
           to the dot spacing.

           /S024  sets pen 1 to solid, pen 2 to 50%, pen 3..40 to 12.5%

         /T - Temporary File Option -------------------------------------------

           /T[+]f - temporary file - default /TPLOT.TMP

           PrintCAD  uses  a temporary file when it does not have enough memory
           to handle  a plotfile.  You can use /T to put it on a RAM  disk  for
           extra speed.  You can force the use of a temporary file, if the plot
           has over  1024 data points, with +.  If you use a RAM  disk this may
           speed printing.                                                     


                                                                           p-17
         /W - Pen Width Option ------------------------------------------------

           /Wc.. - pen widths - default /WA

           The W option assigns pen line widths. Each width may be 0..9, .10 ..
           .24 dots, A..I for 2..10 units of 4/1016 inch (.1  mm), or N to turn
           off the  pen.  A..I widths are  approximations, based  on the device
           technology. Odd widths of 9 or above are modified to the next higher
           (even) width. Unassigned pens use the last assigned width.

           For nonsquare  matrix printers, PrintCAD  uses pen points  optimized
           for  an  h/v  ratio of .67,  1, or  1.5.  Widths  are figured in the
           direction of higher resolution, and are  not accurate  in  the other
           direction.

           Line widths  of over eight dots are  distorted at  the print  window
           edge to fit within the four dot border.

           /WA      sets pen 1..40 to 0.2 mm
           /WB2.16  sets pen 1 to .3 mm, pen 2 to 2 dots, pens 3..40 to 16 dots

         /X - Control Option --------------------------------------------------

           /XQ - queries PrintCAD installation
           /XR - removes PrintCAD if allowed
           /X[E|N|X][A][M][L][W][P][S][-|+] - controls PrintCAD's setup

           /XQ  checks to see  if  PrintCAD is installed.  /XR removes PrintCAD
           from memory, if allowed. /XQ and /XR disallow all other options.

           The other  suboptions  control setup,  and  are  effective only  for
           initial setup. X specifies XMS for swapping - this is the default. E
           forces the use  of  EMS  for  swapping instead  of  XMS.  N inhibits
           swapping.  This forces the  entire program to load in low memory and
           it will  take a large chunk of  DOS  memory.  In return,  all of the
           compatibility problems of  swapping TSRs  are removed.  This  can be
           very useful with DOS extender based CAD programs.

           A sets  an  alternate  handle  (use  with PC-Draft-CAD,  Drafix, and
           DesignCAD).  M sets an alternate mouse handler. These suboptions may
           improve compatibility.

           L forces PrintCAD to load its resident  part low.  W forces PrintCAD
           to load its swapping work area low.  P causes program prefix segment
           checking.  These  suboptions may  improve compatibility  in  unusual
           situations, but are generally not needed and may make things worse.

           + or  -  increases  or  decreases  the PrintCAD  memory  space,  for
           improved speed or reduced resource usage.

           S adds progress beeps. This is not advised with the N suboption.

           /XM  sets up PrintCAD with its alternate mouse handler              


                                                                           p-18
         /Y - D/Y and S/E Settings, ADI Handler Option ------------------------

           /Y[D|Y][S|E][A] - D/Y and S/E  setting, ADI handler - default /YDS

           The Y option sets the plotter's D/Y  switch to  D  or Y and the  S/E
           switch to S or  E.  Y starts  with the  plotter off and responds  to
           esc.(, esc.Y, esc.), and esc.Z commands.  D  starts with the plotter
           on and ignores these commands. S sets the standard interpretation of
           IW (clipping window) commands.  E sets 7550 enhanced  interpretation
           of IW commands, so that they use scaled coordinates.

           The A  suboption  turns on  PrintCAD's ADI  handler.  In  this  mode
           Autodesk  ADI  4.0  vector plotter binary  commands  are interpreted
           (along with  HP-GL).  The ADI  driver  should  be  set  up  at  1016
           steps/inch with up to forty pens and up to six non-solid line types.
           This is not needed when you specify /PADI.

           /YD  puts the YD switch in the usual D position

         /Z - Chord Angle Option ----------------------------------------------

           /Z[E]i,j - default, min chord angle, enhanced font - default /Z10,5

           This option is  not useful with AutoCAD or any software that outputs
           HP-GL  that draws circles,  arcs, and  text as line segments  rather
           than using HP-GL circle, arc, and label commands.

           The  Z  option  specifies the  default and minimum chord angles  for
           circles and arcs. The HP 7475 defaults to a chord angle of 5 with no
           minimum.  Using chord angles of less than 10  returns  little  print
           quality  improvement  and adds to processing  time.  The default  is
           /Z10,5. For better emulation use /Z5,2.

           The  E suboption  says to use the enhanced font,  which  doubles the
           number of chords on curves in text, improving the  curve smoothness.
           This is only effective on character heights above .5 cm.

           /Z5,2  sets the default chord angle to 5 degrees, the minimum to 2  


                                                                           p-19
         Large Paper ----------------------------------------------------------

           PrintCAD can handle printing on  paper larger than the usual 8.5x11,
           but  this  takes  some  extra  work.  First  you  need  to  increase
           PrintCAD's print window to cover the large paper.  This is done with
           the /L option.  The  print  window plus the  margins  (/L)  must fit
           within the printer's printable area.

           And  then you must make sure that your printer recognizes the larger
           paper  height.  For  continuous forms  paper  this is best  done  by
           setting skip perforation to  off,  either by printer switch or  with
           PrintCAD prefix codes.  For Canon, Epson, Fujitsu, IBM, and NEC line
           printers (dot matrix, ink jet, thermal) use /J27 79.

           For  cut  sheet  paper,  on Canon  (except BJ  native  mode), Epson,
           Fujitsu, IBM, and  NEC line printers use /J27 67 0 n, where n is the
           page length in inches.  For the PDP ProTracer use /J27 67 n, where n
           is the page length in lines, at six lines per inch.

           And for some printers you need to increase the right margin. For the
           Canon BJC  in  Epson  mode  use  /J27 81 114.  For the HI V50/100 in
           printer mode use /J27 91 88 2 0 1 255.

           For page  printers, legal size  paper  may  be specified  with these
           printer code prefixes: HP-PCL  printers  /J27 38 108 51 65  (/K27 38
           108 50 65 to  reset to letter), Canon  LBP  /J27 91  51 50 59 59 112
           (/K27 91 51 48  59 59 112 to reset), IBM LaserPrinter /J27 91 70 5 0
           3 1 2 1 (/J27 91 70 5 0 3 1 1 1 to reset).

           To  get a  10x16 print  window on 11x17 paper with a  Canon,  Epson,
           Fujitsu, IBM, or NEC line printer, use these options: /L10 16 .4 .25
           /J27 67 0 17.  You will probably need to adjust the margins (.4 .25)
           for best centering.

           The  maximum  width  of  the print  window on  most  narrow carriage
           printers is 8  - 8/(horizontal dpi).  For 300 dpi printers,  this is
           7.97.  At 120 dpi it is 7.93.  The maximum width of the print window
           on most wide carriage printers is 13.6 - 8/(horizontal dpi).  At 180
           dpi this is 13.55.  At 360 dpi it is 13.57.  The  horizontal  margin
           should be set to 0 to get this width.                               


                                                                           p-20
         Color Processing -----------------------------------------------------

           Color graphics devices use a variety of color technologies. PrintCAD
           supports these basic types.

           CMY or  cyan/magenta/yellow is used by inkjet printers with no black
           ink. This uses three color planes and give eight pure colors.

           CMYK or  cyan/magenta/yellow/black  is used by inkjet and dot matrix
           printers.  This uses  four color planes  and give eight pure colors.
           Using black ink instead  of  a cyan/magenta/yellow mix gives a  more
           neutral black color.

           RGB or red/green/blue is used by  bit  maps.  This uses  three color
           planes and give eight pure colors.

           RGBI  or red/green/blue/intensity is  used and bit  maps.  This uses
           four color planes. All simple colors except black are intense.  When
           you  specify any color mixed with black at  shade 0, then instead of
           mixing the  colors at  50%, the intensity is turned off.  This gives
           fifteen pure colors.

           CMYK and RGBI are used by default when they are appropriate. You can
           switch to CMY or RGB with  the  ` suboption of /F.  For  dot  matrix
           printers this  may speed  printing  by  reducing  memory  usage  and
           eliminating the use of the black ribbon.

           /FA!  (300  dpi color  HP-PCL) uses  CMY  color  by  default.  /FA!`
           switches to CMYK color to let you  access true  black on the DeskJet
           550C.

         DESQview and Windows -------------------------------------------------

           PrintCAD  can generally be  run  inside  a  window  of  DESQview  or
           Windows. In this case it can be accessed only from that window.

           PrintCAD  can  generally be  run  under (installed  before starting)
           DESQview  or Windows.  In  this  case it  can be accessed  from  any
           window, but while running all other tasks will be stopped.          


                                                                           p-21
         Answers --------------------------------------------------------------

           To access PrintCAD from a CAD package you must PLOT. Do NOT print.

           If you  are getting system crashes or nothing from PrintCAD, try the
           options  /XA, /XM, /XE,  and all  combinations of these (/XAM, /XAE,
           /XME, ...).  Try /XN for DOS extender based software.  Try /XL, /XW,
           and /XLW if none of the above work.

           If  your plot is messed up, with wraparound lines covering the page,
           you have probably  exceeded the PrintCAD  internal coordinate limit.
           This happens when the HP-GL coordinates exceed 32 inches. Reduce the
           internal resolution  with /R762 for  coordinates up to 42  inches or
           /R508 for coordinates up to 64 inches.

           If  you  are  having  trouble getting  the  print  size or  location
           correct, check your  /L  option.  The print window  plus  the  print
           margins  must define an area that fits in the printable area  of the
           paper. Printers cannot print over the entire area of the paper. They
           usually require .25 to .5 inch margins.

           To get color output from PrintCAD, you must:

             Define a multipen plotter in your CAD package.

             Set up the pens in your CAD package so each color is assigned to a
             pen.

             Use the /C option to assign the same colors to PrintCAD's pens.

           Plot spoolers are  not generally compatible with PrintCAD, and would
           be  of little value if they were.  Do  not  bother  with one.  Print
           buffers/caches are generally compatible. You must install the buffer
           first. A print buffer may be very useful.

           If your prints are coming out not quite to scale:

             For ADI plotters,  check  that your  plotter  is  defined  as 1016
             steps/inch.

             Check that no calibration is being done by the CAD package.

             See /F - Output Format Option for print size correction.

           For the Canon BJC-800 in Epson mode, the right margin  defaults to 8
           inches. Use /J27 64 27 81 114 to set it to 11.4 inches.

           For the  Canon BJ-330 and most wide  carriage printers,  the maximum
           print window  width is 13.57  inches.  This is a printer  limitation
           that you cannot get around.

           If your  printer ejects the paper  before the plot is  finished, you
           probably needed to specify a paper length prefix code. For most line
           printers use /J27 67 0 n where n is the page length in inches.      


                                                                           p-22
         Useful Prefix and Suffix Codes ---------------------------------------

           Below,  n  represents any number 0..255, nA represents any number in
           ASCII format (1 becomes 49, 2 becomes 50, 43 becomes 52 51, etc.).

           Canon,      Reset                    27 64
           Epson,      N inch paper             27 67 0 n
           Fujitsu,    17 inch paper            27 67 0 17
           IBM, NEC    Right margin n columns   27 81 n       (not for IBM)
           dot matrix, Skip perforation off     27 79
           inkjet      Unidirectional printing  27 85 1

           HP PCL,     Reset                 27 69
           DeskJet,    Portrait mode         27 38 108 48 79
           LaserJet,   Top margin 0          27 38 108 48 69
           PaintJet    Skip perforation off  27 38 108 48 76
                       11 inch paper         27 38 108 50 65
                       14 inch paper         27 38 108 51 65
                       11x17 inch paper      27 38 108 54 65
                       Manual feed           27 38 108 50 72
                       N copies              27 38 108 nA 88  (page printers)

           HP DJ500C   High quality, slow    27 42 111 49 81
                       No ink depletion      27 42 111 49 68

           HP PJXL300  Low quality, fast     27 42 111 45 49 81

           HP QJ       HP-PCL mode           27 37 65
                       DIP switch mode       27 37 64

           IBM LP      11 inch paper, tray 1, n copies  27 91 70 5 0 3 1 1 n
                       14 inch paper, tray 1, n copies  27 91 70 5 0 3 1 2 n
                       14 inch paper, manual, n copies  27 91 70 5 0 1 1 2 n
                       N copies                         27 91 70 5 0 0 0 0 0 n

           Can BJ nat  Page length, right margin x 10   27 40 103 3 0 n 1 n

           Can CaPSL   Reset                  27 99
                       11 inch paper          27 91 51 48 59 59 112
                       14 inch paper          27 91 51 50 59 59 112
                       Manual feed            27 91 49 113
                       Automatic feed         27 91 48 113
                       Full page memory mode  27 59 27 91 50 38 122
                       N copies               27 91 nA 118
                       Cursor to top of page  27 91 48 100
                       Diablo mode            27 58
                       ISO mode               27 59

           PostScript  N copies      nA 32 88 67
                       Paper tray n  nA 32 88 80

           ProTracer   N line paper  27 67 n

           HI V50/100  Max margins   27,91,88,2,0,1,255                        


                                                                           p-23
         Output Devices -------------------------------------------------------

           Canon BJ and BJC Printers, IBM ExecJet

             PrintCAD has five basic drivers for Canon  BJ and  BJC and the IBM
             ExecJet.  /F7  is the IBM mode driver.  It  works with the BJ130e,
             BJ5,  BJ10/10e/10ex, BJ20, BJ200,  BJ300/330,  and  ExecJet.  /F7+
             gives dark print with line to line overlap.

             /FJ is the BJ130 mode driver.  It works with all Canon BJ printers
             in IBM or native mode. The printer is set to 10 pitch text.

             /FB is  the  Epson  mode  driver.  It  works  with  the BJ200  and
             BJC800/820.  Color is supported.  /FB+ gives sparse  line to  line
             overlap.  For the BJC800/820  the  prefix code 27  81 114 sets the
             print width to 11.4 inches.

             /F&  is the  native mode  driver.  It works  with  the  BJ200  and
             BJC800/820 in any mode. Color is supported.  Epson/IBM mode prefix
             codes are not compatible and are not needed.

             /F@ is the CaPSL mode driver for the BJC880. Color is supported.

             Some  of these printers have  an image density option (DIP  switch
             and/or  front panel switch).  Low density  eliminates every second
             dot. To get the full 360 dpi resolution, use high density.

           Canon LBP Printers

             /FD works with any Canon LBP printer.  If the printer is in Diablo
             mode,  it is switched to ISO mode.  At 300 dpi it  takes up to one
             meg of printer memory to print a full page of graphics.

             The ! suboption switches to CaPSL 4 data compression. /FD+! is the
             best driver for the LBP 8 Mk4 at 600 dpi.

             You might need to set up the printer with /J27 59 27 91 50 38 122.

             To switch back to Diablo mode on completion, use /K27 58.

           Epson, IBM 9 Pin Printers

             /FN, /FW, and /F1 cover a wide range of Epson/IBM compatible 9 pin
             dot matrix printers.  You need a  cyan/magenta/yellow/black ribbon
             to get color prints. The * drivers use 1/240 graphics. /FN+, /FN*,
             /FW+,  and  /FW*  use  1/216  indexing  and  do  three  vertically
             interleaved passes.  /F1+  and /F1* use  1/144 indexing and do two
             vertically interleaved passes. /FW sets line feeds to 1/6 inch.

             For  Epson  printers  and  other  printers  with  1/216   indexing
             hardware,  /FN  is  preferred.   For  some  not  quite  compatible
             printers,  /FW works.  For IBM Proprinters and other printers with
             1/144 indexing hardware, /F1 gives better results.                


                                                                           p-24
           Epson, Fujitsu, NEC, Toshiba 24 Pin Printers

             /FT  covers  all  Epson LQ printers and  many  compatible printers
             (Panasonic in LQ mode and others).  /FF works with  Fujitsu 24 pin
             printers in Fujitsu mode.  /F9 works with NEC 24 pin printers. /FO
             works  with Toshiba 24  pin printers.  /FO  resets the  line  feed
             distance to 1/6 inch on completion.

             For all of  these  drivers, you  need  a cyan/magenta/yellow/black
             ribbon to get color prints. The + and * drivers use 1/360 graphics
             mode,  and  the * drivers use 1/360  (1/120 for /FO*) indexing and
             reset the line  feed distance to 1/6 inch on completion.  A  clean
             paper path with  equal tension on  each side  is  needed  for good
             360x360 graphics.

             Many 24 pin printers are not capable of 360x360 graphics and a few
             cannot handle 360x180 graphics.

             The compression mode drivers  (! suboption)  may or  may not be an
             improvement with these printers.

           Houston Instruments JetPro V50/100

             You can  drive  the  HI V50/100  as an  HP-GL/2  device.  Set  the
             resolution to 360 (/F0  360) and reverse the  width and height  in
             the print window, for example use 10x8 instead of 8x10  for 8.5x11
             paper. The maximum print window height is 15.25.

             In printer mode the HI V50/100 acts as a Canon BJ IBM mode printer
             (/F7).  The  maximum  print width is 15.25 and you need the prefix
             code 27,91,88,2,0,1,255 to get beyond 13.6 inches.

           HP DeskJet, HP PaintJet XL300, Mannesmann Tally MT92C

             /FI works with any black/white DeskJet in portrait mode.

             /FA drives the  DeskJet 500C, PaintJet XL300, MT92C, and any color
             300 dpi HP-PCL printer that supports data transfer mode 2.

             /FA  has three modes and covers different  levels of 300 dpi color
             HP-PCL printers.  /FA uses RGB color  and  works with the  DeskJet
             500C and Mannesmann  Tally MT92C.  /FA!  uses  CMY color which can
             speed printing  in some  cases.  This works with the DeskJet 500C,
             DeskJet 550C, and PaintJet XL300.  /FA!` uses  CMYK  color to give
             give better blacks on the DeskJet 550C.                           


                                                                           p-25
           HP LaserJet

             /FL works with any LaserJet compatible printer. /FL! works with LJ
             2 (PCL 4) printers.  /FI works with LJ 3 (PCL 5) printers. /FI+ is
             a 600 dpi driver for the LaserJet 4.

             All  of these drivers work in portrait mode, which may be set with
             /J 27 38 108 48 79 or you can reset the printer with /J 27 69.

             LaserJets with under one meg of memory may not be able to handle a
             full page of graphics. /FL!  uses less printer memory than /FI, so
             it may be preferred on LaserJet 3s with limited memory.

           HP PaintJet

             /FP drives 180 dpi PaintJet printers.  The compression mode driver
             (/FP!)  uses  data  transfer  mode 2 (instead of 1) and works only
             with a PaintJet XL.

             /FA! (the DeskJet 500C CMY driver) works with the PaintJet XL300.

           HP QuietJet

             /FQ works with QuietJets in HP-PCL mode.

           HP-GL, HP-GL/2, HP and IBM Pen Plotters

             /F8  outputs low level  HP-GL, converting text,  arcs,  fill,  and
             clips to  vectors.  The output  is HP 7220 and HP-GL/2 pen plotter
             compatible, containing  IN,  IP, SC, SP, IW,  LT,  PA, PU,  and PD
             commands.  PG is used for form feeds.  If you specify no form feed
             then multiple plots may be appended to the same page.

             /F0  drives  HP-GL/2  raster  devices.  Use  /F8  for HP-GL/2  pen
             plotters.

             You  can specify the nominal resolution  of  HP-GL  or  HP-GL/2 by
             appending it to the /F option (for example /F8 300).  When you set
             the nominal  resolution of HP-GL to other  than 1016,  enhanced IW
             command interpretation (HP 7550 enhanced mode) is needed to handle
             dashed lines correctly.

             For HP-GL output  the  width parameter  (/W)  is  used  as  a  pen
             selector, so for each pen in the original HP-GL, you can specify a
             new  pen  in  the  output.  The  default  /W  option  for  /F8  is
             /W12345678. Shading and color are ignored.

           IBM LaserPrinter

             /F4 drives any LaserPrinter in PPDS  (native) mode.  /FL will work
             for HP LaserJet mode. At 300 dpi it takes up to one meg of printer
             memory to print a full page of graphics.

             The !  suboption switches  to 4029 data compression.  /F4+!  works
             with the 4029 with 600 dpi PPDS upgrade.                          


                                                                           p-26
           IBM 24 Pin Printers

             PrintCAD has three drivers for Proprinter X24 compatible printers.
             Use  native mode, not AGM.  /F6 is for all IBM X24s  and the  24P.
             These printers do  1/144 inch indexing and using them  at  180 dpi
             gives horizontal white  streaks every  2/3 inch.  The  /F6 drivers
             compensate  for this by indexing 19/144 per line, giving  182 dpi.
             To work  properly the printer  must start on a 1/72 boundary so it
             is best to keep line feeds at a multiple of 1/72 (1/6, 1/8, 1/9).

             /F5 is referred to as X24 alternate 1 and is for printers that are
             X24 compatible  except for  1/180 inch indexing.  This is the case
             with  most X24 compatible printers, including the IBM  Quickwriter
             and IBM 2390 and 2391. /F5* works only with printers that do 1/360
             indexing, including the 2390 and 2391 but not the Quickwriter.

             /FX  is referred to  as X24  alternate 2  and is  the same  as /F5
             except for the  vertical units command.  /FX  works with Panasonic
             printers in X24 mode.

             The  compression  mode drivers (!  suboption) may or may not be an
             improvement.

           IBM Quietwriter 2 and 3

             /F2 and /F3 drive  the Quietwriter 2 and 3.  Do not use  1 for pen
             widths because  Quietwriters do not  print consistent 1 dot lines.
             These  drivers  reset  the  line  feed distance to  1/6  inch upon
             completion.

           Kodak Diconix Color 4

             /FK drives the Color 4.

           Pacific Data Products ProTracer

             /FG drives the ProTracer (base model) in IBM Proprinter mode.  The
             maximum print window width is 14.97. Use the prefix code 27,67,144
             for cut sheet paper longer than 11 inches.

           PostScript Printers

             /FS outputs PostScript.  All characters, arcs, fill, and clips are
             converted to simple vectors.

             PrintCAD's pen  color and shading parameters are  mapped into gray
             levels or RGB color levels.

             You can specify  the  nominal  resolution  of  the  PostScript  by
             appending it to the /F option (for example /FS 300).

             You can  specify  the  number  of copies with a  prefix code  that
             includes the number of copies followed by " XC". For example /J 50
             32 88 67  makes 2 (ASCII  050) copies.  You  can specify the paper
             tray with the XP macro.                                           


                                                                           p-27
           Tektronix ColorQuick

             /FR drives the ColorQuick.

           ZSoft PCX and Fax

             Use /FZ to output a ZSoft PCX bit map. The horizontal and vertical
             dots/inch may  be appended  to override  the default 100x100,  for
             example /FZ80,80.  Such output  should generally be directed to  a
             file with the /D option.

             Since  most  fax  software can  take PCX files  as  input, this is
             useful for  faxing  drawings.  Use /FZ200,196  to  match  the  fax
             resolution.                                                       


                                                                           p-28
         Compatibility and Technical Information ------------------------------

           PrintCAD will run on any IBM compatible  DOS computer  with 400K  of
           EMS or XMS memory and a base memory region of 304K.  Because it is a
           swapping   resident  program,  it   may   have  problems   in   some
           environments.  PrintCAD can handle  VCPI  (Virtual  Control  Program
           Interface) based  DOS extenders,  but DPMI based programs  and stand
           alone DOS extenders may cause problems.

           When  using a DOS extender  based program  such  as  AutoCAD  386 or
           Microstation   4,  use  an  extended/expanded  memory  manager  that
           provides VCPI, such as MS-DOS 5 EMM386/HIMEM, QEMM 386, or 386MAX.

           PrintCAD  is  a TSR that takes over interrupt hex 21 and watches for
           DOS 2.0+ file management open functions.  If the filename on an open
           command matches either "pcad#.plt"  or  the mask  specified with /P,
           then file handle dec 99 (dec  19  if /XA  is used)  is returned  and
           PrintCAD is awakened. It then responds to write, device information,
           close, commit, seek, and set date functions.

           When awake, PrintCAD stores HP-GL commands (from  the write command)
           until its 16K buffer is filled  and then it swaps in its 304K memory
           space, processes the data, and swaps the original memory back.

           PrintCAD  was written  by Cary Ravitz and  compiled  with  Borland's
           Turbo Pascal 6.0. PrintGL Printer Driver is the graphics engine.

         User Support ---------------------------------------------------------

           Correspondence about PrintCAD may be sent via the  support  bulletin
           board, fax, Compuserve, or mail.

           BBS:        606-268-0577  1200..9600,N,8,1  24 hours/day

             To ask a question, prepare an ASCII text file with the details  of
             your question.  Then call the bulletin board and choose the upload
             question option.  XMODEM  file transfer  protocol  is required for
             this.  Your  question will  be assigned a  number (such as 1015) -
             remember  this number.  An answer file (with the  assigned number)
             will be posted, usually within  24 hours.  To get an answer,  call
             the  bulletin board, choose the  download option,  then the answer
             option, and then enter the answer number.

           Compuserve: Cary Ravitz [70431,32]

           Fax:        606-268-0577

             If  you hand dial,  the BBS  will answer  and  hang up  (about  20
             seconds), then the call is routed  to the fax.  Faxes from outside
             the  USA may be answered via  letter.  The  fax may be unavailable
             sometimes.

           Mail:       Ravitz Software Inc.
                       P.O. Box 25068
                       Lexington, KY  40524-5068
                       USA