The switch now contains code to support external Hardware Drivers.
The following is an outline spec of the interface. This feature is still
under development - any comments from potential users would be appreciated.

The driver is called by a software interrupt, and must be loaded before
the switch. Each driver can support multiple channels, and more than one
driver may be loaded, so long as each has its own software interrupt number.

At the moment the driver supplies only the Level 1 funtions, ie it effectively
provides a KISS-like interface. Later I hope to support external Level 2
drivers as well.

The transmit buffer will have a 5 byte header, with the length in 4th and
5th bytes. The length includes the header. The received frame passed to 
the switch should have the same format.


;	THE ROUTINE IS CALLED VIA A SIMULATED INT, SO SHOULD RETURN
;	WITH AN IRET. THE DRIVER MAY SUPPORT MULTIPLE LOGICAL CHANNELS -
;	THE CHANNEL NUMBER IS PASSED IN AL
;
;	THE ROUTINE MUST PRESERVE ALL SEGMENT REGISTERS, UNLESS USED TO
;	RETURN A VALUE (IE DS IN FUNCTION 1). OTHER REGISTERS NEED NOT BE
;	SAVED
;
;	THE ROUTINE MUST PROVIDE THE FOLLOWING FUNCTIONS:
;
;
;	AH=0	INITIALISE. CALLED ONCE ON LOAD 
;
;	AH=1	RETURNS POINTER TO RECEIVED FRAME IN DS:SI, LENGTH IN CX
;		RETURNS CX=0 IF NO FRAME READY
;
;	AH=2	SEND FRAME IN BUFFER IN DS:DI - LENGTH IS IN WORD AT 3[DI]
;						DATA FOLLOWS LENGTH
;
;	AH=3	STATUS. RETURNS AX=0 IF TX NOT BUSY. CX=0 IF RX NOT READY
;

The driver does not need to queue transmitted frames, but performance is
likely to be improved if it can buffer a reasonable number of frames. The
receive process must always be capable of buffering frames.


John Wiseman, G8BPQ

9/2/92


The following sample code is equivalent to the INTERNAL Loopback 
driver - ie anything sent to it is received.

 	PAGE    62,132
;

CODE   SEGMENT PUBLIC 'CODE'


	ASSUME  CS:CODE,DS:CODE,ES:CODE
;
;	INTERFACE TO SWITCH IS VIA SOFTWARE INTERRUPT
;
;	COMMANDS SUPPORTED ARE:
;
;	SUBCHANNEL IS IN AL
;
;	AH = 0	INIT Driver
;
;	AH = 1  Poll for data. Returns CX = 0 if none available,
;		otherwise CX=length, DS:SI=Data
;
; 	AH = 2	Send frame. DS:DI = Buffer header.
;
;	AH = 3  Status - Return AX=0 If OK to send a frame.
;			        CX=0 If no frame available to receive
;
	ORG	100H

GO:
	JMP	INIT

SWITCHINT:

	CMP	AH,3
	JE	STATUS

	CMP	AH,2
	JE	PUTFRAME

	CMP	AH,1
	JE	POLL

	IRET

STATUS:

	MOV	AX,0
	CMP	CS:FRAMEFLAG,0		; TX BUSY?
	JZ	STAT00			; NO

	MOV	AX,1

STAT00:

	CMP	CS:FRAMEFLAG,0		; RX READY?
	JE	POLLRET			; NO

	MOV	CX,1

	IRET

POLL:

	CMP	CS:FRAMEFLAG,0
	JE	POLLRET

	PUSH	CS
	POP	DS

	MOV	SI,OFFSET FRAMECOPY
	MOV	CX,3[SI]
	MOV	FRAMEFLAG,0

	IRET

POLLRET:

	MOV	CX,0
	IRET



PUTFRAME:

	PUSH	SI
	PUSH	DI
	PUSH	CX
	PUSH	ES			; save regs

	MOV	CX,3[DI]

	MOV	SI,DI
	MOV	DI,OFFSET FRAMECOPY

	MOV	CS:FRAMEFLAG,1

	PUSH	CS
	POP	ES			; ES TO OUR SEGMENT

	REP MOVSB			; SAVE FRAME
	
	POP	ES
	POP	CX
	POP	DI
	POP	SI

	IRET


FRAMECOPY	DB	400 DUP (0)

FRAMEFLAG	db	0


ENDOFCODE	LABEL	BYTE

MSG	DB	'Sample EXTERNAL Interface for G8BPQ switch '
	db	0dh,0ah,'$'

ERRORMSG	DB	0AH,'Parameter error:',0dh,0ah,0ah
		db	'Format is DRIVER interrupt'
		db	0dh,0ah,'Program NOT installed'
		DB	0dh,0ah,0AH,'$'


INIT:

	MOV	DX,OFFSET MSG
	MOV	AH,9
	INT	21H
;
 	MOV	SI,82H			; PARAM STRING

	CALL	GETVALUE		; interrupt number
	JC	BADPORTVAL

	MOV	AL,BYTE PTR NEWVALUE
	OR	AL,AL
	JZ	BADPORTVAL
;
	MOV	AL,BYTE PTR NEWVALUE	; VECTOR
	MOV	DX,OFFSET SWITCHINT
	MOV	AH,25H
	INT	21H			; SET VECTOR
;
	MOV	DX,OFFSET ENDOFCODE
	INT	27H


BADPORTVAL:

	MOV	AH,9
	MOV	DX,OFFSET ERRORMSG
	INT	21H

	RET

NEWVALUE	DW	0
D16		DW	16
D10		DW	10

GETVALUE:
;
;	EXTRACT NUMBER (HEX OR DECIMAL) FROM INPUT STRING
;
	MOV	NEWVALUE,0

	LODSB
	CMP	AL,'$'			; HEX?
	JE	DECODEHEX
	DEC	SI
VALLOOP:
	LODSB
	CMP	AL,' '
	JE	ENDVALUE
	CMP	AL,0DH
	JE	ENDVALUE
	CMP	AL,','
	JE	ENDVALUE
;
;	ANOTHER DIGIT - MULTIPLY BY 10
;
	MOV	AX,NEWVALUE
	MUL	D10
	MOV	NEWVALUE,AX

	MOV	AL,-1[SI]
	SUB	al,'0'
	JC	DUFFVALUE
	CMP	AL,10
	JNC	DUFFVALUE

	MOV	AH,0
	ADD	NEWVALUE,AX

	JC	DUFFVALUE
	JMP	VALLOOP

DECODEHEX:
HEXLOOP:
	LODSB
	CMP	AL,' '
	JE	ENDVALUE
	CMP	AL,0DH
	JE	ENDVALUE
	CMP	AL,','
	JE	ENDVALUE
;
;	ANOTHER DIGIT - MULTIPLY BY 16
;
	MOV	AX,NEWVALUE
	MUL	D16
	MOV	NEWVALUE,AX

	MOV	AL,-1[SI]
	SUB	al,'0'
	JC	DUFFVALUE
	CMP	AL,10
	JC	HEXOK
	SUB	AL,7
	CMP	AL,10
	JC	DUFFVALUE

	CMP	AL,16
	JNC	DUFFVALUE
HEXOK:
	MOV	AH,0
	ADD	NEWVALUE,AX
	JMP	HEXLOOP

ENDVALUE:
	CLC
	RET

DUFFVALUE:
	STC
	RET


CODE	ENDS
;               
        END     GO





John Wiseman, G8BPQ

21/3/92